UP YOUR ACP


                                 Version 02.00
                                 April 17, 1980




                              Ralph W. Stamerjohn
                                    Monsanto







                                    FOREWORD


                  Dedicated to Esther, who  knows  more  about
                  ACP's  than  any other 370 programmer in the
                  world.



             This document is written by an  RSX-11M  user  for  RSX-11M
        users.   The  initial  seed for this document was planted when I
        researched a project to implement DECNET DAP protocol at the FCS
        level  and  discovered,  contrary  to  popular  belief, there is
        nothing to prevent an user  from  writing  an  ACP.   Quite  the
        contrary, I can now implement ACP's as easily as device drivers.

             The one thing lacking is documentation.  This is my attempt
        to  fill  the  gap  and save others the long nights spent poring
        over listings and  manuals.   This  is  not  to  say  ACP's  are
        trivial.   It is important to remember that while the concept of
        an ACP is simple, the implementation will be as difficult as the
        problem you are attempting to solve.

             The manual is directed  towards  three  types  of  readers.
        First  is  the  developer faced with the task of writing an ACP.
        The entire manual applies to such a reader.  Before refering  to
        this  material,  the  RSX-11M Guide to Writing an I/O Driver and
        the chapters in the RSX-11M  System  Logic  Manual  on  the  I/O
        mechanism and data structures should be covered.

             Next, the manual can be used by someone who merely wants  a
        better  understanding  of  the  ACP  mechanism.  The first three
        chapters should be sufficient for an introduction.  Finally, the
        manual can be used for reference.  In particular, the appendices
        contains useful reference material.

             A sample ACP and supporting enabling  and  disabling  tasks
        have been developed to be used with the manual.  The source code
        should also be studied, especially when reading chapter 3.   The
        sample code can also be used as a basis for a user-written ACP.

             This document reflects ACP's as of  version  RSX-11M  V3.2.
        It does not apply to IAS or VAX/VMS.  The thrust of the document
        is how to fit an ACP into RSX-11M, not how to write any specific
        ACP.

             Naturally, neither the author, Monsanto,  nor  DECUS  claim
        any  responsibility  of  the  accuracy  for the material in this
        document.  If mistakes are found  or  misinterpretations  occur,
        please  notify the author so that the material can be corrected.
        ACP's are moving targets and, at best, this  document  can  only
        move slightly behind them.








             The reader should be aware  that  some  material  has  only
        recently been added and has not been proofread by anyone but the
        author.  This includes all of chapters 4, 5, and 6.  The  manual
        should  be  considered with a grain of salt, especially, the new
        chapters.

             The manual would have been impossible without  the  aid  of
        many  people.   The  management  of  the  Monsanto  Agricultural
        Research department, especially John Schaefer and Larry  Jasper,
        must  be  thanked  for  providing  an  environment  that  allows
        programmers to be imaginative.  From the RSX SIG, Rick  Aurbach,
        Fred  Veck,  John  Wood, and Jim McGlinchey have all contributed
        ideas and time.  Jim and Rick has been  especially  valuable  in
        editting  the  material  and  providing  insight  into  how  the
        material should be presented.  Finally, the manual  would  never
        have been completed without the constant aid of by wife, Esther.


                                      Ralph Stamerjohn
                                      Monsanto, Zone T1A
                                      800 N. Lindbergh
                                      St. Louis, MO, 63166



TABLE OF CONTENTS



                               TABLE OF CONTENTS



        CHAPTER 1 - ACP PHILOSOPHY. . . . . . . . . . . . . . . . . .1-1

            1.1  DEFINITION OF "ACP". . . . . . . . . . . . . . . . .1-1
            1.2  ACP CHARACTERISTICS. . . . . . . . . . . . . . . . .1-2
            1.3  I/O HIERARCHY. . . . . . . . . . . . . . . . . . . .1-4
            1.3.1  FCS/RMS. . . . . . . . . . . . . . . . . . . . . .1-4
            1.3.2  QIO Directive. . . . . . . . . . . . . . . . . . .1-5
            1.3.3  Device Drivers . . . . . . . . . . . . . . . . . .1-5
            1.3.4  ACP's. . . . . . . . . . . . . . . . . . . . . . .1-6
            1.3.5  Summary. . . . . . . . . . . . . . . . . . . . . .1-6
            1.4  ACP ABILITIES. . . . . . . . . . . . . . . . . . . .1-6
            1.5  ACP IMPLEMENTATION . . . . . . . . . . . . . . . . .1-8
            1.5.1  DCP Approach . . . . . . . . . . . . . . . . . . .1-9
            1.5.2  UCP Approach . . . . . . . . . . . . . . . . . . 1-12
            1.5.3  FCP Approach . . . . . . . . . . . . . . . . . . 1-14
            1.6  ACP APPLICATIONS . . . . . . . . . . . . . . . . . 1-16

        CHAPTER 2 - DATA STRUCTURES . . . . . . . . . . . . . . . . .2-1

            2.1  QIO DATA STRUCTURES. . . . . . . . . . . . . . . . .2-1
            2.1.1  QIO Directive Parameter Block. . . . . . . . . . .2-2
            2.1.2  I/O Packet . . . . . . . . . . . . . . . . . . . .2-2
            2.1.3  Logical Unit Table . . . . . . . . . . . . . . . .2-3
            2.2  DEVICE DATA STRUCTURES . . . . . . . . . . . . . . .2-4
            2.2.1  Device Control Block . . . . . . . . . . . . . . .2-4
            2.2.2  Unit Control Block . . . . . . . . . . . . . . . .2-5
            2.2.3  Status Control Block . . . . . . . . . . . . . . .2-5
            2.3  ACP COMMON DATA STRUCTURES . . . . . . . . . . . . .2-6
            2.3.1  Volume Control Block . . . . . . . . . . . . . . .2-6
            2.3.2  Window Control Block . . . . . . . . . . . . . . .2-6
            2.4  ACP SPECIFIC DATA STRUCTURES . . . . . . . . . . . .2-7
            2.5  OTHER DATA STRUCTURES. . . . . . . . . . . . . . . .2-8

        CHAPTER 3 - ACP CHECKLIST . . . . . . . . . . . . . . . . . .3-1

            3.1  QIO DESIGN . . . . . . . . . . . . . . . . . . . . .3-1
            3.1.1  Function Code Selection. . . . . . . . . . . . . .3-2
            3.1.2  I/O Parameter Selection. . . . . . . . . . . . . .3-3
            3.1.3  Relationship Between I/O Requests. . . . . . . . .3-4
            3.2  DEVICE DATA BASE DESIGN. . . . . . . . . . . . . . .3-5
            3.2.1  Device Control Block . . . . . . . . . . . . . . .3-5
            3.2.2  Unit Control Block . . . . . . . . . . . . . . . .3-6
            3.3  ACP DATA BASE DESIGN . . . . . . . . . . . . . . . .3-8
            3.3.1  Volume Control Block . . . . . . . . . . . . . . .3-8
            3.3.2  Window Block . . . . . . . . . . . . . . . . . . .3-9
            3.3.3  Other Data Structures. . . . . . . . . . . . . . .3-9
            3.4  DEVICE DRIVER IMPLEMENTATION . . . . . . . . . . . .3-9
            3.4.1  Driver Entry . . . . . . . . . . . . . . . . . . 3-10
            3.4.2  Driver Packet Processing . . . . . . . . . . . . 3-11



TABLE OF CONTENTS



            3.5  ACP IMPLEMENTATION . . . . . . . . . . . . . . . . 3-12
            3.5.1  ACP Packet Dequeuing . . . . . . . . . . . . . . 3-12
            3.5.2  ACP Packet Processing. . . . . . . . . . . . . . 3-13
            3.5.3  ACP Packet Termination . . . . . . . . . . . . . 3-14
            3.6  TASK TERMINATION . . . . . . . . . . . . . . . . . 3-14
            3.7  ACP ENABLING . . . . . . . . . . . . . . . . . . . 3-14
            3.8  ACP DISABLING. . . . . . . . . . . . . . . . . . . 3-16
            3.9  CHECKLIST SUMMARY. . . . . . . . . . . . . . . . . 3-17

        CHAPTER 4 - ACP/TASK INTERFACE. . . . . . . . . . . . . . . .4-1

            4.1  QIO INTERFACE. . . . . . . . . . . . . . . . . . . .4-1
            4.2  FCS INTERFACE. . . . . . . . . . . . . . . . . . . .4-2
            4.2.1  File Specification . . . . . . . . . . . . . . . .4-3
            4.2.2  File Access. . . . . . . . . . . . . . . . . . . .4-4
            4.2.3  Input/Output . . . . . . . . . . . . . . . . . . .4-5
            4.2.4  File Control . . . . . . . . . . . . . . . . . . .4-6

        CHAPTER 5 - ACP/EXECUTIVE INTERFACE . . . . . . . . . . . . .5-1

            5.1  EXECUTIVE PROCESSING REQUIREMENTS. . . . . . . . . .5-1
            5.2  DCP INTERFACE. . . . . . . . . . . . . . . . . . . .5-3
            5.2.1  $DRQIO Processing. . . . . . . . . . . . . . . . .5-4
            5.2.2  $DRQRQ Processing. . . . . . . . . . . . . . . . 5-10
            5.2.3  $GTPKT Processing. . . . . . . . . . . . . . . . 5-10
            5.3  UCP INTERFACE. . . . . . . . . . . . . . . . . . . 5-11
            5.4  FCP INTERFACE. . . . . . . . . . . . . . . . . . . 5-11
            5.5  ACP INTERFACE. . . . . . . . . . . . . . . . . . . 5-12
            5.6  TASK TERMINATION . . . . . . . . . . . . . . . . . 5-12

        CHAPTER 6 - ACP ENABLING/DISABLING. . . . . . . . . . . . . .6-1

            6.1  ENABLING REQUIREMENTS. . . . . . . . . . . . . . . .6-1
            6.2  DISABLING REQUIREMENTS . . . . . . . . . . . . . . .6-3
            6.3  STANDARD APPROACH. . . . . . . . . . . . . . . . . .6-4
            6.3.1  MOU Task . . . . . . . . . . . . . . . . . . . . .6-5
            6.3.2  MOU /FOREIGN . . . . . . . . . . . . . . . . . . .6-8
            6.3.3  DMO Task . . . . . . . . . . . . . . . . . . . . .6-8
            6.4  NON-STANDARD APPROACHES. . . . . . . . . . . . . . .6-8
            6.4.1  Self-Initialization. . . . . . . . . . . . . . . .6-9
            6.4.2  Driver Initialization. . . . . . . . . . . . . . .6-9
            6.4.3  Alternate Task . . . . . . . . . . . . . . . . . .6-9

        CHAPTER 7 - ACP IMPLEMENTATION. . . . . . . . . . . . . . . .7-1

            7.1  TASK ATTRIBUTES. . . . . . . . . . . . . . . . . . .7-1
            7.1.1  Task Mapping . . . . . . . . . . . . . . . . . . .7-1
            7.1.2  Task Build Requirements. . . . . . . . . . . . . .7-2
            7.2  DESIGN CONSIDERATIONS. . . . . . . . . . . . . . . .7-3
            7.2.1  ACP I/O. . . . . . . . . . . . . . . . . . . . . .7-3
            7.2.2  Transportability . . . . . . . . . . . . . . . . .7-3
            7.2.3  Pool Utilization . . . . . . . . . . . . . . . . .7-4
            7.2.4  ACP Variables. . . . . . . . . . . . . . . . . . .7-4



TABLE OF CONTENTS



            7.2.5  Performance Statistics . . . . . . . . . . . . . .7-4
            7.2.6  Serial Versus Parallel Processing. . . . . . . . .7-5
            7.3  DEBUGGING NOTES. . . . . . . . . . . . . . . . . . .7-5

        CHAPTER 8 - EXECUTIVE SERVICES. . . . . . . . . . . . . . . .8-1

            8.1  SYSTEM STATE . . . . . . . . . . . . . . . . . . . .8-1
            8.2  I/O TERMINATION. . . . . . . . . . . . . . . . . . .8-2
            8.3  ADDRESS CHECKING . . . . . . . . . . . . . . . . . .8-2
            8.4  ADDRESS RELOCATION . . . . . . . . . . . . . . . . .8-2
            8.5  BUFFER ALLOCATION. . . . . . . . . . . . . . . . . .8-3
            8.6  BUFFER DEALLOCATION. . . . . . . . . . . . . . . . .8-3
            8.7  QUEUE MANIPULATION . . . . . . . . . . . . . . . . .8-4
            8.8  DATA TRANSFER. . . . . . . . . . . . . . . . . . . .8-4
            8.9  TASK SCHEDULING. . . . . . . . . . . . . . . . . . .8-4

        APPENDIX A - READINGS/REFERENCES. . . . . . . . . . . . . . .A-1

            A.1  DIGITAL MANUALS. . . . . . . . . . . . . . . . . . .A-1
            A.1.1  RSX-11M Executive Reference Manual . . . . . . . .A-1
            A.1.2  RSX-11M Crash Dump Analyzer Reference Manual . . .A-1
            A.1.3  IAS/RSX-11 I/O Operations Reference Manual . . . .A-2
            A.1.4  IAS/RSX-11 RMS-11 Programmer's Reference Manual. .A-2
            A.1.5  RSX-11M I/O Drivers Reference Manual . . . . . . .A-2
            A.1.6  RSX-11M Guide to Writing an I/O Driver . . . . . .A-2
            A.1.7  RSX-11M System Logic Manuals . . . . . . . . . . .A-2
            A.2  SOURCES. . . . . . . . . . . . . . . . . . . . . . .A-3
            A.2.1  Executive Sources. . . . . . . . . . . . . . . . .A-3
            A.2.2  MOU Sources. . . . . . . . . . . . . . . . . . . .A-3
            A.2.3  DMO Sources. . . . . . . . . . . . . . . . . . . .A-4
            A.2.4  F11ACP Sources . . . . . . . . . . . . . . . . . .A-4
            A.2.5  DECNET Sources . . . . . . . . . . . . . . . . . .A-4
            A.2.6  FCS-11 Sources . . . . . . . . . . . . . . . . . .A-5
            A.2.7  Other Sources. . . . . . . . . . . . . . . . . . .A-5

        APPENDIX B - DATA STRUCTURE DETAILS . . . . . . . . . . . . .B-1

            B.1  QIO DATA STRUCTURES. . . . . . . . . . . . . . . . .B-1
            B.1.1  QIO Directive Parameter Block. . . . . . . . . . .B-3
            B.1.2  I/O Packet . . . . . . . . . . . . . . . . . . . .B-4
            B.1.3  Logical Unit Table . . . . . . . . . . . . . . . .B-7
            B.2  DEVICE DATA STRUCTURES . . . . . . . . . . . . . . .B-8
            B.2.1  Device Control Block . . . . . . . . . . . . . . .B-8
            B.2.2  Unit Control Block . . . . . . . . . . . . . . . B-10
            B.2.3  Status Control Block . . . . . . . . . . . . . . B-14
            B.3  ACP COMMON DATA STRUCTURES . . . . . . . . . . . . B-16
            B.3.1  Volume Control Block . . . . . . . . . . . . . . B-16
            B.3.2  Window Block . . . . . . . . . . . . . . . . . . B-17
            B.4  OTHER DATA STRUCTURES. . . . . . . . . . . . . . . B-17
            B.4.1  Clock Queue Entry. . . . . . . . . . . . . . . . B-18
            B.4.2  Partition Control Block. . . . . . . . . . . . . B-19
            B.4.3  Task Control Block . . . . . . . . . . . . . . . B-21
            B.4.4  Task Header. . . . . . . . . . . . . . . . . . . B-24



TABLE OF CONTENTS



        APPENDIX C - FCS-11 MODULES . . . . . . . . . . . . . . . . .C-1

            C.1  FCS CONDITIONALS . . . . . . . . . . . . . . . . . .C-1
            C.2  FCS DATA STRUCTURES. . . . . . . . . . . . . . . . .C-4
            C.2.1  File Descriptor Block. . . . . . . . . . . . . . .C-4
            C.2.2  Filename Block . . . . . . . . . . . . . . . . . .C-4
            C.2.3  Dataset Descriptor . . . . . . . . . . . . . . . .C-4
            C.2.4  $$FSR1 Region. . . . . . . . . . . . . . . . . . .C-4
            C.2.5  $$FSR2 Region. . . . . . . . . . . . . . . . . . .C-4
            C.3  FCS INTERNALS. . . . . . . . . . . . . . . . . . . C-11
            C.4  FCS MODULES. . . . . . . . . . . . . . . . . . . . C-11
            C.4.1  ANSPAD . . . . . . . . . . . . . . . . . . . . . C-11
            C.4.2  ASCPPN . . . . . . . . . . . . . . . . . . . . . C-11
            C.4.3  ASCR50 . . . . . . . . . . . . . . . . . . . . . C-12
            C.4.4  ASSLUN . . . . . . . . . . . . . . . . . . . . . C-12
            C.4.5  BDBREC . . . . . . . . . . . . . . . . . . . . . C-13
            C.4.6  BIGBUF . . . . . . . . . . . . . . . . . . . . . C-13
            C.4.7  BKRG . . . . . . . . . . . . . . . . . . . . . . C-14
            C.4.8  CKALOC . . . . . . . . . . . . . . . . . . . . . C-14
            C.4.9  CLOSE. . . . . . . . . . . . . . . . . . . . . . C-15
            C.4.10  COMMON. . . . . . . . . . . . . . . . . . . . . C-16
            C.4.11  CONTRL. . . . . . . . . . . . . . . . . . . . . C-16
            C.4.12  CREATE. . . . . . . . . . . . . . . . . . . . . C-17
            C.4.13  DEL . . . . . . . . . . . . . . . . . . . . . . C-17
            C.4.14  DELETE. . . . . . . . . . . . . . . . . . . . . C-17
            C.4.15  DIDFND. . . . . . . . . . . . . . . . . . . . . C-18
            C.4.16  DIFND . . . . . . . . . . . . . . . . . . . . . C-18
            C.4.17  DIRECT. . . . . . . . . . . . . . . . . . . . . C-19
            C.4.18  DIRFND. . . . . . . . . . . . . . . . . . . . . C-19
            C.4.19  DIRNAM. . . . . . . . . . . . . . . . . . . . . C-20
            C.4.20  DLFNB . . . . . . . . . . . . . . . . . . . . . C-20
            C.4.21  ELPARS. . . . . . . . . . . . . . . . . . . . . C-20
            C.4.22  EOFCHK. . . . . . . . . . . . . . . . . . . . . C-21
            C.4.23  EXTEND. . . . . . . . . . . . . . . . . . . . . C-21
            C.4.24  FCSFSR. . . . . . . . . . . . . . . . . . . . . C-22
            C.4.25  FINIT . . . . . . . . . . . . . . . . . . . . . C-22
            C.4.26  GET . . . . . . . . . . . . . . . . . . . . . . C-22
            C.4.27  GETDI . . . . . . . . . . . . . . . . . . . . . C-23
            C.4.28  GETDID. . . . . . . . . . . . . . . . . . . . . C-23
            C.4.29  GETDIR. . . . . . . . . . . . . . . . . . . . . C-24
            C.4.30  MKDL. . . . . . . . . . . . . . . . . . . . . . C-24
            C.4.31  MOVREC. . . . . . . . . . . . . . . . . . . . . C-25
            C.4.32  MRKDL . . . . . . . . . . . . . . . . . . . . . C-25
            C.4.33  OPEN. . . . . . . . . . . . . . . . . . . . . . C-25
            C.4.34  PARDI . . . . . . . . . . . . . . . . . . . . . C-26
            C.4.35  PARDID. . . . . . . . . . . . . . . . . . . . . C-26
            C.4.36  PARSDI. . . . . . . . . . . . . . . . . . . . . C-27
            C.4.37  PARSDV. . . . . . . . . . . . . . . . . . . . . C-28
            C.4.38  PARSE . . . . . . . . . . . . . . . . . . . . . C-28
            C.4.39  PARSFN. . . . . . . . . . . . . . . . . . . . . C-29
            C.4.40  PGCR. . . . . . . . . . . . . . . . . . . . . . C-29
            C.4.41  PNTMRK. . . . . . . . . . . . . . . . . . . . . C-30
            C.4.42  POINT . . . . . . . . . . . . . . . . . . . . . C-31



TABLE OF CONTENTS



            C.4.43  POSIT . . . . . . . . . . . . . . . . . . . . . C-31
            C.4.44  POSREC. . . . . . . . . . . . . . . . . . . . . C-32
            C.4.45  PPNASC. . . . . . . . . . . . . . . . . . . . . C-32
            C.4.46  PPNR50. . . . . . . . . . . . . . . . . . . . . C-33
            C.4.47  PUT . . . . . . . . . . . . . . . . . . . . . . C-33
            C.4.48  RDRN. . . . . . . . . . . . . . . . . . . . . . C-34
            C.4.49  RDWAIT. . . . . . . . . . . . . . . . . . . . . C-34
            C.4.50  RDWRIT. . . . . . . . . . . . . . . . . . . . . C-35
            C.4.51  READ. . . . . . . . . . . . . . . . . . . . . . C-36
            C.4.52  RENAME. . . . . . . . . . . . . . . . . . . . . C-36
            C.4.53  RETADR. . . . . . . . . . . . . . . . . . . . . C-36
            C.4.54  RSTFDB. . . . . . . . . . . . . . . . . . . . . C-37
            C.4.55  RWBLK . . . . . . . . . . . . . . . . . . . . . C-37
            C.4.56  RWFSR2. . . . . . . . . . . . . . . . . . . . . C-38
            C.4.57  RWLONG. . . . . . . . . . . . . . . . . . . . . C-38
            C.4.58  TRNCLS. . . . . . . . . . . . . . . . . . . . . C-39
            C.4.59  UDIREC. . . . . . . . . . . . . . . . . . . . . C-39
            C.4.60  UPWARD. . . . . . . . . . . . . . . . . . . . . C-39
            C.4.61  WAITI . . . . . . . . . . . . . . . . . . . . . C-40
            C.4.62  WAITU . . . . . . . . . . . . . . . . . . . . . C-41
            C.4.63  WATNOD. . . . . . . . . . . . . . . . . . . . . C-41
            C.4.64  WATSET. . . . . . . . . . . . . . . . . . . . . C-41
            C.4.65  WRITE . . . . . . . . . . . . . . . . . . . . . C-42
            C.4.66  WTWAIT. . . . . . . . . . . . . . . . . . . . . C-42
            C.4.67  XQIOI . . . . . . . . . . . . . . . . . . . . . C-43
            C.4.68  XQIOU . . . . . . . . . . . . . . . . . . . . . C-44

        APPENDIX D - FILES-11 QIO'S . . . . . . . . . . . . . . . . .D-1

            D.1  FILES-11 QIO DPB . . . . . . . . . . . . . . . . . .D-1
            D.2  FILES-11 QIO PARAMETERS. . . . . . . . . . . . . . .D-2
            D.2.1  Parameter Word  1 - FID Pointer. . . . . . . . . .D-2
            D.2.2  Parameter Word  2 - Attribute List Pointer . . . .D-2
            D.2.3  Parameter Words  3 and  4 - Size/Extend Control. .D-6
            D.2.4  Parameter Word  5 - Window Size/Access Control . .D-7
            D.2.5  Parameter Word  6 - Filename Block Pointer . . . .D-8
            D.3  FILES-11 QIO FUNCTIONS . . . . . . . . . . . . . . .D-8
            D.4  PLACEMENT CONTROL. . . . . . . . . . . . . . . . . D-10
            D.5  BLOCK LOCKING. . . . . . . . . . . . . . . . . . . D-11

        APPENDIX E - SAMPLE ACP . . . . . . . . . . . . . . . . . . .E-1

            E.1  SOURCES. . . . . . . . . . . . . . . . . . . . . . .E-1
            E.2  PROCEDURE. . . . . . . . . . . . . . . . . . . . . .E-2

        APPENDIX F - USER-WRITTEN ACP'S . . . . . . . . . . . . . . .E-1

            F.1  DAPACP . . . . . . . . . . . . . . . . . . . . . . .F-2














                               CHAPTER 1

                             ACP PHILOSOPHY




             Ancillary  Control  Processors  (ACP's)  are  an   integral
        component  of the RSX-11M operating system.  Yet they remain one
        of the least understood portions of the  system.   This  chapter
        will   develop   a   definition   for   "ACP"  and  explore  the
        functionality ACP's provide in an RSX-11M system.



        1.1  DEFINITION OF "ACP"


             Ancillary control processors are a part of the RSX-11M  I/O
        mechanism.  They implement device protocols for a variety of I/O
        devices.  Because the operation of  ACP's  is  hidden  from  the
        programmer,  they  have been considered untouchable in the past.
        Conceptually, however, an ACP is nothing more than a task  which
        is  tied  to  a  device  driver  via the I/O mechanism.  As this
        manual will show, the interface between an ACP and a  driver  is
        very  simple  and  allows ACP's to be a powerful tool for system
        developers.

             Every operating system's I/O mechanism can be  broken  into
        various  functional  components.   At  the  lowest level are the
        device service routines.   These  routines  perform  the  actual
        device  I/O.   The  next level are the device protocol routines.
        The protocols allow various devices to be classed together as  a
        single  logical  type and extend the device functionality beyond
        the actual device capabilities.  File systems and communications
        protocols  fall  into  this  class.   At  the  next level is the
        mechanism for program I/O requests.  The same mechanism  can  be
        used  for  each  device  or  different devices may use different
        methods.  The final level of functionality are the  logical  I/O
        services.   Record  I/O  falls  into this category.  Logical I/O
        services allow data to be represented in  logical,  rather  than
        the  actual machine format.  In many systems, this level is also
        used to implement device independence.

             While   different   operating   systems    use    different
        implementations  for their I/O mechanism, similarities do exist.



ACP PHILOSOPHY                                                  PAGE 1-2



        Device service routines are  usually  included  in  the  monitor
        because  of  their  requirements  for  responsiveness  and close
        coupling with the hardware devices.  On the other hand, while  a
        property  of  the  operating  system,  device  protocol  code is
        usually  excluded  from  the  kernel  monitor  because  of   its
        complexity and size.  Some mechanism is used to allow the device
        protocol code to communicate with the device service routine.

             RSX-11M uses ACP's  to  implement  device  protocols.   The
        concept  of  an ACP was first used for RSX-11D.  Each device was
        serviced by a task which also contained  the  interrupt  service
        code.   These  tasks were called device handlers and allowed the
        programmer to use the power of both task  and  executive  state.
        For  very  complicated  protocols such as the file system, other
        tasks were used to perform the various file I/O functions.

             This approach suffered  from  several  flaws.   For  simple
        devices  such  as line printers, using a task for device service
        was overkill.  For complex devices, the  structural  limitations
        complicated  the  implementation.   When RSX-11M was introduced,
        device service and device protocol were separated into  distinct
        components.   Simple  device drivers were included in the kernel
        executive.  Special tasks (ACP's) were coupled to the  executive
        to  perform  the  device  protocols.  The coupling mechanism has
        changed with various releases, but the  separation  of  the  two
        components has remained.

             In summary, an ACP is a task  which  is  tied  to  the  I/O
        mechanism  and  is  used  to  provide  a protocol for a class of
        devices.  ACP's enjoy both the features of a task and the  power
        of the executive.  As will be shown later, the coupling of ACP's
        to the executive and  device  drivers  is  very  simple,  making
        user-written  ACP's  a  workable  solution  to a wide variety of
        application problems.



        1.2  ACP CHARACTERISTICS


             Several ACP's have been written  by  Digital.   The  common
        Digital  ACP's  are  the  the  disk  file  system (F11ACP), ANSI
        magtapes (MTAACP), and  the  NSP  portion  of  DECNET  (NETACP).
        These ACP's have the following attributes and characteristics.

             1.  Each  ACP  is  a  privileged  task  and  has  all   the
                 attributes  of  a  task  (stack,  priority,  task name,
                 checkpointing, etc.).

             2.  Each ACP can be considered  a  portion  the  executive.
                 ACP's  are  mapped into the executive and run in kernel
                 state whenever necessary.



ACP PHILOSOPHY                                                  PAGE 1-3



             3.  Each ACP implements a protocol for a class of devices:

                 1.  F11ACP implements the  Files-11  protocol  for  all
                     disks (RK05, RP06, etc.) and DECtapes.

                 2.  MTAACP implements the ANSI magtape protocol for all
                     supported tape drives (TU10, TE16, etc.).

                 3.  NETACP implements the NSP  portion  of  the  DECNET
                     protocol   for  a  wide  variety  of  communication
                     interfaces (DL11, DMC11, etc.).


             4.  The protocols extend the functionality of  the  devices
                 in several ways:

                 1.  The burden of direct device manipulation is removed
                     from  the  programmer  and is handled by the ACP in
                     conjunction with the device drivers.

                 2.  The burden of protocol level data  manipulation  is
                     handled  by  the  ACP's.   The ACP's strip any data
                     related to protocol and return only the information
                     related to the application.

                 3.  The ACP's allow the devices to function as logical,
                     rather  than  physical,  entities.   In the case of
                     Files-11, a program deals  with  files  instead  of
                     physical  disk  blocks.   F11ACP  handles all block
                     mapping and allocation.  Programs view files  as  a
                     set  of contiguous blocks, regardless of the actual
                     allocation.

                 4.  The ACP's allow different devices to be treated the
                     same   from   the  program's  viewpoint.   DECNET's
                     support  of  logical   links   over   asynchronous,
                     synchronous,  and  parallel  interfaces is the most
                     vivid example of this.

                 5.  The devices can be shared for simultaneous  access.
                     Each  accessing process is protected from others by
                     the ACP's.  The ACP's also  synchronize  access  to
                     the physical devices when necessary.

                 6.  The devices are protected against unauthorized  and
                     destructive  access.   When  an  ACP is used with a
                     device, the ACP "owns" the device.


             5.  Each ACP can be mounted/dismounted for a given  device.
                 When  mounted,  the device is available only for use in
                 the context of the device protocol provided by the ACP.




ACP PHILOSOPHY                                                  PAGE 1-4



             One  lack  of  similarity  must  also  be  mentioned.   The
        internal  implementation  of  the  Digital ACP's have nothing in
        common.  The only similarities  are  in  the  interface  to  the
        operating  system.   How an ACP accomplishes its purpose is left
        to the individual ACP.



        1.3  I/O HIERARCHY


             As was stated before, all I/O mechanisms can be broken into
        four  functional  components:  logical I/O services, program I/O
        requests, device handling, and device protocol  services.   This
        section will discuss how each of these functional components are
        implemented by RSX-11M.  In particular, the relationship of each
        component to an ACP will be discussed.

             The I/O mechanism for RSX-11M can be mapped  directly  into
        the  four  areas.  The FCS/RMS libraries provide the logical I/O
        services.   The  QIO  directive  and  the  associated  executive
        processing  form  the I/O request mechanism.  Device drivers are
        used for  device  service.   And  finally,  ACP's  are  used  to
        implement device protocols.



        1.3.1  FCS/RMS


             Logical I/O  services  for  RSX-11M  are  provided  by  the
        file/record service libraries:  Record Management Services (RMS)
        and  File  Control  Services  (FCS).   The  two  most  important
        services  provided by these packages are device independence and
        logical  records.   The  packages  also  provide  a   convenient
        programming interface for issuing I/O requests.

             Both FCS and RMS are implemented as  macro  and  subroutine
        libraries.  RMS is the newer package.  It extends the concept of
        logical records, particularly in the area of record organization
        (relative  and  keyed).   FCS  is the traditional package and is
        more widely used in RSX-11M systems.  However, the libraries are
        equivalent  in their relationship to the other components of the
        I/O mechanism.

             When called, FCS/RMS translate  the  logical  I/O  requests
        into  device  specific  I/O requests.  This is done by examining
        the characteristics of  the  assigned  device  and  issuing  the
        appropriate  QIO directives.  The packages are also aware of the
        existence of the  Files-11  and  magtape  ACP's  and  issue  I/O
        requests  specific  to these ACP's.  It is important to remember
        that FCS/RMS do not implement the file  system,  they  are  only
        aware  of  how  to  interface  to  it to accomplish the services



ACP PHILOSOPHY                                                  PAGE 1-5



        requested by the programmer.  A new ACP  can  be  interfaced  to
        FCS/RMS by teaching the packages the proper usage of the ACP.



        1.3.2  QIO Directive


             All user I/O is requested by using the QIO directive.   The
        directive can be issued directly by a program or indirectly from
        the various run-time systems.

             The QIO directive together with  the  executive  processing
        form  the program I/O request component of RSX-11M.  The RSX-11M
        executive is responsible for translating the QIO  requests  into
        their   internal  representation  (I/O  packets),  checking  for
        parameter validity,  and  dispatching  the  I/O  packet  to  the
        correct processing routine.

             The  device  data  bases  are  used  by  the  executive  to
        determine  how  a  packet is to be processed.  The executive may
        pass the function directly to  a  device  driver  or  queue  the
        packet  to  the  driver I/O queue.  If an ACP is mounted for the
        device, the packet is specially processed and sent  to  the  ACP
        instead  of  the  device  driver.   It is extremely important to
        understand this mechanism when writing an ACP.



        1.3.3  Device Drivers


             Device drivers are the lowest  level  in  the  RSX-11M  I/O
        hierarchy.  Drivers provide the device service functionality and
        are small, responsive modules.  RSX-11M device drivers do little
        more than physical data transfers and device manipulations.  The
        driver I/O parameters are specified in  a  basic,  often  device
        dependent form.

             An ACP can interface to a device driver  in  a  variety  of
        ways.   The  most  common  approach  is  to  use  the normal QIO
        directive.  An ACP will typically take the I/O request queued to
        it  and  issue  device  specific  I/O  requests  to  satisfy the
        request.  The driver code itself is not aware  that  an  ACP  is
        calling it.

             Device drivers serve another purpose in implementing ACP's.
        The  driver  mechanism  is  convenient  for  extending executive
        processing.  As will  be  seen  later,  pseudo  drivers  can  be
        implemented  to  provide  the  processing  necessary for ACP I/O
        requests that is normally done by the  executive.   The  use  of
        such  drivers  permits  user-written  ACP's  to  be  implemented
        without modifying the kernel executive.



ACP PHILOSOPHY                                                  PAGE 1-6



        1.3.4  ACP's


             Finally, ACP's are the  component  which  implement  device
        protocols.   These  tasks  take I/O functions from the executive
        and perform the desired operation according to the rules of  the
        protocol.



        1.3.5  Summary


             At this  stage,  a  simplistic  view  of  the  RSX-11M  I/O
        mechanism  has  been  developed.   The  simplest  case  is a QIO
        request from a task to a non-ACP device.  The  flow  is  through
        the  executive's  QIO  processor  to  the  device  driver to the
        device.  By adding FCS/RMS, the task makes a subroutine call  to
        the  run-time  library  which  then  issues the actual QIO.  The
        final case (Figure 1-1) adds an ACP to the  device.   Here,  the
        I/O  request is routed to the ACP by the executive.  The ACP may
        issue its own I/O requests to the device driver or  satisfy  the
        request  using  its internal data bases.  In some special cases,
        the executive may route the packet directly to the driver.



        1.4  ACP ABILITIES


             It is not often clear why ACP's are such a  necessary  part
        of  the  RSX-11M  I/O  mechanism.  This section will discuss the
        abilities which are  unique  to  ACP's  and  make  them  such  a
        powerful application tool.

             The key abilities come from the fact  an  ACP  is  a  task.
        ACP's  are allowed to do things which are impossible from device
        drivers.  They  can  issue  all  the  RSX-11M  directives.   For
        example,  the  ability  of  an  ACP  to issue QIO's allows it to
        service a complicated I/O request by using the simpler  services
        provided by a device or another ACP.



ACP PHILOSOPHY                                                  PAGE 1-7



         
        		|---------------|
        		|		|
        		|      Task	|
        		|		|
        		|---------------|
        		|      FCS	|
        		|---------------|
        			|
        			| QIO
        		       \|/
        		|---------------|
        		|		|
        	|-------|   Executive	|
        	|	|		|
        	|	|---------------|
        	|		|
        	|		| I/O Packet
        	|		|
        	|	       \|/
        	|	|---------------|
        	|  |--->|		|
        	|  |    |      ACP	|
        	|  |----|		|
        	|	|---------------|
        	|		|
        	|-------------->| I/O Packet
        			|
        		       \|/
        		|---------------|
        		|		|
        		| Device Driver	|
        	 	|		|
        		|---------------|
        		       | |
        		       | |
        		      \| |/
        		|---------------|
        		|		|
        		|    Device	|
        		|		|
        		|---------------|
         
        		    Figure 1-1
        	      RSX-11M I/O MECHANISM




ACP PHILOSOPHY                                                  PAGE 1-8



             At the same time, ACP's are  privileged  tasks.   The  full
        abilities  of  the  executive are available.  For example, ACP's
        can allocate and return  system  pool  merely  by  switching  to
        system  state  and calling the executive routines.  In addition,
        as privileged tasks, ACP's are mapped into the system  pool  and
        can   examine   and   manipulate   all  RSX-11M  executive  data
        structures.

             Also, because ACP's are tasks, they can be  used  with  all
        the  programming  tools  provided by RSX-11M.  For example, they
        may use disk and memory-resident overlays, be checkpointed,  and
        link  to  ODT.   The  last  ability  is a very key feature as it
        allows ACP's to be debugged much less destructively than  device
        driver code.

             The executive interface to ACP's  also  has  abilities  not
        normally   available  to  device  drivers.   A  feature  of  the
        interface allows ACP's to establish a  mapping  between  several
        separate  I/O  requests.  The process of opening a file, reading
        and writing disk blocks, and closing the file is an  example  of
        this  mechanism.   Similarly,  DECNET  supports  establishing  a
        logical link, transmitting and receiving data,  and  terminating
        the link.

             This feature allows an "I/O process" to be established  for
        a  logical unit in a task.  Each process uses an ACP unique data
        structure called a window to establish the linkage  between  the
        lun  and  the operations being performed by the ACP.  The window
        address is stored in the second word of the logical unit  table.
        This  address  is passed to the ACP in the I/O packet and allows
        the ACP to reference the window when  serving  a  request.   The
        mechanism  also  includes support for notifying the ACP when the
        task terminates and I/O processes are still outstanding, even if
        the task has no outstanding I/O.



        1.5  ACP IMPLEMENTATION


             This manual will cover three types of ACP  implementations:
        standard,  user,  and  foreign.   While  each  form fulfills the
        definition of "ACP", standard ACP's follow  the  rules  used  by
        Digital in writing F11ACP and MTAACP.  Such ACP's are "known" to
        the executive and special code is included for their support.

             On the other hand,  user  ACP's  are  not  "known"  to  the
        system,  only  to  the  device driver which uses their services.
        The major advantage of  the  approach  is  that  no  changes  to
        existing executive code are necessary for the user ACP, yet, all
        the advantages of having an ACP remain.

             Foreign ACP's are between standard and user ACP's.  The ACP



ACP PHILOSOPHY                                                  PAGE 1-9



        is  known to the executive, yet no special services are provided
        for support of the ACP.

             Throughout this paper,  references  will  be  made  to  the
        requirements  for writing standard, user, and foreign ACP's.  In
        order to simplify the  terminology,  "ACP"  will  be  used  when
        discussing  material  relevant  to  all  styles.  "DCP" (Digital
        Control Processor)  will  be  used  when  refering  strictly  to
        standard ACP's.  "UCP" (User Control Processor) will be used for
        references concerned with  the  user  form  and  "FCP"  (Foreign
        Control  Processor)  will  refer  to ACP's which use the foreign
        feature of RSX-11M.

             The choice of writing a DCP, UCP, or  FCP  depends  on  the
        purpose  of  the  ACP.  The major difference between the various
        forms of ACP's is how and where the I/O requests designated  for
        the  ACP  are processed.  No matter which form is implemented, a
        certain amount of  pre-processing  is  required  before  an  I/O
        request  is received by an ACP.  The next three sections examine
        how each form of ACP interfaces to the executive.



        1.5.1  DCP Approach


             Figure 1-2 diagrams the flow of an I/O request from an user
        task  to a DCP.  When a QIO is issued from a task, the directive
        dispatcher calls the entry $DRQIO.  The common QIO processing is
        performed  first.   The  current task state is checked to see if
        the QIO can be issued at this time.  If it can, the  common  QIO
        fields  are  checked  for  legality.   Finally, an I/O packet is
        allocated from the system pool and initialized with  information
        taken from the QIO directive parameter block.

             Once the common processing is completed, the QIO  processor
        dispatches  to  the  function  unique  code.  The current device
        status stored in the Unit Control Block (UCB) and  the  function
        bit  masks  in the Device Control Block (DCB) determine the type
        of function processing selected.  In the case of an  I/O  packet
        designated  for  a  DCP,  the  device driver must be loaded, the
        device marked as mountable, mounted, and not  foreign,  and  the
        function  marked  as legal and ACP in the DCB mask fields.  When
        these conditions are met, the ACP special packet  processing  is
        invoked.   Each  I/O  function  supported  by  Digital  ACP's is
        processed using special polish-driven routines.



ACP PHILOSOPHY                                                 PAGE 1-10



        		|-------------------------------|
        		|	    Task Code		| Task
        		|-------------------------------|
        				|
        				| ACP QIO
        				|
        			       \|/
        		|-------------------------------|
        		|	Check for Legality	|
        		|---			     ---|
        		|      Construct I/O Packet	|
        		|---			     ---| $DRQIO
        		|     Special ACP Processing	|
        		|---			     ---|
        	|-------|   Queue to ACP if Specified	|
        	|	|-------------------------------|
        	|			|
        	|			| JMP
        	|			|
        	|		       \|/
        	|	|-------------------------------|
        	|	|	Queue I/O Packet	|
        	|	|---			     ---| $DRQRQ
        	|	|     Call Driver Initiator	|
        	|	|-------------------------------|
        	|			|
        	|			| JSR
        	|			|
        	|		       \|/
        	|	|-------------------------------|
        	|	|	  Call $GTPKT		| Device Driver
        	|	|-------------------------------|
        	|			|
        	|			| JSR
        	|			|
        	|		       \|/
        	|	|-------------------------------|
        	|	|	 Get I/O Packet		|
        	|	|---			     ---| $GTPKT
        	|	|     Determine ACP Function	|
        	|	|-------------------------------|
        	|			|
        	|---------------------->| JSR
        				|
        			       \|/
        		|-------------------------------|
        		|	Queue Packet to TCB	|
        		|---			     ---| $EXRQP
        		|	   Request ACP		|
        		|-------------------------------|
         
        			  Figure 1-2
        			   DCP FLOW



ACP PHILOSOPHY                                                 PAGE 1-11



             One function of the special processing is to decide whether
        the  I/O packet needs sequencing with the device driver state or
        whether it can be queued directly to the  ACP.   If  the  packet
        does  not  need  sequencing,  DRQIO queues the I/O packet to the
        receive queue of the ACP and schedules the  ACP  for  execution.
        Otherwise,  the  packet is placed in the I/O queue of the driver
        and the driver initiator is called.  The packet will  be  queued
        to  the  ACP  when  it  is  dequeued  by  $GTPKT.   This  occurs
        transparently to the driver.

             I/O packets are queued to an ACP via the ACP task's receive
        queue.   This  is the same queue used by normal tasks to receive
        messages from other programs.  The entries $EXRQP/$EXRQF in  the
        executive  queue  the  I/O  packet  and also cause the ACP to be
        scheduled for execution.

             In short, a DCP is known to the executive.  Special code in
        the  executive's DRQIO module handles functions designated for a
        DCP.  The features of this approach are as follows:

             1.  I/O functions processed by the DCP are marked as  legal
                 and  ACP  functions  in  the  DCB  function masks.  DCP
                 function codes are required to be from 7-31(10).

             2.  The  device  is  marked  as  mountable,  mounted,   and
                 not-foreign in the UCB.

             3.  The I/O packet is specially processed  by  DRQIO.   The
                 type   of  processing  performed  depends  on  the  I/O
                 function code and is done by the polish-driven routines
                 in DRQIO.

             4.  The I/O packet is queued to the DCP by  the  executive,
                 however,  for  some  functions  the  packet  is  queued
                 directly by DRQIO and  for  others  it  is  handled  by
                 GTPKT.


             The DCP approach is appropriate for a user-written ACP when
        the  new  ACP  processes current Digital ACP functions.  In this
        case, no modification of the code in the executive is  necessary
        to  support  the  user-written  ACP.   It  is  also important to
        understand the DCP approach when using the methods discussed  in
        the  next  two  sections.   The  FCP  and UCP approaches are not
        short-cuts, they merely move the special processing performed in
        DRQIO to outside the executive.



ACP PHILOSOPHY                                                 PAGE 1-12



        1.5.2  UCP Approach


             The UCP approach provides all the  functionality  found  in
        Digital's  implementation  of ACP's.  The approach uses features
        of the RSX-11M I/O mechanism to move the special  code  for  ACP
        I/O processing to outside the executive.  This permits a user to
        write a totally new ACP without modifying the executive.

             The key to the UCP approach is the UC.QUE bit in  the  UCB.
        When  this  bit is set, I/O packets are not queued to either the
        device driver  or  any  associated  ACP.   Instead,  the  driver
        initiator  is called directly from the DRQIO module.  The driver
        can then perform any necessary special packet processing in-line
        with  the  executive's I/O processing.  When finished the driver
        is responsible for placing the I/O packet in the correct queue.

             The fact that no  context  switch  can  occur  between  the
        executive  and  the call to the device driver is critical to the
        UCP implementation.  Certain types of processing done on the I/O
        packet,  such  as address checking and relocation, must occur in
        the context of the task which issued the I/O  request.   Once  a
        packet  is  placed  in driver or ACP queue, a context switch may
        occur before it is retrieved.  In the case of a packet queued to
        an  ACP,  a  context  switch is implied by the fact that the ACP
        must be scheduled.

             Figure 1-3 illustrates the flow of an I/O request  from  an
        user  task  to  a UCP.  First, the common QIO processing occurs.
        The first difference between a DCP and UCP is evident  when  the
        dispatch  is made to the function unique code.  The UCP approach
        marks all functions serviced by the UCP  as  legal  and  control
        functions.   By  marking the function as a control function, the
        executive merely copies  the  six  QIO  parameters  to  the  I/O
        packet.   This  avoids  any  special  processing  built into the
        executive for DCP-style ACP's.

             Once the I/O packet is constructed, the driver initiator is
        called  without  any  queueing,  due  to  UC.QUE being set.  The
        driver can then process the I/O parameters in the I/O packet  as
        needed.   The driver then queues the packet and requests the UCP
        by calling the normal ACP scheduling  routine.   If  the  packet
        should not be routed to the UCP, the driver queues the packet to
        itself and calls $GTPKT to correctly synchronize  driver  packet
        processing.



ACP PHILOSOPHY                                                 PAGE 1-13



         
        		|-------------------------------|
        		|	    Task Code		| Task
        		|-------------------------------|
        				|
        				| CTL QIO
        				|
        			       \|/
        		|-------------------------------|
        		|	Check for Legality	|
        		|---			     ---|
        		|      Construct I/O Packet	| $DRQIO
        		|---			     ---|
        		|	Copy I/O Parameters	|
        		|-------------------------------|
        				|
        				| JMP
        				|
        			       \|/
        		|-------------------------------|
        		|     Call Driver Initiator	| $DRQRQ
        		|-------------------------------|
        				|
        				| JSR
        				|
        			       \|/
        		|-------------------------------|
        		|      Special ACP Processing	|
        		|---			     ---| Device Driver
        		|	   Queue to ACP		|
        		|-------------------------------|
        				|
        				| JSR
        				|
        			       \|/
        		|-------------------------------|
        		|	Queue Packet to TCB	|
        		|---			     ---| $EXRQP
        		|	   Request ACP		|
        		|-------------------------------|
         
        			  Figure 1-3
        			   UCP FLOW




ACP PHILOSOPHY                                                 PAGE 1-14



             Therefore, an UCP is  known  to  the  device  driver.   The
        executive  is  unaware  that  a  UCP  is being interfaced to the
        driver.  This has the disadvantage of generally limiting  a  UCP
        to  supporting  only one device driver.  The features of the UCP
        approach are as follows:

             1.  The I/O functions processed by the UCP  are  marked  as
                 legal and control functions in the DCB function masks.

             2.  The device is typically marked as  mountable,  mounted,
                 and not-foreign in the UCB.  The driver is also set for
                 no queueing of the I/O packet (UC.QUE=1).

             3.  The I/O packet is processed as a  control  function  by
                 DRQIO.   Any  special processing required by the UCP is
                 performed in the device driver.

             4.  The I/O packet is queued  to  the  UCP  by  the  device
                 driver when it finishes its special processing.




        1.5.3  FCP Approach


             The FCP approach is between the  DCP  and  UCP  techniques.
        The approach is based on the RSX-11M V3.2 executive's support of
        the foreign ACP bit in the UCB (US.FOR).  When this bit is  set,
        the  special  processing  applied  to DCP functions is bypassed.
        The I/O parameters are merely copied to the I/O packet.

             Figure 1-4 shows the flow of  an  I/O  request  to  a  FCP.
        Functions  to  be  routed to the FCP are marked as legal and ACP
        functions in the DCB function bit masks.  The  device  state  in
        the UCB must be mountable, mounted, and foreign ACP.  When these
        conditions are met, the QIO parameters are  copied  without  any
        checks  to  the  I/O packet.  This is the same as the processing
        applied to a DCP.  At this point, the I/O packet  is  routed  to
        the  FCP  by DRQIO if the queue disable bit is not set (UC.QUE).
        This is acceptable only if no special  processing  needs  to  be
        applied to the packets.

             If this condition cannot be met, the same approach used for
        UCP's  must  be  applied.   The  packet  must  be passed without
        queueing to the driver initiator which then applies any  special
        processing  needed.  When completed, the driver can either queue
        the packet directly to the FCP or queue it  to  itself  and  let
        $GTPKT dequeue the packet and send it to the FCP.

             While FCP's are known to the executive, the same processing
        is  applied no matter what the I/O function.  The following is a
        summary of the FCP approach:



ACP PHILOSOPHY                                                 PAGE 1-15



        		|-------------------------------|
        		|	    Task Code		| Task
        		|-------------------------------|
        				|
        				| ACP QIO
        			       \|/
        		|-------------------------------|
        		|	Check for Legality	|
        		|---			     ---|
        		|      Construct I/O Packet	|
        		|---			     ---| $DRQIO
        		|	Copy I/O Parameters	|
        		|---			     ---|
        	|-------|   Queue to ACP if UC.QUE=0	|
        	|	|-------------------------------|
        	|			|
        	|			| JMP
        	|			|
        	|		       \|/
        	|	|-------------------------------|
        	|	|     Call Driver Initiator	| $DRQRQ
        	|	|-------------------------------|
        	|			| JSR
        	|			|
        	|		       \|/
        	|	|-------------------------------|
        	|	|      Special ACP Processing	|
        	|	|---			     ---|
        	|	|	 Queue I/O Packet	| Device Driver
        	|	|---			     ---|
        	|	|	  Call $GTPKT		|
        	|	|-------------------------------|
        	|			|
        	|			| JSR
        	|			|
        	|		       \|/
        	|	|-------------------------------|
        	|	|	 Get I/O Packet		|
        	|	|---			     ---| $GTPKT
        	|	|     Determine ACP Function	|
        	|	|-------------------------------|
        	|			|
        	|---------------------->| JSR
        				|
        			       \|/
        		|-------------------------------|
        		|	Queue Packet to TCB	|
        		|---			     ---| $EXRQP
        		|	   Request ACP		|
        		|-------------------------------|
         
        			  Figure 1-4
        			    FCP FLOW



ACP PHILOSOPHY                                                 PAGE 1-16



             1.  The I/O functions processed by the FCP  are  marked  as
                 legal and ACP functions in the DCB function masks.

             2.  The device is marked as mountable, mounted, and foreign
                 in the UCB.  Any necessary special packet processing is
                 performed by the device driver and  the  queue  disable
                 bit (UC.QUE) must be set.

             3.  The executive only copies the QIO parameters to the I/O
                 packet.   As  stated  above,  any special processing is
                 must be done by the device driver

             4.  The I/O packet can be queued to the FCP by  DRQIO,  the
                 device driver, or GTPKT.

        The advantage of the FCP over the UCP approach is not in the I/O
        packet  processing.  The executive services are minimal and like
        all Digital software, subject to change.  The advantage  is  the
        support  provided  by  the  MOU  and  DMO  task for mounting and
        dismounting the foreign ACP.



        1.6  ACP APPLICATIONS


             ACP's can be written for a wide  variety  of  applications.
        One   type   of  application  is  a  non-Files-11  file  system,
        particularly,  if  the  ACP  is  interfaced   to   FCS/RMS   for
        device/file independence.  Two examples are listed below:

             1.  If a site supports mixed systems (RT-11 and RSX-11M for
                 example),  an  ACP  could be implemented to support the
                 foreign file structure.   If  interfaced  to  FCS,  the
                 RSX-11M  utilities  could be used to access the foreign
                 disk directly.

             2.  If  a  site  has  a  requirement  to  process   foreign
                 magtapes,  an ACP could be written for this task.  This
                 is basically what occurred when MTAACP  was  introduced
                 by Digital.


             ACP's  could  also  be  used  to  implement  communications
        protocols.    Digital   took   this  approach  with  DECNET.   A
        user-written  ACP  could  be  used  to  communicate  with  other
        computers  via some established protocol (BYSYNC, SDLC, etc.) or
        a  site-specific  protocol.   Alternatively,  an  ACP  could  be
        written to replace NSP within the DECNET architecture.  This ACP
        could implement a specialized link level protocol.

             Another  class  of  applications  is  be  to   extend   the
        functionality  of  a  current  Digital device.  For example, one



ACP PHILOSOPHY                                                 PAGE 1-17



        method of implementing transparent line printer  spooling  would
        be  via  a  line  printer  ACP.  This task would intercept write
        requests to the line printer and output them  to  a  disk  file.
        When  the  output  is  terminated,  the  file  is  queued to the
        printer.

             ACP's can also be used to solve application problems.   For
        example,   an   application   system  may  use  a  complex  file
        organization for storing and retrieving data.  Usually with such
        implementations,   special   subroutine  libraries  have  to  be
        developed and linked to each task to access the information  and
        coordinate  updating  the  data.   An  ACP could be written that
        would essentially implement a special database management system
        for the application.

             Many  other  applications  for  ACP's  could   be   listed.
        Appendix  F  list  various  user-written  ACP's  that  have been
        reported to the author.  Other users who have written ACP's  are
        invited  to  submit  a  summary  of  their  implementation to be
        included in future versions of this manual.














                               CHAPTER 2

                            DATA STRUCTURES




             ACP's, like most system tasks, deal with the RSX-11M system
        data  structures.   In  the  case  of  ACP's,  some  of the data
        structures are  integral  to  the  ACP  concept.   This  chapter
        examines  the  RSX-11M  data  structures  in  the context of ACP
        usage.  The emphasis is on the global relationship  between  the
        data   structure,  the  RSX-11M  I/O  mechanism,  and  the  ACP.
        Appendix B presents a  detailed  view  of  the  data  structures
        mentioned in this chapter.

             The data structures of interest to  ACP's  can  be  divided
        into  seven categories:  QIO data structures, device driver data
        structures,  common  ACP  data  structures,  ACP  specific  data
        structures,  FCS data structures, RMS data structures, and other
        structures.  This chapter deals with the first four areas.   The
        FCS and RMS structures are discussed in Chapter 4.  This chapter
        will also touch on the how some of the other data structures are
        used by ACP's.



        2.1  QIO DATA STRUCTURES


             The QIO  data  structures  are  used  to  package  the  I/O
        requests  and route the request to the correct device.  The data
        structures used to package I/O requests are  the  QIO  directive
        parameter block and the I/O packet.  The QIO directive parameter
        block is formed in the issuing task.   The  I/O  packet  is  the
        executive  representation of this structure.  The data structure
        used to route I/O packets to the correct device is  the  logical
        unit  table.  This table is found in the task header and is used
        to map a logical unit number to a specific device.



DATA STRUCTURES                                                 PAGE 2-2



        2.1.1  QIO Directive Parameter Block


             The QIO directive parameter block (DPB) is the form an  I/O
        request takes in a user task.  The block is normally constructed
        by the QIO$ and  QIOW$  macros.   All  I/O  requests,  including
        requests  to ACP's, are issued from a task by using the QIO$ and
        QIOW$ directives.

             While the format of a QIO DPB  is  constant,  some  special
        consideration must be given the DPB when writing a new ACP.  The
        ACP design must consider the I/O functions it will  service  and
        the format of the six QIO parameters.

             The I/O function is a two byte field.  The  executive  only
        considers the high byte in processing an I/O request.  This byte
        is the function code and has a legal range of 0-31(10).  The low
        byte  is  the  subfunction field.  All values are legal for this
        byte.  The subfunction codes are used by drivers  and  ACP's  to
        further  delimit  I/O  functions.   The only requirement for the
        subfunction code  is  that  all  subfunctions  of  a  particular
        function  code  must  be  the  same  type  of request (transfer,
        control, etc.).

             Some rules also apply to  the  function  code  byte.   Some
        codes   have   been   traditionally  reserved  for  special  I/O
        functions;   in  particular,  codes  0-7  all  have  traditional
        meanings  and  should  not  be considered for new ACP I/O codes.
        Also, if  the  new  ACP  follows  the  DCP  implementation,  the
        executive  $GTPKT  routine  requires  the  ACP function codes to
        range from 7-31(10).

             Because the I/O parameters for an ACP function are  usually
        processed  specially,  there  is almost complete freedom in what
        parameters are used.  The only RSX-11M  requirement  applies  to
        transfer  functions.   For  such  I/O  requests,  the  executive
        expects the first parameter to be the address of  a  buffer  and
        the second parameter to be the size of the buffer in bytes.



        2.1.2  I/O Packet


             The I/O packet is the internal  representation  of  an  I/O
        request.   DRQIO  allocates  the I/O packet from system pool and
        initializes  it  with  values  taken  from  the  QIO   directive
        parameter  block.   The packet is then queued to the appropriate
        driver or ACP for servicing.

             When writing a new ACP, the process of initializing the I/O
        packet  parameter fields must be considered.  For DCP's, this is
        the main purpose of the special ACP code in  DRQIO.   A  typical



DATA STRUCTURES                                                 PAGE 2-3



        ACP   I/O   request  may  pass  several  addresses  and  special
        parameters.  Each address must be checked and  relocated  before
        stored  in  the packet.  In some cases, the parameters passed to
        the ACP have little physical resemblance  to  the  original  QIO
        parameters.   The  special  ACP  processing  has  repackaged the
        information for the ACP.

             The rest of the I/O packet is typically of no  interest  to
        ACP's,  with  two exceptions:  the function code and the address
        of the second lun word.  The executive copies the function  code
        from the QIO directive parameter block into the I/O packet.  The
        function code can then used by the ACP to dispatch the packet to
        the appropriate function processor.

             The second lun word address field is the one  part  of  the
        I/O  packet which is not typically used by device drivers.  This
        location contains the address of the second word in the  logical
        unit  table  entry  for  the  lun of the I/O request.  (see next
        section).  The importance of this word will be explained in  the
        section on window blocks.



        2.1.3  Logical Unit Table


             The purpose of the logical  unit  table  (LUT)  is  to  map
        logical  unit numbers to devices.  The LUT table is also used to
        map luns to I/O processes.  The table is a portion of  the  task
        header and consist of a two word entry for each possible logical
        unit a task may  use.   The  size  of  the  table  is  fixed  at
        taskbuild time by the UNITS option.

             TKB fills the table with the ASCII  device  name  and  unit
        number.   When a task is installed, the first word of each entry
        is replaced with the device UCB address and the second  word  is
        zeroed.   When an I/O request is issued, the logical unit number
        maps the appropriate entry in the LUT.   Any  redirect  pointers
        are  followed  and the I/O packet is dispatched to the resulting
        device.  This may result in the packet being queued  to  an  ACP
        serving the device.

             The second word of the LUT entry is used by  ACP's  to  map
        I/O  processes  to  logical  unit  numbers.   The address of the
        window block is kept in this word.  A window block  is  the  I/O
        process  unique  data  structure  and  is  discussed in a latter
        section.  An example of  window  blocks  is  the  F11ACP  window
        blocks  used  to map virtual blocks to logical blocks.  Note, an
        ACP window block is  different  from  a  PLAS  or  task  mapping
        window.

             The second LUT word has two other uses important to  ACP's.
        Bit  0  of  the word is the lun lock bit.  When this bit is set,



DATA STRUCTURES                                                 PAGE 2-4



        the executive prevents the user task from issuing any QIO's  for
        the  logical  unit.   This can be used by ACP's to insure proper
        synchronization between a request it is currently servicing  and
        the user task.

             The other use of the second LUT word  is  to  notify  ACP's
        when a task exits with outstanding I/O processes.  A task is not
        permitted to exit until all second LUT words in the logical unit
        table  are  zero.  When a non-zero entry is found, the executive
        queues a special I/O request to the ACP.  The ACP is responsible
        for terminating the I/O process and zeroing the second LUT word.



        2.2  DEVICE DATA STRUCTURES


             The device data structures are used to describe the generic
        device type, each separate device, and each hardware controller.
        The Device Control Block (DCB) names the device and contains the
        I/O  dispatch  tables.   There  is one DCB for each device type.
        The Unit Control Block (UCB) contains the information  for  each
        device  unit.   The  Status  Control  Block  (SCB)  is  used  to
        coordinate activity among device controllers.  There is one  SCB
        for  each  controller.   The RSX-11M executive typically permits
        only one I/O request to be outstanding for each controller.   If
        the  controller  supports  multiple  units  (UCB's) but requires
        serial access, one SCB will be  used  for  all  UCB's.   If  the
        controller  permits  multiple  access, one SCB will be allocated
        for each UCB.

             Most of the information in the device  data  structures  is
        specific to the needs of device drivers.  ACP's are usually only
        concerned with a few fields.  The next three sections comment on
        how the DCB, UCB, and SCB are involved with ACP implementation.



        2.2.1  Device Control Block


             The Device Control Block (DCB) names the device, points  to
        the  device  unit  structures and controls how I/O functions for
        the device are processed.  This last feature is important to ACP
        implementation.    The  DCB  function  masks  decide  whether  a
        particular I/O function  is  legal  or  invalid.   They  further
        classify  legal  functions into four types:  control, noop, ACP,
        and transfer.  When implementing a DCP or FCP,  functions  which
        should  be  routed to the ACP are marked as legal and ACP in the
        DCB function masks.  This causes the special  packet  processing
        in  DRQIO  for ACP functions to be invoked.  When implementing a
        UCP, the functions are marked as legal and control.



DATA STRUCTURES                                                 PAGE 2-5



        2.2.2  Unit Control Block


             The Unit Control Block (UCB) is the key  device  structure.
        There  is  one  UCB for each separate device.  The UCB's are the
        one device structure that are  variable  in  length.   The  only
        requirement  for  UCB's  is that all UCB's belonging to a DCB be
        allocated contiguously and that all are the same size.

             When a device supports an ACP, the UCB's  are  extended  at
        least  two  words  beyond  the  normal length.  These additional
        words are used to hold the Task Control Block address of the ACP
        (U.ACP)  and  the  Volume  Control  Block  address (U.VCB).  The
        address stored in U.ACP is the task TCB  address  the  executive
        will use when queueing ACP I/O packets.

             The flag fields in the UCB are also of interest  to  ACP's.
        The  control  flags  byte (U.CTL) are used to decide how various
        I/O requests are to be handled.  One bit in this  field  is  the
        UC.QUE  bit  used by UCP and FCP implementations to pass the I/O
        packet to the device driver for ACP processing.  The unit status
        flags  byte  (U.STS) contains bits which define whether the unit
        is busy (US.BSY), mounted (US.MNT), foreign (US.FOR), or  marked
        for dismount (US.MDM).  The correct manipulation of all of these
        bits is necessary for the correct operation of an ACP.  A device
        is  marked  busy  whenever  an  I/O function is dequeued for the
        device driver.  The busy bit is cleared whenever an I/O function
        is completed by calling $IODON.  A function will not be dequeued
        for a device if it is marked busy.  Because  ACP  functions  are
        not  processed  by  the  device driver, the driver is not marked
        busy when an ACP function is dequeued and  passed  to  the  ACP.
        This  allows  the  driver  to  continue to service functions and
        requires ACP's to not clear the busy bit when they finish an I/O
        request.   The  mounted  bit signifies an ACP is mounted for the
        device and can process I/O requests.  When an device  is  marked
        mounted,  U.ACP  and  U.VCB are assumed to contain valid values.
        The US.MDM bit signifies a dismount request has  been  made  for
        the  unit.   No new I/O processes should be allowed to start and
        when all outstanding processes are  completed,  the  ACP  should
        mark  itself  not mounted by setting US.MOU.  The ACP exits when
        all devices are finally dismounted.  Finally, the US.FOR bit  is
        the  indication  to  the  executive  that  the foreign ACP logic
        should be invoked.



        2.2.3  Status Control Block


             The Status Control  Block  (SCB)  is  used  to  define  and
        control  access  to  the hardware controller.  ACP's are usually
        not concerned with this data structure unless they  are  closely
        coupled to the device driver.



DATA STRUCTURES                                                 PAGE 2-6



        2.3  ACP COMMON DATA STRUCTURES


             Two data  structures  are  common  to  all  ACP's:   Volume
        Control Blocks and Window Blocks.  The Volume Control Blocks are
        used to hold information  about  each  separate  device  an  ACP
        services.   The  Window Blocks hold the I/O process information.
        While all ACP's typically use these structures, their format  is
        ACP dependent.



        2.3.1  Volume Control Block


             One feature of ACP's is their ability  to  service  several
        different   devices.   The  data  structure  used  to  keep  the
        information for each device is called  a  volume  control  block
        (VCB).   A  VCB is allocated from the system pool when an ACP is
        mounted for a device.  The address  of  the  VCB  is  stored  in
        offset U.VCB of the device UCB.  The VCB is returned to the pool
        when the ACP completes dismounting the device.

             The length and format of a VCB is ACP-dependent.  Only  the
        first  word has a common meaning across ACP's.  This word of the
        VCB is the volume transaction count and is used as a counter  of
        the number of outstanding I/O requests queued to the ACP for the
        device.  It also counts the number of I/O processes  created  by
        the  ACP  for  the  device.   The ACP cannot dismount the device
        until the transaction count reaches zero, indicating no activity
        for the device.

             For DCP and FCP implementations, the  executive  increments
        the  transaction  count  whenever it queues an I/O packet to the
        ACP.  It is the responsibility of the device driver to increment
        the transaction count when it queues a packet to a UCP.  The ACP
        is  then  responsible  for  decrementing  the  counter  when  it
        completes  an I/O function and incrementing and decrementing the
        counter when it creates and destroys I/O processes.

             The remainder of the  VCB  can  be  used  for  any  purpose
        desired  by the implementation.  The typical information kept in
        a VCB is any data which is unique to the volume.   For  example,
        F11ACP  keeps  the  index  file  mapping  information and volume
        defaults in disk VCB's.



        2.3.2  Window Control Block


             As mentioned before, one powerful feature of ACP's is their
        ability  to  establish  a  mapping  between  I/O  requests.  For



DATA STRUCTURES                                                 PAGE 2-7



        example, F11ACP maps read and write virtual block I/O to logical
        disk  blocks.   The  information necessary to do this mapping is
        established when the file is opened.

             This ability  to  create  an  "I/O  process"  uses  a  data
        structure called window blocks.  These structures are completely
        ACP  dependent  in  length  and  format  and  contain   whatever
        information  the  ACP  needs  to keep for each separate process.
        Typically, window blocks keep access masks,  pointers  to  other
        ACP  unique  data structures, and retrieval information for read
        and write requests.

             Window blocks are allocated by the ACP when it  creates  an
        I/O process.  While the window block is typically allocated from
        system pool, it can be allocated from the ACP task space if only
        the ACP accesses the window.  The window block address is stored
        in the second word  of  the  logical  unit  table  entry.   This
        address  is  passed  in the I/O packet in offset I.LN2.  Further
        I/O requests from the same logical unit  will  always  reference
        the  same logical unit table entry, allowing the ACP to retrieve
        the window block address.


                                      NOTE

             The address of the second  LUT  word  cannot  be  kept
             internally  by  the  ACP.  The LUT table is located in
             the task header, which is destroyed and reallocated if
             the task is checkpointed.  An ACP cannot depend on any
             location in the task header being the same across  I/O
             requests.





        2.4  ACP SPECIFIC DATA STRUCTURES


             ACP's also can  create  their  own  data  structures.   For
        example,  F11ACP creates File Control Blocks (FCB) for each open
        file.  The type and extent  of  data  structures  created  by  a
        user-written ACP is one of the keys in the ACP design.

             One  guideline  to  ACP  specific  data  structures  is  to
        minimize the usage of system pool.  Any information used only by
        the ACP should be allocated first from an internal ACP pool  and
        overflow  to  system  pool only if allocation fails.  One way to
        minimize system pool usage is to use the window block  to  point
        to  the  internal  ACP  data  structures,  allowing  I/O process
        structures to be mapped on a process basis  instead  of  keeping
        all  information in the window block.  Similarly, volume control
        blocks can point to information in the ACP pool  which  is  used



DATA STRUCTURES                                                 PAGE 2-8



        only by the ACP.



        2.5  OTHER DATA STRUCTURES


             The structures mentioned so far are the key  structures  to
        ACP's.  Other structures an ACP may need to use include the Task
        Control Blocks (TCB), task headers, and Partition Control Blocks
        (PCB).   Depending  on the application, any and all RSX-11M data
        structures may be used by an ACP.

             One important structure to an ACP is its own TCB.   An  I/O
        request  is  queued  to  an ACP by placing it in the ACP receive
        queue.  The ACP dequeues the  I/O  packet  by  getting  its  TCB
        address  and  removing  an  entry  from  the receive queue.  The
        technique for this operation will be shown later.














                               CHAPTER 3

                             ACP CHECKLIST




             ACP implementation is  a  paradox.   ACP's  are  integrally
        coupled  to  the  executive.   It  appears  that a comprehensive
        knowledge of the RSX-11M design philosophy, data structures, and
        executive  code  is  needed to implement an ACP.  However, after
        implementing an ACP, it is obvious  that  the  coupling  to  the
        executive  is loose, logical, and straightforward.  It is simple
        to interface an ACP to RSX-11M;  any difficulties come from  the
        internal ACP design.

             This chapter walks through the design of an UCP-style  ACP.
        In  order  to  keep the emphasis on the executive/ACP interface,
        the example ACP serves no  useful  function.   Rather,  the  ACP
        merely  demonstrates the functionality available to an ACP.  The
        chapter emphasizes the empirical rules that apply to ACP design.
        Later   material  will  develop  the  rationale  for  the  logic
        presented here.


                                      NOTE

             Included with the distribution of this manual are  the
             sources for the sample ACP, its associated driver, and
             the enable and disable task.  It would  be  useful  to
             obtain a listing or the sources and refer to them when
             studying this material.





        3.1  QIO DESIGN


             The first step in ACP design is to decide what I/O services
        the  ACP  will provide.  It is assume the nature of the services
        needed is known;  these fall out of the reasons an  ACP  is  the
        chosen  solution.   This  section  deals  with selecting the I/O
        function codes to be used, the format of the I/O parameters  for
        each function, and what relationships will the user I/O requests



ACP CHECKLIST                                                   PAGE 3-2



        have to each other.

             The example ACP supports five user  functions.   The  first
        function  creates  an  I/O process.  Another function terminates
        the process.  Two other functions perform input  and  output  to
        the  process.   The  last  function  is  a control function to a
        created process.   The  sample  ACP  services  the  requests  by
        outputting  a  message  to the console terminal that the request
        was processed and returns success.  The driver serviced  by  the
        ACP supports two I/O requests, read and write logical block.



        3.1.1  Function Code Selection


             The choice of I/O function codes is fairly straightforward.
        If  the  ACP  is emulating F11ACP for a new device, the Files-11
        QIO functions will be used.  If the ACP will provide unique  I/O
        services, new QIO codes should be chosen.

             The latter  is  the  case  with  the  sample  ACP.   It  is
        advantageous  not  to  redefine  existing I/O codes because this
        could have undesirable effects if I/O is directed to  the  wrong
        device.   For  the sample ACP, the I/O function code 31(10) will
        be used for all user requests.   The  advantage  of  using  this
        function  code  is  that  it is the least used by Digital device
        drivers and is not  used  by  any  Digital  ACP.   The  function
        modifier  field  will  be  used  to  differentiate  the separate
        requests.  The following codes will be assigned:

                  IX.CRE 037,000 Create process
                  IX.CLO 037,001 Terminate process
                  IX.PUT 037,002 Output to process
                  IX.GET 037,003 Input from process
                  IX.CTL 037,004 Process control


             ACP's also typically service ACP control functions such  as
        mount  and dismount ACP, and abort process.  The sample ACP will
        use the traditional I/O function codes for these services:

                  IO.MOU 005,000 Mount ACP
                  IO.DMO 006,000 Dismount ACP
                  IO.CLN 007,000 Abort I/O process

        The IO.MOU and IO.DMO symbolics  are  not  defined  by  Digital.
        However,  tradition  has used these symbolic names and values as
        local definitions.  The IO.CLN symbolic is defined and the value
        must be associated with this function.

             Finally, the function codes for the driver must be  chosen.
        For  the  sample driver, the traditional read and write function



ACP CHECKLIST                                                   PAGE 3-3



        codes are used, IO.RLB and IO.WLB.



        3.1.2  I/O Parameter Selection


             The next step in designing the QIO's is to  decide  on  the
        format  of  the  I/O parameters to be used for each I/O request.
        Because ACP functions are processed uniquely,  you  have  almost
        complete  freedom  in  this  area.   However, the ACP and driver
        implementations  will  depend  heavily  on  the  choice  of  I/O
        parameters  and the format chosen for each I/O request.  This is
        a critical area in the design process.

             The parameters for the sample ACP I/O  requests  have  been
        chosen  mostly to reflect some of the more common features found
        in ACP parameter processing.  The following is  the  format  for
        each  request.   In  order  to  keep  the logic simple, the same
        parameter format is  used  for  each  I/O  function.   The  only
        difference  between  functions is whether a particular parameter
        is required or not present (zero) for the function.

             Parameter #1 - If present,  the  parameter  is  the  output
                  buffer  address.   Byte  alignment  is allowed for the
                  buffer

             Parameter #2 - If parameter #1 is present,  this  parameter
                  is  the  size of the output buffer in bytes.  The size
                  may be byte aligned.

             Parameter #3 - If  present,  the  parameter  is  the  input
                  buffer  address.   Byte  alignment  is allowed for the
                  buffer.

              Parameter #4 - If parameter #3 is present, this  parameter
                  is the size of the input buffer.  The size may be byte
                  aligned

              Parameter #5 - If present, the parameters  is  the  access
                  control  value.  The parameter has legal values from 0
                  to 3.  A zero indicates no process I/O is allowed.   A
                  value  of  one  indicates IX.PUT functions are allowed
                  and a value of  two  indicates  IX.GET  functions  are
                  allowed.  A value of three allows both type of process
                  I/O

             Parameter #6 - This parameter is never user and must always
                  be zero.

             The following table maps what I/O parameters  are  required
        (R) and illegal (blank) for the five ACP I/O requests:




ACP CHECKLIST                                                   PAGE 3-4



                  I/O Code | P1 | P2 | P3 | P4 | P5 | P6 |
                  ---------|----|----|----|----|----|----|
                  IX.CRE   |    |    |    |    | R  |    |
                  ---------|----|----|----|----|----|----|
                  IX.CLO   |    |    |    |    |    |    |
                  ---------|----|----|----|----|----|----|
                  IX.PUT   | R  | R  |    |    |    |    |
                  ---------|----|----|----|----|----|----|
                  IX.GET   |    |    | R  | R  |    |    |
                  ---------|----|----|----|----|----|----|
                  IX.CTL   |    |    |    |    | R  |    |
                  ---------|----|----|----|----|----|----|



        3.1.3  Relationship Between I/O Requests


             The final step in QIO design is to decide the  relationship
        between  I/O  requests.  The typical requests serviced by an ACP
        have relationships defined by the I/O process.  For example,  it
        would  be  illegal to perform an input before the I/O process is
        established.  The general rules that must be applied to each ACP
        I/O request are as follows:

             1.  Must the ACP be mounted to service the  request?   This
                 rule applies to all functions serviced by the ACP.  I/O
                 request serviced by the driver may be allowed if no ACP
                 is  mounted.   If  an  ACP  is  mounted,  I/O  requests
                 serviced  by  the  driver  may  only  be  allowed  from
                 privileged tasks.

             2.  Must the ACP not be marked for dismounting  to  service
                 the  request?   If an ACP is marked for dismounting but
                 has  not  yet  completed  the  dismount,  no  new   I/O
                 processes  should be allowed.  However, all current I/O
                 processes should be allowed to run to completion.

             3.  Must an I/O  process  be  established  to  service  the
                 request?   This rule applies to functions which the ACP
                 will map to an I/O process.  Typically, input,  output,
                 and  terminate  process  functions  cannot  be serviced
                 until the I/O process is established.

             4.  Must an I/O process not be in  effect  to  service  the
                 request?  This is the reverse of the above rule.  A new
                 process cannot be created until  the  previous  process
                 has terminated.


             Any other rules that make sense  for  your  design  may  be
        applied.   In the case of the example ACP, the only special rule
        applies to the IX.PUT and IX.GET functions.  When the process is



ACP CHECKLIST                                                   PAGE 3-5



        created  using  the  IX.CRE function, parameter #5 specifies the
        type of process I/O allowed (see  section  3.1.2).   The  access
        parameter can be changed by the IX.CTL function.

             The following table summarizes how the  four  common  rules
        listed  above  (R1-R4)  and  the  one special case rule (SC) are
        applied to each ACP function.  An entry of "A" means the rule is
        applied.   Otherwise,  the particular rule does not apply to the
        function.

                  I/O Code | R1 | R2 | R3 | R4 | SC |
                  ---------|----|----|----|----|----|
                  IX.CRE   | A  | A  |    | A  |    |
                  ---------|----|----|----|----|----|
                  IX.CLO   | A  |    | A  |    |    |
                  ---------|----|----|----|----|----|
                  IX.PUT   | A  |    | A  |    | A  |
                  ---------|----|----|----|----|----|
                  IX.GET   | A  |    | A  |    | A  |
                  ---------|----|----|----|----|----|
                  IX.CTL   | A  |    | A  |    |    |
                  ---------|----|----|----|----|----|



        3.2  DEVICE DATA BASE DESIGN


             After it is determined how a user program will interface to
        the  ACP, the next step is to add ACP support to the device data
        structures.  This  is  a  simple  step.   The  basic  structures
        documented  in  the  Guide to Writing an I/O Driver manual still
        apply.  Adding ACP support to the driver merely involves setting
        up some of the fields not normally used.

             Only the device control block and unit control  block  need
        to  be  considered  when  adding  ACP  support to a driver.  The
        status control block (SCB) is strictly driver related.



        3.2.1  Device Control Block


             The Device Control Block (DCB) is used to name  the  device
        and control the executive processing of I/O packets.  For an ACP
        supported device, the documentation on pages 4-7 to 4-15 of  the
        Guide  to  Writing  an  I/O Driver applies.  The additional step
        necessary for the support of the ACP is to decide on how the ACP
        functions  will be processed and therefore, how the DCB function
        masks should be set up.

             If a DCP  or  FCP  style  ACP  is  being  implemented,  the



ACP CHECKLIST                                                   PAGE 3-6



        functions  designated  for  the ACP will be marked as "legal and
        ACP" in the mask field.  If a  UCP  is  being  implemented,  the
        functions will be marked as "legal and control".

             The following shows how the DCB function masks are  set  up
        for  the  sample  ACP.  Note how the IO.RLB and IO.WLB functions
        are marked as  legal  only,  implying  that  the  functions  are
        transfer  functions  and  will  be  handled  by the driver.  The
        IX.???  functions are marked as "legal and control".  Also  note
        that  the  special  IO.CLN  function  is  marked  as  "legal and
        control" but the mount and dismount requests are not included in
        the  DCB  masks.  These functions are queued directly to the ACP
        by the enable and disable tasks and are  not  processed  by  the
        executive.

                 .WORD   000206  ;Legal   (IO.CLN, IO.WLB, IO.RLB)
                 .WORD   000200  ;Control (IO.CLN)
                 .WORD   000000  ;No-op
                 .WORD   000000  ;ACP
                 .WORD   100000  ;Legal   (IX.???)
                 .WORD   100000  ;Control (IX.???)
                 .WORD   000000  ;No-op
                 .WORD   000000  ;ACP



        3.2.2  Unit Control Block


             The Unit Control Block is the key structure as far as ACP's
        are  concerned.  The basic UCB design is documented in the Guide
        to Writing an I/O Driver  Manual  (pages  4-19  to  4-26).   The
        fields  in the UCB that must be properly set up for ACP's are as
        follows:

             U.CTL - Unit Control Masks.  The bit masks  in  this  field
                     will   typically   be   set  up  for  the  driver's
                     requirements.  The one bit which may be  turned  on
                     for  ACP  support  is  UC.QUE.   This bit tells the
                     executive to call the driver with  the  I/O  packet
                     without  queuing first.  This is the mechanism used
                     for FCP and UCP style ACP's that allows the  driver
                     to specially process the ACP I/O packets.

             U.STS - Unit Status Masks.  Some of the bit masks  in  this
                     field  are  used to mark whether an ACP is mounted,
                     foreign, and/or marked  for  dismount.   The  field
                     will  be  initialized as not mounted (US.MNT=1) for
                     all ACP's and foreign (US.FOR=1)  for  FCP's.   The
                     ACP  is  then responsible for properly handling the
                     states of these bits and the  marked  for  dismount
                     bit (US.MDM).



ACP CHECKLIST                                                   PAGE 3-7



                                            NOTE

                          The sense of the US.MNT mask is  opposite
                          to most masks.  The bit is set if the ACP
                          is not mounted and cleared when  the  ACP
                          is mounted.



             U.CW1 - Device Characteristics Word #1.  The word  contains
                     bit  masks which define the device characteristics.
                     The masks are used by RSX-11M  to  properly  handle
                     different devices.  For example, FCS uses this word
                     to decide whether disk or  terminal  I/O  is  being
                     performed.

                     For ACP's, the DV.MNT bit signifies that an ACP can
                     be  mounted  for the device.  The DV.COM and DV.F11
                     bits are used by  RSX-11M  MOU  and  DMO  tasks  to
                     decide  what  ACP  should  be mounted.  If a DCP is
                     being implemented, the characteristics  that  apply
                     to  currently  supported  Digital devices should be
                     used for the new device/ACP.

                     If an FCP or UCP is being implemented, only  DV.MNT
                     needs  to be set.  In addition, the low byte of the
                     word should be set to accurately reflect the nature
                     of  the  device  itself.   A description of the bit
                     masks for the U.CW1 field can be found in  Appendix
                     B.

             U.ACP - ACP TCB Address.  This word is an extension to  the
                     normal  UCB  used  by  RSX-11M.   The  word must be
                     allocated for devices which are connected to  ACP's
                     and  follows  the  U.CNT  field.   When  an  ACP is
                     enabled, the word will contain the address  of  the
                     ACP's Task Control Block.  This the the TCB the I/O
                     packet will be queued to when it  is  sent  to  the
                     ACP.  U.ACP is initialized when the ACP is enabled.

             U.VCB - Volume Control Block Address.  This word is also an
                     extension to the normal UCB and follows U.ACP.  The
                     word contains the address  of  the  volume  control
                     block.  It is initialized when the ACP is enabled.

             The following code segment  is  the  UCB  for  the  example
        device.  The values are set for a UCP-style ACP implementation.



ACP CHECKLIST                                                   PAGE 3-8



                 .IF DF  M$$MUP

                 .WORD   0       ;(U.OWN ) OWNING TERMINAL UCB ADDRESS

                 .ENDC

        .AC0::                   ;REF. LABEL.
                 .WORD   .ACDCB  ;(U.DCB ) POINTER TO DCB
                 .WORD   .-2     ;(U.RED ) REDIRECT UCB POINTER
                 .BYTE   UC.QUE  ;(U.CTL ) CONTROL FLAGS
                 .BYTE   US.MNT  ;(U.STS ) STATUS FLAGS
                 .BYTE   0       ;(U.UNIT) UNIT NUMBER
                 .BYTE   US.RED  ;(U.STS2) STATUS FLAGS
                 .WORD   DV.MNT  ;(U.CW1 ) DEVICE CHARACTERISTICS
                 .WORD   0       ;(U.CW2 ) DEVICE CHARACTERISTICS
                 .WORD   0       ;(U.CW3 ) DEVICE CHARACTERISTICS
                 .WORD   1000    ;(U.CW4 ) BUFFER SIZE
                 .WORD   $AC0    ;(U.SCB ) SCB POINTER
                 .WORD   0       ;(U.ATT ) ATTACH WORD
                 .WORD   0,0     ;(U.BUF ) BUFFER RELOCATION ADDRESS
                 .WORD   0       ;(U.CNT ) BUFFER SIZE (BYTES)
                 .WORD   0       ;(U.ACP ) ACP TCB ADDRESS
                 .WORD   0       ;(U.VCB ) VCB ADDRESS



        3.3  ACP DATA BASE DESIGN


             The final step  in  the  general  ACP  design  is  the  ACP
        specific  data bases.  Here, the ACP implementation has complete
        freedom as RSX-11M imposes very few rules.



        3.3.1  Volume Control Block


             One data structure  common  to  all  ACP's  is  the  volume
        control block.  This structure is allocated from the system pool
        when an ACP is mounted for a device.  The VCB is linked  to  the
        UCB by storing its address in U.VCB.

             The VCB is used to hold all unit specific  information  for
        the  ACP.   The ACP philosophy allows several devices to use the
        same  ACP.   Typically,  the  ACP  treats  each  device  as   an
        independent  entity;   therefore,  a separate data base is need.
        The VCB serves this purpose.

             The length and format of VCB's is ACP dependent.  Only  the
        first  word  has  a common usage.  This is the transaction count
        and is used to count the number of outstanding I/O requests  and
        processes  for the device.  When the VCB is allocated, this word



ACP CHECKLIST                                                   PAGE 3-9



        should be zeroed.



        3.3.2  Window Block


             The other structure common to  most  ACP's  is  the  window
        block.   This structure is completely ACP dependent and need not
        be even allocated from pool.  Window blocks are  the  structures
        used  to  keep I/O process-dependent information.  The window is
        allocated when the process is created by the ACP.   The  address
        of  the window is stored in the second LUN word of the LUT table
        for the task which  issued  the  I/O  request.   The  LUT  table
        address  can  then be retrieved from future I/O packets from the
        same lun, and from it, the window address.

             Window blocks contain whatever information is needed by the
        ACP  to  map the individual I/O request to the I/O process.  For
        example, F11ACP windows contains the mapping information between
        the  logical  blocks  of  a  file  and the physical disk blocks.
        Window blocks also typically point to other data structures used
        by the ACP and form the key structure for the I/O process.



        3.3.3  Other Data Structures


             Finally, ACP's may create new  data  structures.   Any  ACP
        implementation  should  keep  the  system  pool utilization to a
        minimum.  One method of accomplishing this is to use an ACP task
        pool  for  the structures used only by the ACP and overflow into
        the system pool only when the internal pool is  exhausted.   The
        VCB and window blocks, which are usually in the system pool, are
        kept short and point to the new data structures.  This technique
        is used by F11ACP for File Control Blocks.



        3.4  DEVICE DRIVER IMPLEMENTATION


             Once the design of the  QIO  requests  and  data  bases  is
        finished,  the  next step is to implement support for the ACP in
        the executive (DCP) or device driver (FCP, UCP).   This  section
        follows the example UCP, so the special support will be added to
        the sample device driver.

             In most cases, the ACP is being  used  with  a  new  device
        driver.  If this is the case, the recommendation is to implement
        and test the device driver without ACP support.  Once the driver
        is functional, it is a small step to add the ACP.



ACP CHECKLIST                                                  PAGE 3-10



             If the implementation uses a DCP,  the  driver  is  usually
        unaware  of  the  ACP;   not driver modifications are necessary.
        The ACP packet processing is done in  DRQIO.   In  the  case  of
        FCP's  and UCP's, the code to support the special processing for
        the ACP I/O  packets  is  in  the  driver.   In  any  case,  the
        functionality  provided  by  the code is the same.  The next two
        subsections discuss the considerations on driver entry  and  ACP
        packet processing.



        3.4.1  Driver Entry


             For FCP's and UCP's, the driver is called directly from the
        executive  and  the  I/O packet is not queued, because UC.QUE in
        the UCB is set.  The driver logic then determines if the  packet
        is  for  the  ACP  or  for itself.  If the latter, the packet is
        queued to the SCB and  the  driver  calls  $GTPKT  to  correctly
        sequence  I/O  service.  The driver then processes the packet in
        the typical  fashion.   For  ACP  packets,  the  special  packet
        processing discussed in the next section is used.

             The following  code  segment  illustrates  how  the  driver
        works.   The  example  is  taken from the driver for the example
        presented so far.
         
        ;
        ; DRVINI IS CALLED WHENEVER A I/O REQUEST IS ISSUED TO
        ; THE SAMPLE DRIVER. THE PACKET IS NOT QUEUED AND THE
        ; FOLLOWING REGISTERS ARE SET:
        ;
        ;	R1 = I/O PACKET ADDRESS
        ;	R4 = SCB ADDRESS
        ;	R5 = UCB ADDRESS
        ;
        DRVINI:	MOVB	I.FCN+1(R1),R0	;GET FUNCTION CODE
        	CMPB	#IX.ACP/400,R0	;IS THIS A ACP REQUEST?
        	BEQ	DRVACP		; IF EQ - YES, GO PROCESS
        	CMPB	#IO.CLN/400,R0	;IS THIS A IO.CLN REQUEST?
        	BEQ	DRVACP		; IF EQ - YES, GO PROCESS
        ;
        ; QUEUE PACKET TO DEVICE AND GET NEXT PACKET.
        ;
        DRVPKT:	MOV	U.SCB(R5),R0	;GET DEVICE QUEUE LISTHEAD
        	CALL	$QINSP		;QUEUE PACKET TO DEVICE
        	CALL	$GTPKT		;GET NEXT PACKET
        	BCC	DRVSRV		; IF CC - SERVICE REQUEST
        	RETURN			;NO PACKET, RETURN



ACP CHECKLIST                                                  PAGE 3-11



        3.4.2  Driver Packet Processing


             Once the driver decides the  packet  is  for  the  ACP,  it
        performs  the special packet processing and queues the packet to
        the ACP.  There are any number of special checks that  could  be
        performed  and  any number of methods to perform the check.  The
        Digital approach used in DRQIO is to use polish-driven  routines
        to  perform  each  check.   This allows a list of routines to be
        specified for each type of I/O function.  The same  approach  is
        used in the sample driver.

             More important than the technique used to process  the  I/O
        packet  is  the  type  of  processing  performed.   The  typical
        processing performed before queueing the packet to  the  ACP  is
        listed  below  (the order of the list is basically the order the
        items would be applied;  however, this is not  hard  and  fast).
        The list of items below are typical of the processing applied by
        the executive for DCP style ACP's.  The example driver code also
        demonstrates  all  of  the below operations in its processing of
        the  ACP   functions.    The   rule   which   decides   if   the
        executive/driver  or  the  ACP  should perform the processing is
        whether the processing needs to be performed in the  context  of
        the  task  which  issued  the  I/O request.  If not, the ACP can
        perform  the  operation.   Otherwise,  the  operation  must   be
        performed by the executive for DCP's and by the driver for FCP's
        and UCP's.  Once a packet is queued to an ACP, an  indeterminate
        amount of time and events may happen before the ACP dequeues and
        services the request.

             1.  The function code is verified for legal  ACP  function.
                 The executive only checks the high byte when processing
                 function  codes,  the  driver  needs   to   check   any
                 subfunction fields.

             2.  The UCB is checked to see if the ACP is mounted for the
                 device.

             3.  For functions which create  I/O  process,  the  UCB  is
                 checked to see if the ACP is marked for dismount.

             4.  For functions which create I/O processes,  the  logical
                 unit  table  is  checked to see if a process is already
                 active for the lun.

             5.  For functions which must be mapped to an  I/O  process,
                 the  logical  unit table is checked to see if a process
                 is active for the lun.

             6.  For functions which require a specific relationship  to
                 another,  the  window is checked to see if the function
                 is legal for the current state of the I/O process.



ACP CHECKLIST                                                  PAGE 3-12



             7.  If specific parameters are not used  or  required,  the
                 I/O  parameters  are checked to see if they are zero or
                 non-zero.

             8.  Any user task addresses are address checked.

             9.  Any user task addresses are relocated so  the  ACP  can
                 map the user task.

             10. In some cases, user buffers are copied to  system  pool
                 buffers.   This  allows  the  ACP to access information
                 without mapping the  user  task.   This  is  especially
                 applicable to attribute lists.

             11. The volume transaction count is incremented.

             12. If the ACP requires no further I/O  request  be  issued
                 from  the  lun,  the  lun  is  locked.  This is done by
                 setting the low bit of  the  second  lun  word  in  the
                 logical unit table.

             13. The packet is queued to the ACP and the  ACP  scheduled
                 for  execution.   This  is  a simple operation which is
                 done by calling the executive routine  $EXRQP  with  R0
                 set to the ACP TCB address and R1 set to the I/O packet
                 address.




        3.5  ACP IMPLEMENTATION


             Once  the   driver   interface   is   finished,   the   ACP
        implementation  can  begin.   Some of the implementation will be
        common to all ACP's.   However,  most  will  be  unique  to  the
        application being addressed.



        3.5.1  ACP Packet Dequeuing


             One common function of all ACP's is the  dequeuing  of  the
        I/O  packets  queued  to  it  from the executive.  The executive
        passes I/O packets to ACP's by linking them to the ACP's receive
        queue  and  scheduling the ACP for execution.  The ACP retrieves
        the packet by entering system  state  and  dequeuing  the  first
        entry from its receive queue.

             The following code segment is taken from  the  example  ACP
        and  illustrates the basic root of an ACP.  On task startup, the
        ACP initializes itself.  Once  done,  it  enters  a  loop  where



ACP CHECKLIST                                                  PAGE 3-13



        packets  are  dequeued  and processed.  If no work is found, the
        ACP stops itself.  When the executive queues another packet, the
        ACP will be rescheduled and can repeat the loop.

        NULACP::			;REF. LABEL
        ;
        ; GO PERFORM THE INITIALIZATION PROCESS.
        ;
        	CALL	ACPINI		;INITIALIZE ACP
        ;
        ; ENTER SYSTEM STATE AND CHECK RECEIVE QUEUE.
        ;
        1000$:	CLR	R1		;MARK NOTHING DEQUEUED
        	CALL	$SWSTK,2000$	;;ENTER SYSTEM STATE
        	MOV	$TKTCB,R0	;;GET OUR TCB ADDRESS
        	ADD	#T.RCVL,R0	;;POINT TO RECEIVE QUEUE LISTHEAD
        	CALL	$QRMVF		;;REMOVE QUEUE ENTRY
        	BCS	1100$		;; IF CS - NO ENTRY, STOP
        	MOV	R1,4(SP)	;;RETURN PACKET ADDRESS
        	RETURN			;;RETURN TO TASK STATE
        ;
        ; STOP TASK. WHEN WOKE, RETURN TO TASK STATE.
        ;
        1100$:	CALLR	$STPCT		;;STOP CURRENT TASK (US)
        ;
        ; IF NO ENTRY DEQUEUED,  LOOP.
        ;
        2000$:	MOV	R1,R3		;WAS ENTRY FOUND?
        	BEQ	1000$		; IF EQ - NO, CONTINUE LOOP
        ;
        ; DISPATCH ON I/O FUNCTION AND CALL PROCESSING ROUTINE.
        ;
        	MOV	I.UCB(R3),R5	;GET UCB ADDRESS
        	<function dispatch code>
        ;
        ; WHEN FINISHED, CHECK FOR DISMOUNT PENDING.
        ;
        4000$:	BITB	#US.MDM,U.STS(R5) ;IS A DISMOUNT PENDING?
        	BEQ	1000$		; IF EQ - NO, LOOP THROUGH QUEUES
        	CALL	ACPMDM		;TRY TO COMPLETE DISMOUNT
        	BR	1000$		; NO LUCK - LOOP THROUGH QUEUE
         
        	.END	NULACP



        3.5.2  ACP Packet Processing


             The real work of an ACP takes place  after  the  packet  is
        dequeued.   How  ACP's process packets is strictly a function of
        the individual ACP.  The sample  ACP  illustrates  some  of  the
        common  types of processing that may take place, such as reading



ACP CHECKLIST                                                  PAGE 3-14



        and writing buffers in the user task.   However,  most  of  code
        implemented to service the packets will be of your own creation.



        3.5.3  ACP Packet Termination


             The final step an ACP  takes  in  processing  a  packet  is
        packet  termination.  This is done by calling the $IOFIN routine
        in the executive.  This routine, rather than  the  $IODON/$IOALT
        routines, should be used since the driver is not busy.



        3.6  TASK TERMINATION


             One important, but often overlooked, feature  of  ACP's  is
        properly   handling  of  user  task  termination.   The  RSX-11M
        executive will not let a task exit  until  all  outstanding  I/O
        requests  are  terminated  and all outstanding I/O processes are
        destroyed.  The former is typically a function  handled  by  the
        I/O driver.  In the latter case, the executive checks the second
        lun word for each entry in the logical unit table.  If the value
        is  non-zero,  an  I/O  process  is  assumed.   The  value would
        normally be the window block address.

             When  a  non-zero  second  lun  word  is  encountered,  the
        executive  constructs  a  IO.CLN  packet and issues it as if the
        task had issued the QIO from the lun with  the  outstanding  I/O
        process.   The ACP is expected to abort the I/O process and zero
        the second lun word entry.

             The logic of the ACP must  be  able  to  handle  an  IO.CLN
        function  no  matter  what  the state of the I/O process.  It is
        impossible to predict when a task will encounter  an  unexpected
        trap,  be  aborted  by the operator, or exit without terminating
        all I/O processes.



        3.7  ACP ENABLING


             Two final  steps  remain  after  the  ACP  and  driver  are
        finished.  A mechanism must be implemented to enable and disable
        the ACP for the device.  The common name for these operations is
        mount  and dismount.  There are a variety of methods that can be
        used.  These are discussed in detail in chapter 6.

             ACP mounting is really quite  simple.   The  complexity  of
        Digital's MOU task comes from the multiple functions it provides



ACP CHECKLIST                                                  PAGE 3-15



        and the details  of  actually  performing  a  Files-11  or  ANSI
        magtape  mount.   The  essential steps that must be accomplished
        when an ACP  is  mounted  are  listed  below.   The  first  list
        contains  steps typically performed by a separate enabling task.
        The sample task ENA demonstrates each of the steps.

             1.  If wanted, get any "mount-time" options from the  mount
                 command  line.   It  may be necessary to allow operator
                 specified options to provide greater ACP flexibility.

             2.  Check if the device is mountable (DV.MNT=1).

             3.  Check  if  the  device   is   not   currently   mounted
                 (US.MNT=1).

             4.  Check  if  the  device  is  not  marked  for   dismount
                 (US.MDM=0).

             5.  Allocate the VCB from system pool and store its address
                 in U.VCB of the UCB.

             6.  Search the task directory for the ACP task and get  its
                 TCB address.

             7.  Check the found task is an ACP (T3.ACP=1).

             8.  Store the ACP's TCB address in U.ACP of the UCB.

             9.  If necessary, add an entry to the mounted volume  list.
                 This  will  typically  not be required for user-written
                 ACP's.

             10. Schedule the ACP task for execution.  The ACP will then
                 typically  start  with  its  initialization code.  This
                 step is traditionally combined with  a  IO.MOU  request
                 being  queued  to  the  ACP.  This request contains the
                 "mount-time"  parameters  for  the  ACP.   The   IO.MOU
                 request  is not necessary if no information needs to be
                 communicated to the ACP.

             11. If  the  IO.MOU  I/O  request  was  issued,  wait   for
                 success/failure.   If failure, output an error message.
                 Otherwise, just exit.


             The remaining steps in the mounting process  are  typically
        performed by the ACP.  These steps are as follows:

             1.  If an IO.MOU request was queued, dequeue  it  from  the
                 receive queue and process the parameters.

             2.  Count the device mounted.  This is usually an  internal
                 ACP counter.



ACP CHECKLIST                                                  PAGE 3-16



             3.  Perform any device I/O necessary for the ACP to  become
                 active.

             4.  Mark the device mounted (US.MNT=0).

             5.  Enter the ACP main loop.


             The steps above are followed by  the  sample  ACP  and  ENA
        task.   This  code  can  be  used  as  a  template  for your ACP
        implementation, or one of the alternate approaches discussed  in
        chapter  6  can be used.  In any case, in order for an ACP to be
        successfully mounted, the following must have happened:

             1.  The VCB has been allocated and its  address  stored  in
                 U.VCB.

             2.  The ACP's TCB address must have been stored in U.ACP.

             3.  The ACP must have been marked as mounted (US.MNT=0).

             4.  The ACP  must  be  active  and  ready  to  receive  ACP
                 functions.




        3.8  ACP DISABLING


             The last step in the checklist  is  to  implement  the  ACP
        disabling (dismount) mechanism.  If the system will not function
        without the ACP, no dismount mechanism other than rebooting  may
        be  needed.  However, usually a dismounting method will be used.
        The following steps are usually accomplished by a dismount task.
        The sample DIS task demonstrates these steps.

             1.  Check if the device is mountable (DV.MNT=1).

             2.  Check if the device is mounted (US.MNT=0).

             3.  Check if the device  is  already  marked  for  dismount
                 (US.MDM=1).

             4.  Mark the device for dismount (US.MDM=1).

             5.  Construct and queue an IO.DMO request to the ACP.

             6.  Wait for completion of the IO.DMO and exit.


             When an ACP  receives  a  dismount  request,  it  typically
        performs the following steps.



ACP CHECKLIST                                                  PAGE 3-17



             1.  Marks a dismount is pending for the device.   This  can
                 already  be considered done as the US.MDM bit is set in
                 the UCB.

             2.  Return the IO.DMO request.


             After a dismount becomes pending, the ACP  then  waits  for
        all  activity  to the unit to cease.  This means no I/O requests
        are outstanding and all I/O  processes  have  terminated.   When
        this occurs, the following steps are taken.

             1.  Mark the device dismounted (US.MNT=1).

             2.  Mark the dismount complete (US.MDM=0).

             3.  Perform any device I/O necessary to  deaccess  the  ACP
                 from the device.

             4.  Return the VCB to the pool and zero U.VCB.

             5.  Zero the U.ACP word in the UCB.

             6.  When all mounted units are dismounted, exit the ACP.




        3.9  CHECKLIST SUMMARY


             This chapter has  described  all  the  steps  necessary  to
        implement  an ACP.  The checklist presented here was followed to
        implement the sample ACP, its driver, and the ENA and DIS tasks.
        These  routines  can  be used as a basis for a user-written ACP,
        leaving only the job of solving the actual problem.

             It is usually easiest to implement a UCP.  This involves no
        modifications to the executive and is a straightforward approach
        once  the  checklist  is  followed.   For  the   more   advanced
        programmer,  the  DCP  and FCP approaches may offer advantanges.
        However, you are at the mercy of Digital with  regard  to  their
        future executive implementations.

             The remaining chapters discuss the material presented  here
        in  more  detail.   In  particular,  they present the philosophy
        behind the actual operations.














                               CHAPTER 4

                           ACP/TASK INTERFACE




             A user task interfaces to an ACP using the  QIO  directive.
        The  I/O  requests  can be issued directly from the task or from
        one of the logical I/O service libraries:   FCS  or  RMS.   This
        chapter  discusses  the  ACP/task  interface  from the first two
        perspectives.  The RMS sources are unavailable  to  the  author.
        However,  the  approach  used  for  adding  an new ACP to FCS is
        expected to apply to RMS.



        4.1  QIO INTERFACE


             The most common way to interface to a user-written  ACP  is
        the  QIO  directive.  In an RSX-11M system, all I/O is requested
        using this directive, including I/O from ACP's.  Adding  support
        for  I/O  service  from a user-written ACP is the same as adding
        new  QIO  directives  for  a  user-written  driver.   The   only
        decisions necessary are what function codes the ACP will service
        and the I/O parameters that will be used for each function.

             The choice of I/O function codes is  simple.   If  existing
        Digital  function  codes  apply  to  the new ACP, they should be
        used.  When using existing codes, the I/O parameters should also
        be the same as the current Digital format.  Then, no errors will
        occur when I/O is directed to different devices.

             However, the more typical case is that the new ACP will  be
        implementing   new   functionality.   In  this  case,  the  less
        frequently used I/O function codes should be considered.   These
        are the codes from 25-31(10).  The subfunction field can be used
        to actually distinguish between separate ACP functions.

             Because ACP's typically use special processing for the  I/O
        parameters,  there  is  a great deal of freedom in their layout.
        The parameters can be as complex as needed to pass  and  receive
        information from the ACP.

             One common technique used by ACP's to allow passing of many



ACP/TASK INTERFACE                                              PAGE 4-2



        parameters  are  attribute lists.  An attribute list is a buffer
        which contains attribute descriptors.  Each descriptor describes
        a separate parameter to the ACP.  A typical attribute descriptor
        consist of a code to identify the attribute, the address of  the
        actual  attribute,  and  size  of  the  attribute.  When the I/O
        request is processed,  the  special  processing  code  maps  the
        attribute list and individually address checks and relocates the
        attribute addresses.

             This technique is used  by  F11ACP  to  allow  reading  and
        writing  of  the  various  fields  in the file header.  When the
        attribute list is processed, a  buffer  is  allocated  from  the
        system  pool and the attribute code and size are copied from the
        user task.  The attribute buffer is relocated and the relocation
        bias and displacement are stored in the system buffer.  When the
        I/O packet is received by F11ACP, it can use the information  in
        the system buffer to read and write the attribute buffers in the
        user task.  Appendix D contains a detailed  description  of  the
        Files-11  attribute  list processing.  Also see the DRQIO module
        for an example of how the executive processes attribute lists.



        4.2  FCS INTERFACE


             In some special cases, interfacing an user-written  ACP  to
        FCS  can result in significant advantages.  FCS is the component
        of RSX-11M that provides device  independence  and  record  I/O.
        FCS  examines  the device characteristics of the assigned device
        and issues I/O appropriate for the type of device.  For example,
        if a terminal is the assigned device, a PUT$ request will result
        in a IO.WVB being issued  to  the  terminal.   However,  if  the
        device  is a disk, FCS will block the record to the virtual disk
        block.

             By adding support for new ACP's to FCS, users  can  perform
        I/O  from FCS to the devices supported by the ACP.  In addition,
        the languages and utility  programs  which  use  FCS  will  then
        support  the new device.  For example, Fortran I/O uses FCS.  If
        FCS supports the new ACP, standard Fortran I/O statements  could
        be a powerful method of performing I/O.  The users of the ACP do
        not have to learn any new syntax to use the ACP and its devices.

             Only a fraction of user-written ACP's  are  candidates  for
        interfacing  to  FCS.   The  typical application will involve an
        implementation of an alternate file system.  For example, if  an
        ACP  was  written to support RT-11 disks, interfacing the ACP to
        FCS would allow the standard RSX-11M utilities to directly  read
        and  write  RT-11  files.   Another  possibility is an ACP which
        supports remote I/O.  For  example,  an  ACP  could  implemented
        Digital's  Data  Access  Protocol  (DAP).   If  such  an ACP was
        interfaced to FCS, RSX-11M programs could  transparently  access



ACP/TASK INTERFACE                                              PAGE 4-3



        remote file and devices.

             There are two methods for interfacing a user-written ACP to
        FCS.   If  the  ACP  uses the Files-11 QIO's, the new ACP merely
        needs to emulate the services supplied  by  F11ACP.   With  this
        approach,  little  or  no  modifications would be needed to FCS.
        However, the ACP will probably have to go to  great  lengths  to
        translate the device protocol into Files-11 compatible format.

             The other approach involves modifying FCS to perform unique
        operations  for  the  new  ACP.   Here,  the  goal is to provide
        complete compatibility at the user interface into FCS.  In other
        words,   the   functionality   documented  in  the  RSX/IAS  I/O
        Operations Reference Manual is provided by  the  combination  of
        the modified FCS and the new ACP.  As long as a program does not
        depend on Files-11 specifics, it should function correctly  when
        used with the new ACP.

             There are no hard and fast  rules  which  apply  to  adding
        support  for  a  new  ACP  to  FCS.   The overall approach is to
        examine how FCS operates for current  ACP's  and  modifying  the
        appropriate  points to add logic for the new ACP.  The next four
        subsections comment on some of the basic points.   In  addition,
        Appendix C provides detailed descriptions of each FCS module and
        the various data structures.

             Some  general  rules  are  to  apply  conditional  assembly
        statements   to  all  new  code  and  to  maintain  object-level
        compatibility.  By  conditionalizing  the  new  code,  different
        versions  of  the FCS library can be maintained.  For user tasks
        which do not need to support the new ACP, the  Digital  standard
        version of FCS can be used.  Only tasks requiring the new device
        support  need  to  be  linked  to  the  special   version.    By
        maintaining  object-level compatibility, a task needs only to be
        relinked  to  receive  the  benefits   of   the   new   support.
        Object-level  compatibility  requires that the code generated by
        the  FCS  macros  is  not  changed  by  the  modifications.   In
        particularly,  the space generated for the File Descriptor Block
        and Filename Blocks  should  stay  the  same.   However,  fields
        within  these  data  structures can be redefined by the modified
        FCS for support of the new device.



        4.2.1  File Specification


             The FCS modules can be broken into  four  categories.   The
        first  are  modules  which  are  concerned with parsing the file
        specification  into  the   device,   directory,   and   filename
        components  and  assigning the user lun to the specified device.
        The major modules in this category are the four parsing modules:
        PARSE  (parsing  control),  PARSDV  (parse  device name), PARSDI



ACP/TASK INTERFACE                                              PAGE 4-4



        (parse directory), and PARSFN (parse  filename).   In  addition,
        the  ASSLUN  module assigns the user lun to the specified device
        and reads the device characteristics.  The  auxiliary  directory
        modules  (DIDFND,  DIFND,  GETDI,  GETDID,  GETDIR,  PARDI,  and
        PARDID) process Files-11 directory files.  Finally, the  RSX-11M
        command  scanning  routines (CSI1, CSI2) are used to scan entire
        command lines

             When adding support for a new ACP, the  major  concern  for
        these  modules  is  to  add  support  for  any  new form of file
        specifications and to set up  the  FCS  device  characteristics.
        For  example,  if  adding  network  file  support,  it  would be
        necessary to add a nodename field to the  device  specification.
        If  adding RT-11 support, the routines would have to be modified
        to ignore or declare an error if a directory was specified.

             The key is the fact that the first step  performed  by  FCS
        for  all operations is to assign the lun to the specified device
        and establish the device  characteristics.   The  ASSLUN  module
        performs the assignment and gets the device characteristics.  It
        stores the low byte of the devices U.CW1 field in F.RCTL and the
        device buffer size in F.VBSZ and F.BBSZ.  The important field is
        the device characteristics byte.  This  byte  contains  the  bit
        masks  which  are  examined  by FCS to determine the appropriate
        operation  to  take  for  a  device.   For   example,   if   the
        record-oriented bit (FD.REC) is set, FCS assumes the device is a
        terminal-like device and performs no record  blocking.   If  the
        bit  is  clear,  a  block-oriented  device is assumed (disk) and
        records are block within virtual blocks.  Therefore,  the  first
        step  in  adding  support  for a new ACP is to modify PARSDV and
        ASSLUN to correctly assign  the  new  device  and  to  establish
        device  characteristics  which  will  allow other FCS modules to
        uniquely  identify  the  new  ACP.    Then,   whenever   special
        processing  is  needed  to support the new ACP, the F.RCTL field
        can be tested and the a branch made  to  the  appropriate  code.
        For example, special directory and filename parsing logic can be
        invoked if the device is established as  a  RT-11  disk  volume.
        The  easiest  method  to identify a new type of device is to use
        one of the undefined bits in the F.RCTL field (bits 6 and 7) and
        set the remaining bits as appropriate for the new device.



        4.2.2  File Access


             The next category of  FCS  modules  are  the  various  OPEN
        routines.  FCS supports three methods of opening files:  normal,
        filename block, and file-ID.  The first form calls  the  parsing
        routines  to  setup  the  filename  block  and  then  opens  the
        specified device/file.  The filename block version  assumes  the
        parsing  routines have already been called.  The final form uses
        information from a previous file access  to  directly  open  the



ACP/TASK INTERFACE                                              PAGE 4-5



        file.  No parsing logic is invoked.

             Adding  a  new  ACP  merely  involves  dispatching  at  the
        appropriate  point in the OPEN logic to perform any I/O required
        by the ACP to establish  an  I/O  process.   The  new  logic  is
        responsible  for  returning  the  appropriate information to the
        FDB, particularly the file-attribute  section  (F.RTYP,  F.RATT,
        F.RSIZ,  F.HIBK,  F.EFBK, and F.FFBY).  These fields are used by
        FCS to determine how  records  should  be  processed,  when  new
        blocks  need  to be allocated to the file, and where the logical
        EOF is positioned.  For Files-11, these fields are stored in the
        file header.  FCS retrieves them when an existing file is opened
        and stores the current FDB values when a file is created.

             Unless the new type of device  supports  some  unique  file
        identifier, the open by file-ID mechanism will either have to be
        emulated by the ACP or made illegal.  The  most  common  use  of
        file-ID's  is  by  programs which open a file briefly, close it,
        and reopen it at a later point in time.  The  file-ID  from  the
        first open is saved and reused on the next access.  For example,
        the MACRO assembler uses this technique.  One method for an  ACP
        to   emulate  file-ID's  would  be  to  save  file  names  in  a
        least-recently used buffer or file and assign a  number  to  map
        the  entry.   If an open by file-ID is attempted, the file-ID is
        used to  address  the  table  and  retrieve  the  original  file
        specification.   When  a  new  filename  is  entered, the oldest
        previous entry is destroyed.  In this fashion, the  most  common
        use of file-ID's by RSX-11M utilities can be supported.



        4.2.3  Input/Output


             FCS supports two  forms  of  input/output.   The  first  is
        record  I/O  which  uses the GET$/PUT$ calls.  The other form is
        virtual  block  I/O  and  is  implemented  by  the  READ$/WRITE$
        routines.  The general approach for adding support for a new ACP
        is the same  as  for  the  OPEN  routines:   add  logic  at  the
        appropriate points to test for the new ACP and branch to special
        I/O logic.

             It is important to remember that  FCS  is  the  element  of
        RSX-11M  that  defines  what  is  a  record, not Files-11.  When
        performing record output to a disk, FCS packs the  records  into
        disk   blocks   and  issues  write  virtual  blocks  to  F11ACP.
        Similarly, when  inputting  records  from  a  disk,  FCS  inputs
        virtual   blocks  and  unpacks  the  records  using  the  record
        information it originally provided when the record was  written.
        Most  importantly,  user  programs do not care that block I/O is
        being performed for their record I/O.  They are only  interested
        in the record itself.




ACP/TASK INTERFACE                                              PAGE 4-6



             Therefore, if the concept of block I/O does  not  apply  to
        the  new  ACP, there is no need for any new logic to be added to
        FCS to block the user records.  Instead, each GET$/PUT$ call can
        result  in  an I/O request to the new ACP.  FCS block I/O can be
        treated as merely fixed-length record I/O.  An example would  be
        an  ACP which implements the DAP protocol.  The protocol is only
        concerned with records, so each GET$/PUT$ call would generate an
        input/output record request to the ACP.  This greatly simplifies
        the  modifications  necessary  to  FCS  because  all  the   code
        concerned with record blocking can be bypassed.



        4.2.4  File Control


             The final category  of  FCS  routines  are  used  for  file
        control operations:  delete, rename, truncate, extend, etc.  The
        modules in this category are straightforward and can be modified
        for support of a new ACP with little difficulty.

             If a particular operation is not appropriate  for  the  new
        device,  it  can  either  be  ignored or an error returned.  For
        example, FCS has  a  user  call  to  enter  a  filename  into  a
        directory.   It  would  typically  be appropriate to just return
        success if this operation does not make any  sense  to  the  new
        ACP.














                               CHAPTER 5

                        ACP/EXECUTIVE INTERFACE




             The ACP/executive interface is almost totally contained  in
        two  executive  modules:   DRQIO  and  IOSUB.  These modules are
        concerned with processing user I/O requests  and  providing  the
        common  I/O  services  used  by drivers and ACP's.  This chapter
        discusses the basic principles of ACP I/O processing  and  walks
        through the code used for each style of ACP.



        5.1  EXECUTIVE PROCESSING REQUIREMENTS


             The module DRQIO contains all the code to transform a  user
        I/O  request  into  its  internal  representation  and route the
        resulting packet to the correct device and/or  DCP.   For  FCP's
        and  UCP's,  DRQIO  is used to perform the common operations and
        device drivers are used for any unique  processing  required  by
        the  ACP.   For this section, where any particular piece of code
        is placed is ignored.  The emphasis is on  the  operations  that
        must be performed before an I/O packet can be queued.

             Up to a certain point, user I/O requests must be  processed
        in  the  context of the user task.  The following list documents
        operations which fall into this class.

             1.  Any address in the user task space must  be  validated.
                 Specifically,   the   address   of  the  QIO  directive
                 parameter block, I/O status block, AST address must  be
                 checked.    In  addition,  any  addresses  in  the  I/O
                 parameters must also be address checked.

             2.  Any address in the user task space to be  used  by  the
                 device  driver  or  ACP  must be relocated to a address
                 bias and displacement.  In other words, the 16-bit user
                 virtual  address must be converted to a physical memory
                 address  in  order  for  ACP's  to  access   or   store
                 information.





ACP/EXECUTIVE INTERFACE                                         PAGE 5-2



             The above list applies  equally  to  I/O  for  drivers  and
        ACP's.   When  the  executive  determines  a I/O packet is to be
        routed to an ACP, there are  some  other  tests  which  must  be
        applied  before  the packet can be queued to the ACP.  ACP's are
        running as tasks and are affected by the scheduling  algorithms.
        Therefore,  an indeterminate amount of time may elapse before an
        I/O packet queued to an ACP is actually processed  by  the  ACP.
        This  requires  the  state  of  the  ACP  and any I/O process be
        checked before the packet is queued and that no changes  in  the
        state  can  be  allowed  until  the  packet  is  dequeued.   The
        following operations fall into this class:

             1.  The device must  be  checked  to  see  if  the  ACP  is
                 mounted.   This  is  done by checking the US.MOU bit in
                 the U.STS field.  The bit will be zero if  the  ACP  is
                 mounted.

                 This rule implies the state  of  the  US.MOU  will  not
                 change  once the I/O request is queued to the ACP until
                 it is dequeued.  This is the reason for the transaction
                 count  (see  below).   An  ACP  should not be marked as
                 dismounted until the transaction count for  the  device
                 is zero.

             2.  The device must be checked to see if the ACP is  marked
                 for  dismount.  This is done by checking the US.MDM bit
                 in the U.STS field.  The bit will be set if a  dismount
                 has been requested.

                 When an ACP is in the marked-for-dismount state, no new
                 I/O  processes should be allowed.  Therefore, this test
                 is only performed for I/O requests which will create an
                 new  I/O  process.  The test will not be applied to any
                 functions which operate on an existing I/O process.

             3.  For functions which create I/O processes, a check  must
                 be made to see if an I/O process is already created for
                 the user lun.  This is done by checking the second word
                 in  the  LUT  table  entry for the presence of a window
                 block address.  If the word is zero, no I/O process  is
                 in effect and the request can be allowed.

                 This rule implies that  an  I/O  process  will  not  be
                 created for the user lun once the I/O request is queued
                 to the ACP and until it is dequeued by the  ACP.   This
                 is  the  reason  the the lun lock bit in the LUT table.
                 When the lock bit is set for a user lun, the user  task
                 cannot  issue  any further I/O request from the logical
                 unit.  Therefore, the I/O packet  processing  will  set
                 the  lock bit when a I/O packet which creates a process
                 is queued to the ACP and clear the bit once the process
                 is  created.   Similarly,  functions  which destroy I/O
                 processes will also set the lock bit to  insure  proper



ACP/EXECUTIVE INTERFACE                                         PAGE 5-3



                 synchronization between the ACP and the user task.

             4.  For functions which must be mapped to an I/O process, a
                 check  must  be  performed  to  see  if the I/O process
                 exists.  This is done by checking the  second  word  of
                 the LUT table entry for the presence of a window block.
                 If the word is non-zero, an I/O process  is  in  effect
                 and the request can be allowed.

             5.  Finally, any specific relationships required by the ACP
                 between  I/O requests are checked.  For example, an ACP
                 may not allow a particular operation until  some  other
                 criteria  have  been  established.   This  is  done  by
                 checking information in the window block.

                 Also, the window block may contain  enough  information
                 for  the  I/O  requests  to be mapped at this point and
                 queued directly to the device  driver.   This  is  what
                 occurs for I/O to disk files.  If the disk window block
                 contains the mapping  information  for  the  read/write
                 virtual  request,  the  remapping is performed directly
                 and the packet is sent directly  to  the  disk  driver.
                 Otherwise,  the  read/write  virtual request is sent to
                 the ACP which updates the window information and routes
                 the packet to the driver.


             The purpose of the transaction count is to insure no change
        in  the state of the ACP can occur between the time the state is
        checked and the I/O packet is  actually  received  by  the  ACP.
        Therefore,  an  ACP  can only be dismounted when the transaction
        count is zeroed.  The transaction count is incremented  whenever
        a  packet  is  queued  to  the  ACP and decremented when the ACP
        completes the packet.  The transaction count  is  also  used  to
        indicate the presence of I/O processes.

             Similarly, the lun lock bit  is  used  to  insure  the  I/O
        process  state  is  not  changed  between  the time the state is
        checked and the packet is dequeued by the ACP.  When this bit is
        set,  the executive guarantees no I/O request can be issued from
        the lun.  Therefore, any I/O request which will change the state
        of  the  I/O  process  should lock the lun before the request is
        queued to the ACP.  The bit does not need to be set if  the  I/O
        request will not affect the process state.



        5.2  DCP INTERFACE


             All of the operations described by the previous section can
        be observed by reading how I/O requests are processed for DCP's.
        The overall process is described by the RSX-11M Guide to Writing



ACP/EXECUTIVE INTERFACE                                         PAGE 5-4



        an  I/O  Driver  manual.   In addition, the RSX-11M System Logic
        Manual contains a flow-chart  of  the  executive  processing  in
        Chapter 6.

             The above descriptions are oriented towards  processing  of
        functions  which  will  eventually  be routed to device drivers.
        The next two sections outline the processing that occurs  for  a
        I/O function which will be routed to a DCP.  The following notes
        assume the I/O request is to be routed to F11ACP  and  that  the
        following features have been selected/not selected/optional:

                 A$$CHK  Address checking                selected
                 A$$CPS  ACP support                     selected
                 D$$IAG  On-line diagnostics             not selected
                 L$$DRV  Loadable drivers                optional
                 M$$MGE  Memory management               selected
                 M$$MUP  Multi-user protection           optional



        5.2.1  $DRQIO Processing


             All QIO directive processing starts at the label $DRQIO  in
        the  DRQIO  module.   The  first  operations  apply  to  all I/O
        functions.  The initial code checks that a QIO is legal  at  for
        the  current  task and device state.  Then the parameters to the
        QIO are verified.  The following checks are made.  If all checks
        prove false, processing continues with at label 24$.

             1.  The lun is  mapped  to  the  device  and  any  redirect
                 pointers   are   followed.    If  the  lun  is  illegal
                 ([Q.IOLN] > [H.NLUN]), a directive error  of  -96.   is
                 returned.

             2.  If the lun is  unassigned  ([first  lun  word] = 0),  a
                 directive error of -5.  is returned.

             3.  If the lun is interlocked for use (bit  0  [second  lun
                 word] = 1), the task PC is backed up to reissue the QIO
                 and the task is placed in WAIT  FOR  SIGNIFICANT  EVENT
                 state.


                                          NOTE

                      This is the feature use by ACP  functions  to
                      synchronize access to the I/O processes.



             4.  If  the  driver  is  not  resident   ([D.DSP] = 0),   a
                 directive error of -6.  is returned.



ACP/EXECUTIVE INTERFACE                                         PAGE 5-5



             5.  If an event flag was specified, clear it.  A  directive
                 error  of  -97.   is  returned  if  the  event  flag is
                 illegal.

             6.  If an I/O status block address was specified, check the
                 address and clear both words.

             7.  Allocate an I/O PACKET.   If  this  fails  a  directive
                 error of -1.  is returned.


                                          NOTE

                      This is the last  possible  directive  error.
                      Both  the  event  flag  and  I/O  status  are
                      cleared before this error can be detected.



             8.  Increment      the      outstanding      I/O      count
                 ([T.IOC] <- [T.IOC]+1).

             9.  If  the  function  was  QIOW  and  an  event  flag  was
                 specified,  place the task in WAIT FOR EVENT FLAG state
                 for the specified event flag.


             If no directive errors occured, the common  fields  in  the
        I/O  packet  are  filled  in.   The code that performs this step
        starts at label 24$.  The next step is  dispatch  based  on  the
        type of I/O function.  The following steps are performed:

             1.  If the I/O function code was kill I/O ([Q.IOFN+1] = 0),
                 control  is  passed  to  the  kill I/O code.  This code
                 calls $IOKIL and  returns  success  for  the  kill  I/O
                 function.

             2.  If multiuser support was  selected  (M$$MUP),  the  I/O
                 request  access  to  the  device is checked.  Access is
                 denied and an I/O status code of IE.PRI is returned  if
                 the all of the following are true.

                 1.  The device is owned ([U.OWN] # 0).

                 2.  Public  access  is   not   allowed   (bit   US.PUB,
                     [U.ST2] = 0).

                 3.  The current owner is not the task that  issued  the
                     I/O request ([U.OWN] # [T.UCB of current task]).

                 4.  The current task is  not  privileged  (bit  T3.PRV,
                     [T.ST3] = 0).




ACP/EXECUTIVE INTERFACE                                         PAGE 5-6



             3.  The I/O function code is checked to make sure  it  does
                 not  exceed  the  maximum (31.).  If it is does, an I/O
                 status code of IE.IFC is returned.

             4.  The I/O function code is changed into a bit mask.

             5.  The I/O function code  is  checked  against  the  legal
                 function  table in the DCB.  If it is not legal, an I/O
                 status code of IE.IFC is returned.

             6.  The device is checked to see  if  it  is  offline  (bit
                 US.OFL,  [U.ST2] = 1).  If it is, an I/O status code of
                 IE.OFL is returned.

             7.  The I/O function code is checked  against  the  control
                 function table in the DCB.  If it is, control is passed
                 to control function service.  This service  copies  the
                 six  I/O  parameters to the I/O packet and continues at
                 $DRQRQ.


                                          NOTE

                      This is the point  a  UCP  departs  from  the
                      normal  DCP  packet  processing.  See section
                      5.3 for a discussion of how the remainder  of
                      the packet is processed.



             8.  The I/O function code  is  checked  against  the  no-op
                 function  table  in  the  DCB.  If it is, an I/O status
                 code of IS.SUC is returned.

             9.  The device is checked to see if  it  is  not  mountable
                 ([U.CW1] > 0).   If it is not, control is passed to 80$
                 and the following checks are made.

                 1.  The I/O function code is checked  against  the  ACP
                     function  table  in  the  DCB.  If it is not an ACP
                     function,  control  is  passed  to   the   transfer
                     function service code.

                 2.  If function is an ACP function, the  function  code
                     is  changed  to IO.WLB unless the I/O function code
                     was IO.RVB which is converted to  IO.RLB.   Control
                     is  then  passed  to  the transfer function service
                     code.  



ACP/EXECUTIVE INTERFACE                                         PAGE 5-7



                                            NOTE

                          If you get here, the  I/O  function  code
                          must  be  either  IO.RVB  or IO.WVB.  All
                          others will be handled incorrectly.





             At this point, the function is known that the  function  is
        for  a  device  which could have an ACP servicing it.  The first
        check performed is to see if an ACP is mounted or is mounted  as
        foreign.   If  the  device  is not mounted or mounted as foreign
        (bits US.MNT!US.FOR [U.STS] = 0), control is passed to 60$.   If
        no  ACP  is mounted (bit US.MNT, [U.STS] = 1), the following two
        steps are performed.

             1.  If the function is  an  ACP  function,  an  I/O  status
                 return of IE.PRI is made.

             2.  Otherwise  the  control  is  passed  to  the   transfer
                 function service code.  


             If instead, a foreign ACP is mounted, control is passed  to
        label 65$ and the foreign ACP processing is used.


                                      NOTE

             This is the point a FCP-style  ACP  departs  from  the
             normal  DCP  packet  processing.   See section 5.4 for
             further details.



             If the device is  mounted  by  a  known  ACP,  a  check  is
        performed  to  see if the function is an ACP function.  If it is
        not, a branch is made to label  75$  and  the  following  checks
        made:

             1.  If  the  I/O  function  is   load   overlay   (IO.LOV),
                 processing  continues  as if the function is a transfer
                 request.

             2.  If  the  issuing  task  is  privileged   (bit   T3.PRV,
                 [T.ST3] = 1),  the function is allowed and treated as a
                 transfer request.

             3.  Otherwise, an I/O status error of IE.PRI is returned.





ACP/EXECUTIVE INTERFACE                                         PAGE 5-8



             At  this  point,  DRQIO  has  finally  recognized  the  I/O
        function  as  an  ACP function to a mounted device.  The special
        processing code  used  for  DCP's  is  then  invoked.   This  is
        performed  by  using  the  polish  tables listed in the front of
        DRQIO.   These  tables  are  used  to  correctly  dispatch   ACP
        functions  to  the  appropriate setup routines.  The tables have
        two parts.  Table FCDSP contains the  starting  address  of  the
        appropriate polish table for each function.  This is followed by
        the polish tables.  The registers and stack are setup  as  shown
        below when the dispatch into the polish code begins.

                 R0     = Address of UCB.
                 R1     = Address of second lun word.
                 R2     = Index into polish function dispatch table.
                 R3     = Address of Q.IOPL in QIO DPB.
                 R4     = Address of I.PRM  in I/O PACKET.
                 R5     = Address of next polish dispatch vector.
                 (SP)   = Address of second lun word.
                 (SP)+2 = Address of UCB.
                 (SP)+4 = I/O function code.

             The processing performed by the individual polish  routines
        is listed below.  To see which routines are used by a particular
        DCP function, see the tables in DRQIO.  The routines are  listed
        in alphabetical order.

             BDPKT - This routine completes the I/O  packet  for  F11ACP
                     and   MTAACP.    It   expects   the  following  I/O
                     parameters in the QIO request:

                         Q.IOPM+0  = Address of file-ID
                         Q.IOPM+2  = Address of attribute list
                         Q.IOPM+4  = Extend control word 1
                         Q.IOPM+6  = Extend control word 2
                         Q.IOPM+10 = Access control word
                         Q.IOPM+12 = Address of filename block

                     The file ID block and filename block are  relocated
                     if  present.   The  attribute  descriptor  block is
                     processed by allocating a buffer  from  the  system
                     pool  and copying the attributes from the user task
                     to the system buffer.  The attribute addresses  are
                     relocated.  If any address do not check out, an I/O
                     status code of IE.SPC is  returned.   Otherwise  it
                     dispatches to the next entry.

                     When BDPKT is finished, the parameters in  the  I/O
                     packet are formatted as follows:

                         I.PRM+00 = File-ID relocation bias
                         I.PRM+02 = File-ID relocation displacement
                         I.PRM+04 = Address of system attribute buffer
                         I.PRM+06 = Extend control word 1



ACP/EXECUTIVE INTERFACE                                         PAGE 5-9



                         I.PRM+10 = Extend control word 2
                         I.PRM+12 = Access control word
                         I.PRM+14 = Filename block bias
                         I.PRM+16 = Filename block displacement

             CKALN - This routine checks if a file is  already  accessed
                     on  the  lun ([second lun word] # 0) and returns an
                     I/O status code of  IE.ALN  if  so.   Otherwise  it
                     dispatches to the next entry.

             CKCON - This routine copies the QIO parameters into the I/O
                     packet.    The   routine  requires  the  first  two
                     parameters to be a  buffer  address  and  size  and
                     relocates the buffer before storing.  If the buffer
                     is not specified or is illegal, an I/O status  code
                     of  IE.BAD is returned.  Otherwise it dispatches to
                     the next entry.  This routine is  used  for  DECNET
                     processing.

             CKDIS - This routine copies the QIO parameters into the I/O
                     packet  and  dispatches  to  the next entry.  It is
                     used for processing the DECNET disconnect request.

             CKDMO - This routine checks if the  volume  is  marked  for
                     dismount  (bit  US.MDM, [U.STS] = 1) and returns an
                     I/O status code of  IE.PRI  if  so.   Otherwise  it
                     dispatches to the next entry.

             CKMOU - This routine checks the mounted volume list to  see
                     if  the  volume  can be access by the user.  If the
                     volume is public or the  user  is  entered  in  the
                     mounted  volume list, the routine dispatches to the
                     next entry.  Otherwise an I/O status code of IE.PRI
                     is returned.

             CKNLN - This routine checks if a files is accessed  on  the
                     lun  ([second  lun  word] # 0)  and  returns an I/O
                     status  code  of  IE.NLN  if  not.   Otherwise   it
                     dispatches to the next entry.

             CKRAC - This routine checks if the user has read privileges
                     for the I/O process.  If processing for F11ACP, the
                     window is then addressed to see if the read request
                     can be directly mapped and queued to the driver.

             CKWAC - This routine performs the same processing for write
                     requests that CKRAC performs for reads.

             CKXIT - This  routine  cleans  the  stack,  increments  the
                     volume  transaction count ([V.TRCT] <- [V.TRCT]+1),
                     and exits queue I/O PACKET code (see section 7).

             When all polish processing is finished, control  is  passed



ACP/EXECUTIVE INTERFACE                                        PAGE 5-10



        to label FCXIT.  The polish code flags whether the packet can be
        queued directly to the ACP or needs to be queued to  the  device
        driver   for  proper  synchronization.   The  listing  of  DRQIO
        contains a complete description of the queueing and interlocking
        performed by the executive.



        5.2.2  $DRQRQ Processing


             The second entry in the DRQIO module is  $DRQRQ.   This  is
        the code that queues I/O packets to drivers and calls the driver
        initiator.  The following steps are performed.

             1.  Get the SCB address ([U.SCB]).

             2.  If  the  packet  is  not  to  be  queued  (bit  UC.QUE,
                 [U.CTL] = 1), goto step 4.

             3.  Queue the I/O packet to the SCB I/O queue.

             4.  If the driver is loadable, map KISAR5 into the driver.

             5.  Call the driver at the initiator entry point.

             6.  If the  driver  is  loadable,  restore  KISAR5  to  its
                 original contents.

             7.  Exit from the DRQIO code.



                                      NOTE

             The entry $DRQRQ can be used to queue  an  I/O  packet
             that  has  been constructed by other means.  R1 should
             be the packet address and R5 the UCB address.





        5.2.3  $GTPKT Processing


             The executive normally queues I/O  packets  to  DCP's  from
        DRQIO.   However,  if  the packet needs synchronization with the
        device driver, it is queued to the device instead.  The  routine
        $GTPKT is used by device drivers to get their next packet.  When
        $GTPKT recognizes the I/O function as an ACP function, it queues
        the  packet  to  the ACP and loops to attempt to dequeue another
        packet for the driver.  The tests for this step occur  at  label



ACP/EXECUTIVE INTERFACE                                        PAGE 5-11



        80$.   Basically,  $GTPKT  assumes  if  the  device is mountable
        ([U.CW1] < 0) and an DCP-style ACP, all I/O functions from 7  to
        31(10) should be queued to the ACP.

             If the ACP is marked as foreign, $GTPKT will check the  DCB
        function  dispatch  masks to see if the function is for the ACP.
        If the DCB mask bit is set, the packet will  be  queued  to  the
        ACP, otherwise, it is returned to the driver.



        5.3  UCP INTERFACE


             UCP-style ACP's are used to avoid modifying the  executive,
        particularly  DRQIO, for support for the new ACP.  Section 5.2.1
        notes the point in the I/O processing  where  the  UCP  approach
        deviates from the traditional ACP packet processing logic.

             The deviation occurs because the I/O function is marked for
        control  processing.   Control functions are processed beginning
        at the label FCCTL.  First, the device is checked to see  if  it
        is a mountable magtape device and the I/O request is rejected if
        the task is not  privileged.   To  avoid  this  processing,  the
        US.LAB bit in the UCB status byte (U.STS) should be zero.

             The next step is to copy the six QIO parameters to the  I/O
        packet.  This done by a call to FCXP1 at label FCXOP.  No checks
        are made on the parameters.  Once the parameters are copied, the
        packet  is  passed  to $DRQRQ for queueing to the device.  Here,
        the packet is passed directly to the  driver  initiator  because
        the  UC.QUE  bit  in  the  UCB control byte (U.CTL) is set.  The
        driver than performs any processing  necessary  and  queues  the
        request on to the ACP.

             Note  that  the  UCP  interface  does   not   require   any
        modifications to the executive.  In addition, the interface uses
        standard features of the I/O  mechanism.   Therefore,  UCP-style
        ACP's  can  be interfaced easily to RSX-11M and future operating
        system releases will not affect the user-written code.



        5.4  FCP INTERFACE


             The  interface  for  FCP's  is  very  similar  to  the  UCP
        processing.   The  FCP  logic is invoked if the device is marked
        mounted and foreign and  the  function  masks  indicate  an  ACP
        request.   Section  5.2.1  notes the point in the I/O processing
        where the FCP approach deviates from the DCP logic.

             The FCP logic first checks if an ACP has been specified  by



ACP/EXECUTIVE INTERFACE                                        PAGE 5-12



        checking  that  U.ACP in the UCB is nonzero.  If the location is
        zero, a privilege violation is declared (IE.PRI).   Next,  if  a
        VCB  address  is  stored  in U.VCB, the VCB transaction count is
        incremented.

             The next step is to copy the six QIO parameters to the  I/O
        packet.   This done by a call to FCXP1 at label FCXOP.  Note, at
        this point, the processing is identical to  the  UCP  interface.
        However,  if  the  UC.QUE  bit  is not set, the packet is queued
        directly to the ACP.  Otherwise, the packet is passed to  $DRQRQ
        for  queueing to the device and the packet is passed directly to
        the driver initiator because the UC.QUE bit in the  UCB  control
        byte  (U.CTL)  is  set.  The driver than performs any processing
        necessary and queues the request on to the ACP.

             While the FCP approach does not require  any  modifications
        to  the  executive,  it  does  depend  on  continued support for
        foreign ACP processing.  For this reason, the  UCP  approach  is
        favored  if  all  other  considerations  are  equal.   The  main
        advantage of FCP's is the support provided by MOU and DMO.



        5.5  ACP INTERFACE


             No matter how the  I/O  packet  is  processed,  the  actual
        queueing  to  the ACP is done by the executive routine $EXRQP or
        $EXRQF.  These routines place the packet in the receive queue of
        the  desired  task  and schedule the task for execution.  $EXRQP
        queues the packet by priority.   The  alternate  entry,  $EXRQF,
        queues using first-in, first-out logic.

             Note, that the  routines  are  used  by  the  executive  to
        interface  to  other  tasks besides ACP's.  For example, this is
        the mechanism used to  pass  command  lines  to  MCR  and  abort
        messages to TKTN.

             An ACP receives the packet by  entering  system  state  and
        removing  the  first  entry  from  its receive queue.  The logic
        necessary has already been discussed in section 3.5.1.



        5.6  TASK TERMINATION


             The only other module in the executive which  is  aware  of
        ACP's  besides  DRQIO  and IOSUB is DREIF.  This module contains
        the code used to clean-up the system  data  bases  when  a  task
        exits.  A part of this clean-up is to check that all outstanding
        I/O is completed and all I/O processes have been terminated.




ACP/EXECUTIVE INTERFACE                                        PAGE 5-13



             The code for these steps starts at label 5$ in DREIF.   The
        first  step is to test for outstanding I/O by testing T.IOC.  If
        the value is nonzero, $IOKIL is called for each device  assigned
        by the exitting task.

             Once the I/O count has been reduced to  zero,  the  logical
        unit  table  is  scanned  again  for  attached  devices  and I/O
        processes.  Any attached devices  result  in  an  IO.DET  packet
        being issued by the executive on behalf of the task.  Similarly,
        an I/O processes still active will result in  an  IO.CLN  packet
        being  queued  to  the  device.  This is done by calling $DRQRQ.
        The packet should then be forwarded to the  ACP  and  it  should
        terminate  the  I/O process in a timely fashion.  Otherwise, the
        task exit will not be completed.

             The test for an I/O process is to check the second word  of
        each  logical  unit table entry.  If the lun is non-zero, an I/O
        process is assumed.  However, if the lun is locked,  the  IO.CLN
        function will not be issued.














                               CHAPTER 6

                         ACP ENABLING/DISABLING




             An ACP must be enabled before it can be used for user  I/O.
        Similarly,  the  reverse  capability  is  usually provided.  The
        common names for these operations are mount and dismount.   This
        chapter  will  discuss  the  requirements  for  ACP enabling and
        disabling and present five approaches that could be used  by  an
        ACP implementation.



        6.1  ENABLING REQUIREMENTS


             ACP enabling merely  means  satisfying  certain  conditions
        that allow user tasks to issue I/O requests to the ACP.  For the
        Digital ACP's, enabling a device is performed by the  MOU  task.
        However,  the  MOU  task  is not the only method for enabling an
        ACP.  Essentially, an ACP can be considered as enabled  when  it
        is  servicing  I/O requests from user task.  The conditions that
        must be met to reach this state are as follows:

             1.  The device is marked as mounted.  The US.MOU bit in the
                 device  status  byte  of the UCB indicates if an ACP is
                 mounted or dismounted.  If the bit is zero, the ACP  is
                 considered as being mounted.

             2.  The TCB address of the ACP is stored in  U.ACP  of  the
                 UCB.   This  value  will  be used when an I/O packet is
                 queued to the ACP.  The field will  be  assumed  to  be
                 valid   if  US.MOU  indicates  the  device  is  mounted
                 (US.MOU=0).

             3.  The VCB is allocated from the system pool.  The address
                 of  the  VCB  is stored in U.VCB of the UCB.  The first
                 word of the VCB will be used as a  transaction  counter
                 and will be incremented when an I/O packet is queued to
                 the ACP.  The field will be  assumed  to  be  valid  if
                 US.MOU indicates the device is mounted (US.MOU=0).

             4.  The ACP  has  performed  any  operations  necessary  to



ACP ENABLING/DISABLING                                          PAGE 6-2



                 initialize itself and the device.  It has verified user
                 I/O request will  be  legal  for  the  device  and  the
                 current state of the RSX-11M system.

             5.  Finally, the ACP is  dequeuing  I/O  packets  from  its
                 receive  queue  when  they  are  queued  to  it  by the
                 executive.


             The logic necessary to reach the state listed above is very
        simple.   The  complexity  of the Digital MOU task is because of
        the device initialization operations and command  processing  it
        performs  and  not the actual mounting of the ACP.  For example,
        when mounting a Files-11 disk, MOU must read the  Files-11  data
        structures  on  the disk and setup all the information needed by
        F11ACP for using the volume.

             Before an ACP can be mounted,  the  current  state  of  the
        system  must  be  checked  to  see  if conditions will allow the
        operation.  Among the  more  common  checks  performed  are  the
        following:

             1.  The device characteristics word (U.CW1) in the  UCB  is
                 checked  to  see  if  the  device is mountable.  If the
                 device is not mountable (DV.MNT=0), the  mount  request
                 is disallowed.

             2.  The device status byte (U.STS) in the UCB is checked to
                 see if the device is already mounted.  If the device is
                 already marked as mounted (US.MNT=0), the mount request
                 is disallowed.

             3.  The device status byte (U.STS) in the UCB is checked to
                 see  if  the  device  is  marked  for  dismount.   If a
                 dismount  request  is  pending  (US.MDM=1),  the  mount
                 request is disallowed.

             4.  The device DCB is checked to see if the  device  driver
                 is  loaded.  If the driver is not loaded (D.DSP=0), the
                 mount request is disallowed.

             5.  The system task directory is searched for the ACP.   If
                 the TCB is not found, the mount request is disallowed.

             6.  The third status word of the ACP's TCB  is  checked  to
                 see  if  the  task  was built as an ACP.  If is was not
                 (T3.ACP=0), the mount request is disallowed.

             7.  The privileges of the user are checked to see if he  is
                 allowed  to  mount the device.  Typically, if multiuser
                 protection was selected and the user is  nonprivileged,
                 he  must own the device or it must be marked as public.
                 Otherwise, the user must  be  privileged  in  order  to



ACP ENABLING/DISABLING                                          PAGE 6-3



                 mount the device.


             Besides the common checks list above,  usually  device  and
        specific  ACP  checks  will  be  made.  For example, if labeling
        information is available on  the  device,  it  will  be  checked
        against user supplied values to insure the right volume is being
        mounted.

             The other operation performed when an ACP is mounted is  to
        process  command  options  specified.   A typical ACP will allow
        options which to be specified when it is mounted.   The  options
        override any defaults established at assembly and build time.

             In summary, mounting an ACP  involves  determining  if  the
        mount  request  can  be  allowed,  processing  any  options, and
        setting up the ACP to process user requests.   A  separate  task
        can  be  used for this process, the ACP can be self-mounting, or
        some combination of the two approaches can be used.



        6.2  DISABLING REQUIREMENTS


             Disabling an ACP reverses the process of mounting it.   The
        same  approach  is  followed.   First,  the  dismount request is
        validated, any options are processed, and the ACP is dismounted.
        An  ACP  is considered dismounted when it is no longer marked as
        mounted for a device (US.MOU=1).  When all devices  serviced  by
        the ACP are dismounted, the ACP task exits.

             One point to note is that the actual dismounting of an  ACP
        occurs  asynchronously  from  the  dismount request.  Before the
        device can be marked as dismounted, all outstanding I/O requests
        queued  to the ACP must be completed and all I/O process must be
        terminated.  For this reason, a mark-for-dismount  bit  (US.MDM)
        is  available  in  the  U.STS byte of the UCB.  When this bit is
        set, it signifies a dismount request has  been  made.   The  ACP
        will  complete  the process when all outstanding activity on the
        device is complete.  Also, no new I/O processes will be  allowed
        to be initiated.

             The usual approach to dismount an ACP  is  for  a  separate
        task to process the dismount request from the terminal and queue
        an IO.DMO packet to the ACP.  Once the packet is received by the
        ACP,  it completes the process when all activity for the unit is
        finished.  Digital's DMO task is an  example  of  this  process.
        The  checks  performed  by  DMO  are typical for any dismounting
        process:

             1.  The device characteristics word (U.CW1) in the  UCB  is
                 checked  to  see  if  the  device is mountable.  If the



ACP ENABLING/DISABLING                                          PAGE 6-4



                 device  is  not  mountable  (DV.MNT=0),  the   dismount
                 request is disallowed.

             2.  The device status byte (U.STS) in the UCB is checked to
                 see  if  the  device  is mounted.  If the device is not
                 mounted (US.MNT=1), the dismount request is disallowed.

             3.  The device status byte (U.STS) in the UCB is checked to
                 see  if  a  dismount  request is already pending.  If a
                 request  is  (US.MDM=1),  the   dismount   request   is
                 disallowed.

             4.  The privileges of the user are checked to see if he  is
                 allowed  to  dismount  the  device.   Usually, the same
                 checks performed for mount privileges are applied.


             When all checks are finished, the dismount process sets the
        US.MDM  bit and queues an IO.DMO packet to the ACP.  This packet
        is processed by the ACP in the following manner.

             1.  The IO.DMO packet  is  returned  with  the  appropriate
                 code.  Usually, this will be success

             2.  If the transaction count in the  VCB  is  used  in  the
                 usually   fashion,  it  will  indicate  the  number  of
                 outstanding I/O packets  queued  to  the  ACP  and  I/O
                 processes.   When  the  count reaches zero, the ACP can
                 complete the dismount process.  Otherwise, it continues
                 to service I/O packets, reexaming the transaction count
                 after every packet is finished.

             3.  The ACP is marked as not mounted (US.MOU=1).

             4.  The mark-for-dismount bit is turned off (US.MDM=0).

             5.  The VCB is returned to the system pool.

             6.  The internal count of mounted devices  is  decremented.
                 When the count reaches zero, the ACP can finally exit.




        6.3  STANDARD APPROACH


             Digital's solution to enabling and disabling ACP's  is  the
        MOU  and DMO MCR tasks.  The next two sections outline how these
        tasks functions and their applicability to  user-written  ACP's.
        In  general,  the  use  of the MOU and DMO task for user-written
        ACP's is not recommended because  of  the  support  problem  for
        future releases of the operating system.



ACP ENABLING/DISABLING                                          PAGE 6-5



        6.3.1  MOU Task


             The MOU task supports  mounting  Files-11  disks  and  ANSI
        magtapes.    It  also  contains  support  for  DECNET  Phase  I.
        However, MOU is no longer used  by  DECNET.   In  addition,  the
        RSX-11M  V3.2  version  of MOU provides support for the /FOREIGN
        switch.  This is intended to allow MOU to be used for  FCP-style
        ACP's.

             The flow through MOU is  diagrammed  in  Figure  6-1.   MOU
        consist  of  two  common  modules  used  for  all ACP's (MOUROT,
        MOUPAR) and ACP specific parsing  and  mounting  routines.   The
        overall  approach  to  adding a new ACP is to code a new parsing
        and mounting routine and modify the dispatch points  in  MOU  to
        correctly call these routines for the new device.

             The task entry to MOU is in the  module  MOUROT.   On  task
        entry,  an immediate dispatch is made to the entry $MPREP in the
        module MOUPAR.  The  initial  command  processing  performed  by
        MOUPAR is as follows:

             1.  The parameter area used by MOU is zeroed.  This area is
                 in MOUROT and is referenced throughout the task.

             2.  The command line is input from the users terminal.

             3.  The device to be mounted is  parsed  from  the  command
                 line.   The remaining switches are not examined at this
                 point.

             4.  Lun 2 of the MOU task  is  assigned  to  the  specified
                 device.

             5.  The UCB address is retrieved from  the  LUT  table  and
                 stored at label $MDEV.

             6.  The device DCB is checked to see if the  device  driver
                 is loaded.

             7.  If the device is not a magtape (DV.REC=0), the unit  is
                 attached.


             Once the common command parsing  is  finished,  the  device
        specific  parsers  are  called  from  MOUPAR.   The  UCB  device
        characteristics are examined to determine  which  device  parser
        should  be  used:  MPAR11 (Files-11), MPARMT (ANSI magtapes), or
        MPARCM (communications device).  If MOU is  to  be  used  for  a
        user-written  ACP,  the  code  at  this  point  will  have to be
        modified to dispatch to the new ACP parsing module.



ACP ENABLING/DISABLING                                          PAGE 6-6



        			     $MOUEP             (MOUROT)
        			       |
        			       | JSR
        			       |
        			      \|/
        			     $MPREP             (MOUPAR)
        			       |
        			       | JMP
        			       |
        	-----------------------+-------------------------
        	|		       |			|
        	| Files-11	       | Magtape		| DECNET
        	|		       |			|
               \|/		      \|/		       \|/
              $M11PR (MPAR11)	     $MMTPR (MPARMT)	      $MCMPR (MPARCM)
        	|		       |			|
        	|		       | Return			|
        	|		       |			|
        	-----------------------+-------------------------
        			       |
        			       | JSR
        			       |
        	-----------------------+-------------------------
        	|		       |			|
        	| Files-11	       | Magtape		| DECNET
        	|		       |			|
               \|/		      \|/		       \|/
              $M11EP (M11OV)	     $MMTEP (MMTOV)	      $MCMEP (MCMOV)
        	|		       |			|
        	|		       | Return			|
        	|		       |			|
        	-----------------------+-------------------------
        			       |
        			       | JSR
        			       |
        			      \|/
        			    $MDISEP (MDISOV)
        			       |
        		               | Return
        			       |
        			      \|/
        			   Exit Task
         
        			   Figure 6-1
        			  MOU TASK FLOW




ACP ENABLING/DISABLING                                          PAGE 6-7



             The parsing modules perform basically the same  operations.
        The following steps are performed:

             1.  The VCB is allocated from the system pool.  The address
                 of  the  buffer  is  stored  in  $MVCB  and the size in
                 $MVCBL.  The initial VCB is zeroed.

             2.  The remainder of the command line is parsed for the ACP
                 specific switches.

             3.  The user privileges are examined to see if the user has
                 the necessary access to mount the device.  The check is
                 performed by the routine $PVTST in the module MOUPAR.

             4.  If needed, the mount list entry is allocated and filled
                 in with the users terminal UCB.  The mount list entries
                 are used for disks and do  not  need  to  be  used  for
                 user-written ACP's.


             When all parsing  is  completed,  control  is  returned  to
        MOUROT.   Here,  some  of  the  basic  tests are performed and a
        dispatch is made to the device specific  mount  modules:   M11OV
        (Files-11),  MMTOV  (ANSI  magtapes),  or  MCMOV (communications
        devices).  This is the second point modifications will  need  to
        be added to correctly dispatch for the new ACP.

             The actual device mount takes place in the device  specific
        mount modules.  The disk and magtape routines perform device I/O
        to read the volume labeling information.  The  best  routine  to
        use as an example is MCMOV.  This routine has no device specific
        I/O and therefore can be more easily read.  The usual processing
        performed for a device is as follows:

             1.  The system task directory is  searched  for  the  ACP's
                 TCB.

             2.  The TCB is examined to see if the task was built as  an
                 ACP.

             3.  The I/O packet for the IO.MOU request is allocated from
                 system pool and initialized.

             4.  The device is detached.

             5.  The address of the VCB allocated previously  is  stored
                 in the UCB.

             6.  The VCB transaction count is incremented.

             7.  The device is marked as mounted by clearing US.MNT.

             8.  The TCB address of the ACP is stored in the UCB.



ACP ENABLING/DISABLING                                          PAGE 6-8



             9.  The IO.MOU function is queued directly to the ACP.  MOU
                 is  placed  into  I/O  wait  and  it increments its I/O
                 count.


             When the ACP completes  the  IO.MOU  function,  it  returns
        success/failure  to  MOU.   The MOU task then cleans up, outputs
        any volume information, and exits.



        6.3.2  MOU /FOREIGN


             A new feature of MOU in RSX-11M V3.2 is the support of  the
        /FOREIGN  switch.   This  switch allows user-written ACP's to be
        enabled for devices.  Unfortunately, the implementation  is  not
        easy  to  follow.  However, the feature does provide a mechanism
        for mounting user-written ACP's without modifing MOU or  writing
        any new code.  If used, the MOU sources should be studied to see
        how the switch affects the normal processing performed by MOU.



        6.3.3  DMO Task


             The DMO task consists of one module, DISMNT.  The procedure
        for  dismounting  a device is much simplier.  In some cases, the
        DMO  task  may  be   used   for   user-written   ACP's   without
        modification.

             The flow through DMO begins at the task entry, $DMOEP.  The
        processing is as follows:

        <To be written>



        6.4  NON-STANDARD APPROACHES


             As stated before, the use of the Digital MOU and  DMO  task
        is not recommended for user-written ACP's because of the support
        problem from release to release of the  operating  system.   The
        following approaches can be used instead.



ACP ENABLING/DISABLING                                          PAGE 6-9



        6.4.1  Self-Initialization


             The easiest method of initializing an ACP is for it do  the
        mounting  itself  when  it is first scheduled.  This approach is
        appropriate for ACP's which service only one device  driver  and
        involve  no  option  processing.   The ACP can allocate the VCB,
        setup  the  UCB  status  as  needed,  and  perform  any   device
        initialization.   Once  mounted,  the initialization code can be
        overwritten as data space.  Another possibility is to place  the
        initialization code in an overlay segment.

             Usually, when this approach is used, the ACP  is  essential
        to  the  operation of the device and there is no reason to every
        dismount it.  Therefore, the disabling step can be ignored.



        6.4.2  Driver Initialization


             A alternative to the ACP self-initialization approach would
        be  for  the  device drivers serviced by the ACP to initiate the
        mount.  If the UC.PWF bit is set  in  UCB,  the  power  recovery
        entry  in  the driver is called when the system is booted or the
        driver is loaded.  This entry can be used  to  start  the  mount
        process.   Either  the  driver  can  set  the  necessary  status
        directly or it could queue a IO.DMO packet to the ACP and let it
        finish the operation.

             The same disadvantages apply to this approach  as  for  the
        previous section.  There is no convenient method for dismounting
        the ACP and inputting mount-time options.  However, the approach
        does  allow  several  different  drivers  to  each mount the ACP
        separately for themselves.



        6.4.3  Alternate Task


             A final approach  is  to  implement  new  system  tasks  to
        specifically mount and dismount the user-written ACP.  The tasks
        can be modeled after the MOU and DMO tasks.  The new  tasks  can
        perform any special processing required.  The major advantage of
        this approach is the independence  gained  from  future  Digital
        modifications to MOU and DMO.

             This approach was used by DECNET to mount NETACP and set up
        the other software.  The sample ENA and DIS programs distributed
        with this manual can be used as a basis  for  the  ACP  specific
        enabling and disabling tasks.














                               CHAPTER 7

                           ACP IMPLEMENTATION




             This chapter covers some of the basic considerations of ACP
        implementation.   The  material  is  not exhaustive and will not
        apply to every ACP.  All ACP implementations will  be  different
        and  no  fixed  set  of  guidelines  can  govern how an ACP will
        function internally.



        7.1  TASK ATTRIBUTES


             ACP's are constrained  by  the  limits  RSX-11M  places  on
        privileged  tasks.   RSX-11M  associates  a set of attributes to
        each task  in  the  system.   The  proper  definition  for  each
        attribute  will  have to be decided when the ACP is implemented.
        Some  of  the  attributes  involve   trivial   decisions:    the
        partition,  taskname,  etc.   Others  are more important and are
        discussed in the following two sections.



        7.1.1  Task Mapping


             The major task attribute to be considered is the  ACP  task
        mapping.  Figure 7-1 diagrams the mapping for a privileged task.
        The first four  APR's  (APR0-APR3)  are  always  mapped  to  the
        executive.   APR4  is  mapped  to the executive if 20K executive
        support was selected when the system was generated.  If the  ACP
        is to be portable between systems, APR4 should not be used.

             Normally, the ACP is then left with APR5 and  APR6  to  map
        its  task  code  and  APR7  to map the I/O page.  If 8 KW is not
        enough memory, the ACP can extend into the I/O  page.   However,
        when  a switch is made to system state, the executive will unmap
        the ACP's APR7 and map the I/O page.  If the top of the  ACP  is
        used for data and not code, this restriction will usually not be
        a problem.



ACP IMPLEMENTATION                                              PAGE 7-2



                        |-------------------------------|
                    7   |           I/O Page            | 160000-177776
                        |-------------------------------|
                    6   |                               | 
                        |---          ACP            ---| 120000-157776
                    5   |                               |
                        |-------------------------------|
                    4   |          ? (R$$EXV)           | 100000-117776
                        |-------------------------------|
                    3   |                               |
                        |---                         ---|
                    2   |                               |
                        |---        Executive        ---| 000000-077776
                    1   |                               |
                        |---                         ---|
                    0   |                               |
                        |-------------------------------|

                                    Figure 7-1
                                   TASK MAPPING



        7.1.2  Task Build Requirements


             When linking the ACP, several TKB  options  apply.   First,
        the task should be declared as an ACP with the /AC switch.  This
        TKB switch causes T3.ACP to be set in the TCB when  the  ACP  is
        installed.   When T3.ACP is set, the executive prevents sends to
        the ACP task.  This is desirable because the  ACP  is  receiving
        the  I/O  packets on its receive queue and would have trouble if
        some other task were allowed  to  send  it  messages.   The  /AC
        switch  is  also  useful for identifying the task as an ACP when
        the device is mounted.

             The /AC switch  also  causes  the  task  to  be  marked  as
        privileged.   The  other  TKB switches used can be set according
        the ACP implementation.

             There are no special TKB options  that  apply  strictly  to
        ACP's.   Therefore,  the options specified will be a function of
        the ACP implementation and  the  environment  the  ACP  will  be
        executed in when it is mounted.  One consideration is whether to
        use a separate partition for the ACP other than the one used for
        user  tasks.   A  lock-out  condition  can  occur if a user task
        issues an I/O request to an ACP which is swapped out because  of
        the user task.



ACP IMPLEMENTATION                                              PAGE 7-3



        7.2  DESIGN CONSIDERATIONS


             This section comments on some general design considerations
        for ACP's The list is not exhaustive and has been developed from
        past experience in writing ACP's.



        7.2.1  ACP I/O


             Besides receiving  I/O  requests  from  user  tasks,  ACP's
        usually  issue  I/O  request.   These  request  can be to device
        drivers or to other ACP's.  Normally, the ACP would use the  QIO
        directive  for  any  I/O  it  needs  to  perform.  However, when
        performance is an issue, the ACP can bypass the normal executive
        directives   and   interface   directly   to  the  drivers.   In
        high-performance  environments,  the  ACP  and  the  driver  may
        actually  use  cooperating  code  and bypass RSX-11M altogether.
        How an ACP performs its I/O using non-standard logic is strictly
        up to the implementation.



        7.2.2  Transportability


             Often, an ACP is required to run on a variety of  machines.
        The  ACP  coding  can  be  greatly  simplified  if  the  ACP  is
        restricted  to  one  type  of  machine.    However,   by   using
        conditional  assembly  symbols  and interfacing correctly to the
        executive, it is possible to write an  ACP  that  will  properly
        function on all PDP-11's.

             The biggest difference between machines is the presence  or
        absence  of memory management.  Typically, any code used to move
        information between the ACP and a user task  must  be  assembled
        with  conditionals  for  memory management.  On a mapped system,
        the APR's must be  manipulated.   On  an  unmapped  system,  the
        entire  system  can  be  addressed directly.  The problem can be
        avoided  by  using  the  executive  routines  to   manage   data
        transfers.

             The other large difference between machines  is  arithmetic
        instructions.   The  older  PDP-11's  do  not  have  the MUL/DIV
        instructions.  If transportablity is desired to  such  machines,
        the executives $DIV/$MUL routines should be used.



ACP IMPLEMENTATION                                              PAGE 7-4



        7.2.3  Pool Utilization


             Most RSX-11M systems suffer from a lack of pool.  ACP's are
        a potential large user of pool.  Limits on the amount of pool an
        ACP can use and use of internal versus system  pools  should  be
        considered in the design of an ACP.

             The typical approach is to create an internal ACP pool that
        is  structured the same as the RSX-11M system pool.  The size of
        the pool is a mount or link-time option.  Whenever the ACP needs
        to  allocate  an internal structure, an attempt is first made to
        allocate from the ACP pool.  If this fails,  the  allocation  is
        attempted   from   the  system  pool.   When  the  structure  is
        deallocated, the address indicates to which pool the  memory  is
        returned.



        7.2.4  ACP Variables


             The  design  of  an  ACP  should  consider  the  amount  of
        flexibility  that  will  be built into the code.  There are four
        types of ACP variables:  assembly-time statements, TKB switches,
        mount-time options, and run-time I/O functions.  For example, an
        ACP may use a separate LUN for each I/O process it supports.   A
        TKB  option would specify the maximum number of luns the ACP can
        use.  A mount-time option  would  then  specify  the  number  of
        actual luns to be used (up to the taskbuilder limit).

             A good practice is to make the  defaults  for  each  option
        settable  by  the  taskbuilder GBLPAT and GBLSYM commands.  This
        allows each installation of the ACP  to  specifically  configure
        its default options.



        7.2.5  Performance Statistics


             If the ACP supports  options,  it  should  then  accumulate
        statistics  on  its performance.  This would allow adjustment of
        the options to maximize  performance  in  a  given  environment.
        Without  statistics,  the  users of the ACP will be faced with a
        situation similar  to  F11ACP.   There  are  many  switches  for
        mounting  a  disk.   However,  except  for eyeballing the system
        performance, there is no way to tell how a particular option  is
        performing.

             If performance measurements are used by  the  ACP,  it  the
        performance  code should be conditionally assembled.  This would
        allow a smaller  version  of  the  ACP  to  be  assembled  after



ACP IMPLEMENTATION                                              PAGE 7-5



        sufficient  experience with the various options is obtained.  In
        addition, some method of examining  the  statistics  is  needed.
        This  can  be as simple as using the MCR OPEN command to examine
        known locations.  In  other  cases,  the  ACP  may  support  I/O
        functions to return is performance data.  One final method is to
        keep the performance data in the system  pool  and  implement  a
        separate task to access the data and print reports.



        7.2.6  Serial Versus Parallel Processing


             The final consideration in the design of the ACP is whether
        it  will  process  user  I/O  requests in serial or parallel.  A
        serial ACP will only process one I/O request at  a  time.   This
        greatly  simplifies  the  implementation because only one set of
        internal data bases needs to be kept and the  flow  through  the
        ACP is completely synchronous.  The ACP only attempts to dequeue
        an I/O request from its receive queue when it has  finished  the
        previous request.  F11ACP is implemented as a serial ACP.

             The serial approach is appropriate for ACP's which  service
        fast  devices such as disks.  There will be little delay for ACP
        I/O The disadvantage of the serial approach is that the ACP is a
        bottleneck in the I/O mechanism.

             An  ACP  which  allows  parallel  processing  of  user  I/O
        requests  will  typically  support  one I/O request for each I/O
        process.  Such an approach is particularly applicable for  ACP's
        which  service communication devices.  NETACP is an example of a
        parallel implementation.  There is a significant  delay  between
        the  time  the  user  DECNET QIO is issued and the necessary NSP
        protocol has been exchanged to fulfill the request.

             However, this approach is much more complex  to  implement.
        Many  of  the data bases and variables used by the ACP will have
        to be duplicated for each I/O process.  In addition,  the  logic
        of  the  ACP  must  be able to save the context of one operation
        when it reaches a checkpoint, process another I/O  function  for
        another  process,  and  eventually  resume the original process.
        This requires the ACP code to be  reentrant  and  some  sort  of
        internal scheduling algorithm to be implemented.



        7.3  DEBUGGING NOTES


             Because ACP's usually involve complex  logic  to  implement
        their  protocols,  much of the time spent in development will be
        devoted to debugging.  In addition, because bugs in the ACP  are
        likely  to  corrupt  the  operating system, the stability of the



ACP IMPLEMENTATION                                              PAGE 7-6



        machine for other users will be reduced.

             One advantage of ACP's is that ODT can be used on the  task
        portions  of the implementation.  However, ODT cannot be used to
        breakpoint within portions of the ACP code that  run  at  system
        state.  In such code, XDT would have to be used.  Similarly, XDT
        would have to be used for debugging any driver or executive code
        involved with the ACP.

             Another problem in  developing  ACP's  occurs  if  the  ACP
        terminates  abnormally while still mounted.  The data structures
        still mark the ACP as being mounted and the  typical  method  to
        clean  them up is to reboot the system.  One alternative to this
        approach would  be  to  write  a  special  privilege  task  that
        destroys  the  ACP  data  structures  to the point where you can
        remount the ACP.   While  some  pool  may  be  lost,  the  basic
        integrity of the system can be preserved.














                               CHAPTER 8

                           EXECUTIVE SERVICES




             There are many executive services an  ACP  can  use.   This
        chapter  briefly  describes  some of the services available from
        the executive.  There are many other facilities  which  are  not
        documented in the chapter.  The actual calling sequences for the
        routines can be found in the executive listings.   The  routines
        are also documented in the RSX-11M System Logic Manual.



        8.1  SYSTEM STATE


             Before an ACP can use an executive  service  or  manipulate
        system  data  structures,  it  must  make sure its access to the
        executive is correctly sychronized with other  system  activity.
        This  is  done  by  switching to system state.  Once a switch to
        system state is made, the ACP  is  running  as  a  part  of  the
        executive  and  must  follow  all rules applicable to the kernel
        state.  For example, directives cannot  be  issued  from  system
        state  and  any  unexpected trap will cause the system to crash,
        rather than aborting the ACP.

             The switch to system state is accomplished  by  issuing  an
        EMT  376.  This instruction is followed by the address to return
        to  when  a  return  is  made  to  task  state.   The  following
        summarizes the switching to system state process:

        Call By:    CALL    $SWSTK,addr    (RSXMC.MAC)

        Generates:  EMT     376
                    .WORD   addr

        Effect:     Returns to next instruction
                    Switches to kernel mode
                    Maps user APR's 4(?),5,6 to kernel space
                    Kernel APR's 0,1,2,3,4(?) mapped to executive
                    Kernel APR 7 mapped to I/O page
                    Saves all registers




EXECUTIVE SERVICES                                              PAGE 8-2



        Exit By:    RETURN instruction. Exit is to "addr"
                    Pre-kernel registers restored

                    Values can be returned in R0-R3 by storing value
                    in 2(SP) to 10(SP) before RETURN



        8.2  I/O TERMINATION


             One service used by ACP's is I/O packet  termination.   The
        I/O  termination  code is located in the executive module IOSUB.
        Three entries are provided by the  executive:   $IODON,  $IOALT,
        and  $IOFIN.   The first two entries are used by device drivers.
        In addition to the I/O packet termination, these  routines  free
        the  device  for the next I/O packet.  The $IOFIN routine is the
        entry usually used by ACP's as it does  not  affect  the  driver
        data bases.



        8.3  ADDRESS CHECKING


             Another service provided  by  IOSUB  is  address  checking.
        Whenever  an  address  is  passed from a user task to an ACP, it
        must be checked by the executive to make  sure  the  address  is
        within the boundaries of the user task.  This check must be done
        in the context of the user task.   Therefore,  address  checking
        must be performed before the I/O packet is queued to the ACP.

             The executive provides five entries for  address  checking.
        The  first  three, $ACHKP, $ACHKW, and $ACHK2, are only used for
        directive processing and do not return  errors  to  the  caller.
        Instead,  they  return  an directive status error if the address
        check failed.

             The two entries used for I/O-related address  checking  are
        $ACHKB  and  $ACHCK.   The  first  entry  checks for proper byte
        alignment.  The $ACHCK requires word  alignment.   The  routines
        return  with  the  carry  bit  clear/set  as  a  success/failure
        indicator.



        8.4  ADDRESS RELOCATION


             In order for an ACP to address a  user-task  address  on  a
        mapped system, the user-task virtual address must be transformed
        into a relocation bias and offset.  As in address checking, this
        process must be performed in the context of the user task.



EXECUTIVE SERVICES                                              PAGE 8-3



             Two  entries  in  IOSUB   provide   support   for   address
        relocation.   The  first  routine,  $RELOC,  transforms the user
        virtual address into a relocation bias to be  loaded  into  APR6
        and  the  APR6 displacement.  These values can then be passed to
        the ACP, which can then use them to map the user task addresses.

             The  second  routine  is  named  $RELOM.   The  routine  in
        addition to performing the address relocation, loads kernel APR6
        with the address bias.  This routine is used  by  the  executive
        and/or   drivers   when   processing  an  ACP  I/O  request  and
        reading/writing user-task memory.



        8.5  BUFFER ALLOCATION


             The executive module CORAL contains support for buffer pool
        allocation.   The  routines  are  normally  used to allocate and
        deallocate space in the system pool, however, they can  be  used
        to  manage any buffer pool which follows the RSX-11M system pool
        mechanism.  The System Logic Manuals  provide  details  on  this
        mechanism.

             Two entries in CORAL can be  used  for  buffer  allocation.
        The  $ALOCB entry is the general system pool allocation routine.
        The $ALOC1 is an alternate entry.   Here,  the  buffer  listhead
        address  is  passed  to the routine instead of defaulting to the
        system pool as in $ALOCB.


                                      NOTE

             The $ALCLK (allocate clock  queue  entry)  and  $ALPKT
             (allocate  I/O  packet)  should  not be used by ACP's.
             These routines return a directive status error if  the
             allocation  fails  instead  of  an error return to the
             caller.





        8.6  BUFFER DEALLOCATION


             CORAL  also  provides  two  buffer  deallocation   entries.
        $DEACB  is the general system pool deallocation routine.  $DEAC1
        is the alternate entry for general deallocation of  buffers  for
        non-system pools.



EXECUTIVE SERVICES                                              PAGE 8-4



        8.7  QUEUE MANIPULATION


             The  module  QUEUE  provides  a  variety  of   entries   to
        manipulate  the  various  RSX-11M queues.  The most used entries
        are  $QINSF,  $QINSP,  and  $QRMVF.   The  first  two   routines
        respectively  insert  by  first-in,  first-out or by queue entry
        priority.  When priority insertion is used, byte 2 of the  queue
        entry is assumed to contain the priority.

             $QRMVF removes the first entry in the queue.  This  routine
        is  used  by  all  ACP's  to remove I/O packets from the receive
        queue.  It may also be used for internal  ACP  queues  or  other
        RSX-11M data structures.



        8.8  DATA TRANSFER


             The module BFCTL contains an extremely useful  routine  for
        passing  data  between  ACP's  and  the  user task.  The routine
        $BLXIO moves a block of data between any two points in a  mapped
        system.   It  is  called  with  the number of bytes to move, the
        source APR5 bias and offset, and the destination APR6  bias  and
        offset.


                                      NOTE

             The other routines  in  this  module  are  for  device
             driver  usage.   They  expect the UCB to be set up and
             should not be used by ACP's.





        8.9  TASK SCHEDULING


             The last executive services  commonly  used  by  ACP's  are
        found  in the module REQSB.  The routines in this module perform
        task scheduling.  The most useful entries  are  $EXRQF,  $EXRQP,
        and  $EXRQN.   These  routines pass an I/O packet to the receive
        queue of the requested task and schedule the task for execution.
        If  the  task  is  not  active,  it  is  run for the first time.
        Otherwise,  the  task  is  unstopped  and  potentially   becomes
        available for execution.

             Another useful routine is $STPCT.  This routine  stops  the
        current  task  and is used by ACP's to stop themselves when they
        have no work to do.  Note, when called at system state  to  stop



EXECUTIVE SERVICES                                              PAGE 8-5



        the  ACP, the routine merely marks the ACP TCB as being stopped.
        The actual rescheduling does  not  occur  until  the  ACP  exits
        system state.














                               APPENDIX A

                          READINGS/REFERENCES




             This appendix lists documents that anyone  writing  an  ACP
        should  be  familiar  with.   It  is  impossible  to  present an
        exhaustive list because "everything" one needs to know to  write
        an ACP is an intimate knowledge of the system.



        A.1  DIGITAL MANUALS


             The following is  a  list  of  the  most  relevant  RSX-11M
        manuals.   No single manual deals with the subject of ACP's.  In
        fact, the manuals contain little information directly applicable
        to ACP's.  The information concerning ACP's must be extrapolated
        from descriptions of other subjects.



        A.1.1  RSX-11M Executive Reference Manual


             This manual describes the available executive services  and
        system  directives.   It  also  presents  some  material  on the
        structure and design of the operating system.



        A.1.2  RSX-11M Crash Dump Analyzer Reference Manual


             This manual describes the use of the  Crash  Dump  Analyzer
        (CDA)  utility.  While the ACP implementor will certainly become
        very  familiar  with  crashes,  the  most  valuable  section  is
        Appendix  B  which  list the system data structures and symbolic
        offsets.



READINGS/REFERENCES                                             PAGE A-2



        A.1.3  IAS/RSX-11 I/O Operations Reference Manual


             This manual describes the use of the File Control  Services
        (FCS),  including  diagrams  of  the  FCS  data structures.  The
        manual is only important to someone interfacing an ACP to FCS.



        A.1.4  IAS/RSX-11 RMS-11 Programmer's Reference Manual


             This manual describes the  use  of  the  Record  Management
        Services  (RMS).   However,  it  contains  no information on RMS
        internals or data structures.  The manual is only  important  to
        someone interfacing an ACP to RMS.



        A.1.5  RSX-11M I/O Drivers Reference Manual


             This manual describes  each  RSX-11M  I/O  driver  and  the
        format  of  the  I/O  requests  serviced  by  each  driver.  The
        appendices contain useful summaries of all Digital  defined  I/O
        requests and error codes.



        A.1.6  RSX-11M Guide to Writing an I/O Driver


             This manual contains the information necessary to write  an
        I/O  driver.   It  also  presents  the  best  description of the
        overall I/O process.  It contains descriptions of the  I/O  data
        bases  and basic I/O flow.  This manual is a good starting point
        for anyone considering writing an ACP.



        A.1.7  RSX-11M System Logic Manuals


             This  two-volume  set  is  not  included  in  the   RSX-11M
        documentation  kit.   However,  it should be considered a "must"
        purchase for implementing an ACP.  The set contains  information
        on  the  structure  and  design  of  RSX-11M.   It also includes
        descriptions of all executive modules and data bases.



READINGS/REFERENCES                                             PAGE A-3



        A.2  SOURCES


             The final authority on RSX-11M is the source listings.  The
        RSX-11M  binary  distribution  kit  includes the sources for the
        executive, device drivers, and  MCR.   The  utility  source  kit
        supplies  sources  for all utilities, FCS, F11ACP, and the macro
        libraries.

             The sources are very well written.  This  section  mentions
        the most useful modules.



        A.2.1  Executive Sources


             A complete listing of the  executive  should  be  available
        before  writing  an  ACP.   In particular, the following modules
        should be read:

             1.  DRQIO - This module contains  all  the  QIO  processing
                 code, including the executive ACP processors.

             2.  IOSUB - This module contains all  routines  related  to
                 I/O.

             3.  DREIF - This module contains the code related  to  task
                 exit.   Of  interest  to  the  ACP  writer  is the code
                 relating to I/O cleanup.




        A.2.2  MOU Sources


             The sources for the MOU task are found on the  RSX-11M  MCR
        source disk in UIC [12,10].  The following modules comprise this
        task.

             1.  MOUROT - This module is the  root  for  the  task.   It
                 contains the dispatching code for the mount process and
                 the error handling code.

             2.  MOUPAR - This module is  the  general  parser  for  the
                 task.   It  determines the device name specified in the
                 command  line  and  dispatches   to   the   appropriate
                 device-specific parser.

             3.  MPAR11 - This module is the  command  line  parser  for
                 Files-11.



READINGS/REFERENCES                                             PAGE A-4



             4.  MPARMT - This module is the  command  line  parser  for
                 ANSI magtapes.

             5.  MPARCM - This module is the  command  line  parser  for
                 DECNET Phase I.

             6.  M11OV  -  This  module  is  the  mount  processor   for
                 Files-11.

             7.  MMTOV - This module is the  mount  processor  for  ANSI
                 magtapes.

             8.  MCMOV - This module is  the  command  line  parser  for
                 DECNET Phase I.

             9.  MDISOV - This module displays the volume attributes.




        A.2.3  DMO Sources


             The DMO task source is the module DISMNT.MAC.  This file is
        found on the MCR source volume in UIC [12,10].



        A.2.4  F11ACP Sources


             F11ACP is  the  one  Digital  ACP  for  which  sources  are
        available  at  most  sites.   The  ACP  sources are found in UIC
        [13,10] on the MCR/FCP source disk of  the  RSX-11M  V3.1  kits.
        The  source code was omitted from the RSX-11M V3.2 distribution.
        Perhaps  the  most  useful  file  is  DISPAT.MAC.   This  module
        contains the I/O packet dequeueing and dispatching code.



        A.2.5  DECNET Sources


             The DECNET sources are another example of an ACP.  However,
        the  sources  are only available by purchasing the DECNET source
        kit.  



READINGS/REFERENCES                                             PAGE A-5



        A.2.6  FCS-11 Sources


             The FCS sources are found on the RSX-11M utility source kit
        in  UIC  [50,10].  If FCS must be modified to use your ACP, this
        kit should be purchased.  FCS is very old and not written to the
        standards  used  for  other code.  The reader will find that the
        code jumps around considerably and is difficult to follow.   One
        very  useful  way  of  listing  FCS  is  to make a concantenated
        listing.  The sources contain directions for doing this.



        A.2.7  Other Sources


             The RSX-11M source distribution  kit  contains  many  other
        useful modules.  Among the most significant are the following:

             1.  [32,10] - PIP sources.

             2.  [55,10] - Command line routines (GCML, CSI).

             3.  [60,10] - PIP utility (PIPUTL) sources.

             4.  [66,10] - Macro definition files.















                               APPENDIX B

                         DATA STRUCTURE DETAILS




             This section details the features  of  data  structures  of
        interest to the ACP implementor.  Only the fields of interest to
        ACP's are discussed in this document.  Further  information  can
        be  obtained from the references listed.  A diagram is presented
        for each structure, along with information on which  macros  and
        files define the symbolic offsets, values, and bit masks.


                                      NOTE

             The macro definition files refered to are  located  on
             the  RSX-11M  Utility  Source  kit  in UIC [66,10].  A
             listing of these files is a  very  valuable  reference
             tool.

             The global definition file is the file used to  create
             an  object  module  containing  the symbols defined as
             globals.





        B.1  QIO DATA STRUCTURES


             The QIO data structures structures are used to hold the I/O
        parameters  and  route  the  request to the correct device.  The
        structures in this category  are  the  QIO  directive  parameter
        block,  the I/O packet, and the window block portion of the task
        header.



DATA STRUCTURE DETAILS                                          PAGE B-2



         






                 |===============================|
             00  |      12.      |      DIC      |
                 |-------------------------------|
             02  |       I/O Function Code       | Q.IOFN
                 |-------------------------------|
             04  |      Logical Unit Number      | Q.IOLU
                 |-------------------------------|
             06  |    Priority   |      EFN      | Q.IOEF Q.IOPR
                 |-------------------------------|
             10  |    I/O Status Block Address   | Q.IOSB
                 |-------------------------------|
             12  |         AST Address           | Q.IOAE
                 |-------------------------------|
             14  |                               | Q.IOPL
                 |---                         ---|
             16  |                               |
                 |---                         ---|
             20  |         I/O Parameters        |
                 |---                         ---|
             22  |                               |
                 |---                         ---|
             24  |                               |
                 |---                         ---|
             26  |                               |
                 |===============================|

             Symbol Definition Macro: QDPB$
             Macro  Source  Filename: RSMDIR.MAC
             Macro  Library Filename: RSXMAC.SML
             Global Definition  File: DIRDEF.MAC
             Object Library Filename: SYSLIB.OLB

                         Figure B-1
                           QIO DPB



DATA STRUCTURE DETAILS                                          PAGE B-3



        B.1.1  QIO Directive Parameter Block


             The user task constructs a QIO  directive  parameter  block
        (DPB) and issues a QIO directive whenever I/O is to be requested
        from a device.  This includes I/O requests to  ACP's.   The  QIO
        DPB  is  normally constructed by the QIO$ and QIOW$ macros.  The
        format of the QIO DPB is shown in Figure B-1.

             The following fields in the QIO DPB must be considered when
        writing an ACP:

             Q.IOFN  The I/O function is split into two bytes.  The high
                     byte   is  the  function  code  and  must  be  from
                     0-31(10).  This is the value which is used  by  the
                     executive  to  determine the action to be taken for
                     the  function.   The  low  byte  is  the   function
                     modifier.  It is not processed by the executive but
                     is passed to the driver/ACP.

                     The choice of I/O functions will depend on  whether
                     a  DCP  or UCP is being written.  DCP typically use
                     an  existing  set  of  function  codes   (such   as
                     Files-11).   Note,  DCP's  require all ACP function
                     codes to be greater than or  equal  to  seven.   In
                     fact,  $GTPKT  assumes  all  I/O request with codes
                     from 7-31(10)  issued  to  a  device  with  an  ACP
                     enabled  are  ACP  functions and dispatches them to
                     the ACP.

                     When writing a UCP, it is wise to choose a function
                     code  that  is not used by other drivers and ACP's.
                     If a I/O request is issued  to  the  wrong  device,
                     this  prevents unexpected operations from occuring.
                     The modifier byte can be used to separate  a  class
                     of    I/O   functions   into   separate   requests.
                     Currently, all function codes but 31(10) have  been
                     used  by  Digital.  However, codes above 24(10) are
                     used   only   for   specialized    functions    for
                     communications devices and real-time interfaces.

             Q.IOPL  How the I/O parameter words will be used by an  ACP
                     is  ACP dependent.  The only constraint on this set
                     of parameters is that for  transfer  functions  the
                     first  parameter  must  be a buffer address and the
                     Q.IOPL+2 must be the buffer size in bytes.

             References:

             RSX-11M Executive Reference Manual,  pages  6-90  to  6-94.
                  This  section  documents the format of the DPB and how
                  to setup the QIO macros.




DATA STRUCTURE DETAILS                                          PAGE B-4



             RSX-11M Guide to Writing a Device Driver, pages  4-6,  4-7.
                  This section documents the format of a DPB.

             RSX-11M  I/O  Drivers  Reference   Manual.    This   manual
                  documents all current, device driver QIO functions and
                  their  associated  parameter  lists.   Of   particular
                  interest  are  Appendices  A and B which summaries the
                  QIO's, their parameters, and the various error codes.

             IAS/RSX-11 I/O Operations  Reference  Manual,  Appendix  I.
                  This  appendix contains a listing of QIOSYM.MAC.  This
                  file defines all I/O function and error codes.

             RSX-11M System Logic Manual, Volume 2, pages C-41 to  C-45.
                  This  section  documents  the  various  macros used to
                  create QIO DPB's and issue the QIO request.



        B.1.2  I/O Packet


             The I/O packet is constructed by  the  executive  from  the
        information  in  the  QIO  directive  parameter  block.  The I/O
        packet is then dispatched to the proper service routine.  If  an
        ACP  is  enabled  for  a device, the service routine is the ACP.
        The format of the I/O packet is shown in Figure B-2.

             ACP's are concerned with the following  fields  in  an  I/O
        packet.   In  general, the I/O packet should be considered to be
        read-only.  The  only  exceptions  are  the  function  code  and
        parameter  fields.   These  can  be  changed  when  the  ACP  is
        reformating the request and forwarding it to a device driver.

             I.TCB   This  field  contains  the  TCB  address   of   the
                     requesting  task.   The  ACP may store this address
                     away for further reference.

             I.LN2   This is a very important field for ACP's because it
                     contains  the  address of the address of the window
                     block (see next section).  Note, that this  address
                     cannot  be  saved  but should be obtained from each
                     separate I/O packet.  Task headers may be destroyed
                     and  recreated  during task execution.  In general,
                     only the TCB address can be saved by an ACP  for  a
                     task with an active connection.



DATA STRUCTURE DETAILS                                          PAGE B-5



         






                 |===============================|
             00  |    Link to Next I/O Packet    | I.LNK
                 |-------------------------------|
             02  |      EFN      |   Priority    | I.PRI  I.EFN
                 |-------------------------------|
             04  |          TCB Address          | I.TCB
                 |-------------------------------|
             06  |   Address of Second LUT Word  | I.LN2
                 |-------------------------------|
             10  |    Address of Redirect UCB    | I.UCB
                 |-------------------------------|
             12  | Function Code |    Modifier   | I.FCN
                 |-------------------------------|
             14  |    Virtual Address of IOSB    | I.IOSB
                 |-------------------------------|
             16  |    Relocation Bias of IOSB    |
                 |-------------------------------|
             20  |     Real Address of IOSB      |
                 |-------------------------------|
             22  |    Virtual Address of AST     | I.AST
                 |-------------------------------|
             24  /                               / I.PRM
                 /     Parameters (8 words)      /
                 /                               /
                 /===============================/
             44                                    I.LGTH

             Symbol Definition Macro: PKTDF$
             Macro  Source  Filename: PKTDF .MAC
             Macro  Library Filename: EXEMC .MLB
             Global Definition  File: EXEDF .MAC
             Object Library Filename: EXELIB.OLB

                         Figure B-2
                         I/O PACKET




DATA STRUCTURE DETAILS                                          PAGE B-6



                     I.LN2 can also be used to obtained the original UCB
                     address  for the lun.  The previous location in the
                     logical  unit  table  is  the  original  lun.   The
                     redirect  chain  is  followed for every QIO request
                     and the final UCB address is stored in I.UCB.

             I.FCN   This is the I/O function issued by the user.  It is
                     copied from Q.IOFN of the QIO DPB.

             I.PRM   These are the parameters for the I/O request.  Note
                     that  eight  words  are available as opposed to the
                     original six in the  QIO  DPB.   Except  for  these
                     fields,  common  code  is  used  to fill in the I/O
                     packet.  The parameter fields are established  from
                     the   QIO  parameters  according  to  the  type  of
                     request.

                     For control functions, the six QIO  parameters  are
                     copied  unmodified to the first six locations.  For
                     transfer functions, the buffer  address  doubleword
                     is  placed  in  I.PRM+0 and I.PRM+2.  The remaining
                     five parameters are copied into  I.PRM+4,  I.PRM+6,
                     etc.

                     For  ACP's,  the  QIO  parameters   are   specially
                     processed and the results stored in the I/O packet.
                     All addresses passed as parameters must be  address
                     checked  and  relocated before the packet is queued
                     to the ACP.  In the case of a DCP, this  processing
                     takes  place  in  DRQIO.   For UCP's, the packet is
                     processed as a control function  by  the  executive
                     and  passed  to  the  driver without queueing.  The
                     driver then performs the necessary  checking,  sets
                     the  I/O  packet  parameters and send the packet to
                     the ACP.

             References:

             RSX-11M Guide to Writing a Device Driver, pages 4-2 to 4-5.
                  This  section  documents the various fields in the I/O
                  packet.

             RSX-11M Guide to Writing a Device Driver, page C-16.   This
                  section  documents  the  macro  PKTDF$.  This macro is
                  used to declare the I/O packet symbolic offsets.

             RSX-11M Crash Dump Analyzer Manual,  pages  B-39  to  B-41.
                  This  section  documents the macro PKTDF$.  This macro
                  is used to declare the I/O packet symbolic offsets.

             RSX-11M System Logic Manual, Volume 1,  pages  8-30,  8-31.
                  This  section  documents the macro PKTDF$.  This macro
                  is used to declare the I/O packet symbolic offsets.



DATA STRUCTURE DETAILS                                          PAGE B-7



                 |===============================|
             74  |         Number of LUN's       | H.NLUN
                 |-------------------------------|
             76  |          UCB Address          | H.LUN
                 |-------------------------------|
                 |         Window Address      |L|
                 |-------------------------------|
                 |                               |
                 |---                         ---|
                 |       Remaining Entries       |
                 |---            .            ---|
                 |               .               |
                 |---            .            ---|
                 |               .               |
                 |---            .            ---|

             Symbol Definition Macro: HDRDF$
             Macro  Source  Filename: HDRDF .MAC
             Macro  Library Filename: EXEMC .MLB
             Global Definition  File: EXEDF .MAC
             Object Library Filename: EXELIB.OLB

                         Figure B-3
                          LUT TABLE



        B.1.3  Logical Unit Table


             The logical unit table (LUT) is used to determine to  which
        device the I/O request is directed.  It is also used by ACP's to
        establish a logical connection  between  a  specific  LUN  in  a
        specific  task  and a I/O process (such as an open file or a NSP
        logical connection).  A diagram of the LUT  table  is  shown  in
        Figure B-3.

             The LUT table is located in the task header,  beginning  at
        offset  H.LUN.   The  previous  location,  H.NLUN,  contains the
        number of entries in the LUT table.  The LUT table consist of  a
        series  of  two  word  entries, one entry for every possible LUN
        number the task may use.  The first word of the entry is the UCB
        of the assigned device.  Note, this is not the redirected UCB.

             The second word is used for the window block address.  This
        is  the structure which is used to link a LUN to an ACP process.
        This word also serves  two  other  purposes.   The  low  bit  is
        refered  to  as  the  lock bit.  If this bit is set, another I/O
        request cannot be issued on the LUN.  The executive backs up the
        issueing  task  PC and places it in a wait-for-significant event
        state if such a request is issued.  This is very useful when  an
        ACP  must  enter  a  state  where  another  I/O packet cannot be
        processed until the current request completes.



DATA STRUCTURE DETAILS                                          PAGE B-8



                                      NOTE

             Only QIO's are effected by the lock bit.   Any  packet
             in the ACP queue for the locked lun can be dequeued by
             the ACP.  In order to effectively lock a lun, the  bit
             must  be set during the I/O packet processing prior to
             queueing to the ACP.



             The final use of the second word is to notify  ACP's  about
        abnormal  task  termination  when it has an active process for a
        lun.  If the second word of the LUT entry is non-zero (exclusive
        of the lock bit), a IO.CLN (code 3400) will be issued to the ACP
        by the executive task termination routine.



        B.2  DEVICE DATA STRUCTURES


             The device data structures structures are used to  describe
        a  generic  device  type,  each  unit, and each controller.  The
        Device Control Block (DCB) names the device and contains the I/O
        dispatch  tables.   One Unit Control Block (UCB) exists for each
        device unit and forms the data base necessary for  handling  one
        I/O  request.   The  Status  Control  Block  (SCB)  is  used  to
        coordinate activity among device controllers.



        B.2.1  Device Control Block


             One device control block (DCB) is created for each  generic
        device  type.   The  DCB supplies the device name, points to the
        device unit structures (UCB's), and controls how  I/O  functions
        will  be  processed  for  the  device.   It is the function mask
        fields (D.MSK) that are important to the ACP writer.

             In general, DCP's will set the appropriate ACP function bit
        masks.   When DRQIO matches the function against this field, the
        special processing code for ACP's is then used.  UCP's,  on  the
        otherhand,   will  mark  its  functions  as  control  functions.
        Section 4.2.1 discusses how the DCB fields should  be  setup  in
        more detail.

             References:

             RSX-11M Guide to Writing a  Device  Driver,  pages  4-8  to
                  4-15.   This  is a location by location description of
                  the DCB.  It is oriented to device drivers.



DATA STRUCTURE DETAILS                                          PAGE B-9



         






                 |===============================|
             00  |       Link to Next DCB        | D.LNK
                 |-------------------------------|
             02  |       First UCB Address       | D.UCB
                 |-------------------------------|
             04  |         Device Name           | D.NAM
                 |-------------------------------|
             06  |  High Unit #  |   Low Unit #  | D.UNIT
                 |-------------------------------|
             10  |       Length of an UCB        | D.UCBL
                 |-------------------------------|
             12  | Driver Dispatch Table Address | D.DSP
                 |-------------------------------|
             14  |   Legal Function Mask (0-15)  | D.MSK
                 |-------------------------------|
             16  |  Control Function Mask (0-15) |
                 |-------------------------------|
             20  |  NOP'ed Function Mask (0-15)  | 
                 |-------------------------------|
             22  |    ACP Function Mask (0-15)   |
                 |-------------------------------|
             24  |   Legal Function Mask (16-31) |
                 |-------------------------------|
             26  | Control Function Mask (16-31) |
                 |-------------------------------|
             30  |  NOP'ed Function Mask (16-31) | 
                 |-------------------------------|
             32  |    ACP Function Mask (16-31)  |
                 |-------------------------------|
             34  |       Driver PCB Address      | D.PCB
                 |===============================|

             Symbol Definition Macro: DCBDF$
             Macro  Source  Filename: DCBDF .MAC
             Macro  Library Filename: EXEMC .MLB
             Global Definition  File: EXEDF .MAC
             Object Library Filename: EXELIB.OLB

                         Figure B-4
                             DCB




DATA STRUCTURE DETAILS                                         PAGE B-10



             RSX-11M Guide to Writing a Device Driver, page  C-5.   This
                  section  documents  the  macro  DCBDF$.  This macro is
                  used to declare the DCB symbolic offsets.

             RSX-11M Crash Dump Analyzer Manual, pages B-8,  B-9.   This
                  section  documents  the  macro  DCBDF$.  This macro is
                  used to declare the DCB symbolic offsets.

             RSX-11M System Logic Manual, Volume 1, pages 8-34 to  8-36.
                  This  section  documents the macro DCBDF$.  This macro
                  is used to declare the DCB symbolic offsets.



        B.2.2  Unit Control Block


             The Unit Control Block (UCB) is the  key  device  structure
        and  is  very  important  to  ACP's.   There is one UCB for each
        separate device.  The UCB provides the  characteristics  of  the
        device,  pointers  to  the  other device structures, and working
        space for storing I/O related parameters.

             The UCB's are variable in length.  The following  locations
        are of concern to ACP's:

             U.CTL   Control Flags.   This  byte  contains  flags  which
                     control  how  and  when  the RSX-11M executive will
                     call  the  device  driver.   While  ACP's  are  not
                     directly  concerned  with this process, the setting
                     of these bits is important  to  correct  operation,
                     particularly  if writing a UCP.  The following bits
                     are defined for this byte:

                     UC.ALG  Alignment bit.  If this bit = 0, then  byte
                             alignment   of  data  buffers  is  allowed.
                             Otherwise,    the    buffers    must     be
                             word-aligned.   This setting is typically a
                             function  of  the  device  and  is  not  of
                             importance to ACP's.

                     UC.ATT  Attach/Detach notification.  If this bit is
                             set,  the  driver  is  called  when  $GTPKT
                             process  an  Attach/Detach  I/O   function.
                             However,  if the device is marked mountable
                             (DV.MNT=1)  and  is  mounted  (US.MNT   and
                             US.FOR=0), then attaches are never allowed.
                             The device will not be notified  regardless
                             of the state of this bit.



DATA STRUCTURE DETAILS                                         PAGE B-11



         






                 |===============================|
             -2  |   UCB Address of Owner TT:    | U.OWN
                 |-------------------------------|
             00  |          DCB Address          | U.DCB
                 |-------------------------------|
             02  |      Redirect UCB Address     | U.RED
                 |-------------------------------|
             04  |  Unit Status  | Control Flags | U.CTL  U.STS
                 |-------------------------------|
             06  |  Unit Status  |  Unit Number  | U.UNIT U.ST2
                 |-------------------------------|
             10  |    Characteristics Word #1    | U.CW1
                 |-------------------------------|
             12  |    Characteristics Word #2    | U.CW2
                 |-------------------------------|
             14  |    Characteristics Word #3    | U.CW3
                 |-------------------------------|
             16  |    Characteristics Word #4    | U.CW4
                 |-------------------------------|
             20  |          SCB Address          | U.SCB
                 |-------------------------------|
             22  |      TCB of Attached Task     | U.ATT
                 |-------------------------------|
             24  |                               | U.BUF
                 |---      Buffer Address     ---|
             26  |                               |
                 |-------------------------------|
             30  |          Byte Count           | U.CNT
                 |-------------------------------|
             32  |        ACP TCB Address        | U.ACP
                 |-------------------------------|
             34  |          VCB Address          | U.VCB
                 |===============================|

             Symbol Definition Macro: UCBDF$
             Macro  Source  Filename: UCBDF .MAC
             Macro  Library Filename: EXEMC .MLB
             Global Definition  File: EXEDF .MAC
             Object Library Filename: EXELIB.OLB

                         Figure B-5
                             UCB




DATA STRUCTURE DETAILS                                         PAGE B-12



                     UC.KIL  Unconditional Cancel I/O notification.   If
                             this  bit  is  set,  the  driver  is called
                             whenever a cancel I/O  request  is  issued,
                             even  if  the  device is not busy.  For ACP
                             enabled devices (US.MNT=0), the  I/O  queue
                             is never flushed.  However, the driver will
                             be called if the  unit  is  busy  and  will
                             always  be called if this bit is set.  This
                             feature can be used during I/O rundown (see
                             section 4.5).

                     UC.QUE  Queue bypass bit.  If this bit is set,  the
                             QIO  processor  calls  the  driver  without
                             queueing the request.  When writing an UCP,
                             this bit is set.  This allows the driver to
                             process the I/O request and send it to  the
                             ACP,   bypassing   the   normal   executive
                             processing.

                     UC.PWF  Unconditional call on power  recovery.   If
                             this  bit is set, the device driver will be
                             always be called when  power  recovers  and
                             also  whenever  the driver is loaded or the
                             system booted.  If the driver  is  involved
                             with  enabling  its  ACP, this bit provides
                             one mechanism for calling the driver so  it
                             can enable the ACP.

                     UC.NPR  NPR device.  This bit is set if the  device
                             is  an NPR device.  It determines how U.BUF
                             will be setup.  The setting of this bit  is
                             a   function  of  the  device  and  is  not
                             important to the ACP writer.

                     UC.LGH  Buffer size mask.  These bits determine the
                             required  buffer size.  They are a function
                             of the device and are not important to  the
                             ACP writer.

             U.STS   Unit status.   This  byte  contains  various  flags
                     related  to  the  status  of  the device unit.  The
                     following bits are defined:

                     US.BSY  Unit busy.   This  bit  is  set  by  $GTPKT
                             whenever  a packet is dequeued for a device
                             driver and cleared  by  $IODON/$IOALT  when
                             the  packet  is  finished.   The bit is not
                             affected by queueing a packet to an ACP and
                             is not of concern to the ACP writer.

                     US.MNT  Device mounted.  The bit is cleared  if  an
                             ACP  is  enabled  for  the unit.  It is the
                             responsibility of the ACP enabling  process



DATA STRUCTURE DETAILS                                         PAGE B-13



                             to  clear this bit.  The ACP itself usually
                             sets the bit when  it  finally  exits  (see
                             US.MDM below).

                     US.FOR  Foreign ACP.  This bit is  supposed  to  be
                             set  if non-Digital ACP's are enabled for a
                             device.   However,  the  interpretation  of
                             this bit by the executive is currently is a
                             state of flux.  For both DCP's  and  UCP's,
                             this bit should be left off.

                     US.MDM  Device marked for dismount.   This  bit  is
                             set  by  the disabling process when the ACP
                             is  initially  requested  to  be  disabled.
                             ACP's  cannot  exit until all processes are
                             terminated.   Normally,  the  ACP  examines
                             this  bit and its own internal state.  When
                             this bit is set and the ACP is idle, it may
                             then exit properly.

             U.CW1   Device characteristics word #1.  This word contains
                     bit  flags  defining the type of device.  This word
                     and other three device characteristics are returned
                     by  a GLUN$ directive.  In particular, this word is
                     used by FCS to determine the type of I/O request to
                     issue  to  the assigned device.  The following bits
                     are defined for this word.

                     DV.REC  Record-oriented device
                     DV.CCL  Carriage-control device
                     DV.TTY  Terminal device
                     DV.DIR  Directory device
                     DV.SDI  Single directory device
                     DV.SQD  Sequential device
                     DV.MXD  Mixed Massbus device
                     DV.UMD  Device supports user-mode diagnostics
                     DV.SWL  Device is software write-locked
                     DV.PSE  Pseudo device
                     DV.COM  Device mountable as DECNET Phase I device
                     DV.F11  Device mountable as Files-11 device
                     DV.MNT  Device mountable

                          These bits should be set carefully.  They  are
                     examined  in  many places and the interpretation is
                     not always consistent.  FCS  considers  any  device
                     with   DV.REC   off  to  be  a  block  I/O  device,
                     supporting  the  Files-11  QIO's.   It  also  tests
                     DV.DIR  to see if directory operations are allowed.
                     The  MOU/DMO  tasks  also  examine  the   bits   to
                     determine the proper steps to be taken.  In general
                     DV.MNT should always be set for  devices  your  ACP
                     will  service.  The remainder of the bits should be
                     setup according to the nature of the  ACP  and  its



DATA STRUCTURE DETAILS                                         PAGE B-14



                     devices.

             U.ACP   ACP TCB address.  This word  is  an  UCB  extension
                     used for mountable devices.  It is set when the ACP
                     is enabled to contain the TCB address of the ACP.

             U.VCB   VCB address.  This word is an  UCB  extension  used
                     for  mountable  devices.  It is set when the ACP is
                     enabled to contain the address of the VCB  for  the
                     unit.

             References:

             RSX-11M Guide to Writing a Device  Driver,  pages  4-19  to
                  4-26.   This  is a location by location description of
                  the UCB.  It is oriented to device drivers.

             RSX-11M Guide to Writing a Device  Driver,  pages  C-21  to
                  C-23.  This section documents the macro UCBDF$.

             RSX-11M Crash Dump Analyzer Manual,  pages  B-18  to  B-25.
                  This section documents the macro UCBDF$.

             RSX-11M System Logic Manual, Volume 1, pages 8-51 to  8-56.
                  This  section  documents the macro UCBDF$.  This macro
                  is used to declare the UCB symbolic  offsets  and  bit
                  masks.



        B.2.3  Status Control Block


             The status control block is used to control access  to  the
        hardware  controller.  ACP's are usually not concerned with this
        data structure unless they are closely  coupled  to  the  device
        driver.

             References:

             RSX-11M Guide to Writing a Device  Driver,  pages  4-15  to
                  4-19.   This  is a location by location description of
                  the SCB.  It is oriented to device drivers.

             RSX-11M Guide to Writing a Device Driver, pages C-17, C-18.
                  This  section  documents the macro SCBDF$.  This macro
                  is used to declare the SCB symbolic offsets.

             RSX-11M Crash Dump Analyzer Manual, pages B-10, B-11.  This
                  section  documents  the  macro  SCBDF$.  This macro is
                  used to declare the SCB symbolic offsets.



DATA STRUCTURE DETAILS                                         PAGE B-15



         






                 |===============================|
             00  |          Controller           | S.LHD
                 |---           I/O           ---|
             02  |        Queue Listhead         | 
                 |-------------------------------|
             04  |    Vector/4   |   Priority    | S.PRI  S.VCT
                 |-------------------------------|
             06  |  Initial TMO  |  Current TMO  | S.CTM  S.ITM
                 |-------------------------------|
             10  |     Status    |     Index     | S.CON  S.STS
                 |-------------------------------|
             12  |          CSR Address          | S.CSR
                 |-------------------------------|
             14  |  Current I/O Packet Address   | S.PKT
                 |-------------------------------|
             16  |                               | S.FRK
                 |---                         ---|
             20  |                               |
                 |---       Fork Block        ---|
             22  |                               |
                 |---                         ---|
             24  |                               |
                 |---                         ---|
             26  |                               |
                 |===============================|

             Symbol Definition Macro: SCBDF$
             Macro  Source  Filename: SCBDF .MAC
             Macro  Library Filename: EXEMC .MLB
             Global Definition  File: EXEDF .MAC
             Object Library Filename: EXELIB.OLB

                         Figure B-6
                             SCB




DATA STRUCTURE DETAILS                                         PAGE B-16



             RSX-11M System Logic Manual, Volume 1, pages 8-44 to  8-46.
                  This  section  documents the macro SCBDF$.  This macro
                  is used to declare the SCB symbolic offsets.



        B.3  ACP COMMON DATA STRUCTURES


             Two type of  data  structures  are  common  to  all  ACP's:
        window blocks and volume control blocks.  Window blocks are used
        to map a logical process to a  specific  logical  unit.   Volume
        control  blocks are used to hold information about each separate
        entity the ACP processes.  While all ACP's use these structures,
        their content is ACP dependent.

                 |===============================|
             00  |       Transaction Count       |
                 |-------------------------------|
             02  /                               /
                 /          Remainder is         /
                 /          ACP Dependent        /
                 /               .               /
                 /               .               /
                 /               .               /

                         Figure B-7
                              VCB



        B.3.1  Volume Control Block


             Typically, each mounted unit  serviced  by  an  ACP  has  a
        volume  control  block.  This is the data structure in which the
        ACP should hold information relating to each mounted  unit.   As
        such, VCB's are ACP dependent except for the first word.

             The first word  is  called  the  transaction  count.   This
        counter  is  used  by the ACP to determine whether it is idle or
        not.  For DCP's, the  counter  is  incremented  whenever  a  I/O
        request  is  queued to the DCP and decrement by the DCP when the
        request is finished.  It is also incremented by the DCP  when  a
        process  is  established  and  decremented  when  the process is
        terminated.  The DCP cannot exit unit the counter reaches zero.

             The executive does not  touch  the  transaction  count  for
        UCP's,  however,  it  is  recommended  that  the  UCP's  use the
        transaction count for the same purpose.  It is important that an
        ACP never exit with I/O requests still outstanding in its queue.
        These requests will never be terminated,  leaving  the  issueing
        task stuck in I/O rundown.



DATA STRUCTURE DETAILS                                         PAGE B-17



                 |===============================|
             00  /                               /
                 /           Totally             /
                 /        ACP Dependent          /
                 /               .               /
                 /               .               /
                 /               .               /

                         Figure B-8
                        WINDOW BLOCK



        B.3.2  Window Block


             One of the most useful features of an ACP is the ability to
        establish  an  I/O  process  and  tie various I/O request to the
        process.  In the case  of  Files-11,  this  takes  the  form  of
        opening a file, reading and writing blocks and closing the file.
        For DECNET, logical links  are  created,  data  transmitted  and
        received, and the link closed.

             The window block  is  the  data  structure  used  for  such
        processes.   It  ties  the  task's  LUN to a particular process.
        However, the format of window blocks and how they are  allocated
        and deallocated is ACP dependent.

             The window block address is stored in the  second  word  of
        the LUT entry.  The address of this word is passed to the ACP in
        the I/O packet.  While typically the window  is  allocated  from
        the  executive's  pool but this need not be true.  The executive
        never references window address, therefore, the window may  come
        the  the  ACP's address space.  However, if access to the window
        is needed in processing the I/O request, the window will have to
        come from the pool.



        B.4  OTHER DATA STRUCTURES


             This is a broad category of every thing  else.   ACP's  are
        privileged  task  and  have  the ability to examine, modify, and
        create any structure necessary.  Some of the most important  are
        mentioned.



DATA STRUCTURE DETAILS                                         PAGE B-18



        B.4.1  Clock Queue Entry


             ACP's often have a requirement for keeping internal timers,
        particularly  for  event timeouts.  One mechanism for doing this
        is to use the mark time and event flag directives like a  normal
        task.   An  alternative  mechanism is to issue an internal timer
        request.  When this request  expires,  an  executive  or  device
        driver routine is called.  The format of such a request is shown
        below.

             When the internal timer mechanism is used, a  linkage  must
        be  made  between  the kernel code servicing the timer event and
        the ACP.  One method for doing this is for the device driver  to
        issue  a  special  I/O  request  to the ACP that signifies timer
        service.




                 |===============================|
             00  |       Clock Queue Link        | C.LNK
                 |-------------------------------|
             02  |  EFN (Unused) | Request Type  | C.RQT C.EFN
                 |-------------------------------|
             04  |  TCB or System Subroutine ID  | C.TCB
                 |-------------------------------|
             06  |                               | C.TIM
                 |--- Absolute Time Entry Due ---|
             10  |                               |
                 |-------------------------------|
             12  |       Subroutine Address      | C.SUB
                 |-------------------------------|
             14  |         Relocation Base       | C.AR5
                 |-------------------------------|
             16  |            Unused             |
                 |===============================|
             20                                    C.LGTH

             Symbol Definition Macro: CLKDF$
             Macro  Source  Filename: CLKDF .MAC
             Macro  Library Filename: EXEMC .MLB
             Global Definition  File: EXEDF .MAC
             Object Library Filename: EXELIB.OLB

                         Figure B-9
                       CLOCK QUEUE ENTRY




DATA STRUCTURE DETAILS                                         PAGE B-19



             The advantage of the internal method is related to the  ACP
        stop  mechanism.   When  idle,  ACP's can be swapped out and not
        brought back until there is something to do.   However,  if  the
        ACP   maintains   a  constant  timer,  it  will  be  swapped  in
        continuely, even if idle.  If the timer is moved  to  a  driver,
        the driver can have the intelligance to notify the ACP only when
        an actual timer event processing is needed.

             References:

             RSX-11M Guide to Writing a Device Driver, pages  C-3,  C-4.
                  This  section  documents the macro CLKDF$.  This macro
                  is used to declare  the  clock  queue  entry  symbolic
                  offsets and bit masks.

             RSX-11M Crash Dump Analyzer Manual, pages B-26, B-27.  This
                  section  documents  the  macro  CLKDF$.  This macro is
                  used to declare the clock queue entry symbolic offsets
                  and bit masks.

             RSX-11M System Logic Manual, Volume 1,  pages  8-31,  8-32.
                  This  section  documents the macro CLKDF$.  This macro
                  is used to declare  the  clock  queue  entry  symbolic
                  offsets and bit masks.



        B.4.2  Partition Control Block


             The Partition Control Block (PCB)  defines  how  memory  is
        allocated.  It also provides the linkage between the TCB and the
        task header.   Typically,  ACP's  are  unconcerned  with  PCB's,
        however, special applications may involve their usage.

             References:

             RSX-11M Guide to Writing a Device Driver, pages C-14, C-15.
                  This  section  documents the macro PCBDF$.  This macro
                  is used to declare the PCB symbolic  offsets  and  bit
                  masks.

             RSX-11M Crash Dump Analyzer Manual,  pages  B-12  to  B-15.
                  This  section  documents the macro PCBDF$.  This macro
                  is used to declare the PCB symbolic  offsets  and  bit
                  masks.

             RSX-11M System Logic Manual, Volume 1, pages 8-41 to  8-43.
                  This  section  documents the macro PCBDF$.  This macro
                  is used to declare the PCB symbolic  offsets  and  bit
                  masks.



DATA STRUCTURE DETAILS                                         PAGE B-20



         




                 |===============================|
             00  |       Link to Next PCB        | P.LNK
                 |-------------------------------|
             02  |   I/O Count   |   Priority    | P.PRI  P.IOC
                 |-------------------------------|
             04  |                               | P.NAM
                 |---     Partition Name      ---|
             06  |                               |
                 |-------------------------------|
             10  |  Pointer to Next Subpartition | P.SUB
                 |-------------------------------|
             12  |   Pointer to Main Partition   | P.MAIN
                 |-------------------------------|
             14  |     Starting Address Bias     | F.REL
                 |-------------------------------|
             16  |       Size of Partition       | P.BLKS
                 |-------------------------------|
             20  |                               | P.WAIT
                 |---  Partition Wait Queue   ---|
             22  |                               |
                 |-------------------------------|
             24  |       Partition Swap Size     | P.SWSZ
                 |-------------------------------|
             26  |       Partition Busy Flags    | P.BUSY
                 |-------------------------------|
             30  |   TCB Address of Owning Task  | P.OWN
                 |-------------------------------|
             32  |      Partition Status Flags   | P.STAT
                 |-------------------------------|
             34  |      Address of Task Header   | P.HDR
                 |-------------------------------|
             36  |       Protection Word         | P.PRO
                 |-------------------------------|
             40  |                               | P.ATT
                 |---  Attachment Descriptors ---|
             42  |                               |
                 |===============================|

             Symbol Definition Macro: PCBDF$
             Macro  Source  Filename: PCBDF .MAC
             Macro  Library Filename: EXEMC .MLB
             Global Definition  File: EXEDF .MAC
             Object Library Filename: EXELIB.OLB

                         Figure B-10
                              PCB



DATA STRUCTURE DETAILS                                         PAGE B-21



        B.4.3  Task Control Block


             The Task Control Block is the primary data structure for  a
        task.   ACP's  are  tasks  and  have  a TCB.  Besides the normal
        treatment,  the  ACP's  TCB  receives  the   following   special
        treatment.

             1.  The address of the ACP's TCB is stored in the  UCB  for
                 each  enabled device.  The address is used to determine
                 to which task to queue the I/O request.

             2.  The I/O packets are  queued  to  the  ACP  through  the
                 receive  queue listhead (T.RCVL) and deallocated by the
                 ACP by removing an entry from this queue.

             3.  ACP's are marked by a special bit in the  third  status
                 word  (T.ST3).   This  bit  (T3.ACP) is used to prevent
                 tasks from  sending  messages  to  the  ACP.   This  is
                 necessary  to prevent confusion resulting from multiple
                 usage of the receive queue.  The bit is set by the task
                 builder /AC switch.

             4.  For certain Digital ACP's (F11ACP, MTAACP), the  second
                 event  flag word (T.EFLG+2) is used as a mounted volume
                 counter and therefore event  flags  16-31(10)  are  not
                 used.    However,  this  restriction  applies  only  if
                 desired.


             References:

             RSX-11M Guide to Writing a Device Driver, pages C-19, C-20.
                  This  section  documents the macro TCBDF$.  This macro
                  is used to declare the TCB symbolic  offsets  and  bit
                  masks.

             RSX-11M Crash Dump Analyzer Manual,  pages  B-15  to  B-17.
                  This  section  documents the macro TCBDF$.  This macro
                  is used to declare the TCB symbolic  offsets  and  bit
                  masks.

             RSX-11M System Logic Manual, Volume 1, pages 8-47 to  8-49.
                  This  section  documents the macro TCBDF$.  This macro
                  is used to declare the TCB symbolic  offsets  and  bit
                  masks.



DATA STRUCTURE DETAILS                                         PAGE B-22



                 |===============================|
             00  |       Utility Link Word       | T.LNK
                 |-------------------------------|
             02  |   I/O Count   |   Priority    | T.PRI  T.IOC
                 |-------------------------------|
             04  |         Checkpoint PCB        | T.CPCB
                 |-------------------------------|
             06  |                               | T.NAM
                 |---      Task Name          ---|
             10  |                               |
                 |-------------------------------|
             12  |                               | T.RCVL
                 |--- Receive Queue Listhead  ---|
             14  |                               |
                 |-------------------------------|
             16  |                               | T.ASTL
                 |---   AST Queue Listhead    ---|
             20  |                               |
                 |-------------------------------|
             22  |                               | T.EFLG
                 |---    Local Event Flags    ---|
             24  |                               |
                 |-------------------------------|
             26  |       TI: UCB Address         | T.UCB
                 |-------------------------------|
             30  |     Task List Thread Word     | T.TCBL
                 |-------------------------------|
             32  |  Status Word (Blocking Bits)  | T.STAT
                 |-------------------------------|
             34  |    Status Word (State Bits)   | T.ST2
                 |-------------------------------|
             36  |  Status Word (Attribute Bits) | T.ST3
                 |-------------------------------|
             40  |               | Def. Priority | T.DPRI T.LBN
                 |               |---------------|
             42  |       LBN of Load Image       |
                 |-------------------------------|
             44  |   UCB Address of Load Device  | T.LDV
                 |-------------------------------|
             46  |         PCB Address           | T.PCB
                 |-------------------------------|
             50  |       Maximum Task Size       | T.MXSZ
                 |-------------------------------|
             52  |   Pointer to Next Active TCB  | T.ACTL
                 |-------------------------------|
             54  |    Specified AST Listhead     | T.SAST
                 |-------------------------------|
         
                         Figure B-11
                              TCB



DATA STRUCTURE DETAILS                                         PAGE B-23



                 |-------------------------------|
             56  |                               | T.ATT
                 |---  Attachment Listhead    ---|
             60  |                               |
                 |-------------------------------|
             62  | Task Image Partition Offset   | T.OFF
                 |-------------------------------|
             64  |   EFN Count   |    Unused     |        T.SRCT
                 |-------------------------------|
             66  |                               | T.RRFL
                 |--- Receive by Ref Listhead ---|
             70  |                               |
                 |-------------------------------|
             72  |                               | T.OCBH
                 |--- Offspring Control List  ---|
             74  |                               |
                 |-------------------------------|
             76  |       Offspring Count         | T.RDCT
                 |===============================|
             100                                   T.LGTH

             Symbol Definition Macro: TCBDF$
             Macro  Source  Filename: TCBDF .MAC
             Macro  Library Filename: EXEMC .MLB
             Global Definition  File: EXEDF .MAC
             Object Library Filename: EXELIB.OLB

                         Figure B-11
                              TCB



DATA STRUCTURE DETAILS                                         PAGE B-24



        B.4.4  Task Header


             The task header contains the context of the task.  The most
        important  thing to remember about task headers is that they are
        destroyed when a task is checkpointed and recreated when  it  is
        swapped  in.   Therefore,  ACP's cannot store the address of the
        header (or the LUT table) for later use.

             References:

             RSX-11M Guide to Writing a Device Driver, pages C-9,  C-10.
                  These  sections document the macro HDRDF$.  This macro
                  is used to declare the task header symbolic offsets.

             RSX-11M Crash Dump  Analyzer  Manual,  pages  B-4  to  B-6.
                  These  sections document the macro HDRDF$.  This macro
                  is used to declare the task header symbolic offsets.

             RSX-11M System Logic Manual, Volume 1,  pages  8-49,  8-50.
                  These  sections document the macro HDRDF$.  This macro
                  is used to declare the task header symbolic offsets.



DATA STRUCTURE DETAILS                                         PAGE B-25



                 |===============================|
             00  |    Current Stack Pointer      ! H.CSP
                 |-------------------------------|
             02  |         Header Length         ! H.HDLN
                 |-------------------------------|
             04  |                               | H.EFLM
                 |---    Event Flag Masks     ---|
             06  |                               |
                 |-------------------------------|
             10  |       Current Task UIC        | H.CUIC
                 |-------------------------------|
             12  |       Default Task UIC        ! H.DUIC
                 |-------------------------------|
             14  |         Initial PS            | H.IPS
                 |-------------------------------|
             16  |         Initial PC            | H.IPC
                 |-------------------------------|
             20  |         Initial SP            | H.ISP
                 |-------------------------------|
             22  |    ODT SST Vector Address     | H.ODVA
                 |-------------------------------|
             24  |    ODT SST Vector Length      | H.ODVL
                 |-------------------------------|
             26  |   Task SST Vector Address     | H.TKVA
                 |-------------------------------|
             30  |   Task SST Vector Length      | H.TKVL
                 |-------------------------------|
             32  |  Powerfail AST Block Address  | H.PFVA
                 |-------------------------------|
             34  |      FPP AST Block Address    | H.FPVA
                 |-------------------------------|
             36  |   Receive AST Block Address   | H.RCVA
                 |-------------------------------|
             40  |    Event Flag Save Address    | H.EFSV
                 |-------------------------------|
             42  |      FPP/EAE Save Address     | H.FPSA
                 |-------------------------------|
             44  |   Pointer to Number Windows   | H.WND
                 |-------------------------------|
             46  |             DSW               | H.DSW
                 |-------------------------------|
             50  |       FCS Impure Pointer      | H.FCS
                 |-------------------------------|
             52  |     Fortran Impure Pointer    | H.FORT
                 |-------------------------------|
             54  |     Overlay Impure Pointer    | H.OVLY
                 |-------------------------------|
             56  |  Work Area Extension Pointer  | H.VEXT
                 |-------------------------------|

                         Figure B-12
                         TASK HEADER



DATA STRUCTURE DETAILS                                         PAGE B-26



                 |-------------------------------|
             60  |  Mailbox LUN  | Swapping Pri. | H.SPRI H.NML
                 |-------------------------------|
             62  |   Rec/Ref AST Block Address   | H.RRVA
                 |-------------------------------|
             64  /                               /
                 /          Reserved             /
                 /                               /
                 |-------------------------------|
             72  |    Pointer to Guard Word      | H.GARD
                 |-------------------------------|
             74  |       Number of LUN's         | H.LUN
                 |-------------------------------|
             76  /                               /
                 /         LUT Table             /
                 /                               /

             Symbol Definition Macro: HDRDF$
             Macro  Source  Filename: HDRDF .MAC
             Macro  Library Filename: EXEMC .MLB
             Global Definition  File: EXEDF .MAC
             Object Library Filename: EXELIB.OLB

                         Figure B-12
                         TASK HEADER














                               APPENDIX C

                             FCS-11 MODULES




             The File Control Services are a set of routines  which  are
        linked  to a task to perform various I/O services.  The routines
        are typically called via macros.  The documentation for  FCS  is
        found in the IAS/RSX-11 I/O Operation Reference Manual.

             There are two levels of  FCS  routines.   The  upper  level
        routines  are  called directly by the user's task or via the FCS
        macros.  These routines are named  '.XXXXX'.   The  lower  level
        routines  are intended for FCS's own use and are not expected to
        be called directly  by  the  user.   These  routines  are  named
        '..XXXX'.  This appendix describes each FCS module, its entries,
        and their calling parameters and function.   The  appendix  also
        discusses  the  FCS  data  structures  and  some  basic internal
        concepts.



        C.1  FCS CONDITIONALS


             Each  FCS  module  is  assembled  with  the   prefix   file
        FCSPRE.MAC.   The  file establishes various symbolic definitions
        and common macros and defines the assembly control  flags.   FCS
        is  very  heavily conditionally assembled.  The symbols used and
        their default RSX-11M values are as follows:

             R$$ANI ANSI magtape support.  This variable is set to  zero
                    for no support and to one if ANSI magtape support is
                    desired.  The default for RSX-11M is zero unless the
                    ANSI prefix file, ANSPRE.MAC, is used for assembly.

             R$$BBF Big buffer support.  This feature is  used  for  I/O
                    devices  that  support  block sizes greater then 512
                    bytes.  The variable is set to zero for  no  support
                    and  to  one if support is desired.  The default for
                    RSX-11M  is  zero  unless  the  ANSI  prefix   file,
                    ANSPRE.MAC, is used for assembly.

             R$$DPB QIO DPB format.  This variable is set  to  zero  for



FCS-11 MODULES                                                  PAGE C-2



                    old  style  QIO's  and  to  one  for the new QIO DPB
                    format.   At  this  time,  all  systems   (including
                    RSX-11M) use the new format.

             R$$EIS Extended  Instruction  Set  (EIS)   support.    This
                    variable  is  set  to  zero  if  no EIS instructions
                    should be used by FCS and to one if EIS instructions
                    are  allowed.   RSX-11M always sets this variable to
                    zero.

             R$$ELP Extened parsing support.  This variable  is  set  if
                    extended  parsing  support  for  VAX/VMS  systems is
                    desired.  RSX-11M always sets this variable to zero.

             R$$LCL Force local definition of symbols.  This variable is
                    set  to  zero if global definitions for FCS variable
                    should be used  and  to  one  if  local  definitions
                    should be declared in FCSPRE.MAC.  RSX-11M sets this
                    variable to one.

             R$$MPL RSX-11M PLUS support.  This variable is set  to  one
                    if  FCS  should  be  assembled  for  an RSX-11M PLUS
                    system.  RSX-11M always sets this variable to zero.

             R$$MUL Multiple buffering support.  This variable is set to
                    zero  if  FCS supports only one I/O block buffer and
                    non-zero if multiple I/O buffers are supported.  The
                    symbol  R$$MBF  is  equated to this symbol.  RSX-11M
                    always sets this variable to zero.

             R$$NAM Named directory support.  This variable is  set  one
                    or  two  for  named  directory  support.   This is a
                    feature of  the  SCS-11  version  of  FCS.   RSX-11M
                    always sets this variable to zero.

             R$$OPF Type of open.  This variable is used to control  the
                    type  of  assembly  desired for the module OPEN.  If
                    set to zero, the normal OPEN routine  is  assembled.
                    Otherwise,  a value of one (OPFNB.MAC) assembles the
                    open by FNB and a value of two (OPFID.MAC) assembles
                    the open by FID module.  This variable is not set in
                    FCSPRE.MAC.

             R$$RSL Assemble  for  SYSLIB  or  resident  library.   This
                    variable  is  set to zero if FCS should be assembled
                    for placement in SYSLIB.OLB or  one  if  a  resident
                    library  should  be  built from FCS.  RSX-11M always
                    sets this variable  to  one.   This  causes  FCS  to
                    assembled using the PSECT $$RESL.

             R$$SCS SCS-11 support.  This variable is set to one if  FCS
                    should be assembled for the SCS-11 operating system.
                    RSX-11M always sets the variable to zero.



FCS-11 MODULES                                                  PAGE C-3



             R$$SEQ Type of file I/O.  This variable is used to  control
                    the  type  of  assembly  desired for the GET and PUT
                    modules.  If set to zero, the modules  support  both
                    sequential  and  random  I/O.  If set to one (PUTSQ,
                    GETSQ), the modules  are  restricted  to  sequential
                    I/O.  This variable is not set in FCSPRE.MAC.

             R$$SPL Automatic spooling support.  This variable is set to
                    zero if no automatic spooling support is desired and
                    to one if it is supported.  RSX-11M always sets this
                    variable  to  zero,  support  of  automatic spooling
                    requires the IAS spooling mechanism.

             R$$VMS VAX/VMS support.  This variable is set to one if FCS
                    should  be  assembled  for VAX/VMS operating system.
                    RSX-11M always sets this variable to zero.

             R$$11M RSX-11M support.  This variable is set  to  zero  if
                    IAS support is desired and to one if RSX-11M support
                    is to be generated.  Naturally,  RSX-11M  sets  this
                    variable to one.

             Figure  C-1  summarizes  the  default  conditional   switch
        settings  for  the  five operating systems supported by FCS.  In
        general, RSX-11M sets the FCS conditional  symbols  to  assemble
        the  simplest version of FCS.  It is unclear what will happen if
        some of the more useful features (R$$EIS,  R$$SPL,  R$$MUL)  are
        turned on and used in an RSX-11M system.

        +--------+---------+----------+----------+----------+---------+
        |        | RSX-11M | RSX-11M+ |  SCS-11  | VAX/VMS  | IAS/11D |
        |--------+---------+----------+----------+----------+---------|
        | R$$11M |    1    |    1     |     1    |    1     |    0    |
        | R$$MPL |    0    |    1     |     0    |    0     |    0    |
        | R$$SCS |    0    |    0     |     1    |    0     |    0    |
        | R$$VMS |    0    |    0     |     0    |    1     |    0    |
        |--------+---------+----------+----------+----------+---------|
        | R$$ANI |    0    |    0     |     0    |    1     |    1    |
        | R$$BBF |    0    |    0     |     0    |    0     |    0    |
        | R$$DPB |    1    |    1     |     1    |    1     |    1    |
        | R$$EIS |    0    |    0     |     1    |    0     |    1    |
        | R$$ELP |    0    |    0     |     1    |    0     |    0    |
        | R$$LCL |    1    |    1     |     1    |    1     |    1    |
        | R$$MPL |    0    |    0     |     0    |    0     |    1    |
        | R$$NAM |    0    |    0     |     2    |    0     |    0    |
        | R$$RSL |    1    |    1     |     1    |    1     |    0    |
        | R$$SPL |    0    |    0     |     0    |    0     |    1    |
        +--------+---------+----------+----------+----------+---------+

                               FIGURE C-1
                        FCS DEFAULT CONDITIONALS



FCS-11 MODULES                                                  PAGE C-4



        C.2  FCS DATA STRUCTURES


             <To be written>



        C.2.1  File Descriptor Block


             <To be written>



        C.2.2  Filename Block


             <To be written>



        C.2.3  Dataset Descriptor


             <To be written>



        C.2.4  $$FSR1 Region


             <To be written>



        C.2.5  $$FSR2 Region


             <To be written>




FCS-11 MODULES                                                  PAGE C-5



                 |===============================|
             00  |  Record Attr. |  Record Type  | F.RTYP F.RATT
                 |-------------------------------|
             02  |          Record Size          | F.RSIZ
                 |-------------------------------|
             04  |                               | F.HIBK
                 |---  Highest VBN Allocated  ---|
             06  |                               |
                 |-------------------------------|
             10  |                               | F.EFBK
                 |---     EOF Block Number    ---|
             12  |                               |
                 |-------------------------------|
             14  |  First Free Byte in EOF Block | F.FFBY
                 |-------------------------------|
             16  |  Device Chars | Record Access | F.RACC F.RCTL
                 |-------------------------------|
             20  |  Block I/O Buffer Descriptor  | F.BKDS/F.NRBD
                 |---            or           ---|
             22  | User-record Buffer Descriptor |
                 |-------------------------------|
             24  | Block I/O Status & AST Addr.  | F.BKST/F.NRBD
                 |---            or              |
             26  | Next-record Buffer Descriptor |
                 |-------------------------------|
             30  | Buffer Size/Next Record Addr. | F.OVBS/F.NREC
                 |-------------------------------|
             32  |       End-of-block Value      | F.EOBB
                 |-------------------------------|
             34  | Create Quantity & Statistics  | F.CNTG/F.RCNM
                 |---            or           ---|
             36  |          Record Number        | F.STBK
                 |-------------------------------|
             40  |       Extend Quantity         | F.ALOC
                 |-------------------------------|
             42  |  File Access  |  LUN Number   | F.LUN  F.FACC
                 |-------------------------------|
             44  |   Dataset Descriptor Pointer  | F.DSPT
                 |-------------------------------|
             46  |  Default Filename Block Addr. | F.DFNB
                 |-------------------------------|
             50  |  Bookkeeping  |    EFN        | F.BKEF F.BKP1
                 |-------------------------------|
             52  |          Error Word           | F.ERR
                 |-------------------------------|

                         Figure C-2
                              FDB



FCS-11 MODULES                                                  PAGE C-6



                 |-------------------------------|
             54  |  Buffer Count | Mul. Buf. No. | F.MBCT F.MBC1
                 |-------------------------------|
             56  |   Reserved    | Mul. Buf. Bit | F.MBFG F.BGBC
                 |-------------------------------|
             60  |       Device Buffer Size      | F.VBSZ
                 |-------------------------------|
             62  |       Block  Buffer Size      | F.BBSZ
                 |-------------------------------|
             64  |                               | F.BKVB/F.VBN
                 |---       VBN Number        ---|
             66  |                               |
                 |-------------------------------|
             70  |    Block Buffer Descriptor    | F.BDB
                 |-------------------------------|
             72  |        Spooling Device        | F.SPDV
                 |-------------------------------|
             74  |   Reserved    | Spooling Unit | F.SPUN F.CHR
                 |-------------------------------|
             76  |          Control Bits         | F.ACTL
                 |-------------------------------|
             100 |         Sequence Number       | F.SEQN
                 |===============================|
             102            Start of FNB           F.FNB

             Symbol Definition Macro: FCSBT$, FDOFF$
             Macro  Source  Filename: FCSMAC.MAC
             Macro  Library Filename: RSXMAC.SML
             Global Definition  File: FCSGBL.MAC
             Object Library Filename: SYSLIB.OLB

                                 Figure C-2
                                     FDB




FCS-11 MODULES                                                  PAGE C-7



                 |===============================|
             00  |                               | N.FID
                 |---                         ---|
             02  |           File-ID             |
                 |---                         ---|
             04  |                               |
                 |-------------------------------|
             06  |                               | N.FNAM
                 |---                         ---|
             10  |          Filename             |
                 |---                         ---|
             12  |                               |
                 |-------------------------------|
             14  |          File Type            | N.FTYP
                 |-------------------------------|
             16  |           Version             | N.FVER
                 |-------------------------------|
             20  |           Status              | N.STAT
                 |-------------------------------|
             22  |          Next File            | N.NEXT
                 |-------------------------------|
             24  |                               | N.DID
                 |---                         ---|
             26  |         Directory ID          |
                 |---                         ---|
             30  |                               |
                 |-------------------------------|
             32  |         Device Name           | N.DVNM
                 |-------------------------------|
             34  |         Unit Number           | N.UNIT
                 |===============================|

             Symbol Definition Macro: FCSBT$, NBOFF$
             Macro  Source  Filename: FCSMAC.MAC
             Macro  Library Filename: RSXMAC.SML
             Global Definition  File: FCSGBL.MAC
             Object Library Filename: SYSLIB.OLB

                         Figure C-3
                              FNB



FCS-11 MODULES                                                  PAGE C-8



         




















                 |===============================|
             00  |     Device String Length      | N.DEVD
                 |-------------------------------|
             02  |     Device String Address     |
                 |-------------------------------|
             04  |   Directory String Length     | N.DIRD
                 |-------------------------------|
             06  |   Directory String Address    |
                 |-------------------------------|
             10  |    Filename String Length     | N.FNMD
                 |-------------------------------|
             12  |    Filename String Address    |
                 |===============================|

             Symbol Definition Macro: FDSOF$
             Macro  Source  Filename: FCSMAC.MAC
             Macro  Library Filename: RSXMAC.SML
             Global Definition  File: FCSGBL.MAC
             Object Library Filename: SYSLIB.OLB

                         Figure C-4
                      DATASET DESCRIPTOR



FCS-11 MODULES                                                  PAGE C-9



         










                 |===============================|
             00  |                               |
                 |---    I/O Status Block     ---|
             02  |                               |
                 |-------------------------------|
             04  |                               | B.VBN
                 |---   Virtual Block Number  ---|
             06  |                               |
                 |-------------------------------|
             10  |      Address of Next Buffer   | B.NXBD
                 |-------------------------------|
             12  | Buffer Status |     Empty     |        B.BFST
                 |-------------------------------|
             14  |             Empty             |
                 |-------------------------------|
             16  /       Start of I/O Buffer     / S.BFHD
                 /               .               /
                 /               .               /
                 /               .               /

             Symbol Definition Macro: BDOFF$
             Macro  Source  Filename: FCSMAC.MAC
             Macro  Library Filename: RSXMAC.SML
             Global Definition  File: FCSGBL.MAC
             Object Library Filename: SYSLIB.OLB

                         FIGURE C-5
                           $$FSR1



FCS-11 MODULES                                                 PAGE C-10



         










                 |===============================|
             00  |                               |
                 |---   Allocation Listhead   ---|
             02  |                               |
                 |-------------------------------|
             04  |     First Address in FSR1     | A.BFSR
                 |-------------------------------|
             06  |     Last  Address in FSR1     | A.EFSR
                 |-------------------------------|
             10  |       File Owner UIC          | A.OWUI
                 |-------------------------------|
             12  |   Default File Protection     | A.FIPR
                 |-------------------------------|
             14  /                               / A.DPB
                 /   Scratch Area and QIO DPB    /
                 /                               /
                 |-------------------------------|
             44  |                               | A.IOST
                 |--- Scratch I/O Status Area ---|
             46  |                               |
                 |-------------------------------|
             50  /                               / A.DFDR
                 / Default Directory Information /
                 /                               /
                 |-------------------------------|
             100 |    Default Buffer Count       | A.DFBC
                 |-------------------------------|
             102 |      Default Task UIC         | A.DFUI
                 |===============================|

             Symbol Definition Macro: FSROF$
             Macro  Source  Filename: FCSMAC.MAC
             Macro  Library Filename: RSXMAC.SML
             Global Definition  File: FCSGBL.MAC
             Object Library Filename: SYSLIB.OLB

                         FIGURE C-6
                           $$FSR2



FCS-11 MODULES                                                 PAGE C-11



        C.3  FCS INTERNALS


             <To be written>



        C.4  FCS MODULES


             The remainder of  this  appendix  covers  each  FCS  source
        module.   For  each  module,  the  calling  label and inputs and
        outputs are detailed



        C.4.1  ANSPAD


             This routine pads the rest of the buffer for  magtape  ANSI
        "D" format.  It is only generated if magtape support (R$$ANI) is
        selected.


             Entry:  ..ANSP

             Input:  R0 = FDB address

                     F.NREC(R0) = Starting address in buffer to pad
                     F.EOBB(R0) = Byte address beyond end of buffer

             Output: C = 0, If buffer padded
                       = 1, If buffer not padded

                     R0-R4 preserved, R5 destroyed

             Conditionals: R$$ANI



        C.4.2  ASCPPN


             This routine translates  an  UIC  string  in  the  form  of
        "[200,210]"  to the binary equivalent.  Both the group and owner
        numbers are assumed to be octal unless followed by a period.  In
        this case, the numbers are translated as decimal.  The output is
        stored in ".BYTE owner,group" form.


             Entry:  .ASCPP

             Input:  R2 = Address of UIC string descriptor



FCS-11 MODULES                                                 PAGE C-12



                     R3 = Address to return the binary UIC

                     0(R2) = Size of UIC string
                     2(R2) = Address of UIC string

             Output: C = 0, String converted and value stored
                       = 1, UIC string syntax error

                     All registers preserved

             Conditionals: None



        C.4.3  ASCR50


             This routine converts an ASCII string to RAD50  and  stores
        in the specified location(s).


             Entry:  ..SGR5

             Input:  R2 = Address of ASCII string
                     R3 = Size of ASCII string
                     R4 = Starting address to store RAD50 string

                     The storage area must be previously zeroed.

             Output: C = 0, Conversion complete
                       = 1, Conversion failed, nonalphanumeric character

                     R4 = Address of last word written in RAD50

                     R0,R1 preserved, R2,R3,R5 destroyed

             Conditionals: R$$EIS



        C.4.4  ASSLUN


             This routine assigns the lun in F.LUN of  the  FDB  to  the
        device  specified  by  the  filename  block.   If  no  device is
        specified, the previously assigned device is used.  If no device
        was assigned, the default device (SY:) is assigned.

             Once the device is assigned, the device characteristics are
        stored in the FDB.  Specifically, the low byte of the the device
        characteristics (U.CW1) is  stored  in  F.RCTL  and  the  device
        buffer  size  (U.CW4) is stored in F.VBSZ and F.BBFS.  Also, the
        true device name and unit are stored in the filename block.



FCS-11 MODULES                                                 PAGE C-13



             Entry:  .ASLUN,..ALUN

             Input:  R0 = FDB address
                     R1 = FNB address

                     N.UNIT(R1) = Device unit number
                     N.DVNM(R1) = Device name or 0 if none

             Output: C = 0, Assign successful
                       = 1, Bad device name

                     F.RCTL(R0) = Device characteristics
                     F.VBSZ(R0) = Device block size
                     F.BBSZ(R0) = Device block size

                     If entry at .ASLUN, all registers preserved

                     If entry at ..ALUN, R0,R1 preserved, R2-R5
                     destroyed

             Conditionals: R$$ANI,R$$SPL,R$$11M



        C.4.5  BDBREC


             This routine sets up the block buffer header  and  the  FDB
        for the next virtual block I/O.


             Entry:  ..BDRC

             Input:  R0 = FDB address
                     R1 = Buffer descriptor address

             Output: B.VBN(R1)  = Set to F.VBN(R0)
                     B.BBFS(R1) = Set to F.BBFS(R0)
                     F.NREC(R0) = Set to start of I/O buffer
                     F.EOBB(R0) = Set to end of I/O buffer

                     R0,R2-R5 preserved, R1 destroyed

             Conditionals: None



        C.4.6  BIGBUF


             This  module  contains  routines  used  for  large   buffer
        support.   This  support  is not enabled for RSX-11M (R$$BBF>0).
        INMBB checks for a specified VBN in the  block  buffer.   RSTEOF



FCS-11 MODULES                                                 PAGE C-14



        correctly processes EOF's for large buffer I/O.



        C.4.7  BKRG


             This routine sets up the registers for block I/O, using the
        block buffer definition in the FDB.


             Entry:  ..BKRG

             Input:  R0 = FDB address

                     F.BDB(R0) = Buffer descriptor address

             Output: R1 = Address of I/O buffer
                     R2 = Buffer size (F.BBFS)
                     R3 = Carriage control, always set to zero

                     R0,R4,R5 preserved

             Conditionals: None



        C.4.8  CKALOC


             This module contains routines to allocate blocks to a file.
        The routines are designed for internal FCS usage.

             The ..ALOC and ..ALC1 routines are used to allocate  blocks
        if necessary.  The desired allocation is compared to the current
        allocation and more blocks are allocated if necessary.


             Entry:  ..ALOC

             Input:  R0 = FDB address

                     F.EFBK(R0) specifies block to allocate to.

             Entry:  ..ALC1

             Input:  R0 = FDB address
                     R1 = High VBN to allocate to
                     R2 = Low  VBN to allocate to

             Output: C = 0, Blocks allocated, F.HIBK(R0) updated
                       = 1, Allocation failed, F.ERR(R0) contains
                            error code



FCS-11 MODULES                                                 PAGE C-15



                     All registers preserved

             The ..EXTD and ..EXT1 routines are used to extend the file.
        ..EXTD computes the extend size, using F.ALOC if it is non-zero.
        Otherwise it subtracts the current  block  allocation  from  the
        contents of R1,R2 and uses the resulting value.  ..EXT1 actually
        issues the extend QIO request.


             Entry:  ..EXTD

             Input:  R0 = FDB address
                     R1 = High VBN to extend to
                     R2 = Low  VBN to extend to

             Output: C = 0, Extend successful
                       = 1, Extend failed

                     All registers preserved


             Entry:  ..EXT1

             Input:  R0 = FDB address
                     R1 = 0, noncontiguous allocation
                        = 1, contiguous allocation
                     R2 = Number of blocks to extend

             Output: C = 0, Successful extend, F.HIBK adjusted
                       = 1, Extend failed

                     R0 preserved, R1-R5 destroyed

             Conditionals: R$$DPB



        C.4.9  CLOSE


             This module closes an  open  file,  writing  any  remaining
        buffers  and  rewriting  the  file  header with the final record
        attributes.  The FDB is reset.


             Entry:  .CLOSE

             Input:  R0 = FDB address

             Output: C = 0, successful completion
                       = 1, error writing header

                     All registers preserved



FCS-11 MODULES                                                 PAGE C-16



             Conditionals: R$$ANI,R$$BBF,R$$MBF,R$$SPL



        C.4.10  COMMON


             This module  contains  two  commonly  used  routines.   The
        first, ..FCSX, is used to properly set the carry bit if an error
        code is set in F.ERR.


             Entry:  ..FCSX

             Input:  R0 = FDB address

             Output: C = 0, F.ERR(R0) is positive
                       = 1, F.ERR(R0) is LE 0

                     All registers preserved

             Conditionals: None

             The second entry, .FATAL, is used by FCS to  declare  fatal
        errors.   A  BPT  instruction is issued.  The current version of
        FCS only uses this routine if an event flag directive fails.



        C.4.11  CONTRL


             This module is used to issue the IO.APC  function.   It  is
        normally intended for use with magtapes.


             Entry:  .CTRL,..CTRL

             Input:  R0 = FDB address
                     R1 = Function code
                     R2 = Value
                     R3 = Parameter list address

             Output: C = 0, operation successful
                       = 1, operation failed, F.ERR(R0) = error code

                     If .CTRL, all registers preserved

                     IF ..CTRL, R0 preserved, R1-R5 destroyed

             Conditionals: None



FCS-11 MODULES                                                 PAGE C-17



        C.4.12  CREATE


             This module contains the internal FCS code for  creating  a
        new  file  on  the  disk.   If  called  for  a record I/O device
        (FD.REC=1), the routine is effectively a no-op.  Otherwise,  the
        IO.CRE function is issued.


             Entry:  ..CREA

             Input:  R0 = FDB address
                     R1 = FNB address

             Output: C = 0, file created
                       = 1, operation failed, F.ERR(R0) = error code

                     R0,R1 preserved, R2-R5 destroyed

             Conditionals: R$$ANI



        C.4.13  DEL


             This module contains the internal  FCS  delete  code.   The
        file  is  removed from the directory and marked for delete.  The
        FNB is assumed to contain the filename and file-ID.


             Entry:  ..DEL1

             Input:  R0 = FDB address
                     R1 = FNB address

             Output: C = 0, delete successful
                       = 1, operation failed, F.ERR(R0) set

                     R0,R1 preserved, R2-R5 destroyed

             Conditionals: None



        C.4.14  DELETE


             This module contains the  user  interface  for  deleting  a
        file.   If  the file is opened it is first closed.  Then the FNB
        is set up using the dataset descriptor in F.DSPT(R0) and default
        filename block in F.DFNB(R0).  Finally, the file is deleted.



FCS-11 MODULES                                                 PAGE C-18



             Entry:  .DELET

             Input:  R0 = FDB address

             Output: C = 0, delete successful
                       = 1, operation failed, F.ERR(R0) set

                     All registers preserved

             Conditionals: None



        C.4.15  DIDFND


             This routine begins to find  the  default  task  directory.
        The  directory number stored in A.DFUI of $$FSR2 is converted to
        RAD50 and stored in  the  filename  portion  of  the  FNB.   The
        routine continues at ..DID.


             Entry:  ..DIDF

             Input:  R0 = FDB address
                     R1 = FNB address
                     R2 = FSR2 address

             Output: Binary UIC converted to RAD50 and stored in FNB.

                     See DIFND (next section) for remainder.

             Conditionals: None



        C.4.16  DIFND


             This module continues the directory  lookup  process.   The
        file  type is set to DIR (RAD50) and the version to one.  A find
        is then performed on the master file directory.  If  successful,
        the  resulting  file-ID  is  set  as  the  directory-ID  and the
        remainder of the FNB is cleared.


             Entry:  ..DID1, ..DID

             Input:  R0 = FDB address
                     R1 = FNB address

                     N.FNAM(R1) = Directory name




FCS-11 MODULES                                                 PAGE C-19



                     0(SP) = Saved R2
                     2(SP) = Saved R3
                     4(SP) = Return address

                     ..DID1 saves R2,R3 on stack and falls into ..DID

             Output: C = 0, directory found, N.DID setup
                       = 1, no directory, F.ERR(R0) set

                     R0-R3 preserved, R4,R5 destroyed

             Conditionals: None



        C.4.17  DIRECT


             This module contains the code used to issue  the  directory
        primitives:  enter filename in directory (IO.ENA), find filename
        in  directory  (IO.FNA),  and  remove  filename  from  directory
        (IO.RNA).


             Entry:  ..ENTR, ..FIND, ..RMOV

             Input:  R0 = FDB address
                     R1 = FNB address

                     Filename block setup for desired operation

             Output: C = 0, operation successful, FNB filled in
                       = 1, operation failed, F.ERR(R0) set

                     R0,R1 preserved, R2-R5 destroyed

             Conditionals: R$$ANI,R$$DPB



        C.4.18  DIRFND


             This module contains the first  half  of  directory  string
        processing.   The directory string is turned into a RAD50 string
        and stored as the desired  filename.   Processing  continues  in
        DIFND  at  ..DID.   The  routine  is mostly concerned with named
        directories, however, this code is disabled for RSX-11M.


             Entry:  ..DIRF

             Input:  R0 = FDB address



FCS-11 MODULES                                                 PAGE C-20



                     R1 = FNB address
                     R2 = Directory string descriptor

             Output: C = 0, operation successful, directory-ID setup
                       = 1, operation failed, F.ERR(R0) set

                     R0-R3 preserved, R4,R5 destroyed

             Conditionals: R$$NAM,R$$SCS



        C.4.19  DIRNAM


             This routine is only used for SCS-11 systems.  It is a part
        of that systems directory processing.



        C.4.20  DLFNB


             This routine is the user interface for deleting a  file  by
        filename  block.   The  FNB  portion of the FDB is assumed to be
        setup with the  filename,  type,  version  (must  be  explicit),
        directory-ID,  device,  and  unit.   The  file  is first closed,
        removed from the directory, and then deleted.


             Entry:  .DLFNB

             Input:  R0 = FDB address

             Output: C = 0, operation successful
                       = 1, operation failed, F.ERR(R0) set

                     All registers preserved

             Conditionals: None



        C.4.21  ELPARS


             This routine contains code which bypasses  the  normal  FCS
        filename  parsing  and  uses  the  facilities  provided  by  the
        operating system.  Such support is only  turned  on  if  FCS  is
        assembled for a VAX/VMS system



FCS-11 MODULES                                                 PAGE C-21



        C.4.22  EOFCHK


             This module contains the EOF checking code for record  I/O.
        The  routine  ..SEFB  checks to see if the current virtual block
        (F.VBN) is at or beyond the EOF block (F.EFBK).


             Entry:  ..SEFB

             Input:  R0 = FDB address

                     F.VBN(R0)  = Current virtual block number
                     F.EFBK(R0) = EOF block number
                     F.FFBY(R0) = Last byte in EOF block

             Output: C = 0, if before or at EOF block
                       = 1, if beyond EOF block

                     FD.EFB in F.BKP1(R0) set if at or beyond EOF block

                     All registers preserved

             The routines ..EFCK and ..EFC1 check to see if the  current
        record  position  is  at  or beyond the EOF position.  The first
        entry calls ..SEFB to properly  setup  FD.EFB.   ..EFC1  assumes
        this  bit  is  already  properly  set.  If at the EOF block, the
        current record position is compared against the placement of the
        EOF within the block.


             Entry:  ..EFCK, ..EFC1

             Input:  R0 = FDB address

             Output: C = 0, if not at EOF
                       = 1, if at EOF, F.ERR(R0) = IE.EOF

                     R0,R2-R5 preserved, R1 destroyed

             Conditionals: None



        C.4.23  EXTEND


             This module contains the user  interface  for  extending  a
        file.  The file may be opened or closed.


             Entry:  .EXTND




FCS-11 MODULES                                                 PAGE C-22



             Input:  R0 = FDB address
                     R1 = Number of blocks to extend file by
                     R2 = Type of extend

                          0 = Non-contiguous
                          1 = Contiguous

             Output: C = 0, operation successful, F.HIBK(R0) adjusted
                       = 1, operation failed, F.ERR(R0) set

                     All registers preserved

             Conditionals: None



        C.4.24  FCSFSR


             This module contains the FSR region  declarations.   $$FSR1
        is declared as a blank psect.  The user is expected to expand it
        later.  The $$FSR2 region is declared to be of size S.FSR2.



        C.4.25  FINIT


             This  module  contains   the   FCS   initialization   code.
        Specifically,  the  size  of the $$FSR1 region is calculated and
        the default UIC is set from the task's UIC.


             Entry:  .FINIT, ..FINI

             Input:  R1 = Address of $$FSR2 region (..FINI only)

             Output: FSR regions initialized

                     All registers preserved if entry at .FINIT

                     R0,R1 preserved, R3-R5 destroyed if entry at ..FINI

             Conditionals: None



        C.4.26  GET


             This module contains  the  code  for  inputting  a  logical
        record  from  the  device/file.  The module can be assembled for
        either sequential-only  support  (R$$SEQ)  or  random/sequential



FCS-11 MODULES                                                 PAGE C-23



        support.   See  the  RSX-11/IAS I/O Operations Reference Manual,
        pages 3-18 to 3-23 for further details on calling  sequence  and
        return values.


             Entry:  .GET, .GETSQ

             Input:  R0 = FDB address

             Output: C = 0, record input
                       = 1, operation failed, F.ERR(R0) set

                     All registers preserved

             Conditionals: R$$ANI,R$$BBF,R$$EIS,R$$RSL,R$$SEQ,R$$11M



        C.4.27  GETDI


             This routine is the second part of  the  directory  look-up
        process.   It  saves  the  current  context of the FNB and calls
        either ..PDID or ..DIRF to set the  directory-ID.   The  FNB  is
        then restored.


             Entry:  ..GTDI

             Input:  R0 = FDB address
                     R1 = FNB address
                     R2 = Directory string descriptor address

                     0(SP) = Directory lookup routine (..PDID/..DIRF)
                     2(SP) = Return address

             Output: C = 0, operation successful
                       = 1, operation failed, F.ERR(R0) set

                     All registers preserved

             Conditionals: R$$SPL



        C.4.28  GETDID


             This routine gets the default task directory-ID and  stores
        it  in  the specified filename block.  It sets-up to call ..PDID
        and continues in ..GTDI.





FCS-11 MODULES                                                 PAGE C-24



             Entry:  .GTDID

             Input:  R0 = FDB address
                     R1 = FNB address

             Output: See ..GTDI

                     All registers preserved

             Conditionals: R$$ELP



        C.4.29  GETDIR


             This routine look ups the specified directory and stores it
        in  directory-ID  in  the  filename  block.   It sets-up to call
        ..DIRF and continues in ..GTDI.


             Entry:  .GTDID

             Input:  R0 = FDB address
                     R1 = FNB address
                     R2 = Directory descriptor address

             Output: See ..GTDI

                     All registers preserved

             Conditionals: R$$ELP



        C.4.30  MKDL


             This module contains the internal routine to  mark  a  file
        for  deletion.   While  the file is deleted by this routine, the
        directory entry is not removed.


             Entry:  ..MKDL

             Input:  R0 = FDB address
                     R1 = FNB address

             Output: C = 0, delete successful
                       = 1, delete failed, F.ERR(R0) set

                     R0 preserved, R1-R5 destroyed




FCS-11 MODULES                                                 PAGE C-25



             Conditionals: None



        C.4.31  MOVREC


             This routine transfers records to and  from  user  buffers.
        It  is  designed  to work correctly for odd address and odd byte
        counts.


             Entry:  ..MVR1

             Input:  R0 = FDB address
                     R1 = Address of source
                     R2 = Address of destination
                     R3 = Size of block to move

             Output: R1 = Address of last byte moved+1
                     R2 = Address of last byte stored+1

                     R0,R4 preserved, R3,R4 destroyed

             Conditionals: None



        C.4.32  MRKDL


             This module contains the user interface for deleting a file
        without removing the directory entry.


             Entry:  .MRKDL

             Input:  R0 = FDB address

             Output: C = 0, delete successful
                       = 1, delete failed, F.ERR(R0) set

                     All registers preserved

             Conditionals: None



        C.4.33  OPEN


             This module contains the code for accessing a file.  It can
        be   assembled  into  three  different  versions:   normal  open



FCS-11 MODULES                                                 PAGE C-26



        (R$$OPF=0), open by  filename  block  (R$$OPF=1),  and  open  by
        file-ID (R$$OPF=2).  See the RSX-11/IAS I/O Operations Reference
        Manual, pages 3-2  to  3-17  for  further  descriptions  of  the
        calling sequence and outputs.


             Entry:  .OPEN, .OPFNB, .OPFID

             Input:  R0 = FDB address

             Output: C = 0, operation successful
                       = 1, operation failed, F.ERR(R0) set

                     All registers preserved

             Conditionals: R$$ANI,R$$BBF,R$$DPB,R$$EIS
                           R$$MBF,R$$NAM,R$$OPF,R$$RSL,R$$11M



        C.4.34  PARDI


             This routine continues the directory  parsing  process  for
        the  default  directory.   If the device and unit agree with the
        current  saved  directory-ID's   device,   the   saved   default
        directory-ID is copied.  Otherwise, the directory-ID is obtained
        and saved for later use.


             Entry:  ..PDI

             Input:  R0 = FDB address
                     R1 = FNB address

                     0(SP) = Directory lookup routine (..DIDF/..DIRF)
                     2(SP) = Return address

             Output: C = 0, operation successful
                       = 1, operation failed, F.ERR(R0) set

                     All registers preserved

             Conditionals: R$$SCS



        C.4.35  PARDID


             This routine is  a  short-hand  version  of  the  directory
        lookup  process,  specifically designed for default directories.
        It sets up to call ..DIDF for directory processing and continues



FCS-11 MODULES                                                 PAGE C-27



        in ..PDI.


             Entry:  ..PDID

             Input:  R0 = FDB address
                     R1 = FNB address

             Output: See ..PDI

                     All registers preserved

             Conditionals: None



        C.4.36  PARSDI


             This module contains the logic for  parsing  the  directory
        specification.


             Entry:  .PRSDI, ..PSDI

             Input:  R0 = FDB address
                     R1 = FNB address
                     R2 = DSD address or zero if none
                     R3 = Default FNB address or zero if none

             Output: C = 0, operation successful
                       = 1, operation failed, F.ERR(R0) set

                     All registers preserved

             Conditionals: None

             Directory processing in FCS appears  somewhat  complex  the
        first  time  it is examined.  The following routines and entries
        are involved:

             DIDFND  ..DIDF
             DIFND   ..DID1 ..DID
             DIRFND  ..DIRF
             GETDI   ..GTDI
             GETDID  .GTDID
             GETDIR  .GTDIR
             PARDI   ..PDI
             PARDID  ..PDID
             PARSDI  .PRSDI ..PSDI

        For the three user-level entries (.GTDID,.GTDIR, and .PRSDI) the
        following flow occurs.  Note, for .PRSDI, there are three flows:



FCS-11 MODULES                                                 PAGE C-28



        dataset(1), default-FNB(2), and neither(3):

             .GTDID  .GTDIR   (1)     (2)     (3)
             ..GTDI  ..GTDI  ..DIRF  none    ..PDI
             ..PDID  ..DIRF  ..DID           ..DIRF
             ..PDI   ..DID                   ..DID
             ..DIDF



        C.4.37  PARSDV


             This module contains the code to parse the device name  and
        assign the FDB's LUN to the parsed device.


             Entry:  .PRSDV, ..PSDV

             Input:  R0 = FDB address
                     R1 = FNB address
                     R2 = DSD address or zero if none
                     R3 = Default FNB address or zero if none

             Output: C = 0, operation successful
                       = 1, operation failed, F.ERR(R0) set

                     If .PRSDV, all registers preserved

                     If ..PSDV, R0-R3 preserved, R4,R5 destroyed

             Conditionals: R$$ELP



        C.4.38  PARSE


             This module contains the routines  to  completely  parse  a
        file  specification.   The  individual  parsing modules (PARSDI,
        PARSDV,  and  PARSFN)  are  called  for  each  component  of   a
        specification.

             The routine ..STFN is an internal entry used to  parse  the
        filename  if  no file-ID has been set.  If parsing is needed, it
        falls into ..PARS.  Otherwise the routine merely exits.


             Entry:  ..STFN

             Input:  R0 = FDB address

             Output: R1 = FNB address



FCS-11 MODULES                                                 PAGE C-29



                     R0 preserved, R2-R5 destroyed

             The  routines  .PARSE   and   ..PARS   parse   a   complete
        specification.


             Entry:  .PARSE, ..PARS

             Input:  R0 = FDB address
                     R1 = FNB address
                     R2 = DSD address or zero if none
                     R3 = Default FNB address or zero if none

             Output: C = 0, operation successful
                       = 1, operation failed, F.ERR(R0) set

                     If .PARSE, all registers preserved

                     If ..PARS, R0-R3 preserved, R4,R5 destroyed

             Conditionals: R$$ELP,R$$SPL



        C.4.39  PARSFN


             This module contains the code to parse the filename.


             Entry:  .PRSFN, ..PSFN

             Input:  R0 = FDB address
                     R1 = FNB address
                     R2 = DSD address or zero if none
                     R3 = Default FNB address or zero if none

             Output: C = 0, operation successful
                       = 1, operation failed, F.ERR(R0) set

                     If .PRSFN, all registers preserved

                     If ..PSFN, R0-R3 preserved, R4,R5 destroyed

             Conditionals: None



        C.4.40  PGCR


             This routine checks to see if the FDB is properly setup for
        record  input  and output.  The file is checked to see if it has



FCS-11 MODULES                                                 PAGE C-30



        been   opened   and   the   proper   I/O   mode    is    checked
        (sequential/random/block).   The  module  is  assembled into two
        versions depending on the definition of R$$SEQ.

             The routine ..PGCR checks for proper random  or  sequential
        I/O.  If random I/O, it checks that the device is not sequential
        in nature.  The routine ..PGCS checks for sequential  I/O  only.
        The calling arguments to both are the same.


             Entry:  ..PGCR, ..PGCS

             Input:  R0 = FDB address

             Output: C = 0, operation OK
                       = 1, operation illegal, F.ERR(R0) set

                     All registers preserved

             Conditionals: R$$SEQ



        C.4.41  PNTMRK


             This module contains the user routines for returning  to  a
        previously  noted position in a file and for getting the current
        position in the file.  A file's  position  is  designated  by  a
        double-word  block  number  and  a  single  word byte within the
        block.

             The .POINT routine positions a file to  a  previous  marked
        position.


             Entry:  .POINT

             Input:  R0 = FDB address
                     R1 = New VBN number (high part)
                     R2 = New VBN number (low part)
                     R3 = Byte number within block

             Output: C = 0, operation successful
                       = 1, operation failed, F.ERR(R0) set

                     All registers preserved

             The .MARK routine retrieves the  current  record  position.
        The  virtual  block  number  is taken from the F.VBN doubleword.
        The byte number is calculated from the current position  in  the
        block I/O buffer (F.NREC+F.VBSZ-F.EOBB).



FCS-11 MODULES                                                 PAGE C-31



             Entry:  .MARK

             Input:  R0 = FDB address

             Output: R1 = VBN number (high part)
                     R2 = VBN number (low part)
                     R3 = Byte number within block

                     R0,R4,R5 preserved

             Conditionals: None



        C.4.42  POINT


             This module contains the internal code for repositioning  a
        file.  If the desired block is different from the current block,
        the old block is written if dirty and the new block  read.   The
        record pointers are then set up for the desired position.


             Entry:  ..PNT1

             Input:  R0 = FDB address
                     R1 = New VBN number (high part)
                     R2 = New VBN number (low part)
                     R3 = Byte number within block

             Output: C = 0, operation successful
                       = 1, operation failed, F.ERR(R0) set

                     R0 preserved, R1-R5 destroyed

             Conditionals: R$$ANI,R$$BBF



        C.4.43  POSIT


             This  module  contains  the  code   for   calculating   the
        positioning information necessary for use with .POINT for a file
        with fixed-length records.


             Entry:  .POSIT, ..PSIT

             Input:  R0 = FDB address

                     F.RCNM doubleword set to desired record number




FCS-11 MODULES                                                 PAGE C-32



             Output: C = 0, operation success
                       = 1, operation failed, F.ERR(R0) set

                     If successful, following registers returned:

                     R1 = VBN number (high part)
                     R2 = VBN number (low part)
                     R3 = Byte number within block

                     If .POSIT, R0,R4,R5 preserved

                     If ..PSIT, R0 preserved, R4,R5 destroyed

             Conditionals: R$$EIS



        C.4.44  POSREC


             This module  contains  the  routines  used  to  position  a
        fixed-length  file  to  a  specific  record.   Besides the entry
        documented below  (.POSRC),  the  entries  ..PSR1,  ..PSRC,  and
        ..PSRG  are  also in this module.  However, they are merely call
        other routines are are therefore are not documented further.


             Entry:  .POSRC

             Input:  R0 = FDB address

                     F.RCNM doubleword set to desired record

             Output: C = 0, operation successful
                       = 1, operation failed, F.ERR(R0) set

                     All registers preserved

             Conditionals: None



        C.4.45  PPNASC


             This routine translates a binary UIC into its ASCII  string
        representation.


             Entry:  .PPASC

             Input:  R2 = String address to store ASCII UIC
                     R3 = Binary UIC (.BYTE owner,group)



FCS-11 MODULES                                                 PAGE C-33



                     R4 = Conversion Flags

                     Bit 0 = 0, suppress leading zeros
                           = 1, output leading zeros
                     Bit 1 = 0, output separators ([,])
                           = 1, suppress separator output

             Output: String output

                     R2 = Last byte output+1

                     R0,R1,R3-R5 preserved

             Conditionals: R$$EIS



        C.4.46  PPNR50


             This routine translates a binary UIC into two RAD50 words.


             Entry:  .PPR50

             Input:  R1 = Doubleword address to store RAD50 results
                     R2 = Binary UIC (.BYTE owner,group)

             Output: UIC converted to RAD50

                     R0,R4,R5 preserved, R1-R3 destroyed

             Conditionals: None



        C.4.47  PUT


             This module contains the  code  for  outputting  a  logical
        record  to  the  device/file.   The  module can be assembled for
        either sequential only  support  (R$$SEQ)  or  random/sequential
        support.   See  the  RSX-11/IAS I/O Operations Reference Manual,
        pages 3-23 to 3-28 for further details on calling  sequence  and
        return values.


             Entry:  .PUT, .PUTSQ

             Input:  R0 = FDB address

             Output: C = 0, record input
                       = 1, operation failed, F.ERR(R0) set



FCS-11 MODULES                                                 PAGE C-34



                     All registers preserved

             Conditionals: R$$ANI,R$$EIS,R$$RSL,R$$SEQ,R$$11M



        C.4.48  RDRN


             This routine inputs the next  virtual  block,  writing  the
        current one if it is dirty (FD.WRT=1).


             Entry:  ..RDRN

             Input:  R0 = FDB address

             Output: C = 0, operation successful
                       = 1, operation failed, F.ERR(R0) set

                     R0 preserved, R1-R5 destroyed

             Conditionals: None



        C.4.49  RDWAIT


             This module contains the  routines  for  reading  the  next
        virtual  block.   ..RWAT increments the block number (F.VBN) and
        falls into ..RWAC.  It also checks for record-oriented transfers
        and handles them correctly.


             Entry:  ..RWAT

             Input:  R0 = FDB address

                     See ..RWAC for remaining description

             The routine ..RWAC reads the  current  virtual  block.   It
        only expects to be called for block I/O.


             Entry:  ..RWAC

             Input:  R0 = FDB address

                     F.VBN(R0)  = Block number
                     F.BDB(R0)  = Address of buffer header
                     F.BBFS(R0) = Number of bytes to read




FCS-11 MODULES                                                 PAGE C-35



             Output: C = 0, operation successful
                       = 1, operation failed, F.ERR(R0) set

                     F.NREC(R0) = Address of start of block
                     F.EOBB(R0) = Address of last byte+1

                     R0 preserved, R1-R5 destroyed

             Conditionals: R$$BBF,R$$MBF



        C.4.50  RDWRIT


             This module contains the  common  routines  for  READ/WRITE
        I/O.   The  routine ..RWCK checks that block I/O is allowed.  It
        checks that the file is opened (F.DBD nonzero), READ/WRITE  mode
        is set (FD.RWM=1), and the device is block oriented (FD.REC=0).


             Entry:  ..RWCK

             Input:  R0 = FDB address

             Output: C = 0, Block I/O allowed
                       = 1, Block I/O not allowed, F.ERR(R0) = IE.ILL

                     All registers preserved

             The routine ..WTRD actually issues the block I/O  requests.
        The block number is bumped after the I/O completes.


             Entry:  ..WTRD

             Input:  R0 = FDB address
                     R4 = I/O function code (IO.WVB/IO.RVB)

                     F.VBN(R0)  = Block number to read/write
                     F.BKDS(R0) = Buffer descriptor
                     F.BKST(R0) = I/O status block address
                     F.BKDN(R0) = I/O done AST address

             Output: C = 0, operation successful
                       = 1, operation failed, F.ERR(R0) set

                     R0 preserved, R1-R5 destroyed

             Conditionals: None



FCS-11 MODULES                                                 PAGE C-36



        C.4.51  READ


             This routine is the user interface for reading a block  via
        block  I/O  mode.   See  the RSX-11/IAS I/O Operations Reference
        Manual, pages 3-28  to  3-31  for  further  details  on  calling
        sequence and return values.


             Entry:  .READ

             Input:  R0 = FDB address

             Output: C = 0, operation successful
                       = 1, operation failed, F.ERR(R0) set

                     All registers preserved

             Conditionals: None



        C.4.52  RENAME


             This routine is the user interface  for  renaming  a  file.
        Only  the  file's  directory  entry is manipulated, the filename
        internal to the file header is untouched.


             Entry:  .RENAM

             Input:  R0 = FDB address (old filename)
                     R1 = FDB address (new filename)

             Output: C = 0, operation successful
                       = 1, operation failed, F.ERR(R0) set

                     All registers preserved

             Conditionals: None



        C.4.53  RETADR


             This routine correctly sets up the FDB record pointers  for
        locate mode I/O.  If called for move mode, it is a no-op.


             Entry:  ..RTAD




FCS-11 MODULES                                                 PAGE C-37



             Input:  R0 = FDB address

             Output: F.NRBD(R0) = Set to record size, address

                     R0,R1,R3-R5 preserved, R2 destroyed

             Conditionals: R$$ANI,R$$BBF



        C.4.54  RSTFDB


             This routine resets a FDB so it can  be  used  for  another
        open.   If  record I/O was used, the block buffer is returned to
        the pool.  Locations in the FDB that are assumed to be  zero  if
        no file is opened are cleared.


             Entry:  ..RFDB

             Input:  R0 = FDB address

             Output: FDB reset to non-opened state

                     R0 preserved, R1-R5 destroyed

             Conditionals: R$$MBF



        C.4.55  RWBLK


             This  module  contains  the  routines  used  to  issue  the
        read/write  requests  for record I/O.  The routines are used for
        both record and block oriented  devices.   The  only  difference
        between  the entries is the I/O codes used.  ..RBLK uses IO.RVB.
        ..WBLK uses IO.WVB.

             The carriage control and  VBN  are  always  stored  in  the
        constructed  QIO.  When issued to record devices, QIO parameters
        4 and 5 are typically ignored.   Similarly,  block  I/O  devices
        ignore  parameter  3.   The I/O status block is assumed to be at
        the beginning of the buffer  header,  which  is  assumed  to  be
        immediately in front of the data buffer.

             No implicit wait for I/O completion is made.  The carry bit
        will be set only if the QIO directive fails.


             Entry:  ..RBLK, ..WBLK




FCS-11 MODULES                                                 PAGE C-38



             Input:  R0 = FDB address
                     R1 = Address of data buffer
                     R2 = Size of data buffer
                     R3 = Carriage control character

                     F.VBN(R0)  = Block number

             Output: R1 = Address of I/O status block

                     R0 preserved, R2-R5 destroyed

             Conditionals: R$$MBF



        C.4.56  RWFSR2


             This module contains a collection of routines to allow  the
        user  to read and write fields in $$FSR2.  The routines (.RDFDR,
        .WDFDR, .RDFFP, .WDFFP, .RFOWN, .WFOWN, .RDFUI, and .WDFUI)  are
        described  in  the  RSX-11/IAS  I/O Operations Reference Manual,
        pages 4-2 to 4-6.



        C.4.57  RWLONG


             This routine is used to perform block  I/O  transfers  when
        the  byte  count  is  greater  than one block (512 bytes).  This
        routine  is  selected  by   the   .READ/.WRITE   routines   when
        appropriate.  Otherwise, ..WTRD is used.


             Entry:  ..RWLG

             Input:  R0 = FDB address
                     R4 = I/O function code (IO.RVB/IO.WVB)

                     FDB setup for block I/O request

             Output: C = 0, operation successful
                       = 1, operation failed, F.ERR(R0) set

                     All registers preserved

             Conditionals: None



FCS-11 MODULES                                                 PAGE C-39



        C.4.58  TRNCLS


             This routine truncates a  file  to  its  EOF  position  and
        closes the file.


             Entry:  .TRNCL

             Input:  R0 = FDB address

                     F.EFBK, F.FFBY set to EOF position

             Output: C = 0, operation successful
                       = 1, operation failed, F.ERR(R0) set

                     All registers preserved

             Conditionals: None



        C.4.59  UDIREC


             This  module  contains  the  user  interface  routines  for
        issueing  the  directory  primitive  functions:   find  filename
        (.FIND), enter filename (.ENTER), and remove filename  (.REMOV).
        The  calling sequences and return values are documented fully in
        the RSX-11/IAS I/O Operations Reference Manual,  pages  4-12  to
        4-14.


             Entry:  .FIND, .ENTER, .REMOV

             Input:  R0 = FDB address
                     R1 = FNB address

             Output: C = 0, operation successful
                       = 1, operation failed, F.ERR(R0) set

                     All registers preserved

             Conditionals: R$$NAM



        C.4.60  UPWARD


             This routine provides extended file  lookup  abilities  for
        SCS-11 systems.  It is not compiled for RSX-11M systems



FCS-11 MODULES                                                 PAGE C-40



        C.4.61  WAITI


             This module contains routines used to issue QIO's  for  FCS
        and  wait  for  their  completion.   The  first routine, ..QIOW,
        issues a QIO and falls into ..WAIT.  It watches for  errors  due
        to  insufficient  pool  and will loop, waiting for a significant
        event if this happens.


             Entry:  ..QIOW

             Input:  R0 = FDB address
                     R4 = I/O function code

                     Scratch DPB setup in $$FSR2

             Output: C = 0, operation successful
                       = 1, operation failed, F.ERR(R0) set

                     R1 = I/O status block address

                     R0 preserved, R2-R5 destroyed

             The routine ..WAIT stores the I/O  status  into  F.ERR(R0).
        It waits for I/O completion by waiting for a non-zero I/O status
        value.  If the I/O status is zero, it falls into ..WAEF and then
        repeats.


             Entry:  ..WAIT

             Input:  R0 = FDB address
                     R1 = I/O status block address

             Output: C = 0, I/O completed successfully
                       = 1, I/O failed, F.ERR(R0) set from status block

                     All registers preserved

             The  routine  ..WAEF  waits  for  the  FDB's  event   flag,
        F.EFN(R0).   If  no event flags was specified, event flag 32(10)
        is used.  The flag is cleared after the wait completes.


             Entry:  ..WAEF

             Input:  R0 = FDB address

             Output: Event flag cleared 

                     All registers preserved




FCS-11 MODULES                                                 PAGE C-41



             Conditionals: None



        C.4.62  WAITU


             This routine is the user  interface  for  waiting  for  I/O
        completion  when  performing  block I/O.  If an I/O status block
        has been specified (F.BKST nonzero), the routine ..WAIT is used.
        Otherwise, the routine ..WAEF is called.


             Entry:  .WAIT

             Input:  R0 = FDB address

             Output: I/O wait completed

                     All registers preserved

             Conditionals: None



        C.4.63  WATNOD


             This routine checks  the  I/O  status  for  errors  due  to
        insufficient  pool  (IE.UPN)  and  doers  a wait-for-significant
        event if true.  Otherwise it merely returns.


             Entry:  ..WAND

             Input:  R0 = FDB address
                     R1 = I/O status block address

             Output: C = 0, IE.UPN occured, wait completed
                       = 1, Error was not IE.UPN

                     All registers preserved

             Conditionals: None



        C.4.64  WATSET


             This routine waits for  I/O  completion  and  sets  up  the
        record  pointers based on the contents the the second I/O status
        word.



FCS-11 MODULES                                                 PAGE C-42



             Entry:  ..WAST

             Input:  R0 = FDB address
                     R1 = I/O status block address

                     I/O status is assumed to be at start of buffer
              descriptor.

             Output: C = 0, I/O completed successfully
                       = 1, I/O failed, F.ERR(R0) set

                     F.NREC(R0) set to beginning of data
                     F.EOBB(R0) set to end of data

                     R0,R1,R3-R5 preserved, R2 destroyed

             Conditionals: R$$BBF



        C.4.65  WRITE


             This routine is the user interface for writing a block  via
        block  I/O  mode.   See  the RSX-11/IAS I/O Operations Reference
        Manual, pages 3-31, 3-32 for further details on calling sequence
        and return values.


             Entry:  .WRITE

             Input:  R0 = FDB address

             Output: C = 0, operation successful
                       = 1, operation failed, F.ERR(R0) set

                     All registers preserved

             Conditionals: None



        C.4.66  WTWAIT


             This module contains the  routines  for  writing  the  next
        virtual  block.   ..WTWA  outputs  the  VBN and returns with the
        record buffers set up for the next PUT.


             Entry:  ..WTWA

             Input:  R0 = FDB address



FCS-11 MODULES                                                 PAGE C-43



                     F.VBN(R0)  = Block number
                     F.BDB(R0)  = Address of buffer header
                     F.BBFS(R0) = Number of bytes to read

             Output: C = 0, operation successful
                       = 1, operation failed, F.ERR(R0) set

                     F.NREC(R0) = Address of start of block
                     F.EOBB(R0) = Address of last byte+1

                     R0 preserved, R1-R5 destroyed

             Conditionals: R$$BBF,R$$MBF



        C.4.67  XQIOI


             This module contains the routines used to build  and  issue
        internal  FCS  QIO's.   They  use  the  QIO  DPB in $$FSR2.  The
        routine ..XQIO sets up the standard parameters  and  issues  the
        QIO  directive.  It assumes the I/O parameters have already been
        set.  This routine gets the I/O status  block  address  and  AST
        address from the FDB.


             Entry:  ..XQIO

             Input:  R0 = FDB address
                     R3 = Directive code, size
                     R4 = I/O function code
                     R5 = DPB address

             Output: See ..XQI1 below

             An alternate entry is ..XQI1.  This routine is  passed  the
        I/O  status  block address and AST address.  It gets the lun and
        event flag from the FDB, sets up the DPB,  and  issues  the  I/O
        request.


             Entry:  ..XQI1

             Input:  R0 = FDB address
                     R1 = I/O status block address or zero
                     R2 = I/O Done AST address or zero
                     R3 = Directive code, size
                     R4 = I/O function code
                     R5 = DPB address

             Output: C = 0, operation successful
                       = 1, QIO directive failed, F.ERR(R0) set from



FCS-11 MODULES                                                 PAGE C-44



              $DSW

                     R1 = I/O status block address

                     R0,R4 preserved, R2,R3,R5 destroyed

             The routine  ..IDPB  initializes  the  DPB  in  $$FSR2  and
        returns the address of the parameter area.


             Entry:  ..IDPB

             Input:  None

             Output: R5 = Address of parameter area

                     R0-R4 preserved

             Conditionals: None



        C.4.68  XQIOU


             This routine is  the  user  interface  for  issuing  a  QIO
        request using the lun and event flag from the FDB.


             Entry:  .XQIO

             Input:  R0 = FDB address
                     R1 = I/O function code
                     R2 = Size of parameter list or zero if none
                     R3 = Address of parameter list

             Output: C = 0, operation successful
                       = 1, operation failed, F.ERR(R0) set

                     All registers preserved

             Conditionals: None














                               APPENDIX D

                             FILES-11 QIO'S




             This section documents the various QIO's used  by  Files-11
        (F11ACP  and  MTAACP)).   The  material is taken from an article
        written by Andrew Goldstein of Digital  in  November,  1976  and
        from examination of various source modules.



        D.1  FILES-11 QIO DPB


             All F11ACP QIO directive parameter  blocks  have  the  same
        format.   The  following  diagram  illustrates this format (note
        only the parameter fields are different from all other QIO's):

        |-----------------------------------------------|
        |          Size         |          DIC          | 
        |-----------------------|-----------------------|
        |       Function Code   |       Modifier        | Q.IOFN Q.IOFN
        |-----------------------|-----------------------|
        |       Reserved        |          LUN          |        Q.IOLU
        |-----------------------|-----------------------|
        |       Priority        |          EFN          | Q.IOPR Q.IOEF
        |-----------------------------------------------|
        |               I/O Status Block                | Q.IOSB
        |-----------------------------------------------|
        |                 AST Address                   | Q.IOAE
        |-----------------------------------------------|
        |                 FID Pointer                   | Q.IOPL
        |-----------------------------------------------|
        |          Attribute List Pointer               |
        |-----------------------------------------------|
        |   Extend Control      |   Delta Size (High)   |
        |-----------------------------------------------|
        |          Delta Size (low 16 bits)             |
        |-----------------------------------------------|
        |   Access Control      |   Window Size         |
        |-----------------------------------------------|
        |                  FNB Pointer                  |
        |-----------------------------------------------|



FILES-11 QIO'S                                                  PAGE D-2



             Each parameter field is used for a  specific  purpose.   If
        the  particular  QIO  does not require the field, it must not be
        specified (set to zero).   F11ACP  range  checks  all  parameter
        fields.



        D.2  FILES-11 QIO PARAMETERS


             This section will discuss the  six  parameter  words  in  a
        Files-11 QIO.  While none of the parameters require the FCS data
        structures, it is obvious the fields are set up for use  in  the
        FCS environment.



        D.2.1  Parameter Word #1 - FID Pointer


             This word contains the address of a three word block in the
        issuing task's space.  This block is or will become the file ID.
        If the word is zero, no file ID is specified.

             In the FCS environment, this word  will  typically  contain
        the  address  of  the filename block.  The file ID block has the
        following format:

        |-----------------------------------------------|
        |                   File Number                 |
        |-----------------------------------------------|
        |               File Sequence Number            |
        |-----------------------------------------------|
        |                    Reserved                   |
        |-----------------------------------------------|

             The file number is used by F11ACP as an index to  the  file
        header  block  in  the  index file.  The file sequence number is
        used to maintain header integrity.  Each time a header block  is
        used  for  a  new file, the file sequence number is incremented.
        The final word has no current meaning.



        D.2.2  Parameter Word #2 - Attribute List Pointer


             This word contains the address of an attribute list in  the
        issuing  task's space.  This list controls which file attributes
        are to be read or written by F11ACP.  If no  attribute  list  is
        specified, the word is zero.

             File attributes are various  fields  in  the  file  header.



FILES-11 QIO'S                                                  PAGE D-3



        These  fields are documented in Appendix F of the IAS/RSX-11 I/O
        Operations Reference Manual (AA-2515C-TC).

             An  attribute  list  consists  of  zero  to  six  attribute
        entries,  followed  by a byte of zero.  Each attribute entry has
        the following format:

                .BYTE   <Attribute type>,<N>
                .WORD   <Pointer to 'N' byte buffer>

             The sign of the attribute type determines the direction  of
        the operation.  If the attribute type is negative, the attribute
        is read from the file header to the buffer.   If  the  attribute
        type  is  positive,  the buffer is written to the file header as
        the new attribute.  The magnitude of the attribute type and size
        of  the buffer determine which fields in the file header will be
        accessed.  The following table lists all  valid  read  attribute
        types,  valid  buffer sizes, and the starting offset in the file
        header.  To write the attribute, make the sign of the  attribute
        type positive.

             -01,02  Read file owner UIC (H.FOWN).  The UIC is a  binary
                     word.   The  low byte (H.PROG) is the owner number.
                     The high byte (H.PROJ) is the group  number.   Note
                     that  the  file  owner  UIC  is  independent of the
                     directory UIC.

             -01,04  Read file owner UIC, protection (H.FOWN).  The  UIC
                     is returned as described above.  The second word is
                     set to the  file  protection  code  (see  attribute
                     -02,02).

             -01,05  Read file owner  UIC,  protection,  characteristics
                     (H.FOWN).   The  UIC and protection are returned as
                     described above.  The fifth  byte  is  set  to  the
                     user-controlled    characterics    (see   attribute
                     -03,01).

             -02,02  Read protection (H.FPRO).  The file protection word
                     is a bit mask with the following format:

                     Bit 15       12 11        8 7         4 3         0
                         |----------|-----------|-----------|----------|
                         |   World  |   Group   |   Owner   |  System  |
                         |----------|-----------|-----------|----------|

                     Each of the four categories above  has  four  bits.
                     Each  bit has the following meaning with respect to
                     file access:



FILES-11 QIO'S                                                  PAGE D-4



                     Bit      3          2            1          0      
                      
                         |----------|-----------|-----------|----------|
                         |  Delete  |  Extend   |   Write   |   Read   |
                         |----------|-----------|-----------|----------|

                     A bit value of zero (0)  indicates  the  respective
                     type of access is allowed to the file.  A bit value
                     of one (1) indicates access is denied.

             -02,03  Read  protection,  characteristics  (H.FPRO).   The
                     protection  is  returned  as  described above.  The
                     third  byte   is   set   to   the   user-controlled
                     characteristics (see attribute -03,01).

             -03,01  Read   characteristics    (H.UCHA).     The    user
                     characteristics  is  a  one  byte  field containing
                     various bit definitions.  The current bits  defined
                     are listed below:

                     UC.CON = 200  Logically continuous file.  When  the
                                   file   is   extended,   this  bit  is
                                   cleared.

                     UC.DLK = 100  File improperly  closed.   When  ever
                                   the  file  is  opened for write, this
                                   bit is set.  It is not cleared  until
                                   the   file  is  closed  (deaccessed).
                                   This is the famous lock bit.

                     In addition to the user-controlled characteristics,
                     the    next    byte    in   the   header   is   the
                     system-controlled   characteristics.    This   byte
                     cannot  be  accessed  by  an  attribute field.  The
                     current bits defined in this byte are listed below:

                     SC.MDL = 200  File marked for delete.

                     SC.BAD = 100  Bad data block in file.

             -04,40  Read record I/O area (U.UFAT).  The first  7  words
                     of this area are a direct copy of the first 7 words
                     of the FDB when the file is opened (see Table  A-1,
                     I/O  Operations Reference Manual, offsets F.RTYP to
                     F.FFBY).  The remaining 9 words of  this  area  are
                     not  used.   I do not know how this area is defined
                     in the case of RMS-11.

             -05,06  Read filename (I.FNAM).  The filename is stored  as
                     nine (9) RAD50 characters.

             -05,10  Read filename,  type  (I.FNAM).   The  filename  is
                     returned  as described above.  The type is returned



FILES-11 QIO'S                                                  PAGE D-5



                     to the fourth word (see attribute -06,02).

             -05,12  Read  filename,  type,   version   (I.FNAM).    The
                     filename  and type are returned as described above.
                     The version is returned  to  the  fifth  word  (see
                     attribute -07,02).

             -06,02  Read type (I.FTYP).  The type is  stored  as  three
                     (3) RAD50 characters.

             -06,04  Read type, version (I.FTYP).  The type is  returned
                     as decsribed above.  The version is returned to the
                     second word (see attribute -07,02).

             -07,02  Read version (I.FVER).  The version is stored as  a
                     binary number.


                                            NOTE

                          The filename, type, and version  are  set
                          when the file is created.  If the file is
                          renamed by  PIP,  these  fields  are  not
                          changed.



             -10,07  Read expiration date (I.EXDT).  The expiration date
                     is  intended  to  be  the  time  the  file  becomes
                     eligible  for  deletion.   This  feature   is   not
                     implemented.  The date is kept in ASCII form in the
                     format day, month, and year (2 bytes, 3 bytes,  and
                     2 bytes).

             -11,12  Read statistics block.   The  statistics  block  is
                     defined  in Appendix H of the I/O reference manual.
                     No specific fields exist in  the  file  header  for
                     this attribute.  Therefore, it cannot be written.

             -12,00  Read  entire  file  header.   The  buffer  size  is
                     assumed to be 1000(8) bytes.  This attribute has no
                     corresponding write function.

             -13,02  Read block size (ANSI  labelled  tape  only).   The
                     block size is returned as a positive 16-bit number

             -14,xx  Read user label (ANSI labelled  tape  only).   This
                     attribute  allows  access  to  the user label on an
                     ANSI standard tape.  "xx"  is  the  length  of  the
                     label  (maximum  80).   If  the function is a read,
                     user header labels are read if a file is  accessed.
                     If  no  file  is  accessed, user trailer labels are
                     read.  If the function  is  a  write,  user  header



FILES-11 QIO'S                                                  PAGE D-6



                     labels  are  written during a create.  User trailer
                     labels are written during a deaccess.

             -15,xx  Read complete date information (disk  files  only).
                     This  attribute  allows  the revison, creation, and
                     expiration dates to be read.  Dates are stored  and
                     returned  in  the  format  day  (2 bytes), month (3
                     bytes), and year since 1900 (2 bytes).   Times  are
                     stored  and returned in the format hours (2 bytes),
                     minutes (2 bytes), and  seconds  (2  bytes).   "xx"
                     bytes  of  time/day information are returned in the
                     following format:

                          00-01   Revision  number.   This   number   is
                                  incremented  each  time  the  file  is
                                  closed after being opened for output.

                          02-10   Revision date.

                          11-16   Revison time.

                          17-25   Creation date.

                          26-33   Creation time.

                          33-42   Expiration date.

             +16,16  Allocation control (disk  files  only).   Used  for
                     file  placement  control,  currently  by  RMS only.
                     Processed only by  create  or  write  (i.e.,  write
                     attribute only).

             The magitude of the attribute type determines  the  maximun
        valid buffer size.  Any smaller size is legal.  The sizes listed
        above are  sufficient  to  handle  the  named  attributes.   The
        largest  size  for  each  attribute  is  also the largest buffer
        allowed.



        D.2.3  Parameter Words #3 and #4 - Size/Extend Control


             These two parameters are used to specify  how  many  blocks
        are  to be allocated to a new file or added to an existing file.
        The words are also used to control the type of block allocation.
        The format of the two parameters is as follows:

                .BYTE   <Delta size (high 8 bits)>,<Extend control>
                .WORD   <Delta size (low 16 bits)>

             The high bit of parameter word #3 (bit 15) controls whether
        the  remaining  fields  are  used by F11ACP.  If the bit is zero



FILES-11 QIO'S                                                  PAGE D-7



        (0), no size change is desired.  If the  bit  is  one  (1),  the
        remaining fields are processed.

             The  high  byte  of  parameter  word  #3  (extend  control)
        determines the type of allocation desired.  The low byte of this
        word and parameter word #4 form a 24-bit  number  of  blocks  to
        allocate  (delta size).  This number is the initial file size in
        the case of a create and the change in size in the  case  of  an
        extend.

             The extend control byte consists of a bit mask.   The  bits
        have the following meanings:

             Bit 0   All blocks must be allocated contigously (EX.AC1).

             Bit 1   Allocate largest contigious chunk up to delta  size
                     (EX.AC2).  This bit is not examined unless bit 0 is
                     on (1).

             Bit 2   File must  end  up  contigious  at  operations  end
                     (EX.FCO).

             Bit 3   Use volume default as delta size (EX.ADF).

             Bit 4   Placement control is desired (EX.ALL).

             Bit 5   Unused.

             Bit 6   Unused.

             Bit7   Enable extend (EX.ENA) (see above).



        D.2.4  Parameter Word #5 - Window Size/Access Control


             This word is used to specify the window size (low byte) and
        the  access  control  (high byte).  The word is processed if the
        high bit (bit 15) is one (1).  If this bit is zero (0), the word
        is disabled.  The format of the word is shown below:

                .BYTE   <Window size>,<Access control>

             The window size is the number of mapping entries the window
        is  to  hold at once.  This is not the window size in bytes.  If
        the byte is zero, the volume default is used.

             The access control byte consists of a bit mask.   The  bits
        have the following meanings:

             Bit 0   Lock file from further accesses  for  write  and/or
                     extend (AC.LCK).



FILES-11 QIO'S                                                  PAGE D-8



             Bit 1   Enable deaccess lock (AC.DLK).

             BIT 2   Enable block locking (AC.LKL).

             Bit 3   Enable explicit block unlocking (AC.EXL).

             Bit 4   Unused

             Bit 5   Unused.

             Bit 6   Unused.

             Bit 7   Enable access (AC.ENB) (see above).



        D.2.5  Parameter Word #6 - Filename Block Pointer


             This word contains the address of a 13(10)  word  block  in
        the  issuing  task's  space.   This block is the filename block.
        See Appendix B in the I/O Reference Manual for a description  of
        a  filename  block.   If  the word is zero, no filename block is
        specified.

             If the QIO  function  is  a  directory  operation  (IO.FNA,
        IO.RNA,  IO.ENA), the directory ID field (N.DID) of the filename
        block is used.  Files-11 directories are merely files with names
        of  the form [0,0]gggooo.DIR;1 where [0,0] refers to master file
        directory and "ggg" is the group number and "ooo" is  the  owner
        number.  The master file directory is the file with ID 4,4,0 and
        is also entered in the master file directory.  The directory for
        UFD [123,456] is the file [0,0]123456.DIR;1



        D.3  FILES-11 QIO FUNCTIONS


             This section will discuss the various  functions  processed
        by  F11ACP.   This  functions are normally issued by FCS or RMS,
        however, the clever user can use  them  directly  and  save  the
        overhead of the run-time systems.

             The following are  the  functions  implemented  by  F11ACP.
        Each  function  is  followed  by a list of required and optional
        parameters.  If a parameter is not listed, it  must  be  set  to
        zero.   Also,  parameter  4  is  not  shown  as  it is a part of
        parameter 3.

             IO.CRE  Create File

                     #1 - FID block pointer, FID value returned with  ID



FILES-11 QIO'S                                                  PAGE D-9



                          of file created.
                     #2 - Write attribute control list (optional).
                     #3 - Size/extend control (optional).
                     #5 - Access control (may be non-zero  but  must  be
                          disabled).

             IO.DEL  Delete or Truncate File

                     #1 - FID  block  pointer  (optional  if   file   is
                          accessed).
                     #3 - Size/extend  control.   If  not   present   or
                          enabled,  file  is  deleted.   Otherwise,  the
                          remaining 31 bits specify the size the file is
                          to be after truncation.

             IO.ACR  Access File for Read Only
             IO.ACW  Access File for Read/Write
             IO.ACE  Access File for Read/Write/Extend

                     #1 - File ID pointer.
                     #2 - Read attributes control list (optional).
                     #5 - Access control.

             IO.DAC  Deaccess File

                     #1 - File ID pointer (optional).
                     #2 - Write attribute control list (optional).
                     #5 - Access control (may be non-zero  but  must  be
                          disabled).

             IO.EXT  Extend File

                     #1 - File  ID  pointer  (optional  if  file  aready
                          accessed).
                     #3 - Size/extend control.

             IO.RAT  Read Attributes

                     #1 - File  ID  pointer  (optional  if  file  aready
                          accessed).
                     #2 - Read attribute control list.

             IO.WAT  Write Attributes

                     #1 - File  ID  pointer  (optional  if  file  aready
                          accessed).
                     #2 - Write attribute control list.

             IO.FNA  Find Filename in Directory
             IO.RNA  Remove Name from Directory
             IO.ENA  Enter Name into Directory

                     #5 - Access control (may be non-zero, but  must  be



FILES-11 QIO'S                                                 PAGE D-10



                          disabled).
                     #6 - Filename block pointer.

             The following table summarizes the  optional  and  required
        parameters  for  each  I/O  request.  The key to the table is as
        follows:

                  * = Required parameter.
                  O = Optional parameter.
                  A = Optional if file already accessed.
                  D = May be non-zero, but must be disabled (bit 15 =
                   0).

        If the entry is blank, the parameter must be  zero  or  the  I/O
        will  be  in  error.  Parmeter 4 is a part of parameter 3 and is
        not listed in the table.

             |----------|-----|-----|-----|-----|-----|
             | Function | P 1 | P 2 | P 3 | P 5 | P 6 |
             |----------|-----|-----|-----|-----|-----|
             | IO.ACE   |  *  |  O  |     |  *  |     |
             |----------|-----|-----|-----|-----|-----|
             | IO.ACR   |  *  |  O  |     |  *  |     |
             |----------|-----|-----|-----|-----|-----|
             | IO.ACW   |  *  |  O  |     |  *  |     |
             |----------|-----|-----|-----|-----|-----|
             | IO.CRE   |  *  |  O  |  O  |  D  |     |
             |----------|-----|-----|-----|-----|-----|
             | IO.DAC   |  O  |  O  |     |  D  |     |
             |----------|-----|-----|-----|-----|-----|
             | IO.DEL   |  A  |     |  O  |     |     |
             |----------|-----|-----|-----|-----|-----|
             | IO.ENA   |     |     |     |  D  |  *  |
             |----------|-----|-----|-----|-----|-----|
             | IO.EXT   |  A  |     |  *  |     |     |
             |----------|-----|-----|-----|-----|-----|
             | IO.FNA   |     |     |     |  D  |  *  |
             |----------|-----|-----|-----|-----|-----|
             | IO.RAT   |  A  |  *  |     |     |     |
             |----------|-----|-----|-----|-----|-----|
             | IO.RNA   |     |     |     |  D  |  *  |
             |----------|-----|-----|-----|-----|-----|
             | IO.WAT   |  A  |  *  |     |     |     |
             |----------|-----|-----|-----|-----|-----|



        D.4  PLACEMENT CONTROL


             One undocumented feature of Files-11 is placement  control.
        This feature allows the create or extend functions to specify an
        exact or approxomate position to allocate  the  desired  blocks.



FILES-11 QIO'S                                                 PAGE D-11



        Placement  control  is  implemented  by an attribute list entry.
        The placement attribute is valid for either the IO.CRE or IO.EXT
        functions  and  if  used,  must  be  the  first attribute in the
        attribute list.  The format of the placement  control  attribute
        block is as follows:

                .BYTE   <Placement control>,0
                .WORD   <High order bits of VBN or LBN>
                .WORD   <Low  order bits of VBN or LVB>
                .BLKW   4      (Optional, see below)

             The placement control byte consists of  a  bit  mask.   The
        bits have the following meanings:

             Bit 0   Set if block specified is  VBN,  otherwise  LBN  is
                     assumed (AL.VBN).

             Bit 1   Set if approximate placement is desired, otherwise,
                     exact placement is assume (AL.APX).

             BIT 2   Set if  starting  and  ending  LBN  information  is
                     desired (AL.LBN).

             Bit 3   Unused.

             Bit 4   Unused

             Bit 5   Unused.

             Bit 6   Unused.

             Bit 7   Unused.

             If AL.LBN is set, the control block  must  be  16(8)  bytes
        long.   F11ACP  will  return  the  starting LBN in the first two
        optional words and the last LBN in the last two optional  words.
        Otherwise,  the  attribute  size  must be 6 bytes.  If AL.VBN is
        specified, AL.APX must  also  be  set  and  the  attribute  will
        allocate  the  new  blocks  as  close  to the specified block as
        possible.  This is useful if file extensions are desired  to  be
        as close to the previous as possible.



        D.5  BLOCK LOCKING


             Another undocumented feature of Files-11  is  block-locking
        support.   This feature was implemented to support RMS, however,
        it can be used for FCS.   Locking  only  occurs  for  access  to
        shared files and AC.LKL set in the access control byte.  For FCS
        users, this can be done by setting the FA.LKL bit in the  F.ACTL
        field  of  the  FDB before opening a file shared.  From then on,



FILES-11 QIO'S                                                 PAGE D-12



        whenever a user reads or writes a block, the system will  insure
        no  other user can have accesses to it.  If the block is locked,
        the second access will have a lock error  (IE.LCK)  returned  to
        it.   This  feature, when properly used, allows multiple readers
        and writers to the same file.

             There are two options for unlocking blocks.   The  simplest
        method  is  to  unlock the block whenever a new block is read or
        written.  This will occur when the AC.EXL  bit  is  set  in  the
        access  control  byte.   FCS  users  can enabled this feature by
        setting the bit in the F.ACTL byte of the FDB.

             If the application requires multiple block locks, an unlock
        QIO  is  used  to  unlock blocks.  To unlock a block, the IO.ULK
        function is issued with the following parameters.

             Parameter #1 - Always zero.

             Parameter #2 - Zero or number of blocks to unlock.

             Parameter #3 - Always zero.

             Parameter #4 - High part of VBN number or zero.

             Parameter #5 - Low part of VBN number or zero.

             Parameter #6 - Always zero.

             If all the specified  blocks  are  currently  unlocked,  an
        error  will  be  returned  (IE.ULK).   If  no  VBN  and count is
        specified, all currently locked blocks are unlocked if  all  I/O
        is  completed.   If  a user is waiting for I/O, this could leave
        some blocks locked because the I/O was not finished.  If  a  VBN
        and  not  count is specified, the first lock-list entry with the
        specified VBN is unlocked.  Therefore, if the  user  issued  two
        requests  for  the  same VBN with different sizes, the first one
        encountered will be unlocked.  The order of locked blocks  bears
        no  relationship  to  the  order  the  orignal reads/writes were
        issued.  Finally, if a VBN and count  are  specified,  an  exact
        match is located.














                               APPENDIX E

                               SAMPLE ACP




             Included with the manual distribution is a sample  ACP  and
        its associated device driver.  The kit also includes sources for
        sample ACP enabling and disabling tasks.



        E.1  SOURCES


             The  software  implements  a  UCP-stype  ACP.   No   system
        modifications  are  required  to  run  the sample ACP.  The file
        ACPGEN.CMD is an indirect command file that  will  assemble  and
        taskbuild  all  sample software.  The other files in the kit are
        as follows:

             COMACP.MAC - Prefix file used  to  define  special  symbols
                  used by the ACP and its device driver.

             NULACP.MAC - Source for sample ACP.  The  ACP  performs  no
                  useful   operations.   However,  it  does  demonstrate
                  packet dequeuing, device  mounts  and  dismounts,  I/O
                  process  creation  and termination, and data transfers
                  from an ACP to a user task.

             NULDRV.MAC - Source for sample driver.  The driver contains
                  a loadable database supports two devices (AC0:, AC1:).
                  The driver demonstrates how ACP packets are  processed
                  and queued to an ACP.

             ENABLE.MAC - Source for basic NULACP mount task.  This task
                  performs the basic steps required for enabling an ACP.
                  It supports switches to  specify  the  ACP  task  name
                  (/ACP=name) and volume control block size (/VCB=size).
                  The /PRM="string" switch can be used to pass an  ASCII
                  string to the ACP.

             DISABL.MAC - Source for basic NULACP dismount  task.   This
                  task  performs  the basic steps required for disabling
                  an ACP.  It supports the /PRM="string" switch.



SAMPLE ACP                                                      PAGE E-2



             NULTST.FOR - Source for test package for  sample  software.
                  This  is  a  Fortran program that queries the user for
                  the I/O function to issue and can be used to test  the
                  other software.

             The kit also includes command files to link all tasks.  The
        ENABLD.CMD  file  allows  the  default  ACP task name and volume
        control block size to be set.  The current defaults are "NULACP"
        and 2 bytes respectively.



        E.2  PROCEDURE


             The procedure for using the sample code is to  execute  the
        ACPGEN command file and generate the tasks.  The listings should
        then be printed and read.  The ACDRV should be loaded using  the
        MCR  LOA  command and NULACP mounted using the ...ENA task.  The
        NULTST task can then be used to issue I/O requests  to  the  ACP
        and  report success/failure.  When finished, the mounted devices
        can be dismounted with the ...DIS task and the driver unloaded.

             The sample ACP  processes  I/O  packets  by  outputting  an
        appropriate  message  to  the  console  terminal  and  returning
        success to the user task.  The software is intended to  be  used
        in  conjuction  with  the  manual, particularly, Chapter 3 which
        outlines the designed processed used in the development  of  the
        sample  ACP.   The  sources can also be used as a starting point
        for a user-written ACP.














                               APPENDIX F

                           USER-WRITTEN ACP'S




             This appendix describes  various  user-written  ACP's  that
        have  been  reported  to  the  author.   The author welcomes new
        additions.  Please  send  a  description  of  your  ACP  to  the
        following address:


                  Ralph W. Stamerjohn
                  Monsanto, Zone T1A
                  800 N. Lindbergh
                  St. Louis, MO, 63166


        The submission should be typed and follow the  format  used  for
        the  current  submissions.   Please limit the description to one
        page if possible.



USER-WRITTEN ACP'S                                              PAGE F-2



        F.1  DAPACP

        Author:   Ralph W. Stamerjohn           Date: 17-APR-80

        Address:  Monsanto, Zone T1A            Phone: (314) 694-4252
                  800 N. Lindbergh
                  St. Louis, MO, 63166


        DAPACP implements Digital's Data Access Protocol (DAP).  The ACP
        is  interfaced to FCS and allows RSX-11M utilities and languages
        to transparently  access  remote  files  on  other  RSX-11M  and
        DECsystem-10  systems.   For example, normal Fortran IV Plus I/O
        statements can be used to read and write remote files.


        ACP-Style:              UCP, using pseudo driver as gateway

        I/O Functions Codes:    Uses 31(10), subfunctions
        Serial/Parallel:        Parallel
        Transportability:       Requires memory management, EIS 
        Pool Utilization:       Minimumal, uses internal ACP pool

        Mounting:               Uses alternate task
        Dismounting:            Uses alternate task

        FCS Support:            Yes
        RMS Support:            No

        Contact Author:         Yes
        Availablity:            No, proprietary Monsanto software

        References:             Reports of the DECsystem-10/20 Fall '79
                                U.S. DECUS Meeting, pages 57-65.