CHANGES TO INDIRECT MCR TO IMPLEMENT
1. A /LI SWITCH
2. SECONDARY SEARCH FOR COMMAND FILES
3. POSITIONAL AND KEYWORD PARAMETERS ON THE COMMAND LINE

FILE DIRECTORY

*.COR SLPR CORRECTION FILES TO APPLY CHANGES TO DEC FILES
	THESE FILES ARE CORRECT FOR IAS V3.0 SUPPORTED INDIRECT MCR
	THEY SHOULD BE CLOSE FOR RSX-11M V3.2
	THEY PROBABLY WON'T BE CLOSE FOR THE UNSUPPORTED VERSIONS

	THE FILES CONTAIN THE SLPR COMMAND LINE WHICH WILL 
	PROBABLY HAVE TO BE EDITED FOR YOUR DISK CONFIGURATION.

INDPRM.MAC SOURCE FOR THE COMMAND LINE PARSER ROUTINE

*.CMD	VARIOUS COMMAND FILES USED DURING GENERATION OF THE
	DISTRIBUTION TAPE AND FOR USE IN GENERATING MCR

	OF PARTICULAR INTEREST

	SLPR.CMD	APPLIES CORRECTION FILES TO DEC SOURCE
			WILL NEED EDITING FOR DEVICE NAMES
	INDASM.CMD	ASSEMBLE ALL FILES INCLUDING INDPRM
	INDBLD.CMD	BUILD INDMCR INCLUDING INDPRM
	INDDBG.CMD	BUILD INDMCR WITH ODT
	RENAME.CMD	MAKE A COPY OF ALL SOURCE FILES TO BE CHANGED

*.NRO	SOURCE DOCUMENTATION FILES
	INDMCR.NRO IS A SHORT MEMO GIVING INTRODUCTORY INFORMATION
	APPA.NRO   IS AN UPDATE TO THE USERS GUIDE
	APPB.NRO   IS A SHORT DICRIPTION OF THE INTERNALS OF THE CHANGES

	THE FILES ARE IN A FORMAT FOR INPUT TO NROFF OR TROFF ON UNIX
	 (UNIX IS A TRADEMARK OF BELL LABORATORIES)
	FOR THOSE OF YOU WHO DO NOT HAVE ACCESS TO UNIX, TOO BAD!

PROCEDURES

1.	MAKE A COPY OF ALL .MAC FILES TO BE CHANGED.  THE COPY SHOULD
	BE TYPE .001.  SLPR FILES WILL APPLY EDITS TO THIS BASE
	LEVEL 001 FILE.  RENAME.CMD SHOULD DO IT.

2.	ASSEMBLE SOURCE MODULES CHANGED.  ALL SOURCE MODULES
	CAN BE ASSEMBLED WITH INDASM.CMD

3.	BUILD NEW INDMCR USING INDBLD.CMD. THIS MAY NOT BE CORRECT
	FOR M USERS.  THE ONLY CHANGE TO THE STANDARD BUILD FILE
	WAS TO INCLUDE INDPRM.OBJ

4.	REMOVE THE OLD INDMCR AND INSTALL THE NEW ONE.

TESTING
	THE FILE FORTRY.CMD CAN PROVIDE A LIMITED QUICK TEST TO
	SEE IF THE CHANGES ARE WORKING. IT CAN BE CALLED WITH THE
	/LI AND /-MC SWITHCES TO GET A LISTING OF THE COMMANDS PRODUCED
	WITHOUT EXECUTING THEM.  IT HAS TWO POSITIONAL PARAMETERS
	AND ONE KEYWORD PARAMETER. THE 1ST PARAMETER IS ONE OR
	MORE SOURCE FILES TO BE COMPILED.  THE 2ND PARAMETER IS
	1ST 6 CHARS OF THE NAME OF A TKB COMMAND FILE.  IF NOT
	SPECIFIED THE 1ST SOURCE FILE NAME IS USED.  THE KEYWORD
	PARAMETER IS COPT AND CAN BE ANY LIST OF SWITCHES TO BE
	APPENDED TO THE SOURCE FILE NAMES WHEN COMPILING.
	FOR EXAMPLE
	@FORTRY/LI/-MC (PROGA,PROGB,PROGC) MYTASK COPT=/DA
	SHOULD RESULT IN
	FOR DC:PROGA,LP:=DC:PROGA/DA
	FOR DC:PROGB,LP:=DC:PROGB/DA
	FOR DC:PROGC,LP:=DC:PROGC/DA
	TKB @DC:MYTASKTKB

	@FORTRY X
	SHOULD RESULT IN
	FOR DC:X,LP:=DC:X
	TKB @DC:XTKB

ONE CHANGE NOT IN THE DOCUMENTS
	THE @ IS NOT NEEDED ON NESTED COMMAND FILE CALLS
	IF THE COMMAND IS NOT INSTALLED INDMCR AUTOMATICALLY TRIES
	TO FIND A COMMAND FILE NAMED COMMAND.CMD.