POOLFL - A PRIVILEGED TASK TO DISPLAY A SNAPSHOT MAP OF THE CURRENT CONTENTS
	OF POOL!!!! (currently for version 3.1 only)

NOTE WELL:  This program is sufficiently valuable to all system managers/
programmers who have pool space problems that it is (to my mind) well worth
the risk of using.  However, it is necessary while this program is scanning
through pool to be on the system stack.  Therefore if it encounters any data
structure which it misinterprets or which has been corrupted, it is highly
likely to cause a system crash with an odd address trap!!!  It does, however,
seem to work well on both our 11/34 and 11/70 systems, and has given us a
good deal of insight into what fragments and/or gobbles up pool.  The only
known bug at this time is that it will crash your system if there are dynamic
regions (created via the PLAS directives) existing at the time the program
is run.

	The program will identify about 90% of the data structures kept in
pool, in its current version.  Remaining known structures not identified are:
AST control blocks (see version 3.2 CDA manual description of same to see
why I haven't yet tracked them down).
RECEIVE packets (certain tasks [notably TKTN, LOADER] have non-standard message
sizes, and without significant checking any attempt to map those packets along
with the standard ones would certainly cause crashes).
ACTIVE I/O packets (that is relatively easy, having already found all
SCB's, but I haven't done it yet).
FCB's for other than INDEXF.SYS (I need to track through all the luns of all
active task headers).
BUFFERS allocated by the terminal driver for as-yet incomplete unsolicited
input.
OTHERS which I don't remember at the moment.
	The program output will appear on the invoking terminal, unless the
task is installed and the LUN reassigned to something like the lineprinter.

Output format:
1st line: # of fragment of pool
2nd line: total words of pool
next n lines: addresses and sizes of all free segments in pool
next line: total # words free in pool
Then the good part:
In this display, each ASCII character represents a minimum allocatable piece
of pool, i.e. 4 bytes.  Each line is 64(10) characters, corresponding to
400(8) bytes of pool.
Free area is shown by --------
Used but not identified is shown by UUUUUUUU
<A> represents an attachment discriptor block
<TCB = ...MCR> is the task control block for task ...MCR, e.g.
<Cn> is a clock queue control block, where n is the type (see system data
structure definitions for types)
<Lx is a logical assignment control block.  The most interesting from the
point of pool fragmentation is <L/> which is a login assignment, which of course
will not move while the terminal is logged in.
<VCB=DBn:> the volume control block for device DBn:  Note that this is the
only data structure which I know has changed enough for version 3.2 that source
code change is necessary (the new VCB contains 12 bytes more to save the volume
name).
<FCB @DBn:> a file control block found for a file on DBn:  Note that at the
moment that is usually only for INDEXF.SYS, unless the ACP is a small one that
keeps all its FCB's in pool. (You can't trace the FCB chain through the ACP
internal storage in a reasonable way).
<WB=========> a window block for a file, again (as for the FCB's) mostly for
INDEXF.SYS
<I DV: > an interrupt control block for device DV:  The program might get
a bit confused as to who owns these, since it is hard without reading the
device driver .STB files to find out which is full-duplex, thus the program
makes an intellligent guess.
<DCB+UCB+SCB = DV:##> The data structures for a loadable driver with a loadable
database.  This may not be quite right if you have a 22-bit system with a DMA
device that does not say it is but still allocates space in the SCB for saving
the UNIBUS mapping register assignments.  There is a real example of such a
device (the VERSATEC DMA interface)!
<HEADER POOLFL###########> is of course a task header for task POOLFL.
Note that this is one of the significant pool fragmenters, particularly if
you get either MCR or an ACP checkpointed, since the header then will wind
up in the middle of pool somewhere when the task comes back in, and since the
task never exits (just stops) the header never goes back out.
<PKT OPT> is a saved I/O size packet for QIO optimization.  These devils will
really fragment your pool, as they get allocated mostly when your system is
busy, then hang around later so it's hard to move/get rid of them, except of
course by turning off the optimization (we've had to do that to avoid pool
problems occurring on a regular basis).
( FCSRES) is a PCB for a permanent partition,
while (/POOLFL) is a subpartition control block, typically for the partition
control block for a running task in a system controlled partition. A sub
partition control block for a driver is (/ ZB:  )
<MCR LINE FOR ...RMD> is an example of a task invoked as an external MCR
function (i.e. RMD<cr> for a task called ...RMD) which hasn't gotten around
to doing a GMCR$.  This structure may stay until the task exits, so you
should remember to to a GMCR$ for any task which will be invoked as an external
MCR function and which will be active for awile, even if it doesn't need to
get any information from the command line.

A sample output might look like:

17.
8940.
055064-055067 2.
055234-055237 2.
055430-055437 4.
.
.
.
070634-071753 296.
072004-071753 4178.
4652.
<A>-<A><TCB = ...LOA><C0><C0>-<VCB=DB0:><FCB @DB0:>(/ TM:  )--(/
 VT:  )<HEADER F11ACP############><TCB = ...SLG>(/...PSZ)<A>---<
A><WB========================================>-(/ PL:  )--------
-<DCB+UCB+SCB = TM:%%>------<L/<TCB = ...PSZ>-------------<HEADE
.
.
.
#############<A><A>UUUUUUUU<C2><C2><HEADER POOL  ###############
##><HEADER ...PSZ###########>-----------------------------------
----------------------------------------------------------------
------------------------------------------------<L/<L/<PKT OPT><
PKT OPT>----------------------------------<PKT OPT>-------------
.
.
.
)( GEN   )( CD    )( F4PRES)( FCSRES)( TERCOM)( MUXCOM)( REJLIB)
( FCSLIB)(DVRPAR)(FCPPAR)( TKNPAR)( MCRPAR)( SYSPAR)



Note that in general the stuff at the top of pool is put there by VMR, which
incidentally from this program I learned does a terrible job by not filling
any holes created by removing tasks, for example.

Comments and suggestion are welcome, but please don't complain if your system
crashes.  Hopefully I or others will get around to doing a few more data
structures,and there will be fewer areas labelled UUUUUUUU.  Keep in mind
that it will never be possible to do all areas, since privileged tasks and
drivers may take blocks out of pool which are not referred to by any standard
data structures.
	Jim Neeland
	Hughes Research Labs
	3011 Malibu Canyon Rd.
	Malibu, California 90265
	(213) 456-6411 ext. 333