The MXTST demonstration

	The MSX operating system has a demonstration program
in the file MXTST containing several tasks that run under
MSX and serve to show a few of the things MSX can do. The system
normally assembles for a 3 CPU configuration, and once running,
will try to balance the processing load between all 3 emulated
CPUs.
	To get started, you will find yourself in DDT, a symbolic
debugger that has many MSX system variables predefined. Each
emulated CPU must at a minimum have its CPU number entered. To
do so, type a command like
MX.CPU[1      2
to change the CPU number from its default value of CPU 1 to CPU 2.
Each CPU number must be unique in the range 1 to 3 (larger ranges
for a system with MXSTLS set up for more CPUs). Once this is done,
you may then type $G (escape,G) to start the task. Once 3 tasks
are running (at 3 terminals) you can begin real actions. (If less
terminals are available, you can set CPU.PR, CPU.PR+2, and/or
CPU.PR+4 to large numbers (positive) to tell MSX not to start
tasks there. Be prepared for waits however as MSX times out its
interprocessor communication when you do this. MSX uses an emulated
bus that is fairly slow (about 1 second per message) to avoid
loading the rest of the system too much.
	Once the system comes up, your console tasks will be active,
one per CPU, and other tasks named A through E are able to be
started. The console tasks prompt with "MSX CONSOLE>" and await
commands. Each console task, and tasks A through E, have classification
blocks you can alter. These are available through DDT, and will limit
what communication or other activity may be done. The console device
also has a classification.
	The format of a classification block is as follows:

	classification privilege word
	default classification (maximum permitted classification level)
	byte with current classification
	up to 10 bytes of special category numbers.

	The privilege word bits have the following meanings:

	100000		Ignore all MLS issues
	10000		Allow I/O to be asynchronous
	4000		Violate special categories if MLS is violated
				on a device
	2000		Violate special categories if MLS is OK on levels
				on a device
	1000		Violate special categories if MLS levels bad on
				a message transfer
	400		Violate special categories if MLS levels OK
				on a message transfer
	200		Allow write to lower levels on device
	100		Allow read from higher level device
	40		Allow write to lower levels with message
	20		Allow read from higher levels with message
	10		Allow write to higher levels in device
	4		Allow read from lower levels in device
	2		Allow write to higher levels in a message
	1		Allow read from lower levels in a message

	If the "asynchronous I/O" bit is clear, all I/O will take
place synchronously and the task will not receive control until it
has completed.

	The commands permitted at console level are the following

AC A	List all active tasks and their status in octal
DD A	Issue a BPT to get to DDT. The $P command resumes the
		program.
SP a	Spawns task a  (a is A,B,C,D, or E)
RQ a	Requests task a (A-E). Differs from Spawn in that hierarchy
		is not kept. Note that spawns where the same
		classification cannot be given are treated as
		requests.
AB a	Aborts task named as a (A-E). If the task was spawned
		successfully, the task that initiated it will
		receive an error notification.
SE a "message"	Sends the text "message" (whatever you like) to
		task a (which may be A through E) and awaits its
		delivery or notice from the system that it cannot
		be delivered.
	Several special cases occur:
		Messages of form "c=message" are received as usual
			and echoed, but are RETRANSMITTED to the
			task whose letter is given as c after the
			first part is changed from 'c=' to 'a>'
			and then sent on. If the transmit fails, the
			task a will print an error message.
		When a message of form "c<message" is received, it
			has the first 2 characters stripped off and
			the message is sent to task c. This allows
			messages to be routed to several tasks.
		A message of form "#c" will abort task c.
		A message of form "@c" will spawn task c.

	Exit ASTs will be displayed when the console tasks see them
		and possibly for subtasks too.

		Further note: The console tasks KBA, KBB, and KBC
			are given as letters F, G, and H and may be
			sent messages to also. These messages will be
			received via AST traps in the console tasks
			and displayed after a message indication
			that an AST was received.

	To set classification blocks, the following are global names for
them which are known to DDT:

	Task		Classification Block

	KBA (Console, CPU 1)	CLSKBA
	KBB (Console, CPU 2)	CLSKBB
	KBC (Console, CPU 3)	CLSKBC
	AAA (Task A)		CLSAAA
	BBB (Task B)		CLSBBB
	CCT (Task C)		CLSCCT
	DDD (Task D)		CLSDDD
	EEE (Task E)		CLSEEE

	These may be accessed symbolically via DDT and the system resumed.
Note that some MSX actions are illegal if classifications are wrong
(such as aborts) and may cause the system to hang as MXTST was not written
for complete variability of the classifications. The original assumption
was that the console would have the Ignore MLS bit set at least.
	There may be some bugs in MSX. Please let me know about any
you see.
			Glenn Everhart