DSCCPY.DOC
 
	DSCCPY - FORTRAN program to copy just a few files from a DSC
		tape without restoring the entire volume.
 
		William D. Burton, Jr.
		Texas Research Institute of Mental Sciences
		1300 Moursund
		Houston, Texas  77030
		(713) 797-1976  ext 501
 
	I needed a program to copy some files from a DSC (Disk-Save-and-
Compress) tape from a large disk onto an RK-05.  DSCCPY is the result.
It was written in FORTRAN (Fortran-IV-Plus v 2.51) and MACRO and has
run under RSX-11M V3.0 (sic).
 
USING THE PROGRAM:
 
	This program is controlled by user responses to prompts.  It will
not accept indirect command files).  The input tape(s) are UNMOUNTED.
The reels of a multi-reel set do not have to be read in sequence PROVIDED
that the data file being copied does not cross reels.
 
1. The Input tape must be UNMOUNTED
 
2. The Output Disk must be MOUNTED.
 
3. Run DSCCPY and answer the questions:
 
	a. prompt = INPUT DEVICE
	   answer = input tape device name (e.g. MT1:)
	   program action = Assign Fortran LUN 3 to the specified device.
		    Attach device and rewind.
	   answer = control-Z
	   program action = exit.
 
	b. prompt = DSC TAPE FILE NAME
	   answer = 12-character file name specified when tape was created.
		    a wildcard (*) matches any name.  A wild character (?)
		    matches any single character.
 
	   answer = <return>  a null input (carriage return only) inhibits
		    the search for a named DSC output file.  This is the
		    response which must be used if the first reel of a
		    multiple reel tape is NOT being read.
	   program action = Search for the ANSI HDR1 record with the
		    specified label.  If not found on the current reel, 
		    return to step 3a.
 
	c. prompt = OUTPUT DEVICE AND UIC DDU:[UIC]
	   answer = Disk output device where the restored file is to be
		    put.  No wildcards.  The defaults are the normal 
		    Fortran defaults for LUN 4.
	   program action = Check for the desired volume being mounted.


DSCCPY.DOC (continued)
 
	d. prompt = FILE TO BE COPIED
	   answer = [OWNING UIC]filename.ext;version of the file to be
		    located and copied.  Any field can be wildcard (*)
		    or contain wild-characters (?)
 
	   answer = /FI:filn,filsn
		    this allows the user to copy a single file using its
		    original file-number (filn),file-sequence-number.
		    NO wildcards or wild-characters.
 
	   program action = Search for the file specified and copy to 
		    the output.  If the file is not on the current reel
		    of a multi-reel tape, a prompt for the new reel will
		    be issued.
		    If the file is not in this volume (i.e. an ANSI EOF
		    record is found) an error message is output.
		    If the file already exists (same Directory, name,
		    extension, version) an error message is produced and
		    the file is not copied.
 
NOTES AND LIMITATIONS:
 
1. This program has been used on both 7-track and 9-track TM-11 look-alike
	drives.  Routine NXTAPE will need changing to set up a tape for
	1600 bpi.
 
2. If DATA OVERRUN errors (-13. IE.DAO) occur, the size of the tape input
	buffer can be increased using PARAMETER NRLTH= newsize in the
	main program.  The buffer should never be less than 1040. bytes.
 
3. Error checking on the prompt input filenames is very primitive.  
	Only a simple check on the syntax of the file specifier is done.
	Illegal characters in the fields are not detected.  This will
	lead to "NOT FOUND" type errors.
 
4. There is no verify of the copied data.
 
5. The /FI:filn,seqn   command does not accept wildcards or wild characters
 
6. Because directory files are not guaranteed to be on the same reel as
	the file being copied, and I didn't want to have to read the
	whole DSC volume, I chose to use the file identifier as found
	in the files-11 file header.  If a file has been re-named before
	being DSC-ed this file identifier will not match the directory
	entry.  The /FI:  option can be used to find the file, given
	a DSCDIR listing of the directories.


DSCDIR.DOC (continued)
 
 
7. As much information as practical of the original file-header is preserved
	with the copied file.  Because I did not want to do the copy with
	the index-file UNLocked not all information is preserved.
	The following items from the file header are preserved during the
	copy:
		file name, extension, version
		space allocated and contiguous/non-contiguous indication
		end-of-file pointer
		record attributes
 
	The following information is NOT preserved:
		DIRECTORY uic
		OWNING uic
		creation date and time
		last update date and time
		mapping
 
 
INSTALLING DSCCPY
 
	DSCCPY was originally compiled under F4P (version 2.51).  It uses
some MACRO-11 routines for string and FDB manipulation.  The distribution
includes the following files:
 
	DSCCPY.FTN -- Fortran main program
	DSCFTN.FTN -- Fortran subroutines
	DSCMAC.MAC -- Macro-11 subroutines
	DSCCPY.CMD -- Task build command file
	DSCCPY.DOC -- This document.
 
Compile or Assemble as appropriate, the 3 source files.
 
Edit the task build command file to reflect your configuration if needed.
The device assignments for luns 3 and 4 are changed in response to user
prompts at run-time.