From the Wizzards Book of RSX MAGIC
                                  D. B. Curtis
                           SCIENCE APPLICATIONS, INC.
                                 Oak Brook, IL



        This article describes how to send non-standard ASTs  to  tasks.
        More  articles  in  this vein will occur as I have time to write
        them up.  Help from other wizards would be  appreciated.   These
        articles  are  dangerous to use:  Incorrect usage will result in
        system  crashes  and  other   inconsistent   system   operation.
        However,  there  are times when the only way that RSX is able to
        satisfy your needs is to use these tricks.  Only use  them  when
        you  need  to.   This article describes how to send non-standard
        ASTs to tasks.  This can be used in a variety of ways.   One  is
        for  full  duplex  drivers  that  need  to  wake  up a task when
        unsolicited input occurs.  Another is as a variable  send  data.
        The  routine  and  test  program  are listed later.  The routine
        SNDAST may be called only from system state.  You are in  system
        state after a SWSTK$ or FORK.  The routine will send an AST of a
        specified size to a specified task.   If  the  task  is  out  of
        memory, it will be brought into memory and scheduled to run.


	.TITLE	NSTAST
	.IDENT	/V1/
;
;
; WRITTEN BY D.B.CURTIS
; SCIENCE APPLICATIONS, INC.
; 28-SEP-81
; ARGONNE NATIONAL LAB
;
;
; VERSION 01
; EDIT NUMBER = 0001
; FILE = NSTAST.MAC
; EDITED BY: D.B.CURTIS  28-SEP-81 14:51:11
;
;
; MODIFICATIONS:
;
;+
; FILE DESCRIPTION
;
;	THIS ROUTINE SENDS AN AST TO A SPECIFIED TASK.
;	THE ROUTINE MUST BE CALLED FROM SYSTEM STATE.
;-
;
;
	.PAGE
;+
;  **-SNDAST-SEND AST TO TASK
;
; THIS ROUTINE SENDS AN AST TO A SPECIFIED TASK
; NOTE! IT DOES NOT CHECK THAT THE PARAMETERS ARE CORRECT.
; INCORRECT CALLS TO THIS ROUTINE WILL CRASH YOUR SYSTEM!
;
; YOU MUST BE IN SYSTEM STATE BEFORE CALLING THIS ROUTINE. 
;
; THE AST BLOCK MUST BE LESS THEN 200 AS THE SIZE BYTE IS USED BY THE
; SYSTEM TO INDICATE TYPE OF AST. 
;
; THE AST THAT IS SENT HAS THE NUMBER OF BYTES THAT MUST BE REMOVED
; FROM THE USER STACK AS THE FIRST PARAMETER  ON THE STACK.
; THE MAXIMUN NUMBER OF PARAMETERS THAT YOU CAN SEND IS 125(10)
;
; INPUTS:
;	R5 = TCB ADDRESS OF TASK TO SEND AST TO
;	R0 = NUMBER OF USER PARAMITERS TO PUT IN AST
;	R1 = POINTER TO USER PARAMITERS
;	R2 = AST ADDRESS IN RECIEVER TASK
;
; OUTPUTS:
;	CARRY CLEAR IF NO PROBLEMS, SET IF ERROR
;
;	
;
; STANDARD REGISTER USAGE
;
;-
;
; ROUTINES CALLED
;
	.GLOBL	$QASTT		; QUEUE AST TO TASK
	.GLOBL	$ALOCB		; ALLOCATE CORE BLOCK 

	.PAGE

SNDAST::
	JSR	R5,$SAVRG		;; SAVE REGISTERS R3-R5
	INC	R0			;; ADD OUR PARAMETER
	MOV	R0,R4			;; SAVE SIZE
	MOV	R1,R3			;; AND POINTER TO USER DATA
	MOV	R2,-(SP)		;; SAVE R2 AS ALOCB MODIFIES IT
	ASL	R0			;; MAKE NUMBER OF BYTES FOR USER PARAMS
	ADD	#5*2,R0			;; ADD ON THE SYSTEM PARAMS
	MOV	R0,R1			;; COPY SIZE TO R1
	CMP	#177,R1			;; CHECK SIZE IS LEGAL
	BHIS	4$			;; 200 AND MORE IS ILLEGAL SEE
					;; CRASH DUMP ANALYZER MANUAL PAGE B-39
	SEC				;; CARRY IS ALREADY SET BUT FOR CLARITY...
	BR	5$

4$:	CALL	$ALOCB			;; ALLOCATE A CORE BLOCK, SEE 
					;;   EXEC MODULE CORAL
					;;  R0 = ADDRESS, R1= SIZE, R2 = WIPED
5$:	MOV	(SP)+,R2		;; RESTORE R2
	BCC	10$
	RETURN				;; ERROR RETURN

10$:	MOV	R0,-(SP)		;; SAVE ADDRESS OF AST BLOCK
	CLR	(R0)+			;; CLEAR THE LINK
	MOV	R1,(R0)+		;; SAVE THE SIZE
	MOV	R4,R1			;; GET NUMBER OF USER PARAMS
	ADD	#7,R1			;; ADD NUMBER OF SYSTEM PARAMS
					;;   LOOK AT EXEC MODULE DRATX FOR MAGIC 7
	ASL	R1			;; TIMES 2 TO MAKE BYTES ON USER STACK
	MOV	R1,(R0)+		;; SAVE NUMBER OF BYTES ON USER STACK
	MOV	R2,(R0)+		;; SET AST ADDRESS
	MOV	R4,(R0)+		;; SAVE NUMBER OF USER PARAMITERS
	MOV	R4,R1			;; GET NUMBER OF USER PARAMITERS
	ASL	R4			;; MAKE SIZE AS BYTES
	MOV	R4,(R0)+		;; AND MAKE FIRST ARGUMENT ON STACK
	DEC	R1			;; HAVE ALREADY SAVED SIZE
11$:	MOV	(R3)+,(R0)+		;; SAVE USER PARAMITERS
	SOB	R1,11$
	MOV	(SP)+,R1		;; GET AST BLOCK ADDRESS
	MOV	R5,R0			;; GET RECIEVER TASK TCB
	CALLR	$QASTT			;; SEND AST AND RETURN, SEE REQSB

	.END


	.TITLE	TSTAST
	.IDENT	/V1/
;
;
; WRITTEN BY D.B.CURTIS
; SCIENCE APPLICATIONS, INC.
; 29-SEP-81
; ARGONNE NATIONAL LAB
;
;
; VERSION 01
; EDIT NUMBER = 0001
; FILE = TSTASTA.MAC
; EDITED BY: D.B.CURTIS  29-SEP-81 16:28:05
;
;
; MODIFICATIONS:
;
;+
; FILE DESCRIPTION
;
;	THIS FILE IS USED TO TEST THE SNDAST ROUTINE.
;	IT IS A PRIVALIGED PROGRAM (TO ALLOW A SWSTK$) WHICH CALLS
;	THE SNDAST ROUTINE WITH A LINE OF TEXT AS THE PARAMETERS.
;	THE AST ROUTINE ATTEMPTS TO PRINT THE LINE WHEN THIS TASK FROM THE
;	STACK. THIS TEST PROGRAM SENDS AN AST TO ITSSELF AND PRINTS THE
;	AST DATA FROM OFF OF ITS STACK.
;	
;	REMEMBER, THE SNDAST ROUTINE CAN SEND AN AST TO ANY TASK.
;-
;
;
	.MCALL	QIOW$S,EXIT$S,ASTX$S

	.PAGE
;
; IMPORTAINT GLOBALS
;
	.GLOBL	SNDAST		; ROUTINE TO SEND ASTS
 
;
; LOCAL DATA
;


SAVSP:	.BLKW	1		; VALUE OF STACK AT STARTUP

PRAMS:	.ASCII	/THIS IS A TEST OF THE AST CODE/ ; TEST MESSAGE
BLKSZ=.-PRAMS
	.PAGE

START:
	MOV	SP,SAVSP		; SAVE STARTUP TIME SP
1$:	SWSTK$	15$			;; GO TO SYSTEM STATE

	MOV	$TKTCB,R5		;; GET OUR TCB ADDRESS
	MOV	#<BLKSZ+1>/2,R0		;; GENERATE NUMBER OF PARAMETERS
	MOV	#PRAMS,R1		;; GET POINTER TO USER PARAMETERS
	MOV	#ASTAD,R2		;; AND AST ADDRESS
	CALL	SNDAST			;; SEND AST AND RETURN
	RETURN

15$:	CMP	SP,SAVSP		; CHECK THAT SP OK
	BEQ	1$			; AND IF SO, CONTINUE FOREVER
	IOT				; ELSE CRASH

ASTAD:					;-- AST ENTRY POINT
	.IRPC	REG,<012345>		; SAVE REGISTERS
	MOV	R'REG,-(SP)
	.ENDM

	MOV	SP,R0			; GENERATE POINTER 
	ADD	#14,R0			; TO LINE
	MOV	(R0)+,R1		; GET SIZE
	QIOW$S	#IO.WVB,#5,#1,,,,<R0,R1,#40> ; WRITE LINE

	.IRPC	REG,<543210>		; RESTORE REGISTERS
	MOV	(SP)+,R'REG
	.ENDM

	ADD	(SP),SP			; CLEAN STACK
	ASTX$S				; EXIT AST


	.END	START