A BIT MORE USEFUL " P O O L   M O N I T O R "
                 =============================================

             The POOL program, as published in The Multitasker  (even  a
        great tool) requires more than skilled operator to come out from
        the Pool-lock.  It is usually  very  dificult  to  discover  the
        task, which consumed Pool and forced the system to freeze.  Help
        is simple to add a few code and POOL will (at the  system  fatal
        state) display also active tasks and their memmory state:
         
        12-FEB-81 18:41:30 POOL -- FATAL STATE -- FREE POOL EXHAUSTED
        ACTIVE:
        TT0:  IN   MCR...
        CO0:  IN   F11ACP
        TT2:  OUT  LPP0
        CO0:  OUT  QMG...
        TT4:  IN   TT4		- probbably the "POOL CONSUMER"
        CO0:  IN   POOL 
        POOL -- PLEASE, ENTER TASK TO ABORT: 

             This makes system recovery (especially for larger  systems)
        much  more  probbably.   I note, POOL works very good with STSE$
        and 30 sec pause between the Pool-checks.  Since there  are  too
        many hand-typed versions of POOL, I don't include SLP correction
        file, but example of the part of code:
         
        FATMSG:	.BYTE	7,15,12,12
        	.BLKB	9.
        	.BYTE	40
        	.BLKB	8.
        	.BYTE	40
        	.ASCII	/POOL -- FATAL STATE -- FREE POOL EXHAUSTED/<7>
        	.ASCIZ	<15><12><15><12>/ACTIVE:/<15><12>
        TSKMSG:	
        TSKTTI:	.ASCII	/TT7   /
        TSKMEM:	.ASCII	/OUT  /
        TSKNAM:	.ASCIZ	/TTTTTT/
        ABOMSG:	.ASCIZ	<15><12>/POOL -- PLEASE, ENTER TASK TO ABORT:/
        INVNAM:	.ASCIZ	<177><177>/POOL -- INVALID TASKNAME, TRY AGAIN:/
        NOTABO:	.ASCIZ	<177><177>/POOL -- TASK NOT ABORTED, TRY AGAIN:/
        	............
        ; NOT ENOUGH FREE POOL TO QUEUE A LINE TO MCR.
        ; TAKE OVER THE SYSTEM, ASK TO ABORT TASKS UNTIL POOL RETURNS.
        ;
        120$:	MOV 	#FATMSG+4,R3
        	CALL	DATSUB
        	CALL	$SWSTK,160$
        	MOV	@#TTISTA,-(SP)
        	MOV	@#TTOSTA,-(SP)
        	CLR	@#TTISTA
        	CLR	@#TTOSTA
        	MOV	#FATMSG,R0
        	CALL	TTYOUT
        ;
        ; FIND ACTIVE TASKS AND TELL THEIR NAME, TI AND MEMORY STATE


                                                                  PAGE 2



        ;
        	MOV	#$TSKHD-T.TCBL,R4	;FIRST POINTER
        122$:	MOV	T.TCBL(R4),R3		;GET NEXT TCB ADDRESS
        	MOV	R3,R4			;SAVE IT FOR NEXT LOOP
        	CMP	#$HEADR,R3		;IS IT NULL TASK
        	BEQ	126$			;EQ=YES, ALL DONE
        	BIT	#TS.EXE,T.STAT(R3)	;IS TASK ACTIVE?
        	BNE	122$			;NE=NOT, TRY NEXT ONE
        	CMP	R3,$LDRPT		;IS IT LOADR?
        	BEQ	122$			;EQ=YES, SKIP IT
        	MOV	#TSKNAM,R0		;GET TASK STRING ADDR
        	MOV	T.NAM(R3),R1		;R50 TASKNAME 1-3
        	CALL	$C5TA			;CONVERT IT TO ASCII
        	MOV	T.NAM+2(R3),R1		;R50 TASKNAME 4-6
        	CALL	$C5TA			;CONVERT IT TO ASCII
        	MOV	#TSKMEM,R0		;GET MEMMORY ATR. ADDR 
        	MOVB	#'O,(R0)		;AND
        	MOVB	#'U,1(R0)		;PREPARE TASK OUT
        	MOVB	#'T,2(R0)		;MESSAGE
        	BIT	#TS.OUT,T.STAT(R3)	;IS TASK IN MEMORY?
        	BNE	124$			;NE=NOT=OUT
        	MOVB	#'I,(R0)+		;REPLACE
        	MOVB	#'N,(R0)+		;OUT MESSAGE BY
        	MOVB	#' ,(R0)		;IN  MESSAGE
        	MOV	#TSKTTI,R0		;TT-NUM STRING ADDR
        	MOV	T.UCB(R3),R3		;TASK'S TI: UCB ADDR
        	CALL	$FMTDV			;FORM DEVICE IDENT
        124$:	MOV	#TSKMSG,R0		;PREPARE AND OUTPUT
        	CALL	TTYOUT			;ACTIVE TASK MESSAGE
        	BR	122$			;REPEAT
        126$:	MOV	#ABOMSG,R0		;PREPARE AND OUTPUT
        	CALL	TTYOUT			;ABORT MESSAGE SEQUENCE
        	.......
         
         
        					Ing.Martin Brunecky
        					Drobneho 28a
        				60000 	BRNO
        					Czechoslovakia