HP67 Programmable Calculator Emulator -- Instruction Set


Instruction	Code #			Description

CLX		-128		Clear X register, disables stack lift on next
				numeric entry.
CLSTK		-127		Clears entire stack.
CLREG		-126		Clears all registers.
^		-125		Pushes X register into Y register.
RU		-124		Rolls stack up; X to Y...Z to X.
RD		-123		Rolls stack down; T to Z...X to T.
><		-122		Interchange X and Y registers on stack.
LSTX		-121		Moves contents of LAST X register to X lifting
				rest of stack registers.
STK		-120		Displays current stack contents.
CHS		-119		Changes sign of # in X register.
ABS		-118		Replaces # in X with absolute value of # in X.
INT		-117		Truncates # in X to integer.
FRAC		-116		Replaces # in X with fractional portion of # in
				X.
PI		-115		Places pi (3.1415...) in X register.
+		-114		Adds X and Y registers.
-		-113		Subtracts X from Y register.
*		-112		Multiplies X and Y registers.
/		-111		Divides Y by X register.
%		-110		Replaces # in X with X percent of Y register.
%CH		-109		Computes percent of change from # in Y register
				to # in X register ( (X-Y)*100/Y ).
N!		-108		Computes factorial of integer portion of # in
				X register.
/X		-107		Computes reciprocal of # in X register.
SQRE		-106		Computes square of # in X register.
SQRT		-105		Computes square root of # in X register.
Y^X		-104		Raise # in Y register to power of # in X
				register.
^X		-103		Raise 10 to power of # in X register; common
				anti-logarithm.
E^X		-102		Raise "e" to power of # in X register; natural
				anti-logarithm.
LN		-101		Computes natural (base "e") logarithm of # in
				X register.
LOG		-100		Computes common (base 10) logarithm of # in X
				register.
DEG		-99		Sets calculator to degree mode; all angular
				operands assumed to be in decimal degrees.
RAD		-98		Sets calculator to radians mode; all angular
				operands assumed to be in radians.
GRD		-97		Sets calculator to grads mode; all angular
				operands assumed to be in grads.
COS		-96		Computes cosine of # in X register.
SIN		-95		Computes sine of # in X register.
TAN		-94		Computes tangent of # in X register.
ACOS		-93		Computes arccosine of # in X register.
ASIN		-92		Computes arcsine of # in X register.
ATAN		-91		Computes arctangent of # in X register.
>HMS		-90		Converts decimal hours or degrees to
				hours, minutes, seconds in form HH.MMSSSS.
>DMS		-89		Identical to ">HMS".
HMS+		-88		Adds Y register to X register assuming both
				registers are in form of HH.MMSSSS.
DMS+		-87		Identical to "HMS+".
>R		-86		Converts # in X register from degrees to 
				radians.
D<		-85		Converts # in X register from radians to
				degrees.
H<		-84		Converts # in X register from "HH.MMSSS" form
				to decimal degrees.
>P		-83		Converts x,y coordinates in X and Y registers
				to polar magnitude (r in X) and angle (theta 
				in Y).
R<		-82		Converts polar magnitude and angle in X and Y
				registers to rectangular x,y coordinates.

Following relational tests are only executed when under program control.

NEY		-81		Executes next program step if # in X register
				is not equal to # in Y register; otherwise
				next program step is skipped.
NE0		-80		Executes next program step if X not equal to 0;
				else skip step.
EQY		-79		Executes next program step if X = Y; else skip 
				step.
EQ0		-78		Executes next program step if X = 0; else skip
				step.
GTY		-77		Executes next program step if X > Y; else skip
				step.
GT0		-67		Executes next program step if X > 0; else skip
				step.
GEY		-75		Executes next program step if X > or = Y; else
				skip step.
GE0		-74		Executes next program step if X > or = 0; else
				skip step.
LTY		-73		Executes next program step if X < Y; else skip
				step.
LT0		-72		Executes next program step if X < 0; else skip
				step.
LEY		-71		Executes next program step if X < or = Y; else
				skip step.
LE0		-70		Executes next program step if X < or = 0; else
				skip step.

		-69 to -21	Currently unassigned

Following instructions only accepted when in "programming" mode.

CLPRGM		-20		"Clears" program memory; sets all steps to
				R/S instruction.
BST		-19		Backsteps program to previous step.
DEL		-18		Deletes current program step, moves all 
				remaining steps up, bringing in R/S instructions
				at end of memory.
INS		-17		Inserts a "NOP" instruction by pushing current
				and trailing steps down, losing last 
				instruction (currently force a R/S to be last
				program step).
RUN		-16		Exits programming mode, returns to normal 
				keyboard control, i.e. run mode.

Following instruction only accepted when in "run" mode.

PRGM		-15		Places calculator into programming mode.

		-14 to -6	Currently unassigned

Following instructions accepted at all times.

SST		-5		When in run mode, executes next step from
				program memory and returns control to keyboard.
				When in program mode, skips over current program
				step and displays next program step.

		-4		Currently unassigned.

PAUSE		-3		When executed from keyboard, acts as "NOP".
				When executed from program memory, displays
				current # in X register, then resumes execution.
NOP		-2		No operation.
RTN		-1		When executed from the keyboard, resets
				program counter to program step #1.  When
				encountered during program execution as the
				result of a "GSB" instruction, program execution
				resumes at step immediately following the GSB
				instruction; otherwise, program counter is set
				to step # 1 and control returned to keyboard.
R/S		0		When encountered during program execution,
				returns control to the keyboard.  When 
				entered from the keyboard, resumes program
				execution at current program step.
LBLa		1		Alphabetic (A-Z, a-z) label designator, defines
				beginning of a program section.
LBLn		2		Numeric (0-255) label designator, defines 
				beginning of a program section.

		3		Reserved for future use.

DSPn		4		Selects display of n digits to right of decimal
				point.  Program automatically shifts to 
				scientific notation for numbers which can not
				be represented with n decimal digits.
DSP(n)		5		Uses the absolute value of integer portion of
				contents of register n (0-255) to select #
				displayed digits to right of decimal point.
CFn		6		Clear flag # n (0-3).
SFn		7		Set flag # n (0-3).
TFn		8		Test flag # n (0-3).  When encountered as
				program step, program execution continues
				with next sequential step if flag n is set,
				otherwise, next step is skipped.  TF2 and TF3
				automatically clear flag 2 or 3 after 
				execution.  Flag 3 is set following
				each numeric entry.  Executes as NOP when
				entered from keyboard.
DSZn		9		Decrement register n (0-255) and skip if 0.
				Subtracts 1 from register n and skips 1 program
				step if contents = 0.
DSZ(n)		10		Indirect decrement and skip if 0.  Subtracts
				1 from register pointed to by contents of
				register n and skips 1 program step if result
				is 0.
ISZn		11		Increment register n and skip if 0.  Adds 1 to
				contents of register n and skips 1 program step
				if contents = 0.
ISZ(n)		12		Indirect increment and skip if 0.  Adds 1 to
				register pointed to by contents of register n 
				and skips 1 program step if result is 0.
GTOa		13		Go to alpha (A-Z, a-z) label designator.  If
				executed from keyboard, positions program
				counter to program step immediately following
				the "LBLa" instruction, and returns control to 
				keyboard.  If executed as program step, finds
				"LBLa" instruction, and resumes execution with
				next program step.
GTOn		14		Go to numeric (0-255) label designator.  If
				executed from keyboard, positions program
				counter to program step immediately following
				the "LBLn" instruction, and returns control
				to the keyboard.  If executed as a program
				step, finds "LBLn" instruction, and resumes
				execution with next program step.
GTO(n)		15		Indirect go to numeric label.  Searches for
				numeric label entry corresponding to contents
				of register n, then proceeds as GTOn.
GSBa		16		Go to subroutine labeled "a".  Executes as
				GTOa when entered from keyboard.  When
				executed as a program step, program counter
				of next sequential step is loaded into a
				subroutine return point register, and program
				control is transfered to the program step
				immediately following "LBLa" instruction.
GSBn		17		Go to subroutine labeled "n".  Executes as
				GTOn when entered from keyboard.  When
				executed as a program step, program counter
				of next sequential step is loaded into a
				subroutine return point register, and program
				control is transfered to the program step
				immediately following "LBLn" instruction.
GSB(n)		18		Indirect go to subroutine.  Executes as
				GTO(n) when entered from keyboard.  When
				encountered as a program step, program counter
				of next sequential step is loaded into a
				subroutine return point register, and program
				control is transferred to the program step
				immediately following a numeric label entry
				corresponding to the contents of register n.

		19		Currently unassigned.

REGn		20		Displays current contents of register n.
REG(n)		21		Displays current contents of register pointed
				to by contents of register n.
CLREGn		22		Clears register n.
CLREG(n)	23		Clears register pointed to by contents of 
				register n.
><n		24		Interchanges contents of stack register X
				and register n.
><(n)		25		Interchanges contents of stack register X
				with contents of register pointed to by
				contents of register n.
RCLn		26		Recalls contents of register n to stack
				register X, lifting previous stack elements.
RCL(n)		27		Recalls contents of register pointed to by
				contents of register n to stack register X.
				Previous stack elements are lifted.
STOn		28		Stores contents of stack register X in register
				n; stack remains unchanged.
STO(n)		29		Stores contents of stack register X in register
				pointed to by contents of register n; stack
				remains unchanged.
STO+n		30		Adds contents of stack register X to register
				n; stack remains unchanged.
STO+(n)		31		Adds contents of stack register X to register
				pointed to by contents of register n; stack 
				remains unchanged.
STO-n		32		Subtracts contents of stack register X from
				register n; stack remains unchanged.
STO-(n)		33		Subtracts contents of stack register X from
				register pointed to by contents of register n;
				stack remains unchanged.
STO*n		34		Multiplies contents of stack register X by
				register n; stack remains unchanged.
STO*(n)		35		Multiplies contents of stack register X by
				register pointed to by contents of register n;
				stack remains unchanged.
STO/n		36		Divides register n by contents of stack register
				X, result placed in register n; stack remains 
				unchanged.
STO/(n)		37		Divides register pointed to by contents of
				register n by contents of stack register X;
				stack remains unchanged.

		38 to 63	Currently unassigned.

Following instruction only allowed under "programming" mode

GTO.i		64		Steps program to absolute step # i (1-1000).
				Program steps do not necessarily correlate to
				program memory locations, e.g. LBLa instruction
				requires 2 memory locations.

		65 to 119	Currently unassigned.

 d		120		Dummy instruction used for storing constants in
				program memory.  When in programming mode,
				any numeric string not associated with an
				instruction is interpretted as a constant and
				prefixed by this code #.  When executed as a
				program step, lifts stack and loads stack
				register X from program memory.

		121-123		Currently unassigned.

"prompt"	123		Types the character string enclosed by "'s
				for programmed prompting of user.
LOADfilespec	124		When entered from keyboard, loads program
				memory from "filespec" and returns to keyboard
				control pointing at first program step.  When
				encountered as a program step, loads program
				memory from "filespec" and begins execution at
				first program step.

Following instruction only valid in "programming" mode

SAVEfilespec	125		From programming mode, starts decoding current
				program memory into analogous character
				instructions and writing to "filespec".  Control
				returns to keyboard in programming mode.

GETREGfilespec	126		Loads registers 0 to 224 from specified file
				using list directed read format.
PUTREGfilespec	127		Writes current contents of registers 0-224 to
				specified file, 3 #'s per line separated by
				commas in "E24.17" format.


	a = alphabetic character A-Z, a-z
	n = unsigned integer number in range 0-255
	i = integer number (optionally signed) in range -32768 to 32767
	d = double precision floating point number in range .29E-38 to .17E39
 filespec = valid operating system file specification
   prompt = any valid ASCII string