Abort AST's in Fortran (and other high level languages).

                                   B. Z. Lederman

                                  Bankers Trust Co.

          Some  time  previously an article was published showing how to do such
     things as AST's from Fortran programs, and  in  particular  the  Abort  AST
     CALL SREA  identified  as  calling  and EXTERNAL function address.  This is
     really nice when you want a program to clean itself up before exiting  when
     it  is  aborted  by  command (or ran over the time limit in a Batch job, or
     some similar contition).  I followed the instructions in the  example,  and
     it  worked very well on RSX-11M-Plus, but I began to run into problems when
     I tried to move the same program  to  a  PRO-350  with  P/OS.   The  system
     documentation  (both  M-Plus  and P/OS) clearly state that there are severe
     limitations  on  doing  AST  servicing  in  Fortran  for  various  reasons,
     including the fact that the OTS impure regions can get very messed up.  You
     are not supposed to do any Fortran I/O or file services in AST state, which
     limits  the  clean-up  you  can do.  My program was doing some I/O, and got
     away with it on M-Plus, but it worked  only  some  of  the  time  on  P/OS.
     Because  I wanted my programs to work every time, I developed the following
     simple subroutine which does all of the AST servicing in  a  macro  module:
     because  it exits AST state when done, your high level language program can
     do what it wants when cleaning up.  

          The module is very simple:  

        .TITLE ABORT
        .IDENT /V2.0/
     ;
     ;  Abort AST function for Fortran programs
     ;
     ;  B. Z. Lederman          Bankers Trust Co.
     ;
     ;  Use of this module is entirely at the users' risk. No liability
     ;          of any kind is assumed.
     ;
        .MCALL  ASTX$S, SREX$S
     ;
     ;  The following PSECT matches the attributes set by Fortran for
     ;          common areas.
     ;
        .PSECT  ABOCOM, RW, D, GBL, REL, OVR
     ABOFLG::
        .WORD   0                       ; LOGICAL*2 data type
     ;
        .PSECT  $ABRTC, RO, I, GBL, CON, LCL
     ;
     ABOINI::
        CLR ABOFLG                      ; set abort to .FALSE.
        SREX$S   ABOAST                 ; specify AST point
        RETURN                          ; return to main program
     ;
     ABOAST::
        ADD (SP), SP                    ; clean up stack
        DEC ABOFLG                      ; set abort to .TRUE.
        ASTX$S                          ; leave AST state
     ;


                                                                         Page  2



        .END

     The  PSECTs  have  been  chosen to be compatible with those produced by the
     Fortran-77 (and Fortran-IV-Plus) compilers, and can be seperated into I and
     D  space.  It is an ABSOLUTE requirement that this module be in the ROOT of
     your program (both the code and the data common PSECTS), otherwise you  may
     not  receive  AST  notification  properly.  An example of how the module is
     used follows.  

        PROGRAM ABOTST
     C
     C  Test Abort-AST action
     C
     C  B. Z. Lederman
     C
        LOGICAL*2 ABOFLG
     C
        COMMON /ABOCOM/ ABOFLG
     C
     C  Initialize abort
     C
        CALL ABOINI
     C
        OPEN (UNIT = 1, FILE = 'ABOTST.DAT', STATUS = 'NEW')
     C
     C  Begin dummy loop
     C
        DO 100 I = 1, 10000
        DO 100 J = 1, 10000
        DO 100 K = 1, 10000
        IF (ABOFLG) GOTO 900
        WRITE (1, 920) I, J, K
     100        CONTINUE
        STOP ' Reached end of all loops'
     C
     900        WRITE (5, 920) I, J, K
     920        FORMAT( 3( 1X, I5) )
        CLOSE (UNIT = 1)
        CALL EXIT
     C
        END

          The declaration of ABOFLG as LOGICAL*2 and ABOCOM are used to match up
     the variable and the area where it is stored.  The call  to  ABOINI  should
     occur  at  the  beginning  of  your program to set ABOFLG and the abort AST
     entry points to the correct values.  The task build would be something like
     this:  

      TKB ABOTST = ABOTST, ABORT 

     Or if overlayed, the ODL file should have something like:  

             .ROOT   ABOTST-ABORT-*( tree1, tree2, etc.) 



                                                                         Page  3



     Both  of  which are intended to force the ABORT module into the root of the
     program.  

          The  benefit  of abort AST's may be seen by running the above program:
     when aborted, the program will close the file ABOTST.DAT, and print out the
     current values of I, J, and K on the terminal.  If you run the same program
     without the AST routines and abort it, the file ABOTST.DAT will be  locked,
     and  you  will  not  learn the state the program was in when aborted.  I am
     sure that nearly every reader can think  of  an  application  where  it  is
     desireable  for  a program to do clean-up work when aborted, or at least to
     leave files properly closed rather than locked.  

          To  derive  the greatest benefit from this abort AST routine, you must
     test ABOFLG fairly often:  the macro module only sets the value of  ABOFLG,
     and  it  is  up to you to test it's status and shutup when you are supposed
     to.  I generally put it at the beginning  of  any  long  loops,  or  before
     reading  new  data  to  process,  or  after  writing out a data item, or in
     similar  "breaks"  in  processing.   In  the  above   example,   the   test
     IF (ABOFLG) GOTO 900  will  occur  on  every  pass  through  the  loop,  so
     notification that an abort AST has been received will be quick.  

          I  would hope the following information is superfluous, but in case it
     isn't:  do not use the variable ABOFLG for anything else in  your  program,
     and don't put any other variables into ABOCOM.  

          This  method  should  work  just  as  well  for  other languages.  The
     requirements are that you be able to declare some kind of common  area  for
     ABOFLG,  and  that  you be able to declare a one word integer and test it's
     state.  It will be zero (all bits off) if false (no abort yet), and a minus
     one  (all bits on) if true (time to abort).  Fortran-77 tests only the sign
     bit, but any test that can distinguish these two states is  equally  valid.
     The   calling   convention   to   ABOINI   is   the  usual  DEC  convention
     (JSR PC, ABOFLG), with the argument list on R5:  in this case, there are no
     arguments,  so  no  registers  are tested or altered.  The RETURN statement
     translates to an RTS PC.  

          An  alternative  I  considered  was  to  have  the  macro  module do a
     subroutine call to an ENTRY in  the  main  program  from  the  AST  service
     routine.   The  problem  with  this would be that the Fortran program would
     have to do servicing at AST  time,  which  is  exactly  what  needs  to  be
     avoided.   However, the restrictions on AST service might not apply to some
     other high level languages, and if declaring a common region  is  difficult
     in that other language, then it might be easier to have the macro module do
     a call to the other language module which will do the abort  clean  up  and
     exit.   If  you  do  try  this, remember that when the AST service state is
     entered, the stack has additional information placed on it, and that  other
     registers may not be preserved.