VSDRV VERSION 2 -- VARIABLE SEND-DATA DRIVER FOR RSX-11M

			by:  John Osudar
			     Science Applications, Inc.
			     1211 W. 22nd Street, Suite 901
			     Oak Brook, IL 60521

	(This document corresponds to VSDRV V2.04, dated 30-Oct-81)
This work was supported by the Light Water Breeder Reactor Proof-of-Breeding
	Analytical Support Project at Argonne National Laboratory.

Introduction
------------

RSX-11M V3.2 provides several means for communication between tasks.  Among
these are global event flags, common memory, and the send/receive data
directives.  The latter provide for data transfer from one task to another,
but restrict the amount of data to 13 words per transfer.  RSX-11M-Plus
allows variable-length data blocks of up to 256 words in length; this
feature is not provided with RSX-11M, because it requires support for
secondary executive pool, which RSX-11M does not have.

Because a "variable length send/receive" function can be useful in a number
of applications, a simple driver has been written to provide some of the
same functionality.  The RSX-11M device name chosen for this driver is VS:
(for Variable Send-data), and its features are as follows:

The driver is actually a queue manager, which has its own private pool of
dynamic memory.  Functions provided include:  create a queue, put a message
in a queue, get a message from a queue, and delete a queue.  Each queue has
a six-character name.  When a task accesses a queue, it specifies the queue
name.  By default, each task can access a queue whose name is the same as
the task's name.  If selected when the driver is assembled, a protection
feature prevents non-privileged tasks from operating on queues other than
their default queue, except for writing.  (Any task can write a message to
any queue).  Queues are created explicitly through driver QIO calls,
and are always accessed in FIFO (first-in, first-out) order.

With VS: Version 2, a number of additional features have been added to the
driver.  The ability to request a "read with wait" has been retained.  (This
feature causes a read request on an empty queue to wait until a message is
available).  However, "read with wait" has the negative effect of causing
the requesting task to be fixed in memory while the request is pending.  To
alleviate this problem, an AST (Asynchronous System Trap) mechanism has been
added in Version 2.  A task can specify an AST routine to be called each
time a message is received in a particular queue.  Unlike "read with wait",
specifying AST's does not cause the task to become fixed in memory, since
RSX-11M will reload a task that has been checkpointed out to disk when an
AST occurs for that task.  Another new feature of VS: Version 2 is the
"create or flush" function, which creates a new empty queue if not already
present, but flushes the queue of all messages (and aborts a waiting read
request) if the queue already exists.  Version 1 required a "delete queue"
followed by a "create queue" to achieve the same effect.

VS: Version 2 is compatible with Version 1, with one exception:  the
function code for the "dump driver pool" function, which is not intended for
general use, has been changed from octal 3400 to octal 4000, because octal
3400 is the code for a standard DEC I/O function that VS: now uses.  This
function is only used for debugging, and by the VS: utility program VSUTIL,
which has been modified for Version 2.


Function, Parameters, Status Codes
----------------------------------

Here is a list of the QIO function codes recognized by the VS: driver.
All function codes are in octal.

IO.KIL		(0012)	Cancel all waiting read requests for this task.
IO.WLB		(0400)	Put a message into any existing queue.
IO.RLB		(1000)	Get a message from a queue.
IO.RLB ! SF.WAI	(1200)	Wait for a message to be put into a queue, and get it.
IO.ATT		(1400)	Device attach -- ignored.
IO.DET		(2000)	Device detach -- ignored.
IO.CRQ		(2400)	Create a new message queue.
IO.CRQ ! SF.FLU	(2500)	Create a new message queue, or flush an existing one.
IO.DLQ		(3000)	Delete a message queue and all queued messages.
IO.CLN		(3400)	Clear all AST's set by this task.
IO.DMP		(4000)	For utilities or debugging, dump a snapshot of the
			driver's pool.
IO.AST		(4400)	Set or clear an AST for an existing queue.
IO.EXM		(5000)	Examine a selected message in a queue, without
			dequeuing it.
IO.DLM		(5400)	Delete a selected message from a queue.

The six-word QIO parameter list is used by VS: as follows:

Word 1 -- 	Buffer address (with IO.WLB, IO.RLB, IO.DMP, IO.EXM)
Word 2 -- 	Buffer length in bytes (with IO.WLB, IO.RLB, IO.DMP, IO.EXM)
Word 3 -- 	First word of RAD50 queue name (with IO.WLB; for privileged
		tasks, also with IO.RLB, IO.CRQ, IO.DLQ, IO.AST, IO.EXM,
		IO.DLM)
Word 4 -- 	Second word of RAD50 queue name (same functions as word 3)
Word 5 -- 	Message ID (with IO.EXM, IO.DLM)
Word 6 -- 	Address of AST routine, or 0 to clear AST (with IO.AST)

Notes:
(*) Buffers used with VS: must be aligned on word boundaries.
(*) The "read" function returns the name of the sending task (in RAD50
    representation) in the first two words of the buffer.  Thus, if you are
    expecting messages of up to  N  bytes in length, you must provide at
    least  N+4  bytes of buffer space for a "read" operation.
(*) Under no circumstances can any task clear an AST other than the task that
    set the AST.  Also, setting an AST for a queue prohibits read-and-wait,
    flush, or delete queue operations, but does not prohibit a simple read
    operation.
(*) The AST routine receives control with three parameter words on its stack:
    the first two words are the queue name in RAD50 representation, and the
    third word is the length of the message in bytes, including four extra
    bytes for the sender task name.  See the Executive Reference Manual for
    details about AST processing.
(*) The "examine message" and "delete message" operations utilize a "message-
    ID", which is actually the virtual address of the message in VSDRV
    space.  Message-ID 0 corresponds to the first message in a queue.
(*) The "examine message" function can be called with a buffer of any length;
    as much of the message as will fit into the buffer will be copied.  The
    buffer will contain four words of information preceding the message.  The
    first word is the message-ID of the NEXT message in the queue, or 0 if
    this is the last one.  The second word contains the length of the message
    text in bytes.  The third and fourth words contain the sender task name
    in RAD50.


Status codes that can be returned by VS: in the first word of the I/O status
block include:

IS.SUC	(+1.)	Successful completion; second word of IOSB is a byte count.
IE.ABO	(-15.)	Operation aborted due to IO.KIL, SF.FLU, IO.DLQ, or I/O
		rundown at task exit.
IE.PRI	(-16.)	Privilege violation--unprivileged task attempted to create,
	 	delete, set an AST in, or read a queue other than its default,
	 	or attempted to do an IO.DMP function (only if protection
		enabled).
IE.QNF	(-101.)	Queue not found.
IE.QEX	(-102.)	Queue already exists (on attempt to create a queue).
IE.NMS	(-103.)	No more space in VS: private pool.
IE.RAW	(-104.)	Read already waiting on queue (for IO.RLB ! SF.WAI, or IO.AST)
IE.NOM	(-105.)	No message available in queue (for IO.RLB without SF.WAI,
 	 	IO.EXM, or IO.DLM).
IE.UBS	(-106.)	User buffer is too small to hold entire message (or to hold
	 	entire driver pool snapshot, for IO.DMP).
IE.ATS	(-107.)	AST is already set (for IO.RLB ! SF.WAI, IO.AST specifying an
	 	AST address, IO.AST clearing another task's AST, IO.CRQ!SF.FLU
		or IO.DLM to a queue whose AST was set by another task)
IE.ATC	(-108.)	No AST is set for queue (for IO.AST clearing an AST).

Disadvantages and advantages of VS: Version 2
---------------------------------------------

Disadvantages (compared to true variable send/receive on RSX-11M-Plus):

1.  At least one LUN must be set aside for use with VS:--this LUN is the one
    you use for setting AST's.  If you use "read and wait", then one LUN must 
    be set aside for each simultaneous outstanding wait.  True variable
    send/receive does not require any LUN's.
2.  The VS: driver and its private pool occupy additional memory space, which
    cannot be used for other purposes when not in use by VS:.  True variable
    send/receive code is part of the exec, and its pool space is part of the
    exec's secondary pool, which is usable by other system components.
3.  VS: requires that queues be created, flushed, and deleted explicitly.
    True variable send/receive automatically has a queue for each task, which
    is created when the task is installed, flushed when the task exits, and
    deleted when the task is removed.

Advantages (compared to true variable send/receive on RSX-11M-Plus):

1.  VS: can be used under RSX-11M, which does not support variable
    send/receive or secondary exec pool; the only cost in terms of exec
    resources is the I/O packet and AST block usage.
2.  VS: queues exist independent of tasks in the system.  When a task exits,
    no messages are deleted (not even from a task's "default" queue); queues
    can still be "flushed" using the "create or flush" function.
3.  VS: allows a task to manipulate several queues of messages, while variable
    send/receive provides only one queue per task.  With VS:, tasks can share
    queues, under some protocol established among them, if the application
    requires.  (For example, you can create a spooling system with several
    despoolers taking requests from the same queue.)
4.  VS: allows selective examination and deletion of messages in any queue.


Use of VS: from FORTRAN
-----------------------

Here are some notes on using VS: Version 2 from a FORTRAN program.  Most of
this information can be found in the RSX-11M/M-PLUS Executive Reference
Manual.

(1) Setting up the QIO parameter list

The QIO parameter list is an array of six integers.  The VS: driver uses
these six words as described previously.  To create the parameter list, use
a statement like this:

	INTEGER IPARM(6)

To put a buffer address into the first word, use the library subroutine
GETADR, like this:

	CALL GETADR(IPARM(1),IBUFER)

(Here, IBUFER is the name of the buffer array that is used to transfer
messages between the driver and the task).  To put a buffer size into the
second word, use a simple assignment statement:

	IPARM(2)=124

(This tells the driver that 124. bytes of storage are available in the
buffer on a read request, or that the message being sent is 124. bytes
long on a write request.  This would require that the buffer array be
declared to contain at least  124/2 = 62  words, e.g.

	INTEGER IBUFER(62)

or the equivalent).  To put a RAD50 queue name into the third and fourth
words, you must create a two-word integer array containing the queue name,
and set the name into the array with a DATA statement, like this:

	INTEGER QNAME(2)
	DATA QNAME/3RMYQ,3RUE5/

(The constant form 3Rxxx is like 3Hxxx or 'xxx' but creates a RAD50
representation of the character string.  In this case, QNAME(1) will contain
the string 'MYQ', and QNAME(2) will contain 'UE5', which together form the
name of the queue 'MYQUE5').  Then, you put the queue name into the
parameter list with two simple assignments:

	IPARM(3)=QNAME(1)
	IPARM(4)=QNAME(2)

(There are other ways to do this, especially for cases where the queue name
is not a constant determined at compilation time, but may be determined when
the program is run.  Consult the FORTRAN User's Guide for subroutines that
convert ASCII character strings to RAD50, if you need them).  Note that you
do not need to set up the first two words of the parameter list unless you
are doing a "read" or "write" function, and that the third and fourth
words can be set to zeroes if you want to use your task's default queue name
(same as the task name).  Setting up parameter word six with the AST
subroutine address is not discussed here, as a special interface routine is
generally used to allow FORTRAN to process AST's.  This routine is described
in detail later.


(2) Assigning a unit to the VS: driver

In order to access the VS: driver, you must have a logical unit assigned to
it.  This can be done when you build your task, with an option like this:

	ASG=VS:3

(which assigns LUN 3 to the VS: driver).  Also, you can do this with a
subroutine call within your program:

	CALL ASNLUN(3,'VS',0)

Here, you specify the LUN as the first parameter; the other parameters must
be 'VS' and 0 as shown.  You can assign as many LUN's to the VS: driver as
you need.  In particular, if your program will be using "read and wait"
with more than one queue at the same time, then you must have as many LUN's
assigned as there will be simultaneous waits.

(3) Doing the actual operation

To do the operation, you call one of the library routines QIO or WTQIO.  In
both cases, the calls are identical:

	CALL QIO  (fnc,lun,[efn],,[isb],[prl][,ids])
	CALL WTQIO(fnc,lun,[efn],,[isb],[prl][,ids])

The parameters enclosed in [  ] are optional, but commas must be included as
shown, even if some parameters are left out.  The parameters are:

fnc	One of the octal function codes, specified in FORTRAN with a leading
	'"' to signify "octal"; e.g.  "1200
lun	The logical unit number on which to perform this operation.  The LUN
	must already be assigned to VS:
efn	An event flag number.  Event flags are single-bit flags that can be
	used to signal the occurrence of certain events, in this case the
	completion of the requested operation.  You should probably use
	"local" event flags here (event flags used only by your task);
	these flags are numbered from 1 to 32.  It is through the event flag
	that you determine when the operation has been completed.
isb	The name of a two-word array, the I/O status block, which receives a
	status code in the low byte of the first word, and a byte count in
	the second word.  The status code should be  +1  for successful
	operations.  The byte count tells you how long the message is when you
	do a read, and should equal your message length when you do a write.
prl	The name of the six-word parameter list array.
ids	An integer variable into which the system places a "directive status";
	if you have made any mistakes in setting up the call, or if some
	condition has occurred that has prevented your request from being
	passed to the VS: driver, this word will contain an error code.
	Normal completion should produce a  +1  status.

The difference between using the QIO and WTQIO calls is this:  WTQIO will
not return control to your program until the operation has been completed,
while QIO will return as soon as the operation has been set up and sent to
the VS: driver.  Look at the Executive Reference Manual for subroutines that
test event flag status, or stop/wait for event flags to be set, if you are
planning on using the QIO call instead of the WTQIO call.


Use of VS: AST's from FORTRAN
-----------------------------

The Executive Reference Manual states that FORTRAN does not support AST
routines.  This does not mean that you can't process AST's in a
FORTRAN routine; it only means that FORTRAN doesn't provide the
necessary interface between the RSX-11M AST mechanism and itself.

When an AST occurs, RSX-11M saves part of the current status of the program,
and transfers control to the specified AST routine.  Depending upon the type
of AST that has occurred, several parameters may be passed by the system to
the AST routine.  The method used for passing these parameters is not
compatible with the way FORTRAN calls subroutines; this is one of the reasons
why FORTRAN doesn't directly support AST routines.  A second reason is that
the system does not save the program's register contents before entering
the AST routine; since FORTRAN subroutines freely modify all registers, this
is also an incompatibility.  Finally, when an AST routine completes its
processing, it must return control to the system (for restoring of the
program's status and clearing of the "AST state" indicator); FORTRAN
subroutines simply perform a "RETURN" operation, which is not enough.
Therefore, in order to process AST's within a FORTRAN routine, some
additional interfacing code must be supplied, written in MACRO-11.

Many different types of AST interface modules for FORTRAN can be written;
you should have a special one written for you if your needs aren't met by
those described here.  Each such module will have the following components:
an initialization routine, a "set AST for queue" routine, a "clear AST
for queue" or "clear all AST's" routine, and an internal AST routine that
gains control when an AST occurs, saves the program's registers, sets up the
parameter list for the FORTRAN AST routine, calls the FORTRAN AST routine,
and finally cleans up the stack, restores the registers, and does an "AST
exit" after the FORTRAN routine returns.

AST setup module IVSAST

IVSAST consists of FORTRAN-callable function IVSAST, and an internal AST
interface routine.  IVSAST allows a list of queues to be specified, and
either a single FORTRAN routine, or a list of FORTRAN routines, to be
associated with the AST's for those queues.  The internal AST routine calls
the appropriate FORTRAN routine when an AST occurs, passing it the queue
name and message length.  Individual clearing of AST's for queues is not
provided, but all AST's set by the program may be cleared by calling IVSAST
a second time, with no queue name list.  For further details, look at
documentation in the source code for IVSAST.

AST setup module BCTVSAST1

BCTVSAST1 consists of FORTRAN-callable subroutines VSAST1, ASTSET, and
ASTCLR, and an internal AST interface routine.  VSAST1 is called once, to
specify the VS: logical unit number, an event flag for internal use, and the
single FORTRAN AST routine.  Then, ASTSET is called to set an AST for a
single queue, and ASTCLR is called to clear the AST for a single queue.  The
internal AST routine calls the FORTRAN routine when an AST for any queue
occurs, passing it the queue name and message length.  To clear all AST's at
once, a call to the Executive subroutine WTQIO must be made.  For further
details, look at documentation in the source code for BCTVSAST1.


VSUTIL Utility Program
----------------------

(This corresponds to version V02.02 of VSUTIL, dated 31-Jul-81.)

VSUTIL provides some utility functions related to the VS: Variable Send-data
driver, Version 2.  The following commands are recognized (each command keyword
can be abbreviated to just the first letter):

QUEUES ["queue"]
	Displays summary of queues on the terminal, or display all
	messages in a single queue.
SHOW ['filename']
	Produces a snapshot of VS: private pool, queues, messages.
CREATE "queue"
	Creates a queue with the specified name.
DELETE "queue"
	Deletes the specified queue, and all messages in it.
FLUSH "queue"
	Flushes the specified queue of all messages
REMOVE msg-id,"queue"
	Removes the specified message from the specified queue

" ... " are required delimiters for queue names, because queue names are
allowed to have embedded (but not leading) blanks; if VSUTIL is run through CCL,
the delimiters must be doubled up ("" ... "") on the MCR command line in order
to be passed through to VSUTIL by CCL.

[ ... ] indicates optional parameters.

"Message-ID" is the virtual address of the message.

If this program is passed an MCR command line, the line must be
one of the valid commands listed above, or the form "@FILENAME".
The latter form is particularly useful if VSUTIL is run from your
STARTUP.CMD file to set up permanent queues.