Send/Receive Driver for RSX-11M                 






















           Variable Length Send/Receive Driver for RSX-11M v.3.2



                              Joseph Sventek
                 Computer Science & Mathematics Department
                       Lawrence Berkeley Laboratory
                            Berkeley, CA  94720



























                                    -1-                               



                      Send/Receive Driver for RSX-11M                 


     The   send/receive   driver  permits  a  variable-length  message
     capability for RSX-11M v.3.2.  The receiver task does not have to
     be installed for the message to be buffered.   The  messages  are
     buffered  in  an internal pool within the driver, thus freeing up
     the Dynamic Storage Region of  RSX  for  other  myriad  uses.   A
     lifetime  is  associated  with  each  message,  after  which  the
     internal buffer space is freed up for further  use.  The  buffers
     are also freed when the message is read by the receiver task.
     
     The flushing of messages is performed as follows: when the driver
     is  loaded, it is called at its powerfail entry point.  There, it
     attempts to allocate a clock queue control block  from  DSR.   If
     this  is  successful, it fills in the appropriate information and
     queues a timer request for itself TINTPT seconds in  the  future.
     If  the  clock block could not be allocated, the device is marked
     off-line and a "DEVICE  NOT  READY"  message  is  issued  at  the
     console via TKTN. If this happens to you, your system is ready to
     crash anyway, but the check is performed nonetheless.
     
     When  the  timer  routine  is  entered,  the queue of messages is
     searched for messages which have outlived their usefulness.   Any
     found  are  removed  from the queue and their buffers returned to
     the  driver's  internal  pool.   Just  before  returning  to  the
     executive,  the  timer  routine  queues another timer request for
     itself TINTPT seconds in the future.
     
     Due to this perpetual timer, just unloading the driver  could  be
     catastrophic,  since the timer request is for a fixed location in
     physical memory.  In order to permit unloading of the  driver,  a
     separate  task is provided (UNX, extended unload).  UNX issues an
     IO.STP QIO to the driver.  If this QIO succeeds, UNX then  spawns
     the following commands to MCR...:
     
                         DEVICE SR:
                         UNLOAD SR:
                         DEVICE SR:
     
     UNX  is  distributed  with  the  Virtual  Aether  driver  on  UIC
     [307,35].   The  QIO  will  fail  if  UNX  is  invoked   from   a
     non-priveleged  terminal.   If  you use SR: for passing arguments
     within the Software Tools system, it is suggested that you VMR it
     into DRVPAR and leave it there.
     
     
     To build the driver,  copy  the  contents  of  [307,34]  to  your
     current UIC and invoke
     
     >@SRGEN
     
     Answer the questions and have fun.
     
     
     After  loading  the  driver,  it  can  be tested by compiling and


                                    -2-                               



                      Send/Receive Driver for RSX-11M                 


     task-building SRTEST.FTN.  This program prompts the  user  for  a
     message  to  send  to itself, and then reads the message from the
     driver.  Unless you get an error message from SRTEST,  everything
     is working OK.
     
     In  case  your wondering at the distinction between SRDRV.MAC and
     srdrv.m, the latter  is  an  archive  of  the  individual  source
     modules  needed  to  generate the former.  To generate SRDRV.MAC,
     type the following command to the shell:
     
     ar p srdrv.m | tr "a-z_" "A-Z$" >srdrv.mac
     
     
     All  driver  routines  subscribe  to   the   following   register
     conventions:
     
                         r0	free for use
                         r1	free for use
                         r2	address of message header block
                         r3	address of i/o request packed
                         r4	address of TCB
                         r5	address of UCB
                         
     If any of r2-r5 are to be used, they must be saved and restored.
     
     The  maximum  message  size  is  kept in U.CW4 of the UCB.  It is
     assembled to be the value specified to SRGEN, but can be  changed
     dynamically via the SET /BUF=SR:n MCR command.



























                                    -3-                               



                      Send/Receive Driver for RSX-11M                 


                             Vital Statistics
     
     Device name - SR0:
     
     Legal Function codes
     
     IO.WVB,IO.WLB
     
          p1	buffer address
          p2	# of bytes to write
          p3	high order half of receiver taskname (rad50)
          p4	low order half of same
          p5	message lifetime (in seconds)
          p6	if non-zero, flush all currently buffered messages for
          	this sender-receiver pair before queueing this message.
          
     IO.RVB,IO.RLB
          
          p1	buffer address
          p2	size of buffer in bytes
          
          
     IO.STP
          
          
     status returns
          
     writes
          IS.SUC - word 2 of iosb has number of bytes written == p2
          IE.BAD - no task name specified in p3-p4
          IE.ALC - could not allocate internal buffers for message
          IE.NOD - could not allocate message header block
          
     reads
          IS.SUC - word 2 of iosb has number of bytes read
          IE.DAO - message bigger than buffer, only p2 bytes copied
          IE.DNA - data not available
          
     stop
          IS.SUC
          IE.PRI - not invoked by a priveleged terminal














                                    -4-