A GKS Subroutine Library for RT-11 (V0.20)
                                  James V.  Flatten
                              Ames Laboratory, ISU/DOE






















                                        NOTE

               This  GKS subroutine library was written by Jim Flatten
               of the Ames Laboratory at Iowa State University as part
               of  U.S.   Department of Energy contract W-7405-ENG-82.
               The right to use this software release  is  allowed  in
               the  public  domain.   The author, Ames Laboratory, and
               USDOE assume no responsibility as to the correctness of
               the code nor the appropriateness for such use as it may
               be applied.  Any  comments  may  be  addressed  to  Jim
               Flatten;   258I  Metals  Development;  Ames Laboratory;
               Ames, IA  50011 

















                                      13 May 87
                                      20:28:36










          CHAPTER 1  GKS FOR RT-11 (V0.20)                              1-1 
                  1.1  INTRODUCTION                                     1-1 
                  1.2  CONCEPTS                                         1-2 
                  1.3  OUTPUT PRIMITIVES                                1-3 
                  1.4  OUTPUT PRIMITIVE ATTRIBUTES                      1-4 
                  1.5  WORKSTATIONS                                     1-5 
                  1.6  COORDINATE SYSTEMS AND TRANSFORMATIONS           1-6 
                  1.6.1  Normalization transformations                  1-6 
                  1.6.2  Clipping                                       1-7 
                  1.6.3  Workstation transformations                    1-7 

          CHAPTER 2  FUNCTIONAL DESCRIPTIONS                            2-1 
                  2.1  ACTIVATE WORKSTATION                             2-2 
                  2.2  CLOSE GKS                                        2-3 
                  2.3  CLEAR WORKSTATION                                2-4 
                  2.4  CLOSE WORKSTATION                                2-6 
                  2.5  DEACTIVATE WORKSTATION                           2-7 
                  2.6  OPEN GKS                                         2-8 
                  2.7  OPEN WORKSTATION                                 2-9 
                  2.8  POLYMARKER                                      2-10 
                  2.9  INQUIRE COLOR FACILITIES                        2-11 
                  2.10  INQUIRE CURRENT CHARACTER HEIGHT               2-12 
                  2.11  INQUIRE CHARACTER UP VECTOR                    2-13 
                  2.12  INQUIRE CLIPPING INDICATOR                     2-14 
                  2.13  INQUIRE CURRENT NORMALIZATION
                        TRANSFORMATION NUMBER                          2-15 
                  2.14  INQUIRE COLOR REPRESENTATION                   2-16 
                  2.15  INQUIRE FILL AREA COLOR INDEX                  2-18 
                  2.16  INQUIRE FILL AREA INTERIOR STYLE               2-19 
                  2.17  INQUIRE LINETYPE                               2-20 
                  2.18  INQUIRE LEVEL OF GKS                           2-21 
                  2.19  INQUIRE POLYMARKER INDEX                       2-22 
                  2.20  INQUIRE NORMALIZATION TRANSFORMATION           2-23 
                  2.21  INQUIRE POLYLINE COLOR INDEX                   2-24 
                  2.22  INQUIRE POLYMARKER COLOR INDEX                 2-25 
                  2.23  INQUIRE TEXT ALIGNMENT                         2-26 
                  2.24  INQUIRE WORKSTATION CONNECTION AND TYPE        2-27 
                  2.25  INQUIRE WORKSTATION TRANSFORMATION             2-28 
                  2.26  SET CHARACTER HEIGHT                           2-30 
                  2.27  SET CHARACTER UP VECTOR                        2-31 
                  2.28  SET CLIPPING INDICATOR                         2-32 
                  2.29  SELECT NORMALIZATION TRANSFORMATION            2-33 
                  2.30  SET FILL AREA COLOR INDEX                      2-34 
                  2.31  SET FILL AREA INTERIOR STYLE                   2-35 
                  2.32  SET LINE TYPE                                  2-36 
                  2.33  SET MARKERTYPE                                 2-37 
                  2.34  SET POLYLINE COLOR INDEX                       2-38 
                  2.35  SET TEXT ALIGNMENT                             2-39 
                  2.36  SET TEXT COLOR INDEX                           2-40 
                  2.37  SET VIEWPORT                                   2-41 
                  2.38  SET WORKSTATION VIEWPORT                       2-42 
                  2.39  SET WORKSTATION WINDOW                         2-43 
                  2.40  SET WINDOW                                     2-44 
                  2.41  TEXT                                           2-45 
                  2.42  UPDATE WORKSTATION                             2-47 

          CHAPTER 3  USING GKS WITH RT-11                               3-1 
                  3.1  INCORPORATING GKS INTO FORTRAN SOURCE
                       PROGRAMS                                         3-1 


                                         -i-





          
          


                  3.2  LINKING PROGRAMS WITH GKS                        3-2 
                  3.2.1  Linking One Driver                             3-2 
                  3.2.2  Linking More than One Driver                   3-2 
                  3.3  RUNNING PROGRAMS THAT USE GKS                    3-3 





















































                                        -ii-

















                                      CHAPTER 1

                                GKS FOR RT-11 (V0.20)





          1.1  INTRODUCTION 


               This  document  describes an implementation of the Graphical
          Kernal System (GKS) for the RT-11 operating system running  on  a
          PDP-11  computer.   GKS  is  both  an international standard (ISO
          7942-1985) and an American National Standard (ANSI  X3.124-1985).
          The standard specifies twelve different levels.  This implementa-
          tion is the lowest level of GKS, GKS level MA.  As such it has no
          support for graphical input, segment support or metafile input or
          output.  Level MA was chosen to  keep  the  graphical  subroutine
          library small and efficient for applications running under RT-11. 

               Three  device drivers are provided.  The drivers are for the
          HP7475 6 pen plotter (DRV745.OBJ), the Tektronix 4107 color  ter-
          minal  (DRV407.OBJ)  and the Visual 550 terminal (DRVV50.OBJ, Tek
          4010 compatible).  More than one driver may be loaded at a  time.
          Source  code for the device drivers is included so that users can
          use them as templates to generate new device drivers.  The driver
          interface  is loosely based on the emerging Computer Graphics In-
          terface (CGI) being developed by the X3H3.3 committee.  

               This  release  of GKS (V0.20) for RT-11 is incomplete.  Ver-
          sion 1.00 will be complete and will be available by the Fall 1987
          DECUS  Symposium in Anaheim.  In particular, the Fill Area output
          primitive has not been  implemented,  error  handling  is  spotty
          (some  errors  cause  something to happen, others don't), the do-
          cumentation is incomplete and a few inquiry  subroutines  produce
          no  result  (specifically  GQCR, INQUIRE COLOR REPRESENTATION and
          GQCF, INQUIRE COLOR FACILITIES), they are just stubs.  There  are
          also  sure to be bugs.  In spite of these problems, you can still
          do useful work with the package as it  stands.   The  implemented
          output  primitives  are  POLYLINE, POLYMARKER, and TEXT.  All the
          specified attributes for these primitives are implemented.  

               My  intention  has  been to follow the GKS standard exactly.
          Where differences occur, it is because the package is  incomplete
          at this time, coding or design errors have crept in or because of
          my misinterpretation of  the  intent  of  the  standard.   Please


                                        -1-1-





          GKS FOR RT-11 (V0.20)
          Introduction


          advise  me of discrepancies and be aware that there may be signi-
          ficant changes between now and the next release, if and when such
          discrepancies are found and corrected.  

               Much  of the following documentation has been taken directly
          from the ANSI GKS document.  Material about segments and  graphi-
          cal  input  has  been  removed  in  most places however, to avoid
          references to functionallity that is not, and probably  will  not
          be, a part of this subroutine library.  


          1.2  CONCEPTS 


               Graphical  output  generated  by  GKS  is  built up from two
          groups of basic elements called output primitives  and  primitive
          attributes.   Output primitives are abstractions of basic actions
          a device  can  perform,  such  as  drawing  lines,  and  printing
          character  strings.   Attributes control the appearance of output
          primitives on a device, such as linestyle, color,  and  character
          height.   Non-geometric aspects, such as color, can be controlled
          for each workstation individually, to make best use of its  capa-
          bilities.  

               Output and Input are the components of an abstract workstat-
          ion.  A GKS workstation has zero or one display surfaces and zero
          or  more  input  devices,  such as keyboard, tablet and lightpen.
          The workstation presents these devices to the application program
          as a configuration of abstract devices thereby shielding the pro-
          grammer from the hardware peculiarities of a particular device.  

               The  geometrical information (coordinates) contained in out-
          put  primitives  can  be  subjected  to  transformations.   These
          transformations  perform  mappings  between three coordinate sys-
          tems, namely:  

               1.  World   Coordinates   (WC),   used  by  the  application
                   programmer;  

               2.  Normalized  Device  Coordinates  (NDC), used to define a
                   uniform coordinate system for all workstations;  

               3.  Device  Coordinates  (DC),  one  coordinate  system  per
                   workstation, representing its display space coordinates. 


               Output  primitives  and attributes are mapped from WC to NDC
          by normalization tranformations, and from NDC to DC  by  worksta-
          tion transformations.  

               The  attributes which control the appearance of parts of the
          picture on the display surface are organized in a uniform manner.
          Two  groups  of attributes apply to the appearance of each output
          primitive:   primitive  attributes  and  workstation  attributes.
          Primitive  attributes  are  specified  modally  and  are  forever


                                        -1-2-





                                                      GKS FOR RT-11 (V0.20)
                                                                   Concepts


          associated with a primitive when it is  created.   The  primitive
          attributes include all geometrical aspects of primitives, such as
          character height for text, and pattern size for  fill  area.   In
          addition,  the  non-geometrical  aspects  of  primitives are con-
          trolled by the primitive attributes in one of two ways.  Either a
          single attribute is used to specify all the non-geometric aspects
          of the primitive by an index which points to a workstation depen-
          dent  representation  (set of values) or one attribute is used to
          specify each of the non-geometric aspects of the primitive  in  a
          workstation  independent  way.   The  former  is  referred  to as
          bundled specification and the latter is referred to as individual
          specification.    [4mLevel   MA  of  GKS  supports  only  individual[0m
          [4mspecifications[0m.  

               At  run  time  GKS can be in one of five different operating
          states.  Associated with each state are the set of GKS  functions
          allowed in this state, and a set of state variables.  The operat-
          ing state concept and the state variables allow for proper speci-
          fication  of  initializations  (for example, at OPEN WORKSTATION)
          and the effect of various functions, especially with  respect  to
          the maintenance of device independence.  One special set of func-
          tions called inquiry functions is allowed in  all  states.   They
          give read-only access to the state lists.  In this way useful in-
          formation can be provided when errors occur.  Other inquiry func-
          tions  allow read-only access to the workstation descriptions, to
          allow the application program to adapt to particular  workstation
          capabilities.   Inquiry  functions  never  cause errors.  Instead
          they return information specifiying whether a valid  inquiry  was
          made.  


          1.3  OUTPUT PRIMITIVES 


               The  graphical  information  that  is  generated  by GKS and
          routed to all active workstations is built  up  of  basic  pieces
          called  output  primitives.   GKS  level  MA provides four output
          primitives:  

               1.  POLYLINE 

               2.  POLYMARKER 

               3.  TEXT 

               4.  FILL AREA 


               The  POLYLINE  primitive  draws  a  line  from  one point to
          another in ordered sets of X and Y  values.   The  type  of  line
          (solid,  dashed,  dotted, etc) can be changed as can the color of
          the line.  





                                        -1-3-





          GKS FOR RT-11 (V0.20)
          Output Primitives


               The  POLYMARKER primitive draws a marker at each point of an
          ordered set of X and Y values.  The type  of  marker  ('+',  '.',
          'o', etc) can be changed as can the color of the marker.  

               The  TEXT  primtive  draws a character string, starting at a
          point specified in world  coordinates.   The  height,  color  and
          justification of the text is controllable.  

               The  FILL  AREA  primitive  draws  a  line from one point to
          another in ordered sets of X and Y values, including a line  from
          X(N), Y(N)  to X(1), Y(1).  The resulting enclosed area is filled
          according to the current specification for fill  area  color  and
          style.  


          1.4  OUTPUT PRIMITIVE ATTRIBUTES 


               Each  output primitive potentially has three types of attri-
          bute (geometric, non-geometric and  identification).   The  first
          two  type  determine the exact appearance of the output primitive
          while the third attribute type is used in conjunction with input.
          The  values  of these attributes are set modally and are recorded
          in the GKS state list.  A separate GKS function is  provided  for
          each  primitive  attribute  to  allow  the application program to
          specify the value of an attribute without unnecessarily  specify-
          ing the values of other attributes.  During creation of an output
          primitive (that is, when one of the GKS  output  primitive  func-
          tions  is invoked) these values are associated with the primitive
          and cannot be changed afterwards.  

               Geometric  attributes  control  the  geometric  aspects of a
          primitive;  these are aspects which affect the shape or size of a
          primitive  (for  example, CHARACTER HEIGHT for TEXT).  Attributes
          of this type are workstation independent and, where  appropriate,
          are expressed in world coordinates (for example, CHARACTER HEIGHT
          is expressed in world coordinates but TEXT PATH takes  one  of  a
          set  of enumerated values).  They are defined separately for each
          primitive and a primitive may have zero, one  or  many  geometric
          attributes.  

               Current values of (workstation independent) geometric attri-
          butes, which are expressed in world coordinates,  are  stored  in
          world  coordinates.   When  they are associated with a primitive,
          the values  are  subject  to  the  same  transformations  as  the
          geometric  data  contained  in  the  definition of the primitive.
          Hence, current values are unaffected by changes in the normaliza-
          tion transformation and the workstation transformation.  

               Non-geometric  attributes do not affect the shape or size of
          a primitive but merely affect its appearance (for example,  line-
          type  for POLYLINE, or color index for all primitives except CELL
          ARRAY).  




                                        -1-4-





                                                      GKS FOR RT-11 (V0.20)
                                                Output Primitive Attributes


               There is a separate attribute for each non-geometric aspect.
          As with the attributes controlling the geometric  aspects,  these
          attributes are workstation independent.  


          1.5  WORKSTATIONS 


               GKS  is  based on the concept of abstract graphical worksta-
          tions.  Workstations provide the logical interface through  which
          the  application  program  controls  physical devices.  For every
          type of workstation present in a GKS implementation  (except  for
          the special workstations), there exists a workstation description
          table which describes the capabilities and characteristics of the
          workstation.   The application can inquire which capabilities are
          available and adapt its behavior accordingly.  

               Each  workstation  has  a type.  GKS defines six workstation
          categories.  They are:  

               1.  Output 

               2.  Input 

               3.  Output and Input 

               4.  Workstation Independent Segment Storage 

               5.  GKS Metafile output 

               6.  GKS Metafile input 

          A workstation of category OUTPUT has only output capabilities and
          is the only workstation type supported by GKS Level MA.  

               The application program references a workstation by means of
          a workstation identifier.  Connection to a particular workstation
          is established by the function OPEN WORKSTATION, which associates
          the workstation identifier with a workstation type and a  connec-
          tion  identifier.   The current state of each open workstation is
          kept in a workstation state list.  Output primitives are sent  to
          all  active  workstations  and no others;  an open workstation is
          made active by the function ACTIVATE WORKSTATION.  

               An  active  workstation  is  made  inactive  by the function
          DEACTIVATE WORKSTATION;  an open workstation  is  closed  by  the
          function CLOSE WORKSTATION.  

               The  following sequence of functions illustrates workstation
          selection:  
                  
                  OPEN WORKSTATION (1)
                  OPEN WORKSTATION (2)
                  ACTIVATE WORKSTATION (1)
                  


                                        -1-5-





          GKS FOR RT-11 (V0.20)
          Workstations


                      Output functions          {generated only on 1}
                  
                  ACTIVATE WORKSTATION (2)
                  
                      Output functions          {generated on 1,2}
                  
                  DEACTIVATE WORKSTATION (1)
                  
                      Output functions          {generated only on 2}
                  
                  CLOSE WORKSTATION (1)
                  DEACTIVATE WORKSTATION (2)
                  CLOSE WORKSTATION (2)
                  


          1.6  COORDINATE SYSTEMS AND TRANSFORMATIONS 



          1.6.1  Normalization transformations 


               In GKS, the application programmer can compose his graphical
          picture from separate parts each of which, conceptually,  is  de-
          fined  with  its  own world coordinate system (WC).  The relative
          positioning of the separate parts is defined by having  a  single
          normalized  device  coordinate space (NDC) onto which all the de-
          fined world coordinate systems are mapped.  A set  of  normaliza-
          tion   transformations   defines  the  mappings  from  the  world
          coordinate systems onto the single normalized  device  coordinate
          space,  which  can  be  regarded  as  a  workstation  independent
          abstract viewing surface.  

               For output, a single normalization transformation is current
          at any one time and this is used to transform  world  coordinates
          specified,  for example in output primitives and geometric attri-
          butes, into normalized device coordinates.  

               A  normalization transformation is specified by defining the
          limits of an area in the world coordinate system  (window)  which
          is  to  be  mapped onto a specified area of the normalized device
          coordinate space (viewport).  Window and viewport limits  specify
          rectangles  parallel  to  the coordinate axes in WC and NDC.  The
          rectangles include their boundaries.  The normalization transfor-
          mation performs a mapping from WC onto NDC that includes transla-
          tion and differential scaling with positive scale factors for the
          two axes.  

               Although  NDC  space  conceptually  extends to infinity, the
          part of NDC space in which the viewport needs to be  located  and
          that  can  be  viewed  at  a  workstation  is  the  closed  range
          [0,1]x[0,1].  




                                        -1-6-





                                                      GKS FOR RT-11 (V0.20)
                                     COORDINATE SYSTEMS AND TRANSFORMATIONS


               Each   normalization   transformation  is  identified  by  a
          transformation number which is an integer between 0  and  an  im-
          plementation dependent value n which can be inquired from the GKS
          state list.  The normalization transformation with transformation
          number  0  is  the unity transformation which maps [0,1]x[0,1] in
          world coordinates to [0,1]x[0,1]  in  normalized  device  coordi-
          nates.  It cannot be changed.  

               Initially, all other normalization tranformations are set to
          a default transformation which  is  the  same  as  transformation
          number 0.  Different transformations can be specified at any time
          when GKS is open.  Since GKS provides a number of different  nor-
          malization  transformations,  it  is possible for the application
          program to specify them prior to outputting  the  graphical  pic-
          ture.   The separate parts of the picture are output by selecting
          a particular normalization transformation before  outputting  the
          associated  graphical primitives.  However, specifying a normali-
          zation transformation,  while  the  graphical  output  is  taking
          place, is allowed.  

               A  normalization  transformation  may  be selected by SELECT
          NORMALIZATION TRANSFORMATION, and it will be used for all  output
          until another is selected.  By default, normalization transforma-
          tion 0 is selected.  


          1.6.2  Clipping 


               The viewport of a particular normalization transformation is
          used to define a clipping rectangle, as well as, with the window,
          specifying  the  normalization transformation.  When the viewport
          of the current normalization transformation is set or when a nor-
          malization  transformation  is selected, the 'clipping rectangle'
          entry in the GKS state list is set to the resulting  viewport  of
          the current normalization transformation.  Clipping to this clip-
          ping rectangle can either be enabled or  disabled.   There  is  a
          single  global  switch  (the  clipping  indicator)  which defines
          whether or not the clipping rectangle is to be used for clipping. 


          1.6.3  Workstation transformations 


               Each  open workstation can select independently some part of
          the NDC space in the range [0,1]x[0,1] to be displayed  somewhere
          on  the  workstation  display  surface.  A particular workstation
          transformation is a mapping from NDC space onto the device  coor-
          dinates (DC) for that workstation.  

               The units of device coordinates are meters on a device capa-
          ble of producing a  precisely  scaled  image  (for  example  most
          plotters)  and  appropriate workstation dependent units otherwise
          (for example, on a display unit with unknown monitor  size).   In



                                        -1-7-





          GKS FOR RT-11 (V0.20)
          COORDINATE SYSTEMS AND TRANSFORMATIONS


          either  case  the  device coordinate system maps onto the display
          surface in the following way:  

               1.  the  DC  origin is at the bottom left corner of the dis-
                   play space;  

               2.  the  device  coordinate units are related to the display
                   space in such a way that a square in device  coordinates
                   appears  as  a  square  on  the display surface (this is
                   trivially  true  if  the  device  coordinate  units  are
                   meters);  

               3.  x and y increase to the right and upwards respectively. 

          On some devices, device coordinate units do not coincide with ad-
          dressable units, for example if the addressable units do not  sa-
          tisfy the above conditions.  

               The  size of the display space in device coordinate units is
          recorded in the workstation description table.  





































                                        -1-8-

















                                      CHAPTER 2

                               FUNCTIONAL DESCRIPTIONS














































                                        -2-1-





          FUNCTIONAL DESCRIPTIONS
          ACTIVATE WORKSTATION


          2.1  ACTIVATE WORKSTATION 



          2.1.1  FORTRAN calling sequence 

          
                CALL GACWK (WKID)
                        
                Input parameters:
                INTEGER WKID            workstation identifier
                        













































                                        -2-2-





                                                    FUNCTIONAL DESCRIPTIONS
                                                                  CLOSE GKS


          2.2  CLOSE GKS 



          2.2.1  FORTRAN calling sequence 

          
                CALL GCLKS
                        


          2.2.2  Description 

          GKS is set into the operating state GKCL = 'GKS closed'.  The GKS
          description table, GKS state list and the workstation description
          tables  become unavailable.  All GKS buffers are released and all
          GKS files are closed.  


                                        NOTE

               GKS can be reopened by invoking the function OPEN GKS. 




          2.2.3  Errors 

                2 GKS not in proper state:  GKS shall be in the state GKOP. 




























                                        -2-3-





          FUNCTIONAL DESCRIPTIONS
          CLEAR WORKSTATION


          2.3  CLEAR WORKSTATION 



          2.3.1  FORTRAN calling sequence 

          
                CALL GCLRWK (WKID, COFL)
                        
                Input parameters:
                INTEGER WKID            workstation identifier
                INTEGER COFL            control flag (GCONDI, GALWAY)
                        


          2.3.2  Description 

          All of the following actions are executed in the given sequence: 

               1.  All  deferred  actions for the specified workstation are
                   executed (without intermediate clearing of  the  display
                   surface).  

               2.  The  surface  is  set  to a clear state according to the
                   control flag as follows:  

                       CONDITIONALLY:  
                         the   display  surface  is  cleared  only  if  the
                         'display surface empty' entry in  the  workstation
                         state list is NOTEMPTY.  
                       ALWAYS:  
                         the display surface is cleared 

               3.  If  the  'workstation transformation update state' entry
                   in the workstation state list is PENDING,  the  'current
                   workstation  window'  and 'current workstation viewport'
                   entries in the workstation state list are  assigned  the
                   values   of   the  'requested  workstation  window'  and
                   'requested   workstation   viewport'    entries;     the
                   'workstation  transformation  update state' entry is set
                   to NOTPENDING.  

               4.  The  'new frame action necessary at update' entry in the
                   workstation state list is set to NO.  

               5.  The  'display  surface  empty'  entry in the workstation
                   state list is set to EMPTY.  










                                        -2-4-





                                                    FUNCTIONAL DESCRIPTIONS
                                                          CLEAR WORKSTATION


          2.3.3  Errors 

                6 GKS  not  in  proper  state:   GKS shall be either in the
                  state WSOP or in the state WSAC 
               20 Specified workstation identifier is invalid 
               25 Specified workstation is not open 
               33 Specified workstation is of category MI 
               35 Specified workstation is of category INPUT 

















































                                        -2-5-





          FUNCTIONAL DESCRIPTIONS
          CLOSE WORKSTATION


          2.4  CLOSE WORKSTATION 



          2.4.1  FORTRAN calling sequence 

          
                CALL GCLWK (WKID)
                        
                Input parameters:
                INTEGER WKID            workstation identifier
                        


          2.4.2  Description 

          An  implicit  UPDATE  WORKSTATION  is performed for the specified
          workstation.  The workstation state  list  is  deallocated.   The
          workstation  identifier  is deleted from the set of open worksta-
          tions in the GKS state list.  

               The  connection  to the workstation is released.  GKS is set
          into operating state GKOP if no workstations  remain  open.   The
          display surface need not be cleared when CLOSE WORKSTATION is in-
          voked, but it may be cleared.  


          2.4.3  Errors 

                7 GKS  not  in  proper  state:   GKS shall be in one of the
                  states WSOP, WSAC, or SGOP.  
               20 Specified workstation identifier is invalid 
               25 Specified workstation is not open 
               29 Specified workstation is active 
              147 Input queue has overflowed 






















                                        -2-6-





                                                    FUNCTIONAL DESCRIPTIONS
                                                     DEACTIVATE WORKSTATION


          2.5  DEACTIVATE WORKSTATION 



          2.5.1  FORTRAN calling sequence 

          
                CALL GDAWK (WKID)
                        
                Input parameters:
                INTEGER WKID            workstation identifier
                        


          2.5.2  Description 

          The  specified  workstation is marked inactive in the workstation
          state list.  The workstation identifier is deleted from  the  set
          of  active  workstations  in the GKS state list.  GKS is set into
          the operating state WSOP = "At least one workstation open" if  no
          workstation remains active.  


                                        NOTE

               While  a  workstation  is  inactive, primitives are not
               sent to it.  




          2.5.3  Errors 

                3 GKS not in proper state;  GKS shall be in the state WSAC. 
               20 Specified workstation identifier is invalid 
               30 Specified workstation is not active 
               33 Specified workstation is of category MI 
               35 Specified workstation is of category INPUT.  



















                                        -2-7-





          FUNCTIONAL DESCRIPTIONS
          OPEN GKS


          2.6  OPEN GKS 



          2.6.1  FORTRAN calling sequence 

          
                CALL GOPKS (ERRFIL, MEMSIZ)
                        
                Input parameters:
                INTEGER ERRFIL          error file connection ID
                INTEGER MEMSIZ          dynamic memory to allocate
                        


          2.6.2  Description 

          GKS  is  set into the operating state GKOP = "GKS open".  The GKS
          state list is allocated and  initialized.   The  GKS  description
          table and the workstation description tables are made available. 

               The entry 'error file' in the GKS error state list is set to
          the value specified by the first parameter.  The permitted buffer
          area  which  can  be used by GKS for internal purposes is limited
          (this implementation does not use this parameter).  


          2.6.3  Errors 

                1 GKS not in proper state:  GKS shall be in the state GKCL 
              200 Specified error file is invalid 


























                                        -2-8-





                                                    FUNCTIONAL DESCRIPTIONS
                                                           OPEN WORKSTATION


          2.7  OPEN WORKSTATION 



          2.7.1  FORTRAN calling sequence 

          
                CALL GOPWK (WKID, CONID, WTYPE)
                        
                Input parameters:
                INTEGER WKID            workstation identifier
                INTEGER CONID           connection identifier
                INTEGER WTYPE           workstation type
                        


          2.7.2  Description 

          If  GKS is in operating state GKOP, it is set into the state WSOP
          = 'at least one workstation open'.  GKS  requests  the  operating
          system  to  establish  the specified connection for a workstation
          characterized  in  the  workstation  description  table  by   the
          'workstation  type'.  The workstation state list is allocated and
          initialized.  The workstation identifier is added to the  set  of
          open  workstations  in  the GKS state list.  OPEN WORKSTATION en-
          sures that the display surface is clear, but does not  clear  the
          surface needlessly.  

               An  attempt  to  open a workstation with the same connection
          identifier and workstation type as one already open causes  error
          26 to occur.  


          2.7.3  Errors 

                8 GKS  not  in  proper  state:   GKS shall be in one of the
                  states GKOP, WSOP, WSAC or SGOP 
               20 Specified workstation identifier is invalid 
               21 Specified connection identifier is invalid 
               22 Specified workstation type is invalid 
               23 Specified workstation type does not exist 
               24 Specified workstation is open 
               26 Specified workstation cannot be opened 
               28 Workstation Independent Segment Storage is already open 
               42 Maximum  number of simultaneously open workstations would
                  be exceeded 











                                        -2-9-





          FUNCTIONAL DESCRIPTIONS
          POLYMARKER


          2.8  POLYMARKER 



          2.8.1  FORTRAN calling sequence 

          
                CALL GPM (N, PX, PY)
                        
                Input parameters:
                INTEGER N               number of points
                REAL    PX(N), PY(N)    coordinates of points in world
                                        coordinates
                        
           
           









































                                       -2-10-





                                                    FUNCTIONAL DESCRIPTIONS
                                                   INQUIRE COLOR FACILITIES


          2.9  INQUIRE COLOR FACILITIES 



          2.9.1  FORTRAN calling sequence 

          
                CALL GQCF (WTYPE, ERRIND, NCOLI, COLA, NPCI)
                        
                Input parameters:
                INTEGER WTYPE           workstation type
                        
                Output parameters:
                INTEGER ERRIND          error indicator
                INTEGER NCOLI           number of colors
                INTEGER COLA            color available (GMONOC, GCOLOR)
                INTEGER NPCI            number of predefined color indices
                        


          2.9.2  Description 

          If  the inquired information is available, the error indicator is
          returned as 0 and the values are returned in the  output  parame-
          ters.  

               If the number of available colors or intensities is returned
          as 0, the workstation supports a continuous range  of  colors  or
          intensities.  

               If the inquired information is not available, the values re-
          turned in the output parameters are set to one of  the  following
          error numbers to indicate the reason for non-availability:  

                8 GKS  not  in  proper  state:   GKS shall be in one of the
                  states GKOP, WSOP, WSAC or SGOP.  
               22 Specified workstation type is invalid.  
               23 Specified workstation type does not exist.  
               39 Specified  workstation  is neither of category OUTPUT nor
                  of category OUTIN 


          2.9.3  Errors 

                  none 












                                       -2-11-





          FUNCTIONAL DESCRIPTIONS
          INQUIRE CURRENT CHARACTER HEIGHT


          2.10  INQUIRE CURRENT CHARACTER HEIGHT 



          2.10.1  FORTRAN calling sequence 

          
                CALL GQCHH (ERRIND, CHH)
                        
                Output parameters:
                INTEGER ERRIND          error indicator
                REAL    CHH             character height
                        


          2.10.2  Description 

          If  the inquired information is available, the error indicator is
          returned as 0 and the values are returned in the  output  parame-
          ters.  

               If the inquired information is not available, the values re-
          turned in the output parameters are set to one of  the  following
          error numbers to indicate the reason for non-availability:  

                8 GKS  not  in  proper  state:   GKS shall be in one of the
                  states GKOP, WSOP, WSAC or SGOP.  


          2.10.3  Errors 

                  none 

























                                       -2-12-





                                                    FUNCTIONAL DESCRIPTIONS
                                                INQUIRE CHARACTER UP VECTOR


          2.11  INQUIRE CHARACTER UP VECTOR 



          2.11.1  FORTRAN calling sequence 

          
                CALL GQCHUP (ERRIND, CHUX, CHUY)
                        
                Input parameters:
                INTEGER ERRIND          error indicator
                REAL    CHUX, CHUY      character up vector (WC)
                        


          2.11.2  Description 

          If  the inquired information is available, the error indicator is
          returned as 0 and the values are returned in the  output  parame-
          ters.  

               If the inquired information is not available, the values re-
          turned in the output parameters are set to one of  the  following
          error numbers to indicate the reason for non-availability:  

                8 GKS  not  in  proper  state:   GKS shall be in one of the
                  states GKOP, WSOP, WSAC or SGOP.  


          2.11.3  Errors 

                  none 

























                                       -2-13-





          FUNCTIONAL DESCRIPTIONS
          INQUIRE CLIPPING INDICATOR


          2.12  INQUIRE CLIPPING INDICATOR 



          2.12.1  FORTRAN calling sequence 

          
                CALL GQCLIP (ERRIND, CLSW, CLRECT)
                        
                Output parameters:
                INTEGER ERRIND          error indicator
                INTEGER CLSW            clipping indicator (GNCLIP, GCLIP)
                REAL    CLRECT(4)       clipping rectangle
                        


          2.12.2  Description 

          If  the inquired information is available, the error indicator is
          returned as 0 and the values are returned in the  output  parame-
          ters.  

               If the inquired information is not available, the values re-
          turned in the output parameters are set to one of  the  following
          error numbers to indicate the reason for non-availability:  

                8 GKS  not  in  proper  state:   GKS shall be in one of the
                  states GKOP, WSOP, WSAC or SGOP.  


          2.12.3  Errors 

                  none 
























                                       -2-14-





                                                    FUNCTIONAL DESCRIPTIONS
                         INQUIRE CURRENT NORMALIZATION TRANFORMATION NUMBER


          2.13  INQUIRE CURRENT NORMALIZATION TRANSFORMATION NUMBER 



          2.13.1  FORTRAN calling sequence 

          
                CALL GQCNTN (ERRIND, CTNR)
                        
                Output parameters:
                INTEGER ERRIND          error indicator
                INTEGER CTNR            current transformation number
                        


          2.13.2  Description 

          If  the inquired information is available, the error indicator is
          returned as 0 and the values are returned in the  output  parame-
          ters.  

               If the inquired information is not available, the values re-
          turned in the output parameters are set to one of  the  following
          error numbers to indicate the reason for non-availability:  

                8 GKS  not  in  proper  state:   GKS shall be in one of the
                  states GKOP, WSOP, WSAC or SGOP.  


          2.13.3  Errors 

                  none 

























                                       -2-15-





          FUNCTIONAL DESCRIPTIONS
          INQUIRE COLOR REPRESENTATION


          2.14  INQUIRE COLOR REPRESENTATION 



          2.14.1  FORTRAN calling sequence 

          
                CALL GQCR (WKID, COLI, TYPE, ERRIND, CR, CG, CB)
                        
                Input parameters:
                INTEGER WKID            workstation identifier
                INTEGER COLI            color index
                INTEGER TYPE            type of returned values (GSET,
          GREALI)
                        
                Output parameters:
                INTEGER ERRIND          error indicator
                REAL    CR, CG, CB      color (red/green/blue intensities
                        


          2.14.2  Description 

          If  the inquired information is available, the error indicator is
          returned as 0 and the values are returned in the  output  parame-
          ters.  

               If the inquired information is not available, the values re-
          turned in the output parameters are set to one of  the  following
          error numbers to indicate the reason for non-availability:  

                7 GKS  not  in  proper  state:   GKS shall be in one of the
                  states WSOP, WSAC or SGOP.  
               20 Specified workstation identifier is invalid.  
               25 Specified workstation is not open.  
               33 Specified workstation is of category MI.  
               35 Specified workstation is of category INPUT.  
               36 Specified  workstation is Workstation Independent Segment
                  Storage.  
               86 Color index is invalid.  
               87 A  representation  for  the specified color index has not
                  been defined on this workstation.  















                                       -2-16-





                                                    FUNCTIONAL DESCRIPTIONS
                                               INQUIRE COLOR REPRESENTATION


          2.14.3  Errors 

                  none 






















































                                       -2-17-





          FUNCTIONAL DESCRIPTIONS
          INQUIRE FILL AREA COLOR INDEX


          2.15  INQUIRE FILL AREA COLOR INDEX 



          2.15.1  FORTRAN calling sequence 

          
                CALL GQFACI (ERRIND, COLI)
                        
                Input parameters:
                INTEGER ERRIND          error indicator
                INTEGER COLI            fill area color index
                        


          2.15.2  Description 

          If  the inquired information is available, the error indicator is
          returned as 0 and the values are returned in the  output  parame-
          ters.  

               If the inquired information is not available, the values re-
          turned in the output parameters are set to one of  the  following
          error numbers to indicate the reason for non-availability:  

                8 GKS  not  in  proper  state:   GKS shall be in one of the
                  states GKOP, WSOP, WSAC or SGOP.  


          2.15.3  Errors 

                  none 

























                                       -2-18-





                                                    FUNCTIONAL DESCRIPTIONS
                                           INQUIRE FILL AREA INTERIOR STYLE


          2.16  INQUIRE FILL AREA INTERIOR STYLE 



          2.16.1  FORTRAN calling sequence 

          
                CALL GQFAIS (ERRIND, INTS)
                        
                Output parameters:
                INTEGER ERRIND          error indicator
                INTEGER INTS            fill area interior style
                                        (GHOLLO, GSOLID, GPATTR, GHATCH)
                        


          2.16.2  Description 

          If  the inquired information is available, the error indicator is
          returned as 0 and the values are returned in the  output  parame-
          ters.  

               If the inquired information is not available, the values re-
          turned in the output parameters are set to one of  the  following
          error numbers to indicate the reason for non-availability:  

                8 GKS  not  in  proper  state:   GKS shall be in one of the
                  states GKOP, WSOP, WSAC or SGOP.  


          2.16.3  Errors 

                  none 
























                                       -2-19-





          FUNCTIONAL DESCRIPTIONS
          INQUIRE LINETYPE


          2.17  INQUIRE LINETYPE 



          2.17.1  FORTRAN calling sequence 

          
                CALL GQLN (ERRIND, LTYPE)
                        
                Input parameters:
                INTEGER ERRIND          error indicator
                INTEGER LTYPE           linetype
                        


          2.17.2  Description 

          If  the inquired information is available, the error indicator is
          returned as 0 and the values are returned in the  output  parame-
          ters.  

               If the inquired information is not available, the values re-
          turned in the output parameters are set to one of  the  following
          error numbers to indicate the reason for non-availability:  

                8 GKS  not  in  proper  state:   GKS shall be in one of the
                  states GKOP, WSOP, WSAC or SGOP.  


          2.17.3  Errors 

                  none 

























                                       -2-20-





                                                    FUNCTIONAL DESCRIPTIONS
                                                       INQUIRE LEVEL OF GKS


          2.18  INQUIRE LEVEL OF GKS 



          2.18.1  FORTRAN calling sequence 

          
                CALL GQLVKS (ERRIND, LEVEL)
                        
                Output parameters:
                INTEGER ERRIND          error indicator
                INTEGER LEVEL           level of GKS   (LMA, LMB, LMC, 
                                                        L0A, L0B, L0C, 
                                                        L1A, L1B, L1C, 
                                                        L2A, L2B, L2C)
                        









































                                       -2-21-





          FUNCTIONAL DESCRIPTIONS
          INQUIRE POLYMARKER INDEX


          2.19  INQUIRE POLYMARKER INDEX 



          2.19.1  FORTRAN calling sequence 

          
                CALL GQMK (ERRIND, MTYPE)
                        
                Output parameters:
                INTEGER ERRIND          error indicator
                INTEGER MTYPE           marker type
                        


          2.19.2  Description 

          If  the inquired information is available, the error indicator is
          returned as 0 and the values are returned in the  output  parame-
          ters.  

               If the inquired information is not available, the values re-
          turned in the output parameters are set to one of  the  following
          error numbers to indicate the reason for non-availability:  

                8 GKS  not  in  proper  state:   GKS shall be in one of the
                  states GKOP, WSOP, WSAC or SGOP.  


          2.19.3  Errors 

                  none 

























                                       -2-22-





                                                    FUNCTIONAL DESCRIPTIONS
                                       INQUIRE NORMALIZATION TRANSFORMATION


          2.20  INQUIRE NORMALIZATION TRANSFORMATION 



          2.20.1  FORTRAN calling sequence 

          
                CALL GQNT (NTNR, ERRIND, WINDOW, VIEWPT)
                        
                Input parameters:
                INTEGER NTNR            normalization transformation number
                        
                Output parameters:
                INTEGER ERRIND          error indicator
                REAL    WINDOW(4)       window limits in world coordinates
                                        WXMIN, WXMAX, WYMIN, WYMAX
                REAL    VIEWPT(4)       viewport limits in normalized 
                                        device coordinates
                                        VXMIN, VXMAX, VYMIN, VYMAX
                        


          2.20.2  Description 

          If  the inquired information is available, the error indicator is
          returned as 0 and the values are returned in the  output  parame-
          ters.  

               If the inquired information is not available, the values re-
          turned in the output parameters are set to one of  the  following
          error numbers to indicate the reason for non-availability:  

                8 GKS  not  in  proper  state:   GKS shall be in one of the
                  states GKOP, WSOP, WSAC or SGOP.  
               50 Transformation number is invalid 


          2.20.3  Errors 

                  none 

















                                       -2-23-





          FUNCTIONAL DESCRIPTIONS
          INQUIRE POLYLINE COLOR INDEX


          2.21  INQUIRE POLYLINE COLOR INDEX 



          2.21.1  FORTRAN calling sequence 

          
                CALL GQPLCI (ERRIND, COLI)
                        
                Output parameters:
                INTEGER ERRIND          error indicator
                INTEGER COLI            polyline color index
                        


          2.21.2  Description 

          If  the inquired information is available, the error indicator is
          returned as 0 and the values are returned in the  output  parame-
          ters.  

               If the inquired information is not available, the values re-
          turned in the output parameters are set to one of  the  following
          error numbers to indicate the reason for non-availability:  

                8 GKS  not  in  proper  state:   GKS shall be in one of the
                  states GKOP, WSOP, WSAC or SGOP.  


          2.21.3  Errors 

                  none 

























                                       -2-24-





                                                    FUNCTIONAL DESCRIPTIONS
                                             INQUIRE POLYMARKER COLOR INDEX


          2.22  INQUIRE POLYMARKER COLOR INDEX 



          2.22.1  FORTRAN calling sequence 

          
                CALL GQPMCI (ERRIND, COLI)
                        
                Output parameters:
                INTEGER ERRIND          error indicator
                INTEGER COLI            polymarker color index
                        


          2.22.2  Description 

          If  the inquired information is available, the error indicator is
          returned as 0 and the values are returned in the  output  parame-
          ters.  

               If the inquired information is not available, the values re-
          turned in the output parameters are set to one of  the  following
          error numbers to indicate the reason for non-availability:  

                8 GKS  not  in  proper  state:   GKS shall be in one of the
                  states GKOP, WSOP, WSAC or SGOP.  


          2.22.3  Errors 

                  none 

























                                       -2-25-





          FUNCTIONAL DESCRIPTIONS
          INQUIRE TEXT ALIGNMENT


          2.23  INQUIRE TEXT ALIGNMENT 



          2.23.1  FORTRAN calling sequence 

          
                CALL GQTXAL (ERRIND, TXALH, TXALV)
                        
                Output parameters:
                INTEGER ERRIND          error indicator
                INTEGER TXALH           text alignment horizontal
                                        (GAHNOR, GALEFT, GACENT, GARITE)
                INTEGER TXALV           text alignment vertical
                                        (GAVNOR, GATOP, GACAP, GAHALF,
          GABASE,
                                        GABOTT)
                        


          2.23.2  Description 

          If  the inquired information is available, the error indicator is
          returned as 0 and the values are returned in the  output  parame-
          ters.  

               If the inquired information is not available, the values re-
          turned in the output parameters are set to one of  the  following
          error numbers to indicate the reason for non-availability:  

                8 GKS  not  in  proper  state:   GKS shall be in one of the
                  states GKOP, WSOP, WSAC or SGOP.  


          2.23.3  Errors 

                  none 




















                                       -2-26-





                                                    FUNCTIONAL DESCRIPTIONS
                                    INQUIRE WORKSTATION CONNECTION AND TYPE


          2.24  INQUIRE WORKSTATION CONNECTION AND TYPE 



          2.24.1  FORTRAN calling sequence 

          
                CALL GQWKC (WKID, ERRIND, CONID, WTYPE)
                        
                Input parameters:
                INTEGER WKID            workstation identifier
                        
                Output parameters:
                INTEGER ERRIND          error indicator
                INTEGER CONID           connection identifier
                INTEGER WTYPE           workstation type
                        


          2.24.2  Description 

          If  the inquired information is available, the error indicator is
          returned as 0 and the values are returned in the  output  parame-
          ters.  

               If the inquired information is not available, the values re-
          turned in the output parameters are set to one of  the  following
          error numbers to indicate the reason for non-availability:  

                7 GKS  not  in  proper  state:   GKS shall be in one of the
                  states WSOP, WSAC or SGOP.  
               20 Specified workstation identifier is invalid 
               25 Specified workstation is not open 


          2.24.3  Errors 

                  none 



















                                       -2-27-





          FUNCTIONAL DESCRIPTIONS
          INQUIRE WORKSTATION TRANSFORMATION


          2.25  INQUIRE WORKSTATION TRANSFORMATION 



          2.25.1  FORTRAN calling sequence 

          
                CALL GQWKT (WKID, ERRIND, TUS, RWINDO, CWINDO, RVIEWP,
                                  CVIEWP)
                        
                Input parameters:
                INTEGER WKID            workstation identifier
                        
                Output parameters:
                INTEGER ERRIND          error indicator
                INTEGER TUS             workstation transformation update
          state
                                        (GNPEND, GPEND)
                REAL    RWINDO(4)       requested workstation window in NDC
                                        RWXMIN, RWXMAX, RWYMIN, RWYMAX
                REAL    CWINDO(4)       current workstation window in NDC
                                        CWXMIN, CWXMAX, CWYMIN, CWYMAX
                REAL    RVIEWP(4)       requested workstation viewport in
          DC
                                        RVXMIN, RVXMAX, RVYMIN, RVYMAX
                REAL    CVIEWP(4)       current workstation viewport in DC
                                        CVXMIN, CVXMAX, CVYMIN, CVYMAX
                        


          2.25.2  Description 

          If  the inquired information is available, the error indicator is
          returned as 0 and the values are returned in the  output  parame-
          ters.  

               The  workstation transformation update state is PENDING if a
          workstation transformation change has been requested but not  yet
          provided.  

               If the inquired information is not available, the values re-
          turned in the output parameters are set to one of  the  following
          error numbers to indicate the reason for non-availability:  

                7 GKS  not  in  proper  state:   GKS shall be in one of the
                  states WSOP, WSAC or SGOP.  
               20 Specified workstation identifier is invalid 
               25 Specified workstation is not open 
               33 Specified workstation is of category MI 
               36 Specified  workstation is Workstation Independent Segment
                  Storage 
               50 Transformation number is invalid 





                                       -2-28-





                                                    FUNCTIONAL DESCRIPTIONS
                                         INQUIRE WORKSTATION TRANSFORMATION


          2.25.3  Errors 

                  none 






















































                                       -2-29-





          FUNCTIONAL DESCRIPTIONS
          SET CHARACTER HEIGHT


          2.26  SET CHARACTER HEIGHT 



          2.26.1  FORTRAN calling sequence 

          
                CALL GSCHH (CHH)
                        
                Input parameters:
                INTEGER CHH             character height
                        













































                                       -2-30-





                                                    FUNCTIONAL DESCRIPTIONS
                                                    SET CHARACTER UP VECTOR


          2.27  SET CHARACTER UP VECTOR 



          2.27.1  FORTRAN calling sequence 

          
                CALL GSCHUP (CHUX, CHUY)
                        
                Input parameters:
                REAL CHUX, CHUY         character up vector (WC)
                        
           
           











































                                       -2-31-





          FUNCTIONAL DESCRIPTIONS
          SET CLIPPING INDICATOR


          2.28  SET CLIPPING INDICATOR 



          2.28.1  FORTRAN calling sequence 

          
                CALL GSCLIP (CLSW)
                        
                Input parameters:
                INTEGER CLSW            clipping indicator (GNCLIP, GCLIP)
                        
           
           











































                                       -2-32-





                                                    FUNCTIONAL DESCRIPTIONS
                                        SELECT NORMALIZATION TRANSFORMATION


          2.29  SELECT NORMALIZATION TRANSFORMATION 



          2.29.1  FORTRAN calling sequence 

          
                CALL GSELNT (TNR)
                        
                Input parameters:
                INTEGER TNR             transformation number
                        
           
           











































                                       -2-33-





          FUNCTIONAL DESCRIPTIONS
          SET FILL AREA COLOR INDEX


          2.30  SET FILL AREA COLOR INDEX 



          2.30.1  FORTRAN calling sequence 

          
                CALL GSFACI (COLI)
                        
                Input parameters:
                INTEGER COLI            fill area color index
                        


          2.30.2  Description 

          The  'current  fill area color index' entry in the GKS state list
          is set to the value specified by the parameter.   This  value  is
          used for the display of subsequent FILL AREA output primitives.  

               The  color  index  is a pointer into the color tables of the
          workstations.  If the specified color index is not present  in  a
          workstation  color  table, a workstation dependent color index is
          used on that workstation.  


          2.30.3  Errors 

                8 GKS  not  in  proper  state;   GKS shall be in one of the
                  states GKOP, WSOP, WSAC or SGOP.  
               85 Color index is less than zero.  


























                                       -2-34-





                                                    FUNCTIONAL DESCRIPTIONS
                                               SET FILL AREA INTERIOR STYLE


          2.31  SET FILL AREA INTERIOR STYLE 



          2.31.1  FORTRAN calling sequence 

          
                CALL GSFAIS (INTS)
                        
                Input parameters:
                INTEGER INTS            fill area interior style
                                        (GHOLLO, GSOLID, GPATTR, GHATCH)
                        


          2.31.2  Description 

          The  'current  fill  area  interior style' entry in the GKS state
          list is set to the value specified by the parameter.  This  value
          is  used  for  the  display of subsequent FILL AREA output primi-
          tives.  

               The  fill  area  interior style is used to determine in what
          style the area is filled and the possible  values  are:   HOLLOW,
          SOLID, PATTERN and HATCH (see 4.4.6).  

               If  the  requested  interior  style  is  not  available on a
          workstation, HOLLOW is used on that workstation 


          2.31.3  Errors 

                8 GKS  not  in  proper  state;   GKS shall be in one of the
                  states GKOP, WSOP, WSAC or SGOP.  























                                       -2-35-





          FUNCTIONAL DESCRIPTIONS
          SET LINETYPE


          2.32  SET LINE TYPE 



          2.32.1  FORTRAN calling sequence 

          
                CALL GSLN (LTYPE)
                        
                Input parameters:
                INTEGER LTYPE           linetype
                        


          2.32.2  Description 

          The  'current linetype' entry in the GKS state list is set to the
          value specified by the parameter.  This value  is  used  for  the
          display of subsequent POLYLINE output primitives.  

               Linetype values produce linetypes as indicated:  
               1. solid line 
               2. dashed line 
               3. dotted line 
               4. dashed-dotted line 
            5-20. reserved for future standardization 
            >=21. not used 

          If  the  specified  linetype is not available on a workstation,
          linetype 1 is used on that workstation.  


          2.32.3  Errors 

                8 GKS  not  in  proper  state;   GKS shall be in one of the
                  states GKOP, WSOP, WSAC or SGOP 
               63 is equal to zero 




















                                       -2-36-





                                                    FUNCTIONAL DESCRIPTIONS
                                                             SET MARKERTYPE


          2.33  SET MARKERTYPE 



          2.33.1  FORTRAN calling sequence 

          
                CALL GSMK (MTYPE)
                        
                Input parameters:
                INTEGER MTYPE           marker type
                        
           
           











































                                       -2-37-





          FUNCTIONAL DESCRIPTIONS
          SET POLYLINE COLOR INDEX


          2.34  SET POLYLINE COLOR INDEX 



          2.34.1  FORTRAN calling sequence 

          
                CALL GSPLCI (COLI)
                        
                Input parameters:
                INTEGER COLI            polyline color index
                        


          2.34.2  Description 

          The 'current polyline color index' entry in the GKS state list is
          set to the value specified by the parameter.  This value is  used
          for the display of subsequent POLYLINE output primitives.  

               The  color  index  is a pointer into the color tables of the
          workstations.  If the specified color index is not present  in  a
          workstation  color  table, a workstation dependent color index is
          used on that workstation.  


          2.34.3  Errors 

                8 GKS  not  in  proper  state;   GKS shall be in one of the
                  states GKOP, WSOP, WSAC or SGOP.  
               85 Color index is less than zero.  


























                                       -2-38-





                                                    FUNCTIONAL DESCRIPTIONS
                                                         SET TEXT ALIGNMENT


          2.35  SET TEXT ALIGNMENT 



          2.35.1  FORTRAN calling sequence 

          
                CALL GSTXAL (TXALH, TXALV)
                        
                Input parameters:
                INTEGER TXALH           text alignment horizontal
                                        (GAHNOR, GALEFT, GACENT, GARITE)
                INTEGER TXALV           text alignment vertical
                                        (GAVNOR, GATOP, GACAP, GAHALF, 
                                        GABASE, GABOTT)
                        


          2.35.2  Description 

          The  'current  text alignment' entry in the GKS state list is set
          to the value specified by the parameter.  This value is used when
          creating  subsequent  TEXT output primitives.  Text alignment has
          two components:  horizontal and vertical.  


          2.35.3  Errors 

                8 GKS  not  in  proper  state:   GKS shall be in one of the
                  states GKOP, WSOP, WSAC, or SGOP.  



























                                       -2-39-





          FUNCTIONAL DESCRIPTIONS
          SET TEXT COLOR INDEX


          2.36  SET TEXT COLOR INDEX 



          2.36.1  FORTRAN calling sequence 

          
                CALL GSTXCI (COLI)
                        
                Input parameters:
                INTEGER COLI            text color index
                        
           
           











































                                       -2-40-





                                                    FUNCTIONAL DESCRIPTIONS
                                                               SET VIEWPORT


          2.37  SET VIEWPORT 



          2.37.1  FORTRAN calling sequence 

          
                CALL GSVP (TNR, XMIN, XMAX, YMIN, YMAX)
                        
                Input parameters:
                INTEGER TNR             transformation number
                REAL    XMIN, XMAX      viewport limits in normalized
          device
                        YMIN, YMAX      coordinates
                        
           
           








































                                       -2-41-





          FUNCTIONAL DESCRIPTIONS
          SET WORKSTATION VIEWPORT


          2.38  SET WORKSTATION VIEWPORT 



          2.38.1  FORTRAN calling sequence 

          
                CALL GSWKVP (WKID, XMIN, XMAX, YMIN, YMAX)
                        
                Input parameters:
                INTEGER WKID            workstation identifier
                REAL    XMIN, XMAX      workstation viewport limits in
          device
                        YMIN, YMAX      coordinates
                        
           
           








































                                       -2-42-





                                                    FUNCTIONAL DESCRIPTIONS
                                                     SET WORKSTATION WINDOW


          2.39  SET WORKSTATION WINDOW 



          2.39.1  FORTRAN calling sequence 

          
                CALL GSWKWN (WKID, XMIN, XMAX, YMIN, YMAX)
                        
                Input parameters:
                INTEGER WKID            workstation identifier
                REAL    XMIN, XMAX      workstation window limits in nor-
          malized
                        YMIN, YMAX      device coordinates
                        
           
           








































                                       -2-43-





          FUNCTIONAL DESCRIPTIONS
          SET WINDOW


          2.40  SET WINDOW 



          2.40.1  FORTRAN calling sequence 

          
                CALL GSWN (TNR, XMIN, XMAX, YMIN, YMAX)
                        
                Input parameters:
                INTEGER TNR             transformation number
                REAL    XMIN, XMAX,     window limits in world coordinates
                        YMIN, YMAX
                        
           
           









































                                       -2-44-





                                                    FUNCTIONAL DESCRIPTIONS
                                                                       TEXT


          2.41  TEXT 



          2.41.1  FORTRAN calling sequence 

          
                CALL GTX (PX, PY, CHARS)
                        
                Input parameters:
                INTEGER PX, PY          text position in world coordinates
                CHARACTER*(*) CHARS     string of characters
                        


          2.41.2  Description 

          A  character string is generated.  The current values of the text
          attributes, as given by the GKS state  list,  are  bound  to  the
          primitive.  

               The text position is given in WC and transformed by the cur-
          rent normalization transformation.  

               If,  after  the  workstation  transformation,  the height or
          width of a character is zero, no error is generated  and  whether
          anything is drawn is workstation dependent.  

               If  the  character  string contains a control character (for
          example characters outside the range 2/0 to 7/14 inclusive in ISO
          646),  the  effect  is  workstation dependent.Either error 101 is
          generated or some visual effect may be generated or the character
          may  be  ignored.  Even if error 101 occurs, the character string
          is displayed on all active workstations which do not generate er-
          ror 101.  


                                        NOTE

               Text  is clipped in a way that depends on the text pre-
               cision as defined by the text font and  precision  cur-
               rently selected.  















                                       -2-45-





          FUNCTIONAL DESCRIPTIONS
          TEXT


          2.41.3  Errors 

                5 GKS  not  in  proper  state:   GKS shall be either in the
                  state WSAC or SGOP.  
              101 Invalid code in string.  




















































                                       -2-46-





                                                    FUNCTIONAL DESCRIPTIONS
                                                         UPDATE WORKSTATION


          2.42  UPDATE WORKSTATION 



          2.42.1  FORTRAN calling sequence 

          
                CALL GUWK (WKID, REGFL)
                        
                Input parameters:
                INTEGER WKID            workstation identifier
                INTEGER REGFL           update regeneration flag (GPOSTP,
                                        GPERFO)
                        
           Functional Description


          2.42.2  Description 

          All  deferred  actions for the specified workstation are executed
          (without intermediate clearing of the display surface).   If  the
          regeneration  flag  is  set  to PERFORM and the 'new frame action
          necessary at update' entry in the workstation state list is  YES,
          then the following actions are executed in the given sequence:  

               1.  The display surface is cleared only if the 'display sur-
                   face empty' entry  in  the  workstation  state  list  is
                   NOTEMPTY.  The entry is set to EMPTY.  

               2.  If  the  'workstation transformation update state' entry
                   in the workstation state list is PENDING,  the  'current
                   workstation  window'  and 'current workstation viewport'
                   entries in the workstation state list are  assigned  the
                   values   of   the  'requested  workstation  window'  and
                   'requested   workstation    viewport    entries;     the
                   'workstation  transformation  update state' entry is set
                   to NOTPENDING.  

               3.  The  'new frame action necessary at update' entry in the
                   workstation state list is set to NO.  



                                        NOTE

               If the regeneration flag is PERFORM, UPDATE WORKSTATION
               suspends the effect of SET  DEFERRAL  STATE.   In  that
               case,  it  is  equivalent  to the following sequence of
               functions:  



                  INQUIRE WORKSTATION STATE;  
                  save deferral state;  
                  SET DEFERRAL STATE (ASAP, ALLOWED);  


                                       -2-47-





          FUNCTIONAL DESCRIPTIONS
          UPDATE WORKSTATION


                  set deferral state to saved value;  

               If  the  value of the 'new frame action necessary at update'
          entry is NO or the regeneration flag is SUPPRESS, UPDATE WORKSTA-
          TION  merely  initiates the transmission of blocked data.  If the
          value of the entry 'new frame action necessary at update' is  YES
          and  the regeneration flag is PERFORM, UPDATE WORKSTATION behaves
          as REDRAW ALL SEGMENTS ON WORKSTATION (not supported in this  im-
          plementation).  

               The  'new  frame  action  necessary  at update' entry in the
          workstation state list is  set  to  YES  during  deferred  action
          generation if both of the following are true (see 4.5):  

               1.  an  action  causing  modification  of the picture is ac-
                   tually deferred on that workstation;  

               2.  the workstation display surface does not allow modifica-
                   tion of the image without redrawing  the  whole  picture
                   (for example, plotter, storage tube display).  



          2.42.3  Errors 

                7 GKS  not  in  proper  state:   GKS shall be either in the
                  state WSOP, WSAC or SGOP 
               20 Specified workstation identifier is invalid 
               25 Specified workstation is not open 
               33 Specified workstation is of category MI 
               35 Specified workstation is of category INPUT 
               36 Specified  workstation is Workstation Independent Segment
                  Storage 
























                                       -2-48-

















                                      CHAPTER 3

                                USING GKS WITH RT-11





          3.1  INCORPORATING GKS INTO FORTRAN SOURCE PROGRAMS 


               GKS  subroutines  are  accessed by FORTRAN subroutine calls.
          The calling sequence for each of the subroutines is shown in  the
          chapter  on Functional Descriptions.  There is a general sequence
          in which GKS subroutine calls are made.  The sequence is:  

                  CALL GOPKS (...)           !  Open GKS 
                     CALL GOPWK (...)        !  Open a workstation 
                        CALL GACWK (...)     !  Activate the workstation 
                         .  
                         .                   !  Primitive and attribute 
                         .                   !  subroutine calls 
                         .  
                        CALL GDAWK (...)     !  Deactivate the workstation 
                     CALL GCLWK (...)        !  Close the work station 
                  CALL GCLKS (...)           !  Close GKS 

          This  same  general  pattern is repeated in all programs that use
          GKS.  Workstations may be activated and deactivated at any  time,
          and more than one work station may be opened at one time.  

               Many  GKS functions make reference to enumerated data types.
          For example, four line types are mandated for GKS, that  is  they
          must be supported in all implementations.  The four linetypes are
          solid, dashed, dotted and dash-dot.  The FORTRAN calling  conven-
          tion  specifies an integer value for each of these line types (1,
          2, 3 and 4 respectively).  

               Definitions  of all the GKS enumerated types can be found in
          the file GKENUM.FIN (listed in Appendix A).   This  file  can  be
          'INCLUDE'ed  in  FORTRAN 77  programs,  making  it unnecessary to
          remember the correspondence between GKS scalars and their integer
          representations.   For  FORTRAN 66 programs, the PARAMETER state-
          ments would have to be replaced with equivalent  DATA  statements
          and the appropriate definitions would need to be edited into each
          file that calls GKS subroutines.  



                                        -3-1-





          USING GKS WITH RT-11
          


               Some  GKS  subroutines  reference FORTRAN logical units.  In
          particular, GOPKS (Open GKS) references a logical unit to be used
          for error reporting.  GOPWK (Open Workstation) references a logi-
          cal unit to be  used  for  graphical  output  to  the  associated
          workstation.   The  FORTRAN logical unit number supplied to these
          subroutines may be either OPEN for writing or CLOSED prior to the
          subroutine  call.   GKS checks to see if the unit is open.  If it
          isn't, GKS will open the unit.  


                                        NOTE

               This  implementation  of  GKS does its own buffering of
               output streams.  For this reason it only needs to  know
               about  RT-11  channel numbers.  If a FORTRAN LUN is not
               open when a call is made to a GKS subroutine, an  RT-11
               channel will be requested from the runtime system and a
               file opened whose device name is the FORTRAN LUN,  e.g.
               11:OUTPUT.DAT.   Thus the user can still assign FORTRAN
               LUNs to output devices at runtime.  




          3.2  LINKING PROGRAMS WITH GKS 



          3.2.1  Linking One Driver 


               Four  GKS modules are linked with the users program to build
          an executable image.  The modules are the GKS subroutine library,
          GKS.OBJ;   a  driver  table DRIVER.OBJ;  the particular driver or
          drivers to be used, e.g.  DRV745.OBJ;   and  the  driver  utility
          library  DRVUTL.OBJ.  Thus to link MYPROG with GKS and the HP7475
          6 pen plotter driver the command would be:  

                  LINK MYPROG,GKS,DRIVER,DRV745,DRVUTL 



          3.2.2  Linking More than One Driver 


               It  is  possible to link more than one driver with GKS.  The
          procedure for doing this is as follows.  

               1.  Change  the  entry  point name of one of the drivers (it
                   doesn't make any difference which one)  from  $CGID0  to
                   $CGID1 and reassemble it.  

               2.  Change  the  second  entry in the subroutine vector list
                   (shown below) to .WORD $CGID1 and reassemble it.  



                                        -3-2-





                                                       USING GKS WITH RT-11
                                                                           


               3.  Link  the  program as for the single driver case, except
                   include both driver names in the LINK command 

          GKS  will  accept up to eight drivers simultaneously.  However if
          you actually try this you probably won't be able to  do  anything
          because there will be no memory space left!  
          
          -----------------------------------------------------------------
          ;****************************************************************
          ;* Pointers to the workstation subroutine vector lists. Entries *
          ;* with a -1 are unused.                                        *
          ;****************************************************************
          
                  .PSECT  G$$WSV,RW,D,GBL,REL,OVR
          
          WSSBVC::.WORD   $CGID0          ; Device driver number 1
                  .WORD   -1              ; Device driver number 2
                  .WORD   -1              ; Device driver number 3
                  .WORD   -1              ; Device driver number 4
                  .WORD   -1              ; Device driver number 5
                  .WORD   -1              ; Device driver number 6
                  .WORD   -1              ; Device driver number 7
                  .WORD   -1              ; Device driver number 8
                  .END
          ----------------------------------------------------------------
                             Source Code for DRIVER.OBJ
          


          3.3  RUNNING PROGRAMS THAT USE GKS 


               Programs  that  make  calls to GKS subroutines run just like
          any other RT-11 program.  However, it is the user's  responsibil-
          ity  to make the logical connection between FORTRAN logical units
          used by the program and RT-11 devices.  Thus the sequence to  run
          a  program  that was linked with the Visual 550 device driver and
          which specified output to that device on FORTRAN logical unit  10
          would be:  

                  .ASSIGN TT:  10 
          .RUN MYPROG 















                                        -3-3-

















                                     APPENDIX A

                                GKS ENUMERATION TYPES




               All  the  enumeration types of GKS are mapped to FORTRAN IN-
          TEGERs.  The correspondence between GKS scalars and  FORTRAN  IN-
          TEGERs  is  shown  below  in a list of symbolic FORTRAN constants
          which may be included in any  application  program.   These  con-
          stants  are  defines in the file GKENUM.FIN.  This file should be
          'INCLUDE'ed in any program that makes  subroutine  calls  to  GKS
          functions.  
          
          C
          C     Aspect source bundled
          C                Bundled   Individual
                INTEGER    GBUNDL,   GINDIV
                PARAMETER (GBUNDL=0, GINDIV=1)
          C
          C     Clear control flag
          C                conditionally, always
                INTEGER    GCONDI,   GALWAY
                PARAMETER (GCONDI=0, GALWAY=1)
          C
          C     Clipping indicator
          C                noclip,   clip
                INTEGER    GNCLIP,   GCLIP
                PARAMETER (GNCLIP=0, GCLIP=1)
          C
          C     Colour available
          C                monochrome, colour
                INTEGER    GMONOC,   GCOLOR
                PARAMETER (GMONOC=0, GCOLOR=1)
          C
          C     Coordinate switch
          C                WC,       NDC
                INTEGER    GWC,      GNDC
                PARAMETER (GWC=0,    GNDC=1)
          C
          C     Deferral mode
          C                ASAP,     BNIG,     BNIL,     ASTI
                INTEGER    GASAP,    GBNIG,    GBNIL,    GASTI
                PARAMETER (GASAP=0,  GBNIG=1,  GBNIL=2,  GASTI=3)
          C
          C     Detectability


                                        -A-1-





          GKS ENUMERATION TYPES
          


          C                undetectable, detectable
                INTEGER    GUNDET,   GDETEC
                PARAMETER (GUNDET=0, GDETEC=1)
          C
          C     Device coordinate units
          C                metres,   other
                INTEGER    GMETRE,   GOTHU
                PARAMETER (GMETRE=0, GOTHU=1)
          C
          C     Display surface empty
          C                notempty, empty
                INTEGER    GNEMPT,   GEMPTY
                PARAMETER (GNEMPT=0, GEMPTY=1)
          C
          C     Dynamic modification
          C                IRG,      IMM
                INTEGER    GIRG,     GIMM
                PARAMETER (GIRG=0,   GIMM=1)
          C
          C     Echo switch
          C                noecho,   echo
                INTEGER    GNECHO,   GECHO
                PARAMETER (GNECHO=0, GECHO=1)
          C
          C     Fill area interior style
          C                hollow,   solid,    pattern,  hatch
                INTEGER    GHOLLO,   GSOLID,   GPATTR,   GHATCH
                PARAMETER (GHOLLO=0, GSOLID=1, GPATTR=2, GHATCH=3)
          C
          C     Highlighting
          C                normal,   highlighted
                INTEGER    GNORML,   GHILIT
                PARAMETER (GNORML=0, GHILIT=1)
          C
          C     Input device status
          C                none,     ok,       nopick,   nochoice
                INTEGER    GNONE,    GOK,      GNPICK,   GNCHOI
                PARAMETER (GNONE=0,  GOK=1,    GNPICK=2, GNCHOI=3)
          C
          C     Input class
          C                none,     locator,  stroke,   valuator, 
          C                choice,   pick,     string
                INTEGER    GNCLAS,   GLOCAT,   GSTROK,   GVALUA,   
               +           GCHOIC,   GPICK,    GSTRIN
                PARAMETER (GNCLAS=0, GLOCAT=1, GSTROK=2, GVALUA=3, 
               +           GCHOIC=4, GPICK=5,  GSTRIN=6)
          C
          C     Implicit regeneration mode
          C                suppressed, allowed
                INTEGER    GSUPPD,   GALLOW
                PARAMETER (GSUPPD=0, GALLOW=1)
          C
          C     Level of GKS
          C                Lma,      Lmb,      Lmc,      L0a,      L0b,
          C                L0c,      L1a,      L1b,      L1c,      L2a,


                                        -A-2-





                                                      GKS ENUMERATION TYPES
                                                                           


          C                L2b,      L2c
                INTEGER    GLMA,     GLMB,     GLMC,     GL0A,     GL0B,
               +           GL0C,     GL1A,     GL1B,     GL1C,     GL2A,
               +           GL2B,     GL2C
                PARAMETER (GLMA=-3,  GLMB=-2,  GLMC=-1,  GL0A=0,   GL0B=1,
               +           GL0C=2,   GL1A=3,   GL1B=4,   GL1C=5,   GL2A=6,
               +           GL2B=7,   GL2C=8)
          C
          C     New frame action necessary
          C                no,       yes
                INTEGER    GNO,      GYES
                PARAMETER (GNO=0,    GYES=1)
          C
          C     Operating mode
          C                request,  sample,   event
                INTEGER    GREQU,    GSAMPL,   GEVENT
                PARAMETER (GREQU=0,  GSAMPL=1, GEVENT=2)
          C
          C     Operating state values
          C                GKCL,     GKOP,     GWSOP,    GWSAC,    GSGOP
                INTEGER    GKCL,     GKOP,     GWSOP,    GWSAC,    GSGOP
                PARAMETER (GKCL=0,   GKOP=1,   GWSOP=2,  GWSAC=3,  GSGOP=4)
          C
          C     Presence of invalid values
          C                absent,   present
                INTEGER    GABSNT,   GPRSNT
                PARAMETER (GABSNT=0, GPRSNT=1)
          C
          C     Regeneration flag
          C                postpone, perform
                INTEGER    GPOSTP,   GPERFO
                PARAMETER (GPOSTP=0, GPERFO=1)
          C
          C     Relative input priority
          C                higher,   lower
                INTEGER    GHIGHR,   GLOWER
                PARAMETER (GHIGHR=0, GLOWER=1)
          C
          C     Simultaneous events flag.
          C                nomore,   more
                INTEGER    GNMORE,   GMORE
                PARAMETER (GNMORE=0, GMORE=1)
          C
          C     Text Alignment Horizontal
          C                Normal    Left      Center    Right
                INTEGER    GAHNOR,   GALEFT,   GACENT,   GARITE
                PARAMETER (GAHNOR=0, GALEFT=1, GACENT=2, GARITE=3)
          C
          C     Text Alignment Vertical
          C                Normal,   Top,      Cap,      Half,     Base,   
           
          C                Bottom
                INTEGER    GAVNOR,   GATOP,    GACAP,    GAHALF,   GABASE,
               +           GABOTT
                PARAMETER (GAVNOR=0, GATOP=1,  GACAP=2,  GAHALF=3,


                                        -A-3-





          GKS ENUMERATION TYPES
          


          GABASE=4, 
               +           GABOTT=5)
          C
          C     Text path
          C                right     left,     up,       down
                INTEGER    GRIGHT,   GLEFT,    GUP,      GDOWN
                PARAMETER (GRIGHT=0, GLEFT=1,  GUP=2,    GDOWN=3)
          C
          C     Text precision
          C                string,   character, stroke
                INTEGER    GSTRP,    GCHARP,   GSTRKP
                PARAMETER (GSTRP=0,  GCHARP=1, GSTRKP=2)
          C
          C     Type of returned values
          C                set       realized
                INTEGER    GSET,     GREALI
                PARAMETER (GSET=0,   GREALI=1)
          C
          C     Update state
          C                notpending, pending
                INTEGER    GNPEND,   GPEND
                PARAMETER (GNPEND=0, GPEND=1)
          C
          C     Vector/Raster/Other type
          C                vector,   raster,   other
                INTEGER    GVECTR,   GRASTR,   GOTHWK
                PARAMETER (GVECTR=0, GRASTR=1, GOTHWK=2)
          C
          C     Visibility
          C                invisible, visible
                INTEGER    GINVIS,   GVISI
                PARAMETER (GINVIS=0, GVISI=1)
          C
          C     Workstation category
          C                output,   input,    outin,    wiss,     mo,     
           
          C                mi
                INTEGER    GOUTPT,   GINPUT,   GOUTIN,   GWISS,    GMO,    
           
               +           GMI
                PARAMETER (GOUTPT=0, GINPUT=1, GOUTIN=2, GWISS=3,  GMO=4,  
           
               +           GMI=5)
          C
          C     Workstation state
          C                inactive, active
                INTEGER    GINACT,   GACTIV
                PARAMETER (GINACT=0, GACTIV=1)
          C
          C     List of GDP attributes
          C                polyline attribute, polymarker attribute, text 
          C                attribute, fill area attribute
                INTEGER    GPLATT,   GPMATT,   GTXATT,   GFAATT
                PARAMETER (GPLATT=0, GPMATT=1, GTXATT=2, GFAATT=3)
          C


                                        -A-4-





                                                      GKS ENUMERATION TYPES
                                                                           


          C     Line type
          C                solid,    dash,     dot,      dash-dot
                INTEGER    GLSOLI,   GLDASH,   GLDOT,    GLDASD
                PARAMETER (GLSOLI=1, GLDASH=2, GLDOT=3,  GLDASD=4)
          C
          C     Marker type
          C                '.',      '+',      '*',      'o',      
          C                'x'
                INTEGER    GPOINT,   GPLUS,    GAST,     GOMARK,   
               +           GXMARK
                PARAMETER (GPOINT=1, GPLUS=2,  GAST=3,   GOMARK=4, 
               +           GXMARK=5)
          C
          C     Attribute control flag
          C                current,  specified
                INTEGER    GCURNT,   GSPEC
                PARAMETER (GCURNT=0, GSPEC=1)
          C
          C     Polyline/Fill Area control flag
          C                polyline, fill area
                INTEGER    GPLINE,   GFILLA
                PARAMETER (GPLINE=0, GFILLA=1)
          C
          C     Initial choice prompt flag
          C                off       on
                INTEGER    GPROFF,   GPRON
                PARAMETER (GPROFF=0, GPRON=1)






























                                        -A-5-





                                        INDEX





          ACTIVATE WORKSTATION  . . . . . . . . . . . . . . . .    1-5, 2-2
          ANSI  . . . . . . . . . . . . . . . . . . . . . . . . . . .   1-1
          ATTRIBUTES  . . . . . . . . . . . . . . . . . . . . . . . .   1-2

          CGI . . . . . . . . . . . . . . . . . . . . . . . . . . . .   1-1
          CHARACTER HEIGHT  . . . . . . . . . . . . . . . . .    2-12, 2-30
          CHARACTER UP VECTOR . . . . . . . . . . . . . . . .    2-13, 2-31
          CLEAR WORKSTATION . . . . . . . . . . . . . . . . . . . . .   2-4
          CLIP INDICATOR  . . . . . . . . . . . . . . . . . . . . . .   1-7
          CLIPPING  . . . . . . . . . . . . . . . . . . . . . . . . .   1-7
          CLIPPING INDICATOR  . . . . . . . . . . . . . . . .    2-14, 2-32
          CLOSE GKS . . . . . . . . . . . . . . . . . . . . . . . . .   2-3
          CLOSE WORKSTATION . . . . . . . . . . . . . . . . . .    1-5, 2-6
          COLOR FACILITIES  . . . . . . . . . . . . . . . . . . . .    2-11
          COLOR REPRESENTATION  . . . . . . . . . . . . . . . . . .    2-16
          COORDINATE SYSTEMS  . . . . . . . . . . . . . . . . . . . .   1-6

          DEACTIVATE WORKSTATION  . . . . . . . . . . . . . . . . . .   2-7
          DECUS 
          DEVICE DRIVERS  . . . . . . . . . . . . . . . . . . .    1-1, 3-2

          ENUMERATION TYPES . . . . . . . . . . . . . . . . . . . . .   A-1

          FILL AREA . . . . . . . . . . . . . . . . . . . . . . . . .   1-4
          FILL AREA COLOR INDEX . . . . . . . . . . . . . . .    2-18, 2-34
          FILL AREA INTERIOR STYLE  . . . . . . . . . . . . .    2-19, 2-35
          FORTRAN LUN . . . . . . . . . . . . . . . . . . . . . . . .   3-2

          GACWK . . . . . . . . . . . . . . . . . . . . . . . .    2-2, 3-1
          GCLKS . . . . . . . . . . . . . . . . . . . . . . . .    2-3, 3-1
          GCLRWK  . . . . . . . . . . . . . . . . . . . . . . . . . .   2-4
          GCLWK . . . . . . . . . . . . . . . . . . . . . . . .    2-6, 3-1
          GDAWK . . . . . . . . . . . . . . . . . . . . . . . .    2-7, 3-1
          GKS . . . . . . . . . . . . . . . . . . . . . . . . . . . .   2-8
          GOPKS . . . . . . . . . . . . . . . . . . . . . .   2-8, 3-1, 3-2
          GOPWK . . . . . . . . . . . . . . . . . . . . . .   2-9, 3-1, 3-2
          GPM . . . . . . . . . . . . . . . . . . . . . . . . . . .    2-10
          GQCF  . . . . . . . . . . . . . . . . . . . . . . . . . .    2-11
          GQCHH . . . . . . . . . . . . . . . . . . . . . . . . . .    2-12
          GQCHUP  . . . . . . . . . . . . . . . . . . . . . . . . .    2-13
          GQCLIP  . . . . . . . . . . . . . . . . . . . . . . . . .    2-14
          GQCNTN  . . . . . . . . . . . . . . . . . . . . . . . . .    2-15
          GQCR  . . . . . . . . . . . . . . . . . . . . . . . . . .    2-16
          GQFACI  . . . . . . . . . . . . . . . . . . . . . . . . .    2-18
          GQFAIS  . . . . . . . . . . . . . . . . . . . . . . . . .    2-19
          GQLN  . . . . . . . . . . . . . . . . . . . . . . . . . .    2-20
          GQLVKS  . . . . . . . . . . . . . . . . . . . . . . . . .    2-21
          GQMK  . . . . . . . . . . . . . . . . . . . . . . . . . .    2-22
          GQNT  . . . . . . . . . . . . . . . . . . . . . . . . . .    2-23
          GQPLCI  . . . . . . . . . . . . . . . . . . . . . . . . .    2-24
          GQPMCI  . . . . . . . . . . . . . . . . . . . . . . . . .    2-25
          GQTXAL  . . . . . . . . . . . . . . . . . . . . . . . . .    2-26
          GQWKC . . . . . . . . . . . . . . . . . . . . . . . . . .    2-27


                                        -X-1-





          
          


          GQWKT . . . . . . . . . . . . . . . . . . . . . . . . . .    2-28
          GSCHH . . . . . . . . . . . . . . . . . . . . . . . . . .    2-30
          GSCHUP  . . . . . . . . . . . . . . . . . . . . . . . . .    2-31
          GSCLIP  . . . . . . . . . . . . . . . . . . . . . . . . .    2-32
          GSELNT  . . . . . . . . . . . . . . . . . . . . . . . . .    2-33
          GSFACI  . . . . . . . . . . . . . . . . . . . . . . . . .    2-34
          GSFAIS  . . . . . . . . . . . . . . . . . . . . . . . . .    2-35
          GSLN  . . . . . . . . . . . . . . . . . . . . . . . . . .    2-36
          GSMK  . . . . . . . . . . . . . . . . . . . . . . . . . .    2-37
          GSPLCI  . . . . . . . . . . . . . . . . . . . . . . . . .    2-38
          GSTXAL  . . . . . . . . . . . . . . . . . . . . . . . . .    2-39
          GSTXCI  . . . . . . . . . . . . . . . . . . . . . . . . .    2-40
          GSVP  . . . . . . . . . . . . . . . . . . . . . . . . . .    2-41
          GSWKVP  . . . . . . . . . . . . . . . . . . . . . . . . .    2-42
          GSWKWN  . . . . . . . . . . . . . . . . . . . . . . . . .    2-43
          GSWN  . . . . . . . . . . . . . . . . . . . . . . . . . .    2-44
          GTX . . . . . . . . . . . . . . . . . . . . . . . . . . .    2-45
          GUWK  . . . . . . . . . . . . . . . . . . . . . . . . . .    2-47

          HP7475 

          INQUIRY FUNCTIONS . . . . . . . . . . . . . . . . . . . . .   1-3
          ISO . . . . . . . . . . . . . . . . . . . . . . . . . . . .   1-1

          LEVEL OF GKS  . . . . . . . . . . . . . . . . . . . . . .    2-21
          LINETYPE  . . . . . . . . . . . . . . . . . . . . . .   2-20, 3-1

          NORMALIZATION TRANSFORMATION  . . . . . . . . . . .    2-23, 2-33
          NORMALIZATION TRANSFORMATION NUMBER . . . . . . . . . . .    2-15

          OPEN  . . . . . . . . . . . . . . . . . . . . . . . .    2-8, 2-9
          OPEN WORKSTATION  . . . . . . . . . . . . . . . . . . . . .   1-5
          OUTPUT PRIMITIVES . . . . . . . . . . . . . . . . . . . . .   1-3

          POLYLINE  . . . . . . . . . . . . . . . .    1-1, 1-3, 2-36, 2-38
          POLYLINE COLOR INDEX  . . . . . . . . . . . . . . . . . .    2-24
          POLYMARKER  . . . . . . . . . . . . . . . . . .    1-1, 1-4, 2-10
          POLYMARKER COLOR INDEX  . . . . . . . . . . . . . . . . .    2-25
          POLYMARKER INDEX  . . . . . . . . . . . . . . . . . . . .    2-22
          PRIMITIVE ATTRIBUTES  . . . . . . . . . . . . . . . . . . .   1-4
          PRIMITIVES  . . . . . . . . . . . . . . . . . . . . . . . .   1-2

          SELECT NORMALIZATION TRANSFORMATION . . . . . . . . . . . .   1-7
          SET LINETYPE  . . . . . . . . . . . . . . . . . . . . . .    2-36
          SET MARKERTYPE  . . . . . . . . . . . . . . . . . . . . .    2-37
          SET POLYLINE COLOR INDEX  . . . . . . . . . . . . . . . .    2-38
          SET TEXT ALIGNMENT  . . . . . . . . . . . . . . . . . . .    2-39
          SET TEXT COLOR INDEX  . . . . . . . . . . . . . . . . . .    2-40
          SET VIEWPORT  . . . . . . . . . . . . . . . . . . . . . .    2-41
          SET WINDOW  . . . . . . . . . . . . . . . . . . . . . . .    2-44

          TEKTRONICS 4107 . . . . . . . . . . . . . . . . . . . . . .   1-1
          TEXT  . . . . . . . . . . . . . . .    1-1, 1-4, 2-39, 2-40, 2-45
          TEXT ALIGNMENT  . . . . . . . . . . . . . . . . . . . . .    2-26
          TRANSFORMATIONS . . . . . . . . . . . . . . . . . . . . . .   1-6


                                        -X-2-





                                                                           
                                                                           


          UPDATE WORKSTATION  . . . . . . . . . . . . . . . . . . .    2-47

          VIEWPORT  . . . . . . . . . . . . . . . . . . . . . . . .    2-41
          VISUAL 550  . . . . . . . . . . . . . . . . . . . . . . . .   1-1

          WINDOW  . . . . . . . . . . . . . . . . . . . . . . . . .    2-44
          WORKSTATION . . . . . . . . . . . . . . . . . . . . .   2-9, 2-47
          WORKSTATION CONNECTION  . . . . . . . . . . . . . . . . .    2-27
          WORKSTATION TRANSFORMATION  . . . . . . . . . . . . . . .    2-28
          WORKSTATION TRANSFORMATIONS . . . . . . . . . . . . . . . .   1-7
          WORKSTATION TYPE  . . . . . . . . . . . . . . . . . . . .    2-27
          WORKSTATION VIEWPORT  . . . . . . . . . . . . . . . . . .    2-42
          WORKSTATION WINDOW  . . . . . . . . . . . . . . . . . . .    2-43
          WORKSTATIONS  . . . . . . . . . . . . . . . . . . . . . . .   1-5

          X3H3  . . . . . . . . . . . . . . . . . . . . . . . . . . .   1-1

               







































                                        -X-3-