Files-11 On-Disk Structure Specification


     Andrew C. Goldstein
     VAX/VMS Software Devlopment


     15-Jan-1979


     Copyright (C) 1979 Digital Equipment  Corporation,  Maynard,
     Mass.


     The material  included  in  this  functional  specification,
     including but not limited to instruction times and operating
     speeds, is for information purposes only.  All such material
     is  subject  to change without notice.  Consequently Digital
     Equipment Corporation makes no claim and shall not be liable
     for its accuracy.


     This software is furnished under a license for use only on a
     single  computer  system  and  may  be  copied only with the
     inclusion of the above copyright notice.  This software,  or
     any  other  copies thereof, may not be provided or otherwise
     made available to any other person except for  use  on  such
     system  and to one who agrees to these license terms.  Title
     to and ownership of the software shall at all  times  remain
     in Digital Equipment Corporation.


     The information  in  this  document  is  subject  to  change
     without  notice  and should not be construed as a commitment
     by Digital Equipment Corporation.


     Digital Equipment Corporation assumes no responsibility  for
     the use or reliability of its software on equipment which is
     not supplied by Digital Equipment Corporation.


     Files-11 On-Disk Structure                            Page 2


     1.0  SCOPE

     This document is a specification of the  on-media  structure
     that  is  used  by  Files-11.  Files-11 is a general purpose
     file structure which is intended to  be  the  standard  file
     structure  for  all  medium  to large PDP-11 systems.  Small
     systems  such  as  RT-11  have  been  specifically  excluded
     because  the complexity of Files-11 would impose too great a
     burden on their simplicity and small size.

     This document describes structure level 2 of Files-11,  also
     referred  to  as  ODS-2  (on-disk structure 2).  It contains
     feature and reliability improvements over structure level  1
     (ODS-1).    This  version  of  the  specification  has  been
     subsetted to describe  only  the  features  that  have  been
     implemented at present (VMS Version 1.5).



     1.1  Conventions

     All numerical values given in this document are  in  decimal
     radix, unless indicated otherwise.

     Within the  file  structure  are  fields  containing  binary
     integers  of  various  lengths.  Unless otherwise indicated,
     all these fields are in the standard numerical format, which
     means  that  the  most  significant  bits  are stored in the
     highest numbered address.

     In the descriptions of various structures on the disk, there
     are  fields  that are labeled "not used".  These fields must
     be zero, so that they can be made non-zero for  future  use.
     Since  they  are  reserved  for future use, programs reading
     these structures should not assume that these fields are  in
     fact zero.



     2.0  MEDIUM

     Files-11 is a structure which is imposed on a medium.   That
     medium  must have certain properties, which are described in
     the   following   section.    Generally   speaking,    block
     addressable  storage  devices  such as disks and Dectape are
     suitable for Files-11;  hence Files-11 structured media  are
     generically referred to as disks.


     Files-11 On-Disk Structure                            Page 3


     2.1  Volume

     The basic  medium  that  carries  a  Files-11  structure  is
     referred  to  as a volume.  A volume (also often referred to                        ______
     as a unit) is defined as an ordered set of  logical  blocks.          ____                                   _______  ______
     A logical block is an array of 512 8-bit bytes.  The logical
     blocks in a volume are consecutively numbered from 0 to n-1,
     where  the  volume  contains  n  logical blocks.  The number
     assigned to a logical block  is  called  its  logical  block                                                   _______  _____
     number,  or  LBN.  Files-11 is capable of describing volumes     ______       ___
     up to 2**32 blocks in size.  In practice, a volume should be
     at least 100 blocks in size to be useful.

     The logical blocks of a volume must be randomly addressable.
     The volume must also allow transfers of any length up to 65K
     bytes, in multiples of  four  bytes.   When  a  transfer  is
     longer than 512 bytes, consecutively numbered logical blocks
     are transfered until the byte count is satisfied.  In  other
     words,  the  volume  can be viewed as a partitioned array of
     bytes.  It must allow reads and  writes  of  arrays  of  any
     length  less  than  65K bytes, provided that they start on a
     logical block boundary and that the length is a multiple  of
     four  bytes.   When  only  part  of  a block is written, the
     contents of the remainder of  that  logical  block  will  be
     undefined.

     The logical blocks of a volume are  grouped  into  clusters.                                                        ________
     The  cluster  is  the  basic unit of space allocation on the
     volume.  Each cluster contains one or more  logical  blocks;
     the  number  of  blocks  in a cluster is known as the volume                                                           ______
     cluster factor, or storage map cluster factor.     _______ ______     _______ ___ _______ ______

     A volume is identified as a  Files-11  volume  by  the  home
     block.   The  home  block  is  located at a defined physical
     location on the volume, and is identified by the presence of
     checksums   and  predictable  values.   The  home  block  is
     described in detail in section 5.1.  To identify the volume,
     the home block contains a volume label, which is a string of                               ______ _____
     up to 12 ASCII characters.  The characters are restricted to
     the  printing  ASCII set (i.e., excluding control characters
     and rubout).  Further, it is reccommended that volume labels
     be  restricted to alphanumerics only to avoid conflicts with
     the command languages of  supporting  systems.   The  volume
     label of a volume may not be null.



     2.2  Volume Sets

     A volume set is a collection of  related  volumes  that  are       ______ ___
     normally   treated  as  one  logical  device  in  the  usual
     operating system concept.   Each  volume  contains  its  own
     Files-11  structure;   however, files on the various volumes
     in a volume set may be referenced  with  a  relative  volume                                                 ________  ______
     number,  which  uniquely  determines which volume in the set     ______


     Files-11 On-Disk Structure                            Page 4


     the file is located on.

     A volume set has associated with it a structure name,  which                                           _________ ____
     is  an  string of up to 12 ASCII characters which identifies
     the volume set.  The character set limitations of the volume
     label  also apply to the structure name.  The structure name
     may not be null.



     2.2.1  Tightly Coupled Volume Set -

     A tightly coupled volume  set  is  a  volume  set  which  is       _______ _______ ______  ___
     consistent  and  self identifying.  The volume labels of the
     volumes making up the set must be unique within the set, and
     must  be different from the structure name.  Relative volume
     one of the set contains a file which lists the volume labels
     of  all  the  volumes  in  the  set, thus associating volume
     labels  with  relative  volume  numbers.   Each  volume   is
     identified  as  being  part  of  the  set  by  carrying  the
     structure name, its volume label, and  its  relative  volume
     number.



     2.2.2  Loosely Coupled Volume Set -

     A loosely coupled volume set  is  a  collection  of  volumes       _______ _______ ______ ___
     which is not self identifying.  There is no file listing the
     volume labels.  Only one file may cross from any one  volume
     in  the  set  to  another,  and files in the set which cross
     volumes  may  be  processed  only   sequentially.    Correct
     sequencing of the volumes that hold a particular file is the
     responsibility of the system  operator.   There  are  checks
     that  will  catch  most  handling errors, but they cannot be
     foolproof.  The purpose of the loosely coupled volume set is
     to emulate multi-volume magtape, and allow a file to be read
     or written sequentially with only one volume  mounted  at  a
     time.



     3.0  FILES

     Any data in a volume or volume set that is of  any  interest
     (i.e., all blocks not available for allocation) is contained
     in a file.  A file is an  ordered  set  of  virtual  blocks,          ____                                   _______  ______
     where  a  virtual block is an array of 512 8 bit bytes.  The
     virtual blocks of a file are consecutively numbered  from  1
     to  n,  where  n is the highest numbered block that has been
     allocated to the file.  The number  assigned  to  a  virtual
     block  is  called  (obviously)  its virtual block number, or                                         _______ _____ ______
     VBN.  Virtual blocks are mapped to unique logical blocks  in     ___
     the volume set by Files-11.  Virtual blocks may be processed
     in the same manner as logical blocks.  Any  array  of  bytes


     Files-11 On-Disk Structure                            Page 5


     less  than  65K  in  length may be read or written, provided
     that the transfer starts on a  virtual  block  boundary  and
     that its length is a multiple of four.

     For most files, all VBN's less than or equal to the  highest
     VBN allocated map to some LBN in the volume set.  Such files
     are said to  be  dense.   Files  which  are  sparse  contain                      _____                       ______
     virtual blocks which have not been allocated logical blocks.



     3.1  File ID

     Each file in a volume set is uniquely identified by  a  File                                                             ____
     ID.   A  File  ID is a binary value consisting of 48 bits (3     __
     PDP-11 words).  It is supplied by the file system  when  the
     file  is  created, and must be supplied by the user whenever
     he wishes to reference a particular file.

     The three words of the File ID are used as follows:

     Word 1    File Number

               Locates the file within a particular volume of the
               volume  set.   File  numbers ordinarily lie in the
               range 1 through 65535.  The set of file numbers on
               a  volume  is  moderately (but not totally) dense;
               at any instant in  time  a  file  number  uniquely
               identifies one file within that volume.

     Word 2    File Sequence Number

               Identifies the current use of an  individual  file
               number  on  a  volume.   File numbers are re-used;
               when a file is deleted  its  file  number  becomes
               available  for  future  use  for  some other file.
               Each time a file number is  re-used,  a  different
               file  sequence  number  is assigned to distinguish
               the uses of that file number.  The  file  sequence
               number  is  essential  since it is perfectly legal
               for users to remember and attempt to use a File ID
               long after that file has been deleted.

     Word 3    Relative Volume Number

               Identifies which volume of a volume set  the  file
               is located on.  If the volume in question is not a
               member of a volume set, then this  word  is  zero.
               If  the  volume  is part of a volume set, then the
               relative volume number, or RVN, lies in the  range                                          ___
               from   1   to  65535.   In  any  context  where  a
               particular  volume  of  a  volume   set   can   be
               identified as the "current volume", such as a file
               extension linkage, a  relative  volume  number  of
               zero  means  "the current volume".  When a file is


     Files-11 On-Disk Structure                            Page 6


               referred to in the context of the volume on  which
               it  lies, it should be referred to with a relative
               volume number of zero, regardless of the RVN  that
               may be assigned to that volume.

     File Number Extension

               If the maximum number of files  permitted  on  the
               volume  (as recorded in the home block) is greater
               than 65535, then the high  byte  of  the  relative
               volume  number  becomes  a high order extension to
               the file number.  The  volume  set  size  is  then
               limited   to  255  volumes,  while  the  range  of
               allowable file numbers extends from 1 to  2**24-1.
               When 24 bit file numbers are used, the file system
               should not create files whose file  number  is  an
               integer multiple of 65536 (i.e., whose low 16 bits
               are zero).  Such file numbers will break  existing
               PDP-11 software (such as FCS-11).



     3.2  File Header

     Each file on a  Files-11  volume  is  described  by  a  file                                                             ____
     header.   The  file  header is a block that contains all the     ______
     information necessary to access the file.  It is not part of
     the  file;   rather,  it  is contained in the volume's index
     file.  (The index file is described in  section  5.1).   The
     header block is organized into six areas, of which the first
     five are variable in size.



     3.2.1  Header Area -

               The information in the  header  area  permits  the
               file system to verify that this block is in fact a
               file header and,  in  particular,  is  the  header
               being  sought  by  the user.  It contains the file
               number and file sequence number of  the  file,  as
               well  as its ownership and protection codes.  This
               area also contains offsets to the other  areas  of
               the file header, thus defining their size.



     3.2.2  Ident Area -

               The  ident  area  of  a   file   header   contains
               identification and accounting data about the file.
               Stored here are the primary name of the file,  its
               creation  date and time, revision count, date, and
               time, and expiration date.


     Files-11 On-Disk Structure                            Page 7


     3.2.3  Map Area -

               The map area  describes  the  mapping  of  virtual
               blocks  of  the  file to the logical blocks of the
               volume.  The mapping data consists of  a  list  of
               retrieval   pointers.    Each   retrieval  pointer               _________   ________
               describes  one  group  of  consecutively  numbered
               logical  blocks  that  are  allocated to the file.
               Retrieval pointers are arranged in  the  order  of
               the virtual blocks they represent.



     3.2.4  Access Control List -

               The access control list is an optional  area  that
               contains  a  list of users that are allowed access
               to the file.  The access  control  list  makes  it
               possible   to  describe  user  communities  for  a
               particular file that cannot be expressed with  the
               regular protection classes.



     3.2.5  Reserved Area -

               This optional area is reserved for the use by  CSS
               or  special  applications.  It will not be used by
               standard Files-11 systems.



     3.2.6  End Checksum -

               The last two bytes of the file header contain a 16
               bit  additive  checksum of the preceding 255 words
               of the file header.  The checksum is used to  help
               verify that the block is in fact a file header.



     3.3  Multi-header Files

     Since the file header is of fixed  size,  it  is  inevitable
     that  for some files the mapping information will not fit in
     the allocated space.  A file with a large amount of  mapping
     data  is therefore represented with a chain of file headers.
     Each header maps a consecutive set of virtual  blocks;   the
     extension  linkage  in  the  header  area  links the headers
     together in order of ascending virtual block  numbers.   The
     extension  pointer in each file header is the File ID of the
     next header in sequence.


     Files-11 On-Disk Structure                            Page 8


     3.4  Multi-volume Files

     Multiple headers are also needed for files that span volumes
     in  a  volume  set.   A  header  may only map logical blocks
     located on its volume;  therefore  a  multi-volume  file  is
     represented  by headers on all volumes that contain portions
     of that file.  In a multi-volume file contained on a loosely
     coupled  volume set, the File ID of the first header on each
     continuation volume always has the value 7,7,n, where  n  is
     the  RVN  of  the  volume  on which the file starts plus the
     number of preceding volumes containing portions of the file.



     3.5  File Header - Detailed Description

     This section describes in detail the items contained in  the
     file  header.   Each  item  is  identified by a symbol which
     represents the offset address of that item within  its  area
     in  the  file  header.   Any item may be located in the file
     header by locating the area to which  it  belongs  and  then
     adding  the  value of its offset address.  Users who concern
     themselves with the contents of file  headers  are  strongly
     urged to use the offset symbols.

     The symbols may be defined in PDP-11 (and VAX  compatibility
     mode) assembly language programs by calling and invoking the
     macro FHDL2$, which may be found in the macro library of any
     system  that supports Files-11.  Alternatively, one may find
     the macro in the file OD2MAC.MAC, which may be obtained from
     the author.

     VAX native mode assembly  language  programs  can  define  a
     corresponding  set  of  file  header offsets by invoking the
     macros $FH2DEF, $FI2DEF,  and  $FM2DEF.   These  macros  are
     located  in  the macro library LIB.MLB.  The source of these
     macros is located in the file F11DEF.MAR.



     3.5.1  Validity -

     A valid file header is defined by the following rules:

     1.  The contents of  H.IDOF  is  no  less  than  the  offset
         H.FOWN/2.

     2.  The four offset bytes are related in the manner (H.IDOF)
         <= (H.MPOF) <= (H.ACOF) <= (H.RSOF).

     3.  The high byte of H.FLEV contains the value 2.

     4.  The low byte of H.FLEV contains a value greater or equal
         to 1.


     Files-11 On-Disk Structure                            Page 9


     5.  The word H.FNUM contains the file number.

     6.  The word H.FSEQ contains the file sequence number.

     7.  The high byte H.FRVN contains the extended part  of  the
         file number, if any.

     8.  The contents of the byte H.USE  must  be  less  than  or
         equal to (H.ACOF) - (H.MPOF).

     A deleted file header conforms to the format of a valid file
     header with the following exceptions:

     1.  SC.MDL is set in H.FCHA.

     2.  H.FNUM and H.FRVN contain zero.

     3.  The file header checksum contains zero.




     3.5.2  Header Area Description -

     The header area of the file header always starts at byte  0.
     It  contains  the  basic information needed for checking the
     validity of accesses to the file.



     3.5.2.1  H.IDOF - 1 Byte      Ident Area Offset

               This byte contains the  number  of  16  bit  words
               between the start of the file header and the start
               of the ident area.  It defines the location of the
               ident area and the size of the header area.



     3.5.2.2  H.MPOF - 1 Byte      Map Area Offset

               This byte contains the  number  of  16  bit  words
               between the start of the file header and the start
               of the map area.  It defines the location  of  the
               map  area  and,  together with H.IDOF, the size of
               the ident area.



     3.5.2.3  H.ACOF - 1 Byte      Access Control List Offset

               This byte contains the  number  of  16  bit  words
               between the start of the file header and the start
               of  the  access  control  list.   It  defines  the
               location of the ACL and, together with H.MPOF, the


     Files-11 On-Disk Structure                           Page 10


               size of the map area.



     3.5.2.4  H.RSOF - 1 Byte      Reserved Area Offset

               This byte contains the  number  of  16  bit  words
               between  the  start of the header and the start of
               the reserved area.  The reserved area will not  be
               used by Files-11 itself, and may be used by CSS or
               special applications.  Together with H.ACOF,  this
               byte  defines the size of the access control list.
               The size of the reserved area is  implied  by  the
               contents  of  H.RSOF  and  the  end  of the header
               block.

               The presence of the ident, map, ACL, and  reserved
               areas   is  optional.   Absence  of  any  area  is
               signalled  not  by  a  zero  offset,  but  by  the
               equality  of  the  two  offsets  that  define that
               area's size.   All  five  areas  are  variable  in
               length;   implementations  of  Files-11 must check
               the length of a particular area before  attempting
               to reference a particular entry.



     3.5.2.5  H.FSEG - 2 Bytes     Extension Segment Number

               This word contains the value n, where this  header
               is the n+1th header of the file;  i.e., headers of
               a file are numbered sequentially starting with 0.



     3.5.2.6  H.FLEV - 2 Bytes     Structure Level and Version

               The file structure level and version  is  used  to
               identify  different  versions  of Files-11 as they
               affect the structure of  the  file  header.   This
               permits  upwards  compatibility of file structures
               as Files-11 evolves, in that the  structure  level
               word  identifies  the  version  of  Files-11  that
               created  this  particular  file.   This   document
               describes structure level 2 of Files-11.  The high
               byte of H.FLEV must contain the value 2.  The  low
               byte  contains  the  version number, which must be
               greater or equal to 1.  The version number will be
               incremented whenever compatible additions are made
               to the  Files-11  structure  that  may  be  safely
               ignored  by  an  old  version  of the file system.
               This document describes  version  1  of  structure
               level 2.


     Files-11 On-Disk Structure                           Page 11


     3.5.2.7  H.FNUM - 2 Bytes     File Number

               This word contains the file number of the file.



     3.5.2.8  H.FSEQ - 2 Bytes     File Sequence Number

               This word contains the file sequence number of the
               file.



     3.5.2.9  H.FRVN - 2 Bytes     Relative Volume Number

               This word is used to hold part of the  third  word
               of  the  File  ID  when appropriate.  This word is
               usually referred to as the relative volume number.
               When used as such (i.e., to indicate the volume of
               a volume set), it is  not  recorded  in  the  file
               header,  since  the  RVN  of  a  volume may change
               during a file's life, and the  RVN  portion  of  a
               File  ID may be zero or non-zero, depending on the
               context.  However, when the high byte of  the  RVN
               is  used  as an extension to the file number, then
               it is recorded in the high byte of this word.  The
               low byte of H.FRVN is always zero.



     3.5.2.10  H.EFNU - 2 Bytes    Extension File Number

               This word contains the file  number  of  the  next
               sequential  extension  header  for  this file.  If
               there is no extension header, this  word  contains
               0.



     3.5.2.11  H.EFSQ - 2 Bytes    Extension File Sequence Number

               This word contains the file sequence number of the
               next  sequential  extension  header for this file.
               If  there  is  no  extension  header,  this   word
               contains 0.



     3.5.2.12  H.ERVN - 2 Bytes    Extension Relative Volume No.

               This word contains the relative volume  number  of
               the  volume  in  the  volume set that contains the
               next sequential extension header  for  this  file.
               If  there  is  no  extension  header,  or  if  the
               extension header is located on the same volume  as


     Files-11 On-Disk Structure                           Page 12


               this header, this word contains 0.



     3.5.2.13  H.UFAT - 32 Bytes   User File Attributes

               This area is used by the record  manager,  or  any
               other  higher  level  access  mechanism,  to store
               information necessary  for  processing  the  file,
               e.g., record control data, end of file mark, etc.



     3.5.2.14  H.FCHA - 4 Bytes    File Characteristics
               H.UCHA =  H.FCHA+0  User Controlled Char.
               H.SCHA =  H.FCHA+1  System Controlled Char.

               The  file  characteristics   words   contain   the
               following flag bits:

               UC.CON    Set if the file is logically contiguous;                                            _________ __________
                         i.e.,  if  for all virtual blocks in the
                         file, virtual block i  maps  to  logical
                         block   k+i   on  one  volume  for  some
                         constant k.  This bit may be  implicitly
                         set or cleared by file system operations
                         that allocate space to  the  file;   the
                         user may only clear it explicitly.

               UC.CNB    Set if the file is allocated  contiguous
                         best  effort;   i.e.,  as  contiguous as
                         possible.

               UC.DLK    Set  if  the  file  is  deaccess-locked.
                         This  bit is used as a flag warning that
                         the file was not properly closed and may
                         contain  inconsistent  data.   Access to
                         the file is denied if this bit is set.

               UC.RCK    Set if the file is to  be  read-checked.
                         All   read   operations   on  the  file,
                         including reads of the  file  header(s),
                         will   be   performed   with   a   read,
                         read-compare to assure data integrity.

               UC.WCK    Set if the file is to be  write-checked.
                         All   write   operations  on  the  file,
                         including  modifications  of  the   file
                         header(s),  will  be  performed  with  a
                         write,  read-compare  to   assure   data
                         integrity.

               UC.NID    Set if incremental dump (backup)  is  to
                         be disabled for this file.


     Files-11 On-Disk Structure                           Page 13


               UC.WBC    Set if the  file  is  to  be  write-back
                         cached;   i.e.,  if  a cache is used for
                         the file data, data written by a user is
                         only written back to the disk when is it
                         removed  from  the  cache.   Clear   for
                         write-through cache operation.

               The second byte of the file characteristics  words
               is  historically  known  as  the system controlled
               file characteristics.  It contains  the  following
               flag bits, defined as referenced within the byte:

               SC.MDL    Set if the file is  marked  for  delete.
                         If  this bit is set, further accesses to
                         the file are denied, and the  file  will
                         be  physically deleted when no users are
                         accessing it.

               SC.BAD    Set if there is a bad data block in  the
                         file.  This bit is as yet unimplemented.
                         It is intended  for  dynamic  bad  block
                         handling.

               SC.DIR    Set if the file is a directory.

               SC.ACL    Set if an access control list exists for
                         this file.

               SC.CHK    This bit  is  set  if  the  file  header
                         checksum  was not computed.  If this bit
                         is set, the checksum word  must  contain
                         the  octal value 125252.  This "feature"
                         is for small systems that cannot  afford
                         the  millisecond or two that it takes to
                         compute the header checksum;  its use is
                         strongly discouraged.




     3.5.2.15  2 Bytes   (not used)




     3.5.2.16  H.USE - 1 Byte      Map Words in Use

               This byte contains a count of the  number  of  map
               area words currently in use.


     Files-11 On-Disk Structure                           Page 14


     3.5.2.17  H.PRIV - 1 Byte     Accessor Privilege Level

               This byte defines the lowest  privilege  level  at
               which  an  accessor must be running in order to be
               allowed access to the file.  Each privilege  level
               is  a  two bit integer;  zero refers to the lowest
               privilege and 3 is the highest.  Privilege  levels
               may  be  assigned  separately  to  the  basic file
               access modes, using the following bit assigment in
               this byte:

               Read      Bits 0 - 1
               Write     Bits 2 - 3
               Execute   Bits 4 - 5
               Delete    Bits 6 - 7

               An operating system should map its privilege level
               coding  onto  this  code  in  the smoothest manner
               possible.  For example, the four access  modes  of
               VMS, user, supervisor, exec, and kernel, are coded
               as 0 through 3, respectively.  A  system  such  as
               RSX-11M  which has only two levels (privileged and
               non-privileged), should map the two onto 3 and  0,
               respectively.

               Privilege levels are meant to  confine  access  to
               the  contents  of  files  to  suitably trustworthy
               procedures.  Thus, a  user  might  be  denied  the
               ability to write a record structured file directly
               (on a virtual block basis), but would be permitted
               to  write  the  file  through  the record manager,
               which would be suitably privileged.

               For a record structured file, an  appropriate  set
               of privilege levels would be 0,2,0,0, expressed in
               the order read - write - execute - delete.



     3.5.2.18  H.FOWN - 4 Bytes    File Owner UIC
               H.PROG =  H.FOWN+0  Programmer (Member) Number
               H.PROJ =  H.FOWN+2  Project (Group) Number

               These words contain the binary user identification
               code  (UIC)  of  the  owner of the file.  The file
               owner is usually (but not necessarily) the creator
               of the file.


     Files-11 On-Disk Structure                           Page 15


     3.5.2.19  H.FPRO - 2 Bytes    File Protection Code

               This word controls what access all  users  in  the
               system  may have to the file.  Accessors of a file
               are  categorized  according  to  the  relationship
               between the UIC of the accessor and the UIC of the
               owner of the file.  Each category is controlled by
               a  four  bit  field  in  the protection word.  The
               category of the accessor is selected as follows:

               System    Bits 0 - 3

                         The  accessor  is  subject   to   system
                         protection  if the project number of the
                         UIC under which  he  is  running  is  10
                         octal or less.

               Owner     Bits 4 - 7

                         The  accessor  is   subject   to   owner
                         protection  if the UIC under which he is
                         running exactly matches the  file  owner
                         UIC.

               Group     Bits 8 - 11

                         The  accessor  is   subject   to   group
                         protection  if the project number of his
                         UIC matches the project  number  of  the
                         file owner UIC.

               World     Bits 12 - 15

                         The  accessor  is   subject   to   world
                         protection  if  he does not fit into any
                         of the above categories.

               Four types of  access  are  defined  in  Files-11:
               read,  write,  execute, and delete.  Each four bit
               field in the protection word  is  bit  encoded  to
               permit  or  deny any combination of the four types
               of access to that category of accessors.   Setting
               a bit denies that type of access to that category.
               The bits are  defined  as  follows  (these  values
               apply to a right-justified protection field):

               FP.RDV    Deny read access
               FP.WRV    Deny write access
               FP.EXE    Deny execute access
               FP.DEL    Deny delete access

               When a user attempts to access a file,  protection
               checks  are  performed  in  all  the categories to
               which he is eligible, in the order system -  owner
               -  group  -  world.  The user is granted access to


     Files-11 On-Disk Structure                           Page 16


               the file if any of the categories to which  he  is
               eligible grants him access.

               Recommended defaults for file  protection  for  an
               "open  shop"  system are [RWD,RWD,RW,R] (expressed
               in the order of system - owner -  group  -  world,
               where  each  letter  denotes  the presence of that
               permission).   Observe  that  only   files   which
               contain  executable  programs  should have execute
               protection turned on.  Recommended defaults for  a
               "closed shop" system are [RWD,RWD,R,].



     3.5.2.20  H.BFNU - 6 Bytes    File header back link

               The back link is the file ID of the directory file
               containing  the  primary  directory  entry  of the
               file.  If the file header is an extension  header,
               the  back link contains the file ID of the primary
               header.



     3.5.2.21  4 Bytes   (not used)



     3.5.2.22  S.HDHD - 74 Bytes   Size of Header Area

               This symbol  represents  the  total  size  of  the
               header area containing all of the above entries.



     3.5.3  Ident Area Description -

     The ident area  of  the  file  header  begins  at  the  word
     indicated   by   H.IDOF.   It  contains  identification  and
     accounting data about the file.



     3.5.3.1  I.FNAM - 20 Bytes    File Name

               This area contains the name of the file in  ASCII.
               A  dot  separates  name from type, and a semicolon
               separates type  from  version;   both  are  always
               present.  If the name is shorter than 20 bytes, it
               is padded with blanks;  if it  is  longer,  it  is
               truncated.


     Files-11 On-Disk Structure                           Page 17


     3.5.3.2  I.RVNO - 2 Bytes     Revision Number

               This word contains the revision count of the  file
               in  binary.   The  revision count is the number of
               times the file has been accessed for write.



     3.5.3.3  I.CRDT - 8 Bytes     Creation Date and Time

               These eight bytes contain the  date  and  time  at
               which the file was created.  The time is expressed
               in the standard internal time format, which  is  a
               64 bit integer representing tenths of microseconds
               elapsed since midnight, 17 November 1858.



     3.5.3.4  I.RVDT - 8 Bytes     Revision Date and Time

               The revision time is the time at  which  the  file
               was  last  deaccessed  after  being  accessed  for
               write.  It is expressed as the same format as  the
               creation time above.



     3.5.3.5  I.EXDT - 8 Bytes     Expiration Date and Time

               These eight bytes contain the  date  and  time  at
               which  the  file  becomes  eligible to be deleted.
               The format is the same as that of the creation and
               revision times above.



     3.5.3.6  I.BKDT - 8 Bytes     Backup Date and Time

               These eight bytes contain the  date  and  time  at
               which  the file was last backed up.  The format is
               the same as the other dates and times.



     3.5.3.7  S.IDHD - 36 Bytes    Size of Ident Area

               This symbol represents the size of the ident  area
               containing all of the above entries.


     Files-11 On-Disk Structure                           Page 18


     3.5.4  Map Area Description -

     The map area of the file header starts at the word indicated
     by H.MPOF.  It contains the information necessary to map the
     virtual blocks of the file to  the  logical  blocks  of  the
     volume.   This  area  contains  the  retrieval pointers that
     actually map the virtual blocks of the file to  the  logical
     blocks  of  the  volume.  Each retrieval pointer describes a
     consecutively numbered group  of  logical  blocks  which  is
     allocated  to the file.  The count field contains the binary
     value n to represent a group of  n+1  logical  blocks.   The
     logical block number field contains the logical block number
     of  the  first  logical  block  in  the  group.   Thus  each
     retrieval  pointer  maps  virtual  blocks j through j+n into
     logical blocks k through k+n, respectively, where j  is  the
     total  number  plus one of virtual blocks represented by all
     preceding retrieval  pointers  in  this  and  all  preceding
     headers  of  the file, n is the value contained in the count
     field, and k is the value contained  in  the  logical  block
     number  field.   Observe  that  j, k, and n+1 must always be
     integer multiples of v, the volume cluster factor.

     If the LBN field of a retrieval pointer  contains  all  ones
     (i.e.,  points  to  block  2**22-1  or  2**32-1),  then that
     retrieval pointer represents an  unallocated  portion  of  a
     sparse  file.   The  count  field  describes  the  number of
     unallocated virtual blocks in the normal manner.

     There are four formats of retrieval pointers, identified  by
     escape  codes.   The  different  formats  may  be intermixed
     within a file header.

     Format 0 - two bytes

                     |--|------------------|
                     |00|    Placement     |
                     |--|------------------|

     Retrieval pointer format 0 is used to store  placement  data
     in  the  file  header.   It  describes the placement control
     supplied with the  allocation  that  created  the  following
     retrieval  pointer,  allowing  the placement of a file to be
     replicated  when  the  file  is  copied  or  backed  up  and
     restored.   The  coding  of the placement data is at present
     undefined.  Format 0 is identified by bits 15 and 14 of  the
     first word being set to 00.

     Format 1 - four bytes.

                     |--|-------|----------|
                     |01| High  |  Count   |
                     |--|-     -|----------|
                     |    Low Order LBN    |
                     |---------------------|


     Files-11 On-Disk Structure                           Page 19


     Retrieval pointer format 1 provides an 8 bit count field and
     a 22 bit LBN field.  It is therefore capable of representing
     a group of up to 256 blocks on a volume up to  2**22  blocks
     in  size.   Format  1 is identified by bits 15 and 14 of the
     first word being set to 01.

     Format 2 - six bytes.

                     |--|------------------|
                     |10|      Count       |
                     |--|------------------|
                     |                     |
                     |-        LBN        -|
                     |                     |
                     |---------------------|

     Retrieval pointer format 2 provides a 14 bit count field and
     a  32  bit LBN field.  It is capable of representing a group
     of up to 16384 blocks on a volume  up  to  2**32  blocks  in
     size.  Format 2 is identified by bits 15 and 14 of the first
     word being set to 10.

     Format 3 - eight bytes.

                     |--|------------------|
                     |11|       High       |
                     |--|-                -|
                     |   Low Order Count   |
                     |---------------------|
                     |                     |
                     |-        LBN        -|
                     |                     |
                     |---------------------|

     Retrieval pointer format 3 provides a 30 bit count field and
     a  32 bit LBN field.  It is capable of describing a group of
     up to 2**30 blocks on a volume up to 2**32 blocks  in  size.
     Format  3  is identified by bits 15 and 14 of the first word
     being set to 11.





     3.5.5  Access Control List - (Reserved  for  future  use  by
     DEC).



     3.5.6  Reserved Area -

     The reserved area of the file  header  starts  at  the  word
     indicated  by  the  byte  H.RSOF.   This area is not used by
     standard Files-11 file managers, but is available for use by
     CSS and special applications.


     Files-11 On-Disk Structure                           Page 20


     3.5.7  End Checksum Description -

     The header check sum occupies the last two bytes of the file
     header.   It is verified every time a header is read, and is
     recomputed every time a  header  is  written.   If  the  bit
     SC.CHK  is set in the system controlled characteristics word
     H.SCHA, then the checksum has not  been  computed,  and  the
     checksum word must contain the octal value 125252.



     3.5.7.1  H.CKSM - 2 Bytes     Block Checksum

               This word is a simple  additive  checksum  of  all
               other  words  in the block.  It is computed by the
               following PDP-11 routine or its equivalent:

                         MOV       Header-address,R0
                         CLR       R1
                         MOV       #255.,R2
               10$:      ADD       (R0)+,R1
                         SOB       R2,10$
                         MOV       R1,(R0)



     3.6  File Header Layout

     The following is a graphical layout of  the  fields  in  the
     file header.


     Files-11 On-Disk Structure                           Page 21


     Header Area

               |-------------------|-------------------|
     H.MPOF    |  Map Area Offset  | Ident Area Offset |   H.IDOF
               |-------------------|-------------------|
     H.RSOF    | Resv. Area Offset |  ACL Area Offset  |   H.ACOF
               |-------------------|-------------------|
               |          File Segment Number          |   H.FSEG
               |---------------------------------------|
               |         File Structure Level          |   H.FLEV
               |---------------------------------------|
               |              File Number              |   H.FNUM
               |---------------------------------------|
               |         File Sequence Number          |   H.FSEQ
               |---------------------------------------|
               |        Relative Volume Number         |   H.FRVN
               |---------------------------------------|
               |         Extension File Number         |   H.EFNU
               |---------------------------------------|
               |       Extension File Seq. Num.        |   H.EFSQ
               |---------------------------------------|
               |             Extension RVN             |   H.ERVN
               |---------------------------------------|
               |                                       |   H.UFAT
               |                                       |    
               |                                       |    
               |          User Attribute Area          |    
               |                                       |    
               |                                       |    
               |                                       |    
               |---------------------------------------|   H.FCHA
     H.SCHA    |                                       |   H.UCHA
               |--        File Characteristics       --|
               |                                       |
               |---------------------------------------|
               |               (not used)              |
               |-------------------|-------------------|
     H.PRIV    |    Access Level   | Map Words in Use  |   H.USE
               |-------------------|-------------------|   H.FOWN
               |                                       |   H.PROG
               |--          File Owner UIC           --|
               |                                       |   H.PROJ
               |---------------------------------------|
               |            File Protection            |   H.FPRO
               |---------------------------------------|
               |                                       |   H.BFNU
               |--                                   --|
               |         File Header Back Link         |
               |--                                   --|
               |                                       |    
               |---------------------------------------|
               |                                       |    
               |--             (not used)            --|
               |                                       |
               |---------------------------------------|   S.HDHD


     Files-11 On-Disk Structure                           Page 22


     Ident Area

               |---------------------------------------|
               |                                       |   I.FNAM
               |--                                   --|
               |                                       |    
               |--                                   --|
               |               File Name               |    
               |--                                   --|
               |                                       |    
               |--                                   --|
               |                                       |    
               |---------------------------------------|
               |            Revision Number            |   I.RVNO
               |---------------------------------------|
               |                                       |   I.CRDT
               |--                                   --|
               |                                       |   
               |--           Creation Date           --|
               |                                       |    
               |--                                   --|
               |                                       |   
               |---------------------------------------|
               |                                       |   I.RVDT
               |--                                   --|
               |                                       |   
               |--           Revision Date           --|
               |                                       |    
               |--                                   --|
               |                                       |   
               |---------------------------------------|
               |                                       |   I.EXDT
               |--                                   --|
               |                                       |   
               |--          Expiration Date          --|
               |                                       |    
               |--                                   --|
               |                                       |   
               |---------------------------------------|   
               |                                       |   I.BKDT
               |--                                   --|
               |                                       |   
               |--            Backup Date            --|
               |                                       |    
               |--                                   --|
               |                                       |   
               |---------------------------------------|   S.IDHD


     Files-11 On-Disk Structure                           Page 23


     Map, ACL, and Reserved Areas

               |---------------------------------------|
               |                                       |
               |                                       |    
               |                                       |    
               |          Retrieval Pointers           |    
               |                                       |    
               |                                       |    
               |                                       |    
               |---------------------------------------|
               |                                       |    
               |                                       |    
               |                                       |    
               |          Access control List          |    
               |                                       |    
               |                                       |    
               |                                       |    
               |---------------------------------------|
               |                                       |   
               |                                       |   
               |                                       |   
               |             Reserved Area             |   
               |                                       |   
               |                                       |   
               |                                       |   
               |---------------------------------------|
               |         File Header Checksum          |   H.CKSM
               |---------------------------------------|



     4.0  DIRECTORIES

     Files-11 provides directories to allow the  organization  of
     files  in a meaningful way.  While the File ID is sufficient
     to locate a file uniquely on a  volume  set,  it  is  hardly
     mnemonic.   Directories  are  files  whose  function  is  to
     associate symbolic names with File ID's.



     4.1  Directory Heirarchies

     Since directories are  files  with  no  special  attributes,
     directories  may  list  files  that are in turn directories.
     Thus  the  user  may  construct  directory  heirarchies   of
     arbitrary  depth and complexity to structure his files as he
     pleases.


     Files-11 On-Disk Structure                           Page 24


     4.1.1  Two Level Directory Heirarchy -

     Implementations of Files-11 on existing PDP-11  systems  all
     support  a  two  level  directory heirarchy which is tied in
     with the user  identification  mechanism  of  the  operating
     system.   Each  UIC known to the system is associated with a
     user file directory (UFD).  References to files that do  not     ____ ____ _________
     specify  a  directory  are  generally  defaulted  to the UFD
     associated with the user's UIC.  The syntax used to refer to
     UIC's  is the same as that used to identify the directory in
     a file name string.  The construct "[n,m]" is used to  refer
     to group number n, member number m.  All UFD's are listed in
     the volume's master file directory (MFD) under a  file  name
     constructed from the directory string.  (See section 5.0 for
     a description of the MFD.) A string  of  "[n,m]"  associates
     with  a  directory name of "nnnmmm.DIR;1", where nnn and mmm
     are n and m padded out to three  digits  each  with  leading
     zeroes.  Note that all number conversions are done in octal.

     Two  points  should  be  noted  here.   The  UFD   structure
     described  here  is  not  intrinsically part of the Files-11
     on-disk structure;  rather, it is  a  convenient  cataloging
     system applied by various operating systems.  Also, there is
     no hard and fast relationship between the  owner  UIC  of  a
     file  and  the  UFD  in which it is listed.  Generally, they
     will correspond, but not necessarily.



     4.1.2  Multi-level Directory Heirarchy -

     New implementations of Files-11 use a multi-level  directory
     heirarchy,  where  the first level below the MFD is referred
     to as the user file directory (UFD)  and  subsequent  levels
     are  referred to as sub file directories (SFD's).  Users are
     identified at the command level by ASCII names;  the  system
     translates  user  names  into  UIC's  internally.   Thus MFD
     entries  will  correspond  to  the  ASCII  user  names.    A
     directory     specifier     will     have     the     format
     "[name1.name2.name3. ... ]".   Each   name   in   the   list
     translates to a directory file name of the form "name.DIR;1"
     and is searched for in the current directory level.

     Observe that the directory  protocol  is  not  tied  to  the
     structure  level  of the disk.  Thus new systems will always
     have to handle the "[n,m]" construct, which maps  to  a  UFD
     name  of  "nnnmmm.DIR;1"  and  provides  only  two levels of
     directory.  Old systems will not be able to handle volumes


     Files-11 On-Disk Structure                           Page 25


     4.1.3  Multi-Volume Directory Structure -

     In a volume set, the MFD for the all of the  user  files  on
     the volume set is the MFD of relative volume 1.  Its entries
     can point to UFD's located on any volume in the  set,  whose
     entries  can  in  turn point to files and sub directories on
     any volume in the set.  The MFD's of the  remaining  volumes
     in the set only list the reserved files on each volume.

     The assignment of volumes to specific directories and  files
     is not covered by this specification.  Different systems may
     implement different policies to trade off  factors  such  as
     performance,  reliability, and separability.  Optimizing for
     performance, for example, usually means scattering the files
     as  randomly  as  possible across the volume set to make the
     most use of the  available  multiple  positioners.   Maximum
     separability  (the  ability  to make use of only part of the
     volume set) is achieved by locating files on the same volume
     as  their directories, and possibly entering the directories
     in the MFD's of the volumes on which they reside.



     4.2  Directory Structure

     A directory is a contiguous file, organized as a  sequential
     file  with  variable  length records, with the attribute set
     that records do not cross block boundaries, and no  carriage
     control attributes.  Directory entries within each block are
     packed together to conform to  the  variable  length  record
     format;  a -1 byte count signals the end of records for that
     block.  (See section 6 for a discussion of record  formats.)
     The  entries  in  a  directory  are  sorted  alphabetically,
     permitting the use of an optimized  search.   Entries  which
     are multiple versions of the same name and type are arranged
     in order of decreasing version number  to  optimize  version
     related  operations.   Each directory record consists of the
     following:


               |---------------------------------------|
               |           Record Byte Count           |
               |---------------------------------------|
               |             Version Limit             |
               |-------------------|-------------------|
               |  Name Byte Count  |       Flags       |
               |-------------------|-------------------|
               |                                       |
               |                                       |
               |                                       |
               |           File Name String            |
               |                                       |
               |                                       |
               |                                       |
               |---------------------------------------|


     Files-11 On-Disk Structure                           Page 26


               |                                       |
               |                                       |
               |              Value Field              |
               |                                       |
               |                                       |
               |---------------------------------------|



     Count     This two byte field is  the  standard  byte  count
               field of a variable length record.

     Limit     This word contains the maximum number of  versions
               that  are  to  be retained for this name and type.
               An attempt to enter more versions than  the  limit
               will  result  in  the deletion of the least recent
               version, or an error return, at  the  implementing
               system's option.

     Flags     This byte contains the type code of the  directory
               entry  and  assorted  flag bits.  The type code is
               contained in the three low bits of the flags byte.
               It is one of the following values:

               DV.FID              The value field is a  list  of
                         version numbers and 48 bit File Id's.

               The following flag bits are defined:

               DF.PRV              Set if the preceding directory
                         record  contains  the same name and type
                         as this one.
               DF.NXV              Set  if  the  next   directory
                         record  contains  the same name and type
                         as this one.

     Name      This field contains the  file  name  and  type  in
               ASCII,  separated  by a a dot.  The dot is present
               even if either name, or type, or both,  are  null.
               Only  upper case alphabetic and numeric characters
               may be present in  the  name  and  type.   If  the
               length  of  the  name  is odd, it is padded with a
               single null.

     Value     This field contains the "value" of  the  directory
               entry;  i.e., the information returned to the user
               from a lookup operation.  If the directory  record
               is  a File ID list (the type field is DV.FID), the
               value field is  a  list  of  version  numbers  and
               corresponding  file  ID's, appearing in descending
               order by version number.  The number of entries in
               the list is deduced from the record byte count.




     Files-11 On-Disk Structure                           Page 27


                    |---------------------------------------|
                    |            Version Number             |
                    |---------------------------------------|
                    |                                       |
                    |--                                   --|
                    |                File ID                |
                    |--                                   --|
                    |                                       |
                    |---------------------------------------|
                    |            Version Number             |
                    |---------------------------------------|
                    |                                       |
                    |--                                   --|
                    |                File ID                |
                    |--                                   --|
                    |                                       |
                    |---------------------------------------|
                    |                                       |
                                        :
                                        :
                                        :
                                        :
                                        :
                    |                                       |
                    |---------------------------------------|
                    |            Version Number             |
                    |---------------------------------------|
                    |                                       |
                    |--                                   --|
                    |                File ID                |
                    |--                                   --|
                    |                                       |
                    |---------------------------------------|


     Version   This word  contains  the  version  number  of  the
               directory  entry  in binary.  Version numbers must
               lie in the range from 1 to 32767.

     File ID   These  three  words  are  the  file  ID  that  the
               directory entry points to.



     5.0  RESERVED FILES

     Clearly any file system must maintain some data structure on
     the  medium  which is used to control the file organization.
     In Files-11 this data is kept in several files.  These files
     are  created  when  a  new  volume is initialized.  They are
     unique in that their File ID's are known  constants.   Note,
     however, that the relative volume number used when accessing
     one of these files depends  upon  the  context.   The  exact
     number  of  these  files  which  is  present on a particular
     volume may vary;  however, at least five  must  be  present.


     Files-11 On-Disk Structure                           Page 28


     All  of these files are non-deletable.  These files have the
     following uses:

     File ID 1,1 is the index file.  The index file is  the  root                        _____ ____
     of  the entire Files-11 structure.  It contains the volume's
     bootstrap block  and  the  home  block,  which  is  used  to
     identify  the  volume  and  locate  the  rest  of  the  file
     structure.  The index file also contains  all  of  the  file
     headers  for  the  volume,  and  a  bitmap  to  control  the
     allocation of file headers.

     File ID 2,2 is the storage  bitmap  file.   It  is  used  to                        _______  ______  ____
     control the allocation of logical blocks on the volume.

     File ID 3,3 is the bad block file.  It is a file  containing                        ___ _____ ____
     all of the known bad blocks on the volume.

     File ID 4,4 is the volume master file  directory  (or  MFD).                               ______ ____  _________       ___
     It  forms the root of the volume's directory structure.  The
     MFD lists  the  five  known  files,  all  first  level  user
     directories,  and  whatever  other files the user chooses to
     enter.

     File ID 5,5 is the system  core  image  file.   Its  use  is                                ____  _____  ____
     operating system dependent;  its basic purpose is to provide
     a file of known File ID for the use of the operating system.

     File ID 6,6 is the volume set list file.  If this volume  is                        ______ ___ ____ ____
     relative  volume  one  of a tightly coupled volume set, this
     file contains a list of the labels of all the volumes in the
     set.

     File ID 7,7 is the  standard  continuation  file.   If  this                         ________  ____________  ____
     volume  is  part  of a loosely coupled volume set, this file
     contains  the  first  segment  of   the   portion   of   the
     multi-volume file that resides on this volume.

     File ID 8,8 is the backup journal file.  This file  is  used                        ______ _______ ____
     to log and control the use of an incremental backup system.

     File ID 9,9 is the pending bad block log  file.   This  file                        _______ ___ _____ ___  ____
     contains  a  list of suspected bad blocks on the volume that
     have not yet been turned over to the bad block file.

     More File ID's may be reserved in the future;  users  should
     not  make  any  assumptions about the values of user created
     File ID's.


     Files-11 On-Disk Structure                           Page 29


     5.1  Index File

     The index file is File ID 1,1.  It is listed in the  MFD  as
     INDEXF.SYS;1.   The  index  file is the root of the Files-11
     structure in that it provides the means  for  identification
     and  initial  access  to a Files-11 volume, and contains the
     access data for all files on the volume (including  itself).
     This file has the FCS record format of 512 byte fixed length
     records, with no carriage control.  (See  section  6  for  a
     description of the FCS file format.)



     5.1.1  Bootstrap Block -

     Virtual block 1 of the  index  file  is  the  volume's  boot                                                             ____
     block.  It is almost always mapped to logical block 0 of the     _____
     volume.  If the volume is the system device of an  operating
     system,   the   boot  block  contains  an  operating  system
     dependent program which  reads  the  operating  system  into
     memory  when  the  boot  block  is  read  and  executed by a
     machine's hardware bootstrap.  If the volume is not a system
     device, the boot block contains a small program that outputs
     a message on the system console to inform  the  operator  to
     that  effect.   If  block  0  of  a  volume  is  bad,  it is
     permissible to map virtual block 1 of the index file to some
     other block.  In this case, obviously, volume cannot be used
     as a system volume.



     5.1.2  Home Block -

     Virtual block 2 of the  index  file  is  the  volume's  home                                                             ____
     block.   The  purpose  of  the home block is to identify the     _____
     volume as Files-11, establish the specific identity  of  the
     volume,  and  serve  as the ground zero entry point into the
     volume's file structure.  The home block is recognized as  a
     home  block by the presence of checksums in known places and
     by the presence of predictable values in certain locations.

     The home block is located on the first  good  block  of  the
     home  block  search sequence.  The search sequence is of the
     form

             1 + n * delta, n = 0, 1, 2, 3, 4 ......

     The home block search delta is computed from the geometry of
     the  volume  such  that,  if the volume is viewed as a three
     dimensional  space,  the   search   sequence   will   travel
     approximately  down  the  body diagonal of the space.  Since
     volume failures tend to occurr across  one  dimension,  this
     minimizes  the  chance  of  a single failure destroying both
     home blocks of the volume.  The  search  delta  is  computed
     from  the  volume  geometry,  expressed  in  sectors, tracks


     Files-11 On-Disk Structure                           Page 30


     (surfaces), and cylinders, according to the following rules,
     to  handle  the  cases  where  one  or two dimensions of the
     volume have a size of 1.

               Geometry:     Delta

               s x 1 x 1:    1
               1 x t x 1:    1
               1 x 1 x c:    1

               s x t x 1:    s+1
               s x 1 x c:    s+1
               1 x t x c:    t+1

               s x t x c:    (t+1)*s+1

     In most cases, the home block is located on LBN 1.



     5.1.3  Cluster Filler -

     If v, the cluster factor of the volume, is greater  than  1,
     then  the  next v*2-2 blocks of the index file are copies of
     the home block used to fill out the first  two  clusters  of
     the index file.  Note that, for cluster factors greater than
     1, this results in a wasted disk cluster.   The  benefit  of
     this technique is a much simpler rule for finding the VBN of
     interesting parts of the index file.



     5.1.4  Backup Home Block -

     The backup home block is a second copy  of  the  home  block
     located  farther  down  the  home block search sequence.  It
     permits the volume to be used even if the primary home block
     is destroyed.

     In general, the backup home block should be allocated on the
     second  good  block  of  the search sequence.  If it is not,
     then all preceding  blocks  on  the  sequence  must  not  be
     available  for allocation.  This is to prevent the situation
     of a malicious user constructing a counterfeit  index  file,
     which would be used if the primary home block ever went bad.

     The cluster which contains the backup home block  is  mapped
     into  the  index  file  as virtual blocks v*2+1 through v*3,
     where v is the volume  cluster  factor.   Observe  that  the
     backup  home  block  may  be  located  anywhere  within this
     cluster, because there is  no  hard  and  fast  relationship
     between  the  cluster  factor  and  the  volume's  track and
     cylinder boundaries.  The entire cluster is therefore filled
     out with copies of the home block.


     Files-11 On-Disk Structure                           Page 31


     5.1.5  Backup Index File Header -

     The next cluster of the index file contains a backup copy of
     the  index  file  header,  so that data on the volume can be
     recovered if the index file header goes  bad.   The  cluster
     occupies  virtual  blocks  v*3+1 through v*4, where v is the
     volume cluster factor.  The LBN of  the  backup  index  file
     header  is stored in location H.IHLB in the home block.  The
     backup index file header occupies the first  block  of  this
     cluster;   the  remaining  blocks  are  not  used  and their
     contents are undefined.



     5.1.6  Index File Bitmap -

     The index file bitmap is used to control the  allocation  of         _____ ____ ______
     file  numbers  (and hence file headers).  It is simply a bit
     string of length n, where n is the maximum number  of  files
     permitted  on  the volume (contained in offset H.FMAX in the
     home block).  The bitmap spans over as  many  blocks  as  is
     necessary  to  hold it, i.e., max number of files divided by
     4096 and rounded up.  The number of blocks in the bitmap  is
     contained in offset H.IBSZ of the home block.

     The bits in the index file bitmap are numbered  sequentially
     from  0  to  n-1  in the obvious manner, i.e., from right to
     left in each byte, and in order of increasing byte  address.
     Bit  j  is used to represent file number j+1:  if the bit is
     1, then that file number is in use;  if the bit is  0,  then
     that  file  number  is  not  in use and may be assigned to a
     newly created file.

     The index file bitmap starts at virtual block v*4+1  of  the
     index  file  and continues through VBN v*4+m, where m is the
     number of blocks in the bitmap, and v  is  the  storage  map
     cluster   factor.   It  is  located  at  the  logical  block
     indicated by offset H.IBLB in the home block.



     5.1.7  File Headers -

     The rest of the index file contains all the file headers for
     the  volume.   The first 16 file headers (for file numbers 1
     to 16) are logically contiguous with the index  file  bitmap
     to  facilitate  their  location;   the rest may be allocated
     wherever the file system sees fit.  Thus the first  16  file
     headers  may  be located from data in the home block (H.IBSZ
     and H.IBLB) while the  rest  must  be  located  through  the
     mapping  data in the index file header.  The file header for
     file number n is located at virtual block v*4+m+n  (where  m
     is  the  number of blocks in the index file bitmap, and v is
     the storage map cluster factor).


     Files-11 On-Disk Structure                           Page 32


     The FCS end of file mark for the index file  is  located  at
     the  last  file header ever used.  All header blocks located
     before the EOF are subject to validation when used to create
     a  new  file.  If the block contains garbage, the new header
     is assigned a file sequence number of 1, being the first use
     of  this header block.  If the block contains a deleted file
     header, the new header is assigned  a  sequence  number  one
     higher  than  the  one  contained  in  the  block.   A block
     containing a valid file header must never be used to  create
     a  new  file,  even  if  it is marked free in the index file
     bitmap.  This prevents files from being  lost  if  bits  are
     dropped in the bitmap.  Index file blocks beyond the EOF are
     assumed to contain garbage for the purpose of  creating  new
     file headers.



     5.1.8  Index File Layout -

     The following is a sketch of the blocks in the  index  file.
     Observe that this illustration assumes a storage map cluster
     factor greater than 2.


               |-------------------|---
               |                   |   \
               |       Boot        |    |  
               |       Block       |    |  
               |                   |    |  
               |-------------------|    |  
               |                   |    |  
               |       Home        |    |  
               |       Block       |    | Cluster 1
               |                   |    |
               |-------------------|    |
               |       More        |    |
               |       Home        |    |
               |      Blocks       |    |
               |         :         |    |
               |         :         |    |
               |         :         |   /
               |-------------------|---
               |                   |   \ 
               |       More        |    |
               |       Home        |    |
               |      Blocks       |    | Cluster 2
               |         :         |    |
               |         :         |    |
               |         :         |   /
               |-------------------|---
               |      Backup       |   \ 
               |       Home        |    |
               |       Block       |    |
               |                   |    |
               |-------------------|    |


     Files-11 On-Disk Structure                           Page 33


               |       More        |    | Cluster 3
               |       Home        |    |
               |      Blocks       |    |
               |         :         |    |
               |         :         |    |
               |         :         |   / 
               |-------------------|---
               |      Backup       |   \ 
               |       Index       |    |
               |       File        |    |
               |      Header       |    |
               |-------------------|    |
               |                   |    | Cluster 4
               |                   |    |
               |       (not)       |    |
               |      (used)       |    |
               |                   |    |
               |                   |   /
               |-------------------|---
               |                   |   \
               |       Index       |    |
               |       File        |    |
               |      Bitmap       |    |
               |                   |    |
               |                   |    |
               |-------------------|    | Contiguous
               |                   |    |
               |        16         |    |
               |       File        |    |
               |      Headers      |    |
               |                   |    |
               |                   |   /
               |-------------------|---
               |                   |
               |                   |
               |                   |
               |       Lots        |
               |       More        |
               |       File        |
               |      Headers      |
               |                   |
               |                   |
               |                   |
               |                   |
               |-------------------|



     5.1.9  Home Block Details -

     The following is a detailed description of the  home  block.
     Note  that all copies of the volume's home block contain the
     same data, with the exception of the  cells  containing  the
     block's VBN and LBN.


     Files-11 On-Disk Structure                           Page 34


     Items contained in the home block are identified by symbolic
     offsets in the same manner as items in the file header.  The
     symbols may be defined  in  assembly  language  programs  by
     calling and invoking the macro HMBL2$, which may be found in
     the macro library of  any  system  that  supports  Files-11.
     Alternatively,   one   may   find  the  macro  in  the  file
     F11MAC.MAC, which is available from the author.





     5.1.9.1  H.HBLB - 4 Bytes     Home Block LBN

               This double word contains the logical block number
               of this particular copy of the home block.



     5.1.9.2  H.AHLB - 4 Bytes     Alternate Home Block LBN

               This double word contains the LBN of the  volume's
               secondary  home  block.   One  may determine, when
               scanning the  home  block  sequence,  whether  the
               block  read is the primary or secondary home block
               by comparing H.HBLB and H.AHLB.  This  value  must
               be non-zero for a valid home block.



     5.1.9.3  H.IHLB - 4 Bytes     Backup Index File Header LBN

               This double word contains  the  logical  block  on
               which  the  backup  index  file header is located.
               This value must  be  non-zero  for  a  valid  home
               block.



     5.1.9.4  H.VLEV - 2 Bytes     Structure Level and Version

               The volume structure level and version is used  to
               identify  different  versions  of Files-11 as they
               affect the structure of all parts  of  the  volume
               except  the  file  header.   This  permits upwards
               compatibility  of  file  structures  as   Files-11
               evolves,   in   that   the  structure  level  word
               identifies the version of  Files-11  that  created
               this  particular  volume.  This document describes
               structure level 2 of Files-11.  The high  byte  of
               H.VLEV  must  contain  the  value 2.  The low byte
               contains the version number, which must be greater
               or  equal  to  1.   The  version  number  will  be
               incremented whenever compatible additions are made
               to  the  Files-11  structure  that  may  be safely


     Files-11 On-Disk Structure                           Page 35


               ignored by an old  version  of  the  file  system.
               This  document  describes  version  1 of structure
               level 2.



     5.1.9.5  H.SBCL - 2 Bytes     Storage Bitmap Cluster Factor

               This word contains the cluster factor used in  the
               storage  bitmap  file.   The cluster factor is the
               number of blocks represented by each  bit  in  the
               storage bitmap.  This value is also referred to as
               the volume cluster factor.



     5.1.9.6  H.HBVB - 2 Bytes     Home Block VBN

               This word contains the  virtual  block  that  this
               particular  copy of the home block occupies in the
               index file.  This value must  be  non-zero  for  a
               valid home block.



     5.1.9.7  H.AHVB - 2 Bytes     Backup Home Block VBN

               This word contains the virtual block  number  that
               the  cluster  containing  the secondary home block
               occupies in the index file.  The contents of  this
               word  is v*2+1, where v is the storage map cluster
               factor.



     5.1.9.8  H.IHVB - 2 Bytes     Backup Index File Header VBN

               This word contains the virtual block  number  that
               the backup index file header occupies in the index
               file.  The contents of this word is v*3+1, where v
               is the storage map cluster factor.



     5.1.9.9  H.IBVB - 2 Bytes     Index File Bitmap VBN

               This word  contains  the  starting  virtual  block
               number  of the index file bitmap.  The contents of
               this word is the  value  v*4+1,  where  v  is  the
               storage map cluster factor.


     Files-11 On-Disk Structure                           Page 36


     5.1.9.10  H.IBLB - 4 Bytes    Index File Bitmap LBN

               This double word  contains  the  starting  logical
               block  address of the index file bitmap.  Once the
               home block of a volume has been found, it is  this
               value  that  provides  access  to  the rest of the
               index file and to the volume.  This value must  be
               non-zero for a valid home block.



     5.1.9.11  H.FMAX - 4 Bytes    Maximum Number of Files

               This double word contains the  maximum  number  of
               files  that  may  be  present on the volume at any
               time.   This  value  must  be  greater  than   the
               contents of H.RSVF for the home block to be valid.
               If the maximum number of files is less than 65536,
               then the third word of File ID's referencing files
               on this  volume  is  simply  the  relative  volume
               number, and the volume set of which this volume is
               a member may contain up to 65535 volumes.  If  the
               maximum  number  of files is greater than or equal
               to 65536, however, then the high byte of the third
               word  of  File  ID's  is the high byte of the file
               number, and the volume set may consist  of  up  to
               255  volumes.   Under  no  circumstances  may  the
               maximum number of files be greater than 2**24-1.



     5.1.9.12  H.IBSZ - 2 Bytes    Index File Bitmap Size

               This 16 bit word contains  the  number  of  blocks
               that  make  up  the index file bitmap.  This value
               must be non-zero for a valid home block.



     5.1.9.13  H.RSVF - 2 Bytes    Number of Reserved Files

               This word contains the number of of reserved  file
               on  the  volume.  The file sequence number of each
               reserved file is always equal to its file  number.
               Reserved files may not be deleted.  This word must
               contain a minimum value of 5 to be valid.



     5.1.9.14  H.DVTY - 2 Bytes    Disk Device Type

               This word is an index identifying the type of disk
               that  contains  this  volume.  It is currently not
               used and always contains 0.


     Files-11 On-Disk Structure                           Page 37


     5.1.9.15  H.RVN - 2 Bytes     Relative Volume Number

               This word contains the relative volume number that
               this volume has been assigned in a volume set.  If
               the volume is not part of a volume set, then  this
               word contains zero.



     5.1.9.16  H.NVOL - 2 Bytes    Number of Volumes

               This word contains the total number of volumes  in
               this  volume  set  if  the  contents of H.RVN is 1
               (i.e., if this volume is the first volume  of  the
               volume set).  Otherwise, this word contains zero.



     5.1.9.17  H.VCHA - 2 Bytes    Volume Characteristics

               This word contains bits which  provide  additional
               control  over access to the volume.  The following
               bits are defined:

               CH.NDC    Set if device control functions are  not
                         permitted   on   this   volume.   Device
                         control functions are  those  which  can
                         threaten  the  integrity  of the volume,
                         such as direct reading  and  writing  of
                         logical blocks, etc.

               CH.NAT    Set if the volume may not  be  attached,
                         i.e.,  reserved  for the sole use by one
                         task or user.

               CH.RCK    Set if the volume is to be read checked.
                         All  block  reads  done  on this volume,
                         both for data and  for  file  structure,
                         will   be   performed   with   a   read,
                         read-compare  sequence  to  insure  data
                         integrity.

               CH.WCK    Set  if  the  volume  is  to  be   write
                         checked.   All block writes done on this
                         volume,  both  for  data  and  for  file
                         structure,  will  be  performed  with  a
                         write, read-compare sequence  to  insure
                         data integrity.


     Files-11 On-Disk Structure                           Page 38


     5.1.9.18  H.VOWN - 4 Bytes    Volume Owner UIC

               This double word contains the binary  UIC  of  the
               owner  of  the  volume.  The format is the same as
               that of the file owner  UIC  stored  in  the  file
               header.



     5.1.9.19  4 Bytes (not used)



     5.1.9.20  H.VPRO - 2 Bytes    Volume Protection Code

               This word contains the  protection  code  for  the
               entire volume.  All operations on all files on the
               volume must pass both  the  volume  and  the  file
               protection  check  to  be permitted.  Accessors to
               the volume are  categorized  into  system,  owner,
               group,  and world with respect to the volume owner
               UIC in the same manner  as  for  file  protection.
               Each  category  is controlled by the familiar four
               bit field.  The four access modes are bit  encoded
               as follows:

               VP.RDV    Deny reading files
               VP.WRV    Deny writing existing files
               VP.CRE    Deny creating files
               VP.DEL    Deny deleting files



     5.1.9.21  H.DFPR - 2 Bytes    Default File Protection

               This word contains the file protection  that  will
               be assigned to all files created on this volume if
               no file protection is specified by the user.



     5.1.9.22  2 Bytes (not used)



     5.1.9.23  H.CHK1 - 2 Bytes    First Checksum

               This word is an additive checksum of  all  entries
               preceding  in  the  home  block  (i.e.,  all those
               listed above).  It is computed by the same sort of
               algorithm as the file header checksum (see section
               3.5.7.1).


     Files-11 On-Disk Structure                           Page 39


     5.1.9.24  H.VDAT - 8 Bytes    Volume Creation Date

               This area contains the  date  and  time  that  the
               volume  was initialized.  It is in the same binary
               format  used  in  the  file  header  (see  section
               3.4.2).



     5.1.9.25  H.WISZ - 1 Byte     Default Window Size

               This  byte  contains  the  number   of   retrieval
               pointers  that  will  be used for the "window" (in
               core file access data) when files are accessed  on
               the  volume,  if  not  otherwise  specified by the
               accessor.



     5.1.9.26  H.LRUC - 1 Byte     Directory Pre-access Limit

               This byte  contains  a  count  of  the  number  of
               directories  to  be  stored  in  the file system's
               directory access cache.  More generally, it is  an
               estimate  of the number of concurrent users of the
               volume and its  use  may  be  generalized  in  the
               future.



     5.1.9.27  H.FIEX - 2 Bytes    Default File Extend

               This word contains the number of blocks that  will
               be  allocated  to  a  file when a user extends the
               file and asks for the  system  default  value  for
               allocation.



     5.1.9.28    - - 388 Bytes     Not Used



     5.1.9.29  H.SNAM - 12 Bytes   Structure Name

               This area contains the ASCII name  of  the  volume
               set to which this volume belongs, padded out to 12
               bytes with spaces.  If this volume is not a member
               of  a  volume  set,  then this area is filled with
               nulls.


     Files-11 On-Disk Structure                           Page 40


     5.1.9.30  H.INDN - 12 Bytes   Volume Name

               This area contains the volume label in ASCII.   It
               is  padded  out  to  12  bytes with spaces.  It is
               placed here in accordance with the proposed volume
               identification standard.



     5.1.9.31  H.INDO - 12 Bytes   Volume Owner

               This area contains an ASCII string identifying the
               owner of the volume.  The area is padded out to 12
               bytes with trailing spaces.  It is placed here  in
               accordance with the proposed volume identification
               standard.



     5.1.9.32  H.INDF - 12 Bytes   Format Type

               This field contains the ASCII string  "DECFILE11B"
               padded out to 12 bytes with spaces.  It identifies
               the volume as being of Files-11 format,  structure
               level 2.  It is placed here in accordance with the
               proposed volume identification standard.



     5.1.9.33    - - 2 Bytes       Not Used



     5.1.9.34  H.CHK2 - 2 Bytes    Second Checksum

               This word is the last word of the home block.   It
               contains an additive checksum of the preceding 255
               words of the home block, computed according to the
               algorithm listed in section 3.5.7.1.


     Files-11 On-Disk Structure                           Page 41


     5.1.9.35  Home Block Layout -


               |---------------------------------------|
               |                                       |   H.HBLB
               |--         LBN of This Block         --|
               |                                       |    
               |---------------------------------------|
               |                                       |   H.AHLB
               |--    LBN of Secondary Home Block    --|
               |                                       |    
               |---------------------------------------|
               |            LBN of Secondary           |   H.IHLB
               |--                                   --|
               |           Index File Header           |    
               |---------------------------------------|
               |        Volume Structure Level         |   H.VLEV
               |---------------------------------------|
               |     Storage Bitmap Cluster Factor     |   H.SBCL
               |---------------------------------------|
               |           VBN of This Block           |   H.HBVB
               |---------------------------------------|
               |         Backup Home Block VBN         |   H.AHVB
               |---------------------------------------|
               |        Backup Index Header VBN        |   H.IHVB
               |---------------------------------------|
               |         Index File Bitmap VBN         |   H.IBVB
               |---------------------------------------|
               |              Index File               |   H.IBLB
               |--                                   --|
               |              Bitmap LBN               |    
               |---------------------------------------|
               |                                       |   H.FMAX
               |--      Maximum Number of Files      --|
               |                                       |   
               |---------------------------------------|
               |        Index File Bitmap Size         |   H.IBSZ
               |---------------------------------------|
               |       Number of Reserved Files        |   H.RSVF
               |---------------------------------------|
               |           Disk Device Type            |   H.DVTY
               |---------------------------------------|
               |         Relative Volume Number        |   H.RVN
               |---------------------------------------|
               |       Number of Volumes in Set        |   H.NVOL
               |---------------------------------------|
               |        Volume Characteristics         |   H.VCHA
               |---------------------------------------|
               |                                       |   H.VOWN
               |--         Volume Owner UIC          --|
               |                                       |   
               |---------------------------------------|
               |                                       |
               |--             (not used)            --|
               |                                       |   


     Files-11 On-Disk Structure                           Page 42


               |-------------------|-------------------|
               |           Volume Protection           |   H.VPRO
               |---------------------------------------|
               |        Default File Protection        |   H.DFPR
               |---------------------------------------|
               |               (not used)              |
               |---------------------------------------|
               |            First Checksum             |   H.CHK1
               |---------------------------------------|
               |                                       |   H.VDAT
               |--                                   --|
               |                                       |   
               |--       Volume Creation Date        --|
               |                                       |    
               |--                                   --|
               |                                       |    
               |---------------------------------------|
     H.LRUC    |  Directory Limit  | Def. Window Size  |   H.WISZ
               |-------------------|-------------------|
               |          Default File Extend          |   H.FIEX
               |---------------------------------------|
               |                                       |    
               |                                       |    
               |                                       |    
               |                                       |    
               |              (not used)               |    
               |                                       |    
               |                                       |    
               |                                       |    
               |                                       |    
               |---------------------------------------|
               |                                       |   H.SNAM
               |--                                   --|
               |                                       |    
               |--                                   --|
               |                                       |    
               |--          Structure Name           --|
               |                                       |    
               |--                                   --|
               |                                       |    
               |--                                   --|
               |                                       |    
               |---------------------------------------|
               |                                       |   H.INDN
               |--                                   --|
               |                                       |    
               |--                                   --|
               |                                       |    
               |--            Volume Name            --|
               |                                       |    
               |--                                   --|
               |                                       |    
               |--                                   --|
               |                                       |    
               |---------------------------------------|


     Files-11 On-Disk Structure                           Page 43


               |                                       |   H.INDO
               |--                                   --|
               |                                       |    
               |--                                   --|
               |                                       |    
               |--           Volume Owner            --|
               |                                       |    
               |--                                   --|
               |                                       |    
               |--                                   --|
               |                                       |    
               |---------------------------------------|
               |                                       |   H.INDF
               |--                                   --|
               |                                       |    
               |--                                   --|
               |                                       |    
               |--            Format Type            --|
               |                                       |    
               |--                                   --|
               |                                       |    
               |--                                   --|
               |                                       |    
               |---------------------------------------|
               |              (not used)               |    
               |---------------------------------------|
               |            Second Checksum            |   H.CHK2
               |---------------------------------------|



     5.2  Storage Bitmap File

     The storage bitmap file is File ID 2,2.  It is listed in the
     MFD  as BITMAP.SYS;1.  The storage bitmap is used to control
     the available space on a volume.  It consists of  a  storage                                                          _______
     control  block  which contains summary information about the     _______  _____
     volume, and the bitmap itself which lists  the  availablilty
     of  individual  blocks.  This file has the FCS record format
     of 512 byte fixed length records, with no carriage  control.
     The  end  of  file  mark  is positioned to point to the last
     block used.  The storage bitmap file must be contiguous.



     5.2.1  Storage Control Block -

     Virtual block 1 of the storage bitmap is the storage control
     block.   It  contains  summary information about the volume.
     Note that implementation of some  of  the  features  in  the
     storage  control block may require it to be written at mount
     and dismount.


     Files-11 On-Disk Structure                           Page 44


     5.2.1.1  C.VLEV - 2 Bytes     Storage Map Structure Level

               This word contains  the  structure  level  of  the
               storage control block.  The high byte contains the
               value 2 to indicate Files-11  structure  level  2.
               The  low  byte  contains the version number, which
               must be equal to or greater then 1.



     5.2.1.2  C.SBCL - 2 Bytes     Storage Map Cluster Factor

               This word contains the storage map cluster  factor
               of  the volume.  Its contents are identical to the
               contents of H.SBCL  in  the  home  block.   It  is
               placed here for convenience.



     5.2.1.3  C.VSIZ - 4 Bytes     Volume Size

               These four bytes contain the volume size expressed
               in logical blocks.



     5.2.1.4  C.BLKF - 4 Bytes     Blocking Factor

               These words contain the  blocking  factor  of  the
               volume;   i.e.,  the  number of physical blocks or
               sectors that make up one logical block.



     5.2.1.5  C.SECT - 4 Bytes     Sectors Per Track

               These words contain the number of  logical  blocks
               in each track of the volume.



     5.2.1.6  C.TRAK - 4 Bytes     Tracks Per Cylinder

               These words contain the number of tracks contained
               in each cylinder of the volume.



     5.2.1.7  C.CYLN - 4 Bytes     Number of Cylinders

               These words contain the total number of  cylinders
               on  the  volume.   The  above three quantities are
               present to assist optimized allocation of space on
               physical boundaries in the volume.


     Files-11 On-Disk Structure                           Page 45


     5.2.1.8  C.STAT - 2 Bytes     Status Word

               This word contains the following status bits:

               CS.TRN    Volume in transition.  This bit  is  set
                         if  the volume may be in an inconsistent
                         state  because  it  was  not  dismounted
                         properly.   A system which does write on
                         replace caching of the storage map,  for
                         example,  should  set  this bit on mount
                         and clear it on dismount.



     5.2.1.9    - - 488 Bytes      (not used)



     5.2.1.10  C.CKSM - 2 Bytes    Block Checksum

               This word contains the ubiquitous block  checksum.
               It  is  computed  using  the same algorithm as the
               file header checksum (section 3.5.7.1).



     5.2.1.11  Storage Control Block Layout -


               |---------------------------------------|
               |            Structure Level            |   C.VLEV
               |---------------------------------------|
               |      Storage Map Cluster Factor       |   C.SBCL
               |---------------------------------------|
               |                                       |   C.VSIZ
               |--       Volume Size in Blocks       --|
               |                                       |   
               |---------------------------------------|
               |                                       |   C.BLKF
               |--          Blocking Factor          --|
               |                                       |   
               |---------------------------------------|
               |                                       |   C.SECT
               |--         Sectors Per Track         --|
               |                                       |   
               |---------------------------------------|
               |                                       |   C.TRAK
               |--        Tracks Per Cylinder        --|
               |                                       |   
               |---------------------------------------|
               |                                       |   C.CYLN
               |--        Cylinders on Volume        --|
               |                                       |   
               |---------------------------------------|
               |             Volume Status             |   C.STAT


     Files-11 On-Disk Structure                           Page 46


               |---------------------------------------|
               |                                       |   
               |                                       |   
               |                                       |   
               |                                       |   
               |                                       |   
               |              (not used)               |   
               |                                       |   
               |                                       |   
               |                                       |   
               |                                       |   
               |                                       |   
               |---------------------------------------|
               |            Block Checksum             |   C.CKSM
               |---------------------------------------|



     5.2.2  Storage Bitmap -

     Virtual blocks 2 through n+1 are the storage bitmap  itself.
     It is best viewed as a bit string of length m, numbered from
     0 to m-1,  where  m  is  the  total  number  of  allocatable
     clusters  on  the  volume rounded up to the next multiple of
     4096.  Each cluster contains v logical blocks,  where  v  is
     the  storage  map  cluster  factor  (also referred to as the
     volume cluster factor) contained in location H.SBCL  in  the
     home  block.   The  bits  are  addressed in the usual manner
     (packed right  to  left  in  sequentially  numbered  bytes).
     Since  each virtual block holds 4096 bits, n blocks, where n
     = m/4096, are used to hold the bitmap.  Bit j of the  bitmap
     represents logical blocks j*v through j*v+v-1 of the volume;
     if the bit is set, the  blocks  are  free;   if  clear,  the
     blocks are allocated.  Clearly the last k bits of the bitmap
     are always clear, where k is the difference between the true
     size of the volume and m, the length of the bitmap.

     Rounding the storage map file up to the next multiple of the
     volume  cluster  factor  may result in some unused blocks at
     the end of the file.  The FCS end of file mark points to the
     last block used.



     5.3  Bad Block File

     The bad block file is File ID 3,3.  It is listed in the  MFD
     as  BADBLK.SYS;1.   The  bad  block  file  is  simply a file
     containing all of the known bad blocks on the volume.   This
     file  has  the  FCS  record  format of 512 byte fixed length
     records, with no carriage control.  The end of file mark may
     be  placed  as  the  operating  system's  bad block handling
     strategy finds useful.  Volume initialization  should  place
     the   EOF  at  the  end  of  the  bad  blocks  found  during
     initialization.  At all times, the EOF should at least point


     Files-11 On-Disk Structure                           Page 47


     past  the  bad block descriptor data, described below.  This
     ensures that the bad block  data  is  preserved  for  future
     re-initialization of the volume.



     5.3.1  Factory Bad Block Descriptor -

     On disks which have factory generated last track  bad  block
     data,  such  as  the RK06, RK07, and RM03, the first several
     clusters of the bad block file should include the last track
     of  the  volume.   This  track contains redundantly recorded
     descriptions of the bad blocks on the volume,  as  described
     in  DEC STD.  144, "Disk Standard for Recording and Handling
     Manufacturing Detected Bad Sectors".



     5.3.2  Software Bad Block Descriptor -

     On disks that do not have factory last track bad block data,
     the  first  cluster  of  the bad block file contains the bad
     block descriptor for the volume.  It is  always  located  on
     the last good block of the volume.  This block may contain a
     listing of the bad blocks on the volume produced  by  a  bad
     block  scan  program  or diagnostic.  The software bad block
     descriptor is most of a Files-11 Structure  Level  1  header
     map  area.   The first two bytes contain the constants 1 and
     3, respectively.  The third  byte  contains  the  number  of
     words  that  contain  data.   The  fourth  byte contains the
     number of words available for bad block data.  The last word
     of  the  block  contains  the  usual additive checksum.  The
     retrieval pointers are structure level 1 format 1  pointers,
     as described below.


     Bad Block Descriptor Layout


               |-------------------|-------------------|
               |         3         |         1         |
               |-------------------|-------------------|
               | Map Words Avail.  | Map Words in Use  |
               |-------------------|-------------------|
               |                                       |
               |                                       |    
               |                                       |    
               |          Retrieval Pointers           |    
               |                                       |    
               |                                       |    
               |                                       |    
               |---------------------------------------|
               |            Block Checksum             |
               |---------------------------------------|


     Files-11 On-Disk Structure                           Page 48


     Each retrieval pointer is four  bytes  in  length.   Byte  1
     contains  the  high  order  bits  of the 24 bit LBN.  Byte 2
     contains the count field, and bytes 3 and 4 contain the  low
     16 bits of the LBN.

                    |----------|----------|
                    |  Count   |   High   |
                    |----------|-        -|
                    |    Low Order LBN    |
                    |---------------------|



     5.4  Master File Directory

     The master file directory is File ID 4,4.  It is  listed  in
     the  MFD  (itself)  as 000000.DIR;1.  The MFD is the root of
     the volume's directory structure.   It  lists  the  reserved
     files,  plus whatever the user chooses to enter.  The format
     of the MFD is the  same  as  all  directory  files,  and  is
     described  in  section 4.3.  In the UFD structures described
     in sections 4.1.1 and 4.1.2, the MFD  contains  entries  for
     all user file directories.



     5.5  Core Image File

     The core image file is File ID 5,5.  It is listed in the MFD
     as CORIMG.SYS;1.  Its use is operating system dependent.  In
     general, it provides a file of known File ID for the use  of
     the  operating  system, for use as a swap area, for example,
     or as a monitor overlay area, etc.  This file  has  the  FCS
     record  format  of  512  byte  fixed length records, with no
     carriage control.  The end of file  mark  is  positioned  to
     point to the physical end of file.



     5.6  Volume Set List

     The volume set list is File ID 6,6.  It is listed in the MFD
     as  VOLSET.SYS;1.  It is used only on relative volume one of
     a tightly coupled volume set.  There, it contains a list  of
     the  volume  labels  of the volumes contained in this volume
     set.  The format of this file is FCS 64  byte  fixed  length
     records  with  implied carriage control.  The first 12 bytes
     of record 1 contain the structure name of  the  volume  set.
     The  first  12 bytes of record n contain the volume label of
     relative volume n-1.  The remaining 52 bytes of each  record
     are reserved for future use.


     Files-11 On-Disk Structure                           Page 49


     5.7  Continuation File

     The standard continuation file is File ID 7,7.  It is listed
     in  the  MFD  as  CONTIN.SYS;1.  It is used as the extension
     File ID when a file crosses from one  volume  of  a  loosely
     coupled volume set to another.  The purpose of this reserved
     File  ID  is  allow  a  multi-volume  file  to  be   written
     sequentially  with  only  one  volume  mounted  at  a  time.
     Ordinarily, when a file is extended onto another volume, the
     new  header  must be created first to obtain the new File ID
     before the extension linkage in the current  header  can  be
     written.   The  use  of  this  reserved  File  ID allows the
     extension linkage to be written with a known constant before
     the next volume is even on line.



     5.8  Backup Log File

     The backup log file is File Id 8,8,0.  It is listed  in  the
     MFD as BACKUP.SYS;1.  This file contains a history of volume
     and incremental backups performed on the volume.  The format
     of  this  file  is  FCS 64 byte fixed length records.  Their
     content is at present undefined.



     5.9  Pending Bad Block Log File

     The pending bad block log file is  File  ID  9,9,0.   It  is
     listed  in  the  MFD  as BADLOG.SYS;1.  This file contains a
     list identifying suspected bad blocks on the volume that are
     not currently contained in the volume's bad block file.  The
     format of this file is FCS 16  byte  fixed  length  records.
     Each  record represents one bad block, and has the following
     format:


               |---------------------------------------|
               |                                       |   P.FID
               |--              File ID              --|
               |               containing              |
               |--             bad block             --|
               |                                       |
               |-------------------|-------------------|
     P.CNT     |    Error Count    |      Flags        |   P.FLGS
               |-------------------|-------------------|
               |                                       |   P.VBN
               |--          VBN within file          --|
               |                                       |
               |---------------------------------------|
               |                                       |   P.LBN
               |--                LBN                --|
               |                                       |
               |---------------------------------------|


     Files-11 On-Disk Structure                           Page 50


     The following bits are defined in the flags byte:

          PF.RDE         Set if a read error has occurred on this
                         block.

          PF.WRE         Set if a write  error  has  occurred  on
                         this block.



     6.0  FCS FILE STRUCTURE

     File Control Services (FCS) is a  user  level  interface  to     ____ _______ ________  ___
     Files-11  implemented  in the RSX-11 systems.  Its principal
     feature is a record control facility that allows  sequential
     processing  of  variable  length  records and sequential and
     random access to fixed length record files.  FCS  interfaces
     to the virtual block facility provided by the basic Files-11
     structure.



     6.1  FCS File Attributes

     FCS stores attribute  information  about  the  file  in  the
     file's  user attribute area (H.UFAT - see section 3.5.2.13).
     It uses only the first 7 words;  the  rest  are  ignored  by
     FCS.   The  following  items  are contained in the attribute
     area;  they are identified by  the  usual  symbolic  offsets
     (relative  to the start of the attribute area).  The offsets
     may be defined in assembly language programs by calling  and
     invoking  the  macro FDOFF$ DEF$L.  Flag values and bits may
     be defined by calling and invoking the macro FCSBT$.   These
     macros  are  in  the  system  macro library of any operating
     system that supports  Files-11.   Alternatively,  all  these
     values  are  defined  in  the  system  object library of any
     system that supports Files-11, and may be obtained  at  link
     time.



     6.1.1  F.RTYP       1 Byte    Record Type -

               This byte identifies which  type  of  records  are
               contained  in  this  file.   The  following  three
               values are legal:

               R.FIX     Fixed length records.
               R.VAR     Variable length records.
               R.SEQ     Sequenced variable length records


     Files-11 On-Disk Structure                           Page 51


     6.1.2  F.RATT       1 Byte    Record Attributes -

               This byte  contains  record  attribute  bits  that
               control  the  handling  of  records  under various
               contexts.  The following flag bits are defined:

               FD.FTN    Use Fortran  carriage  control  if  set.
                         The  first  byte of each record is to be
                         interpreted  as   a   standard   Fortran
                         carriage   control  character  when  the
                         record is copied to a  carriage  control
                         device.

               FD.CR     Use implied  carriage  control  if  set.
                         When  the  file  is copied to a carriage
                         control device, each  record  is  to  be
                         preceded  by a line feed and followed by
                         a carriage return.  Note that the FD.FTN
                         and FD.CR bits are mutually exclusive.

               FD.BLK    Records do not cross block boundaries if
                         set.   Generally,  there  will  be  dead
                         space at the end  of  each  block;   how
                         this  is  handled  is  explained  in the
                         description of record formats in section
                         6.2.

               FD.PRN    Use print file carriage control.   Legal
                         only  if  the record type is R.SEQ.  The
                         leading two byte field of each record is
                         used as carriage control instead of as a
                         sequence number.  The first  and  second
                         bytes  are  used as leading and trailing
                         carriage formatting, respectively.   The
                         interpretation  of  the carriage control
                         bytes  is  described  below  in  section
                         6.2.3.



     6.1.3  F.RSIZ       2 Bytes   Record Size -

               In a fixed length record file, this word  contains
               the  size  of the records in bytes.  In a variable
               length record file, this word contains the size in
               bytes of the longest record in the file.



     6.1.4  F.HIBK       4 Bytes   Highest VBN Allocated -

               This 32 bit number is a count  of  the  number  of
               virtual  blocks allocated to the file.  Since this
               value is maintained by FCS, it is usually correct,
               but it is not guaranteed since FCS is a user level


     Files-11 On-Disk Structure                           Page 52


               package.



     6.1.5  F.EFBK       4 Bytes   End Of File Block -

               This 32 bit number is the VBN in which the end  of
               file  is  located.   Both  F.HIBK  and  F.EFBK are
               stored with the high order half in the  first  two
               bytes, followed by the low order half.



     6.1.6  F.FFBY       2 Bytes   First Free Byte -

               This word is a count of the number of bytes in use
               in  the  virtual block containing the end of file;
               i.e., it is the offset to the first  byte  of  the
               file available for appending.  Note that an end of
               file  that  falls  on  a  block  boundary  may  be
               represented  in  either  of two ways.  If the file
               contains precisely n blocks, F.EFBK may contain  n
               and F.FFBY will contain 512, or F.EFBK may contain                                            __
               n+1 and F.FFBY will contain 0.



     6.1.7  S.FATT       14 Bytes  Size Of Attribute Block -

               This symbol represents the total number  of  bytes
               in the FCS file attribute block.



     6.2  FCS File Attributes Layout

               |-------------------|-------------------|
     F.RATT    |   Record Attr.    |    Record Type    |   F.RTYP
               |-------------------|-------------------|
               |          Record Size (Bytes)          |   F.RSIZ
               |---------------------------------------|
               |              Highest VBN              |   F.HIBK
               |--                                   --|
               |               Allocated               |    
               |---------------------------------------|
               |              End of File              |   F.EFBK
               |--                                   --|
               |                  VBN                  |    
               |---------------------------------------|
               |            First Free Byte            |   F.FFBY
               |---------------------------------------|   S.FATT


     Files-11 On-Disk Structure                           Page 53


     6.3  Attribute Standardization

     To assure a certain consistency of file  record  structures,
     certain   fields   in   the   record   attributes  area  are
     standardized,  and  must   contain   well   defined   values
     regardless  of  the record structure or file organization in
     use.

     1.  The record type byte (F.RTYPE) must contain a code  that
         identifies  the  file organization and record structure.
         All codes must be registered with this specification.

     2.  The record attribute bits should be  used  as  described
         above   when   applicable.   New  attributes  ahould  be
         registered with this specification.

     3.  The high VBN field (F.HIBK) must contain the  number  of
         blocks  allocated to the file.  File managers may modify
         this field during some operations on the file.

     4.  The end of file mark (F.EFBK and F.FFBY) should describe
         the end of data in the file when applicable.




     6.4  Record Structure

     This section describes how records are packed in the virtual
     blocks  of  a disk file.  In general, FCS treats a disk file
     as a sequentially numbered  array  of  bytes.   Records  are
     numbered consecutively starting with 1.



     6.4.1  Fixed Length Records -

     In a file consisting of fixed length  records,  the  records
     are  simply  packed  end  to  end with no additional control
     information.  If the record length is odd,  each  record  is
     padded  with  a single null.  For direct access, the address
     of a record is computed as follows:

     Let:      n = record number
               k = record size (in bytes)
               m = byte address of record in file
               q = number of records per block
               j = VBN containing the start of the record
               i = byte offset within VBN j

     Then      h = ((k+1)/2)*2 (rounded up record length)
               m = (n-1)*h
               j = m/512+1 (truncated)
               i = m mod 512


     Files-11 On-Disk Structure                           Page 54


     The previous discussion assumes  that  records  cross  block
     boundaries  (that is, FD.BLK is not set).  If records do not
     cross block boundaries, they are limited to 512  bytes,  and
     the  following equations apply (the variables are defined as
     above):

               h = ((k+1)/2)*2 (rounded up record length)
               q = 512/h (truncated)
               j = (n-1)/q+1 (truncated)
               i = ((n-1) mod q)*h



     6.4.2  Variable Length Records -

     In a file consisting of variable length records, records may
     be  up to 32767 bytes in length.  Each record is preceded by
     a two byte binary count of the  bytes  in  the  record  (the
     count  does not include itself).  For example, a null record
     is represented by a single zero word.   The  byte  count  is
     always  word aligned;  i.e., if a record ends on an odd byte
     boundary, it is padded with a single null.

     If records do not cross block boundaries  (FD.BLK  is  set),
     they are limited to a size of 510 bytes.  A byte count of -1
     is used as a flag to signal that there are no  more  records
     in  a particular block.  The remainder of that block is then
     dead space and the next record in the  file  starts  at  the
     beginning of the next block.



     6.4.3  Sequenced Variable Length Records -

     The format of a sequenced file is identical  to  a  variable
     length  record  file  except that a two byte sequence number
     field is located immediately after the byte count  field  of
     each  record.   This  field contains a binary value which is
     usually interpreted as the line number of that  record  (see
     Section  6.1.2  FD.PRN  and  Section 6.2.3.1).  The sequence
     number is not returned as part of the data when a record  is
     read,  but  is  available  separately.  Note that the record
     byte count field counts the sequence number field as well as
     the data of the record.



     6.4.3.1  Format Of Two Byte Print  Control  Field  In  R.SEQ
              Records -

     If the FD.PRN bit is set in the record  attribute  then  the
     two byte "sequence number" field is used to contain carriage
     control data for  the  record.   Byte  0  is  print  control
     information  to act upon before the record data is output to
     a unit record device;  byte 1 is print  control  information


     Files-11 On-Disk Structure                           Page 55


     to  act upon after the record data has been output to a unit
     record device.

     The format of each byte is as follows:

     Bit 7  Bits 6-0     Meaning

     0      0            No carriage control
     0      count(1-127) "count" new lines (CR/LF)

     Bit 7  Bit 6  Bit 5  Bits 4-0       Meaning

     1      0      0      ASCII C0 set   ASCII char to
                                         output (CR,FF etc.)
     1      0      1      ASCII C1 set   ASCII char (8 bit code)
                                         to output
     1      1      0      code (0-63)    Device specific code
     1      1      1      -              Reserved


                                 NOTE

         The print control field is not  currently  supported
         by FCS or RMS-11.




     Files-11 On-Disk Structure                           Page 56


     7.0  RECORD MANAGEMENT SERVICES (RMS)

     Record Management Services (RMS) is a user  level  interface
     to  Files-11.  It provides a flexible means of data storage,
     retrieval, and modification through a  combination  of  file
     organization  and record access modes.  File organization is
     the structure  of  data  within  the  virtual  blocks  of  a
     Files-11 file, and record access mode is the manner in which
     storing and retrieving the data in the file occurs.

     RMS supports/defines three file organizations which are:

           . Sequential - compatible with  FCS  fixed,  variable,
             and sequenced variable record files (see Section 6)

           . Relative - RMS only

           . Indexed - RMS only

     RMS interfaces to the virtual block facility provided by the
     Files-11 structure.



     7.1  Data Formats And Representation


     RMS supports file organizations which require a more complex
     degree  of  structuring than that required by FCS.  RMS also
     stores binary values in a different manner in  general  than
     Files-11  defines.   For  these  reasons the data format and
     representations used by  RMS  are  given  in  the  following
     sections.



     7.1.1  String Storage -

     All strings  are  stored  left  justified.   The  left  most
     character  is  in  byte N and the right most character is in
     byte N+M-1 where M is the length of the string.



     7.1.2  String Character Code Set -

     All string values are assumed to be in the 7-bit ASCII  code
     set.


     Files-11 On-Disk Structure                           Page 57


     7.1.3  String Collating Sequence -

     The collating sequence used is  the  7-bit  ASCII  code  set
     where  NUL  is  the  lowest  valued character and DEL is the
     highest valued character.


                                 NOTE

         The internal representation of ASCII  characters  on
         PDP-11  systems  is 7-bit ASCII.  The string compare
         routine of RMS-11 however,  performs  a  full  8-bit
         unsigned   compare  per  character.   RMS  does  not
         perform any "clear bit 7" code on  input  or  output
         operations.   This allows the support of user binary
         byte strings, the KANA character set used in  Japan,
         and  in the future 8-bit ASCII when defined, without
         RMS modifications since the true  colating  sequence
         is lowest character = 0 and highest character = 255.





     7.1.4  Unsigned Binary Value Storage -

     All  unsigned  binary  values  are  stored  with  the  Least
     Significant  Bits  (LSB)  in byte N and the Most Significant
     Bits (MSB) in byte N+M-1 where M is the length of the binary
     value.

             EXAMPLE:  2 byte unsigned binary value

                         ---------
                         |  LSB  | N
                         |-------|
                         |  MSB  | N+1
                         ---------



     7.1.5  Signed Binary Value Storage -

     All signed binary  values  are  stored  as  unsigned  binary
     values  except  that  most  significant  bit  (bit 7 of byte
     N+M-1) of the value is interpreted as the sign of the value.
     Negative  numbers  are stored as the two's complement of the
     positive value.


     Files-11 On-Disk Structure                           Page 58


             EXAMPLE: 2 byte signed binary value

                         -------------
                         |    LSB    | N
                         |-----------|
                         |S|  MSB    | N+1
                         -------------



     7.1.6  Pointer Values -

     All pointers are stored as unsigned binary values.  Pointers
     are  stored  variable length.  The length of a pointer value
     is  specified  by  the  control  bits  associated  with  the
     pointer.  The length requirement for a pointer is determined
     by the range of VBN values it falls in as follows:

             2 bytes start VBN 1 - 65,535

             3 bytes start VBN 65,536 - 16,777,215

             4 bytes start VBN 16,777,216 - 4,294,967,295



     7.1.7  Bucket Pointers -

     A bucket pointer is a  pointer  value  which  specifies  the
     start  VBN  of the bucket.  The length of the bucket (number
     of VBN's in bucket) is interpreted in  the  context  of  its
     usage within the file, and is specified in the file's prolog
     data.

             EXAMPLE:  2 byte bucket pointer

                         ---------
                         |  LSB  | N
                         |-------|
                         |  MSB  | N+1
                         ---------



     7.1.8  Record Pointers -

     Record pointers are composed  of  two  fields,  a  one  byte
     record  ID  field  followed  by a bucket pointer.  The ID is
     used as a unique record  identifier  for  records  within  a
     bucket.   The records are tagged with their ID'S when stored
     in the bucket.

             EXAMPLE:  3 byte record pointer

                         ---------


     Files-11 On-Disk Structure                           Page 59


                         |   ID  | N RECORD ID
                         |-------|
                         |  LSB  | N+1  BUCKET POINTER
                         |-------|
                         |  MSB  | N+2
                         ---------



     7.1.9  Packed Decimal Strings -

     Packed decimal strings are from 1 to  16  bytes  in  length.
     The format is as follows:

                 7     4 3      0
                 ----------------
                 |  d1  |  d2   | A
                 ----------------
                 |  d3  |  d4   | A+1
                 ----------------
                        .        
                        .        
                        .        
                 ----------------
                 |  di  | sign  | A+N-1
                 ----------------

                 where:

                 d = digit in the  range  of  0  thru  9  (binary
                 value)

                 sign is plus if value is 10, 12, 14, or 15

                 sign is minus if value is 11 or 13

                 N is length of strings in bytes

                 i = (N-1)*2+1 and is an odd number in the  range
                 of 1 thru 31

                 d1 is most significant digit (may be  a  leading
                 zero)

                 di is least significant digit



     7.2  RMS File Attributes

     RMS stores attribute  information  about  the  file  in  the
     file's  user  attribute area (H.UFAT - see Section 3.4.1.9).
     It uses the first ten (10) words;  the rest are reserved  by
     RMS.   The  following  items  are contained in the attribute
     area;  they are identified by symbolic offsets into  an  RMS


     Files-11 On-Disk Structure                           Page 60


     internal  structure.  The relative offset into the attribute
     area may be calculated by subtracting F$FORG from the  given
     offset name/value.  The offset definitions may be defined in
     assembly language programs by calling and invoking the macro
     IFAOF$  RMS$L.   Flag  values  and  bits  may  be defined by
     calling and invoking the FAB$BT DFIN$L macro.  These  macros
     can  be  found in the RMSMAC.MLB macro library on all PDP-11
     systems supporting RMS.



     7.2.1  F$FORG 1 Byte - Record Format and File Organization

               This byte identifies the file's  organization  and
               which  type  of  record  format  it contains.  The
               record format is contained in bits 0 - 3, and  the
               file's  organization  is  contained in bits 4 - 7.
               The symbolic values are defined such that they may
               be  OR'ED  to  yield  the  contents  of the F$FORG
               field.

               Record Formats:

               FB$UDF   Undefined record format (Block  I/O  only
                        file)

               FB$FIX   Fixed length records

               FB$VAR   Variable length records

               FB$VFC   Variable with Fixed Control (VFC) records
                        (the  FCS R.SEQ is a special case form of
                        the record format i.e., the fixed control
                        area  is  two bytes long and contains the
                        records sequence number)

               FB$STM   ASCII stream records.  RMS-11  used  only
                        as   a   means   for  RSTS/E  ASCII  data
                        interchange.  Records  are  delimited  by
                        vertical  form  effecter  characters (LF,
                        VT, FF and CR/LF pairs).

               File Organizations:

               FB$SEQ   Sequential File organization (FB$SEQ =  0
                        to maintain compatibility with FCS)

               FB$REL   Relative File organization

               FB$IDX   Index File organization

               FB$HSH Hashed File Organization (not implemented)


     Files-11 On-Disk Structure                           Page 61


     7.2.2  F$RATT 1 Byte - Record Attributes

               This byte contains  record  attributes  bits  that
               control  the  handling  of  records  under various
               contexts.  The following flag bits are defined:

               FB$FTN   See Section 6.1.2 FD.FTN

               FB$CR    See Section 6.1.2 FD.CR

               FB$PRN   See Section 6.1.2 FD.PRN and 6.2.3.1

               FB$BLK   Record do not cross block boundaries  for
                        the  Sequential file organization if set.
                        See  Section  6.1.2  FD.s1LK   for   more
                        detail.



     7.2.3  F$RSIZ 2 Bytes - Record Size

               In file containing  fixed  length  format  records
               this  word  contains  the  size  of the records in
               bytes.  In Sequential files containing variable or
               variable with fixed control formatted records this
               field contains the size in bytes  of  the  longest
               record  in  the file.  This field is undefined for
               Relative and Indexed files containing variable  or
               variable with fixed control format records.



               7.2.4  F$HVBN 4 Bytes - Highest VBN Allocated

               RMS updates this field whenever the file is opened
               for  write  access.  For details on this field see
               Section 6.1.4 F.HIBK.



               7.2.5  F$HEOF 4 Bytes - End of File Block

               This 32 bit number is the VBN in which the end  of
               file   is   located   for   the   Sequential  file
               organization.  Both F$HVBN and F$HEOF  are  stored
               with  the  high order half in the first two bytes,
               followed by the low order  half.   The  low  order
               half  is  symbolically  referenced  by  F$LVBN and
               F$LEOF  respectively.   These  are  the  only  two
               places  that  RMS  stores  block  numbers  in this
               manner (see  Section  7.1),  and  is  done  so  to
               maintain compatibility with FCS.  The Relative and
               Index file does not use this field and  its  value
               is   usually   (but  not  guaranteed)  either  the
               contents of F$HVBN or the contents of F$HVBN  plus


     Files-11 On-Disk Structure                           Page 62


               one.



               7.2.6  F$FFBY 2 Bytes - First Free Byte

               This  field  is  used  for  the  Sequential   file
               organization  as a count of the number of bytes in
               use in the virtual block  containing  the  end  of
               file.   The Relative and Indexed file organization
               do not use this field and its value will be either
               0  or  512.   For  more  details on this field see
               Section 6.1.6 F.FFBY.



               7.2.7  F$BKSZ 1 Byte - Bucket Size

               This field contains the  bucket  size  or  maximum
               bucket  size  for  the  Relative  and Indexed file
               organization respectively.   The  bucket  size  is
               represented  as  the  number  of virtual blocks it
               contains.  Legal values are  from  1  -  32.   For
               compatibility with FCS a value of 0 is interpreted
               as 1.



               7.2.8  F$HDSZ 1 Byte - Fixed Header Size

               This field contains the number of bytes (1 -  255)
               in  the  fixed control area when the file contains
               Variable with Fixed  Control  format  records.   A
               value   of   0   is   interpreted  as  2  so  that
               compatibility with FCS'S Sequenced Variable length
               record format file (R.SEQ) is maintained.



               7.2.9  F$MRS 2 Bytes - Maximum Record Size

               This  field  contains  a  user  specified  maximum
               record  size  limit  in  bytes,  to be enforced on
               output operations.  Files containing Fixed  length
               format  records  have  F$MRS  set equal to F$RSIZ.
               For all other record formats F$MRS is set  to  the
               user  specified  value  given  when  the  file was
               created.  A  value  of  0  is  interpreted  as  no
               maximum record size limit specified.


     Files-11 On-Disk Structure                           Page 63


               7.2.10  F$DEQ 2 Bytes - default Extend Quantity

               This field contains a user specified default  file
               extend  quantity  to be used whenever RMS needs to
               extend the file.  A value of 0 is  interpreted  as
               use the volumes default extend.


     Files-11 On-Disk Structure                           Page 64


               7.2.11  RMS File Attributes Layout -

               |---------------------------------------|
               |    Record Attr.   | File Org./rec fmt |  F$FORG
               |---------------------------------------|
               |          Record Size (bytes)          |  F$RSIZ
               |---------------------------------------|
               |              Highest VBN              |  F$HVBN
               |--                                   --|
               |               Allocated               |
               |---------------------------------------|
               |              End of file              |  F$HEOF
               |--                                   --|
               |                  VBN                  |
               |---------------------------------------|
               |            First Free Byte            |  F$FFBY
               |---------------------------------------|
     F$HDSZ    |  Fixed Ctr. Size  |    Bucket Size    |  F$BKSZ
               |---------------------------------------|
               |       Maximum Record Size Limit       |  F$MRS
               |---------------------------------------|
               |        Default Extend Quantity        |  F$DEQ
               |---------------------------------------|

     To calculate the offset into the User Attributes area in the
     file header subtract F$FORG from all symbolic offsets.



     7.3  Prologue Blocks

     The RMS Relative and  Indexed  file  organizations  use  the
     first   several  virtual  blocks  of  the  file  to  contain
     additional file description data.  This area of the file  is
     called   the   file   prologue.    In   the   Relative  file
     organization, the prologue is exactly one  block  long;   in
     the  Indexed  organization  its length varies.  The symbolic
     offset names, and flag values and  bits  used  in  the  file
     prologue  blocks  and  record  formats  may  be  obtained by
     calling  and  invoking  the  following   macros   from   the
     RMSMAC.MLB  macro  library  on all PDP-11 systems supporting
     RMS.

             ARDOF$      RMS$L
             BKTOF$      RMS$L
             KDXOF$      RMS$L
             KDX$BT      DFIN$L
             XAB$BT      DFIN$L
             BKT$BT      DFIN$L

     The last word of every prologue block contains the  standard
     Files-11 check sum (see Section 3.4.4.1).


     Files-11 On-Disk Structure                           Page 65


     7.3.1  Prologue Block 1 (VBN 1) -

     Prologue Block 1 contains common data for both  the  Indexed
     and  Relative  files,  and file organization dependent data.
     The major Indexed file dependent data  is  the  primary  key
     definition  (the  K$XXXX  symbols).  The major Relative file
     dependent data are the maximum record number, the address of
     the  first  data  bucket,  and  the "real" End of File Block
     (last initialized, zeroed, VBN).  The primary key definition
     offsets (K$XXXX) are used for all key definitions within the
     prologue of the index file and are relative to the start  of
     each key descriptor.

     The key definitions supply all the information needed by RMS
     to  retrive,  insert,  update,  and  delete  records for the
     Indexed  file  organization.   The  basic  data  which   are
     contained in a key definition are as follows:

           . Where the associated key field is positioned in  the
             record, and how long it is.

           . The VBN address of the associated Root bucket.

           . Various key field options

     The key definitions are linked  into  a  chain  by  the  VBN
     address  and  byte  offset within the prologue block for the
     next key definition.  The Indexed file organization  can  be
     viewed  as a multi-partitioned file.  The first partition is
     the prologue, the second partition is the  index  associated
     with  the primary key definition, and the third partition is
     the user data associated  with  the  primary  index.   Every
     indexed  organized file contains these three partitions.  In
     addition when alternate keys are defined then two additional
     partitions   per  alternate  key  are  created.   The  first
     partition is the index associated  with  the  alternate  key
     definition,  and  the  second  partition  is  the  RMS  data
     associated with the index.  The RMS  data  contain  pointers
     into  the  user  data  partition for the records meeting the
     various key values.  The index is  structured  as  an  n'ary
     tree  where  the  nodes of the index are buckets.  The index
     structure is the same for all key definitions.



     7.3.1.1  K$NLVB 4 Bytes - VBN for Next Key Descriptor

               This field contains the virtual block  address  in
               which  the next key descriptor may be found.  This
               field is only looked  at  when  the  K$BNYT  field
               contains a 0.  When K$NLVB and K$NBYT = 0 the last
               key  descriptor  has  been   found.    The   least
               significant  16  bits  of  the  VBN  are stored in
               K$NLVB and the most significant 16 bits are stored
               in K$NLVB+2 (K$NHVB).


     Files-11 On-Disk Structure                           Page 66


               7.3.1.2  K$NBYT 2 Bytes - Byte Offset for Next Key
               Descriptor

               This word field contains the byte offset  relative
               to  the  beginning  of the VBN contained in K$NLVB
               for the next key descriptor in the  chain  of  key
               descriptors.   The  first key descriptor contained
               in a VBN starts at byte offset 0,  and  the  chain
               will  thread  through the current VBN before going
               to the next VBN.  This means  that  the  VBN  will
               only change when K$NBYT contains a 0.



               7.3.1.3  K$IAN 1 Byte - Index Area Number

               This byte contains the number  of  the  Allocation
               Area  to use for the index buckets associated with
               this key starting at  level  2  going  up  to  and
               including the Root bucket.



               7.3.1.4  K$LAN 1 Byte - Lowest  Level  Index  Area
               Number

               This byte contains the number  of  the  Allocation
               Area  to  use  for  Level  1  of the index buckets
               associated with this key (a value of 0  means  use
               the contents of K$IAN).



               7.3.1.5  K$DAN 1 Byte - Data Level Area Number

               This field contains the number of  the  Allocation
               Area  to  use  for the data level (level 0) of the
               index buckets associated with this key descriptor.



               7.3.1.6  K$LVL 1 Byte - Level of Root

               This field contains the level number of  the  Root
               bucket  associated with this key descriptor.  This
               field is not supported by RMS-11 release one.



               7.3.1.7  K$IBKS 1 Byte - Index Bucket Size

               This field contains the bucket size in  VBN'S  for
               all  index  level (level 1 through the root level)
               buckets (1 - 32) for this key descriptor.


     Files-11 On-Disk Structure                           Page 67


               7.3.1.8  K$DBKS 1 Byte - Data Bucket Size

               This field contains the bucket size in  VBN'S  for
               all data level (level 0) buckets (1 - 32) for this
               key descriptor.



               7.3.1.9  P$DBKS 1 Byte - Data Bucket Size

               This is a symbolic redefinition of K$DBKS for  use
               by the Relative file organization.



               7.3.1.10  K$LVBN 4 Bytes - Address of Root Bucket

               This field contains the bucket address of the Root
               bucket  for  the  index  associated  with this key
               descriptor.  The 32  bit  VBN  is  stored  in  the
               manner described in Section 7.2.1.1.



               7.3.1.11  K$FLGS 1 Byte - Key Descriptor Flags

               This field contains a bit vector for  the  various
               key options supported by RMS as follows:

               XB$DUP    Duplicate key values allowed

               XB$CHG    Key  value   may   change   on   $UPDATE
                         operation

               XB$NUL    Null key character enabled (K$NULL)

               XB$INI    Index must be initialized

               When the  XB$INI  bit  is  set  the  K$LVBN  field
               contains the following:

               K$LVBN   = C(K$DAN)
               K$LVBN+1 = C(K$IAN)
               K$LVBN+2 = C(K$LAN)
               K$LVBN+3 = 0 not used

               This information is used once only when the  index
               for  this  key  definition  is created.  Since the
               area number information is not normally stored  in
               the  in  memory data base for an open indexed file
               the required area numbers to create the index  are
               stored in the root bucket field for this once only
               operation.  The area numbers are not needed in the
               in   memory  data  base  since  on  future  bucket
               allocation the area number stored  in  the  bucket


     Files-11 On-Disk Structure                           Page 68


               which is "splitting" is used as the area number to
               allocate  the  new  bucket   from   (see   section
               7.5.1.1.2).



               7.3.1.12  P$FLGS 1 Byte - Prologue Flags

               This field  is  a  symbolic  redefinition  of  the
               K$FLGS   field   for  use  by  the  Relative  file
               organization.  Bits defined for this field are:

               PR$NEX    Error encounted extending Relative  file
                         no further extending is possible.



               7.3.1.13  K$DTP 1 Byte - Data Type for Key

               This field contains the data type of the key field
               within  the  user  data  records.   The only legal
               value  currently  for  RMS-11  is   XB$STG.    The
               following data types are defined.

               XB$STG    String data type (unsigned 8-bit bytes)
               XB$IN2    Signed 15 bit integer (2-bytes)
               XB$BN2    Unsigned 16 bit binary (2 bytes)
               XB$IN4    Signed 31 bit integer (4-bytes)
               XB$BN4    Unsigned 32 bit binary (4-bytes)
               XB$PAC    Packed decimal (1-16 bytes)



               7.3.1.14  K$NSEG 1 Byte - Number  of  Segments  in
               Key

               This field contains the number of segments (1 - 8)
               that  make  up  the  definition of the logical key
               field.  The XB$IN2, XB$BN2,  XB$IN4,  XB$BN4,  and
               XB$PAC  key  field data types may only contain one
               (1) segment.



               7.3.1.15  K$NULL 1 Byte - "NULL" Character

               This field contains a  user  specified  character.
               If the key field within the data record associated
               with this  key  descriptor  contains  only  "null"
               characters  the  record  will not be inserted into
               the associated Index.  The "null"  value  for  the
               XB$IN2,  XB$BN2,  XB$IN4,  XB$BN4,  and XB$PAC key
               field data types is defined  as  zero  (0).   This
               field  is  enabled by the XB$NUL bit in the K$FLGS
               and is only valid for alternate keys.


     Files-11 On-Disk Structure                           Page 69


               7.3.1.16  K$KYSZ 1 Byte - Total Key Size

               This field contains the sum of all the key segment
               sizes  to yield the total size of the key field in
               bytes (1 - 255).



               7.3.1.17  K$KEY 1 Byte - Key of Reference

               This field contains the key of reference number (0
               -  254) for this key descriptor.  Primary key = 0;
               alternate keys = 1 - 254.



               7.3.1.18  K$MINL 2 Bytes - Minimum Record Length

               This field contains the minimum length  record  in
               bytes to contain the complete key field.



               7.3.1.19  K$IFIL 2 Bytes - Index Fill Quantity

               This field contains the number of bytes to use for
               index level buckets (levels 1 - n) before a bucket
               split is considered when the user requests RMS  to
               follow fill quantities.



               7.3.1.20  K$DFIL 2 Bytes - Data Fill Quantity

               This field contains the number of bytes to use for
               user level buckets (level 0) before a bucket split
               is considered when the user requests RMS to follow
               fill quantities.



               7.3.1.21  K$POS  16  Bytes - Key  Segment   Offset
               Positions

               This  is  a  set  of  eight  (8)  2  byte   fields
               (K$POS0-K$POS7)  which contain the relative offset
               (0 - n) into the data record for each key segment.


     Files-11 On-Disk Structure                           Page 70


               7.3.1.22  K$SIZ 8 Bytes - Key Segment Size

               This is a set of 8 1 byte  fields  (K$SIZ0-K$SIZ7)
               which  contain  the  size  in  bytes  for  the key
               segment.



               7.3.1.23  K$KNM 32 Bytes - Key Name

               This is a 32 byte string supplied by the user when
               the key was defined.  If not supplied will contain
               NULLS.



               7.3.1.24  K$LDVB 4 Bytes - First Data Bucket

               This field contains  the  bucket  address  of  the
               first   bucket   at   the  data  level  (level  0)
               associated with this key descriptor.   This  field
               is  not supported by RMS-11 release 1 and contains
               a zero.



               7.3.1.25  14 Spare Bytes -



               7.3.1.26  P$AVBN  1  Byte - VBN  of   First   Area
               Descriptor

               This field contains the VBN (2 - 255) of the first
               Allocation Area descriptor block.  Allocation Area
               descriptor blocks are virtually contiguous and are
               directly  accessed  by  area  number.  See Section
               7.2.3.



               7.3.1.27  P$AMAX 1 Byte - Maximum Number of Areas

               This field contains the maximum number of  defined
               Allocation  Area  descriptors  ( 1 - 255) for this
               file.  Eight (8) Allocation  Area  descriptor  can
               fit  in a virtual block since each area descriptor
               is 64 bytes long.  The file address  of  any  Area
               descriptor may be calculated as follows:

               Let:      a = area number (0 - 254)
                         v = VBN address for a
                         o = offset into v for a

               Then:     v = a/8 (truncated) + c(P$AVBN)


     Files-11 On-Disk Structure                           Page 71


                         o = (a mod 8)*64



               7.3.1.28  P$DVBN 4 Bytes - Address of  First  Data
               Bucket

               This field contains the 32 bit VBN  of  the  first
               data bucket in a Relative file.



               7.3.1.29  P$LMRN 4 Bytes - Maximum Record Number

               This field contains  the  user  specified  maximum
               record  number  which  will  be  allowed  on  $PUT
               operations to the Relative file organization.   If
               the  user specifies 0 then this field will contain
               the maximum record number possible (2**31-1).



               7.3.1.30  P$LEOF 4 Bytes - EOF VBN

               This field contains the  last  initialized  (i.e.,
               zeroed)  VBN  (i.e., the EOF VBN) for the Relative
               file organzation.



               7.3.1.31  P$VERN 2 Bytes - Prologue Version Number

               This field contains  a  prologue  version  nubmer.
               The only legal value at this time is one (1).



               7.3.1.32  392 Bytes - Reserved for Future Use



               7.3.1.33  2 Bytes - Prologue Checksum (see 7.2)


     Files-11 On-Disk Structure                           Page 72


               7.3.1.34  Prologue Block 1 Layout -


               |---------------------------------------|
               |           VBN For Next Key            | K$NLVB
               |--                                   --|
               |              Descriptor               |
               |---------------------------------------|
               |       Offset To Next Key Descp.       | K$NBYT
               |---------------------------------------|
               |                                       | K$IAN
               |---------------------------------------|
     K$LVL     |     Root Level    |    Data Area #    | K$DAN
               |---------------------------------------|
     K$DBKS    |     Data Bkts     |     Index Bkts    | K$IBKS
     P$DBKS    |       Size        |       Size        |
               |---------------------------------------|
               |               Root Bucket             | K$LVBN
               |--                                   --|
               |                 Pointer               |
               |---------------------------------------| K$FLGS
     K$DTP     |     Data Type     |       Flags       | P$FLGS
               |---------------------------------------|
     K$NULL    | "NULL" Character  | # of key segments | K$NSEG
               |---------------------------------------|
     K$KEY     |    Key Of Ref.    |   Total Key Size  | K$KYSZ
               |---------------------------------------|
               |         Minimum Record Length         | K$MINL
               |---------------------------------------|
               |          Index Fill Quantity          | K$IFIL
               |---------------------------------------|
               |           Data Fill Quantity          | K$DFIL
               |---------------------------------------| 
               |                                       |
               |           Key Field Segment           |
               !                                       |
               |            Offset Positions           | K$POS
               |                                       |
               |            (K$POS0-K$POS7)            |
               |                                       |
               |                                       |
               |---------------------------------------|
               |                   :                   | K$SIZ
               |       Key Field Segment Sizes         |
               |           (K$SIZ0-K$SIZ7)             |
               |                   :                   |
               |---------------------------------------|
               |            Key Name String            |
               |               (32 Bytes)              | K$KNM
               |                                       |
               |---------------------------------------|
               |           First Data Bucket           | K$LDVB
               |--                                   --|
               |                Pointer                |
               |---------------------------------------|


     Files-11 On-Disk Structure                           Page 73


               /            Spare (14 Bytes)           /
               |                                       |
               |---------------------------------------|
     P$AMAX    |     Max Area #    | VBN Of 1st Area   |P$AVBN
               |---------------------------------------|
               |      Start VBN of 1st Data Bucket     | P$DVBN
               |--                                   --|
               |          (relative file only)         |
               |---------------------------------------|
               |             Maximum Record            | P$LMRN
               |--                                   --|
               |                Number                 |
               |---------------------------------------|
               |         Relative File EOF VBN         | P$LEOF
               |--                                   --|
               |    (Last Initialized VBN - Zeroed)    |
               |---------------------------------------|
               |        Prologue Version Number        | P$VERN
               |---------------------------------------|
               |                                       |
               /           Spare (392 Bytes)           /
               |                                       |
               |---------------------------------------|
               |            Block Checksum             | 
               |            Byte Offset 510            |
               |---------------------------------------|



     7.3.2  Alternate Key Prologue Blocks -

     Alternate key prologue blocks are chained  together  through
     the  K$NLVB  field  of  the  key  descriptors  (see  Section
     7.2.1.1).  Five alternate key descriptors can fit in a VBN.






     7.3.3  Area Descriptor Prologue Blocks -

     The  Indexed  file  organization  requires   a   method   of
     allocating  the  virtual blocks  of  the file to the various
     usages  within  the  file  (e.g.,  Index  buckets  and  Data
     buckets).   The  structure  which  allows this virtual block
     allocation management is the Area Descriptor.   The  Indexed
     file  supports  multiple  allocation  areas  to  achieve the
     following user file design capabilities:

     1.  Different bucket sizes between  the  index  buckets  and
         associated data buckets.


     Files-11 On-Disk Structure                           Page 74


     2.  Different index and data  bucket  sizes  on  a  per  key
         basis.

     3.  Allocation placement control for the various elements of
         the file.


     Eight area descriptor can be contained in a  virtual  block,
     and  all  the  area descriptor prologue blocks are virtually
     contiguous (see Sections  7.3.1.26  and  7.3.1.27  for  more
     details).



     7.3.3.1  Spare 1 Byte -



     7.3.3.2  A$FLG 1 Byte - Flags (not used)



     7.3.3.3  A$AID 1 Byte - Area Number (0 - 254)

               This byte contains the Area's number and  is  used
               as  a  redundancy check since all area descriptors
               are located at a fixed relative  position  to  the
               start of the Area Descriptor prologue blocks.



               7.3.3.4  A$BKZ 1 Byte - Bucket Size for Area

               This field contains the  areas's  bucket  size  in
               blocks  (1  -  32)  which  is  the  granularity of
               allocation.



               7.3.3.5  A$VOL 2 Byte - Relative Volume Number

               This field contains the relative volume number for
               the  last file extend for this area when placement
               control was requested.



               7.3.3.6  A$ALN    1    Byte - Extend    Allocation
               Alignment

               This field contains the allocation alignment  used
               for the last file extend for this area.

               Legal values for this field are:


     Files-11 On-Disk Structure                           Page 75


               0         placement control not requested
               XB$CYL    cylinder alignment (not implemented)
               XB$LBN    logical block alignment
               XB$VBN    virtual block alignment
               XB$RFI    allocate close to related file  
                         by FID  (not implemented)



               7.3.3.7  A$AOP 1 Byte - Alignment Options

               This field contains option  bits  to  qualify  the
               A$ALN field.  Legal values are as follows:

               XB$HRD    Alignment is absolute and  fail  if  not
                         available  (note:  illegal for XB$VBN or
                         XB$RFI alignment).

               XB$CTG    Allocation is to be contiguous.



               7.3.3.8  A$AVL  4   Bytes - Available   (Returned)
               Buckets

               This field contains the 32 bit VBN  of  the  first
               available  bucket  in  a chain (linked through the
               first 4 bytes of the  bucket)  of  buckets.   This
               chain  of buckets would be the result of returning
               buckets  back  to  the  area.   The  returning  of
               buckets  is not currently supported by RMS so that
               the only legal value for this field is zero (0).



               7.3.3.9  A$CVB 4  Bytes - Start  VBN  for  Current
               Extent

               This field contains the 32 bit start VBN  for  the
               current  extent.  The current extent is the extent
               from which buckets will be allocated.



               7.3.3.10  A$CNB  4  Bytes - Number  of  blocks  in
               Current Extent

               This field contains the number of blocks that were
               allocated to this current extent.  The combination
               of A$CVB and  A$CNB  describes  in  virtual  block
               terms  the result of the file extend operation for
               the current extent.


     Files-11 On-Disk Structure                           Page 76


               7.3.3.11  A$NUS 4 Bytes - Number of blocks used

               This field contains the number of blocks that have
               been allocated from the current extent.



               7.3.3.12  A$NVB 4 Bytes - Next VBN to Use

               This field contains the 32 bit VBN to use for  the
               start  VBN  of  the next bucket allocated from the
               current extent.



               7.3.3.13  A$NXT  4  Bytes - Start  VBN  for   Next
               Extent

               This field contains the 32 bit start VBN  for  the
               next  extent.   When the current extent is used up
               the next extent is made the current extent and the
               next  extent  description is zeroed.  The area can
               only be extended when the next extent  description
               is zero.



               7.3.3.14  A$XBY 4 Bytes - Number of blocks in Next
               Extent

               This field contains the number of blocks that were
               allocated  to  this next extent.  Thie combination
               of A$NXT and  A$XBY  describes  in  virtual  block
               terms  the result of the file extend operation for
               the next extent.



               7.3.3.15  A$DEQ 2 Bytes - Default Extend Quantity

               This field contains  the  user  specified  default
               file  extend quantity to be used whenever the area
               is to be extended by RMS.  A value of 0 means  use
               the  file's  DEQ.   However,  in no case will less
               than one bucket size for this area be requested.



               7.3.3.16  Reserved 2 Bytes -


     Files-11 On-Disk Structure                           Page 77


               7.3.3.17  A$LOC 4 Bytes - Start LBN on Volume

               This field contains the start logical block number
               for the last extent performed for this area.



               7.3.3.18  A$RFI 6 Bytes - Related File ID

               This field contain the FID of a related  file  for
               the   XB$RFI  allocation  alignment  (A$ALN)  (not
               implemented)



               7.3.3.19  Spares 12 Bytes -



               7.3.3.20  A$CRC 2 Bytes - Checksum

               This field is a dummy field to pad  out  the  area
               decriptor  to  64  bytes.   This  also  allows the
               standard Files-11 checksum to  be  stored  in  the
               last word of the Area Descriptor Prologue block.


     Files-11 On-Disk Structure                           Page 78


     7.3.3.21  Area Descriptor Layout -

               |---------------------------------------|
     A$FLG     |        Flags      |      Spare        |
               |---------------------------------------|
     A$BKZ     |     Bucket Size   |    Area Number    |  A$AID
               |---------------------------------------|
               |         Relative Volume Number        |  A$VOL
               |---------------------------------------|
     A$AOP     |    Align Options  |   Alloc. Align.   |  A$ALN
               |---------------------------------------|
               |            Available Bucket           |  A$AVL
               |                  List                 |
               |---------------------------------------|
               |             Start VBN For             |  A$CVB
               |             Current Extent            |
               |---------------------------------------|
               |           Number Of VBN's In          |  A$CNB
               |             Current Extent            |
               |---------------------------------------|
               |          Number Of VBN's Used         |  A$NUS
               |           In Current Extent           |
               |---------------------------------------|
               |           Next VBN To Use For         |  A$NVB
               |             Current Extent            |
               |---------------------------------------|
               |             Start VBN For             |  A$NXT
               |              Next Extent              |
               |---------------------------------------|
               |           Number Of VBN's In          |  A$XBY
               |              Next Extend              |
               |---------------------------------------|
               |         Default Extend Quantity       |  A$DEQ
               |---------------------------------------|
               |                 Spare                 |
               |---------------------------------------|
               |           Start LBN For Last          |  A$LOC
               |          Extend For This Area         |
               |---------------------------------------|
               |               File ID For             |  A$RFI
               |            Related File For           |
               |              File Extends             |
               |---------------------------------------|
               |                                       |
               |                                       |
               |                 Spares                |
               |               (12 Bytes)              |
               |                                       |
               |                                       |
               |---------------------------------------|
               |  Dummy Field To Allow Block Checksum  |  A$CRC
               |---------------------------------------|


     Files-11 On-Disk Structure                           Page 79


     7.4  Sequential File Format

     The RMS Sequential file is compatible with the FCS Fixed and
     Variable  length  record files.  Please refer to Section 6.2
     through 6.2.3.  The RMS variable  with  Fix  Control  record
     format  is a generalization of the Sequenced Varialbe Length
     Records of FCS (Section 6.2.3) in  that  the  fixed  control
     area (always 2 bytes for FCS) can be varied between 1 to 255
     bytes.



     7.5  Relative File Format

     The Relative file currently uses virtual block one  (1)  for
     its  prologue,  and starts its data buckets at virtual block
     2.   Records  are  stored  in  fixed  length  cells   within
     unformated buckets (no overhead bytes in bucket) starting at
     byte 0 and packed end to  end  (i.e.,  byte  aligned).   The
     virtual  blocks within the relative file must be initialized
     (zeroed) when they are allocated  to  the  file  to  support
     deleted record control.



     7.5.1  Relative File Record Formats -

     Records are stored in fixed length cells.  The first byte of
     each  cell  is a record control byte used to provide deleted
     record control.  The following bits are defined:

             DC$DEL record has been deleted
             DC$REC record exists

     A value of 0  indicates  the  cell  has  never  contained  a
     record.

     The relative file supports variable and variable with  fixed
     control  length  record  up  to  the required user specified
     Maximum Record  Size  (MRS).   In  these  cases  the  record
     control byte is followed with a two byte binary count of the
     bytes in the record (the count does not include itself).  If
     the  cell  size  does not evenly divide the bucket size then
     the remaining space in the bucket is dead space and the next
     record  in  the file will be stored in the first cell of the
     next bucket.  In  other  words  records  never  span  bucket
     boundaries.


     Files-11 On-Disk Structure                           Page 80


     7.5.1.1  Fixed Length Records -

               ---------------------------
               | ctrl | data (mrs bytes) |
               ---------------------------

               cell size = MRS+1



     7.5.1.2  Variable Length Records -

               ---------------------------------------
               | ctrl | size | data (size bytes) |   |
               ---------------------------------------

               cell size = MRS+3



     7.5.1.3  Variable With Fixed Control Records -

     ----------------------------------------------------------
     | ctrl | size | fixed | data (size-fixed ctrl bytes) |   |
     ----------------------------------------------------------

          cell size = MRS+fixed ctrl size+3



     7.6  Indexed File Format

     The Indexed File uses virtual blocks 1, 2 and  if  necessary
     up  to  and including 84 as a maximum for its prologue.  The
     current implementation  on  the  PDP-11  will  result  in  a
     prologue of the following forms:

                 Single Key

                    |-----------------------------|       
                    |         Primary Key         |
     VBN 1          |         Description         |
                    |                             |
                    |-----------------------------|
                    |    P$AMAX    |    P$AVBN    |----
                    |-----------------------------|   |
                    |                             |   |
                    |-----------------------------|   |
                                                      |
                                                      |
                    |-----------------------------|   |
     VBN 2          |                             |<---
                    |       Area Descriptors      |
                    |        (Up To 8) For        |
                    |   single key 4 is all that  |


     Files-11 On-Disk Structure                           Page 81


                    |         can be used         |
                    |-----------------------------|
     VBN3-N         |-----------------------------|
                    |        Index and Data       |
                    |           Buckets           |
                    |                             |
                    |-----------------------------|



               Multiple Key

                    |-----------------------------|
     VBN 1          |          Primary Key        |----
                    |          Descriptor         |   |
                    |                             |   |
                    |-----------------------------|   |
                    |    P$AMAX    |    P$AVBN    |   |
                    |-----------------------------|   |
                    |                             |   |
                    |-----------------------------|   |
                                                      |
                    |-----------------------------|   |
     VBN 2          |                             |<---
                    |                             |
                    |          Up To 5 Key        |
                    |          Descriptors        |
                    |                             |
                    |-----------------------------|
                    |       Key 5 Descriptor      |----
                    |                             |   | 
                    |-----------------------------|   |  
     If more than 5 alternate keys                    |
                                                      |
                    |-----------------------------|   |
     VBN 3          |                             |<---
                    |        Key Descriptors      |
                    |             etc.            |
                    |                             |
                    |-----------------------------|
                              .
                              .
                              .
                    |-----------------------------|
     VBN P$AVBN     |       Area Descriptors      |
                    |       8 Per Block           |
                    |                             |
                    |-----------------------------|

     index and data bucket space starts at:

     ((P$AMAX/8(truncated))+P$AVBN)

     Records  are  stored  in  formatted  buckets  (buckets  have
     overhead  bytes)  and  are  packed  end  to  end (i.e., byte


     Files-11 On-Disk Structure                           Page 82


     aligned).  The bucket format and the various record  formats
     are given in the following sections.



     7.6.1  Index Structure -

     The Index is structured as a balanced tree.   The  nodes  in
     the  tree  are buckets, and the nodes are serially searched.
     The Index  node  contains  index  records  as  specified  in
     Section 7.5.2.1.

     The bucket size is constant for  index  nodes,  but  may  be
     different  than  the Data buckets.  The Data buckets are all
     the same size.

     Each level of the index is horizontaly linked via  the  Next
     bucket  pointers.   The  horizontal linking is circular with
     the last bucket (noted by BC$LBK) pointing back to the first
     bucket.   The Data buckets for an Index may be viewed as the
     data level (set) of the index and are  linked  in  the  same
     manner  as  buckets in any other level of the Index.  Figure
     7-2 shows the structure of the Index.

     The key value associated with  index  records  (see  Section
     7.5.2.1) is the highest or highest possible key value in the
     bucket pointed to by the bucket pointer in the record.

     The basic search rule for an index search is to  follow  the
     first path for which the search key is equal to or less than
     the key value stored in the index record.



     7.6.1.1  Primary Key Index Structure -

     The primary key index for a file is structured as stated  in
     Section  7.5.0  above  where  the  data level is composed of
     buckets which contain the User's  data  records.   The  data
     buckets may also contain RRV records.  See Section 7.5.3 and
     7.5.2.3 for details on RRV records.



     7.6.1.2  Alternate Key Index Structure -

     An alternate key index for a file is structured as stated in
     Section  7.5.0  above  where  the  data level is composed of
     buckets which contain pointer array records as specified  in
     Section  7.5.2.4.   Therefore the indices within the Indexed
     File Organization have the same structure,  where  only  the
     interpretation  of  the  records within the data level of an
     index is different.


     Files-11 On-Disk Structure                           Page 83


     7.6.2  Record Reference Vector (RRV) -

     When a record is inserted in an Indexed file the  record  is
     assigned  a  reference  vector  address  and this address is
     stored in the data record in the record pointer  field  (see
     Section  7.5.2.2).   This  address is the initial address of
     the  record  itself.   Whenever  the  record  is  moved  the
     record's  reference  vector  record  is updated with its new
     address.  The record, in turn, points back to its  reference
     vector  so  that  it  can  be updated if the record is moved
     again.  The reference vector  record  is  created  when  the
     record  is  moved  for the first time.  Using this technique
     the worst case indirection for a record is kept at one,  and
     we  can  always  find  the  record  via its reference vector
     address.

     The  record  pointers   used   within   the   Indexed   file
     organization,  and  the RFA (Record's File Address) returned
     to the user in the RFA field  of  the  RAB  are  always  the
     record's reference vector address.

     The space required for RRV pointers in the data records of a
     file  is  required  to  insure  RFA addressing and alternate
     keys.  The RRV records are stored at the  end  of  the  data
     records  in  the  user  data  buckets.  The use of RRV's and
     secondary indices is graphically shown in Figure 7-3.



     7.6.3  Bucket Format -

     The Indexed organization uses  a  formatted  bucket  as  its
     primary  unit  of seondary storage.  A bucket is composed of
     some number of virtual blocks in the range of 1-32 and has a
     header starting at byte one of the bucket.

     The Bucket is composed of  three  logical  areas,  a  Header
     area, a Record storage area and a Free space area.

     Each of these areas will be described in the  sections  that
     follow.



               7.6.3.1  Header Area -

               The bucket header area is composed of a  RAS  data
               section,  a  bucket storage control section, and a
               structure link section.  The size  of  the  bucket
               header is 14 bytes (S$BHD).


     Files-11 On-Disk Structure                           Page 84


               7.6.3.1.1  B$CHK 1 Byte - Check Byte

               This is a one byte check  character.   Whenever  a
               bucket  is  written the value in the check byte is
               changed and copied  into  the  last  byte  of  the
               bucket.   Whenever a bucket is read the check byte
               is compared to the copy  for  equality.   By  this
               technique  hardware  failures  during transfer are
               detectable (i.e., the BUS breaks etc.).



               7.6.3.1.2  B$TAA 1 Byte - This Allocation Area

               This field contains  the  allocation  area  number
               that this bucket was allocated from.



               7.6.3.1.3  B$ADR 2 Bytes - Bucket Address Sample

               This  is  a  sample  of  the  bucket's  start  VBN
               address,  and is composed of the low order 16 bits
               of that  address.   This  field  is  written  upon
               bucket  formatting,  and  is  checked whenever the
               bucket is read into main memory.



               7.6.3.1.4  B$NBY 2 Bytes - Next Available Byte

               This field contains the byte address  relative  to
               the  start of the bucket of the first free byte in
               the Free Storage Area of the bucket.



               7.6.3.1.5  B$NID 1 Byte - Next Available ID

               This field contains the ID number to use  for  the
               next record placed in the bucket.



               7.6.3.1.6  B$LID 1 Byte - Last Available ID

               This field contains the ID number of the  last  ID
               in  the  contiguous range of ID's specified by the
               contents of B$NID and B$LID.  When the contents of
               B$NID are greater than the contents of B$LID or is
               zero then there is no "next" available  ID.   When
               this  condition  occurs  the  bucket is scanned to
               find the largest contiguous range of  unused  ID's
               and  B$NID  and B$LID are updated to describe that
               range.


     Files-11 On-Disk Structure                           Page 85


               7.6.3.1.7  B$NBK 4 Bytes - Next Bucket Pointer

               This field contains the  start  VBN  of  the  next
               bucket   at  this  level  of  the  index  or  data
               partition for the Indexed file organization.  This
               pointer  always  points  to  a  bucket of the same
               size.



               7.6.3.1.8  B$LEV 1 Byte - Level Number for Bucket

               This field contains the level number  relative  to
               the data level for this bucket, in the index.  The
               Data level buckets contain a 0, the  lowest  level
               buckets  of  the index contain a 1, the next level
               buckets going towards the root contain a 2 etc.




                                      NOTE

                   "Data buckets" refer to the buckets  which
                   contain  the  data records associated with
                   the index.  For the  primary  index  these
                   are  the  user  data  records, and for the
                   alternate  index  these  are  system  data
                   records which contain an array of pointers
                   to user data records.





               7.6.3.1.9  B$BCB 1 Byte - Control Bits

               This is a bit encoded byte field and  is  used  in
               the  processing  of  a bucket.  The following bits
               are defined for the indexed file organization:

               BC$LBK - last bucket in level
               BC$ROT - root bucket of index



               7.6.3.2  Record Storage Area -

               The record storage area starts at the  first  byte
               after the bucket header area, and ends at the byte
               address stored in B$NBY  minus  one.   The  record
               structures  in  buckets  vary  with the use of the
               bucket.   Section  7.5.2  specifies  the   various
               record structures used.


     Files-11 On-Disk Structure                           Page 86


               7.6.3.3  Free Storage Area -

               The free storage area starts at the  byte  address
               stored  in  B$NBY and up to the check byte copy in
               the bucket.  Any and all free  storage  statistics
               refer   to  this  contiguous  free  storage  area.
               However  it  is  possible  due  to  "fast"  record
               deletions  to  have "free" space within the record
               storage area of the  bucket.   The  reclaiming  of
               this space is done on an as needed basis.



               7.6.3.4  S$BHD 14 Bytes - Size of Header Area

               This symbol represents  the  size  of  the  bucket
               header area.



     7.6.3.5  Bucket Format Layout -


               |---------------------------------------|
     B$TAA     |     This Area     |    Check Byte     |  B$CHK 
               |---------------------------------------|
               |         Bucket Address Sample         |  B$ADR
               |---------------------------------------|
               |          Next Available Byte          |  B$NBY
               |---------------------------------------|
     B$LID     |       Last ID     |      Next ID      |  B$NID 
               |---------------------------------------|
               |          Next Bucket Pointer          |  B$NBK 
               |              (Start VBN)              |
               |---------------------------------------|
     B$BCB     |         BCB       |       Level       |  B$LEV 
               |---------------------------------------|  S$BHD
               |                                       |
               |             Record Storage            |
               |                  Area                 |
               |                                       |
               |---------------------------------------| c(B$NBY)
               |                                       |
               |               Free Space              |
               |                  Area                 |
               |                                       |
               |-------------------|                   |
               |  Check Byte Copy  |                   |
               |-------------------|-------------------|


     Files-11 On-Disk Structure                           Page 87


     7.6.4  Record Structures -

     The following record structures apply to  the  Indexed  file
     organization.



     7.6.4.1  Index Bucket Record -

                       |------------|
                       |      |     |
                       | IRCB |  PS |  1 Byte
                       |      |     |
                       |------------|
                       |            |
                       |  Bucket    |  n Bytes
                       |  Pointer   |
                       |            |
                       |------------|
                       |            |
                       |  Key Value |  m Bytes
                       |            |
                       |------------|

               IRCB contains Index Record Control Bits

               The following bits are defined in the IRCB byte:

               IC$KCP    Compressed  key  value  (not   currently
                         defined).

               IC$EMP    Pointer to empty bucket.

               PS is the pointer size as follows:

                         0 = 2 byte bucket pointer
                         1 = 3 byte bucket pointer
                         2 = 4 byte bucket pointer
                         3 = undefined



               7.6.4.2  General Data Bucket Record -

               |-------------|
               | DRCB |  PS  |  1 Byte
               |-------------|
               |     ID      |  1 Byte
               |-------------|
               |   Record    |  N Bytes Optional
               |   Pointer   |
               |-------------|
               |    Size     |  No Size If Fixed Length Data
               |-------------|
               |             |


     Files-11 On-Disk Structure                           Page 88


               |    Data     |  M Bytes
               |             |  M = Size or Fixed Length
               |-------------|

               DRCB contains Data Record Control Bits

               The following bits are defined in the DRCB byte:

               DC$DEL    Record deleted, or  pointer  to  deleted
                         record.

               DC$RRV    Record reference vector record.

               DC$NPS    No pointer size field present (qualifies
                         PS)

               DC$KDL    Pointer to record for this key no longer
                         applies  $UPDATE  changed  the  key, but
                         record exists;  note ID will  be  zeroed
                         on  all  systems starting with Release 1
                         on RSX-11M V3.

               DC$NCP    Do not compress this deleted record.

               PS is the pointer size for the Record  pointer  as
               follows:

                         0 = 3 byte record pointer
                         1 = 4 byte record pointer
                         2 = 5 byte record pointer
                         3 = undefined



     7.6.4.3  RRV Records -

     Record Reference Vector  (RRV)  records  are  records  which
     point  to  the  record associated with the reference vector.
     They function  as  "forwarding  addresses"  for  the  actual
     records when they are moved.

     The format is as follows:

               |-----------|
               | DRCB | PS |
               |-----------|
               |    ID     |
               |-----------|
               |  Record   |
               |  Pointer  |
               |-----------|

     where the DC$RRV bit is set in the DRCB field.


     Files-11 On-Disk Structure                           Page 89


     7.6.4.4  Deleted RRV Records -

     The RRV record for a deleted record can be as small  as  the
     first  two  bytes  of  the  RRV  record.   In  this case the
     following DRCB bits are set:

               DC$RRV
               DC$NPS
               DC$DEL



               7.6.4.5  Secondary  (or  Alternate)   Index   Data
                        Record  (SIDR)  For  Which Duplicate Keys
                        Are Allowed -

     The data records associated  with  an  alternate  index  are
     pointer arrays to the users data records.  The format of the
     record is as follows:

     - - - - -    |--------------------|
                  |      DRCB     | PS |  1 Byte
                  |--------------------|
     Data Record  |         ID         |  1 Byte
                  |--------------------|
                  |   Duplicate Count  |  4 Bytes (DC$NPS=0)
                  |--------------------|
     Overhead     |        Size        |  2 Bytes
     - - - - -    |--------------------|
                  |     Key Value      |  M Bytes
                  |--------------------|
     Data         |     SIDR Record    |  X Byte    Pointer
      on          |     Pointer #1     |            Array
     Record       |--------------------|
                  |     SIDR Record    |  Y Bytes    record
                  |     Pointer #2     |
                  |--------------------|
                  |         .          |
                  |         .          |
                  |         .          |
                  |--------------------|
                  |     SIDR Record    |  Z Bytes
                  |     Pointer #K     |
     - - - - -    |--------------------|

     Fields within the pointer array record:


     PS        This field contains  the  size  of  the  duplicate
               count field as follows

               0 = 3 bytes
               1 = 4 bytes **THIS IS THE ONLY VALUE USED**
               2 = 5 bytes
               3 = undefined


     Files-11 On-Disk Structure                           Page 90


     DRCB      Bits used for pointer array records

               NC$NPS    If this bit is  set  then  there  is  no
                         duplicate count field.  This is used for
                         all array continuations  records,  since
                         the count applies to the total array.






     7.6.4.6  Secondary  (alternate)  Index  Data  Record  -   No
              Duplicates -

     The data records associated  with  an  alternate  index  for
     which  duplicate  key  values  are  not  allowed is shown in
     Section 7.5.2.4 except that the  duplicate  count  field  is
     omitted  (DC$NPS=1)  and  there  is  only  one  SIDR  Record
     Pointer.


                                 NOTE

         When a record is  deleted  the  No  Duplicates  SIDR
         record  is  compressed  out of the secondary index's
         data bucket at the time of the delete.





     7.6.4.7  SIDR Record Pointers -

     The format of the record pointers used  in  Secondary  Index
     Data Records is as follows:

     - - - - - -------------
     Overhead  | DRCB | PS | 1 Byte
     - - - - - -------------
     Record    |  Record   | N Bytes
     Pointer   |  Pointer  |
     3-5 bytes |           |
     - - - - - -------------

     DRCB bits used for SIDR record pointers:

               DC$KDL    Pointer has  been  deleted  due  to  key
                         change  on a $UPDATE operation.  In this
                         case  the  ID  portion  of  the   record
                         pointer will be zero.

               DC$DEL    Record associated with this pointer  has
                         been deleted.


     Files-11 On-Disk Structure                           Page 91


                    Figure 7-2

                    Index Structure



                        Root
                   --------------
                   | |          |
                   | | Ki .. Kx |
                   | | |       ||
                   --------------
                       |       |
             |----------       |
             ||---------------||
             V|               VV
             --------------   --------------
             | |          |   | |          |
             | |Kab .. Ki |...| |          |
             | | |     |  |   | |          |
             --------------   --------------
             ^   |     |      |
             |----------------|
                 |     |
                 .     .
                 .     .
                 .     .
             |---|     |------|
             |                |
             V                V
             --------------   --------------
             | |          |   | |       |  |
             | | .... Kab |...| |  .... |Ki|
             | |       |  |   | |       |  |
             --------------   --------------
                       |                |
                       |                |
                       |                |
             |----------                |
             |                          |
             V                          V
             --------------             --------------
             | |   |Kab | |             | |     | Ki |
             | |...|data| | ......      | |.....|data|
             | |   |    | |             | |     |    |
             --------------             --------------



     NOTES:

     All buckets in a level are linked horizontally from left  to
     right via next bucket pointers (see Section 7.5.1.1.7).


     Files-11 On-Disk Structure                           Page 92


     CASE 1:  Record Has Never Moved

              ---- Pointer In Secondary Index
              |    Pointer Array
              |
              V
             ------------------
             |    DRCB   | PS | <---
             ------------------    |
             |        ID      |    |
             ------------------    |  User Data Record
             | Record Pointer |-----
             |    (RRVP)      |
             ------------------
             |     Data       |  RRVP = Records Reference
             ------------------  Vector Pointer

     CASE 2:  Record Has Moved

              ---- Pointer In Secondary Index
              |    Pointer Array
              |
              V
             ------------------
             |    DRCB   | PS |<------- Record Reference
             ------------------       |  Vector
             |        ID      |       |
             ------------------       |
             | Record Pointer |----   |
             ------------------   |   |
                                  |   |
              ---------------------   |
              |                       |
              |                       |
              V                       |
             ------------------       |
             |    DRCB   | PS |       |
             ------------------       |
             |        ID      |       |
             ------------------       |
             | Record Pointer |--------
             |    (RRVP)      |        User Data Record
             ------------------
             |     Data       |
             ------------------

                Figure 7-3

                RRV Usage


     [End of ODS2.RNO]