8080.DOC

	Macro package for MACRO-11 to assemble 8080 mnemonic code


The 8080 cross assembly macro and acompanying programs are part of a
masters thesis for Worcester Polytechnic Institute in Worcester,
Massachusetts by Bruce Filgate. Although the entire thesis consisted of
the three herein contained pieces of software plus the design and construction
of the dedicated 8080 processor module, and transmitter/reciever interface for
the radio station, and a video display generator, only the the software
is presented here.  Additional information is available either from the
Worcester Polytechnic Institute library or from the author.


The floppy structure contains four files: 8080.DOC, this documentation;
8080.MAC, the macro library of conversions for 8080 mnemonics; BSRMDP.MAC,
a utility program written in Intel mnemonics to run on a modified DEC LAXX-NS;
and CODE.MAC, a program for Amateur radio usage written in Intel mnemonics.


8080.MAC :  This set of macros should be assembled with the user's
8080 mnemonic program.  A typical command would be:
		
.R MACRO
		*USER.BIN,USER.LST=8080.MAC,USER.MAC

	where	USER.BIN is the binary output
		USER.LST is the assembly listing output
		8080.MAC is the 8080 mnemonic macro file
		USER.MAC is the user's input file in Intel mnemonics

It is recommended that the MACRO-11 manual be used as a reference
document along with the sample programs contained herein.


BSRMDP.MAC :  This is a sample program written in 8080 mnemonics to run on
a specific 8080 hardware configuration (LAXX-NS).  The Program provides a 
loader/dumper and debug environment for a user's system.  The loader/dumper
is compatable with the binary file output from MACRO-11 with 8080.MAC.



CODE.MAC  :  This is a second sample program written in Intel 8080
mnemonics for the code/decode of both Morse code and radio teletype
(Baudot) and maintainance of an Amateur radio log book.  In general,
the assembly of a program the size of CODE.MAC in an LSI-11/RX01
enviornment requires a command of the form:

		.R MACRO
		*CODE.BIN,TT:=8080.MAC,CODE.MAC

The essential difference is that the listing is sent directly to the
terminal (could be a line printer LPT:) to conserve disk space.

For information on the program operation, consult the listing for
comments and operation instructions.  The CODE.MAC program requires
the LAXX-NS to substantially modified for full operation.  Prints for
modification are in the appendix to the published theses.