DYC - A Mapped RX03 Handler for TSX-plus



                              V2c 9-Sep-86



Author:  C G Wilson, 71 Galatea St, Charleville, Australia 4470.


DYC provides an RX03 (double-sided RX02) handler capable of  reading  or
writing  RX01  and  RX02  discs.   It  may  be used under RT-11, but was
primarily designed to run in high memory ("mapped") under TSX-plus, thus
saving low memory space.


This handler is designed for Sigma/Dilog RX03 controllers, with optional
assembly for MTI boards.  It may need minor modification (notably to the
extended addressing code) for other manufacturers' boards.

Full 22-bit addressing is used for either of these boards, removing  the
need for intermediate address buffers.


An SPFUN to allow formatting during  normal  system  operation  (without
requiring  access  to the I/O page) is included.  The handler may be run
as a  programme,  providing  the  formatting  options  with  no  further
programme being required.


DYC.TSX is designed for use as SY:DY.TSX, to replace the  DEC  or  S & H
DY.TSX on the system device.

DYC - Mapped RX03 Handler for TSX-plus                            Page 2














1.0  Assembly Options - DY$22B

If DY$22B is set non-zero  (default),  code  for  22-bit  addressing  is
included.  This unfortunately is controller dependent:

Sigma/Dilog DQ419:  (default)

     22 bit addressing is enabled by setting the <cs22bit>  bit  in  the
     command.   An  extra  <TR> phase is added to all cycles requiring a
     memory access.  In this cycle the high-order address is  passed  to
     the controller, as six bits right justified.  The bits <csma16> and
     <csma17> are not used.

MTI:  (select if MTI$$ is set non-zero)

     22 bit addressing is enabled by setting the <cs22bit>  bit  in  the
     command.   An  extra  <TR> phase is added to all cycles requiring a
     memory access.  In this cycle the  high  order  four  bits  of  the
     address are passed to the controller, right justified.  Bits 16 and
     17 still need to be set in the command word as  per  a  DEC  18-bit
     controller.

DYC - Mapped RX03 Handler for TSX-plus                            Page 3














2.0  Formatting

An SPFUN (code 200) is provided to allow formatting, with the  following
parameters:

     In Buffer:
                First byte:
                        If zero, format side zero
                        If non-zero, format size one
                Second byte:
                        If zero, use single density
                        If non-zero, use double density

     Block Number:      If zero, use soft formatting (header rewrite)
                        If non-zero, use hard formatting



The Sigma/Dilog protocol is assumed.  I hope this goes for all
 controllers:

    Command:
        10 + <20 if unit 1> + <400 if double dens> + <1000 for side 1>
    Followed by (in data register)
        111 for soft format, or 222 for hard format.

DYC - Mapped RX03 Handler for TSX-plus                            Page 4











3.0  Running DYC as a Programme

If DYC is run as a programme, it provides  formatting  capabilities  for
relatively  easy use, requiring no particular privileges under TSX-plus.
[If however you have users who may not access ".TSX" files on the system
device, make a copy of DYC.TSX called DY.SAV on SY:  and run that.]

This facility is best demonstrated by showing how to get the  HELP  text
for this programme:

.r dy.tsx
*/h
DY Commands:
        /H (without any file) - Type this text

        The device specified should be a DY floppy,
        write-enabled.
        /H - hard format;
        /F - soft format;
        /D - double density;
        /S - both sides.
             /S:0 - side 0 only (default);
             /S:1 - side 1 only.
        /I - initialize directory when formatted
             (default 4 segments), or
             /I:n for n segments (1 to 31.)
        /T - tell size of disc (in blocks)
        /Z - equivalent to /F/D/S/I
        (/D and /S imply /F unless /H is specified.
*



Examples:

.r dy.tsx
*dy:/z/h
        Hard formats an RX03 floppy and initializes it.

.r dy.tsx
*dy1:/t
        Tells the size of the floppy in dy1:.

.r dy.tsx
*dy1:/d/i
        Soft formats an RX02 floppy in dy1: and initializes it.

DYC - Mapped RX03 Handler for TSX-plus                            Page 5














4.0  TSMUNG - for modifying TSX plus

With the advent of TSX-plus version 6, no matter what  is  specified  in
the TSGEN file (eg DEVDEF <DY>,MAPH,HANBUF,DMA) TSX refuses to allow the
DY or the DU handler to be mapped into high memory.   This  is  fine  to
protect  people  trying  to do this with DEC or S & H handlers, but is a
nuisance when we have a legitimate handler capable of this performance.

A programme TSMUNG is provided.  This modifies the default values set up
for  the DU and/or DY devices.  It is run, using the name of the TSX.SAV
file to be modified appropriately.  To modify the DY value, append /Y to
the  filename.   (To modify the DU, append /U).  [No switches implies /U
only.]


        .Run TSMUNG
        *sy:tsx.sav/y
        Successful TSX modification
        .
or
        .Run TSMUNG sy:tsx.sav/y
        Successful TSX modification
        .



If it should be desired to run the DU handler mapped in addition to  the
DY  handler (WARNING - again, make sure your handler is capable of being
run mapped and is not the standard DEC or S & H handler), append a /U to
the filename in addition to the /Y.  For example:


        .Run TSMUNG du:tsx.sav/y/u
        Successful TSX modification
        .



If TSMUNG cannot find the relevant string of device  names  in  TSX,  it
will  tell  you  so.   If  this  is the case, you are probably trying to
operate upon a version of TSX different from that for which  TSMUNG  was
written (version 6.01).