Archived Data Recovered with MTLIB

                                       by

                              N. A. Bourgeois, Jr.





           Recently a client came to me with an old archive mag tape and

      requested that I recover some data from it.  The label on the reel

      indicated that the tape was written by ROLLIN.  Some of you other

      old timers may remember it.  ROLLIN was a utility on DEC's DOS/Batch

      operating system and later adapted by Michael Levine to load under

      RT-11.



           I tried to use the copy of ROLLIN on the clients system, a

      PDP-11/34 running RT-11 V5.0 and having two tape drives, but was

      unable to read the tape on either drive.  ROLLIN would not even

      produce a directory.  However, I could get the tape to skip past

      files.  So I positioned the tape to start reading the desired file

      and issued the ROLLIN command to read the file without rewinding and

      searching.  No luck, ROLLIN still would not read the tape.  During

      the course of these efforts I verified that the copy of ROLLIN was

      functional by writing to and then reading from a scratch tape.



           Since this particular client was licensed to use MTLIB, I

      turned to it.  First, I ran MTLIB's TAPLOG utility (Figure 1) to

      obtain a detailed record of the structure of the tape.  An

      abreviated and annotated copy of this log is given in Figure 2.



      Archived Data Recovered with MTLIB                            PAGE 2



      Since the file the client wished to recover was the third one from

      the start of the tape, I used MTLIB's MTAPE utility to space forward

      first past two EOF marks and then past two records.  This positioned

      the tape just before the first of 300 8192-byte data records.



           Next, I spent twenty minutes or so writing, compiling, and

      linking the first draft of MTLIB's latest utility, TAPROL (Figure

      3), to read the file.  Execution of TAPROL recovered the data for

      the client.  The recovered file turned out to be a 4800-block (RK05)

      disk image.  Then, access to his data was obtained using the RT-11

      MOUNT command.  The time from initial request to delivery of the

      data to the client was just under two hours.



           Both ROLLIN and RT-11 consume the computer, only one user may

      be active.  Once, I abandoned further attempts to use ROLLIN, I

      performed the task at hand under TSX-Plus without any further

      interference with the clients normal use of his machine.



                             Figure 1, TAPLOG.FOR.

            PROGRAM TAPLOG
      C
      C Copyright (C) 1984 NAB Software Services, Inc.

        The copyright owner grants permission to copy this software
        provided that the above copyright notice is included.  This
        software may not be sold or used in any commercial product.

      C
      C     Author:  N. A. Bourgeois, Jr.
      C
      C Sample application program for MTLIB.
      C
      C Read a magnetic tape and log the record number and the number of
      C bytes in each record.  A count of zero bytes indicates a tape
      C mark.  The tape may be in any arbitrary format and code.  The
      C output is sent to the file, DK:TAPLOG.DAT.  The program is


      Archived Data Recovered with MTLIB                            PAGE 3
      Figure 1, TAPLOG.FOR, continued


      C terminated when two consecutive tape marks are encountered.  The
      C tape is assumed to be mounted on device, MT0:.
      C
      C     Edit record:
      C
      C 16-Aug-84:  Original creation.
      C 22-Oct-84:  Added copyright notice.
      C 
            DIMENSION BUFFER(16384), MTUNIT(4)
      C
            INTEGER IBRC, IRET, EOFFLG, LUN, RCDNUM, READ, REWIND
      C
            LOGICAL*1 BUFFER, MTUNIT
      C
            DATA IBRC/16384/, EOFFLG/0/, LUN/30/, RCDNUM/0/, READ/1/, 
           *     REWIND/7/
            DATA MTUNIT/"115,"124,"060,"000/
      C
         10 FORMAT (' TAPLOG:  84h29a',/)
         12 FORMAT (' Record   Byte',/,' Number   Count',/)
         14 FORMAT (' ',I6,'  ',I6)
         16 FORMAT ('+',2I6)
         18 FORMAT (' TAPLOG:  All done',/)
      C
            TYPE 10
            CALL MTFOR (MTUNIT,REWIND)
            OPEN (ACCESS='SEQUENTIAL',NAME='DK:TAPLOG.DAT',UNIT=LUN)
            WRITE (LUN,12)
      C
        100 CONTINUE
                RCDNUM = RCDNUM + 1
                CALL MTFOR (MTUNIT,READ,IBRC,BUFFER,IRET)
                TYPE 16,RCDNUM,IRET
                WRITE (LUN,14) RCDNUM,IRET
                IF (IRET .GT. 0) EOFFLG = 0
                IF (IRET .EQ. 0) EOFFLG = EOFFLG + 1
                IF (EOFFLG .EQ. 2) GO TO 110
                GO TO 100
      C
        110 CONTINUE
                CALL MTFOR (MTUNIT,REWIND)
                CLOSE (UNIT=LUN)
                TYPE 18
                CALL EXIT
      C
            END


                             Figure 2, TAPLOG.DAT.

      Record   Byte
      Number   Count

           1      14          ! DOS/Batch file label record.
           2     512          ! Bootstrap for the mag tape.


      Archived Data Recovered with MTLIB                            PAGE 4
      Figure 2, TAPLOG.DAT, continued


           3   14336          ! ROLLIN memory image.
           4     512          ! Reel label record.
           5    8192          !
              .               ! 300 data records.
         304    8192          !
         305       0          ! Tape EOF mark
         306      14          !
         307     512          !
         308    8192          ! Apparantly ROLLIN was reexecuted
         309      14          ! after an unsuccessful initial
         310     512          ! attempt to write this file without
         311    8192          ! repositioning the tape.
              .               !
         610    8192          !
         611       0          ! EOF.
         612      14          ! File label record.
         613     512          ! Reel label record.
         614    8192          !
              .               ! Data records of desired file.
         913    8192          !
         914       0          ! EOF
         915      14
         916     512
         917    8192
              .
        1216    8192
        1217       0
        1218      14
        1219     512
        1220    8192
              .
        1519    8192
        1520       0
        1521      14
        1522     512
        1523    8192
              .
        1768    8192
        1769    3072
        1770       0
        1771      14
        1772     512
        1773    8192
              .
        2032    8192
        2033    3072
        2034       0
        2035      14
        2036     512
        2037    8192
              .
        2308    8192
        2309    3072
        2310       0
        2311      14


      Archived Data Recovered with MTLIB                            PAGE 5
      Figure 2, TAPLOG.DAT, continued


        2312     512
        2313    8192
              .
        2602    8192
        2603    3072
        2604       0          ! EOF.
        2605       0          ! EOF, indicating logical EOT.


                             Figure 3, TAPROL.FOR.

            PROGRAM TAPROL
      C
      C Copyright (C) 1984 NAB Software Services, Inc.

        The copyright owner grants permission to copy this software
        provided that the above copyright notice is included.  This
        software may not be sold or used in any commercial product.

      C
      C     Author:  N. A. Bourgeois, Jr.
      C
      C Sample application program for MTLIB.
      C
      C Read an ROLLIN disk image from a ROLLIN tape mounted on drive MT0
      C to a logical device.  The file name of the logical device file is
      C TAPROL.DSK.  The tape structure may be determined with TAPLOG.
      C The tape may be prepositioned with MTAPE.  The MOUNT command may
      C be used to access the recovered disk image.
      C
      C     Edit Record:
      C
      C 26-Nov-84:  Original creation.
      C 28-Nov-84:  Added request for input of the total number of records
      C              to read and zero fill of any short records.
      C
            DIMENSION
           *    BUFFER(8192), ! I/O data buffer.
           *    MTUNIT(4)     ! tape drive unit name.
      C
            INTEGER
           *    BYTCNT,       ! number of bytes per tape record.
           *    LUN,          ! output device logical unit number.
           *    RCDNO,        ! record number in output file.
           *    RDCNT,        ! number of bytes read from tape.
           *    READ,         ! mag tape read function.
           *    TOTRCD        ! total number of tape records to read.
      C
            LOGICAL*1
           *    BUFFER,
           *    MTUNIT
      C
            DATA
           *    BYTCNT        /8192/,
           *    LUN           /30/,


      Archived Data Recovered with MTLIB                            PAGE 6
      Figure 3, TAPROL.FOR, continued


           *    MTUNIT        /"115,"124,"060,"000/,
           *    READ          /1/
      C
          1 FORMAT (/,' MTUNIT:  84k28a',//)
          2 FORMAT (/,' MTUNIT:  All done',//)
         10 FORMAT ('+',I6,I6)
         11 FORMAT (I5)
      C
            TYPE 1
            CALL GTLIN (BUFFER,'Enter the number of records to copy')
            I = LEN (BUFFER)
            DECODE (I,11,BUFFER) TOTRCD
            OPEN (ACCESS = 'DIRECT',
           *    MAXREC = TOTRCD,
           *    NAME = 'DK:TAPROL.DSK',
           *    RECORDSIZE = BYTCNT/4,
           *    TYPE = 'NEW',
           *    UNIT = LUN)
      C
            DO 100 I = 1,TOTRCD
                RCDNO = I
                CALL MTFOR (MTUNIT,READ,BYTCNT,BUFFER,RDCNT)
                TYPE 10,RCDNO,RDCNT
                IF (RDCNT .EQ. BYTCNT) GO TO 90
                    DO 80 J = RDCNT+1,BYTCNT
                        BUFFER(J) = 0
         80         CONTINUE
         90     CONTINUE
                IF (RDCNT .EQ. 0) GO TO 110
                    WRITE (LUN'RCDNO) BUFFER
                CONTINUE
        100 CONTINUE
      C
        110 CONTINUE
            CLOSE (UNIT=LUN)
            TYPE 2
            CALL EXIT
            END


      *******************************************************************
      * N. A. Bourgeois, Jr. is the president of NAB Software Services, *
      * Inc., PO Box 20009, Albuquerque, NM 87154, (505) 298-2346.      *
      *******************************************************************