RT-11 Interrupt Service Routines
                       By the Rules and Otherwise
                                   or
                           Moral and Immoral








                          N. A. Bourgeois, Jr.
                      Sandia National Laboratories
                   Systems Engineering Division 1738
                             P. O. Box 5800
                         Albuquerque ,NM 87185








                                Abstract


             RT-11's prescribed protocol for  interrupt  service
        routines is briefly described.  More throughly described
        are  several  methods  of  writing   interrupt   service
        routines outside of the system rules.








                                 80j15b


                                                        Page   1
                                                       16 Oct 80


















                This  document  is  issued   by   Sandia
                National  Laboratories, operated for the
                United States Department  of  Energy  by
                Sandia Corporation.


                                 Notice


                This  document  was  sponsored  by   the
                United  States  Government.  Neither the
                United States Government nor the  United
                States  Department of Energy, nor any of
                their  employees,  nor  any   of   their
                contractors,  subcontractors,  or  their
                employees makes any warranty, express or
                implied,  or assumes any legal liability
                or  responsibility  for  the   accuracy,
                completeness   or   usefulness   of  any
                information,   apparatus,   product   or
                process  disclosed,  or  represents that
                its use  would  not  infringe  privately
                owned rights.


                This work was sponsored and funded by:

                    Headquarters, ESD / OCB / Stop 36
                    Hanscom Air Force Base, MA 01731


                                                        Page   2
                                                       16 Oct 80






                              Introduction


             Generally, the best way to respond to  an  external
        event  is  via  an  interrupt service routine (ISR).  An
        interrupt is a forced transfer of program execution as a
        result  of  some external event.  On interrupt the state
        of the processor is saved to permit a proper return once
        the  interrupt  has  been serviced.  The processor state
        for the ISR is  obtained  from  two  preassigned  memory
        locations known as an interrupt vector.

             While RT-11 [1] is faster than  any  of  the  other
        operating  systems,  its  response  time  is longer than
        simple  interrupt  latency.   RT-11's   prescribed   ISR
        protocol  is  responsible  for  this  increased response
        time.  As a  result,  it  is  possible  for  the  system
        response time to interfere with a sufficiently fast data
        rate.  Thus, it can become necessary  to  dispense  with
        prescribed protocol (moral ISR) and use an immoral ISR.

             First I will present a brief outline of  moral  ISR
        protocol.  Then I'll describe several immoral ISR's.



                              Moral ISR's


             Chapter six of  the  Software  Support  Manual  [2]
        offers  an  complete  and  excellent  description of the
        prescribed ISR protocol.  Hence, only an outline will be
        presented  here.   Some of the effects of the .INTEN and
        the .SYNCH macro calls are summarized in Table  1.   The
        stack  on  entry into the ISR may be the system's or the
        user's depending on the state of the main program at the
        time  of the interrupt.  Figure 1. shows an outline of a
        moral ISR along with an outline of its  associated  main
        program.   This  ISR  protocol may be used in either the
        foreground (FG) or the background (BG) partition.


                     Effects     New      Registers
                     Following   Stack    Available

                     .INTEN      System   R4,R5    
                     .SYNCH      User     R0,R1    

                                Table 1.


                                                        Page   3
                                                       16 Oct 80


        MAIN:   .PROTECT                ;grab the vector
                .DEVICE                 ;set up a termination
                                        ;sequence
                ;Load the vector.
                ;Initialize buffers, flags and pointers.
        1$:     BISB    #100,@#CSR      ;enable the interrupt
        2$:     .SPND                   ;wait for something to
                                        ;do
                ;Store and/or massage the data.
                ;If more to do
                ; reset flags, pointers and branch to 1$ or 2$
                ;else
                ; go on to 3$ or 4$.
        3$:     ;Close files and clean up things.
        4$:     .UNPROTECT              ;release the vector
                .EXIT                   ;end it all

        ISR:    ;Do what must be done at CPU priority 7.
                .INTEN                  ;lower CPU priority
                ;Do more things here such as but not limited to
                ;bumping pointers and setting flags.
                ;If more data is required
                ; branch to 2$
                ;else
                ; go on to 1$.
        1$:     .SYNCH                  ;allow programmed
                                        ;requests
                .RSUM                   ;wake up main program
        2$:     RTS     PC              ;monitor will issue RTI

                          Figure 1.  Moral ISR



                             Immoral ISR's


             Once the data  rate  becomes  too  high  for  RT-11
        system  response  time  it  becomes  necessary to use an
        immoral ISR.  At this  point  some  assumptions  may  be
        made.   Only the one job exists.  That job is run either
        under the single job (SJ) monitor, or is run in  the  BG
        partition  under  the foreground/background (FB) monitor
        with no FG job running.  Under these conditions the  ISR
        can  be  the  same  as for a memory only system.  Figure
        2. shows an outline for such a situation.


                                                        Page   4
                                                       16 Oct 80


        MAIN:   ;Load the vector.
                ;initialize buffers, flags and pointers.
        1$:     BISB    #100,@#CSR      ;enable the interrupt
        2$:     TST     RDYFLG          ;time to do something?
                BNE     2$              ;no
                ;Store and/or massage the data.
                ;If more to do
                ; reset flags, pointers and branch to 1$ or 2$
                ;else
                ; go on to 3$ or 4$.
        3$:     ;Close files and cleanup things.
        4$:     .EXIT                   ;end it all

        ISR:    ;Do what must be done immediatly.
                MOV     SP,SPSAVE       ;save the stack pointer
                MOV     #ISRSTK,SP      ;set up a new stack
                CLR     @#PSW           ;lower CPU priority
                                        ;(MTPS #PR0 for LSI-11)
                ;Do more things here such as but not limited to
                ;bumping pointers and setting flags.
                MOV     #PR7,@#PSW      ;raise CPU priority
                                        ;(MTPS #PR7 for LSI-11)
                MOV     SPSAVE,SP       ;restore original stack
                                        ;pointer
                RTI                     ;must issue own RTI

                    Figure 2.  SJ or BG Immoral ISR


             As  with  moral  ISR's  entry  should  be  made  at
        processor  priority  seven.   No registers are available
        unless they are first saved and later  restored.   Also,
        note  that  all  ISR  code  is not executed at processor
        priority seven.

             It is also possible to run an immoral ISR in the FG
        partition   if   suitable  care  is  exercised.   Figure
        3. outlines the requirements for this  situation.   Once
        again  no  registers are available unless they are saved
        and restored.  It is ablolutely essential to  set  up  a
        new  stack  for this ISR in order to avoid problems with
        the  system.   When  running  an  immoral  ISR  in   the
        foreground partition the processor priority must be kept
        at seven.


                                                        Page   5
                                                       16 Oct 80


        MAIN:   .PROTECT                ;grab the vector
                .DEVICE                 ;set up termination
                                        ;sequence
        1$:     BISB    #100,@#CSR      ;enable the interrupt
        2$:     .TWAIT                  ;go to sleep for a while
                ;Store and/or massage the data.
                ;If more to do
                ; reset flags, pointers and branch to 1$ or 2$
                ;else
                ; go on to 3$ or 4$.
        3$:     ;Close files and cleanup things.
        4$:     .UNPROTECT              ;release the vector
                .EXIT                   ;end it all

        ISR:    ;Do what must be done immediately.
                MOV     SP,SPSAVE       ;save original stack
                                        ;pointer
                MOV     #ISRSTK,SP      ;set up new stack
                ;Do more things here such as but not limited to
                ;bumping pointers and setting flags.
                MOV     SPSAVE,SP       ;restore original stack
                                        ;pointer
                RTI                     ;must issue own RTI

                       Figure 3.  FG Immoral ISR



                           Concluding Remarks


             It has been shown that  it  is  possible  to  write
        interrupt service routines both by the rules and outside
        the rules to operate under RT-11.  No  serious  problems
        will be encountered if proper care is exercised with the
        use of the stack.  If the ISR hogs enough processor time
        at  priority  seven  it  is possible to lose 60 Hz clock
        pulses.


















                                                        Page   6
                                                       16 Oct 80






                               References


        1.  "RT-11, Version 4.0 Single-User  Operating  System",
            AE-3393M-TC, Digital Equipment Corporation, Maymard,
            MA, April 1980.

        2.  "RT-11  Software   Support   Manual",   AA-H379A-TC,
            Digital  Equipment  Corporation,  Maynard, MA, March
            1980.