DEPARTMENT OF NATIONAL DEFENCE

                       DIRECTORATE OF AEROSPACE COMBAT SYSTEMS





















                                     SPOOL/RT-11

                            TRANSPARENT PIPELINE SPOOLER

                               USER'S REFERENCE GUIDE

                                      17-OCT-80











                            This document corresponds to:

                              SPOOL/RT-11 V1.00 & V1.01

                               For RT-11 V03B & V4.00



SPOOL/RT-11                                                          1
USER'S REFERENCE GUIDE


                                       FORWARD                                       _______


                    SUPPORT  -  This  document  and  the  software  it                    _______

                    describes are supported by:

                              National Defence Headquarters
                              Ottawa Ontario
                              K1A 0K4
                              Attn: G.  Adams, DACS 2-2-4
                              Phone:(613) 993-9624

                    DISCLAIMER - Her Majesty  and  the  Department  of                    __________

                    National Defence, reserve the right to discontinue

                    support at any time without notice and  assume  no

                    responsibility   for   the   correctness  of  this

                    document  or  the  operation  of  the   associated

                    software.


                    COPYRIGHT - This  document  and  the  software  it                    _________

                    describes   are  property  of  the  Government  of

                    Canada.  They may be used, in full or in part,  by

                    any person or agency provided that such use is not

                    for gain or reward except as explicitly authorized

                    by Her Majesty or her designated representative.


                    CONSERVE - In the interest of conservation, if you                    ________

                    are  having  problems, don't waste time and effort

                    generating a carefully worded, typed  masterpiece.

                    Just  jot  it  down  (legibly)  and  send  it off,

                    preferably on a post card.



SPOOL/RT-11                                                          2
USER'S REFERENCE GUIDE


               1.   SCOPE  -  This  document  describes  the  use  and                    _____

                    installation  procedures  of  a  spooling  package

                    based on the paper "A Transparent  Output  Spooler                                        _ ___________  ______  _______

                    for  RT-11", which was presented at DECUS Chicago,                    ___  _____

                    in April 1980.


               2.   INTRODUCTION - SPOOL/RT-11  offers  some  noteable                    ____________

                    improvements   (and   hopefully   not   too   many

                    disadvantages)  over   other   spooling   packages

                    currently  in  use  on  RT-11  systems.   The main

                    features of the package are:


                        - transparent   operation   such    that
                          commands  like  ".DIR/PRI"  and  "COPY
                          FOO.TXT LP:" will  work  correctly  in
                          the spooled environment;

                        - pipeline operation  such  that  output
                          begins  as  soon as data is available,
                          rather than waiting for  say,  a  .LST
                          file   to   be  completely  built  and
                          closed;

                        - concurrent output for up to 8  devices
                          and

                        - intelligent operation supporting  such
                          features  as  software  forms  control
                          etc.

               3.   PRINCIPLES OF OPERATION - The transparent pipeline                    __________ __ _________

                    spooler is implemented via a pseudo device handler

                    "SP", which works in conjunction with a privileged

                    foreground job named "SPOOL".


                    The SP handler works like any other serial  output

                    handler   except   it  doesn't  handle  a  device.

                    Instead, it manipulates a set  of  pseudo  command



SPOOL/RT-11                                                          3
USER'S REFERENCE GUIDE


                    and  status  registers  (CSRs),  located in vector

                    memory, which are monitored by  the  spooling  job

                    SPOOL.   SPOOL responds to the CSR bit settings as

                    if it were a device, tricking SP.


                    Any output to SP:  will be directed  to  a  buffer

                    within  the  SPOOLer  job,  which  in turn will be

                    written to  a  ring-structured  scratch  file  and

                    then,  as  soon  as  there  is  one  block of data

                    available, on to the final output device,  usually

                    LP:.  This achieves a pipeline effect.


                    Transparent operation is accomplished by utilizing

                    logical  to physical device name assignments.  For

                    example,   if   LP:    is    assigned    to    SP:

                    (ASSIGN SP: LP:) all output to LP:  will, in fact,

                    go to SP:  and hence be spooled.  Note that  there

                    is no conflict in having both a logical LP:  and a

                    physical LP:  under RT-11.  In fact,  the  SPOOLer

                    job  itself  uses the real (physical) line-printer

                    by doing its lookup of LP:, prior to  the  logical

                    assignment.


               4.   GETTING STARTED - The spooling package comes  with                    _______ _______

                    2  pre-built  spoolers.   One  for use in an RT-11

                    V03B  and/or  V4.00   foreground/background   (FB)

                    environment  and  one  for an RT-11 V4.00 extended

                    memory (XM) environment.  (Use of the  XM  package

                    should  work,  but  has never been tested, with an



SPOOL/RT-11                                                          4
USER'S REFERENCE GUIDE


                    RT-11 V03B XM monitor.)


                    In most cases, one of the prebuilt  spoolers  will

                    be suitable for your needs.  If not, you will have

                    to build a customized one as described later.


                    The following points are noted to help you  decide

                    if  a  prebuild  spooler will be suitable for your

                    system.


                        - Only   one    output    device,    the
                          line-printer  'LP:',  is  supported by
                          the pre-built spoolers.  If  you  have
                          more    than    one   device   to   be
                          concurrently  spooled,  or   if   some
                          device  other than LP:  is to be used,
                          then  you  must  generate  a  tailored
                          system.

                        - The prebuilt spoolers  require  a  400
                          block  scratch file on the system disk
                          named 'SPOOL.SYS'.  If you  require  a
                          larger  or smaller scratch file, or if
                          the name  is  unacceptable,  then  you
                          must generate a tailored system.

                        - Physical memory locations 360  to  377
                          are  used  for  the spooler vector and
                          pseudo CSRs.  If  you  have  a  device
                          which  uses any memory location in the
                          range 360 to 377 or if  you  have  set
                          this area aside for the program stack,
                          then  you  must  generate  a  tailored
                          system  and  select  alternate  memory
                          locations.

                        - The RT-11 SYSGEN options error logging
                          and   the   device  time-out  are  not                                                             ___
                          included.   If  your  system  requires
                          either   of   these   options   to  be
                          installed, then you must build  a  new
                          SP handler.

                        - The  spooler  cannot  support   system
                          jobs.  If your monitor includes system
                          jobs and if  they  do  output  to  the
                          line-printer  then you will have to be
                          very careful or very lucky.


SPOOL/RT-11                                                    5
USER'S REFERENCE GUIDE


               5.   INSTALLING A PREBUILT SPOOLER - If you decide that                    __________ _ ________ _______

                    a  prebuilt spooler will do the job, the procedure

                    for its installation is straight forward.   Simply

                    copy  the  appropriate files from the distribution

                    kit to your system disk, reboot the  computer  and

                    start up the spooler.


                    For  example,  an  FB  installation  from   double

                    density  floppy  disks  (RX02s  or  DY:).  You may

                    substitute your device as appropriate.


                    Mount the distribution volume in  DY0:   (or  DY1:

                    if DY0:  is your system disk SY:) and:


                             .ASSIGN DY0: DK:
                             .COPY/SYS SPOOL.REL,SP.SYS SY:*.*
                             ?PIP-W-Reboot
                             .BOOT SY:

               6.   GENERATING A TAILORED SPOOLER - The procedure  for                    __________ _ ________ _______

                    generating a tailored spooler is as follows:


                        - Copy  the  distribution  disk   to   a
                          working  copy  and put the master away
                          in  a  safe  place.   All   subsequent
                          operations  are  done  on  the working
                          copy.

                        - Edit the file SPINIT.MAC to change the
                          parameters as necessary.  The comments
                          in the file describe  each  individual
                          item (honestly).

                        - Execute the command file SPBLD.COM  to
                          build  an  FB  package  or the command
                          SPBLDX.COM to generate an XM version.

                        - Copy the files to the system  disk  as
                          described in section 5.


SPOOL/RT-11                                                          6
USER'S REFERENCE GUIDE


               7.   STARTING THE SPOOLER - Once a spooling package has                    ________ ___ _______

                    been installed, running it is quite simple.


                    The  following  example,  which  is  suitable  for

                    inclusion  in a start-up command file, illustrates

                    how to run the prebuilt FB spooler.  It is assumed

                    that  SPOOL.REL  is  on  the system disk SY:.  The

                    start  up  of  other  variants  is  left  to  your

                    ingenuity.


                             .DEAS LP:       !In case of restart.
                             .DEAS LP0:
                             .LOAD LP:       !SPOOL gets real LP:.
                             .FRUN SY:SPOOL  !Start the spooler.
                             !Wait a moment for SPOOL to lookup LP:
                             .ASSI SP0: LP:  !users get logical LP:
                             .ASSI SP0: LP0: !To ensure LP:=LP0:.

               8.   START UP NOTES - The following points are made  in                    _____ __ _____

                    support of the startup procedure:


                        - The INSTallation of the SP handler may
                          not  be  necessary  under RT-11 V04.00
                          since  it  incorporates  an  automatic
                          installation algorithm.

                        - When you  FRUN SPOOL,  you  must  wait
                          long  enough  for  it  to  lookup  the
                          physical devices, before you  do  your
                          logical  device  assignments.   If you
                          don't, then you may lookup a a logical
                          device  which  translates  to SP.  Ie.
                          concurrent input and  output,  to  and
                          from  SP  makes for some peculiar race
                          conditions.     This    problem     is
                          particularily   noticeable   when  the
                          spooler  is  started  from  a  command
                          file.  A good way to get arround it is
                          to do something else  in  between  the
                          FRUN SY:SPOOL and the ASSIGN commands.

                        - SPOOL may be run as a system job using
                          SRUN SY:SPOOL.REL.   Watch out though,
                          if  you  forget  to  enter  the   .REL
                          extension, you will attempt to run the


SPOOL/RT-11                                                    7
USER'S REFERENCE GUIDE


                          scratch file  SY:SPOOL.SYS,  which  is
                          bound to do something strange.

                        - Always assign both  devices  xx:   and
                          xx0:   to  SP since xx:  and xx0:  may
                          not be  the  same  thing,  "logically"
                          speaking.

               9.   USING THE  SPOOLER  -  Normally  ,the  spooler  is                    _____ ___  _______

                    started   when  the  system  is  booted,  using  a

                    start-up command file.  Once running, its  use  is

                    transparent and no special action need be taken to

                    access the package.


                    For  improved  usability  however,  operators  may

                    control   the  spooler  using  some  SET  commands

                    supported by the SP handler as follows:


                           .SET SP UNIT=n is used in  conjuntion
                          with the other set options;  it has no
                          meaning   alone.    When   given,   it
                          indicates  that the next specification
                          is  to  be  applied  to   the   device
                          associated  with SP unit n (SPn:).  If
                          not given, unit 0 is the default.

                           .SET SP SHOW  is  used   to   display
                          spooler statistics.

                           .SET SP NEXT moves output forward  to
                          the  start  of the next listing in the
                          scratch file, i.e.  to the next  block
                          0.   This  also  can  be  equivalently
                          thought of as  a  delete  the  current
                          listing command.

                           .SET SP LAST moves output back to the
                          start of the last (current) listing in
                          the scratch file, i.e.   to  the  last
                          block 0.

                           .SET SP KILL   removes   all   output
                          currently spooled up for the specified
                          device.

                           .SET SP OFF stops all spooled  output
                          to  the  specified device but does not


SPOOL/RT-11                                                    8
USER'S REFERENCE GUIDE


                          remove the spooled up  data  from  the
                          scratch  file.   Further output to the
                          device may  occur  but  will  be  held
                          until the spooler is set on again.

                           .SET SP ON counter acts  the  effects
                          of setting the spooler off.

                          Note that KILL is to  <CONTROL  O>  as
                          OFF  is  to  <CONTROL S>;  think about
                          it!

               10.  SECONDARY LOGICAL UNIT ASSIGNMENTS - One potential                    _________ _______ ____ ___________

                    difficulty using the spooler comes when one wishes

                    to assign some logical unit name to a device which

                    is already logical.


                    For example, the logical name LST:  is often  used

                    in  command files when the actual device where the

                    listing is to go is not known ahead of  time.   If

                    you  wanted  to  use  the command file to obtain a

                    listing on the line-printer LP:, you  would  enter

                    the   command   .ASSIGN LP: LST:    prior  to  its

                    execution.  If SPOOL/RT-11 is running however, LP:

                    will   have   been   assigned   to   SP:    as  in

                    .ASSIGN SP: LP:,  making  LP:   a  logical   name.

                    Therefore you cannot .ASSIGN LP: LST:  because you

                    cannot  assign  a  logical  to  a  logical.    The

                    solution would be to simply .ASSIGN SP: LST:.