SOME PDP-11 BASIC-11 EXTENSION ROUTINES





                           N. A. Bourgeois, Jr.
                Advanced Systems Development Division 1736
                           Sandia Laboratories
                              P. O. Box 5800
                          Albuquerque, NM 87185
                               505-264-8088
                               FTS 475-8088





                                 ABSTRACT

           Some   extension   routines    to    Digital    Equipment
      Corporation's  BASIC-11 V2 interpreter running under RT-11 V03
      are described.  They provide the means for reading (GET, GETB,
      TBIT)  and  writing (PUT, PUTB, SBIT) words, bytes and bits at
      any  implemented  UNIBUS  address,  identifying   (IDEN)   the
      extended BASIC-11 interpreter and zeroing (NULL) arrays.













                                  79A27A



















           This document is issued by Sandia Laboratories,  operated
      for   the   United  States  Department  of  Energy  by  Sandia
      Corporation.

                                  NOTICE

           This  document  was  sponsored  by  the   United   States
      government.   Neither  the  United  States  government nor the
      United  States  Department  of  Energy,  nor  any   of   their
      employees,  nor  any  of their contractors, subcontractors, or
      their employees makes any warranty,  express  or  implied,  or
      assumes   any   legal  liability  or  responsibility  for  the
      accuracy,  completeness  or  usefulness  of  any  information,
      apparatus,  product  or  process disclosed, or represents that
      its use would not infringe privately owned rights.

           This work was sponsored and funded by:
              Base and Installation Security Systems Program Office
              Electronic Systems Division
              Air Force Systems Command
              Hanscom Air Force Base, MA 01731





                             ****************
                             *              *
                             * UNCLASSIFIED *
                             *              *
                             ****************


      BASIC-11 EXTENSIONS                                   Page   2
      ACKNOWLEDGEMENT                                      27 Mar 79

























                             ACKNOWLEDGEMENT


               The author wishes to express his appreciation  to
          Mr. W. A. Wood   of   Scientific   Systems   Services,
          Incorporated, for his assistance in updating,  to  run
          under  RT-11  V03,  the BASIC-11 V2 extension routines
          described  in  this  paper.   The  author's   original
          software  was written to be compatible with BASIC/RT11
          V1B running under RT-11 V02 [1].


      BASIC-11 EXTENSIONS                                   Page   3
      TABLE OF CONTENTS                                    27 Mar 79










                            TABLE OF CONTENTS



                I.  Introduction                        6

                II.  The Extension Routines             8

                III.  Installation                      11

                IV.  Testing the Routines               14

                A.  Appendix:  Miscellaneous Comments   22

                B.  Appendix:  Flow Charts              36

                References                              65

                Index                                   66



                FIGURES.

                A-1.  Pointer Map:  Null Arguments      23

                A-2.  Pointer Map:  Constants           24

                A-3.  Pointer Map:  Undefined Variables 25

                A-4.  Pointer Map:  Defined Variables   26

                A-5.  Pointer Map:  One Dimension       27-28
                        Arrays, Undefined Elements

                A-6.  Pointer Map:  One Dimension       28-29
                        Arrays, Defined Elements

                A-7.  Pointer Map:  One Dimension       30-31
                        Arrays, Specific Elements

                A-8.  Pointer Map:  Two Dimension       31-33
                        Arrays, Defined Elements

                A-9.  Pointer Map:  Two Dimension       33-34
                        Arrays, Specific Elements


      BASIC-11 EXTENSIONS                                   Page   4
      TABLE OF CONTENTS                                    27 Mar 79


                B-1.  Flow Chart:  GET                  36-37

                B-2.  Flow Chart:  GETB                 38

                B-3.  Flow Chart:  IDEN                 39

                B-4.  Flow Chart:  NULL                 39-40

                B-5.  Flow Chart:  PUT                  40-41

                B-6.  Flow Chart:  PUTB                 42-43

                B-7.  Flow Chart:  SBIT                 44

                B-8.  Flow Chart:  TBIT                 45

                B-9.  Flow Chart:  AG1AG2               46-47

                B-10.  Flow Chart:  BITMSK              48

                B-11.  Flow Chart:  DELARG              49-50

                B-12.  Flow Chart:  DELINT              50

                B-13.  Flow Chart:  DELOCT              51-52

                B-14.  Flow Chart:  DELREL              53

                B-15.  Flow Chart:  GETARG              54-55

                B-16.  Flow Chart:  GETDSC              56

                B-17.  Flow Chart:  GETOCT              57

                B-18.  Flow Chart:  GETREL              58

                B-19.  Flow Chart:  NULARY              59

                B-20.  Flow Chart:  NULNUM              60

                B-21.  Flow Chart:  NULOCT              61

                B-22.  Flow Chart:  POPRGS              62

                B-23.  Flow Chart:  PSHRGS              62

                B-24.  Flow Chart:  TSTADR              63

                B-25.  Flow Chart:  PSHVAL              64


      BASIC-11 EXTENSIONS                                   Page   5
      TABLE OF CONTENTS                                    27 Mar 79


                TABLES

                I-1.  The Extension Routines            7

                III-1.  The DATBAS Files                11

                A-1.  Descriptor Words                  23


      BASIC-11 EXTENSIONS                                   Page   6
      INTRODUCTION                                         27 Mar 79










                             I.  INTRODUCTION


           BASIC-11  allows  the  addition  of   assembly   language
      routines  to  expand  BASIC-11's  capabilities.  Once added to
      BASIC-11, such routines can be executed in immediate  mode  or
      in programs, by means of the CALL statement.

           The routines described in this paper permit access to any
      address   on   DEC's   PDP-11  UNIBUS.*  This  is  useful  for
      exercising any peripheral connected to the  UNIBUS  especially
      if a handler is not present in the operating system.  In fact,
      it is even possible to write entire handlers for  non-standard
      peripherals  such  as  digital  voltmeters  and point plotters
      using BASIC-11  and  the  CALL  statement  with  the  routines
      described  in this paper.  These routines are designed for use
      on any of the PDP-11 family of computers running the RT-11 V03
      operating system.  [2,3,4,5,6]

           The  extension  routines  incorporated  within  the  file
      DATBAS.MAC  provide  the  means for reading and writing words,
      bytes and bits at any implemented UNIBUS address,  identifying
      the  extended  BASIC-11  interpreter,  and  zeroing or nulling
      arrays.  The values of  the  arguments  may  be  expressed  in
      either  decimal or octal.  The routines included are listed in
      Table I-1.



















           *  DEC, PDP and UNIBUS are registered trademarks  of
           Digital Equipment Corporation, Maynard, MA.


      BASIC-11 EXTENSIONS                                   Page   7
      INTRODUCTION                                         27 Mar 79














        GET(ARG1,ARG2)  Input a word from a UNIBUS address
                ARG1  UNIBUS word address
                ARG2  Word value returned

        GETB(ARG1,ARG2)  Input a byte from a UNIBUS address
                ARG1  UNIBUS byte address
                ARG2  Byte value returned

        IDEN  Output identification message

        NULL(ARG1(),ARG2(),...)  Zero array(s)
                ARG()'s  Name(s) of array(s)

        PUT(ARG1,ARG2)  Output a word to a UNIBUS address
                ARG1  Word value delivered
                ARG2  UNIBUS word address

        PUTB(ARG1,ARG2)  Output a byte to a UNIBUS address
                ARG1  Byte value delivered
                ARG2  UNIBUS byte address

        SBIT(ARG1,ARG2,ARG3)  Set or clear a bit at a UNIBUS address
                ARG1  Bit number
                ARG2  UNIBUS word address
                ARG3  Bit value set

        TBIT(ARG1,ARG2,ARG3)  Test a bit at a UNIBUS address
                ARG1  Bit number
                ARG2  UNIBUS word address
                ARG3  Bit value returned

                                TABLE I-1.
                          THE EXTENSION ROUTINES




      BASIC-11 EXTENSIONS                                   Page   8
      THE EXTENSION ROUTINES                               27 Mar 79










                       II.  THE EXTENSION ROUTINES


           The "BASIC-11 Language  Reference  Manual"  [2]  and  the
      "BASIC-11/RT-11  User's Guide" [3] describe the general use of
      BASIC-11 and the CALL statement.  This section  describes  the
      use of the extensions of DATBAS.MAC and their associated error
      messages.

           The arguments for GET, GETB, PUT, PUTB, SBIT and TBIT may
      be  constants,  expressions,  variables and/or array elements.
      These arguments may  also  be  either  decimal  or  octal.   A
      decimal  argument may be either numeric (real) or integer.  An
      octal argument must be a string.  A numeric  is  one  or  more
      decimal  digits,  either  positive  or  negative, in which the
      decimal point is optional.  An integer is one or more  decimal
      digits,  either  positive  or negative, with no decimal point.
      An octal string is one  or  more  of  the  numeric  characters
      excluding the "8" and "9".  [2]

           No arguments are required with the IDEN routine.

           The  NULL  routine  requires  only  the  name(s)  of  the
      argument(s).   The  argument(s)  may be the name(s) of numeric
      array(s), integer array(s) and/or string array(s).

           Null arguments are not allowed.

           Descriptions of the routines  follow.   The  descriptions
      include the calling sequences, and where applicable the ranges
      of the arguments.  Examples of the use of these  routines  may
      be seen in the section on the testing of the routines.


           GET    Deliver the contents of the UNIBUS word address of
      argument one into the BASIC-11 variable named in argument two.

                Calling sequence:
                        CALL GET(ARG1,ARG2)

                                Octal                   Decimal
                ARG1 Range:     0 to  77776             0 to 32766
                                100000 to 177776        -32768 to -2
                ARG2 Range:     100000 to 177777        -32768 to -1
                                0 to 77777              0 to 32767



      BASIC-11 EXTENSIONS                                   Page   9
      THE EXTENSION ROUTINES                               27 Mar 79


           GETB    Deliver the contents of the UNIBUS  byte  address
      of  argument  one into the BASIC-11 variable named in argument
      two.

                Calling sequence:
                        CALL GETB(ARG1,ARG2)

                                Octal                   Decimal
                ARG1 Range:     0 to 77777              0 to 32767
                                100000 t0 177777        -32768 to -1
                ARG2 Range:     200 to 377              -128 to -1
                                0 to 177                0 to 127


           IDEN    Output  a  message   identifying   the   extended
      BASIC-11 interpreter.  No arguments are required.

                Calling sequence:
                        CALL IDEN


           NULL    Null  or  zero  the   array(s)   named   in   the
      argument(s).   The  argument(s)  must be the name(s) of either
      numeric array(s), integer  array(s)  and/or  string  array(s).
      Any  number  of arguments may be given, subject only to normal
      line length limitations.

                Calling sequence:
                        CALL NULL(ARG1(),ARG2(),...)


           PUT    Deposit the value of argument one  at  the  UNIBUS
      word address of argument two.

                Calling sequence:
                        CALL PUT(ARG1,ARG2)

                                Octal                   Decimal
                ARG1 Range:     100000 to 177777        -32768 to -1
                                0 to 77777              0 to 32767
                ARG2 Range:     0 to 77776              0 to 32766
                                100000 to 177776        -32768 to -2


           PUTB    Deposit the value of argument one at  the  UNIBUS
      byte address of argument two.

                Calling sequence:
                        CALL PUTB(ARG1,ARG2)

                                Octal                   Decimal
                ARG1 Range:     200 to 377              -128 to -1
                                0 to 177                0 to 127
                ARG2 Range:     0 to 77777              0 to 32767
                                100000 to 177777        -32768 to -1


      BASIC-11 EXTENSIONS                                   Page  10
      THE EXTENSION ROUTINES                               27 Mar 79


           SBIT    Set the bit named in argument one at  the  UNIBUS
      word  address  of  argument two to the value given in argument
      three.

                Calling sequence:
                        CALL SBIT(ARG1,ARG2,ARG3)

                                Octal                   Decimal
                ARG1 Range:     0 to 17                 0 to 15
                ARG2 Range:     0 to 77776              0 to 32766
                                100000 to 177776        -32768 to -2
                ARG3 Range:     0 or 1                  0 or 1


           TBIT    Test the bit named in argument one at the  UNIBUS
      word  address  of argument two.  The result is returned in the
      variable named in argument three.  If the bit tested is  clear
      then ARG3=0, and if set ARG3=1.

                Calling sequence:
                        CALL TBIT(ARG1,ARG2,ARG3)

                                Octal                   Decimal
                ARG1 Range:     0 to 17                 0 to 15
                ARG2 Range:     0 to 77776              0 to 32766
                                100000 to 177776        -32768 to -2
                ARG3 Range:     0 or 1                  0 or 1


           When BASIC-11  finds  an  error  in  a  program  line  or
      immediate  mode  statement  it prints an error message.  After
      BASIC-11 prints the error message it interrupts  execution  of
      the  program  line or immediate mode statement and then prints
      the READY message.  These routines return  three  fatal  error
      messages,  one  on an argument error, one for lack of adequate
      string storage space and the other on an attempt to access  an
      unimplimented  UNIBUS  address.   Descriptions  of these error
      messages follow along with some suggested corrective actions.

           ?ARGUMENT ERROR [AT LINE xxxxx]    Arguments in a CALL do
      not  match in number, range or type, the arguments defined for
      the CALL.   Ensure  that  there  are  the  correct  number  of
      arguments,  that  their  values  are in the correct range, and
      that they are of the correct type.  [2]

           ?NO STRING SPACE [AT LINE xxxxx]    BASIC-11  was  unable
      to  allocate  space for the output string.  Reduce the size of
      the program or the amount of string utilization.

           ?UNIMPLEMENTED BUS ADDRESS [AT LINE xxxxx]    An  attempt
      in  a  CALL  was  made  to  input  from  or  to  output  to an
      unimplemented UNIBUS address.  Ensure that the  value  of  the
      UNIBUS address to be accessed is valid.


      BASIC-11 EXTENSIONS                                   Page  11
      INSTALLATION                                         27 Mar 79










                            III.  INSTALLATION


           The "BASIC-11/RT-11 Installation Guide" [4] describes the
      general  technique  used to install assembly language routines
      into the BASIC-11 interpreter.

           Table III-1 lists the set of  files  which  make  up  the
      DATBAS  package.   The  files  DATBAS.TEC  and  DATBAS.MAC are
      needed along with  DEC's  BASIC-11/RT-11  binary  distribution
      package to build an extended BASIC-11 interpreter.  

           Installation of these routines requires five steps.  They
      are  modification of BSCLI.MAC, assembly of the DATCLI.MAC and
      the DATBAS.MAC extension files, generation of a  command  file
      to  build the interpreter, editing the command file to provide
      more stack space and finally executing  the  command  file  to
      build the extended BASIC-11 interpreter.


                FILE NAME       DESCRIPTION

                DATBAS.BAS      BASIC-11   program   to   test   the
                                extension routines of DATBAS.MAC.

                DATBAS.DAT      Resulting output from  execution  of
                                DATBAS.BAS.

                DATBAS.DIR      This   directory   of   the   DATBAS
                                package.

                DATBAS.DOC      Full  description  of   the   DATBAS
                                package (this document).

                DATBAS.HLP      Brief description of the use of  the
                                DATBAS.MAC extension routines.

                DATBAS.MAC      MACRO-11  source  of  the  extension
                                routines.

                DATBAS.RNO      Source file for DATBAS.DOC.

                DATBAS.TEC      TECO macro to make DATCLI.MAC.

                               TABLE III-1.
                             THE DATBAS FILES


      BASIC-11 EXTENSIONS                                   Page  12
      INSTALLATION                                         27 Mar 79


           DATCLI.MAC is constructed from BSCLI.MAC by executing the
      TECO  [7]  macro file DATBAS.TEC.  It adds the globals and the
      FTBL entries required to access the DATBAS.MAC routines.   The
      following commands accomplish this.

                .SET EDIT TECO
                .EDIT/EXEC DATBAS

           The  following  commands  will  assemble  DATCLI.MAC  and
      DATBAS.MAC  to  produce  OBJ files which will be used later by
      the command file to build the interpreter.

                .RUN MACRO
                *DATCLI,LP:<BSMAC,DATCLI/C
                *DATBAS,LP:<DATBAS/C

           Now it is necessary to generate the  command  file  which
      will be used to build the extended BASIC-11 interpreter.  This
      is accomplished by  executing  the  single  user  configurator
      program,  SUCNFG.BAS,  as  described  in  the  "BASIC-11/RT-11
      Installation Guide" [4].  The following shows the CALL part of
      the dialogue.  User responses are shown at the far right.

                Do you want CALL support? (Y or N; default is N): Y

                Enter module names (one per line):           DATCLI
                Module name:                                 DATBAS
                Module name:                                 BSCLLB
                Module name:

                                 CAUTION

                Do not use  the  double  precision  option
                with   these   routines.    They  are  not
                compatible with either four-word  floating
                point or two-word integer.

           The extension routines require some  extra  stack  space,
      therefore it is essential that the command file just generated
      be edited to add at least 64  extra  words  to  the  available
      stack  space.  The following sets of command strings show both
      the TECO and EDIT syntax to accomplish this task.

                .RUN TECO               .RUN EDIT
                *EBDATBAS.COM$          *EBDATBAS.COM$
                S/B:1$DI2$              G/B:1$DI2$
                EX$$                    EX$$
                .                       .

           The command file is finally ready for execution to  build
      the  extended BASIC-11 interpreter.  Use the following command
      to execute the command file.

                .@DATBAS


      BASIC-11 EXTENSIONS                                   Page  13
      INSTALLATION                                         27 Mar 79


           At  this  point  the  newly  created  extended   BASIC-11
      interpreter  is  ready  for use.  The next section describes a
      means of testing the extension routines.


      BASIC-11 EXTENSIONS                                   Page  14
      TESTING THE ROUTINES                                 27 Mar 79










                        IV.  TESTING THE ROUTINES


           Once the extended BASIC-11 interpreter has been built  it
      should   be   tested.    The  following  program,  DATBAS.BAS,
      thoroughly tests  the  extensions.   Messages  are  output  to
      identify  the  particular  test  being performed.  Blank lines
      have been added  for  clarity.   Fatal  errors,  if  any,  are
      reported  in  BASIC-11's  normal  error  message  format  [2].
      Non-fatal   errors   are   reported    with    the    message:
      ERROR: xxxxxxxxxxxxxxx.


      100 REM  DATBAS.BAS  NAB/WAW  19-SEP-78/25-OCT-78
      110 T$='TEST THE DATBAS.MAC ROUTINES'
      120 DIM A$(1),V$(1),Z$(1)
      130 DIM A%(1),V%(1),Z%(1)
      140 DIM A(1),V(1),Z(1)
      150 DIM D(100),D%(100),D$(100)
      160 DIM E(10,10),E%(10,10),E$(10,10)
      170 PRINT T$
      180 CALL IDEN
      190 PRINT 'ENTER THE OUTPUT DEVICE NAME',
      200 INPUT O$
      210 IF O$='' THEN O$='TT:'
      220 OPEN O$ FOR OUTPUT AS FILE #1 DOUBLE BUF
      230 PRINT #1
      240 PRINT #1,T$
      250 PRINT #1,DAT$,CLK$
      260 GOSUB 350 \ REM       TEST PUT & GET
      270 GOSUB 870 \ REM       TEST PUTB & GETB
      280 GOSUB 1730 \ REM      TEST SBIT & TBIT
      290 GOSUB 1390 \ REM      TEST NULL
      300 PRINT #1
      310 PRINT #1
      320 PRINT #1,'END OF TESTS',CLK$
      330 CLOSE #1
      340 GO TO 3780 \ REM      END

      350 PRINT #1
      360 PRINT #1
      370 PRINT #1,'TEST PUT & GET'
      380 GOSUB 3000 \ REM      STRING CONSTANTS
      390 CALL PUT('123','376')
      400 CALL GET('376',Z$)
      410 IF Z$<>'   123' THEN PRINT #1,'    ERROR: Z$<>123'
      420 GOSUB 3040 \ REM      INTEGER CONSTANTS


      BASIC-11 EXTENSIONS                                       Page  15
      TESTING THE ROUTINES                                     27 Mar 79


      430 CALL PUT(83%,254%)
      440 CALL GET(254%,Z%)
      450 IF Z%<>83% THEN PRINT #1,'    ERROR: Z%<>83'
      460 GOSUB 3080 \ REM      NUMERIC CONSTANTS
      470 CALL PUT(83,254)
      480 CALL GET(254,Z)
      490 IF Z<>83 THEN PRINT #1,'    ERROR: Z<>83'
      500 GOSUB 3120 \ REM      STRING EXPRESSIONS
      510 CALL PUT(V$&'23',A$&'76')
      520 CALL GET(A$&'76',Z$)
      530 IF Z$<>'   '&V$&'23' THEN PRINT #1,'    ERROR: Z$<>'V$&'23'
      540 GOSUB 3190 \ REM      INTEGER EXPRESSIONS
      550 CALL PUT(V%+100%,A%+200%)
      560 CALL GET(A%+200%,Z%)
      570 IF Z%<>V%+100% THEN PRINT #1,'    ERROR: Z%<>'V%+100%
      580 GOSUB 3260 \ REM      NUMERIC EXPRESSIONS
      590 CALL PUT(V/2,2*A)
      600 CALL GET(2*A,Z)
      610 IF Z<>V/2 THEN PRINT #1,'    ERROR: Z<>'V/2
      620 GOSUB 3330 \ REM      STRING VARIABLES
      630 CALL PUT(V$,A$)
      640 CALL GET(A$,Z$)
      650 IF Z$<>'   '&V$ THEN PRINT #1,'  Z$<>'V$
      660 GOSUB 3400 \ REM      INTEGER VARIABLES
      670 CALL PUT(V%,A%)
      680 CALL GET(A%,Z%)
      690 IF Z%<>V% THEN PRINT #1,'    ERROR: Z%<>'V%
      700 GOSUB 3470 \ REM      NUMERIC VARIABLES
      710 CALL PUT(V,A)
      720 CALL GET(A,Z)
      730 IF Z<>V THEN PRINT #1,'    ERROR: Z<>'V
      740 GOSUB 3540 \ REM      STRING ARRAY ELEMENTS
      750 CALL PUT(V$(0),A$(0))
      760 CALL GET(A$(0),Z$(0))
      770 IF Z$(0)<>'   '&V$(0) THEN PRINT #1,'    ERROR: Z$(0)<>'V$(0)
      780 GOSUB 3610 \ REM      INTEGER ARRAY ELEMENTS
      790 CALL PUT(V%(1),A%(1))
      800 CALL GET(A%(1),Z%(1))
      810 IF Z%(1)<>V%(1) THEN PRINT #1,'    ERROR: Z%(1)<>'V%(1)
      820 GOSUB 3680 \ REM      NUMERIC ARRAY ELEMENTS
      830 CALL PUT(V(0),A(0))
      840 CALL GET(A(0),Z(0))
      850 IF Z(0)<>V(0) THEN PRINT #1,'    ERROR: Z(0)<>'V(0)
      860 RETURN

      870 PRINT #1
      880 PRINT #1
      890 PRINT #1,'TEST PUTB & GETB'
      900 GOSUB 3000 \ REM      STRING CONSTANTS
      910 CALL PUTB('123','376')
      920 CALL GETB('376',Z$)
      930 IF Z$<>'   '&'123' THEN PRINT #1,'    ERROR: Z$<>123'
      940 GOSUB 3040 \ REM      INTEGER CONSTANTS
      950 CALL PUTB(83%,255%)


      BASIC-11 EXTENSIONS                                   Page  16
      TESTING THE ROUTINES                                 27 Mar 79


      960 CALL GETB(255%,Z%)
      970 IF Z%<>83% THEN PRINT #1,'    ERROR: Z%<>83'
      980 GOSUB 3080 \ REM      NUMERIC CONSTANTS
      990 CALL PUTB(83,254)
      1000 CALL GETB(254,Z)
      1010 IF Z<>83 THEN PRINT #1,'    ERROR: Z<>83'
      1020 GOSUB 3120 \ REM     STRING EXPRESSIONS
      1030 CALL PUTB(V$&'23',A$&'77')
      1040 CALL GETB(A$&'77',Z$)
      1050 IF Z$<>'   '&V$&'23' THEN PRINT #1,'    ERROR: Z$<>'V$&'23'
      1060 GOSUB 3190 \ REM     INTEGER EXPRESSIONS
      1070 CALL PUTB(V%+100%,A%+200%)
      1080 CALL GETB(A%+200%,Z%)
      1090 IF Z%<>V%+100% THEN PRINT #1,'    ERROR: Z%<>'V%+100%
      1100 GOSUB 3260 \ REM     NUMERIC EXPRESSIONS
      1110 CALL PUTB(V/2,2*A)
      1120 CALL GETB(2*A,Z)
      1130 IF Z<>V/2 THEN PRINT #1,'    ERROR: Z<>'V/2
      1140 GOSUB 3330 \ REM     STRING VARIABLES
      1150 CALL PUTB(V$,A$)
      1160 CALL GETB(A$,Z$)
      1170 IF Z$<>'   '&V$ THEN PRINT #1,'    ERROR: Z$<>'V$
      1180 GOSUB 3400 \ REM     INTEGER VARIABLES
      1190 CALL PUTB(V%,A%)
      1200 CALL GETB(A%,Z%)
      1210 IF Z$(0)<>'   '&V$(0) THEN PRINT #1,'    ERROR: Z$(0)<>'V$(0)
      1220 IF Z%<>V% THEN PRINT #1,'    ERROR: Z%<>'V%
      1230 GOSUB 3470 \ REM     NUMERIC VARIABLES
      1240 CALL PUTB(V,A)
      1250 CALL GETB(A,Z)
      1260 IF Z<>V THEN PRINT #1,'    ERROR: Z<>'V
      1270 GOSUB 3540 \ REM     STRING ARRAY ELEMENTS
      1280 CALL PUTB(V$(0),A$(0))
      1290 CALL GETB(A$(0),Z$(0))
      1300 GOSUB 3610 \ REM     INTEGER ARRAY ELEMENTS
      1310 CALL PUTB(V%(1),A%(1))
      1320 CALL GETB(A%(1),Z%(1))
      1330 IF Z%(1)<>V%(1) THEN PRINT #1,'    ERROR: Z%(1)<>'V%(1)
      1340 GOSUB 3680 \ REM     NUMERIC ARRAY ELEMTNTS
      1350 CALL PUTB(V(0),A(0))
      1360 CALL GETB(A(0),Z(0))
      1370 IF Z(0)<>V(0) THEN PRINT #1,'    ERROR: Z(0)<>'V(0)
      1380 RETURN

      1390 PRINT #1
      1400 PRINT #1
      1410 PRINT #1,'TEST NULL'
      1420 PRINT #1
      1430 PRINT #1,'  ONE DIMENSION ARRAYS'
      1440 FOR I=0 TO 100
      1450 D(I)=I
      1460 D%(I)=I
      1470 D$(I)=STR$(I)
      1480 NEXT I


      BASIC-11 EXTENSIONS                                   Page  17
      TESTING THE ROUTINES                                 27 Mar 79


      1490 CALL NULL(D(),D%(),D$())
      1500 FOR I=0 TO 100
      1510 IF D(I)<>0 THEN PRINT #1,'    ERROR: D('I')<>0'
      1520 IF D%(I)<>0% THEN PRINT #1,'    ERROR: D%('I')<>0'
      1530 IF D$(I)<>'' THEN PRINT #1,'    ERROR: D$('I') NOT NUL'
      1540 NEXT I
      1550 PRINT #1
      1560 PRINT #1,'  TWO DIMENSION ARRAYS'
      1570 FOR I=0 TO 10
      1580 FOR J=0 TO 10
      1590 E(I,J)=10*I+J
      1600 E%(I,J)=I+J
      1610 E$(I,J)=STR$(E(I,J))
      1620 NEXT J
      1630 NEXT I
      1640 CALL NULL(E(),E%(),E$())
      1650 FOR I=0 TO 10
      1660 FOR J=0 TO 10
      1670 IF E(I,J)<>0 THEN PRINT #1,'    ERROR: E('I','J')<>0'
      1680 IF E%(I,J)<>0% THEN PRINT #1,'    ERROR: E%('I','J')<>0'
      1690 IF E$(I,J)<>'' THEN PRINT #1,'    ERROR: E$('I','J') NOT NUL'
      1700 NEXT J
      1710 NEXT I
      1720 RETURN

      1730 PRINT #1
      1740 PRINT #1
      1750 PRINT #1,'TEST SBIT & TBIT'
      1760 CALL PUT(0,254)
      1770 GOSUB 3080 \ REM     NUMERIC CONSTANTS
      1780 CALL SBIT(5,254,1)
      1790 CALL TBIT(5,254,Z)
      1800 IF Z<>1 THEN PRINT #1,'    ERROR: Z<>'1
      1810 GOSUB 3750 \ REM     TIME DELAY
      1820 CALL SBIT(5,254,0)
      1830 CALL TBIT(5,254,Z)
      1840 IF Z<>0 THEN PRINT #1,'    ERROR: Z<>'0
      1850 GOSUB 3040 \ REM     INTEGER CONSTANTS
      1860 CALL SBIT(10%,254%,1%)
      1870 CALL TBIT(10%,254%,Z%)
      1880 IF Z%<>1% THEN PRINT #1,'    ERROR: Z%<>'1%
      1890 GOSUB 3750 \ REM     TIME DELAY
      1900 CALL SBIT(10%,254%,0%)
      1910 CALL TBIT(10%,254%,Z%)
      1920 IF Z%<>0% THEN PRINT #1,'    ERROR: Z%<>'0%
      1930 GOSUB 3000 \ REM     STRING CONSTANTS
      1940 CALL SBIT('15','376','1')
      1950 CALL TBIT('15','376',Z$)
      1960 IF Z$<>'     1' THEN PRINT #1,'    ERROR: Z$<>1'
      1970 GOSUB 3750 \ REM     TIME DELAY
      1980 CALL SBIT('15','376','0')
      1990 CALL TBIT('15','376',Z$)
      2000 IF Z$<>'     0' THEN PRINT #1,'    ERROR: Z$<>0'
      2010 GOSUB 3260 \ REM     NUMERIC EXPRESSIONS


      BASIC-11 EXTENSIONS                                   Page  18
      TESTING THE ROUTINES                                 27 Mar 79


      2020 CALL SBIT(14/2,2*A,2-1)
      2030 CALL TBIT(3+4,2*A,Z)
      2040 IF Z<>1 THEN PRINT #1,'    ERROR: Z<>'1
      2050 GOSUB 3750 \ REM     TIME DELAY
      2060 CALL SBIT(2*3.5,2*A,3-3)
      2070 CALL TBIT(14-7,2*A,Z)
      2080 IF Z<>0 THEN PRINT #1,'    ERROR: X<>'0
      2090 GOSUB 3190 \ REM     INTEGER EXPRESSIONS
      2100 CALL SBIT(18%/2%,200%+A%,4%/4%)
      2110 CALL TBIT(5%+4%,A%+200%,Z%)
      2120 IF Z%<>1% THEN PRINT #1,'    ERROR: Z%<>'1%
      2130 GOSUB 3750 \ REM     TIME DELAY
      2140 CALL SBIT(4%+5%,A%+200%,4%-4%)
      2150 CALL TBIT(18%-9%,200%+A%,Z%)
      2160 IF Z%<>0% THEN PRINT #1,'    ERROR: Z%<>'0%
      2170 GOSUB 3120 \ REM     STRING EXPRESSIONS
      2180 CALL SBIT('1'&'3',A$&'76','1')
      2190 CALL TBIT('1'&'3',A$&'76',Z$)
      2200 IF Z$<>'     1' THEN PRINT #1,'    ERROR: Z$<>1'
      2210 GOSUB 3750 \ REM     TIME DELAY
      2220 CALL SBIT('1'&'3',A$&'76','0')
      2230 CALL TBIT('1'&'3',A$&'76',Z$)
      2240 IF Z$<>'     0' THEN PRINT #1,'    ERROR: Z$<>0'
      2250 GOSUB 3470 \ REM     NUMERIC VARIABLES
      2260 V0=0
      2270 V1=1
      2280 FOR I=0 TO 15
      2290 CALL SBIT(I,A,V1)
      2300 CALL TBIT(I,A,Z)
      2310 IF Z<>V1 THEN PRINT #1,'    ERROR: Z<>'V1
      2320 GOSUB 3750 \ REM     TIME DELAY
      2330 CALL SBIT(I,A,V0)
      2340 CALL TBIT(I,A,Z)
      2350 IF Z<>V0 THEN PRINT #1,'    ERROR: Z<>'V0
      2360 GOSUB 3750 \ REM     TIME DELAY
      2370 NEXT I
      2380 GOSUB 3400 \ REM     INTEGER VARIABLES
      2390 V0%=0%
      2400 V1%=1%
      2410 FOR I%=0% TO 15%
      2420 CALL SBIT(I%,A%,V1%)
      2430 CALL TBIT(I%,A%,Z%)
      2440 IF Z%<>V1% THEN PRINT #1,'    ERROR: Z%<>'V1%
      2450 GOSUB 3750 \ REM     TIME DELAY
      2460 CALL SBIT(I%,A%,V0%)
      2470 CALL TBIT(I%,A%,Z%)
      2480 IF Z%<>V0% THEN PRINT #1,'    ERROR: Z%<>'V0%
      2490 GOSUB 3750 \ REM     TIME DELAY
      2500 NEXT I%
      2510 GOSUB 3330 \ REM     STRING VARIABLES
      2520 V0$='0'
      2530 V1$='1'
      2540 FOR I=0 TO 7
      2550 I$=STR$(I)


      BASIC-11 EXTENSIONS                                   Page  19
      TESTING THE ROUTINES                                 27 Mar 79


      2560 CALL SBIT(I$,A$,V1$)
      2570 CALL TBIT(I$,A$,Z$)
      2580 IF Z$<>'     '&V1$ THEN PRINT #1,'    ERROR: Z$<>'V1$
      2590 GOSUB 3750 \ REM     TIME DELAY
      2600 CALL SBIT(I$,A$,V0$)
      2610 CALL TBIT(I$,A$,Z$)
      2620 IF Z$<>'     '&V0$ THEN PRINT #1,'    ERROR: Z$<>'V0$
      2630 GOSUB 3750 \ REM     TIME DELAY
      2640 NEXT I
      2650 GOSUB 3680 \ REM     NUMERIC ARRAY ELEMTNTS
      2660 FOR I=0 TO 15
      2670 CALL SBIT(I,A(0),V1)
      2680 CALL TBIT(I,A(0),Z(0))
      2690 IF Z(0)<>V1 THEN PRINT #1,'    ERROR: Z(0)<>'V1
      2700 GOSUB 3750 \ REM     TIME DELAY
      2710 CALL SBIT(I,A(0),V0)
      2720 CALL TBIT(I,A(0),Z(0))
      2730 IF Z(0)<>V0 THEN PRINT #1,'    ERROR: Z(0)<>'V0
      2740 GOSUB 3750 \ REM     TIME DELAY
      2750 NEXT I
      2760 GOSUB 3610 \ REM     INTEGER ARRAY ELEMENTS
      2770 FOR I%=0% TO 15%
      2780 CALL SBIT(I%,A%(1),V1%)
      2790 CALL TBIT(I%,A%(1),Z%(1))
      2800 IF Z%(1)<>V1% THEN PRINT #1,'    ERROR: Z%(1)<>'V1%
      2810 GOSUB 3750 \ REM     TIME DELAY
      2820 CALL SBIT(I%,A%(1),V0%)
      2830 CALL TBIT(I%,A%(1),Z%(1))
      2840 IF Z%(1)<>V0% THEN PRINT #1,'    ERROR: Z%(1)<>'V0%
      2850 GOSUB 3750 \ REM     TIME DELAY
      2860 NEXT I%
      2870 GOSUB 3540 \ REM     STRING ARRAY ELEMTNTS
      2880 FOR I=0 TO 7
      2890 I$=STR$(I)
      2900 CALL SBIT(I$,A$(0),V1$)
      2910 CALL TBIT(I$,A$(0),Z$(0))
      2920 IF Z$(0)<>'     '&V1$ THEN PRINT #1,'    ERROR: Z$(0)<>'V1$
      2930 GOSUB 3750 \ REM     TIME DELAY
      2940 CALL SBIT(I$,A$(0),V0$)
      2950 CALL TBIT(I$,A$(0),Z$(0))
      2960 IF Z$(0)<>'     '&V0$ THEN PRINT #1,'    ERROR: Z$(0)<>'V0$
      2970 GOSUB 3750 \ REM     TIME DELAY
      2980 NEXT I
      2990 RETURN

      3000 PRINT #1
      3010 PRINT #1,'  STRING CONSTANTS'
      3020 GOSUB 3750 \ REM     TIME DELAY
      3030 RETURN

      3040 PRINT #1
      3050 PRINT #1,'  INTEGER CONSTANTS'
      3060 GOSUB 3750 \ REM     TIME DELAY


      BASIC-11 EXTENSIONS                                   Page  20
      TESTING THE ROUTINES                                 27 Mar 79


      3070 RETURN

      3080 PRINT #1
      3090 PRINT #1,'  NUMERIC CONSTANTS'
      3100 GOSUB 3750 \ REM     TIME DELAY
      3110 RETURN

      3120 PRINT #1
      3130 PRINT #1,'  STRING EXPRESSIONS'
      3140 A$='3'
      3150 V$='1'
      3160 Z$=''
      3170 GOSUB 3750 \ REM     TIME DELAY
      3180 RETURN

      3190 PRINT #1
      3200 PRINT #1,'  INTEGER EXPRESSIONS'
      3210 A%=54%
      3220 V%=23%
      3230 Z%=0%
      3240 GOSUB 3750 \ REM     TIME DELAY
      3250 RETURN

      3260 PRINT #1
      3270 PRINT #1,'  NUMERIC EXPRESSIONS'
      3280 A=127
      3290 V=246
      3300 Z=0
      3310 GOSUB 3750 \ REM     TIME DELAY
      3320 RETURN

      3330 PRINT #1
      3340 PRINT #1,'  STRING VARIABLES'
      3350 A$='376'
      3360 V$='123'
      3370 Z$=''
      3380 GOSUB 3750 \ REM     TIME DELAY
      3390 RETURN

      3400 PRINT #1
      3410 PRINT #1,'  INTEGER VARIABLES'
      3420 V%=123%
      3430 A%=254%
      3440 Z%=0%
      3450 GOSUB 3750 \ REM     TIME DELAY
      3460 RETURN

      3470 PRINT #1
      3480 PRINT #1,'  NUMERIC VARIABLES'
      3490 A=254
      3500 V=123
      3510 Z=0
      3520 GOSUB 3750 \ REM     TIME DELAY
      3530 RETURN


      BASIC-11 EXTENSIONS                                   Page  21
      TESTING THE ROUTINES                                 27 Mar 79


      3540 PRINT #1
      3550 PRINT #1,'  STRING ARRAY ELEMENTS'
      3560 A$(0)='376'
      3570 V$(0)='123'
      3580 Z$(0)=''
      3590 GOSUB 3750 \ REM     TIME DELAY
      3600 RETURN

      3610 PRINT #1
      3620 PRINT #1,'  INTEGER ARRAY ELEMENTS'
      3630 A%(1)=254%
      3640 V%(1)=123%
      3650 Z%(1)=0%
      3660 GOSUB 3750 \ REM     TIME DELAY
      3670 RETURN

      3680 PRINT #1
      3690 PRINT #1,'  NUMERIC ARRAY ELEMENTS'
      3700 A(0)=254
      3710 V(0)=123
      3720 Z(0)=0
      3730 GOSUB 3750 \ REM     TIME DELAY
      3740 RETURN

      3750 FOR K%=0% TO 1% \ REM MAKE 1000% FOR ODT
      3760 NEXT K%
      3770 RETURN

      3780 END


      BASIC-11 EXTENSIONS                                   Page  22
      MISCELLANEOUS COMMENTS                               27 Mar 79










                              A.  APPENDIX:
                          MISCELLANEOUS COMMENTS


           The "BASIC-11/RT-11 User's Guide" [3]  describes  how  to
      add assembly language routines to BASIC-11.  This includes the
      general format  of  the  routine,  the  procedures  to  access
      arguments  and  the use of some routines provided by BASIC-11.
      The procedure for incorporating the additional  routines  into
      the  BASIC-11  interpreter is described in the "BASIC-11/RT-11
      Installation Guide"  [4].   This  appendix  will  add  to  the
      information contained in these two references.

           It is convenient to use the  Online  Debugging  Technique
      (ODT)  [6] facility provided by DEC to debug assembly language
      extensions to BASIC-11.  When this is done it is necessary  to
      request a load map during execution of the SUCNFG program.  It
      is also necessary to include ODT  as  the  first  module  name
      during  the CALL statement dialogue.  BASIC-11's start address
      is then found at the global symbol, STARTI, which is contained
      in the root PSECT, BASSCD.

           BASIC-11'S I/O is interrupt driven  and  may  cause  some
      confusion  unless a time delay subroutine is entered following
      any PRINT statement which in turn  is  followed  by  the  CALL
      statement  being debugged.  The time delay subroutine of lines
      3750-3770 of the test program, DATBAS.BAS, is  just  for  this
      purpose.

           Some selected descriptor words are given in Table A-1.

           During debugging it is helpful to set a breakpoint at the
      entry  to  the assembly language routine being debugged.  When
      this breakpoint is reached a pointer map may then be obtained.
      Figures  A-1  through  A-9  are  typical of such pointer maps.
      They  were  obtained  using  a  dummy  routine,  DUMY,   which
      contained  only  a  few NOP instructions plus the required RTS
      instruction.

           Figure 4-4 of the "BASIC-11 User's Guide" [3] illustrates
      an  array  descriptor.  It identifies the third word as "Array
      Size (bytes)", the sixth word as "High limit of 1st subscript"
      and the eighth word as "High limit of 2nd subscript".  This is
      true only if the argument itself points to either the array in
      general  (as  in  Figures  A-5, A-6, and A-8) or to the zeroth
      element of the array (as in  Figure  A-9  C(0,0)).   At  other
      times  when  the  argument  points  to some element beyond the


      BASIC-11 EXTENSIONS                                   Page  23
      MISCELLANEOUS COMMENTS                               27 Mar 79


      zeroth element of the array the value of the third  word  when
      added  to  the  value of the corresponding argument list entry
      equals the address of the first memory location past the upper
      end  of  the array.  The value of the sixth word when added to
      the value of the subscript in the argument  equals  the  upper
      limit  of  the  subscript.  An identical relation prevails for
      the eighth word.



                377     Null argument

                1023    Integer variable

                1100    String variable or array element

                1223    Integer constant

                2041    Numeric variable

                2241    Numeric constant

                21022   Integer array

                21100   String array

                22040   Numeric array

                                TABLE A-1.
                             DESCRIPTOR WORDS



                  CALL DUMY(,,)

                   DSC  LST      ARG  LST
                  ----------    ----------
                  |   377  |<---| 137634 |        R5
                  ----------    ----------    ----------
                  |   377  |    |  10103 |<---| 137624 |
                  ----------    ----------    ----------
                  |   377  |    | 177777 |
                  ----------    ----------
                                | 177777 |
                                ----------
                                | 177777 |
                                ----------

                               FIGURE A-1.
                               POINTER MAP:
                             NULL ARGUMENTS.


      BASIC-11 EXTENSIONS                                   Page  24
      MISCELLANEOUS COMMENTS                               27 Mar 79












              CALL DUMY(1%,2,'3')

                  DSC  LST           ARG  LST
                 ----------         ----------
                 |  1223  |<--------| 137634 |        R5
                 ----------         ----------    ----------
                 |  2241  |         |  10103 |<---| 137624 |
                 ----------         ----------    ----------
              ---| 137604 |  -------| 137620 |
              |  ----------  |      ----------
              |              | -----| 137612 |
              |              | |    ----------
              |              | | ---|  55251 |
              |              | | |  ----------
              |              | | |
              |   '3'  DSC   | | |     '3'
              |  ----------  | | |   -------
              -->|  1300  |  | | --->|  63 |
                 ----------  | |     -------
                 | 137610 |  | |
                 ----------  | |         2
                             | |    ----------
                             | ---->|  40400 |
                             |      ----------
                             |      |    0   |
                             |      ----------
                             |
                             |          1%
                             |      ----------
                             ------>|    1   |
                                    ----------

                               FIGURE A-2.
                               POINTER MAP:
                                CONSTANTS.


      BASIC-11 EXTENSIONS                                   Page  25
      MISCELLANEOUS COMMENTS                               27 Mar 79















              CALL DUMY(A,A%,A$)

                  DSC  LST           ARG  LST
                 ----------         ----------
                 |  2041  |<--------| 137634 |        R5
                 ----------         ----------    ----------
                 |  1023  |         |  10103 |<---| 137624 |
                 ----------         ----------    ----------
              ---| 137616 |  -------|  55130 |
              |  ----------  |      ----------
              |              | -----|  55140 |
              |    A$  DSC   | |    ----------
              |  ----------  | |    |  52262 |
              -->|  1100  |  | |    ----------
                 ----------  | |
              ---|  55146 |  | |        A%
              |  ----------  | |    ----------
              |              | ---->|    0   |
              |      A$      |      ----------
              |  ----------  |
              -->| 177777 |  |           A
                 ----------  |      ----------
                             ------>|    0   |
                                    ----------
                                    |    0   |
                                    ----------

                               FIGURE A-3.
                               POINTER MAP:
                           UNDEFINED VARIABLES.


      BASIC-11 EXTENSIONS                                   Page  26
      MISCELLANEOUS COMMENTS                               27 Mar 79








              A=.5 \ A%=5% \ A$='DUMY'
              CALL DUMY(A,A%,A$,)

                  DSC  LST           ARG  LST
                 ----------         ----------
                 |  2041  |<--------| 137632 |        R5
                 ----------         ----------    ----------
                 |  1023  |         |  10104 |<---| 137620 |
                 ----------         ----------    ----------
              ---| 137612 |  -------|  55130 |
              |  ----------  |      ----------
              |  |   377  |  | -----|  55140 |
              |  ----------  | |    ----------
              |              | | ---|  55331 |
              |              | | |  ----------
              |              | | |  | 177777 |
              |              | | |  ----------
              |              | | |
              |    A$  DSC   | | |      A$
              |  ----------  | | |   -------
              -->|  1100  |  | | --->| 104 |D
                 ----------  | |     -------
                 |  55146 |  | |     | 125 |U
                 ----------  | |     -------
                             | |     | 115 |M
                             | |     -------
                             | |     | 131 |Y
                             | |     -------
                             | |
                             | |        A%
                             | |    ----------
                             | ---->|    5   |
                             |      ----------
                             |
                             |           A
                             |      ----------
                             ------>|  40000 |
                                    ----------
                                    |    0   |
                                    ----------

                               FIGURE A-4.
                               POINTER MAP:
                            DEFINED VARIABLES.


      BASIC-11 EXTENSIONS                                   Page  27
      MISCELLANEOUS COMMENTS                               27 Mar 79





            DIM A(10),A%(10),A$(10)
            CALL DUMY(A(),A%(),A$())

                    DSC  LST           ARG  LST
                   ----------         ----------
            -------| 137546 |<--------| 137574 |        R5
            |      ----------         ----------    ----------
            | -----| 137532 |         |  10103 |<---| 137564 |
            | |    ----------         ----------    ----------
            | | ---| 137516 |  -------| 137656 |
            | | |  ----------  |      ----------
            | | |              | -----| 137630 |
            | | |              | |    ----------
            | | |              | | ---| 137602 |
            | | |              | | |  ----------
            | | |              | | |
            | | |   A$() DSC   | | |     A$()
            | | |  ----------  | | |  ----------
            | | -->|  21100 |  | | -->| 177777 |
            | |    ----------  | |    ----------
            | |    |    0   |  | |    | 177777 |
            | |    ----------  | |    ----------
            | |    |   26   |  | |    :        :
            | |    ----------  | |    ----------
            | |    |    1   |  | |    | 177777 |
            | |    ----------  | |    ----------
            | |    |    0   |  | |
            | |    ----------  | |
            | |    |   12   |  | |
            | |    ----------  | |
            | |                | |
            | |     A%() DSC   | |       A%()
            | |    ----------  | |    ----------
            | ---->|  21022 |  | ---->|    0   |
            |      ----------  |      ----------
            |      |    0   |  |      |    0   |
            |      ----------  |      ----------
            |      |   26   |  |      :        :
            |      ----------  |      ----------
            |      |    1   |  |      |    0   |
            |      ----------  |      ----------
            |      |    0   |  |
            |      ----------  |
            |      |   12   |  |
            |      ----------  |
            V                  V

                               FIGURE A-5.
                               POINTER MAP:
                ONE DIMENSION ARRAYS, UNDEFINED ELEMENTS.


      BASIC-11 EXTENSIONS                                   Page  28
      MISCELLANEOUS COMMENTS                               27 Mar 79









            |                  |
            |       A()  DSC   |          A()
            |      ----------  |      ----------
            ------>|  22040 |  ------>|    0   |
                   ----------         ----------
                   |    0   |         |    0   |
                   ----------         ----------
                   |   54   |         :        :
                   ----------         ----------
                   |    1   |         |    0   |
                   ----------         ----------
                   |    0   |         |    0   |
                   ----------         ----------
                   |   12   |
                   ----------

                         FIGURE A-5 (CONTINUED).
                               POINTER MAP:
                ONE DIMENSION ARRAYS, UNDEFINED ELEMENTS.



            DIM B(2),B%(2),B$(2)
            B(0)=0 \ B%(1)=1% \ B$(2)='TWO'
            CALL DUMY(B(),B%(),B$())

                    DSC  LST           ARG  LST
                   ----------         ----------
            -------| 137606 |<--------| 137634 |        R5
            |      ----------         ----------    ----------
            | -----| 137572 |         |  10103 |<---| 137624 |
            | |    ----------         ----------    ----------
            | | ---| 137566 |  -------| 137716 |
            | | |  ----------  |      ----------
            | | |              | -----| 137710 |
            | | |              | |    ----------
            | | |              | | ---| 137702 |
            | | |              | | |  ----------
            V V V              V V V

                               FIGURE A-6.
                               POINTER MAP:
                 ONE DIMENSION ARRAYS, DEFINED ELEMENTS.


      BASIC-11 EXTENSIONS                                   Page  29
      MISCELLANEOUS COMMENTS                               27 Mar 79






            | | |              | | |
            | | |   B$() DSC   | | |   B$() PTR       B$()
            | | |  ----------  | | |  ----------    -------
            | | -->|  21100 |  | | -->|  55417 |--->|     |
            | |    ----------  | |    ----------    -------------
            | |    |    0   |  | |                  |     |     |
            | |    ----------  | |                  -------------
            | |    |    6   |  | |                 E| 105 | 132 |Z
            | |    ----------  | |                  -------------
            | |    |    1   |  | |                 O| 117 | 122 |R
            | |    ----------  | |                  -------------
            | |    |    0   |  | |                  |     |     |
            | |    ----------  | |                  -------------
            | |    |    2   |  | |                  |     |     |
            | |    ----------  | |                  -------------
            | |                | |                 N| 116 | 117 |O
            | |     B%() DSC   | |       B%()       -------------
            | |    ----------  | |    ----------    |     | 105 |E
            | ---->|  21022 |  | ---->|    0   |    -------------
            |      ----------  |      ----------    |     |     |
            |      |    0   |  |      |    1   |    -------------
            |      ----------  |      ----------   T| 124 |     |
            |      |    6   |  |      |    2   |    -------------
            |      ----------  |      ----------   O| 117 | 127 |W
            |      |    1   |  |                    -------------
            |      ----------  |
            |      |    0   |  |
            |      ----------  |
            |      |    2   |  |
            |      ----------  |
            |                  |
            |       B()  DSC   |          B()
            |      ----------  |      ----------
            ------>|  22040 |  ------>|    0   |
                   ----------         ----------
                   |    0   |         |    0   |
                   ----------         ----------
                   |   14   |         |  40200 |
                   ----------         ----------
                   |    1   |         |    0   |
                   ----------         ----------
                   |    0   |         |  40400 |
                   ----------         ----------
                   |    2   |         |    0   |
                   ----------         ----------

                         FIGURE A-6 (CONTINUED).
                               POINTER MAP:
                 ONE DIMENSION ARRAYS, DEFINED ELEMENTS.


      BASIC-11 EXTENSIONS                                   Page  30
      MISCELLANEOUS COMMENTS                               27 Mar 79







            DIM B(2),B%(2),B$(2)
            B(1)=1 \ B%(2)=2% \ B$(0)='ZERO'
            CALL DUMY(B(1),B%(2),B$(0))

                    DSC  LST           ARG  LST
                   ----------         ----------
            -------| 137606 |<--------| 137634 |        R5
            |      ----------         ----------    ----------
            | -----| 137572 |         |  10103 |<---| 137624 |
            | |    ----------         ----------    ----------
            | | ---| 137566 |  -------| 137722 |
            | | |  ----------  |      ----------
            | | |              | -----| 137714 |
            | | |              | |    ----------
            | | |              | | ---|  55422 |
            | | |              | | |  ----------
            | | |              | | |
            | | |  B$(0) DSC   | | |     B$(0)
            | | |  ----------  | | |    -------
            | | -->|  1100  |  | | ---->| 132 |Z
            | |    ----------  | |      -------
            | |    | 137702 |  | |      | 105 |E
            | |    ----------  | |      -------
            | |                | |      | 122 |R
            | |                | |      -------
            | |                | |      | 117 |O
            | |                | |      -------
            | |                | |
            | |    B%(2) DSC   | |       B%(2)
            | |    ----------  | |    ----------
            | ---->|  21022 |  | ---->|    2   |
            |      ----------  |      ----------
            |      |    0   |  |
            |      ----------  |
            |      |    2   |  |
            |      ----------  |
            |      |    1   |  |
            |      ----------  |
            |      |    0   |  |
            |      ----------  |
            |      |    0   |  |
            |      ----------  |
            V                  V

                               FIGURE A-7.
                               POINTER MAP:
                 ONE DIMENSION ARRAYS, SPECIFIC ELEMENTS.


      BASIC-11 EXTENSIONS                                   Page  31
      MISCELLANEOUS COMMENTS                               27 Mar 79









            |                  |
            |       B(1) DSC   |         B(1)
            |      ----------  |      ----------
            ------>|  22040 |  ------>|  40200 |
                   ----------         ----------
                   |    0   |         |    0   |
                   ----------         ----------
                   |   10   |
                   ----------
                   |    1   |
                   ----------
                   |    0   |
                   ----------
                   |    1   |
                   ----------

                         FIGURE A-7 (CONTINUED).
                               POINTER MAP:
                 ONE DIMENSION ARRAYS, SPECIFIC ELEMENTS.



            DIM C(1,1),C%(1,1),C$(1,1)
            C(0,0)=0 \ C%(0,1)=0% \ C$(1,0)='FIVE'
            CALL DUMY(C(),C%(),C$())

                    DSC  LST           ARG LST
                   ----------         ----------
            -------| 137602 |<--------| 137634 |        R5
            |      ----------         ----------    ----------
            | -----| 137562 |         |  10103 |<---| 137624 |
            | |    ----------         ----------    ----------
            | | ---| 137542 |  -------| 137662 |
            | | |  ----------  |      ----------
            | | |              | -----| 137652 |
            | | |              | |    ----------
            | | |              | | ---| 137642 |
            | | |              | | |  ----------
            V V V              V V V

                               FIGURE A-8.
                               POINTER MAP:
                 TWO DIMENSION ARRAYS, DEFINED ELEMENTS.


      BASIC-11 EXTENSIONS                                   Page  32
      MISCELLANEOUS COMMENTS                               27 Mar 79









            | | |              | | |
            | | |   C$() DSC   | | |   C$() PTR
            | | |  ----------  | | |  ----------
            | | -->|  21100 |  | | -->|  55657 |
            | |    ----------  | |    ----------
            | |    |    0   |  | |
            | |    ----------  | |
            | |    |   10   |  | |
            | |    ----------  | |
            | |    |    2   |  | |
            | |    ----------  | |
            | |    |    0   |  | |
            | |    ----------  | |
            | |    |    1   |  | |
            | |    ----------  | |
            | |    |    0   |  | |
            | |    ----------  | |
            | |    |    1   |  | |
            | |    ----------  | |
            | |                | |
            | |     C%() DSC   | |       C%()
            | |    ----------  | |    ----------
            | ---->|  21022 |  | ---->|    0   |
            |      ----------  |      ----------
            |      |    0   |  |      |    1   |
            |      ----------  |      ----------
            |      |   10   |  |      |    0   |
            |      ----------  |      ----------
            |      |    2   |  |      |    0   |
            |      ----------  |      ----------
            |      |    0   |  |
            |      ----------  |
            |      |    1   |  |
            |      ----------  |
            |      |    0   |  |
            |      ----------  |
            |      |    1   |  |
            |      ----------  |
            V                  V

                         FIGURE A-8 (CONTINUED).
                               POINTER MAP:
                 TWO DIMENSION ARRAYS, DEFINED ELEMENTS.


      BASIC-11 EXTENSIONS                                   Page  33
      MISCELLANEOUS COMMENTS                               27 Mar 79







            |                  |
            |       C()  DSC   |          C()
            |      ----------  |      ----------
            ------>|  22040 |  ------>|    0   |
                   ----------         ----------
                   |    0   |         |    0   |
                   ----------         ----------
                   |   20   |         |    0   |
                   ----------         ----------
                   |    2   |         |    0   |
                   ----------         ----------
                   |    0   |         |    0   |
                   ----------         ----------
                   |    1   |         |    0   |
                   ----------         ----------
                   |    0   |         |    0   |
                   ----------         ----------
                   |    1   |         |    0   |
                   ----------         ----------

                         FIGURE A-8 (CONTINUED).
                               POINTER MAP:
                 TWO DIMENSION ARRAYS / DEFINED ELEMENTS.



            DIM C(1,1),C%(1,1),C$(1,1)
            C(0,0)=0 \ C%(0,1)=1% \ C$(1,0)='FIVE'
            CALL DUMY(C(0,0),C%(0,1),C$(1,0))

                    DSC  LST           ARG  LST
                   ----------         ----------
            -------| 137606 |<--------| 137634 |        R5
            |      ----------         ----------    ----------
            | -----| 137572 |         |  10103 |<---| 137624 |
            | |    ----------         ----------    ----------
            | | ---| 137566 |  -------| 137662 |
            | | |  ----------  |      ----------
            | | |              | -----| 137654 |
            | | |              | |    ----------
            | | |              | | ---|  55731 |
            | | |              | | |  ----------
            V V V              V V V

                               FIGURE A-9.
                               POINTER MAP:
                TWO DIMENSION ARRAYS / SPECIFIC ELEMENTS.


      BASIC-11 EXTENSIONS                                   Page  34
      MISCELLANEOUS COMMENTS                               27 Mar 79




            | | |              | | |
            | | | C$(1,0) DSC  | | |    C$(1,0)
            | | |  ----------  | | |    -------
            | | -->|  1100  |  | | ---->| 106 |F
            | |    ----------  | |      -------
            | |    | 137646 |  | |      | 111 |I
            | |    ----------  | |      -------
            | |                | |      | 126 |V
            | |                | |      -------
            | |                | |      | 105 |E
            | |                | |      -------
            | |                | |
            | |   C%(0,1) DSC  | |      C%(0,1)
            | |    ----------  | |    ----------
            | ---->|  21022 |  | ---->|    1   |
            |      ----------  |      ----------
            |      |    0   |  |
            |      ----------  |
            |      |   10   |  |
            |      ----------  |
            |      |    2   |  |
            |      ----------  |
            |      |    0   |  |
            |      ----------  |
            |      |    2   |  |
            |      ----------  |
            |      |        |  |
            |      ----------  |
            |      |        |  |
            |      ----------  |
            |                  |
            |      C(0,0) DSC  |        C(0,0)
            |      ----------  |      ----------
            ------>|  22040 |  ------>|    0   |
                   ----------         ----------
                   |    0   |         |    0   |
                   ----------         ----------
                   |   20   |
                   ----------
                   |    2   |
                   ----------
                   |    0   |
                   ----------
                   |    3   |
                   ----------
                   |    0   |
                   ----------
                   |    3   |
                   ----------

                         FIGURE A-9 (CONTINUED).
                               POINTER MAP:
                TWO DIMENSION ARRAYS / SPECIFIC ELEMENTS.


      BASIC-11 EXTENSIONS                                   Page  35
      MISCELLANEOUS COMMENTS                               27 Mar 79


           Being  able  to  write  handlers  implies  a  real   time
      capability.  When interacting with hardware in real time it is
      not  advisable  to  use  strings  (octal  values).    BASIC-11
      allocates  string storage space dynamicaly.  In the process of
      doing this dynamic allocation BASIC-11  occasionally  collects
      abandoned   string   storage   space.    This  may  take  some
      considerable amount of time (as much as tens of seconds).

           The PUT and GET routines offer  the  ability  to  perform
      integer arithmetic in octal.  The actual arithmetic operations
      are performed by BASIC-11  in  decimal.   Conversions  between
      octal and decimal are handled by the PUT and GET routines.  An
      unused vector location is a convenient bus  address  for  this
      purpose.


      BASIC-11 EXTENSIONS                                   Page  36
      FLOW CHARTS                                          27 Mar 79










                              B.  APPENDIX:
                               FLOW CHARTS

           This appendix contains flow charts  and  the  code  which
      implements  the extension routines of DATBAS.  The first eight
      charts are of the interface modules and the last chart is of a
      macro.  All the rest describe the supporting subroutines.

           Top down design was used to achieve the  first  draft  of
      the  code  in  one  and  a half working days.  The first draft
      included both  code  and  flow  charts  as  do  the  following
      figures.   Top  down  testing resulted in complete operational
      status by the end of the fourth working day.   This  does  not
      include  the  time  spent  studying  the  new  CALL  statement
      interface for BASIC-11 V2 [8].



                                               -----
        GET$:                                 ( GET )
                                               -----
                                                 |
                                                 V
                                            -----------
                MOV     R5,ORIGR5           | SAVE R5 |
                                            -----------
                                                 |
                                                 V
                                                / \
                                               /   \
                                              / TWO \  NO   -----
                CMP     (R5)+,#101002        < ARGS  >---->( 99$ )
                BNE     99$                   \     /       -----
                                               \   /
                                                \ /
                                                 | YES
                                                 V
                                        -------------------
                MOV     -4(R5),R4       | GET DSC LST PTR |
                                        -------------------
                                                 |
                                                 V

                               FIGURE B-1.
                            FLOW CHART:  GET.


      BASIC-11 EXTENSIONS                                   Page  37
      FLOW CHARTS                                          27 Mar 79










                                                 |
                                                 V
                                          ---------------
                JSR     PC,GETARG         ||  GETARG   ||
                                          || ARG1=>R3  ||
                                          ---------------
                                                 |
                                                 V
                                           -------------
                JSR     PC,TSTADR          || TSTADR  ||
                                           -------------
                                                 |
                                                 V
                                                / \
                                               /   \
                                              /     \  NO   -----
                ROR     R3                   < WORD  >---->( 99$ )
                BCS     99$                   \ ADR /       -----
                                               \   /
                                                \ /
                                                 | YES
                                                 V
                ROL     R3                 -------------
                MOV     R3,BUSADR          | SAVE ARG1 |
                CLR     BYTFLG             -------------
                                                 |
                                                 V
                                           -------------
                JSR     PC,DELARG          || DELARG  ||
                                           -------------
                                                 |
                                                 V
                                               -----
                RTS     PC                    ( RTS )
                                               -----
        99$:    JMP     $ARGER

                         FIGURE B-1 (CONTINUED).
                            FLOW CHART:  GET.


      BASIC-11 EXTENSIONS                                   Page  38
      FLOW CHARTS                                          27 Mar 79



                                              -------
        GETB$:                               ( GETB  )
                                              -------
                                                 |
                                                 V
                                            -----------
                MOV     R5,ORIGR5           | SAVE R5 |
                                            -----------
                                                 |
                                                 V
                                                / \
                                               /   \
                                              / TWO \  NO   -----
                CMP     (R5)+,#101002        < ARGS  >---->( 99$ )
                BNE     99$                   \     /       -----
                                               \   /
                                                \ /
                                                 | YES
                                                 V
                                        -------------------
                MOV     -4(R5),R4       | GET DSC LST PTR |
                                        -------------------
                                                 |
                                                 V
                                          ---------------
                JSR     PC,GETARG         ||  GETARG   ||
                                          || ARG1=>R3  ||
                                          ---------------
                                                 |
                                                 V
                                           -------------
                JSR     PC,TSTADR          || TSTADR  ||
                                           -------------
                                                 |
                                                 V
                                           -------------
                MOV     R3,BUSADR          | SAVE ARG1 |
                INC     BYTFLG             -------------
                                                 |
                                                 V
                                           -------------
                JSR     PC,DELARG          || DELARG  ||
                                           -------------
                                                 |
                                                 V
                                               -----
                RTS     PC                    ( RTS )
                                               -----
        99$:    JMP     $ARGER

                               FIGURE B-2.
                            FLOW CHART:  GETB.


      BASIC-11 EXTENSIONS                                   Page  39
      FLOW CHARTS                                          27 Mar 79




                                              -------
        IDEN$:                               ( IDEN  )
                                              -------
                                                 |
                                                 V
                                             ---------
                JSR     R1,MSG               || MSG ||
                .ASCIZ  \ID MSG\             ---------
                                                 |
                                                 V
                                               -----
                RTS     PC                    ( RTS )
                                               -----

                               FIGURE B-3.
                            FLOW CHART:  IDEN.



                                              -------
        NULL$:                               ( NULL  )
                                              -------
                                                 |
                                                 V
                                            -----------
                MOV     R5,ORIGR5           | SAVE R5 |
                                            -----------
                                                 |
                                                 V
                                          ---------------
                MOV     (R5)+,ARVVAL      | GET # ARGS  |
                CLRB    ARGVAL+1          ---------------
                                                 |
                                                 V
                                        -------------------
                MOV     -4(R5),R4       | GET DSC LST PTR |
                                        -------------------
                                                 |
                                                 V
                                                / \
                                               /   \
                                              / ANY \  NO
                TST     ARGVAL               < ARGS  >-----
                BEQ     2$                    \     /     |
                                               \   /      |
                                                \ /       |
                                                 | YES    |
                                                 V        V

                               FIGURE B-4.
                            FLOW CHART:  NULL.


      BASIC-11 EXTENSIONS                                   Page  40
      FLOW CHARTS                                          27 Mar 79


                                                 |        |
        1$:                             -------->|        |
                                        |        V        |
                                        |  -------------  |
                JSR     PC,NULARY       |  || NULARY  ||  |
                DEC     ARGVAL          |  -------------  |
                                        |        |        |
                                        |        V        |
                                        |       / \       |
                                        |      /   \      |
                                        | NO  /     \     |
                BGT     1$              -----< DONE  >    |
                                              \     /     |
                                               \   /      |
                                                \ /       |
                                                 | YES    |
        2$:                                      |<--------
                                                 V
                                               -----
                RTS     PC                    ( RTS )
                                               -----

                         FIGURE B-4 (CONTINUED).
                            FLOW CHART:  NULL.



                                               -----
        PUT$:                                 ( PUT )
                                               -----
                                                 |
                                                 V
                                            -----------
                MOV     R5,ORIGR5           | SAVE R5 |
                                            -----------
                                                 |
                                                 V
                                                / \
                                               /   \
                                              / TWO \  NO   -----
                CMP     (R5)+,#101002        < ARGS  >---->( 99$ )
                BNE     99$                   \     /       -----
                                               \   /
                                                \ /
                                                 | YES
                                                 V
                                        -------------------
                MOV     -4(R5),R4       | GET DSC LST PTR |
                                        -------------------
                                                 |
                                                 V

                               FIGURE B-5.
                            FLOW CHART:  PUT.


      BASIC-11 EXTENSIONS                                   Page  41
      FLOW CHARTS                                          27 Mar 79







                                                 |
                                                 V
                                          ---------------
                JSR     PC,GETARG         ||  GETARG   ||
                                          || ARG1=>R3  ||
                                          ---------------
                                                 |
                                                 V
                                           -------------
                MOV     R3,ARGVAL          | SAVE ARG1 |
                                           -------------
                                                 |
                                                 V
                                          ---------------
                JSR     PC,GETARG         ||  GETARG   ||
                                          || ARG2=>R3  ||
                                          ---------------
                                                 |
                                                 V
                                           -------------
                JSR     PC,TSTADR          || TSTADR  ||
                                           -------------
                                                 |
                                                 V
                                                / \
                                               /   \
                                              /     \  NO   -----
                ROR     R3                   < WORD  >---->( 99$ )
                BCS     99$                   \ ADR /       -----
                                               \   /
                                                \ /
                                                 | YES
                                                 V
                                            -----------
                ROL     R3                  | DEL VAL |
                MOV     ARGVAL,(R3)         -----------
                                                 |
                                                 V
                                               -----
                RTS     PC                    ( RTS )
                                               -----
        99$:    JMP     $ARGER

                         FIGURE B-5 (CONTINUED).
                            FLOW CHART:  PUT.


      BASIC-11 EXTENSIONS                                   Page  42
      FLOW CHARTS                                          27 Mar 79



                                              -------
        PUTB$:                               ( PUTB  )
                                              -------
                                                 |
                                                 V
                                            -----------
                MOV     R5,ORIGR5           | SAVE R5 |
                                            -----------
                                                 |
                                                 V
                                                / \
                                               /   \
                                              / TWO \  NO   -----
                CMP     (R5)+,#101002        < ARGS  >---->( 99$ )
                BNE     99$                   \     /       -----
                                               \   /
                                                \ /
                                                 | YES
                                                 V
                                        -------------------
                MOV     -4(R5),R4       | GET DSC LST PTR |
                                        -------------------
                                                 |
                                                 V
                                          ---------------
                JSR     PC,GETARG         ||  GETARG   ||
                                          || ARG1=>R3  ||
                                          ---------------
                                                 |
                                                 V
                                                / \
                                               /   \
                                              /  >  \  YES   -----
                CMP     R3,#127.             <  127  >----->( 99$ )
                BGT     99$                   \     /        -----
                                               \   /
                                                \ /
                                                 | NO
                                                 V
                                                / \
                                               /   \
                                              /  <  \  YES   -----
                CMP     R3,#-128.            < -128  >----->( 99$ )
                BLT     99$                   \     /        -----
                                               \   /
                                                \ /
                                                 | NO
                                                 V

                               FIGURE B-6.
                            FLOW CHART:  PUTB.


      BASIC-11 EXTENSIONS                                   Page  43
      FLOW CHARTS                                          27 Mar 79














                                                 |
                                                 V
                                           -------------
                MOV     R3,ARGVAL          | SAVE ARG1 |
                                           -------------
                                                 |
                                                 V
                                          ---------------
                JSR     PC,GETARG         ||  GETARG   ||
                                          || ARG2=>R3  ||
                                          ---------------
                                                 |
                                                 V
                                           -------------
                JSR     PC,TSTADR          || TSTADR  ||
                                           -------------
                                                 |
                                                 V
                                            -----------
                MOVB    ARGVAL,(R3)         | DEL VAL |
                                            -----------
                                                 |
                                                 V
                                               -----
                RTS     PC                    ( RTS )
                                               -----
        99$:    JMP     $ARGER

                         FIGURE B-6 (CONTINUED).
                            FLOW CHART:  PUTB.


      BASIC-11 EXTENSIONS                                   Page  44
      FLOW CHARTS                                          27 Mar 79






                                              -------
        SBIT$:                               ( SBIT  )
                                              -------
                                                 |
                                                 V
                                        -------------------
                                        ||    AG1AG2     ||
                JSR     PC,AG1AG2       || ARG1=>ARGVAL  ||
                                        || ARG2=>BUSADR  ||
                                        -------------------
                                                 |
                                                 V
                                          ---------------
                JSR     PC,GETARG         ||  GETARG   ||
                                          || ARG3=>R3  ||
                                          ---------------
                                                 |
                                                 V
                                                / \
                                               /   \
                                              / SET \  NO
                TST     R3                   <  THE  >------
                BEQ     1$                    \ BIT /      |
                                               \   /       |
                                                \ /        |
                                                 | YES     |
                                                 V         |
                                          ---------------  |
                BIS     ARGVAL,@BUSADR    | SET THE BIT |  |
                BR      2$                ---------------  |
                                                 |         |
                                       -----------         |
                                       |         -----------
        1$:                            |         V
                                       |  ---------------
                BIC     ARGVAL,@BUSADR |  | CLR THE BIT |
                                       |  ---------------
                                       |         |
        2$:                            --------->|
                                                 V
                                               -----
                RTS     PC                    ( RTS )
                                               -----

                               FIGURE B-7.
                            FLOW CHART:  SBIT.


      BASIC-11 EXTENSIONS                                   Page  45
      FLOW CHARTS                                          27 Mar 79




                                              -------
        TBIT$:                               ( TBIT  )
                                              -------
                                                 |
                                                 V
                                        -------------------
                                        ||    AG1AG2     ||
                JSR     PC,AG1AG2       || ARG1=>ARGVAL  ||
                                        || ARG2=>BUSADR  ||
                                        -------------------
                                                 |
                                                 V
                                                / \
                                               /   \
                                              / IS  \  NO
                BIT     ARGVAL,@BUSADR       <  BIT  >-----
                BEQ     1$                    \ SET /     |
                                               \   /      |
                                                \ /       |
                                                 | YES    |
                                                 V        |
                                           -------------  |
                MOV     #1,ARGVAL          | SHOW SET  |  |
                BR      2$                 -------------  |
                                                 |        |
                                        ----------        |
                                        |        ----------
        1$:                             |        V
                                        |  -------------
                CLR     ARGVAL          |  | SHOW CLR  |
                                        |  -------------
                                        |        |
        2$:                             -------->|
                                                 V
                                            -----------
                MOV     #ARGVAL,BUSADR      | GET PTR |
                CLR     BYTFLG              -----------
                                                 |
                                                 V
                                           -------------
                JSR     PC,DELARG          || DELARG  ||
                                           -------------
                                                 |
                                                 V
                                               -----
                RTS     PC                    ( RTS )
                                               -----

                               FIGURE B-8.
                            FLOW CHART:  TBIT.


      BASIC-11 EXTENSIONS                                   Page  46
      FLOW CHARTS                                          27 Mar 79




                                             ---------
        AG1AG2:                             ( AG1AG2  )
                                             ---------
                                                 |
                                                 V
                                            -----------
                MOV     R5,ORIGR5           | SAVE R5 |
                                            -----------
                                                 |
                                                 V
                                                / \
                                               /   \
                                              /  3  \  NO   -----
                CMP     (R5)+,#101003        < ARGS  >---->( 99$ )
                BNE     99$                   \     /       -----
                                               \   /
                                                \ /
                                                 | YES
                                                 V
                                        -------------------
                MOV     -4(R5),R4       | GET DSC LST PTR |
                                        -------------------
                                                 |
                                                 V
                                          ---------------
                JSR     PC,GETARG         ||  GETARG   ||
                                          || ARG1=>R3  ||
                                          ---------------
                                                 |
                                                 V
                                         -----------------
                JSR     PC,BITMSK        ||   BITMSK    ||
                                         || MSK=>ARGVAL ||
                                         -----------------
                                                 |
                                                 V
                                          ---------------
                JSR     PC,GETARG         ||  GETARG   ||
                                          || ARG2=>R3  ||
                                          ---------------
                                                 |
                                                 V
                                           -------------
                JSR     PC,TSTADR          || TSTADR  ||
                                           -------------
                                                 |
                                                 V

                               FIGURE B-9.
                           FLOW CHART:  AG1AG2.


      BASIC-11 EXTENSIONS                                   Page  47
      FLOW CHARTS                                          27 Mar 79


















                                                 |
                                                 V
                                                / \
                                               /   \
                                              /     \  NO   -----
                ROR     R3                   < WORD  >---->( 99$ )
                BCS     99$                   \ ADR /       -----
                                               \   /
                                                \ /
                                                 | YES
                                                 V
                ROL     R3                 -------------
                MOV     R3,BUSADR          | SAVE ARG2 |
                CLR     BYTFLG             -------------
                                                 |
                                                 V
                                               -----
                RTS     PC                    ( RTS )
                                               -----
        99$:    JMP     $ARGER

                         FIGURE B-9 (CONTINUED).
                           FLOW CHART:  AG1AG2.


      BASIC-11 EXTENSIONS                                   Page  48
      FLOW CHARTS                                          27 Mar 79




                                             ---------
        BITMSK:                             ( BITMSK  )
                                             ---------
                                                 |
                                                 V
                                                / \
                                               /   \
                                              / ARG \  YES   -----
                TST     R3                   <  <0   >----->( 99$ )
                BLT     99$                   \     /        -----
                                               \   /
                                                \ /
                                                 | NO
                                                 V
                                                / \
                                               /   \
                                              / ARG \  YES   -----
                CMP     R3,#15.              <  >15  >----->( 99$ )
                BGT     99$                   \     /        -----
                                               \   /
                                                \ /
                                                 | NO
                                                 V
                                            -----------
                CLR     ARGVAL              | CLR MSK |
                SEC                         -----------
                                                 |
        1$:                                      |<--------
                                                 V        |
                                           -------------  |
                ROL     ARGVAL             | MAKE MASK |  |
                DEC     R3                 -------------  |
                                                 |        |
                                                 V        |
                                                / \       |
                                               /   \      |
                                              /     \  NO |
                BGE     1$                   < DONE  >-----
                                              \     /
                                               \   /
                                                \ /
                                                 | YES
                                                 V
                                               -----
                RTS     PC                    ( RTS )
                                               -----
        99$:    JMP     $ARGER

                               FIGURE B-10.
                           FLOW CHART:  BITMSK.


      BASIC-11 EXTENSIONS                                   Page  49
      FLOW CHARTS                                          27 Mar 79



                                             ---------
        DELARG:                             ( DELARG  )
                                             ---------
                                                 |
                                                 V
                                         -----------------
                                         ||   GETDSC    ||
                JSR     PC,GETDSC        || DSC PTR=>R2 ||
                                         || DSC WRD=>R3 ||
                                         -----------------
                                                 |
                                                 V
                                                / \
                                               /   \
                                              / OCT \  NO
                BIT     #100,R3              <  ARG  >-----
                BEQ     1$                    \     /     |
                                               \   /      |
                                                \ /       |
                                                 | YES    |
                                                 V        |
                                           -------------  |
                JSR     PC,DELOCT          || DELOCT  ||  |
                BR      3$                 -------------  |
                                                 |        |
                                        ----------        |
                                        |        ----------
        1$:                             |        V
                                        |       / \
                                        |      /   \
                                        |     /     \  NO
                BIT     #40,R3          |    < REAL  >-----
                BEQ     2$              |     \ ARG /     |
                                        |      \   /      |
                                        |       \ /       |
                                        |        | YES    |
                                        |        V        |
                                        |  -------------  |
                JSR     PC,DELREL       |  || DELREL  ||  |
                BR      3$              |  -------------  |
                                        |        |        |
                                        |<--------        |
        2$:                             |        ----------
                                        |        V
                                        |  -------------
                JSR     PC,DELINT       |  || DELINT  ||
                                        |  -------------
                                        |        |
                                        -------->|
        3$:                                      V

                               FIGURE B-11.
                           FLOW CHART:  DELARG.


      BASIC-11 EXTENSIONS                                   Page  50
      FLOW CHARTS                                          27 Mar 79





                                                 |
                                                 V
                                            -----------
                TST     (R5)+               | BUMP R5 |
                                            -----------
                                                 |
                                                 V
                                               -----
                RTS     PC                    ( RTS )
                                               -----

                         FIGURE B-11 (CONTINUED).
                           FLOW CHART:  DELARG.



                                             ---------
        DELINT:                             ( DELINT  )
                                             ---------
                                                 |
                                                 V
                                                / \
                                               /   \
                                              / DEL \ NO
                TST     BYTFLG               < BYTE  >----
                BEQ     1$                    \     /    |
                                               \   /     |
                                                \ /      |
                                                 | YES   |
                                                 V       V
                                            -----------  |
                MOVB    @BUSADR,@(R5)       | DEL BYT |  |
                BR      2$                  -----------  |
                                                 |       |
                                         ---------       |
                                         |       ---------
        1$:                              |       V
                                         |  -----------
                MOV     @BUSADR,@(R5)    |  | DEL WRD |
                                         |  -----------
                                         |       |
        2$:                              ------->|
                                                 V
                                               -----
                RTS     PC                    ( RTS )
                                               -----

                               FIGURE B-12.
                           FLOW CHART:  DELINT.


      BASIC-11 EXTENSIONS                                   Page  51
      FLOW CHARTS                                          27 Mar 79



                                             ---------
        DELOCT:                             ( DELOCT  )
                                             ---------
                                                 |
                                                 V
                                           -------------
                JSR     R5,PSHRGS          || PSHRGS  ||
                                           -------------
                                                 |
                                                 V
                MOV     #10$,-(SP)         -------------
                MOV     #6,-(SP)           || PSHVAL  ||
                PSHVAL                     -------------
                                                 |
                                                 V
                                            -----------
                JSR     PC,$OCO             || $OCO  ||
                                            -----------
                                                 |
                                                 V
                                                / \
                                               /   \
                                              /     \  YES   -----
                BCS     99$                  <  ERR  >----->( 99$ )
                                              \     /        -----
                                               \   /
                                                \ /
                                                 | NO
                                                 V
                                           -------------
                JSR     R5,POPRGS          || POPRGS  ||
                                           -------------
                                                 |
                MOV     2(R2),11$                V
                MOV     #6,R0               -----------
                MOV     #100,R1             || $ALC  ||
                MOV     R5,CRNTR5           -----------
                MOV     ORIGR5,R5                |
                JSR     PC,$ALC                  V
                                                / \
                                               /   \
                                              /     \  YES   ------
                BCS     100$                 <  ERR  >----->( 100$ )
                                              \     /        ------
                                               \   /
                                                \ /
                                                 | NO
                                                 V

                               FIGURE B-13.
                           FLOW CHART:  DELOCT.


      BASIC-11 EXTENSIONS                                   Page  52
      FLOW CHARTS                                          27 Mar 79





                                                 |
                                                 V
                                           -------------
                MOV     #6,R1              | PREP FOR  |
                MOV     #10$,R3            |  STR MOV  |
                                           -------------
                                                 |
        3$:                                      |<--------
                                                 V        |
                                            -----------   |
                MOVB    (R3)+,(R0)+         | MOV STR |   |
                DEC     R1                  -----------   |
                                                 |        |
                                                 V        |
                                                / \       |
                                               /   \      |
                                              /     \  NO |
                BNE     3$                   < DONE  >-----
                                              \     /
                                               \   /
                                                \ /
                                                 | YES
                                                 V
                MOV     SP,R0              -------------
                MOV     11$,R1             || $STORE  ||
                JSR     PC,$STORE          -------------
                                                 |
                                                 V
                                           -------------
                JSR     PC,$DEALC          || $DEALC  ||
                                           -------------
                                                 |
                                                 V
                                          ---------------
                NOV     CRNTR5,R5         | RESTORE R5  |
                                          ---------------
                                                 |
                                                 V
                                               -----
                RTS     PC                    ( RTS )
                                               -----
        10$:    .BLKB 6         ;STRING SPACE
        11$:    0               ;STRING REFERENCE POINTER
        99$:    JMP     $ARGER
        100$:   JSR     R1,$BOMB
                .ASCIZ  \ERR MSG\

                         FIGURE B-13 (CONTINUED).
                           FLOW CHART:  DELOCT.


      BASIC-11 EXTENSIONS                                   Page  53
      FLOW CHARTS                                          27 Mar 79









                                             ---------
        DELREL:                             ( DELREL  )
                                             ---------
                                                 |
                                                 V
                                           -------------
                PSHVAL                     || PSHVAL  ||
                                           -------------
                                                 |
                                                 V
                                           -------------
                JSR     R4,$POLSH          || $POLSH  ||
                                           -------------
                                                 |
                                                 V
                                             ---------
                $IR                          || $IR ||
                                             ---------
                                                 |
                                                 V
                                           -------------
                $UNPOL                     || $UNPOL  ||
                                           -------------
                                                 |
                                                 V
                                            -----------
                MOV     (R5),R3             | GET PTR |
                                            -----------
                                                 |
                                                 V
                                           -------------
                MOV     (SP)+,(R3)         | DEL REAL  |
                MOV     (SP)+,2(R3)        -------------
                                                 |
                                                 V
                                               -----
                RTS     PC                    ( RTS )
                                               -----

                               FIGURE B-14.
                           FLOW CHART:  DELREL.


      BASIC-11 EXTENSIONS                                   Page  54
      FLOW CHARTS                                          27 Mar 79





                                             ---------
        GETARG:                             ( GETARG  )
                                             ---------
                                                 |
                                                 V
                                         -----------------
                                         ||   GETDSC    ||
                JSR     PC,GETDSC        || DSC PTR=>R2 ||
                                         || DSC WRD=>R3 ||
                                         -----------------
                                                 |
                                                 V
                                                / \
                                               /   \
                                              / OCT \  NO
                BIT     #100,R3              <  ARG  >-----
                BEQ     1$                    \     /     |
                                               \   /      |
                                                \ /       |
                                                 | YES    |
                                                 V        |
                                           -------------  |
                JSR     PC,GETOCT          || GETOCT  ||  |
                BR      3$                 || ARG=>R3 ||  |
                                           -------------  |
                                                 |        |
                                        ----------        |
                                        |        ----------
        1$:                             |        V
                                        |       / \
                                        |      /   \
                                        |     /     \  NO
                BIT     #40,R3          |    < REAL  >-----
                BEQ     2$              |     \ ARG /     |
                                        |      \   /      |
                                        |       \ /       |
                                        |        | YES    |
                                        |        V        |
                                        |  -------------  |
                JSR     PC,GETREL       |  || GETREL  ||  |
                BR      3$              |  || ARG=>R3 ||  |
                                        |  -------------  |
                                        |        |        |
                                        |<--------        |
                                        V                 V

                               FIGURE B-15.
                           FLOW CHART:  GETARG.


      BASIC-11 EXTENSIONS                                   Page  55
      FLOW CHARTS                                          27 Mar 79



















                                        |                 |
                                        |        ----------
        2$:                             |        V
                                        |   -----------
                MOV     @(R5),R3        |   |   INT   |
                                        |   | ARG=>R3 |
                                        |   -----------
                                        |        |
        3$:                             -------->|
                                                 V
                                            -----------
                TST     (R5)+               | BUMP R5 |
                                            -----------
                                                 |
                                                 V
                                               -----
                RTS     PC                    ( RTS )
                                               -----

                         FIGURE B-15 (CONTINUED).
                           FLOW CHART:  GETARG.


      BASIC-11 EXTENSIONS                                   Page  56
      FLOW CHARTS                                          27 Mar 79








                                             ---------
        GETDSC:                             ( GETDSC  )
                                             ---------
                                                 |
                                                 V
                                          ---------------
                MOV     R4,R2             | DSC WRD=>R2 |
                MOV     (R4)+,R3          | DSC PTR=>R3 |
                                          ---------------
                                                 |
                                                 V
                                                / \
                                               /   \
                                              /     \  YES
                BIT     #1,R3                <  R3   >------
                BNE     1$                    \ PTR /      |
                                               \   /       |
                                                \ /        |
                                                 | NO      |
                                                 V         |
                                          ---------------  |
                MOV     R3,R2             | DSC WRD=>R2 |  |
                MOV     (R3),R3           | DSC PTR=>R3 |  |
                                          ---------------  |
                                                 |         |
        1$:                                      |<---------
                                                 V
                                                / \
                                               /   \
                                              /     \  YES   -----
                CMP     #177,R3              < NULL  >----->( 99$ )
                BEQ     99$                   \ ARG /        -----
                                               \   /
                                                \ /
                                                 | NO
                                                 V
                                               -----
                RTS     PC                    ( RTS )
                                               -----
        99$:    JMP     $ARGER

                               FIGURE B-16.
                           FLOW CHART:  GETDSC.


      BASIC-11 EXTENSIONS                                   Page  57
      FLOW CHARTS                                          27 Mar 79



                                             ---------
        GETOCT:                             ( GETOCT  )
                                             ---------
                                                 |
                                                 |
                MOV     2(R2),R0                 V
                MOV     #100,R1             -----------
                MOV     R5,CRNTR5           || $FIND ||
                MOV     ORIGR5,R5           -----------
                JSR     PC,$FIND                 |
                                                 V
                                           -------------
                JSR     R5,PSHRGS          || PSHRGS  ||
                                           -------------
                                                 |
                                                 V
                MOV     R0,-(SP)            -----------
                MOV     R1,-(SP)            || $OCI  ||
                JSR     PC,$OCI             -----------
                                                 |
                                                 V
                                                / \
                                               /   \
                                              /     \  YES   -----
                BCS     99$                  <  ERR  >----->( 99$ )
                                              \     /        -----
                                               \   /
                                                \ /
                                                 | NO
                                                 V
                                            -----------
                MOV     (SP)+,6(SP)         | ARG=>R3 |
                                            -----------
                                                 |
                                                 V
                                           -------------
                JSR     R5,POPRGS          || POPRGS  ||
                                           -------------
                                                 |
                                                 V
                                          ---------------
                MOV     CRNTR5,R5         | RESTORE R5  |
                                          ---------------
                                                 |
                                                 V
                                               -----
                RTS     PC                    ( RTS )
                                               -----
        99$:    JMP     $ARGER

                               FIGURE B-17.
                           FLOW CHART:  GETOCT.


      BASIC-11 EXTENSIONS                                   Page  58
      FLOW CHARTS                                          27 Mar 79








                                             ---------
        GETREL:                             ( GETREL  )
                                             ---------
                                                 |
                                                 V
                                            -----------
                MOV     (R5),R3             | GET PTR |
                                            -----------
                                                 |
                                                 V
                                            -----------
                MOV     2(R3),-(SP)         | PSH REL |
                MOV     (R3),-(SP)          |   ARG   |
                                            -----------
                                                 |
                                                 V
                                           -------------
                JSR     R4,$POLSH          || $POLSH  ||
                                           -------------
                                                 |
                                                 V
                                             ---------
                $RI                          || $RI ||
                                             ---------
                                                 |
                                                 V
                                           -------------
                $UNPOL                     || $UNPOL  ||
                                           -------------
                                                 |
                                                 V
                                            -----------
                MOV     (SP)+,R3            | ARG=>R3 |
                                            -----------
                                                 |
                                                 V
                                               -----
                RTS     PC                    ( RTS )
                                               -----

                               FIGURE B-18.
                           FLOW CHART:  GETREL.


      BASIC-11 EXTENSIONS                                   Page  59
      FLOW CHARTS                                          27 Mar 79




                                             ---------
        NULARY:                             ( NULARY  )
                                             ---------
                                                 |
                                                 V
                                         -----------------
                                         ||   GETDSC    ||
                JSR     PC,GETDSC        || DSC PTR=>R2 ||
                                         || DSC WRD=>R3 ||
                                         -----------------
                                                 |
                                                 V
                                                / \
                                               /   \
                                              /     \  NO   -----
                BIT     #20000,R3            <  ARY  >---->( 99$ )
                BEQ     99$                   \     /       -----
                                               \   /
                                                \ /
                                                 | YES
                                                 V
                                                / \
                                               /   \
                                              /     \  NO
                BIT     #100,R3              <  OCT  >-----
                BEQ     1$                    \     /     |
                                               \   /      |
                                                \ /       |
                                                 | YES    |
                                                 V        |
                                           -------------  |
                JSR     PC,NULOCT          || NULOCT  ||  |
                BR      2$                 -------------  |
                                                 |        |
                                        ----------        |
                                        |        ----------
        1$:                             |        V
                                        |  -------------
                JSR     PC,NULNUM       |  || NULNUM  ||
                                        |  -------------
                                        |        |
        2$:                             -------->|
                                                 V
                                               -----
                RTS     PC                    ( RTS )
                                               -----
        99$:    JMP     $ARGER

                               FIGURE B-19.
                           FLOW CHART:  NULARY.


      BASIC-11 EXTENSIONS                                   Page  60
      FLOW CHARTS                                          27 Mar 79











                                             ---------
        NULNUM:                             ( NULNUM  )
                                             ---------
                                                 |
                                                 V
                                            -----------
                MOV     4(R2),R2            | GET LEN |
                ASR     R2                  | IN WRDS |
                                            -----------
                                                 |
                                                 V
                                            -----------
                MOV     (R5)+,R3            | GET PTR |
                                            -----------
                                                 |
        1$:                                      |<---------
                                                 V         |
                                            -----------    |      
                CLR     (R3)+               | NUL ARY |    |
                DEC     R2                  -----------    |
                                                 |         |
                                                 |         |
                                                / \        |
                                               /   \       |
                                              /     \  NO  |
                BGT     1$                   < DONE  >------
                                              \     /
                                               \   /
                                                \ /
                                                 | YES
                                                 V
                                               -----
                RTS     PC                    ( RTS )
                                               -----

                               FIGURE B-20.
                           FLOW CHART:  NULNUM.


      BASIC-11 EXTENSIONS                                   Page  61
      FLOW CHARTS                                          27 Mar 79











                                             ---------
        NULOCT:                             ( NULOCT  )
                                             ---------
                                                 |
                                                 V
                                            -----------
                MOV     4(R2),R2            | GET LEN |
                ASR     R2                  | IN WRDS |
                                            -----------
                                                 |
                                                 V
                                            -----------
                MOV     (R5)+,R3            | GET PTR |
                                            -----------
                                                 |
        1$:                                      |<---------
                                                 V         |
                                            -----------    |
                MOV     #-1,(R3)+           | NUL ARY |    |
                DEC     R2                  -----------    |
                                                 |         |
                                                 V         |
                                                / \        |
                                               /   \       |
                                              /     \  NO  |
                BGT     1$                   < DONE  >------
                                              \     /
                                               \   /
                                                \ /
                                                 | YES
                                                 V
                                               -----
                RTS     PC                    ( RTS )
                                               -----

                               FIGURE B-21.
                           FLOW CHART:  NULOCT.


      BASIC-11 EXTENSIONS                                   Page  62
      FLOW CHARTS                                          27 Mar 79








                                             ---------
        POPRGS:                             ( POPRGS  )
                                             ---------
                                                 |
                                                 V
                                            -----------
                TST     (SP)+               | ADJ SP  |
                                            -----------
                                                 |
                                                 V
                MOV     (SP)+,R0            -----------
                MOV     (SP)+,R1            | RESTORE |
                MOV     (SP)+,R2            |  REGS   |
                MOV     (SP)+,R3            -----------
                MOV     (SP)+,R4                 |
                                                 V
                                               -----
                RTS     R5                    ( RTS )
                                               -----

                               FIGURE B-22.
                           FLOW CHART:  POPRGS.



                                             ---------
        PSHRGS:                             ( PSHRGS  )
                                             ---------
                                                 |
                                                 V
                MOV     R4,-(SP)             ---------
                MOV     R3,-(SP)             | SAVE  |
                MOV     R2,-(SP)             | REGS  |
                MOV     R1,-(SP)             ---------
                MOV     R0,-(SP)                 |
                                                 V
                                               -----
                JMP     R5                    ( JMP )
                                               -----

                               FIGURE B-23.
                           FLOW CHART:  PSHRGS


      BASIC-11 EXTENSIONS                                   Page  63
      FLOW CHARTS                                          27 Mar 79



                                             ---------
        TSTADR:                             ( TSTADR  )
                                             ---------
                                                 |
                                                 V
                                            -----------
                MOV     @#TIMOUT,2$         |  SAVE   |
                                            | TRP VEC |
                                            -----------
                                                 |
                                                 V
                                            -----------
                MOV     #1$,@#TIMOUT        | NEW VEC |
                                            -----------
                                                 |
                                                 V
                                                / \
                                               /   \
                                              /     \  NO
                TSTB    (R3)                 < REAL  >----
                                              \ ADR /    |
                                               \   /     |
                                                \ /      |
                                                 | YES   |
                                                 V       |
                                            -----------  |
                MOV     2$,@#TIMOUT         | RST VEC |  |
                                            -----------  |
                                                 |       |
                                                 V       |
                                               -----     |
                RTS     PC                    ( RTS )    |
                                               -----     |
                                                 ---------
        1$:                                      V
                                            -----------
                MOV     2$,@#TIMOUT         | RST VEC |
                                            -----------
                                                 |
                                                 V
                                            -----------
                JSR     R1,$BOMB            || $BOMB ||    
                .ASCIZ  \ERR MSG\           -----------
                                                 |
                                                 V
                                               -----
                                              ( RDY )
                                               -----
        2$:     0       ;SAVE TRAP VECTOR HERE

                               FIGURE B-24.
                           FLOW CHART:  TSTADR.


      BASIC-11 EXTENSIONS                                   Page  64
      FLOW CHARTS                                          27 Mar 79













                                             ---------
        .MACRO  PSHVAL                      ( PSHVAL  )
                                             ---------
                                                 |
                                                 V
                                                / \
                                               /   \
                                              /     \  NO
                TST     BYTFLG               < BYTE  >----
                BEQ     1$                    \     /    |
                                               \   /     |
                                                \ /      |
                                                 | YES   |
                                                 V       |
                MOVB    @BUSADR,-(SP)       -----------  |
                CLRB    1(SP)               | PSH BYT |  |
                BR      2$                  -----------  |
                                                 |       |
                                         ---------       |
                                         |       ---------
        1$:                              |       V
                                         |  -----------
                MOV     @BUSADR,-(SP)    |  | PSH WRD |
                                         |  -----------
                                         |       |
        2$:                              ------->|
                                                 V
                                               -----
        .ENDM                                 ( ENM )
                                               -----

                               FIGURE B-25.
                           FLOW CHART:  PSHVAL.


      BASIC-11 EXTENSIONS                                   Page  65
      REFERENCES                                           27 Mar 79










                                REFERENCES


      1.  N. A. Bourgeois, Jr. ,"Set of  Utility  Routines  for  any
          PDP-11 Machine Running RT-11 BASIC", DECUS-11-294, Digital
          Equipment Computer Users Society, Marlboro, MA, 10-Jan-77.

      2.  "BASIC-11 Language  Reference  Manual",  DEC-11-LIBBB-A-D,
          Digital Equipment Corporation, Maynard, MA, Sep-76.

      3.  "BASIC-11/RT-11 User's Guide",  DEC-11-LIBUA-A-D,  Digital
          Equipment Corporation, Maynard, MA, Aug-77.

      4.  "BASIC-11/RT-11  Installation  Guide",   DEC-11-LIBTA-A-D,
          Digital Equipment Corporation, Maynard, MA, Aug-77.

      5.  "PDP-11 MACRO-11 Language Reference Manual",  AA-5075A-TC,
          Digital Equipment Corporation, Maynard, MA, Aug-77.

      6.  "RT-11 System  User's  Guide",  DEC-11-ORGDA-A-D,  Digital
          Equipment Corporation, Maynard, MA, Aug-77.

      7.  "PDP-11  TECO  User's  Guide",  DEC-11-UTECA-A-D,  Digital
          Equipment Corporation, Maynard, MA, Sep-77.

      8.  Edward  Yourdon,  "Techniques  of  Program  Structure  and
          Design", Prentice-Hall, Englewood Cliff, NJ, 1975.


      BASIC-11 EXTENSIONS                                   Page  66
      INDEX                                                27 Mar 79










                                  INDEX


         ARGUMENT ERROR  . . . . . . . 10

         Error messages  . . . . . . . 10
         Extensions  . . . . . . . . . 7

         GET . . . . . . . . . . . . . 7, 8, 14, 15, 35, 36
         GETB  . . . . . . . . . . . . 7, 8, 9, 15, 16, 38

         IDEN  . . . . . . . . . . . . 7, 8, 9, 14, 39
         Installation  . . . . . . . . 11

         NO STRING SPACE . . . . . . . 10
         NULL  . . . . . . . . . . . . 7, 8, 9, 17, 39
         null arguments  . . . . . . . 8

         ODT . . . . . . . . . . . . . 21, 22

         PUT . . . . . . . . . . . . . 7, 8, 9, 14, 15, 17, 35, 40
         PUTB  . . . . . . . . . . . . 7, 8, 9, 15, 16, 42

         Routines  . . . . . . . . . . 7

         SBIT  . . . . . . . . . . . . 7, 8, 10, 17, 18, 19, 44

         TBIT  . . . . . . . . . . . . 7, 8, 10, 17, 18, 19, 45
         Testing . . . . . . . . . . . 14

         UNIMPLEMENTED BUS ADDRESS . . 10


      BASIC-11 EXTENSIONS                                   Page  67
      DISTRIBUTION                                         27 Mar 79










                               DISTRIBUTION


      HEADQUARTERS
      ESD/MCB/STOP 36
      HANSCOM AFB, MA 01731
      ATTN:     COL. R. T. KOZUMA, OCB

      HEADQUARTERS
      ROME AIR DEVELOPMENT CENTER (AFCS)
      GRIFFISS AFB, NY 13441
      ATTN:     MR. R. ALLEN, OCDS

      US ARMY MOBILITY EQUIPMENT RESEARCH AND DEVELOPMENT COMMAND
      FT. BELVOIR, VA 22060
      ATTN:     MR. D. KEEHAN, DRXFB-XS

      NAVAL UNDERSEA CENTER
      SAN DIEGO, CA 92132
      ATTN:     MR. J. REDFERN

      INSTITUTE FOR COMPUTER SCIENCES AND TECHNOLOGY
      US DEPARTMENT OF COMMERCE
      NATIONAL BUREAU OF STANDARDS
      WASHINGTON, DC 20234
      ATTN:     MR. R. T. MOORE, CHIEF
                COMPUTER SYSTEMS SECTION

      DEPARTMENT OF THE NAVY
      NAVAL COASTAL SYSTEMS LABS
      PANAMA CITY, FL 32401
      ATTN:     MR. R. FORBUS

      DIRECTOR
      DEFENSE NUCLEAR AGENCY
      WASHINGTON, DC 20305
      ATTN:     M. BEASLEY, NSSO

      KANSAS STATE UNIVERSITY
      DEPARTMENT OF ELECTRICAL ENGINEERING
      MANHATTAN, KS 66506
      ATTN:     PROF. N. AHMED

      NEW MEXICO STATE UNIVERSITY
      DEPARTMENT OF COMPUTER SCIENCE
      LAS CRUCES, NM 88003
      ATTN:     PROF. D. DEARHOLT


      BASIC-11 EXTENSIONS                                   Page  68
      DISTRIBUTION                                         27 Mar 79















                1111    S. D. STEARNS
                1521    J. L. MORTLEY
                1554    N. J. POLLARD
                1584    T. M. SCHULTHEIS
                1736    D. C. HANSON
                1736    N. A. BOURGEOIS, JR. (6)
                1736    G. W. DONOHOE
                1736    G. R. ELLIOTT (5)
                1736    R. P. KROMER
                2351    T. C. BRYANT, JR.
                2355    D. H. JENSEN
                2522    J. B. ALLEN
                2532    R. A. HAYENGA
                2534    R. W. ROBERTS
                2627    R. M. JAMES
                2648    L. F. TOLENDINO
                2648    T. M. UNKELHAEUSER
                3141    T. L. WERNER (5)
                3151    W. L. GARNER (3)
                                FOR DOE/TIC (UNLIMITED RELEASE)
                3172-3  R. P. CAMPBELL (25)
                                FOR DOE/TIC
                5722    B.    STIEFELD
                8266    E. A. AAS
                8466    D. N. TANNER
                9323    F. I. MAGEE
                9323    R. E. TRELLUE
                9526    A. J. ROTH
                9583    D. M. MORRISON