H 1 9  L I B R A R Y


                                 Version H01.00


                              Date: March 22, 1980

                              System: H11 - HT-11



                                     Author
                                Duncan N. Tanner
                              Livermore, Ca 94550





                                    ABSTRACT

          H19 Library  contains  a  collection  of  H11  assembly  language
     subroutines  for  controlling  the  functions  of the Heath/Zenith H19
     terminal.  H19 mnemonics as well as more conventional names  are  used
     for  the  function  calls.   The subroutines are useable in both HT-11
     assembly language and HT-11 Fortran.  They are NOT useable in BASIC.


                                                                   Page   2



                                  INTRODUCTION


          The H19LIB subroutines allow use of most of the H19 features with
     the  Heath Escape sequences.  The mnemonics in the Heath H19 Operation
     Manual are used  for  most  of  the  subroutine  names.   Calling  the
     subroutine  causes  the  correct  escape  sequence  to  be sent to the
     terminal.  Additional subroutines combine functions to provide special
     functions unique to the H19 terminal.

          The subroutine library is divided into the following categories:

               Cursor control functions
               Erasing and editing
               Terminal configuration
               Modes of operation
               Graphics
               25th line input-output
               Function keys


                                SUBROUTINE USAGE


          The  subroutines  may  be  called  from  either  PDP-11  assembly
     language or from HT-11 Fortran programs.

     ASSEMBLY LANGUAGE

          Most of the routines  require  no  parameters  and  the  call  is
     simply:
             JSR   PC,SUB
     where SUB is the subroutine name.  Each subroutine name must  also  be
     included in a .GLOBL line in your program.

          Some subroutines require parameters or data which is passed to or
     from  the subroutine.  The description and type (character or integer)
     for each parameter is provided.

          The  subroutines  use  the  standard  HT-11  and  RT-11   Fortran
     subroutine  calling  sequence.   Registor  R5  is used to point to the
     parameter  list.   The  subroutine  will  change  R5  so  it  must  be
     re-initialized  each time the subroutine is called.  An example of the
     subroutine usage is one which will enable the 25th line and  move  the
     cursor to the start of the line is shown below.

                 MOV   #LIST1, R5        ;Pointer to parameter list
                 JSR   PC,     HSM       ;Enable 25th line
                 MOV   #LIST,  R5        ;Pointer to parameter list
                 JSR   PC,     HDCA      ;Call HDCA to move cursor
                 -------
                 -------
          LIST1: .WORD  1,ONE
          LIST:  .WORD  2,ILIN,ICOL      ;Parameter list
          ILIN:  .WORD  25.              ;Line 25
          ICOL:  .WORD   1               ;Column 1
          ONE:   .WORD   1               ;Number 1, enable 25th line.


                                                                   Page   3



          The list contains  the  number  of  parameters  followed  by  the
     locations  of the parameters.  NOTE: the list contains the location of
     the parameter not the value.

          In some cases the subroutine has two names.  an example is  CLEAR
     and  HCD.   Both  are  calls  to  the same subroutine which clears the
     screen.


     FORTRAN

          Fortran call sequence is like the call to  any  subroutine.   the
     example above would appear as:
               CALL HSM(1)
               CALL HDCA(25,1)



                                                                   Page   4



                                CURSOR FUNCTIONS

     HCUH      Sends cursor to home position.
     HOME      Same as HCUH

     HCUF      Move cursor forward one position

     HCUB      Move cursor back one position

     HCUD      Move cursor down one line

     HCUU      Move cursor up one line

     HRI       Move cursor up to the same horizontal position on the
               preceeding line.

     HCPR      Gets current cursor position.
                Call is:  CALL HCPR(ILINE,ICOL)
                 ILINE   -  The line number ( 1 to 25 )
                 ICOL    -  The column number (1 to 80)

     HSCP      Save current cursor position in terminal

     HRCP      Restore cursor position to previously saved position.

     HDCA      Direct cursor addressing. Moves cursor to point specified.
                Call is:  CALL HDCA(ILINE,ICOL)
                 ILINE  -  Line number ( 1 to 25 )
                 ICOL   -  Column number ( 1 to 80 )
     POINT     Same as HDCA. CALL POINT(ILINE,ICOL)


                              ERASING and EDITING

     HCD       Clears the display
     CLEAR     Same as HCD

     HBD       Erase from top of screen down to and including
               the cursor position.

     HEOP      Erase to end of page.

     HEL       Erase entire line

     HEBL      Erase line from beginning to and including
               the cursor position.

     HEOL      Erase to end of line.

     HIL       Insert line

     HDL       Delete line

     HDCH      Delete character

     HEIM      Enter insert character mode

     HERM      Exit insert character mode


                                                                   Page   5



                                 CONFIGURATION

     HRAM      Reset to power-up configuration
     HRESET    Same as HRAM

     HSM       Sets modes
                 The call is: CALL HSM(IMODE)
                 IMODE=
                  1   Enable the 25th line.
                  2   No key click.
                  3   Hold screen mode
                  4   Block cursor
                  5   Cursor off
                  6   Keypad shifted
                  7   Alternate keypad mode
                  8   Auto line feed on receipt of CR
                  9   Auto CR on receipt of line feed

     HRM       Reset modes
                 The call is: CALL HRM(IMODE)
                 IMODE=
                  1   Disable 25th line
                  2   Enable key click
                  3   Exit hold screen mode
                  4   Underscore cursor
                  5   Cursor on
                  6   Keypad unshifted
                  7   Exit alternate keypad mode
                  8   No auto line feed
                  9   No auto CR

     HEAM      Enter ANSI Mode.  NOTE:  No other ANSI  modes
                 are supported in H19LIB.


                              MODES of  OPERATION

     HEHS      Enter hold screen mode
     HXHS      Exit hold screen mode

     HERV      Enter reverse video mode
     HXRV      Exit reverse video mode

     HEGM      Enter graphics mode
     HXGM      Exit graphics mode

     HEKS      Enter keypad shifted mode
     HXKS      Exit keypad shifted mode

     HAKM      Enter alternate keypad mode
     HXAM      Exit alternate keypad mode


                                                                   Page   6



                              Additional Functions

     HDK       Keyboard disabled

     HEK       Keyboard enabled

     HEWA      Wraparound at end of line

     HXWA      Discard characters at end of line


                                    GRAPHICS

     HBOX      Draws a single line box of the size specified.
                Call is:  CALL HBOX(ILINE1,ICOL1,ILINE2,ICOL2)
                  ILINE1  - Line number of top of box
                  ICOL1   - Column number of left side of box
                  ILINE2  - Line number of bottom of box
                  ICOL2   - Column number of right side of box

     HXBOX     Replaces a box drawn by HBOX with spaces, thus erasing it.
                Call is:  CALL HXBOX(ILINE1,ICOL1,ILINE2,ICOL2)
                The parameters are the same as for HBOX.


                             25TH LINE INPUT-OUTPUT

     WRIT25   This subroutine writes a  message  on  the  25th  line.   The
               routine  saves the current cursor position, enables the 25th
               line and writes text to the line in  the  starting  position
               specified.   The  cursor  is  then  returned to the previous
               position.  The 25th line can be written in normal or reverse
               video, but it always returns to normal video.

               The call sequence is:

                     CALL WRIT25(ISTR,MODE,IPOSN)

               ISTR   A character string array to be sent to the 25th line.
                    It  must  end  with  a  zero byte (null character).  In
                    assembly language the  .ASCIZ  directive  will  produce
                    this.  In Fortran the text may be placed in the call as
                    a parameter by surrounding it with ' .  An  example  is
                    CALL WRIT25('MESAGE',0,1)

               MODE   An optional integer parameter  indicating  normal  or
                    reverse  video.   MODE=0  is normal video, the default.
                    MODE=1 is reverse video.

               IPOSN  An  optional  integer  parameter  between  1  and  80
                    indicating  the  starting  position  for  the character
                    string.   If  this  parameter  is  omitted  IPOSN=1  is
                    assumed.

                    Parameters MODE and IPOSN may be  omitted,  however  if
                    IPOSN is included then MODE is also required.


                                                                   Page   7



     CLR25     This routine clears the entire 25th line.  IMODE  determines
               the  form of the clear.  IMODE=0 it is cleared.  IMODE=1 the
               25th line is filled with reverse video spaces.

                    CALL CLR25(IMODE)


     GET25     This routine gets a string of characters from the 25th line.
               An optional string prompt may be included.

                    CALL GET25(ISTR,IPRMPT)

               ISTR  A character string array which receives the characters
                    from  the  terminal.   The  string is terminated with a
                    zero byte (null character).

               IPRMPT An optional character array which contains  a  prompt
                    for the 25th line.  If IPRMPT is included the 25th line
                    is cleared prior to displaying the prompt.   If  IPRMPT
                    is  omitted  no  writing is done to the 25th line.  Any
                    previous characters in the line could confuse the user.


     PCLR25    This routine does a partial clear of the 25th line.   Spaces
               are written from ICOL1 to ICOL2.

                    CALL PCLR25(ICOL1,ICOL2)


                                                                   Page   8



                                 FUNCTION KEYS

     HFIN      Function key and character string input.  All the Heath  H19
               function  keys  are  supported  in the Heath Escape Sequence
               mode.  Function keys are decoded and returned as an  integer
               value.  Lower case input is also enabled.

                     CALL HFIN(ISTR,IMODE)


               ISTR is a character string array sized to allow the  longest
                    line  expected  from  the  terminal  plus one.  The H19
                    allows 80 characters per line so we need to  allow  for
                    81.   characters.   This  size  is  needed  only if you
                    expect a full line.

                    ISTR contains the characters from the  terminal  except
                    for valid escape sequences.  Valid escape sequences are
                    those corresponding to the H19 function keys.

                    ISTR is terminated with a zero (NULL  character).   The
                    function key is a line terminator.  This means that you
                    can type any characters before the  function  key,  and
                    the  function key acts like a RETURN.  A RETURN is also
                    a line terminator as it is normally.  

                    If no function key is typed and a RETURN is entered the
                    characters are returned and IMODE is set to zero.

                    The RUBOUT and Control U do their usual thing.

                    Normally none of the function key escape sequences  are
                    echoed  back  to  the  terminal.   The  cursor  control
                    functions can be enabled by calling  subroutine  HCURON
                    (JSR PC,HCURON or CALL HCURON).  After HCURON is called
                    the cursor control function keys  will  be  echoed  and
                    IMODE  will  be set.  A call to HCUROF will disable the
                    echo of the cursor functions.  The default is HCUROF.

               IMODE is an integer indicating which function key,  if  any,
                    was entered.

                    -1 indicates an invalid escape sequence.  The  sequence
                    is returned in ISTR

                    0 Means that no escape sequences  were  entered.   ISTR
                    contains  any  characters entered.  NOTE: a zero in the
                    first byte of ISTR means that only a RETURN was typed.

                    A number greater than zero represents a function key as
                    follows:


                                                                   Page   9



     HFIN      (continued)


               FUNCTIONS
                       IMODE        FUNCTION
                         1           F1 function key
                         2           F2 function key
                         3           F3 function key
                         4           F4 function key
                         5           F5 function key
                         6           Not used
                         7           F7 function key (blue)
                         8           F8 function key (red)
                         9           F9 function key (gray)

               ALTERNATE KEYPAD MODE
                       IMODE         KEY
                         10           0 key
                         11           1 key
                         12           2 key
                         13           3 key
                         14           4 key
                         15           5 key
                         16           6 key
                         17           7 key
                         18           8 key
                         19           9 key
                         20           . key
                         21           ENTER key

               SHIFTED KEYPAD  -  These functions are echoed
                                    if HCURON was called.

                        IMODE        KEY
                         31           1  (IL)  insert line
                         32           2  (down arrow)  cursor down
                         33           3  (DL)  delete line
                         34           4        left arrow
                         35           5        HOME
                         36           6        right arrow
                         37           7  (IC)  enter insert character mode
                         38           8        up arrow
                         39           9 (DC)  delete character
                         40           7        exit insert character mode


               ERASE KEY
                         41            ERASE
                         42            SHIFT ERASE

     HCURON    Enables cursor control  escape  sequence  echoing  with  the
               routine HFIN.

     HCUROF    Disables cursor control escape  sequence  echoing  with  the
               routine HFIN.


                                                                   Page  10



                                   I N D E X


          25th Line  . . . . . . 6

          Additional Functions . 6

          CLEAR  . . . . . . . . 4
          CLR25  . . . . . . . . 7
          Configuration  . . . . 5
          Cursor Functions . . . 4

          Editing  . . . . . . . 4
          Erasing  . . . . . . . 4

          Function Keys  . . . . 8

          GET25  . . . . . . . . 7
          Graphics . . . . . . . 6

          HAKM . . . . . . . . . 5
          HBD  . . . . . . . . . 4
          HBOX . . . . . . . . . 6
          HCD  . . . . . . . . . 4
          HCPR . . . . . . . . . 4
          HCUB . . . . . . . . . 4
          HCUD . . . . . . . . . 4
          HCUF . . . . . . . . . 4
          HCUH . . . . . . . . . 4
          HCUROF . . . . . . . . 9
          HCURON . . . . . . . . 9
          HCUU . . . . . . . . . 4
          HDCA . . . . . . . . . 4
          HDCH . . . . . . . . . 4
          HDK  . . . . . . . . . 6
          HDL  . . . . . . . . . 4
          HEAM . . . . . . . . . 5
          HEBL . . . . . . . . . 4
          HEGM . . . . . . . . . 5
          HEHS . . . . . . . . . 5
          HEIM . . . . . . . . . 4
          HEK  . . . . . . . . . 6
          HEKS . . . . . . . . . 5
          HEL  . . . . . . . . . 4
          HEOL . . . . . . . . . 4
          HEOP . . . . . . . . . 4
          HERM . . . . . . . . . 4
          HERV . . . . . . . . . 5
          HEWA . . . . . . . . . 6
          HFIN . . . . . . . . . 8, 9
          HIL  . . . . . . . . . 4
          HOME . . . . . . . . . 4
          HRAM . . . . . . . . . 5
          HRCP . . . . . . . . . 4
          HRESET . . . . . . . . 5
          HRI  . . . . . . . . . 4
          HRM  . . . . . . . . . 5
          HSCP . . . . . . . . . 4
          HSM  . . . . . . . . . 5


                                                                   Page  11



          HXAM . . . . . . . . . 5
          HXBOX  . . . . . . . . 6
          HXGM . . . . . . . . . 5
          HXHS . . . . . . . . . 5
          HXKS . . . . . . . . . 5
          HXRV . . . . . . . . . 5
          HXWA . . . . . . . . . 6

          Modes of Operation . . 5

          PCLR25 . . . . . . . . 7
          POINT  . . . . . . . . 4

          WRIT25 . . . . . . . . 6


                                                                   Page  12