H 1 9  L I B R A R Y (HT-11)


                                Duncan N. Tanner
                              Livermore, Ca 94550



          H19 Library  contains  a  collection  of  H11  assembly  language
     subroutines  for  controlling  the  functions  of the Heath/Zenith H19
     terminal.  H19 mnemonics as well as more conventional names  are  used
     for  the  function  calls.   The subroutines are useable in both HT-11
     assembly language and HT-11 Fortran.  They are NOT useable in BASIC.

          The H19LIB subroutines allow use of most of the H19 features with
     the  Heath Escape sequences.  The mnemonics in the Heath H19 Operation
     Manual are used  for  most  of  the  subroutine  names.   Calling  the
     subroutine  causes  the  correct  escape  sequence  to  be sent to the
     terminal.  Additional subroutines combine functions to provide special
     functions unique to the H19 terminal.

          The subroutine library is divided into the following categories:

               Cursor control functions
               Erasing and editing
               Terminal configuration
               Modes of operation
               Graphics
               25th line input-output
               Function keys

          Space does not permit a complete rundown of each subroutine.  The
     disk  submitted  to  HUG contains a documentation file which describes
     each subroutine in detail.  Nearly all of the H19 mnemonics have  been
     inplemented  as  subroutines.   They perform the function described in
     the H19 manual.  The graphics section  only  contains  a  box  drawing
     routine  as  this  time.   The  25th  line and function key categories
     include some useful routines to take advantage of the H19 features.


                                                                   Page   2



                             25TH LINE INPUT-OUTPUT

     WRIT25   This subroutine writes a  message  on  the  25th  line.   The
               routine  saves the current cursor position, enables the 25th
               line and writes text to the line in  the  starting  position
               specified.   The  cursor  is  then  returned to the previous
               position.  The 25th line can be written in normal or reverse
               video, but it always returns to normal video.

               The call sequence is:

                     CALL WRIT25(ISTR,MODE,IPOSN)

               ISTR   A character string array to be sent to the 25th line.
                    It  must  end  with  a  zero byte (null character).  In
                    assembly language the  .ASCIZ  directive  will  produce
                    this.  In Fortran the text may be placed in the call as
                    a parameter by surrounding it with ' .  An  example  is
                    CALL WRIT25('MESAGE',0,1)

               MODE   An optional integer parameter  indicating  normal  or
                    reverse  video.   MODE=0  is normal video, the default.
                    MODE=1 is reverse video.

               IPOSN  An  optional  integer  parameter  between  1  and  80
                    indicating  the  starting  position  for  the character
                    string.   If  this  parameter  is  omitted  IPOSN=1  is
                    assumed.

                    Parameters MODE and IPOSN may be  omitted,  however  if
                    IPOSN is included then MODE is also required.

     CLR25     This routine clears the entire 25th line.  IMODE  determines
               the  form of the clear.  IMODE=0 it is cleared.  IMODE=1 the
               25th line is filled with reverse video spaces.

                    CALL CLR25(IMODE)

     GET25     This routine gets a string of characters from the 25th line.
               An optional string prompt may be included.

                    CALL GET25(ISTR,IPRMPT)

               ISTR  A character string array which receives the characters
                    from  the  terminal.   The  string is terminated with a
                    zero byte (null character).

               IPRMPT An optional character array which contains  a  prompt
                    for the 25th line.  If IPRMPT is included the 25th line
                    is cleared prior to displaying the prompt.   If  IPRMPT
                    is  omitted  no  writing is done to the 25th line.  Any
                    previous characters in the line could confuse the user.


     PCLR25    This routine does a partial clear of the 25th line.   Spaces
               are written from ICOL1 to ICOL2.

                    CALL PCLR25(ICOL1,ICOL2)


                                                                   Page   3



                                 FUNCTION KEYS

     HFIN      Function key and character string input.  All the Heath  H19
               function  keys  are  supported  in the Heath Escape Sequence
               mode.  Function keys are decoded and returned as an  integer
               value.  Lower case input is also enabled.

                     CALL HFIN(ISTR,IMODE)


               ISTR is a character string array sized to allow the  longest
                    line  expected  from  the  terminal  plus one.  The H19
                    allows 80 characters per line so we need to  allow  for
                    81.   characters.   This  size  is  needed  only if you
                    expect a full line.

                    ISTR contains the characters from the  terminal  except
                    for valid escape sequences.  Valid escape sequences are
                    those corresponding to the H19 function keys.

                    ISTR is terminated with a zero (NULL  character).   The
                    function key is a line terminator.  This means that you
                    can type any characters before the  function  key,  and
                    the  function key acts like a RETURN.  A RETURN is also
                    a line terminator as it is normally.  

                    If no function key is typed and a RETURN is entered the
                    characters are returned and IMODE is set to zero.

                    The RUBOUT and Control U do their usual thing.

                    Normally none of the function key escape sequences  are
                    echoed  back  to  the  terminal.   The  cursor  control
                    functions can be enabled by calling  subroutine  HCURON
                    (JSR PC,HCURON or CALL HCURON).  After HCURON is called
                    the cursor control function keys  will  be  echoed  and
                    IMODE  will  be set.  A call to HCUROF will disable the
                    echo of the cursor functions.  The default is HCUROF.

               IMODE is an integer indicating which function key,  if  any,
                    was entered.

                    -1 indicates an invalid escape sequence.  The  sequence
                    is returned in ISTR

                    0 Means that no escape sequences  were  entered.   ISTR
                    contains  any  characters entered.  NOTE: a zero in the
                    first byte of ISTR means that only a RETURN was typed.

                    A number greater than zero represents a function key as
                    follows:


                                                                   Page   4



     HFIN      (continued)


               FUNCTIONS
                       IMODE        FUNCTION
                         1           F1 function key
                         2           F2 function key
                         3           F3 function key
                         4           F4 function key
                         5           F5 function key
                         6           Not used
                         7           F7 function key (blue)
                         8           F8 function key (red)
                         9           F9 function key (gray)

               ALTERNATE KEYPAD MODE
                       IMODE         KEY
                         10           0 key
                         11           1 key
                         12           2 key
                         13           3 key
                         14           4 key
                         15           5 key
                         16           6 key
                         17           7 key
                         18           8 key
                         19           9 key
                         20           . key
                         21           ENTER key

               SHIFTED KEYPAD  -  These functions are echoed
                                    if HCURON was called.

                        IMODE        KEY
                         31           1  (IL)  insert line
                         32           2  (down arrow)  cursor down
                         33           3  (DL)  delete line
                         34           4        left arrow
                         35           5        HOME
                         36           6        right arrow
                         37           7  (IC)  enter insert character mode
                         38           8        up arrow
                         39           9 (DC)  delete character
                         40           7        exit insert character mode


               ERASE KEY
                         41            ERASE
                         42            SHIFT ERASE

     HCURON    Enables cursor control  escape  sequence  echoing  with  the
               routine HFIN.

     HCUROF    Disables cursor control escape  sequence  echoing  with  the
               routine HFIN.