DECODE
	RT-11 SAV/LDA DISASSEMBLER

ABSTRACT

	DECODE IS A PROGRAM WRITTEN TO RUN UNDER RT-11
OPERATING SYSTEM TO DECODE .SAV AND .LDA FILES INTO THEIR
EQIVALENT MACRO CODE COMPLETE WITH SELF GENERATED LABELS,
ABSOLUTE LOCATION, SYMBOL TABLE, CROSS REFERENCE TABLE, OCTAL,
ASCII AND RADIX 50 EQUIVALENTS.
	THE OUTPUT CAN BE RUN THROUGH THE MACRO ASSEMBLER
AND LINKED TO RECREATE THE ORIGINAL FILE. BY THE USE OF SWITCHES
THE OUTPUT CODE CAN BE MADE TO REFLECT THE INSTRUCTION SET
OF ONE MACHINE CONFIGURATION ONLY INSTEAD OF ALL POSSABLE
INSTRUCTIONS.


INSTRUCTIONS

	THE COMMAND STRING TO DECODE IS ;
*OUTFIL=INFIL/SW:VAL/SW:VAL

WHERE THE FILES HAVE THE STANDARD RT-11 FORMAT

DEV:FILNAM.EXT[SIZE]

DEFAULT EXTENTIONS ARE
INPUT FILE	.SAV
OUTPUT FILE	.MAC

SWITCHES

/A:VAL		USED TO LIMIT THE ARITHMETIC INSTRUCTIONS DECODED
		INTO NEMONICS. THE ARITHMETIC OPTION GIVEN BY VAL

		VAL=EIS
		    FIS
		    FPU

		GIVES THE SET OF ARITHMETIC INSTRUCTIONS
 		THAT ARE TO BE DECODED INTO NEMONICS. THE /A SWITCH IS
		RECOGNIZED ONLY IF THE /P SWITCH IS ALSO USED AND THE
		PROCESSOR SPECIFIED BY THE /P SWITCH  ALLOWS THE OPTIONS
		GIVEN BY VAL(FIS IS ILLEGAL FOR A 45 AS IS FPU FOR A 40).
		NOTE THAT A VAL OF FIS ALSO IMPILES EIS IS ON THE SYSTEM.	

/L		FLAGS THAT THE INPUT FILE IS AN LDA FILE. IN THIS CASE
		THE .EXT ON THE INPUT FILE MUST BE SPECIFIED AS .LDA.
		SEE EXAMPLES 1 AND 2

/M		USED TO LIMIT THE INSTRUCTION SET DECODED INTO NEMONICS.
		IN THIS CASE IT FLAGS THE EXISTENCE OF A MEMORY
		MANAGEMENT UNIT ON THE SYSTEM. THIS SWITCH IS IGNORED
		IF THE /P SWITCH IS NOT USED OR IF IT IS, THE
		PROCESSOR SPECIFIED DOES NOT HAVE THE CAPABILITY
		OF MEMORY MANAGEMENT(THAT MEANS 40'S AND ABOVE) AND
		THEN ONLY THE MEMORY MANAGEMENT INSTRUCTIONS
		THAT APPLY TO THAT PROCESSOR.


/P:VALUE.	SPECIFIES THE TYPE OF PROCESSOR TO DECODE FOR. IF
		VALUE IS NOT GIVEN-ONLY THE BASIC INSTRUCTION SET IS
		DECODED INTO NEMONICS. IF /P IS NOT USED,ALL POSSABLE
		PDP-11 INSTRUCTIONS ARE DECODED INTO THEIR NEMONICS.
		VALUE IS THE DECIMAL NUMBER OF THE TYPE OF PROCESSOR
		( 03,04,05,10,15,20,34,35,40,45,ETC)
		AND MUST BE FOLLOWED BY A '.' DECIMAL POINT TO TELL
		THE CSI THAT IT IS A DECIMAL NUMBER. THIS SWITCH MUST BE
		USED IF THE /A AND /M SWITCHES ARE TO BE RECOGNIZED AND
		THE OPTIONS SPECIFIED MUST BE COMPATABLE WITH THE
		PROCESSOR TYPE GIVEN BY THE /P:VAL. OR THEY WILL BE
		IGNORED. THE DISSASEMBLER BREAKS DOWN THE PDP-11
		INSTRUCTION SET INTO 9 CATAGORIES

		1	BASIC INSTRUCTION SET AS FOR THE PDP 11/04
			THROUGH THE 11/20 SERIES.

		2	PDP 11/03 UNIQUE INSTRUCTIONS.

		3	PDP 11/40-11/45 UNIQUE BASIC INSTRUCTION SET.
			INCLUDES ALL THOSE NON OPTION INSTRUCTIONS
			UNIQUE TO THE 11/40 AND 45 COMPUTERS.

		4	PDP 11/45 UNIQUE BASIC INSTRUCTION SET.
			INCLUDES ALL THE NON OPTION INSTRUCTIONS
			UNIQUE TO THE 11/45 COMPUTER

		5	PDP 11/40-11/45 MEMORY MANAGEMENT INSTRUCTION
			SET. INCLUDES ALL THE MEMORY MANAGEMENT
			INSTRUCTIONS COMMON TO THE 11/40 AND 45
			COMPUTERS

		6	PDP 11/45 MEMORY MANAGEMENT INSTRUCTION SET.
			INCLUDES ALL THE MEMORY MANAGEMENT INSTRUCTIONS
			UNIQUE TO THE 11/45.

		7	EIS INSTRUCTION SET

		8	FIS INSTRUCTION SET

		9	FPU INSTRUCTION SET



VAL\INS. SET	1    2    3    4    5    6    7    8    9
NOVAL
0-2		X
4-20

3		X    X    X                   A    A

21-40		X         X         A         A    A

41-77		X         X    X    A    A    X         A


WHERE
	X=DEFAULT INSTRUCTION SET FOR VAL
	A=ACCEPTABLE ADDITONAL INSTRUCTION SET AVAILABLE FOR VAL
	 =INSTRUCTIONS NOT AVAILABLE FOR VAL


		THE DECODER USES THE OPTIONS SPECIFIED IN THE COMMAND
		STRING TO CHOOSE WHICH COMBINATION OF INSTRUCTION SETS
		TO DECODE INTO NEMONICS( DEFAULT FOR NO OPTION SWITCHES
		IN THE COMMAND STRING IS ALL OF THEM)


		

EXAMPLE 1	DISASSEMBLE A SAV FILE
.R DECODE
*PIP=PIP
.

EXAMPLE 2	DISASEMBLE AN LDA FILE
.R DECODE
*ROLLIN=ROLLIN.LDA/L
.

EXAMPLE 3	DISASSEMBLE FOR A BASIC MACHINE (11/20)
.R DECODE
*TEST=TEST/P
.
OR
.R DECODE
*TEST=TEST/P:20.
.

EXAMPLE 4	FOR AN LSI-11 WITH ARITHMETIC CHIP
.R DECODE
*TEST=TEST/P:3./A:FIS
.

EXAMPLE 5	AN 11/45 WITH MEMORY MANAGEMENT BUT NO FPU(EIS IS
		PART OF THE BASIC INSTRUCTION SET OF THE 45)
.R DECODE
*TEST=TEST/P:45./M
.

EXAMPLE 6	A FULL UP 55 WITH ALL THE OPTIONS
.R DECODE
*TEST=TEST/P:55./M/A:FPU
.


DISASSEMBLER OPERATION
	THE DISASSEMBLER MAKES 2 OR 3 PASSES OVER THE INPUT
DEPENDING ON THE TYPE OF FILE IT IS:
PASS 0	OPTIONAL LDA REFORMAT PASS
	CONVERTS AN LDA FILE INTO SAV FORMAT USEING A 128. BLOCK
	SCRATCH FILE ON THE SYSTEM DISK TO HOLD THE IMAGE FOR
	THE NEXT TWO PASSES

PASS 1	SEARCH FOR LABELS
	DECODE THE SAV FILE AND LOCATE ALL MEMORY REFERENCES
	(SRC/DEST MODES 2 THRU 7 AND ALL BRANCHES ETC) AND
	ASSIGN A LABEL TO THE VALUE FOUND

PASS 2	OUTPUT SOURCE
	DECODE AGAIN THE SOURCE NOW OUTPUTING IT SUBSTITUTEING
	LABELS FOR THE ABSOLUTE AND RELATIVE ADDRESSES FOUND
	IN PASS 1.



GENERATED CODE

	THE OUTPUT OF THE DISASSEMBLER IS BROKEN INTO 7 PARTS:
PART 1:	DEFINITIONS
	1	DEFINE ALL REGISTERS (AND ACCUMULATORS IF DECODEING FPU
		INSTRUCTIONS)
	2	DECLARE THE LOCATION OF THE STACK STARTING
		LOCATION(IF FOUND) AS THE GLOBAL NAME 'STACK'
		THIS IS SO WHEN LINKING,THE STACK CAN BE PROPERLY
		PLACED BY THE USE OF THE /M SWITCH OF THE LINKER.
		WHEN LINKING,SPECIFY THE /M SWITCH, THE LINKER
		WILL COME BACK ASKING FOR THE STACK SYMBOL, JUST TYPE
		'STACK' AND IT WILL BE PROPERLY PLACED.
	3	DECLARES AN .ASECT
	4	SETS THE POINT TO THE FIRST LOCATION DECODED (FOR SAVE
		FILES EITHER 1000 OR THE STARTING ADDRESS WHICH EVER
		IS LOWER AND FOR LDA FILES THE LOWEST ADDRESS FOUND)
PART 2:	LABEL DEFINITIONS
	THOSE LABELS GENERATED DURING PASS 1 AND WHOS VALUE IS EITHER A
	BYTE OR WHOSE VALUE IS OUTSIDE THE BOUNDRIES OF THE PROGRAM ARE
	DEFINED HERE IN THE FORM:
	LXXX=VALUE
PART 3:	GENERATED CODE
	THE GENERATED CODE LINE HAS SIX SEGMENTS
	1	LABEL	IF THE ADDRESS IS REFFERED TO BY A LABEL
		FOUND IN PASS 1, IT IS PRINTED OUT IN THE FORM
		LXXX:
		(IF THIS IS THE START ADDRESS THE LABEL
		START:
		PRECEEDS THIS LABEL ON THE LINE PREVIOUS ALL BY
		ITSELF)
	2	INSTRUCTION NEMONIC OR .WORD DECLARATION
	3	AS THE FIRST PART OF A COMMENT, THE LOCATION OF THE
		INSTRUCTION
	4	THE NEXT ITEM IN THE COMMENT ARE THE OCTAL CONTENTS
		OF THE WORDS MAKEING UP THE INSTRUCTION.
	5	THE THIRD ITEM IS A LIST OF THE EQUIVALENT ASCII
		CARACTERS OF THE WORDS THAT MAKE UP THE INSTRUCTION
		(ALL ASCII CHARACTERS WITH VALUES LESS THAN 40 ARE 
		REPACED BY BLANKS)
	6	THE LAST ITEM IN THE COMMENT IS THE RADIX 50 EQUIVALENT
		STRING OF THE WORDS OF THE INSTRUCTION


	IN THE CASE OF BLOCKS OF ZERO'S, THE FIRST ONE IS DECODEDED
	AS A HALT AND IF THE BLOCK GOES ON FOR A TOTAL OF MORE THAN
	2 ZEROES, THE NEXT LINE IS A RESET OF THE POINTER TO THE
	FIRST NON ZERO WORD FOLLOWING THE BLOCK(IF THE BLOCK TERMINATES
	THE PROGRAM,THE BLOCK IS TERMINATED AT THE LAST WORD OF THE
	PROGRAM AND THE FINAL ZERO IS DECODED.

PART 4	LEFT OVER LABELS
	ANY LABELS FOUND DURING PASS 1 THAT HAVE NOT BEEN DEFINED IN
	EITHER PARTS 2 OR 3 ARE DEFINED HERE IN THE SAME MANNER AS IN 
	PART 2
PART 5	END STATEMENT
	THE END OF THE PROGRAM IS DECLARED FOR THE ASSEMBLER
	EITHER AS
	.END
	OR
	.END	START
	DEPENDING ON IF A START ADDRESS WAS GIVEN.
PART 6	SYMBOL TABLE
	A COMPLETE SYMBOL TABLE IS PRINTED OUT GIVEING EACH LABEL
	AND ITS VALUE(132 COLLUMN FORMAT).
PART 7 CROSS REFERENCE TABLE
	A LISTING OF ALL LABELS AND THE ABSOLUTE LOCATIONS THAT
	REFERENCE THEM( EXCEPT THE DECLARATION OR LABEL DEFINITION
	LOCATION, THAT MUST BE OBTAINED FROM THE SYMBOL TABLE).


POSSABLE MACRO ASSEMBLER ERRORS

	WHEN RUNNING THE RESULTING CODE THROUGH THE MACRO ASSEMBLER,
THE FOLLOWING ERRORS CAN BE REPORTED:

I	ILLEGAL CHARACTER
	SUCH PRINTING CHARACTERS AS THE GRAVE ACCENT ARE NOT
	ACCEPTABLE TO THE MACRO ASSEMBLER EVEN IF THEY OCCOUR
	IN COMMENTS, SO IF SUCH A CHARACTER IS FOUND IN THE
	.ASCII // STATEMENT, IT WILL FLAGGED AS AN I ERROR
	EVEN THOUGH IT IS IN A COMMENT-THIS ERROR CAN BE IGNORED.

Z	INSTRUCTION INCOMPATABLE ON VARIOUS PDP-11 MODELS
	DATA, INTERPRETED AS INSTRUCTIONS, CAN COME UP AS
	THE MOST UNUSUAL INSTRUCTIONS-THIS ONE CAN BE IGNORED

A	ADDRESS ERROR
	ONLY KNOW CASE IS FOR 
	SOB	RX,.+2
	WHERE DATA IS INTERPRETED AS AN SOB INSTRUCTION WITH
	AN OFFSET BRANCH DISTANCE OF 0 (.+2). THE ASSEMBLER
	TREATS THIS AS AN ERROR AND CHANGES IT TO 
	SOB	RX,.
	WHICH IS NOT THE SAME. DO NOT IGNORE THIS ERROR,CHECK
	ALL OCCOURANCES.