BASIC CROSS REFERENCING PROGRAMS

             Three  versions  of  the  BASIC  cross  referencing
        programs  exist.  They are CROSS.BAS, CROSSV.BAS and the
        three  part  CROSS0.BAS,  CROSS1.BAS   and   CROSS2.BAS.
        CROSS.BAS  requires  the  most  memory  and executes the
        fastest.  CROSSV.BAS puts some arrays out on the  system
        disk  to  reduce  memory  requirements at the expense of
        operating speed.  In addition to putting the  arrays  on
        the system disk CROSS0.BAS chains to CROSS1.BAS which in
        turn  chains  to  CROSS2.BAS.   This  chaining   further
        reduces  memory requirements with an additional decrease
        in operating speed.

             User interaction with all  three  versions  of  the
        cross  referencing  program is identical.  After issuing
        the appropriate RUN command the user is asked  to  enter
        the input file specification for the BASIC program to be
        cross referenced.  The default input device is DK:   and
        the  default  extension is .BAS.  Then the user is asked
        to name the output device.  LP:  is the  default  output
        device.  If a file structured device is named for output
        the output file name is the same as that  of  the  input
        file with an extension of .CRF.

             The following table shows the  memory  requirements
        and  the  execution  times for the three versions of the
        cross referencing program.  The PDP-11/03 had 28K  words
        of  MOS  memory and an RX01 disk.  The PDP-11/10 had 28K
        words of core memory an an  RK05  disk.   Both  machines
        were  running  BASIC-11/RT-11  V02-03O  under  RT-11  SJ
        V03B-00C.  In all cases CROSS.BAS was the input file and
        NL:   was  the  output  device.  A greater difference in
        execution times between CROSSV and CROSS0/1/2 would have
        been observed if a file structured device had been named
        for output.

        Program         Memory          11/03           11/10

        CROSS           12889           6:56            6:21
        CROSSV          7586            15:22           7:13
        CROSS0/1/2 *    5374            15:33           7:34





            *   At this time a bug exists  in  the  BASIC-11
            interpreter  which  causes  the  COMMON  area to
            become  corrupted  during  the  execution  of  a
            COMPILED copy of the CROSS1.BAS module.


        BASIC CROSS REFERENCING PROGRAMS                Page   2
                                                       20 Nov 79


             The following table lists  the  various  files  and
        their current versions:

                        File            Version

                        CROSS.BAS       79H08A
                        CROSSV.BAS      79H09A
                        CROSS0.BAS      79H08A
                        CROSS1.BAS      79H08A
                        CROSS2.BAS      79H08A



                                N. A. Bourgeois, Jr. / 1736
                                Sandia Laboratories
                                P. O.  Box 5800
                                Albuquerque, NM 87185


                                79H13A