ADDENDUM TO THESIS PAPER.
	======== == ====== =====

	THE FOLLOWING CONSTRUCTS HAVE BEEN ADDED TO ALGOL SINCE MY
	THESIS PAPER WAS WRITTEN.

A.  'CHAIN' STATEMENT.

	THE CHAIN STATEMENT HAS THE FOLLOWING FORM.

	<CHAIN STATEMENT>::= CHAIN <FILE NAME DESIGNATOR> <OPTION>
	<FILE NAME DESIGNATOR>::= <QUOTED STRING> ! <FILE IDENTIFIER> !
				  <POINTER EXPRESSION>
	<OPTION>::= <EMPTY> ! , <BOOLEAN EXPRESSION>


	THE CHAIN STATEMENT HAS THE FOLLOWING SEMANTICS:

	IF THE <OPTION> IS EMPTY, THE FILE DESIGNATED BY THE
	<FILE NAME DESIGNATOR> IS LOADED INTO THE ALGOL RUN-TIME
	SYSTEM AND RUN.
	IF THE <OPTION> IS A BOOLEAN EXPRESSION,THEN THE EXPRESSION
	IS EVALUATED AND THE FILE IS CHAINED IF THE EXPRESSION HAS
	THE VALUE OF TRUE.
	WHEN THE CHAINED JOB IS TERMINATED, CONTROL IS PASSED BACK TO
	THE RUN-TIME SYSTEM, NOT TO THE INVOKING PROGRAM.

B.  DEFINE EXPANSION.

	PARAMATERIZED DEFINES MAY NOW BE INVOKED WITH EITHER PARENTHESIS
	OR WITH BRACKETS.

C.  COMPILE-AND-GO SWITCH.

	THE COMPILE AND GO SWITCH HAS BEEN ADDED TO THE COMMAND STRING
	INTERPRETER. IT HAS THE FORM OF '/G' AND MAY APPEAR ANYWHERE
	AS MAY THE OTHER SWITCHES.

D.  MULTIPLE INPUT FILES.

	THE COMPILER NOW ACCEPTS MULTIPLE INPUT FILES. AS MANY FILES AS
	CAN BE READ IN WITHIN 80 COLUMNS WILL BE ACCEPTED. ALL THAT IS
	REQUIRED IS THAT THEY BE SEPARATED BY A COMMA.

E.  INDIRECT FILES.

	THE INPUT COMMAND STRING MAY NOW BE AN INDIRECT FILE.
	THE FORM OF THE INDIRECT FILE SPECIFICATION IS: @FOO.CMD .
	NO EXTENSION IS ASSUMED FOR THIS FILE. THIS FILE IS THEN
	OPENED AND A LINE IS READ FROM IT FOR THE COMMAND STRING
	SPECIFICATIONS. THIS LINE ALSO MAY BE AN INDIRECT FILE
	SPECIFICATION. INDIRECT FILES MAY BE NESTED AS MANY AS FIVE (5)
	DEEP AFTER WHICH AN ERROR MESSAGE IS GENERATED.

F.  BUGS FIXED.

G.  LISTING OUTPUT CHANGED SLIGHTLY.

H.  EXTERNAL DECLARATIONS IMPLEMENTED.

	DOCUMENTATION ON THIS MAY BE FOUND IN SEVERAL PLACES THROUGHOUT
	THE COMPILER LISTING. (BEFORE PURGEIT, BEFORE PROCDEC.)



ALSO
	THE 'REAL' FUNCTION IS NOT PROPERLY DOCUMENTED IN THE THESIS.
	IT IS ESSENTIALLY THE SAME AS IN THE BURRROUGHS MANUAL.

FORM	PARAMETERS		RETURNS
REAL(	<BOOLEAN EXPRESSION>)	16 BIT INTEGER WITH A VALUE OF THE
				BOOLEAN EXPRESSION. NO BITS ARE CHANNGED.

REAL(<INTEGER EXPPESSION>)	16 BIT INTEGER EXPRESSION. NO CHANGE FROM
				THE VALUE OF THE INTEGER EXPRESSION.

REAL(<POINTER EXPRESSION>,<INTEGER EXPRESSION>)
				8 BIT CHARACTERS ARE TAKEN FROM THE
				POINTER EXPRESSION ONE AT A TIME AND
				CONCATTED TO FORM AN INTEGER RESULT.
				NOTE THAT IF THIS RESULT HAS A VALUE
				GREATER THAN 16 BITS, THEN AN ERROR
				MESSAGE IS GENERATED.
I.  UNITS = CHARACTERS ADDED (OF SORTS).
	ALTHOUGH THERE CURRENTLY IS NO FILE ATTRIBUTE 'UNITS',
	THE FILE MAY BE OPENED IN CHARACTER MODE (ASCII SEQUENTIAL FILES
	ONLY) BY SETTING THE HI BYTE OF THE 'MYUSE' ATTRIBUTE IN THE
	FILE DECLARATION. IF THIS IS SET, THEN ALL I/O TRANSFER COUNTS
	ARE TAKEN TO BE BYTE COUNTS RATHER THAN WORD COUNTS.

	E.G.
		FILE TT(KIND=REMOTE,MYUSE=3"400");

		OPENS THE FILE TT: FOR CHARACTER MODE I/O (RATHER THAN
		WORD MODE).
J.  MORE BUGS FIXED SINCE THE INITIAL VERSION (BOTH IN THE COMPILER
	AND IN THE INTERPRETER).

K.  ****RESTRICTION****
    -------------------

	'FOR' STATEMENTS AND 'THRU' STATEMENTS MAY NOT OCCUR IN THE SAME
	BLOCK AS A COMPOUND BLOCK AFTER THE COMPOUND BLOCK.

	E.G.
		BEGIN
		  INTEGER I;
		  THRU I
		  DO I:=I+1;	% THIS THRU STATEMENT OK.

		  BEGIN		% START OF COMPOUND STATEMENT.
		   DEFINE FOOEY=#;
		   END OF COMPOUND BLOCK;

		% FOR AND THRU STATEMENTS MAY NOT OCCUR IN THIS BLOCK
		% BEYOUND THIS POINT. FAILURE TO HEAD THIS WILL RESULT
		% IN BAD CODE BEING GENERATED.
		END.

	THE REASON FOR THIS IS DUE TO THE ADDRESSING INTERNAL TO THE
	INTERPRETER. THE COMPILER ALLOCATES THE TEMPORIES FOR 'FOR'
	AND 'THRU' STATEMENTS, USES THE ASSIGNED ADDRESSES, BUT THE CODE
	TO ALLOCATE THE TEMPS MAY NOT BE EXECUTED. THIS IS DUE TO THE
	ONE PASS NATURE OF THE COMPILER.