The DIRECTORY program provides the user with the ability to
sort and display the directory of a RT-11 disk (or DECtape). 
It is much like the PIP /L switch, but is more flexible. 
DIRECTORY will display for the user a list of all files on the
specified device which match the input file specifications. 
Furthermore, it will sort the directory alphabetically by file
name, alphabetically be extension, coronologically by date, in
order of increasing size, or the reverse of any of these.  In
addition, files whose date is either before or after a specified
date can be excluded from the directory.

After running DIRECTORY (which responds with an *), the user
enters a standard RT-11 command line which includes an optional
output file specification (TT:  will be used by default) where
the user wishes the directory to appear, and up to six input
file specifications (which may include *'s for wildcard file
names or extensions), and one or more switches to control the
nature of the directory sort.  All files matching any of the
input files specification (as modified by the swtiches) will be
included in the directory listing.  The output may be directed
to any normal RT-11 terminal, line printer, or any file
structured device.  After completing a command line, DIRECTORY
will print an *, indicating that it is ready to accept another
command line.  Terminate the program by typing CTRL/C.

 
The switches recognized by DIRECTORY are as follows:

/B		Include the starting block address (in decimal)
		for each file.

/C:N		Format the directory listing into N columns on the
		output device.

/E		Include all empty spaces on the device in the
		directory in addition to any files.

/Q		Do not include the files' date or size in the
		directory listing.

/L		List all files on the specified device meeting one
		or more of the input file specifications, sorted
		according to the switch specification given (if
		any).  This is the default condition.

/M		List only the unused spaces on the device. 
		Regardless of any other file specification or
		switch, only the unused blocks on the specified
		device will be listed, and they will always be
		listed in the order in which they appear on that
		device.

/V		Include DIRECTORY'S version number in the header
		of the directory.

/F		Print the number of free blocks on the specified
		device.  Any other input file specification and
		any other switches in the command line are
		ignored.

/S:ARG	The order in which the directory of file
		names matching the input file specification can be
		specified by including the /S switch with one of
		the following arguments:  "NAM" will cause the
		directory to sorted by fle name (this is the
		default); "EXT" by file name extension, "DAT" by
		file date; "SIZ" by the size (number of blocks)
		of the files; "POS" by position on the device (a
		directory by POS would be in the same order as a
		PIP /L directory).

/S:REV	A second /S switch (or a second argument to
		the first /S switch) can be used to specify that
		the directory is to be in reverse order (that is,
		Z through A, rather than A through Z).

/D		The /D switch is used to specify a date.  Only
		files dated after the specified date will be
		included in the directory.  Three arguments should
		be specified with the /D switch, one for date, one
		for month, and one for year.  The /D would
		normally be followed by an exclamation mark and a
		day of the month, followed by a colon and a three
		character month, followed by an exclamation mark
		and a year.  Note that the numbers representing
		the day and the year would be interpreted as octal
		if they were preceeded by a colon and that the
		three character month representation must be
		preceeded by a colon.  If no arguments are
		specified, with the /D switch todays date is used.
		The arguments may be given in any order.

/D:BEF	If a second /D switch is included in the
		command line (or a fourth argument to a single /D
		switch) only files dated before the specified date
		(rather that after it) will be included in the
		directory.  All dates are inclusive of the
		specified day.

/H		This switch provides a listing of the DIRECTORY
		switches and defaults on the console terminal. 
		All other file specification and switches are
		ignored.

With the exception of the /H, /F, and /M switches all other
switches may be combined in any logical manner.  If no switches
are specified, the default is /L + /S:NAM.  If no file name is
specified, the default is "*.*".  Thus, a simple carriage
return will produce a directory of all files on device DK0: 
sorted alphabetically by file name and will include the date
and size of each file.  If the directory output is directed to
a file structure device, the default file name is DIRECT.DIR.

Each command line may specify only one input device.  The
directory produced will always be for the device associated
with the first input file specification, any other input device
specifications on the line will be ignored.  By default, the input
device is DK0:.

\test 80,