MJCLOK (Multi-Job CLOcK program)
                                   Version II


                                       by


                                   S.C. CRIBBS
                                Pinawa, Manitoba
                                 Canada  R0E1L0











                                    ABSTRACT

             MJCLOK is a Foreground or System job utility that  displays
        current  calendar and time values, and user defined messages, on
        a VT100 RT-11 console terminal in a manner  transparent  to  the
        Background  job.   This  program demonstrates the feasibility of
        routing output to the console from  Foreground  or  System  jobs
        through   Background   job  completion  routines  thus  avoiding
        terminal context switching.  MJCLOK has the  facility  to  avoid
        conflicts  with  Background  jobs  that  require full use of the
        video display.  Version II differs from the original version  in
        two  ways:   Terminal flow control commands are used to regulate
        communication.  A single line display option has been added.






                        MJCLOK (Multi-Job CLOcK program)


             MJCLOK is a PDP-11 program that maintains a current display
        of  date,  day of the week, and time of day on the RT-11 console
        terminal.  The display device used must be  a  VT100  series  or
        equivalent  terminal.  This program has been written in MACRO-11
        for the RT-11 V4 Foreground/Background (FB) and Extended  Memory
        (XM)  monitors.   It  will not execute properly under the Single
        Job (SJ) or Base Line (BL) monitors.



        1.0   PURPOSE


             Apart from providing the user with an incessant reminder of
        his/her life ticking away, MJCLOK has been designed as a vehicle
        to demonstrate the feasibility  of  multi-job  use  of  a  video
        display  under RT-11.  When programs execute concurrently, RT-11
        precedes output to the shared console with a job  identification
        text string.  I'm sure this was designed by DEC as a convenience
        feature and is appreciated when there is infrequent output  from
        more  than just the Background job directed to the same printing
        terminal.  However, the job  identification  string  is  only  a
        liability  to  programmers  attempting  to  create software that
        write to specific display screen zones on a video terminal.

             MJCLOK is intended to be a Foreground or  System  Job  that
        can  be  initiated  when  RT-11  is  bootstrapped  and remain in
        execution until the computer is shut  down.   To  be  practical,
        such  a  job should use very little memory and central processor
        time, be  completely  memory  resident,  require  little  or  no
        operator interaction - yet still be useful.  This program solves
        the multi-job I/O problem and exhibits the above named features.
        Even the price is right!



        2.0   PROGRAM DESCRIPTION


             The program executes a simple loop.  It obtains the current
        time from the monitor, modifies the display fields on the screen
        that must be changed and uses the .TWAIT programmed  request  to
        have  the  monitor put it to sleep for a time interval (eg.  one
        second).  When it  re-awakens  the  cycle  repeats.   MJCLOK  is
        composed   of   five   main  routines:   screen  initialization,
        date-day-time  display,  keyboard  command   processor   and   a
        Background  job  watch  routine.   The  last  two  are  optional
        features that may be omitted to minimize program size.


                                                                  Page 2



        2.1  Screen Initialization Routine


             This subroutine  requests  the  terminal  to  allocate  the
        non-scrolling  display  area  to be used, erases it, and defines
        the display  area  characteristics.   A  program  assembly  time
        option allows for the selection of either double height - double
        width characters or simply double width only characters  in  the
        top  line  of the display area.  If the optional message display
        facility  (see  section  2.4)  has  been  requested,  the   line
        immediately  below  the date - time fields will be cleared.  The
        remaining screen lines are not affected and are defined  as  the
        terminal's scrolling region.  Screen initialization is performed
        once as the program  is  started  and  whenever  called  by  the
        keyboard command processor and Background job watch routines.



        2.2  Date-Day-Time Display Routine


             The time of day field is  updated  each  time  the  program
        awakens.  The date field is written to the terminal whenever the
        screen is initialized and upon time of day rollover.  Each  time
        the  date  field is written, the current day of the week is also
        calculated and written to the screen.  These  three  fields  are
        displayed  in  VT100  oversized characters.  For double height -
        double width fields, the same text must be sent  to  both  lines
        one  and  two  of  the  screen.  The user is given the option of
        having the date field formatted  in  year/month/day  numbers  or
        day-month-year alphanumerics.



        2.3  Keyboard Command Processor


             After each pass through the display routines MJCLOK  checks
        the  terminal  input  buffer  for  a command from the user.  Two
        single character commands are recognized.  Future display  field
        updates  are  suspended  when  an  "S" is received.  MJCLOK then
        becomes almost dormant.  It simply looks for a new command  each
        time  it  awakes and then goes back to sleep if one has not been
        received.   This  feature  allows  the  RT-11  console   to   be
        temporarily shifted to a hardcopy terminal or another program to
        have full control of the VT100 display screen.  Anytime the user
        types  an  "R", the screen is re-initialized, the display fields
        are repainted and normal field updating resumes.


                                                                  Page 3



        2.4  Message Display Routine


             This  is  an  optional  feature  selected  before   program
        assembly.   It's  purpose  is  to allow the user to request that
        various single line text  strings  be  displayed  at  predefined
        times  of  day  for  specified  time  intervals.   Additionally,
        message requests can be made for only on a specific day  of  the
        week,  only  for weekdays (Monday-Friday), only on weekends, and
        for every day of the week.  The user created  messages  will  be
        displayed on the line immediately below the date - time fields.



        2.5  Job Watch Routine


             The  Background  job  watch  routine  is  another  optional
        feature  that  must be selected before the program is assembled.
        It's purpose is to inhibit  MJCLOK  from  interfering  with  the
        output  written  to  the display by Background jobs that utilize
        the VT100's programmable features.  An example of such a program
        is  the KED editor which assumes that it has exclusive ownership
        of the video screen.



        3.0   OUTPUT METHOD


             To defeat the job  identification  features  of  the  RT-11
        console  terminal handler, MJCLOK passes all of it's output text
        through the Background job  for  display.   All  print  requests
        execute  as  completion  routines for the Background job.  Thus,
        there is a clean RT-11 solution to an RT-11 problem.  The output
        from  the  higher priority job gets preference over text written
        by the Background job,  the  output  requests  from  MJCLOK  are
        transparent  to  the  Background  job and terminal direct cursor
        addressing by multiple jobs is made practical.

             Unfortunately there is  no  programmed  request  or  SYSLIB
        routine  that  directly  allows a job to queue such a completion
        routine.  The solution, demonstrated  by  subroutine  DSPLAY  in
        program  MJCLOK,  is  to  simulate an interrupt and then use the
        .SYNCH request to queue the printing of the  text  string.   The
        switch  of  context to the Background job is made by the monitor
        when the job number argument for  .SYNCH  is  defined  as  zero.
        There is always a Background job in RT-11, even if it's only the
        Keyboard monitor, so the request will never fail because it  has
        been  queued  for  a  non-existent  job.   Output performed by a
        completion routine does not interfere with normal  output  of  a
        Background  job  so  it  is  possible  to  execute virtually any
        Background job while MJCLOK is running.



                                                                  Page 4



             The use of this technique is quite straight forward as long
        as  the  following  considerations are observed.  First, the job
        queueing the request must make sure the last  request  completes
        before  an  attempt  is made to re-use the same workspace.  This
        restriction is common to all  usage  of  the  .SYNCH  programmed
        request.   The user must test the word at offset octal 14 of the
        .SYNCH workspace to be sure  it  is  zero  before  re-using  it.
        Second, each call to .SYNCH results in the new request being put
        at the head of the  Background  job  completion  routine  queue.
        This  can  be  a problem if the order of execution of the output
        requests is  important.   An  example  of  this  is  the  screen
        initialization  routine,  INISCN  in  MJCLOK,  which  executes a
        .TWAIT  request  after  it  has  issued  it's  commands  to  the
        terminal.  This insures that the terminal is in the proper state
        before the time and date text fields are output.

             The RT-11 console terminal handler  has  been  designed  to
        throw  away characters that are to be echoed if the job's output
        buffer is full.  If this happened, the user  would  notice  that
        the  occasional character typed as input at the keyboard was not
        echoed on the display.  This is, to say the  least,  undesirable
        and   shows  that  the  output  method  is  somewhat  baud  rate
        dependent.  One solution is to limit the amount of  text  output
        by  the  high  priority  job.  A most significant enhancement in
        version II, is to insert ASCII flow control characters into  the
        output  stream.   Every text string issued by MJCLOK is preceded
        by XOFF  <DC3>  and  terminates  with  XON  <DC1>.   User  typed
        characters  are  temporarily  stored in the terminal's own input
        buffer while MJCLOK updates the display.   In  conjunction  with
        the  above,  the higher priority job should not send text to the
        Background job's output buffer  until  there  is  room  for  it.
        Unfortunately,  RT-11  V4  does  not  provide easy access to the
        character  count  values  associated  with   ring   buffers   in
        non-multiterminal configurations.



        4.0   GENERATING MJCLOK


             A demonstration version of  the  program  (MJCLOK.REL)  has
        been  provided,  but  the  source  code  (MJCLOK.MAC)  has  been
        included for people who wish to take advantage of  the  optional
        features.   An  option  is  selected  by defining the associated
        symbol  at  the  beginning  of  the  source   file.    This   is
        accomplished by simply deleting the semi-colon that proceeds the
        symbol name.



                                                                  Page 5



             Users  of  PDP-11  computers  equipped  with  the  extended
        instruction  set  will  wish  to  define  symbol EIS.  This will
        invoke hardware multiplication and division  instructions  which
        will   speed   execution   and  slightly  reduce  program  size.
        Non-Hardware dependent (NHD) code  is  generated  as  a  default
        condition.   Defining symbol YMD results in the date field being
        displayed as year, month and day two digit numbers seperated  by
        slash characters.  Thus the sub fields are displayed in order of
        decreasing   significance,   a   standard   now   adopted    for
        international  acceptance.  The American traditional date format
        is used if this symbol is not defined, but costs an aditional 52
        words in program size.

             Two more conditional assembly options are available.   They
        are   the  message  display  feature  (symbol  MSGDSP)  and  the
        Background job watch function (symbol  JBWTCH).   These  options
        require more user involvement than the previous two in that code
        at the end of the source file may have to be modified.   I  will
        describe the message display option first.

             If the option  has  been  selected,  MJCLOK  looks  at  the
        current  element  of  an  event table each time it awakens.  The
        event code is tested against the current day of  the  week.   If
        the  test is passed, a check is made to determine if the present
        time of day falls within the time  interval  specified  for  the
        message.   In  that case, the message is written to the display.
        Failure to pass the event code test or on  finding  the  present
        time  to  be  later than the specified interval causes MJCLOK to
        advance the event table pointer.

             The structure of the event table and  message  strings  are
        most  easily  understood by looking at the examples found at the
        end of the MJCLOK source file (begins at symbol  EVNTBL:).   The
        event  table  consists  of  a number of six word table elements.
        The table must be terminated by a zero word.  The first word  of
        each  table  entry  defines  the day of week conditions that the
        message should be displayed.  A code of  -3  specifies  only  on
        weekends,  -2  every  day of the week, -1 means only on weekdays
        and the  positive  numbers  ranging  from  1  to  7  select  the
        appropriate day of the week (Sunday=day#1).  Table element words
        2 and 3 specify, in RT-11 internal time format, the time of  day
        that  the  message  display  should be initiated.  Words 4 and 5
        specify the time that the message should  be  erased.   Finally,
        word  6  is the address of the text string to be displayed.  The
        number of elements in the table is restricted only by the number
        of  clock  ticks  in  a 24 hour period, the amount of memory one
        wants to allocate to MJCLOK and by the user's imagination.   The
        event  table  must  be  terminated with a word containing a zero
        value.  One word of caution, the elements  of  the  event  table
        should be sorted in order of advancing time of day.



                                                                  Page 6



             User defined messages should have the same structure as the
        examples  provided  in  the  program.  First, issue XOFF and the
        terminal's save cursor position command.   The  text  should  be
        routed  one  line  above  the  scrolling  region  (symbol BGNSCL
        defines the first line of the  scrolling  region).   The  cursor
        position  must  be  restored  at  the end of the message and the
        character  XON  inserted  before  the  octal  200  byte   string
        terminator.  I've written MJCLOK assuming that the terminal will
        normally be used in 80 character per line format,  although  132
        character  messages are feasible with the VT100 display.  In the
        examples given, the text string is displayed in  reverse  video,
        centered  on  the  line  and  two  bell  tones are output as the
        message is written.   Remember  any  VT100  character  attribute
        turned  on  within  the  message  must  also be turned off again
        within the same text string.

             Defining symbol JBWTCH selects  the  Background  job  watch
        function.   This  routine  is  the first code executed each time
        MJCLOK re-awakens.  The filename of the current  Background  job
        is tested against each of the filenames stored in the MJCLOK job
        table.  The table begins at symbol JOBTBL:.   When  a  match  is
        made  MJCLOK  goes  back  to  sleep  without  updating  the time
        display, and will execute only the job watch routine  until  the
        match fails.  The first complete scan through the job table that
        does not result in a match causes the program  to  re-initialize
        the  screen and resume normal output.  Elements of the job table
        are three words in length and must be stored  in  RAD50  format.
        The  first two words represent the job name, the last one is the
        job type.  There is no defined  limit  to  the  number  of  data
        elements in the table, but it must terminate with a zero word.



        5.0   USING MJCLOK


             Since the demonstration version (MJCLOK.REL) has been built
        to use NHD code it should execute properly on any RT-11 FB or XM
        system equipped with  a  VT100  terminal.   Note  that  for  the
        program to be useful, the line time clock (LTC) on the processor
        must be enabled.  This program will execute as a  Foreground  or
        System  job.  In fact if it is relinked as a "SAV" file, it will
        run as a Background job.  To start it type:

                  .FRUN MJCLOK
                       or
                  .SRUN MJCLOK.REL


                                                                  Page 7



        Please remember that you must turn off  the  automatic  carriage
        return  -  line  feed  feature  of  the  RT-11  console terminal
        handler.  You accomplish this by entering the command:

                  .SET TT: NOCRLF

        before executing MJCLOK.  Failure to do so will  result  in  the
        terminal  appearing  to occasionally misplace one of the display
        fields.

             Display field  updating  can  be  suspended  with  the  "S"
        command  and  the  display  refreshed  through  use  of  the "R"
        command.   Remember  you  must  change  job  input  context   by
        preceding  commands  to  MJCLOK with CONTROL_F or CONTROL_X.  To
        return to addressing your  input  to  the  Background  job  type
        CONTROL_B.   The  RT-11  command  SUSPEND  will perform the same
        function as the "S"  command  when  MJCLOK  is  executing  as  a
        Foreground  job but RESUME, ofcourse, only continues rather than
        repaints the screen.

             If you have modified the source file, for example to change
        a  display message or to add a new file specification to the job
        table, the  program  will  have  to  be  regenerated.   Use  the
        following RT-11 commands to do so.

                  .MACRO MJCLOK.MAC
                  .LINK/FOREGROUND MJCLOK

        The newly generated program can then be  executed  as  described
        above.



        6.0  ACKNOWLEDGEMENTS


             I would like to thank Peter Dodd of Saint Mary's University
        in  Nova  Scotia  for  suggesting the inclusion of terminal flow
        control commands and the option  of  single  line  double  width
        character displays.  The former makes MJCLOK much more useful to
        users with the slower LSI-11 & LSI-11/2 processors,  the  latter
        leaves  an  additional  free  line  to  the terminal's scrolling
        region.